## Slide 1: Caches (Writing)
Hakim Weatherspoon
CS 3410, Spring 2013
Computer Science
Cornell University
P & H Chapter 5.2-3, 5.5

## Slide 2: Goals for Today: caches
Writing to the Cache
  Write-through vs Write-back
Cache Parameter Tradeoffs
Cache Conscious Programming
Notes: Caches vs memory vs tertiary storage
- Tradeoffs: big & slow vs small & fast
- working set: 90/10 rule
- How to predict future: temporal & spacial locality

## Slide 3
Writing with Caches

## Slide 4: Eviction
Which cache line should be evicted from the cache to make room for a new line?
  Direct-mapped
    no choice, must evict line selected by index
  Associative caches
    random: select one of the lines at random
    round-robin: similar to random
    FIFO: replace oldest line
    LRU: replace line that has not been used in the longest time

## Slide 5: Next Goal
What about writes?
What happens when the CPU writes to a register and calls a store instruction?!

## Slide 6: Cached Write Policies
Q: How to write data?
CPU
Cache
SRAM
Memory
DRAM
addr
data
If data is already in the cache…
No-Write
  writes invalidate the cache and go directly to memory
Write-Through
  writes go to main memory and cache
Write-Back
  CPU writes only to cache
  cache writes to main memory later (when block is evicted)

## Slide 7: What about Stores?
Where should you write the result of a store?
  If that memory location is in the cache?
    Send it to the cache
    Should we also send it to memory right away?
    (write-through policy)
    Wait until we kick the block out (write-back policy)
  If it is not in the cache?
    Allocate the line (put it in the cache)?
    (write allocate policy)
    Write it directly to memory without allocation?
    (no write allocate policy)

## Slide 8: Write Allocation Policies
Q: How to write data?
CPU
Cache
SRAM
Memory
DRAM
addr
data
If data is not in the cache…
Write-Allocate
  allocate a cache line for new data (and maybe write-through)
No-Write-Allocate
  ignore cache, just go to main memory

## Slide 9: Next Goal
Example: How does a write-through cache work?
Assume write-allocate.

## Slide 10: Handling Stores (Write-Through)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
Cache
Processor
V tag data
$0
$1
$2
$3
Memory
78
120
71
173
21
28
200
225
Misses: 0
Hits: 0
0
0
Assume write-allocate
policy
Using byte addresses in this example! Addr Bus = 5 bits
Fully Associative Cache
2 cache lines
2 word block
4 bit tag field
1 bit block offset field

## Slide 11: Write-Through (REF 1)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
Cache
Processor
V tag data
$0
$1
$2
$3
Memory
78
120
71
173
21
28
200
225
Misses: 0
Hits: 0
0
0

## Slide 12: How Many Memory References?
Write-through performance
Each miss (read or write) reads a block from mem
Each store writes an item to mem
Evictions don’t need to write to mem

## Slide 13: Takeaway
A cache with a write-through policy (and write-allocate) reads an entire block (cacheline) from memory on a cache miss and writes only the updated item to memory for a store. Evictions do not need to write to memory.

## Slide 14: Next Goal
Can we also design the cache NOT write all stores immediately to memory?
  Keep the most current copy in cache, and update memory when that data is evicted (write-back policy)
Notes: Do we need to write-back all evicted lines?
No, only blocks that have been stored into (written)

## Slide 15: Write-Back Meta-Data
V = 1 means the line has valid data
D = 1 means the bytes are newer than main memory
When allocating line:
  Set V = 1, D = 0, fill in Tag and Data
When writing line:
  Set D = 1
When evicting line:
  If D = 0: just set V = 0
  If D = 1: write-back Data, then set D = 0, V = 0
V | D | Tag | Byte 1 | Byte 2 | … Byte N

## Slide 16: Write-back Example
Example: How does a write-back cache work?
Assume write-allocate.

## Slide 17: Handling Stores (Write-Back)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
Cache
Processor
V d tag data
$0
$1
$2
$3
Memory
78
120
71
173
21
28
200
225
Misses: 0
Hits: 0
0
0
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
Using byte addresses in this example! Addr Bus = 5 bits
Assume write-allocate
policy
Fully Associative Cache
2 cache lines
2 word block
3 bit tag field
1 bit block offset field

## Slide 18: Write-Back (REF 1)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
Cache
Processor
V d tag data
$0
$1
$2
$3
Memory
78
120
71
173
21
28
200
225
Misses: 0
Hits: 0
0
0
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]

## Slide 19: How Many Memory References?
Write-back performance
Each miss (read or write) reads a block from mem
Some evictions write a block to mem

## Slide 20: How Many Memory references?
Each miss reads a block
  Two words in this cache
Each evicted dirty cache line writes a block

## Slide 21: Write-through vs. Write-back
Write-through is slower
  But cleaner (memory always consistent)
Write-back is faster
  But complicated when multi cores sharing memory

## Slide 22: Takeaway
A cache with a write-through policy (and write-allocate) reads an entire block (cacheline) from memory on a cache miss and writes only the updated item to memory for a store. Evictions do not need to write to memory.
A cache with a write-back policy (and write-allocate) reads an entire block (cacheline) from memory on a cache miss, may need to write dirty cacheline first. Any writes to memory need to be the entire cacheline since no way to distinguish which word was dirty with only a single dirty bit. Evictions of a dirty cacheline cause a write to memory.

## Slide 23: Next Goal
What are other performance tradeoffs between write-through and write-back?
How can we further reduce penalty for cost of writes to memory?

## Slide 24: Performance: An Example
Performance: Write-back versus Write-through
Assume: large associative cache, 16-byte lines
for (i=1; i<n; i++)
A[0] += A[i];
for (i=0; i<n; i++)
B[i] = A[i]
Notes: Q: direct, or associative? A: associative definitely (w/ LRU or LFU, etc.)
A) reads: miss every W’th A[i]
A) writes: n for write-through, 1 eviction for write-back
B) reads: miss every W’th A[i] or B[i]
B) writes: n for write-through, n for write-back

## Slide 25: Performance Tradeoffs
Q: Hit time: write-through vs. write-back?
Q: Miss penalty: write-through vs. write-back?

## Slide 26: Write Buffering
Q: Writes to main memory are slow!
A: Use a write-back buffer
  A small queue holding dirty lines
  Add to end upon eviction
  Remove from front upon completion
Q: What does it help?
A: short bursts of writes (but not sustained writes)
A: fast eviction reduces miss penalty

## Slide 27: Write-through vs. Write-back
Write-through is slower
  But simpler (memory always consistent)
Write-back is almost always faster
  write-back buffer hides large eviction cost
  But what about multiple cores with separate caches but sharing memory?
Write-back requires a cache coherency protocol
  Inconsistent views of memory
  Need to “snoop” in each other’s caches
  Extremely complex protocols, very hard to get right

## Slide 28: Cache-coherency
Q: Multiple readers and writers?
  A: Potentially inconsistent views of memory
Mem
L2
L1
L1
Cache coherency protocol
May need to snoop on other CPU’s cache activity
Invalidate cache line when other CPU writes
Flush write-back caches before other CPU reads
Or the reverse: Before writing/reading…
Extremely complex protocols, very hard to get right
CPU
L1
L1
CPU
L2
L1
L1
CPU
L1
L1
CPU
disk
net
A
A
A
A
A’
A

## Slide 29: Takeaway
A cache with a write-through policy (and write-allocate) reads an entire block (cacheline) from memory on a cache miss and writes only the updated item to memory for a store. Evictions do not need to write to memory.
A cache with a write-back policy (and write-allocate) reads an entire block (cacheline) from memory on a cache miss, may need to write dirty cacheline first. Any writes to memory need to be the entire cacheline since no way to distinguish which word was dirty with only a single dirty bit. Evictions of a dirty cacheline cause a write to memory.
Write-through is slower, but simpler (memory always consistent)/
Write-back is almost always faster (a write-back buffer can hidee large eviction cost), but will need a coherency protocol to maintain consistency will all levels of cache and memory.

## Slide 30
Cache Design Tradeoffs

## Slide 31: Cache Design
Need to determine parameters:
  Cache size
  Block size (aka line size)
  Number of ways of set-associativity (1, N, )
  Eviction policy
  Number of levels of caching, parameters for each
  Separate I-cache from D-cache, or Unified cache
  Prefetching policies / instructions
  Write policy

## Slide 32: A Real Example
> dmidecode -t cache
Cache Information
Configuration: Enabled, Not Socketed, Level 1
Operational Mode: Write Back
Installed Size: 128 KB
Error Correction Type: None
Cache Information
Configuration: Enabled, Not Socketed, Level 2
Operational Mode: Varies With Memory Address
Installed Size: 6144 KB
Error Correction Type: Single-bit ECC
> cd /sys/devices/system/cpu/cpu0; grep cache/*/*
cache/index0/level:1
cache/index0/type:Data
cache/index0/ways_of_associativity:8
cache/index0/number_of_sets:64
cache/index0/coherency_line_size:64
cache/index0/size:32K
cache/index1/level:1
cache/index1/type:Instruction
cache/index1/ways_of_associativity:8
cache/index1/number_of_sets:64
cache/index1/coherency_line_size:64
cache/index1/size:32K
cache/index2/level:2
cache/index2/type:Unified
cache/index2/shared_cpu_list:0-1
cache/index2/ways_of_associativity:24
cache/index2/number_of_sets:4096
cache/index2/coherency_line_size:64
cache/index2/size:6144K
Dual-core 3.16GHz Intel (purchased in 2011)

## Slide 33: A Real Example
Dual 32K L1 Instruction caches
  8-way set associative
  64 sets
  64 byte line size
Dual 32K L1 Data caches
  Same as above
Single 6M L2 Unified cache
  24-way set associative (!!!)
  4096 sets
  64 byte line size
4GB Main memory
1TB Disk
Dual-core 3.16GHz Intel (purchased in 2009)

## Slide 34: Basic Cache Organization
Q: How to decide block size?

## Slide 35: Experimental Results
Notes: For a given total cache size,
larger block sizes mean….
  fewer lines
  so fewer tags (and smaller tags for associative caches)
  so less overhead
  and fewer cold misses (within-block “prefetching”)
But
  fewer blocks available (for scattered accesses!)
  so more conflicts
  and miss penalty (time to fetch block) is larger

## Slide 36: Tradeoffs
For a given total cache size,
larger block sizes mean….
  fewer lines
  so fewer tags (and smaller tags for associative caches)
  so less overhead
  and fewer cold misses (within-block “prefetching”)
But also…
  fewer blocks available (for scattered accesses!)
  so more conflicts
  and larger miss penalty (time to fetch block)
Notes: Same for other parameters: experimental mostly

## Slide 37
Cache Conscious Programming

## Slide 38: Cache Conscious Programming
// H = 12, W = 10
int A[H][W];
for(x=0; x < W; x++)
for(y=0; y < H; y++)
sum += A[y][x];

## Slide 39: Cache Conscious Programming
// H = 12, W = 10
int A[H][W];
for(y=0; y < H; y++)
for(x=0; x < W; x++)
sum += A[y][x];

## Slide 40: Summary
Caching assumptions
  small working set: 90/10 rule
  can predict future: spatial & temporal locality
Benefits
  (big & fast) built from (big & slow) + (small & fast)
Tradeoffs: associativity, line size, hit cost, miss penalty, hit rate

## Slide 41: Summary
Memory performance matters!
  often more than CPU performance
  … because it is the bottleneck, and not improving much
  … because most programs move a LOT of data
Design space is huge
  Gambling against program behavior
  Cuts across all layers: users  programs  os  hardware
Multi-core / Multi-Processor is complicated
  Inconsistent views of memory
  Extremely complex protocols, very hard to get right

## Slide 42: Administrivia
Prelim1: TODAY, Thursday, March 28th in evening
  Time: We will start at 7:30pm sharp, so come early
  Two Location: PHL101 and UPSB17
    If NetID ends with even number, then go to PHL101 (Phillips Hall rm 101)
    If NetID ends with odd number, then go to UPSB17 (Upson Hall rm B17)
  Closed Book: NO NOTES, BOOK, ELECTRONICS, CALCULATOR, CELL PHONE
  Practice prelims are online in CMS
  Material covered everything up to end of week before spring break
    Lecture: Lectures 9 to 16 (new since last prelim)
    Chapter 4: Chapters 4.7 (Data Hazards) and 4.8 (Control Hazards)
    Chapter 2: Chapter 2.8 and 2.12 (Calling Convention and Linkers), 2.16 and 2.17 (RISC and CISC)
    Appendix B: B.1 and B.2 (Assemblers), B.3 and B.4 (linkers and loaders), and B.5 and B.6 (Calling Convention and process memory layout)
    Chapter 5: 5.1 and 5.2 (Caches)
    HW3, Project1 and Project2
Notes: Appendix C (logic, gates, FSMs, memory, ALUs)
Chapter 4 (pipelined [and non-pipeline] MIPS processor with hazards)
Chapters 2 (Numbers / Arithmetic, simple MIPS instructions)
Chapter 1 (Performance)
HW1, HW2, Lab0, Lab1, Lab2

## Slide 43: Administrivia
Next six weeks
  Week 9 (Mar 25): Prelim2
  Week 10 (Apr 1): Project2 due and Lab3 handout
  Week 11 (Apr 8): Lab3 due and Project3/HW4 handout
  Week 12 (Apr 15): Project3 design doc due and HW4 due
  Week 13 (Apr 22): Project3 due and Prelim3
  Week 14 (Apr 29): Project4 handout
Final Project for class
  Week 15 (May 6): Project4 design doc due
  Week 16 (May 13): Project4 due