## Slide 1: Traps, Exceptions, System Calls, & Privileged Mode
Hakim Weatherspoon
CS 3410, Spring 2013
Computer Science
Cornell University
P&H Chapter 4.9, pages 509–515, appendix B.7

## Slide 2: Administrivia: Where are we now in the course?
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard
Stack, Data, Code
Stored in Memory

## Slide 3: Administrivia
Next four weeks
  Week 11 (Apr 8): Lab3 due and Project3/HW4 handout
  Week 12 (Apr 15): Project3 design doc due and HW4 due
  Week 13 (Apr 22): Project3 due and Prelim3
  Week 14 (Apr 29): Project4 handout
Final Project for class
  Week 15 (May 6): Project4 design doc due
  Week 16 (May 13): Project4 due

## Slide 4: Administrivia
Lab3 is due this week, Thursday, April 11th
Project3 available now
  Design Doc due next week, Monday, April 15th
  Schedule a Design Doc review Mtg now, by this Friday, April 12th
  Whole project due Monday, April 22nd
  Competition/Games night Friday, April 26th, 5-7pm. Location: B17 Upson
Homework4 is available now
  Work alone
  Due next week, Wednesday, April 17th
  Question1 on Virtual Memory is pre-lab question for in-class Lab4
  HW Help Session Thurs (Apr 11) and Mon (Apr 15), 6-7:30pm in B17 Upson
Prelim3 is in two and a half weeks, Thursday, April 25th
  Time and Location: 7:30pm in Phillips 101 and Upson B17
  Old prelims are online in CMS

## Slide 5: Summary of Caches/TLBs/VM
Caches, Virtual Memory, & TLBs: answer three questions
Where can block be placed?
  Direct, n-way, fully associative
What block is replaced on miss?
  LRU, Random, LFU, …
How are writes handled?
  No-write (w/ or w/o automatic invalidation)
  Write-back (fast, block at time)
  Write-through (simple, reason about consistency)
Notes: Where?
Caches: direct/n-way/fa
VM: fa, but with a table of contents to eliminate searches
TLB: fa
Replacement?
varied
Writes?
Caches: usually write-back, or maybe write-through, or maybe no-write w/ invalidation
VM: write-back
TLB: usually no-write

## Slide 6: Summary of Caches/TLBs/VM
Caches, Virtual Memory, & TLBs: answer three questions
Where can block be placed?
  Caches: direct/n-way/fully associative (fa)
  VM: fa, but with a table of contents to eliminate searches
  TLB: fa
What block is replaced on miss?
  varied
How are writes handled?
  Caches: usually write-back, or maybe write-through, or maybe no-write w/ invalidation
  VM: write-back
  TLB: usually no-write
Notes: Where?
Caches: direct/n-way/fa
VM: fa, but with a table of contents to eliminate searches
TLB: fa
Replacement?
varied
Writes?
Caches: usually write-back, or maybe write-through, or maybe no-write w/ invalidation
VM: write-back
TLB: usually no-write

## Slide 7: Summary of Cache Design Parameters
 | L1 | TLB | Paged Memory
Size (blocks) | 1/4k to 4k | 64 to 4k | 16k to 1M
Size (kB) | 16 to 64 | 2 to 16 | 1M to 4G
Block size (B) | 16-64 | 4-32 | 4k to 64k
Miss rates | 2%-5% | 0.01% to 2% | 10-4 to 10-5%
Miss penalty | 10-25 | 100-1000 | 10M-100M

## Slide 8: Big Picture: Traps, Exceptions, System Calls (OS)
0xfffffffc
0x00000000
top
bottom
0x7ffffffc
0x80000000
0x10000000
0x00400000
system reserved
(stack grows down)
(heap grows up)
text
reserved
(static) data
(.stack)
.data
.text
system reserved
stack
system reserved
code (text)
static data
dynamic data (heap)
.data
.text

## Slide 9: Big Picture: Traps, Exceptions, System Calls (OS)
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard
Stack, Data, Code
Stored in Memory
$0 (zero)
$1 ($at)
$29 ($sp)
$31 ($ra)
Code Stored in Memory
(also, data and stack)
$$
$$

## Slide 10: Big Picture: Traps, Exceptions, System Calls (OS)
What happens with our pipeline if an exception occurs?
What are exceptions?
Any unexpected change in control flow.
Interrupt -> cause of control flow change external (async)
Exception -> cause of control flow change internal (sync)
  Exception: Divide by 0, overflow
  Exception: Bad memory address
  Exception: Page fault
  Interrupt: Hardware interrupt (e.g. keyboard stroke)

## Slide 11: Goals for Today
Exceptions
Hardware/Software Boundary
Privileged mode
Operating System
Exceptions vs Interrupts vs Traps vs Systems calls

## Slide 12: Next Goal
What are exceptions and how are they handled?

## Slide 13: Exceptions
Exceptions are any unexpected change in control flow.
Interrupt -> cause of control flow change external
Exception -> cause of control flow change internal
  Exception: Divide by 0, overflow
  Exception: Bad memory address
  Exception: Page fault
  Interrupt: Hardware interrupt (e.g. keyboard stroke)
We need software to help resolve exceptions
  Exceptions are at the hardware/software boundary

## Slide 14: Hardware/Software Boundary
Virtual to physical address translation is assisted by hardware
Need both hardware and software support
Software
  Page table storage, fault detection and updating
    Page faults result in interrupts that are then handled by the OS
    Must update appropriately Dirty and Reference bits (e.g., ~LRU) in the Page Tables

## Slide 15: Hardware/Software Boundary
OS has to keep TLB valid
Keep TLB valid on context switch
  Flush TLB when new process runs (x86)
  Store process id (MIPs)
Also, store pids with cache to avoid flushing cache on context switches
Hardware support
  Page table register
  Process id register

## Slide 16: Hardware/Software Boundary
Hardware support for exceptions
  Exception program counter (EPC)
  Cause register
  Special instructions to load TLB
    Only do-able by kernel
Precise and imprecise exceptions
  In pipelined architecture
    Have to correctly identify PC of exception
    MIPS and modern processors support this

## Slide 17: Hardware/Software Boundary
Precise exceptions: Hardware guarantees
  (similar to a branch)
  Previous instructions complete
  Later instructions are flushed
  EPC and cause register are set
  Jump to prearranged address in OS
  When you come back, restart instruction
  Disable exceptions while responding to one
    Otherwise can overwrite EPC and cause

## Slide 18: Hardware/Software Boundary
Drawbacks:
  Any program can muck with TLB, PageTables, OS code…
  A program can intercept exceptions of other programs
  OS can crash if program messes up $sp, $fp, $gp, …
Wrong: Make these instructions and registers available only to “OS Code”
  “OS Code” == any code above 0x80000000
  Program can still JAL into middle of OS functions
  Program can still muck with OS memory, pagetables, …

## Slide 19: Anatomy of an Executing Program
0xfffffffc
0x00000000
top
bottom
0x7ffffffc
0x80000000
0x10000000
0x00400000
system reserved
(stack grows down)
(heap grows up)
text
reserved
(static) data
(.stack)
.data
.text
system reserved
stack
system reserved
code (text)
static data
dynamic data (heap)
.data
.text

## Slide 20: Takeaway
Exceptions are any unexpected change in control flow. Precise exceptions are necessary to identify the exceptional instructional, cause of exception, and where to start to continue execution.
We need help of both hardware and software (e.g. OS) to resolve exceptions. Finally, we need some type of protected mode to prevent programs from modifying OS or other programs.

## Slide 21: Next Goal
How do we protect the operating system (OS) from programs? How do we protect programs from one another?

## Slide 22
Privileged Mode
aka Kernel Mode

## Slide 23: Operating System
Some things not available to untrusted programs:
  Exception registers, HALT instruction, MMU instructions, talk to I/O devices, OS memory, ...
Need trusted mediator: Operating System (OS)
  Safe control transfer
  Data isolation
P1
P2
P3
P4
VM
filesystem
net
driver
driver
disk
eth
MMU
untrusted
Notes: user/kernel/hardware

## Slide 24: Privilege Mode
CPU Mode Bit / Privilege Level Status Register
Mode 0 = untrusted = user domain
  “Privileged” instructions and registers are disabled by CPU
Mode 1 = trusted = kernel domain
  All instructions and registers are enabled
Boot sequence:
  load first sector of disk (containing OS code) to well known address in memory
  Mode  1; PC  well known address
OS takes over…
  initialize devices, MMU, timers, etc.
  loads programs from disk, sets up pagetables, etc.
  Mode  0; PC  program entry point
(note: x86 has 4 levels x 3 dimensions, but only virtual machines uses any the middle)
Notes: boot sequence

## Slide 25: Terminology
Trap: Any kind of a control transfer to the OS
Syscall: Synchronous (planned), program-to-kernel transfer
  SYSCALL instruction in MIPS (various on x86)
Exception: Synchronous, program-to-kernel transfer
  exceptional events: div by zero, page fault, page protection err, …
Interrupt: Aysnchronous, device-initiated transfer
  e.g. Network packet arrived, keyboard event, timer ticks
* real mechanisms, but nobody agrees on these terms

## Slide 26: Sample System Calls
System call examples:
putc(): Print character to screen
  Need to multiplex screen between competing programs
send(): Send a packet on the network
  Need to manipulate the internals of a device
sbrk(): Allocate a page
  Needs to update page tables & MMU
sleep(): put current prog to sleep, wake other
  Need to update page table base register

## Slide 27: System Calls
System call: Not just a function call
  Don’t let program jump just anywhere in OS code
  OS can’t trust program’s registers (sp, fp, gp, etc.)
SYSCALL instruction: safe transfer of control to OS
  Mode  0; Cause  syscall; PC  exception vector
MIPS system call convention:
  user program mostly normal (save temps, save ra, …)
  but: $v0 = system call number, which specifies the operation the application is requesting

## Slide 28: Invoking System Calls
int getc() {
asm("addiu $2, $0, 4");
asm("syscall");
}
char *gets(char *buf) {
while (...) {
buf[i] = getc();
}
}

## Slide 29: Libraries and Wrappers
Compilers do not emit SYSCALL instructions
  Compiler doesn’t know OS interface
Libraries implement standard API from system API
libc (standard C library):
  getc()  syscall
  sbrk()  syscall
  write()  syscall
  gets()  getc()
  printf()  write()
  malloc()  sbrk()
  …

## Slide 31: Where does OS live?
In its own address space?
  But then syscall would have to switch to a different address space
  Also harder to deal with syscall arguments passed as pointers
So in the same address space as process
  Use protection bits to prevent user code from writing kernel
  Higher part of VM, lower part of physical memory

## Slide 32: Anatomy of an Executing Program
0xfffffffc
0x00000000
top
bottom
0x7ffffffc
0x80000000
0x10000000
0x00400000
system reserved
(stack grows down)
(heap grows up)
text
reserved
(static) data
(.stack)
.data
.text
system reserved
stack
system reserved
code (text)
static data
dynamic data (heap)
.data
.text

## Slide 33: Full System Layout
Typically all kernel text, most data
  At same VA in every address space
  Map kernel in contiguous physical memory when boot loader puts kernel into physical memory
The OS is omnipresent and steps in where necessary to aid application execution
  Typically resides in high memory
When an application needs to perform a privileged operation, it needs to invoke the OS
OS Text
Stack
Heap
Data
Text
OS Data
OS Heap
OS Stack
0x000…0
0x7ff…f
0xfff…f
0x800…0
Memory

## Slide 34: SYSCALL instruction
SYSCALL instruction does an atomic jump to a controlled location
  Switches the sp to the kernel stack
  Saves the old (user) SP value
  Saves the old (user) PC value (= return address)
  Saves the old privilege mode
  Sets the new privilege mode to 1
  Sets the new PC to the kernel syscall handler

## Slide 35: SYSCALL instruction
Kernel system call handler carries out the desired system call
  Saves callee-save registers
  Examines the syscall number
  Checks arguments for sanity
  Performs operation
  Stores result in v0
  Restores callee-save registers
  Performs a “return from syscall” (ERET) instruction, which restores the privilege mode, SP and PC

## Slide 36: Takeaway
Exceptions are any unexpected change in control flow. Precise exceptions are necessary to identify the exceptional instructional, cause of exception, and where to start to continue execution.
We need help of both hardware and software (e.g. OS) to resolve exceptions. Finally, we need some type of protected mode to prevent programs from modifying OS or other programs.
It is necessary to have a privileged mode (aka kernel mode) where a trusted mediator, the Operating System (OS), provides isolation between programs, protects shared resources, and provides safe control transfer.

## Slide 37: Next Goal
System call is any control transfer into the OS
Similarly, exceptions and interrupts are control transfers into the OS. How does the CPU and OS handle exceptions and interrupts?

## Slide 38
Interrupts

## Slide 39: Recap: Traps
 Map kernel into every process using supervisor PTEs
 Switch to kernel mode on trap, user mode on return
Trap: Any kind of a control transfer to the OS
Syscall: Synchronous, program-to-kernel transfer
  user does caller-saves, invokes kernel via syscall
  kernel handles request, puts result in v0, and returns
Exception: Synchronous, program-to-kernel transfer
  user div/load/store/… faults, CPU invokes kernel
  kernel saves everything, handles fault, restores, and returns
Interrupt: Aysnchronous, device-initiated transfer
  e.g. Network packet arrived, keyboard event, timer ticks
  kernel saves everything, handles event, restores, and returns

## Slide 40: Exceptions
Traps (System calls) are control transfers to the OS, performed under the control of the user program
Sometimes, need to transfer control to the OS at a time when the user program least expects it
  Division by zero,
  Alert from power supply that electricity is going out
  Alert from network device that a packet just arrived
  Clock notifying the processor that clock just ticked
Some of these causes for interruption of execution have nothing to do with the user application
Need a (slightly) different mechanism, that allows resuming the user application

## Slide 41: Interrupts & Exceptions
On an interrupt or exception
  CPU saves PC of exception instruction (EPC)
  CPU Saves cause of the interrupt/privilege (Cause register)
  Switches the sp to the kernel stack
  Saves the old (user) SP value
  Saves the old (user) PC value
  Saves the old privilege mode
  Sets the new privilege mode to 1
  Sets the new PC to the kernel interrupt/exception handler

## Slide 42: Interrupts & Exceptions
Kernel interrupt/exception handler handles the event
  Saves all registers
  Examines the cause
  Performs operation required
  Restores all registers
  Performs a “return from interrupt” instruction, which restores the privilege mode, SP and PC

## Slide 43: Example: Clock Interrupt
Example: Clock Interrupt*
  Every N cycles, CPU causes exception with Cause = CLOCK_TICK
  OS can select N to get e.g. 1000 TICKs per second
.ktext 0x80000180
# (step 1) save *everything* but $k0, $k1 to 0xB0000000
# (step 2) set up a usable OS context
# (step 3) examine Cause register, take action
if (Cause == PAGE_FAULT) handle_pfault(BadVaddr)
else if (Cause == SYSCALL) dispatch_syscall($v0)
else if (Cause == CLOCK_TICK) schedule()
# (step 4) restore registers and return to where program left off
* not the CPU clock, but a programmable timer clock

## Slide 44: Scheduler
struct regs context[];
int ptbr[];
schedule() {
i = current_process;
j = pick_some_process();
if (i != j) {
current_process = j;
memcpy(context[i], 0xB0000000);
memcpy(0xB0000000, context[j]);
asm(“mtc0 Context, ptbr[j]”);
}
}

## Slide 45: Syscall vs. Interrupt
Syscall vs. Exceptions vs. Interrupts
Same mechanisms, but…
Syscall saves and restores much less state
Others save and restore full processor state
Interrupt arrival is unrelated to user code
Notes: most state

## Slide 46: Takeaway
Exceptions are any unexpected change in control flow. Precise exceptions are necessary to identify the exceptional instructional, cause of exception, and where to start to continue execution.
We need help of both hardware and software (e.g. OS) to resolve exceptions. Finally, we need some type of protected mode to prevent programs from modifying OS or other programs.
It is necessary to have a privileged mode (aka kernel mode) where a trusted mediator, the Operating System (OS), provides isolation between programs, protects shared resources, and provides safe control transfer.
To handle any exception or interrupt, OS analyzes the Cause register to vector into the appropriate exception handler. The OS kernel then handles the exception, and returns control to the same process, killing the current process, or possibly scheduling another process.

## Slide 47: Summary
Trap
  Any kind of a control transfer to the OS
Syscall
  Synchronous, program-initiated control transfer from user to the OS to obtain service from the OS
  e.g. SYSCALL
Exception
  Synchronous, program-initiated control transfer from user to the OS in response to an exceptional event
  e.g. Divide by zero, TLB miss, Page fault
Interrupt
  Asynchronous, device-initiated control transfer from user to the OS
  e.g. Network packet, I/O complete