## Slide 1: Synchronization
Hakim Weatherspoon
CS 3410, Spring 2013
Computer Science
Cornell University
P&H Chapter 2.11 and 5.8

## Slide 2: Big Picture: Parallelism and Synchronization
How do I take advantage of multiple processors; parallelism?
How do I write (correct) parallel programs, cache cohrency and synchronization?
What primitives do I need to implement correct parallel programs?

## Slide 3: Goals for Today
Understand Cache Coherency Problem
  Define Cache coherency problem
Synchronizing parallel programs
  Atomic Instructions
  HW support for synchronization
How to write parallel programs
  Threads and processes
  Critical sections, race conditions, and mutexes

## Slide 4: Big Picture: Parallelism and Synchronization

## Slide 5: Next Goal: Parallelism and Synchronization
Cache Coherency Problem: What happens when to two or more processors cache shared data?

## Slide 6: Next Goal: Parallelism and Synchronization
Cache Coherency Problem: What happens when to two or more processors cache shared data?
i.e. the view of memory held by two different processors is through their individual caches.
As a result, processors can see different (incoherent) values to the same memory location.

## Slide 7: Big Picture: Parallelism and Synchronization
Each processor core has its own L1 cache

## Slide 8: Big Picture: Parallelism and Synchronization
Each processor core has its own L1 cache

## Slide 9: Big Picture: Parallelism and Synchronization
Each processor core has its own L1 cache
Core0
Cache
Memory
I/O
Interconnect
Core1
Cache
Core3
Cache
Core2
Cache

## Slide 10: Shared Memory Multiprocessors
Shared Memory Multiprocessor (SMP)
  Typical (today): 2 – 4 processor dies, 2 – 8 cores each
  HW provides single physical address space for all processors
  Assume physical addresses (ignore virtual memory)
  Assume uniform memory access (ignore NUMA)
Core0
Cache
Memory
I/O
Interconnect
Core1
Cache
Core3
Cache
Core2
Cache
Notes: How do they share data? How do they coordinate? How do they scale?

## Slide 11: Shared Memory Multiprocessors
Shared Memory Multiprocessor (SMP)
  Typical (today): 2 – 4 processor dies, 2 – 8 cores each
  HW provides single physical address space for all processors
  Assume physical addresses (ignore virtual memory)
  Assume uniform memory access (ignore NUMA)
...
Core0
Cache
Memory
I/O
Interconnect
Core1
Cache
CoreN
Cache
...
...
Notes: How do they share data? How do they coordinate? How do they scale?

## Slide 12: Cache Coherency Problem
...
Core0
Cache
Memory
I/O
Interconnect
Core1
Cache
CoreN
Cache
...
...
Thread A (on Core0) Thread B (on Core1) for(int i = 0, i < 5; i++) { for(int j = 0; j < 5; j++) { x = x + 1; x = x + 1; } }
What will the value of x be after both loops finish?
Notes: How do they share data? How do they coordinate? How do they scale?

## Slide 13: Cache Coherency Problem
Thread A (on Core0) Thread B (on Core1) for(int i = 0, i < 5; i++) { for(int j = 0; j < 5; j++) { x = x + 1; x = x + 1; } }
What will the value of x be after both loops finish?
6
8
10
All of the above
None of the above
Notes: How do they share data? How do they coordinate? How do they scale?

## Slide 14: Cache Coherency Problem
...
Core0
Cache
Memory
I/O
Interconnect
Core1
Cache
CoreN
Cache
...
...
Thread A (on Core0) Thread B (on Core1) for(int i = 0, i < 5; i++) { for(int j = 0; j < 5; j++) { LW $t0, addr(x) LW $t0, addr(x)
ADDIU $t0, $t0, 1 ADDIU $t0, $t0, 1
SW $t0, addr(x) SW $t0, addr(x) } }
$t0=0
$t0=1
x=1
$t0=0
$t0=1
x=1
x should be greater than 1 after both threads loop at least once!
Notes: How do they share data? How do they coordinate? How do they scale?

## Slide 15: Cache Coherence Problem
Time step | Event | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  | 0
Suppose two CPU cores share a physical address space
  Write-through caches
Time step | Event | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  | 0
1 | CPU A reads X | 0 |  | 0
Time step | Event | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  | 0
1 | CPU A reads X | 0 |  | 0
2 | CPU B reads X | 0 | 0 | 0
Time step | Event | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  | 0
1 | CPU A reads X | 0 |  | 0
2 | CPU B reads X | 0 | 0 | 0
3 | CPU A writes 1 to X | 1 | 0 | 1
...
Core0
Cache
Memory
I/O
Interconnect
Core1
Cache
CoreN
Cache
...
...

## Slide 16: Coherence Defined
Cache coherence defined...
Informal: Reads return most recently written value
Formal: For concurrent processes P1 and P2
  P writes X before P reads X (with no intervening writes)  read returns written value
  P1 writes X before P2 reads X  read returns written value
  P1 writes X and P2 writes X  all processors see writes in the same order
    all see the same final value for X
    Aka write serialization
Notes: second case: for some definition of “before”
third case: see relativity
complication: clocks are not synchronized across cores
1 light nanosecond = 30cm, so 3GHz can do 1 instruction per 10cm

## Slide 17: Cache Coherence Protocols
Operations performed by caches in multiprocessors to ensure coherence
  Migration of data to local caches
    Reduces bandwidth for shared memory
  Replication of read-shared data
    Reduces contention for access
Snooping protocols
  Each cache monitors bus reads/writes

## Slide 18: Snooping
Snooping for Hardware Cache Coherence
  All caches monitor bus and all other caches
  Bus read: respond if you have dirty data
  Bus write: update/invalidate your copy of data
Snoop
Snoop
Snoop
...
Core0
Cache
Memory
I/O
Interconnect
...
...
Snoop
Core1
Cache
Snoop
CoreN
Cache
Snoop
Notes: In reality: very complicated, lots of corner cases

## Slide 19: Invalidating Snooping Protocols
Cache gets exclusive access to a block when it is to be written
  Broadcasts an invalidate message on the bus
  Subsequent read in another cache misses
    Owning cache supplies updated value
Time Step | CPU activity | Bus activity | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  |  | 0
Time Step | CPU activity | Bus activity | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  |  | 0
1 | CPU A reads X | Cache miss for X | 0 |  | 0
Time Step | CPU activity | Bus activity | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  |  | 0
1 | CPU A reads X | Cache miss for X | 0 |  | 0
2 | CPU B reads X | Cache miss for X | 0 | 0 | 0
Time Step | CPU activity | Bus activity | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  |  | 0
1 | CPU A reads X | Cache miss for X | 0 |  | 0
2 | CPU B reads X | Cache miss for X | 0 | 0 | 0
3 | CPU A writes 1 to X | Invalidate for X | 1 |  | 0
Time Step | CPU activity | Bus activity | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  |  | 0
1 | CPU A reads X | Cache miss for X | 0 |  | 0
2 | CPU B reads X | Cache miss for X | 0 | 0 | 0
3 | CPU A writes 1 to X | Invalidate for X | 1 |  | 0
4 | CPU B read X | Cache miss for X | 1 | 1 | 1

## Slide 20: Writing
Write-back policies for bandwidth
Write-invalidate coherence policy
  First invalidate all other copies of data
  Then write it in cache line
  Anybody else can read it
Permits one writer, multiple readers
In reality: many coherence protocols
  Snooping doesn’t scale
  Directory-based protocols
    Caches and memory record sharing status of blocks in a directory

## Slide 21: Takeaway
Informally, Cache Coherency requires that reads return most recently written value.
With multiprocessors maintaining cache coherency can be difficult and requires cache coherency protocols like Snooping cache coherency protocols.

## Slide 22: Next Goal: Synchronization
Is cache coherency sufficient?
i.e. Is cache coherency (what values are read) sufficient to maintain consistency (when a written value will be returned to a read). Both coherency and consistency are required to maintain consistency in shared memory programs.

## Slide 23: Is Cache Coherency Sufficient?
...
Core0
Cache
Memory
I/O
Interconnect
Core1
Cache
CoreN
Cache
...
...
Thread A (on Core0) Thread B (on Core1) for(int i = 0, i < 5; i++) { for(int j = 0; j < 5; j++) { LW $t0, addr(x) LW $t0, addr(x)
ADDIU $t0, $t0, 1 ADDIU $t0, $t0, 1
SW $t0, addr(x) SW $t0, addr(x) } }
Very expensive and difficult to maintain consistency
Notes: Is cache coherence enough? Maybe?
read (1) 40 read (3) 40
Inc (2) 41 inc (4) 41
Write (5) 41 write (6) 41
second case: for some definition of “before”
third case: see relativity
complication: clocks are not synchronized across cores
1 light nanosecond = 30cm, so 3GHz can do 1 instruction per 10cm

## Slide 24: Synchronization
Two processors sharing an area of memory
  P1 writes, then P2 reads
  Data race if P1 and P2 don’t synchronize
    Result depends of order of accesses
Hardware support required
  Atomic read/write memory operation
  No other access to the location allowed between the read and write
Could be a single instruction
  E.g., atomic swap of register ↔ memory (e.g. ATS, BTS; x86)
  Or an atomic pair of instructions (e.g. LL and SC; MIPS)

## Slide 25: Synchronization in MIPS
Load linked: LL rt, offset(rs)
Store conditional: SC rt, offset(rs)
  Succeeds if location not changed since the LL
    Returns 1 in rt
  Fails if location is changed
    Returns 0 in rt
Example: atomic swap (to test/set lock variable)
  try: MOVE $t0,$s4 ;copy exchange value
  LL $t1,0($s1) ;load linked
  SC $t0,0($s1) ;store conditional
  BEQZ $t0,try ;branch store fails
  MOVE $s4,$t1 ;put load value in $s4
Any time a processor intervenes and modifies the value in memory between the LL and SC instruction, the SC returns 0 in $t0, causing the code to try again.

## Slide 26: Mutex from LL and SC
Linked load / Store Conditional
m = 0; // m=0 means lock is free; otherwise, if m=1, then lock locked
mutex_lock(int *m) {
while(test_and_test(m)){}
}
int test_and_set(int *m) {
old = *m;
*m = 1;
return old;
}
LL Atomic
SC
Notes: LL just like LW
SC jus like SW, but overwrites src register with 1 “success” or 0 “fail”

## Slide 27: Mutex from LL and SC
Linked load / Store Conditional
m =0;
mutex_lock(int *m) {
while(test_and_test(m)){}
}
int test_and_set(int *m) {
LI $t0, 1
LL $t1, 0($a0)
SC $t0, 0($a0)
MOVE $v0, $t1
}
BEQZ $t0, try
try:
Notes: LL just like LW
SC jus like SW, but overwrites src register with 1 “success” or 0 “fail”

## Slide 28: Mutex from LL and SC
Linked load / Store Conditional
mutex_lock(int *m) {
while(test_and_test(m)){}
}
int test_and_set(int *m) {
try:
LI $t0, 1
LL $t1, 0($a0)
SC $t0, 0($a0)
BEQZ $t0, try
MOVE $v0, $t1
}
Notes: LL just like LW
SC jus like SW, but overwrites src register with 1 “success” or 0 “fail”

## Slide 29: Mutex from LL and SC
Linked load / Store Conditional
mutex_lock(int *m) {
test_and_set:
LI $t0, 1
LL $t1, 0($a0)
BNEZ $t1, test_and_set
SC $t0, 0($a0)
BEQZ $t0, test_and_set
}
mutex_unlock(int *m) {
*m = 0;
}
Notes: LL just like LW
SC jus like SW, but overwrites src register with 1 “success” or 0 “fail”

## Slide 30: Mutex from LL and SC
Linked load / Store Conditional
mutex_lock(int *m) {
test_and_set:
LI $t0, 1
LL $t1, 0($a0)
BNEZ $t1, test_and_set
SC $t0, 0($a0)
BEQZ $t0, test_and_set
}
mutex_unlock(int *m) {
SW $zero, 0($a0)
}
This is called a
Spin lock
Aka spin waiting
Notes: LL just like LW
SC jus like SW, but overwrites src register with 1 “success” or 0 “fail”

## Slide 31: Alternative Atomic Instructions
Other atomic hardware primitives
- test and set (x86)
- atomic increment (x86)
- bus lock prefix (x86)
- compare and exchange (x86, ARM deprecated)
- linked load / store conditional (MIPS, ARM, PowerPC, DEC Alpha, …)
Notes: hardware implementation: lock bus while read-modify-write cycle happens, very expensive

## Slide 32: Now we can write parallel and correct programs
Thread A Thread B for(int i = 0, i < 5; i++) { for(int j = 0; j < 5; j++) {
x = x + 1; x = x + 1;
} }
mutex_lock(m); mutex_lock(m);
mutex_unlock(m); mutex_unlock(m);
Notes: Can be done using lock,
Also can be done using atomic increment.

## Slide 33: Takeaway
Informally, Cache Coherency requires that reads return most recently written value.
With multiprocessors maintaining cache coherency can be difficult and requires cache coherency protocols like Snooping cache coherency protocols.
Cache coherency controls what values are read, but may be insufficient or very expensive to maintain consistency (when a written value will be returned to a read). We need synchronization primitives to more efficiently implement parallel and correct programs.

## Slide 34: Next Goal
How do we write parallel programs?

## Slide 35: Processes
How do we cope with lots of activity?
Simplicity? Separation into processes
Reliability? Isolation
Speed? Program-level parallelism
gcc
emacs
nfsd
lpr
ls
www
emacs
nfsd
lpr
ls
www
OS
OS
Notes: (isolation e.g. virtual memory)
(parallelism e.g. during I/O)

## Slide 36: Process and Program
Process
OS abstraction of a running computation
  The unit of execution
  The unit of scheduling
  Execution state + address space
From process perspective
  a virtual CPU
  some virtual memory
  a virtual keyboard, screen, …
Program
“Blueprint” for a process
  Passive entity (bits on disk)
  Code + static data
Header
Code
Initialized data
BSS
Symbol table
Line numbers
Ext. refs
Notes: A virtual machine of sorts
Draw saved PTBR and Registers table

## Slide 37: Process and Program
Code
Initialized data
BSS
Heap
Stack
DLL’s
mapped segments
Header
Code
Initialized data
BSS
Symbol table
Line numbers
Ext. refs
Program
Process

## Slide 38: Role of the OS
Role of the OS
Context Switching
  Provides illusion that every process owns a CPU
Virtual Memory
  Provides illusion that process owns some memory
Device drivers & system calls
  Provides illusion that process owns a keyboard, …
To do:
How to start a process?
How do processes communicate / coordinate?
Notes: Draw OS on next slide

## Slide 39: How to create a process?
Q: How to create a process?
A: Double click
After boot, OS starts the first process
…which in turn creates other processes
  parent / child  the process tree
Notes: 1st process = init

## Slide 40: pstree example
$ pstree | view -
init-+-NetworkManager-+-dhclient
|-apache2
|-chrome-+-chrome
| `-chrome
|-chrome---chrome
|-clementine
|-clock-applet
|-cron
|-cupsd
|-firefox---run-mozilla.sh---firefox-bin-+-plugin-cont
|-gnome-screensaver
|-grep
|-in.tftpd
|-ntpd
`-sshd---sshd---sshd---bash-+-gcc---gcc---cc1
|-pstree
|-vim
`-view

## Slide 41: Processes Under UNIX
Init is a special case. For others…
Q: How does parent process create child process?
A: fork() system call
Wait. what? int fork() returns TWICE!
Notes: 1. creates new address space (Copy-On-Write duplicate of parent’s)
2. creates new execution state in OS process table (Exact copy of parent’s)
3. returns child’s id to parent (context[parent_id]->v0 = child_id)
4. returns zero to child (context[child_id]->v0 = 0)

## Slide 42: Example
main(int ac, char **av) {
int x = getpid(); // get current process ID from OS
char *hi = av[1]; // get greeting from command line
printf(“I’m process %d\n”, x);
int id = fork();
if (id == 0)
printf(“%s from %d\n”, hi, getpid());
else
printf(“%s from %d, child is %d\n”, hi, getpid(), id);
}
$ gcc -o strange strange.c
$ ./strange “Hey”
I’m process 23511
Hey from 23512
Hey from 23511, child is 23512
Notes: Draw OS state

## Slide 43: Inter-process Communication
Parent can pass information to child
  In fact, all parent data is passed to child
  But isolated after (C-O-W ensures changes are invisible)
Q: How to continue communicating?
A: Invent OS “IPC channels” : send(msg), recv(), …
Notes: IPC = inter-process communication
sockets, RMI, ipc, unix-domain sockets, pipes

## Slide 44: Inter-process Communication
Parent can pass information to child
  In fact, all parent data is passed to child
  But isolated after (C-O-W ensures changes are invisible)
Q: How to continue communicating?
A: Shared (Virtual) Memory!
Notes: Before fork: allocate pages, mark as “shared”
During fork: don’t set copy-on-write for these pages
After fork: either can read/write

## Slide 45
Processes and Threads

## Slide 46: Processes are heavyweight
Parallel programming with processes:
  They share almost everything code, shared mem, open files, filesystem privileges, …
  Pagetables will be almost identical
  Differences: PC, registers, stack
Recall: process = execution context + address space
Notes: pstree example: Firefox downloader, renderer, toolbar, etc.
Idea: multiple execution contexts sharing a single address space!

## Slide 47: Processes and Threads
Process
OS abstraction of a running computation
  The unit of execution
  The unit of scheduling
  Execution state + address space
From process perspective
  a virtual CPU
  some virtual memory
  a virtual keyboard, screen, …
Thread
OS abstraction of a single thread of control
  The unit of scheduling
  Lives in one single process
From thread perspective
  one virtual CPU core on a virtual multi-core machine
Notes: d/Unit of scheduling/
s/execution state/one or more threads/
s/virtual CPU/virtual multi-core machine/

## Slide 48: Multithreaded Processes

## Slide 49: Threads
#include <pthread.h>
int counter = 0;
void PrintHello(int arg) {
printf(“I’m thread %d, counter is %d\n”, arg, counter++);
... do some work ...
pthread_exit(NULL);
}
int main () {
for (t = 0; t < 4; t++) {
printf(“in main: creating thread %d\n", t);
pthread_create(NULL, NULL, PrintHello, t);
}
pthread_exit(NULL);
}

## Slide 50: Threads versus Fork
in main: creating thread 0
I’m thread 0, counter is 0
in main: creating thread 1
I’m thread 1, counter is 1
in main: creating thread 2
in main: creating thread 3
I’m thread 3, counter is 2
I’m thread 2, counter is 3
If processes?

## Slide 51: Example Multi-Threaded Program
Example: Apache web server
void main() { setup();
while (c = accept_connection()) {
req = read_request(c);
hits[req]++; send_response(c, req);
}
cleanup();
}
Notes: Use fork
Use threads

## Slide 52: Race Conditions
Example: Apache web server
Each client request handled by a separate thread (in parallel)
  Some shared state: hit counter, ...
(look familiar?)
Timing-dependent failure  race condition
  hard to reproduce  hard to debug
Thread 52
...
hits = hits + 1;
...
Thread 205
...
hits = hits + 1;
...
Thread 52
read hits
addi
write hits
Thread 205
read hits
addi
write hits
Notes: What happens when two threads execute concurrently?
sequential with threads
between threads is unsynchronized

## Slide 53: Programming with threads
Within a thread: execution is sequential
Between threads?
  No ordering or timing guarantees
  Might even run on different cores at the same time
Problem: hard to program, hard to reason about
  Behavior can depend on subtle timing differences
  Bugs may be impossible to reproduce
Cache coherency isn’t sufficient…
Need explicit synchronization to make sense of concurrency!

## Slide 54: Race conditions
Race Condition
Timing-dependent error when accessing shared state
  Depends on scheduling happenstance … e.g. who wins “race” to the store instruction?
Concurrent Program Correctness = all possible schedules are safe
  Must consider every possible permutation
  In other words…
… the scheduler is your adversary

## Slide 55: Critical sections
What if we can designate parts of the execution as critical sections
  Rule: only one thread can be “inside”
Thread 52
read hits
addi
write hits
Thread 205
read hits
addi
write hits
Notes: Show picture

## Slide 56: Mutexes
Q: How to implement critical section in code?
A: Lots of approaches….
Mutual Exclusion Lock (mutex)
acquire(m): wait till it becomes free, then lock it
release(m): unlock it
apache_got_hit() {
pthread_mutex_lock(m);
hits = hits + 1;
pthread_mutex_unlock(m)
}

## Slide 57: Takeaway
Informally, Cache Coherency requires that reads return most recently written value.
With multiprocessors maintaining cache coherency can be difficult and requires cache coherency protocols like Snooping cache coherency protocols.
Cache coherency controls what values are read, but may be insufficient or very expensive to maintain consistency (when a written value will be returned to a read). We need synchronization primitives to more efficiently implement parallel and correct programs.
Processes and Threads are the abstraction that we use to write parallel programs? Fork and Joint and Interprocesses communication (IPC) can be used to coordinate processes. Threads are used to coordinate use of shared memory within a process.

## Slide 58: Next time
Next time. Higher level synchronization primitives (other abstractions to implement a critical section beyond mutexes)?
Notes: A: next time…

## Slide 59: Administrivia
Project3 due next week, Monday, April 22nd
  Design Doc due yesterday, Monday, April 15th
  Games night Friday, April 26th, 5-7pm.
  Location: B17 Upson
Homework4 is due tomorrow, Wednesday, April 17th
  Work alone
  Question1 on Virtual Memory is pre-lab question for Lab4
Prelim3 is next week, Thursday, April 25th
  Time and Location: 7:30pm in Phillips 101 and Upson B17
  Old prelims are online in CMS

## Slide 60: Administrivia
Next three weeks
  Week 12 (Apr 15): Project3 design doc due and HW4 due
  Week 13 (Apr 22): Project3 due and Prelim3
  Week 14 (Apr 29): Project4 handout
Final Project for class
  Week 15 (May 6): Project4 design doc due
  Week 16 (May 13): Project4 due