## Slide 1: Synchronization II
Hakim Weatherspoon
CS 3410, Spring 2013
Computer Science
Cornell University
P&H Chapter 2.11

## Slide 2: Goals for Today
Synchronization
  Threads and processes
  Critical sections, race conditions, and mutexes
  Atomic Instructions
    HW support for synchronization
    Using sync primitives to build concurrency-safe data structures
    Cache coherency causes problems
    Locks + barriers
  Language level synchronization

## Slide 3: Next Goal
Understanding challenges of taking advantage of parallel processors and resources?
i.e. Challenges in parallel programming!

## Slide 4: Programming with Threads
Need it to exploit multiple processing units
…to provide interactive applications
…to parallelize for multicore
…to write servers that handle many clients
Problem: hard even for experienced programmers
  Behavior can depend on subtle timing differences
  Bugs may be impossible to reproduce
Needed: synchronization of threads

## Slide 5: Programming with Threads
Concurrency poses challenges for:
Correctness
  Threads accessing shared memory should not interfere with each other
Liveness
  Threads should not get stuck, should make forward progress
Efficiency
  Program should make good use of available computing resources (e.g., processors).
Fairness
  Resources apportioned fairly between threads

## Slide 6: Two threads, one counter
Example: Web servers use concurrency
Multiple threads handle client requests in parallel.
Some shared state, e.g. hit counts:
  each thread increments a shared counter to track number of hits
What happens when two threads execute concurrently?
…
hits = hits + 1;
…
…
LW R0, addr(hits)
ADDI R0, r0, 1
SW R0, addr(hits)
…

## Slide 7: Two threads, one counters
Possible result: lost update!
Timing-dependent failure  race condition
  Very hard to reproduce  Difficult to debug
ADDIU/SW: hits = 0 + 1
LW (0)
ADDIU/SW: hits = 0 + 1
LW (0)
T1
T2
hits = 1
hits = 0
time

## Slide 8: Race conditions
Def: timing-dependent error involving access to shared state
Whether a Race condition happens depends on
  how threads scheduled
  i.e. who wins “races” to instruction that updates state vs. instruction that accesses state
Challenges about Race conditions
  Races are intermittent, may occur rarely
  Timing dependent = small changes can hide bug
A program is correct only if all possible schedules are safe
  Number of possible schedule permutations is huge
  Need to imagine an adversary who switches contexts at the worst possible time

## Slide 9: Takeaway
Need parallel abstraction like threads to take advantage of parallel resources like multicore. Writing parallel programs are hard to get right! Need to prevent data races, timing dependent updates that result in errors in programs.

## Slide 10: Next Goal
How to prevent data races and write correct parallel programs?

## Slide 11: Critical sections
To eliminate races: use critical sections that only one thread can be in
  Contending threads must wait to enter
CSEnter();
  Critical section
CSExit();
T1
T2
time
CSEnter();
  # wait
  # wait
  Critical section
CSExit();
T1
T2

## Slide 12: Mutexes
Critical sections typically associated with mutual exclusion locks (mutexes)
Only one thread can hold a given mutex at a time
Acquire (lock) mutex on entry to critical section
  Or block if another thread already holds it
Release (unlock) mutex on exit
  Allow one waiting thread (if any) to acquire & proceed
pthread_mutex_lock(&m);
  hits = hits+1;
pthread_mutex_unlock(&m);
T1
T2
pthread_mutex_lock(&m);
# wait
# wait
  hits = hits+1;
pthread_mutex_unlock(&m);
pthread_mutex_init(&m);

## Slide 13: Takeaway
Need parallel abstraction like threads to take advantage of parallel resources like multicore. Writing parallel programs are hard to get right! Need to prevent data races, timing dependent updates that result in errors in programs.
Need critical sections where prevent data races and write parallel safe programs. Mutex, mutual exclusion, can be used to implement critical sections, often implemented via a lock abstraction.

## Slide 14: Next Goal
How to implement mutex locks?
What are the hardware primitives?
Then, use these mutex locks to implement critical sections, and use critical sections to write parallel safe programs.

## Slide 15: Mutexes
Q: How to implement critical section in code?

## Slide 16: Synchronization in MIPS
Load linked: LL rt, offset(rs)
Store conditional: SC rt, offset(rs)
  Succeeds if location not changed since the LL
    Returns 1 in rt
  Fails if location is changed
    Returns 0 in rt
Any time a processor intervenes and modifies the value in memory between the LL and SC instruction, the SC returns 0 in $t0, causing the code to try again.

## Slide 17: Synchronization in MIPS
Time Step | Thread A | Thread B | Thread A $t0 | Thread B $t0 | Memory M[$s0]
0 |  |  |  |  | 0
1 | try: LL $t0, 0($s0) | try: LL $t0, 0($s0) |  |  | 
2 | ADDIU $t0, $t0, 1 | ADDIU $t0, $t0, 1 |  |  | 
3 | SC $t0, 0($s0) | SC $t0, 0 ($s0) |  |  | 
4 | BEQZ $t0, try | BEQZ $t0, try |  |  | 
Load linked: LL rt, offset(rs)
Store conditional: SC rt, offset(rs)
  Succeeds if location not changed since the LL
    Returns 1 in rt
  Fails if location is changed
    Returns 0 in rt
Example: atomic incrementor

## Slide 18: Mutex from LL and SC
Linked load / Store Conditional
m = 0; // m=0 means lock is free; otherwise, if m=1, then lock locked
mutex_lock(int *m) {
while(test_and_set(m)){}
}
int test_and_set(int *m) {
old = *m;
*m = 1;
return old;
}
LL Atomic
SC
Notes: LL just like LW
SC jus like SW, but overwrites src register with 1 “success” or 0 “fail”

## Slide 19: Mutex from LL and SC
Linked load / Store Conditional
m = 0;
mutex_lock(int *m) {
while(test_and_set(m)){}
}
int test_and_set(int *m) {
LI $t0, 1
LL $t1, 0($a0)
SC $t0, 0($a0)
MOVE $v0, $t1
}
BEQZ $t0, try
try:
Notes: LL just like LW
SC jus like SW, but overwrites src register with 1 “success” or 0 “fail”

## Slide 20: Mutex from LL and SC
Linked load / Store Conditional
m = 0;
mutex_lock(int *m) {
while(test_and_set(m)){}
}
int test_and_set(int *m) {
try:
LI $t0, 1
LL $t1, 0($a0)
SC $t0, 0($a0)
BEQZ $t0, try
MOVE $v0, $t1
}
Notes: LL just like LW
SC jus like SW, but overwrites src register with 1 “success” or 0 “fail”

## Slide 21: Mutex from LL and SC
Linked load / Store Conditional
m = 0;
mutex_lock(int *m) {
test_and_set:
LI $t0, 1
LL $t1, 0($a0)
BNEZ $t1, test_and_set
SC $t0, 0($a0)
BEQZ $t0, test_and_set
}
mutex_unlock(int *m) {
*m = 0;
}
Notes: LL just like LW
SC jus like SW, but overwrites src register with 1 “success” or 0 “fail”

## Slide 22: Mutex from LL and SC
Linked load / Store Conditional
m = 0;
mutex_lock(int *m) {
test_and_set:
LI $t0, 1
LL $t1, 0($a0)
BNEZ $t1, test_and_set
SC $t0, 0($a0)
BEQZ $t0, test_and_set
}
mutex_unlock(int *m) {
SW $zero, 0($a0)
}
This is called a
Spin lock
Aka spin waiting
Notes: LL just like LW
SC jus like SW, but overwrites src register with 1 “success” or 0 “fail”

## Slide 23: Mutex from LL and SC
Linked load / Store Conditional
m = 0;
mutex_lock(int *m) {
Time Step | Thread A | Thread B | ThreadA $t0 | ThreadA $t1 | ThreadB $t0 | ThreadB $t1 | Mem M[$a0]
0 |  |  |  |  |  |  | 0
1 | try: LI $t0, 1 | try: LI $t0, 1 |  |  |  |  | 
2 | LL $t1, 0($a0) | LL $t1, 0($a0) |  |  |  |  | 
3 | BNEZ $t1, try | BNEZ $t1, try |  |  |  |  | 
4 | SC $t0, 0($a0) | SC $t0, 0 ($a0) |  |  |  |  | 
5 | BEQZ $t0, try | BEQZ $t0, try |  |  |  |  | 
6 |  |  |  |  |  |  | 
Notes: LL just like LW
SC jus like SW, but overwrites src register with 1 “success” or 0 “fail”

## Slide 24: Mutex from LL and SC
Linked load / Store Conditional
m = 0;
mutex_lock(int *m) {
Time Step | Thread A | Thread B | ThreadA $t0 | ThreadA $t1 | ThreadB $t0 | ThreadB $t1 | Mem M[$a0]
0 |  |  |  |  |  |  | 1
1 | try: LI $t0, 1 | try: LI $t0, 1 |  |  |  |  | 
2 |  |  |  |  |  |  | 
3 |  |  |  |  |  |  | 
4 |  |  |  |  |  |  | 
5 |  |  |  |  |  |  | 
6 |  |  |  |  |  |  | 
7 |  |  |  |  |  |  | 
8 |  |  |  |  |  |  | 
9 |  |  |  |  |  |  | 
Notes: LL just like LW
SC jus like SW, but overwrites src register with 1 “success” or 0 “fail”

## Slide 25: Alternative Atomic Instructions
Other atomic hardware primitives
- test and set (x86)
- atomic increment (x86)
- bus lock prefix (x86)
- compare and exchange (x86, ARM deprecated)
- linked load / store conditional (MIPS, ARM, PowerPC, DEC Alpha, …)
Notes: hardware implementation: lock bus while read-modify-write cycle happens, very expensive

## Slide 26: Synchronization
Synchronization techniques
clever code
  must work despite adversarial scheduler/interrupts
  used by: hackers
  also: noobs
disable interrupts
  used by: exception handler, scheduler, device drivers, …
disable preemption
  dangerous for user code, but okay for some kernel code
mutual exclusion locks (mutex)
  general purpose, except for some interrupt-related cases
Notes: device drivers if interrupts always go to same core

## Slide 27: Takeaway
Need parallel abstraction like threads to take advantage of parallel resources like multicore. Writing parallel programs are hard to get right! Need to prevent data races, timing dependent updates that result in errors in programs.
Need critical sections where prevent data races and write parallel safe programs. Mutex, mutual exclusion, can be used to implement critical sections, often implemented via a lock abstraction.
We need synchronization primitives such as LL and SC (load linked and store conditional) instructions to efficiently implement parallel and correct programs.

## Slide 28: Next Goal
How do we use synchronization primitives to build concurrency-safe data structure?

## Slide 29: Attempt#1: Producer/Consumer
Access to shared data must be synchronized
  goal: enforce datastructure invariants
// invariant: // data is in A[h … t-1]
char A[100];
int h = 0, t = 0;
// producer: add to list tail
void put(char c) {
A[t] = c;
t = (t+1)%n;
}
1
2
3
head
tail
Notes: draw picture
invariant broken just before last/first increments
needs: make the list into a ring buffer, add code in writer to wait if list is full

## Slide 30: Attempt#1: Producer/Consumer
Access to shared data must be synchronized
  goal: enforce datastructure invariants
// invariant: // data is in A[h … t-1]
char A[100];
int h = 0, t = 0;
// producer: add to list tail
void put(char c) {
A[t] = c;
t = (t+1)%n;
}
// consumer: take from list head
char get() {
while (h == t) { };
char c = A[h];
h = (h+1)%n;
return c;
}
1
2
3
4
head
tail
Notes: draw picture
invariant broken just before last/first increments
needs: make the list into a ring buffer, add code in writer to wait if list is full

## Slide 31: Attempt#1: Producer/Consumer
Access to shared data must be synchronized
  goal: enforce datastructure invariants
// invariant: // data is in A[h … t-1]
char A[100];
int h = 0, t = 0;
// producer: add to list tail
void put(char c) {
A[t] = c;
t = (t+1)%n;
}
// consumer: take from list head
char get() {
while (h == t) { };
char c = A[h];
h = (h+1)%n;
return c;
}
2
3
4
head
tail
Error: could miss an update to t or h due to lack of synchronization
Current implementation will break invariant:
only produce if not full and only consume if not empty
Need to synchronize access to shared data
Notes: draw picture
invariant broken just before last/first increments
needs: make the list into a ring buffer, add code in writer to wait if list is full

## Slide 32: Attempt#2: Protecting an invariant
Rule of thumb: all access and updates that can affect invariant become critical sections
// invariant: (protected by mutex m) // data is in A[h … t-1]
pthread_mutex_t *m = pthread_mutex_create();
char A[100];
int h = 0, t = 0;
// producer: add to list tail
void put(char c) {
pthread_mutex_lock(m);
A[t] = c;
t = (t+1)%n;
pthread_mutex_unlock(m);
}
// consumer: take from list head
char get() {
pthread_mutex_lock(m);
while(h == t) {}
char c = A[h];
h = (h+1)%n;
pthread_mutex_unlock(m);
return c;
}
Notes: bug: can’t do busy waiting inside mutex… what to do?

## Slide 33: Guidelines for successful mutexing
Insufficient locking can cause races
  Skimping on mutexes? Just say no!
Poorly designed locking can cause deadlock
  know why you are using mutexes!
  acquire locks in a consistent order to avoid cycles
  use lock/unlock like braces (match them lexically)
    lock(&m); …; unlock(&m)
    watch out for return, goto, and function calls!
    watch out for exception/error conditions!
  P1: lock(m1); lock(m2);
  P2: lock(m2); lock(m1);
Circular
Wait

## Slide 34: Attempt#3: Beyond mutexes
Writers must check for full buffer & Readers must check if for empty buffer
  ideal: don’t busy wait… go to sleep instead
char get() {
acquire(L);
char c = A[h];
h = (h+1)%n;
release(L);
return c;
}
head
last==head
empty
while(empty) {}

## Slide 35: Attempt#3: Beyond mutexes
Writers must check for full buffer & Readers must check if for empty buffer
  ideal: don’t busy wait… go to sleep instead
char get() {
acquire(L);
char c = A[h];
h++;
release(L);
return c;
}
char get() {
acquire(L);
while (h == t) { };
char c = A[h];
h = (h+1)%n;
release(L);
return c;
}
Dilemma: Have to check while holding lock,
but cannot wait while hold lock

## Slide 36: Attempt#4: Beyond mutexes
Writers must check for full buffer & Readers must check if for empty buffer
  ideal: don’t busy wait… go to sleep instead
char get() {
do {
acquire(L);
empty = (h == t);
if (!empty) {
c = A[h];
h = (h+1)%n;
}
release(L);
} while (empty);
return c;
}
Notes: Works, but wasteful sin will spin wait

## Slide 37
Language-level Synchronization

## Slide 38: Condition variables
Use [Hoare] a condition variable to wait for a condition to become true (without holding lock!)
wait(m, c) :
  atomically release m and sleep, waiting for condition c
  wake up holding m sometime after c was signaled
signal(c) : wake up one thread waiting on c
broadcast(c) : wake up all threads waiting on c
POSIX (e.g., Linux): pthread_cond_wait, pthread_cond_signal, pthread_cond_broadcast

## Slide 39: Attempt#5: Using a condition variable
wait(m, c) : release m, sleep until c, wake up holding m
signal(c) : wake up one thread waiting on c
char get() {
lock(m);
while (t == h)
wait(m, not_empty);
char c = A[h];
h = (h+1) % n;
unlock(m);
signal(not_full);
return c;
}
cond_t *not_full = ...;
cond_t *not_empty = ...;
mutex_t *m = ...;
void put(char c) {
lock(m);
while ((t-h) % n == 1)
wait(m, not_full);
A[t] = c;
t = (t+1) % n;
unlock(m);
signal(not_empty);
}

## Slide 40: Monitors
A Monitor is a concurrency-safe datastructure, with…
  one mutex
  some condition variables
  some operations
All operations on monitor acquire/release mutex
  one thread in the monitor at a time
Ring buffer was a monitor
Java, C#, etc., have built-in support for monitors

## Slide 41: Java concurrency
Java objects can be monitors
  “synchronized” keyword locks/releases the mutex
  Has one (!) builtin condition variable
    o.wait() = wait(o, o)
    o.notify() = signal(o)
    o.notifyAll() = broadcast(o)
  Java wait() can be called even when mutex is not held. Mutex not held when awoken by signal(). Useful?

## Slide 42: More synchronization mechanisms
Lots of synchronization variations… (can implement with mutex and condition vars.)
Reader/writer locks
  Any number of threads can hold a read lock
  Only one thread can hold the writer lock
Semaphores
  N threads can hold lock at the same time
Message-passing, sockets, queues, ring buffers, …
  transfer data and synchronize

## Slide 43: Summary
Hardware Primitives: test-and-set, LL/SC, barrier, ...
… used to build …
Synchronization primitives: mutex, semaphore, ...
… used to build …
Language Constructs: monitors, signals, ...

## Slide 44: Administrivia
Project3 due next week, Monday, April 22nd
  Games night Friday, April 26th, 5-7pm. Location: B17 Upson
  Come, eat, drink, have fun and be merry!
Prelim3 is next week, Thursday, April 25th
  Time and Location: 7:30pm in Phillips 101 and Upson B17
  Old prelims are online in CMS
  Prelim Review Session:
  Monday, April 22, 6-8pm in B17 Upson Hall
  Tuesday, April 23, 6-8pm in 101 Phillips Hall
Project4: Final project out next week
  Demos: May 14 and 15
  Will not be able to use slip days

## Slide 45: Administrivia
Next three weeks
  Week 12 (Apr 15): Project3 design doc due and HW4 due
  Week 13 (Apr 22): Project3 due and Prelim3
  Week 14 (Apr 29): Project4 handout
Final Project for class
  Week 15 (May 6): Project4 design doc due
  Week 16 (May 13): Project4 due by May 15th