## Slide 1: Prelim 3 Review
Hakim Weatherspoon
CS 3410, Spring 2013
Computer Science
Cornell University

## Slide 2: Administrivia
Pizza party: Project3 Games Night Cache Race
  Tomorrow, Friday, April 26th, 5:00-7:00pm
  Location: Upson B17
Prelim 3
  Tonight, Thursday, April 25th, 7:30pm
  Two Locations: PHL101 and UPSB17
    If NetID begins with ‘a’ to ‘j’, then go to PHL101 (Phillips 101)
    If NetID begins with ‘k’ to ‘z’, then go to UPSB17 (Upson B17)
Project4: Final project out next week
  Demos: May 14-15
  Will not be able to use slip days

## Slide 3: Goals for Today
Prelim 3 review
  Caching,
  Virtual Memory, Paging, TLBs
  Operating System, Traps, Exceptions,
  Multicore and synchronization

## Slide 4: Big Picture
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard
Notes: Caching,
Virtual Memory, Paging, TLBs
Operating System, Traps, Exceptions,
Multicore and synchronization

## Slide 5
Memory Hierarchy and Caches

## Slide 6: Memory Pyramid
Memory Pyramid
Disk (Many GB – few TB)
Memory (128MB – few GB)
L2 Cache (½-32MB)
RegFile
100s bytes
< 1 cycle access
1-3 cycle access
5-15 cycle access
50-300 cycle access
L3 becoming more common (eDRAM ?)
These are rough numbers: mileage may vary for latest/greatest Caches usually made of SRAM (or eDRAM)
L1 Cache
(several KB)
1000000+ cycle access
Notes: L1 L2 and even L3 all on-chip these days using SRAM and eDRAM

## Slide 7: Memory Hierarchy
Insight for Caches
If Mem[x] is was accessed recently...
… then Mem[x] is likely to be accessed soon
  Exploit temporal locality:
    Put recently accessed Mem[x] higher in memory hierarchy
    since it will likely be accessed again soon
… then Mem[x ± ε] is likely to be accessed soon
  Exploit spatial locality:
    Put entire block containing Mem[x] and surrounding addresses higher in memory hierarchy since nearby address will likely
    be accessed
put entire block containing Mem[x] higher in the pyramid
put recently accessed Mem[x] higher in the pyramid
A: Data that will be used soon
Notes: soon = frequency of loads

## Slide 8: Memory Hierarchy
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
Processor
tag data
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
4 cache lines
2 word block
0
0
0
0
V

## Slide 9: Three Common Cache Designs
A given data block can be placed…
  … in exactly one cache line  Direct Mapped
  … in any cache line  Fully Associative
  … in a small set of cache lines  Set Associative

## Slide 10: Direct Mapped Cache
V
Tag
Block
=
Tag Index Offset
word select
hit?
data
=
hit?
data
word select
32bits

## Slide 11: Fully Associative Cache
V
Tag
Block
word select
hit?
data
line select
=
=
=
=
32bits
64bytes
Tag Offset
Notes: “way” = line

## Slide 12: 3-Way Set Associative Cache
word select
hit?
data
line select
=
=
=
32bits
64bytes
Tag Index Offset
Each set is 3-way
4 sets
Notes: 4 sets, where each set has 3-way associativity (i.e. each set has three cachelines, where an individual cacheline that maps to a particular set can freely associate with any line in that set).

## Slide 13: Cache Misses
Three types of misses
  Cold (aka Compulsory)
    The line is being referenced for the first time
  Capacity
    The line was evicted because the cache was not large enough
  Conflict
    The line was evicted because of another access whose index conflicted

## Slide 14
Writing with Caches

## Slide 15: Eviction
Which cache line should be evicted from the cache to make room for a new line?
  Direct-mapped
    no choice, must evict line selected by index
  Associative caches
    random: select one of the lines at random
    round-robin: similar to random
    FIFO: replace oldest line
    LRU: replace line that has not been used in the longest time

## Slide 16: Cached Write Policies
Q: How to write data?
CPU
Cache
SRAM
Memory
DRAM
addr
data
If data is already in the cache…
No-Write
  writes invalidate the cache and go directly to memory
Write-Through
  writes go to main memory and cache
Write-Back
  CPU writes only to cache
  cache writes to main memory later (when block is evicted)

## Slide 17: What about Stores?
Where should you write the result of a store?
  If that memory location is in the cache?
    Send it to the cache
    Should we also send it to memory right away?
    (write-through policy)
    Wait until we kick the block out (write-back policy)
  If it is not in the cache?
    Allocate the line (put it in the cache)?
    (write allocate policy)
    Write it directly to memory without allocation?
    (no write allocate policy)

## Slide 18
Cache Performance

## Slide 19: Cache Performance
Consider hit (H) and miss ratio (M)
H x ATcache + M x (ATcache + Atmemory)
Hit rate = 1 – Miss rate
Access Time is given in cycles
Ratio of Access times, 1:50
90% : 1 + .1 x 50 = 6
95% : 1 + .05 x 50 = 3.5
99% : 1 + .01 x 50 = 1.5
99.9%: 1 + .001 x 50 = 1.05
= ATcache + M x ATmemory
Notes: %hit*hit time + %miss*miss time, but during the review session for the prelim, it was written as hit time + %miss*miss time.
hit cost = cache hit rate * cache hit time miss cost = cache miss rate * ( cache hit time + time to go to lower-level cache or memory) total cost = hit cost + miss cost = cache hit rate * cache hit time + cache miss rate * ( cache hit time + time to go to lower-level cache or memory) = cache hit rate * cache hit time + cache miss rate * cache hit time + cache miss rate * time to go to lower-level cache or memory = cache hit time * (cache hit rate + cache miss rate) + cache miss rate * time to go to lower-level cache or memory = cache hit time * (1) + cache miss rate * time to go to lower-level cache or memory = cache hit time + cache miss rate * time to go to lower-level cache or memory

## Slide 20
Cache Conscious Programming

## Slide 21: Cache Conscious Programming
Every access is a cache miss!
(unless entire matrix can fit in cache)
// H = 12, NCOL = 10
int A[NROW][NCOL];
for(col=0; col < NCOL; col++)
for(row=0; row < NROW; row++)
sum += A[row][col];
1 | 11 | 21 |  |  |  |  |  |  | 
 |  | 2 | 12 | 22 |  |  |  |  | 
 |  |  |  | 3 | 13 | 23 |  |  | 
 |  |  |  |  |  | 4 | 14 | 24 | 
 |  |  |  |  |  |  |  | 5 | 15
25 |  |  |  |  |  |  |  |  | 
6 | 16 | 26 |  |  |  |  |  |  | 
 |  | 7 | 17 | … |  |  |  |  | 
 |  |  |  | 8 | 18 |  |  |  | 
 |  |  |  |  |  | 9 | 19 |  | 
 |  |  |  |  |  |  |  | 10 | 20

## Slide 22: Cache Conscious Programming
Block size = 4  75% hit rate
Block size = 8  87.5% hit rate
Block size = 16  93.75% hit rate
And you can easily prefetch to warm the cache.
// NROW = 12, NCOL = 10
int A[NROW][NCOL];
for(row=0; row < NROW; row++)
for(col=0; col < NCOL; col++)
sum += A[row][col];
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
11 | 12 | 13 | … |  |  |  |  |  | 

## Slide 23
MMU, Virtual Memory, Paging, and TLB’s

## Slide 24: Multiple Processes
How to Run multiple processes?
Time-multiplex a single CPU core (multi-tasking)
  Web browser, skype, office, … all must co-exist
Many cores per processor (multi-core) or many processors (multi-processor)
  Multiple programs run simultaneously

## Slide 25: Multiple Processes
Q: What happens when another program is executed concurrently on another processor?
A: The addresses will conflict
  Even though, CPUs may take
  turns using memory bus
CPU
Text
Data
Stack
Heap
Memory
CPU
Text
Data
Stack
Heap
0x000…0
0x7ff…f
0xfff…f

## Slide 26: Virtual Memory
Virtual Memory: A Solution for All Problems
Each process has its own virtual address space
  Programmer can code as if they own all of memory
On-the-fly at runtime, for each memory access
  all access is indirect through a virtual address
  translate fake virtual address to a real physical address
  redirect load/store to the physical address

## Slide 27: Virtual Memory Advantages
Advantages
Easy relocation
  Loader puts code anywhere in physical memory
  Creates virtual mappings to give illusion of correct layout
Higher memory utilization
  Provide illusion of contiguous memory
  Use all physical memory, even physical address 0x0
Easy sharing
  Different mappings for different programs / cores
Different Permissions bits

## Slide 28: Address Space
Programs load/store to virtual addresses
Actual memory uses physical addresses
Memory Management Unit (MMU)
  Responsible for translating on the fly
  Essentially, just a big array of integers: paddr = PageTable[vaddr];
CPU
MMU
A
B
C
X
Y
Z
X
Y
Z
C
B
A
CPU
MMU
0x1000
0x1000
Virtual Address
Space
Physical Address Space
Virtual Address
Space
Notes: each mmu has own mappings
Easy relocation
Higher memory utilization
Easy sharing

## Slide 29: Attempt #1: Address Translation
Attempt #1: For any access to virtual address:
  Calculate virtual page number and page offset
  Lookup physical page number at PageTable[vpn]
  Calculate physical address as ppn:offset
vaddr
Page Offset
Virtual page number
Page offset
Physical page number
Lookup in PageTable
paddr
31 12 11 0
12 11 0
CPU
generated
Main
Memory
e.g. Page size
4 kB = 212
Notes: 4kb pages = 12 bits for page offset, 20 bits for VPN

## Slide 30: Beyond Flat Page Tables
Assume most of PageTable is empty
How to translate addresses?
10 bits
PTBR
10 bits
10 bits
vaddr
PDEntry
Page Directory
Page Table
PTEntry
Page
Word
2
Multi-level PageTable
* x86 does exactly this
4kB
#entries = pg sz/pte
4kB / 4B =1024 PTEs
Notes: Q: Benefits?
A1: Don’t need 4MB contiguous physical memory
A2: Don’t need to allocate every PageTable, only those containing valid PTEs
Q: Drawbacks?
A: Longer lookups.

## Slide 31: Virtual Addressing with a Cache
Thus it takes an extra memory access to translate a vaddr (VA) to a paddr (PA)
CPU
Trans-
lation
Cache
Main
Memory
VA
PA
miss
hit
data
This makes memory (cache) accesses very expensive (if every access was really two accesses)

## Slide 32: A TLB in the Memory Hierarchy
A TLB miss:
  If the page is not in main memory, then it’s a true page fault
    Takes 1,000,000’s of cycles to service a page fault
TLB misses are much more frequent than true page faults
CPU
TLB
Lookup
Cache
Main
Memory
VA
PA
miss
hit
data
Trans-
lation
hit
miss

## Slide 33: Virtual vs. Physical Caches
CPU
Cache
SRAM
Memory
DRAM
addr
data
MMU
Cache
SRAM
MMU
CPU
Memory
DRAM
addr
data
Cache works on physical addresses
Cache works on virtual addresses
Q: What happens on context switch?
Q: What about virtual memory aliasing?
Q: So what’s wrong with physically addressed caches?
Notes: A1: Physically-addressed: nothing; Virtually-addressed: need to flush cache
A2: Physically-addressed: nothing; Virtually-addressed: problems

## Slide 34: Indexing vs. Tagging
Physically-Addressed Cache
  slow: requires TLB (and maybe PageTable) lookup first
Virtually-Indexed, Virtually Tagged Cache
  fast: start TLB lookup before cache lookup finishes
  PageTable changes (paging, context switch, etc.)
     need to purge stale cache lines (how?)
  Synonyms (two virtual mappings for one physical page)
     could end up in cache twice (very bad!)
Virtually-Indexed, Physically Tagged Cache
  ~fast: TLB lookup in parallel with cache lookup
  PageTable changes  no problem: phys. tag mismatch
  Synonyms  search and evict lines with same phys. tag
Virtually-Addressed Cache

## Slide 35: Indexing vs. Tagging

## Slide 36: Typical Cache Setup
CPU
L2 Cache
SRAM
Memory
DRAM
addr
data
MMU
Typical L1: On-chip virtually addressed, physically tagged
Typical L2: On-chip physically addressed
Typical L3: On-chip …
L1 Cache
SRAM
TLB SRAM

## Slide 37
Hardware/Software Boundary

## Slide 38: Hardware/Software Boundary
Virtual to physical address translation is assisted by hardware?
  Translation Lookaside Buffer (TLB) that caches the recent translations
    TLB access time is part of the cache hit time
    May allot an extra stage in the pipeline for TLB access
  TLB miss
    Can be in software (kernel handler) or hardware

## Slide 39: Hardware/Software Boundary
Virtual to physical address translation is assisted by hardware?
  Page table storage, fault detection and updating
    Page faults result in interrupts (precise) that are then handled by the OS
    Hardware must support (i.e., update appropriately) Dirty and Reference bits (e.g., ~LRU) in the Page Tables

## Slide 41: Paging

## Slide 42
Traps, exceptions, and operating system

## Slide 43: Operating System
Some things not available to untrusted programs:
  Exception registers, HALT instruction, MMU instructions, talk to I/O devices, OS memory, ...
Need trusted mediator: Operating System (OS)
  Safe control transfer
  Data isolation
P1
P2
P3
P4
VM
filesystem
net
driver
driver
disk
eth
MMU
Notes: user/kernel/hardware

## Slide 44: Terminology
Trap: Any kind of a control transfer to the OS
Syscall: Synchronous (planned), program-to-kernel transfer
  SYSCALL instruction in MIPS (various on x86)
Exception: Synchronous, program-to-kernel transfer
  exceptional events: div by zero, page fault, page protection err, …
Interrupt: Aysnchronous, device-initiated transfer
  e.g. Network packet arrived, keyboard event, timer ticks
* real mechanisms, but nobody agrees on these terms

## Slide 45
Multicore and Synchronization

## Slide 46
Multi-core is a reality…
… but how do we write multi-core safe code?

## Slide 47: Why Multicore?
Moore’s law
  A law about transistors
    (Not speed)
  Smaller means faster
  transistors
Power consumption growing with transistors

## Slide 49: Power Trends
In CMOS IC technology
×1000
×30
5V → 1V

## Slide 50: Uniprocessor Performance
Constrained by power, instruction-level parallelism, memory latency

## Slide 51: Why Multicore?
Moore’s law
  A law about transistors
  Smaller means faster transistors
Power consumption growing with transistors
The power wall
  We can’t reduce voltage further
  We can’t remove more heat
How else can we improve performance?

## Slide 52: Intel’s argument

## Slide 53
1.2x
1.6x

## Slide 54: Why Multicore?
Power
1.0x
1.0x
Performance
Single-Core
Power
1.2x
1.7x
Performance
Single-Core Overclocked +20%
Power
0.8x
0.51x
Performance
Single-Core
Underclocked -20%
1.6x
1.02x
Dual-Core
Underclocked -20%

## Slide 55: Amdahl’s Law
Task: serial part, parallel part
As number of processors increases,
  time to execute parallel part goes to zero
  time to execute serial part remains the same
Serial part eventually dominates
Must parallelize ALL parts of task

## Slide 56: Amdahl’s Law
Consider an improvement E
F of the execution time is affected
S is the speedup
Notes: F = 0.5, S = 2
1/(0.5 + 0.25) = 1/0.75 = 1.333
F = 0.9, S = 2
1/(0.1 + 0.9/2) = 1/(0.1 + 0.45) = 1/0.55 = 1.8
F = 0.99, S = 2
1/(0.01+0.99/2) = 1/(0.01+0.495) = 1.98
F = 0.5, S = 8
1/(0.5+0.5/8) -> 2

## Slide 57: Multithreaded Processes

## Slide 58: Shared counters
Usual result: works fine.
Possible result: lost update!
Occasional timing-dependent failure  Difficult to debug
Called a race condition
hits = 0 + 1
read hits (0)
hits = 0 + 1
read hits (0)
T1
T2
hits = 1
hits = 0
time

## Slide 59: Race conditions
Def: a timing dependent error involving shared state
  Whether it happens depends on how threads scheduled: who wins “races” to instructions that update state
  Races are intermittent, may occur rarely
    Timing dependent = small changes can hide bug
  A program is correct only if all possible schedules are safe
    Number of possible schedule permutations is huge
    Need to imagine an adversary who switches contexts at the worst possible time

## Slide 60: Critical Sections
Basic way to eliminate races: use critical sections that only one thread can be in
  Contending threads must wait to enter
CSEnter();
  Critical section
CSExit();
T1
T2
time
CSEnter();
  Critical section
CSExit();
T1
T2

## Slide 61: Mutexes
Critical sections typically associated with mutual exclusion locks (mutexes)
Only one thread can hold a given mutex at a time
Acquire (lock) mutex on entry to critical section
  Or block if another thread already holds it
Release (unlock) mutex on exit
  Allow one waiting thread (if any) to acquire & proceed
pthread_mutex_lock(m);
  hits = hits+1;
pthread_mutex_unlock(m);
T1
T2
pthread_mutex_lock(m);
  hits = hits+1;
pthread_mutex_unlock(m);
pthread_mutex_init(m);

## Slide 62: Protecting an invariant
// invariant: data is in buffer[head..tail-1]. Protected by m.
pthread_mutex_t *m;
char buffer[1000];
int head = 0, tail = 0;
void put(char c) {
pthread_mutex_lock(m);
buffer[tail] = c;
tail = (tail + 1) % n;
pthread_mutex_unlock(m);
}
Rule of thumb: all updates that can affect invariant become critical sections.
char get() {
pthread_mutex_lock(m);
char c = buffer[head];
head = (head + 1) % n;
pthread_mutex_unlock(m);
}
X what if first==last?

## Slide 63
See you Tonight
Good Luck!