## Slide 1: Data and Control Hazards
CS 3410, Spring 2014
Computer Science
Cornell University
See P&H Chapter: 4.6-4.8

## Slide 2: Announcements
Prelim next week
Tuesday at 7:30
Upson B17 [a-e]*, Olin 255[f-m]*, Philips 101 [n-z]*
Go based on netid
Prelim reviews
Friday and Sunday evening. 7:30 again.
Location: TBA on piazza
Prelim conflicts
Contact KB , Prof. Weatherspoon, Andrew Hirsch
Survey
Constructive feedback is very welcome

## Slide 3: Administrivia
Prelim1:
  Time: We will start at 7:30pm sharp, so come early
  Loc: Upson B17 [a-e]*, Olin 255[f-m]*, Philips 101 [n-z]*
  Closed Book
    Cannot use electronic device or outside material
  Practice prelims are online in CMS
  Material covered everything up to end of this week
    Everything up to and including data hazards
    Appendix B (logic, gates, FSMs, memory, ALUs)
    Chapter 4 (pipelined [and non] MIPS processor with hazards)
    Chapters 2 (Numbers / Arithmetic, simple MIPS instructions)
    Chapter 1 (Performance)
    HW1, Lab0, Lab1, Lab2

## Slide 4: Hazards
3 kinds
  Structural hazards
    Multiple instructions want to use same unit
  Data hazards
    Results of instruction needed before
  Control hazards
    Don’t know which side of branch to take
Notes: Structural: say only 1 memory for instruction read and the MEM stage. That is a structural hazard. We have designed the MIPS ISA and our implementation of separate memory for instruction and data to avoid this problem. MIPS is designed very carefully to not have any structural hazards.
Data hazards arise when data needed by one instruction has not yet been computed (because it is further down the pipeline). We need a solution for this.
Control hazards arise when we don’t know what the PC will be. This makes it not possible to push the next instruction down the pipeline. Till we know what the issue is.

## Slide 5: How to handle data hazards
What to do if data hazard detected?
Options
  Nothing
    Change the ISA to match implementation
  Stall
    Pause current and subsequent instructions till safe
      Slow down the pipeline (add bubbles to pipeline)
  Forward/bypass
    Forward data value to where it is needed
Notes: Nothing: Modify ISA to match implementation (not great as an option, violates abstraction. Requires restructuring by application. Might not always be possible).
Stall: Pause current and all subsequent instruction
Forward/Bypass: Steal correct value from elsewhere in pipeline

## Slide 6: Forwarding
Forwarding bypasses some pipelined stages forwarding a result to a dependent instruction operand (register)

## Slide 7: Forwarding Example
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r5 |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
add r6, r3, r8 |  |  |  |  |  |  |  |  | 
IF | ID 11=r1 22=r2 | EX D=33 | MEM D=33 | WB r3=33 |  |  |  | 
 | IF | ID 33=r3 | EX | MEM | WB |  |  | 
 |  | IF | ID 33=r3 | EX | MEM | WB |  | 
 |  |  | IF | ID 33=r3 | EX | MEM | WB | 
IF
ID
Ex
M
W
IF
ID
IF
W
Ex
M
W
ID
Ex
M
IF
ID
Ex
r3 = 10
r3 = 20
time
M
W

## Slide 8: Forwarding
Forwarding bypasses some pipelined stages forwarding a result to a dependent instruction operand (register)
Three types of forwarding/bypass
  Forwarding from Ex/Mem registers to Ex stage (MEx)
  Forwarding from Mem/WB register to Ex stage (WEx)
  RegisterFile Bypass

## Slide 9: Forwarding Datapath 1
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r1 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
M
W
IF
ID
Ex
IF
ID
Ex
M
W
Notes: Note that the arrow is not going backward in time.

## Slide 10: Forwarding Datapath
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
detect hazard
Three types of forwarding/bypass
Forwarding from Ex/Mem registers to Ex stage (MEx)
Forwarding from Mem/WB register to Ex stage (W  Ex)
RegisterFile Bypass
IF/ID
ID/Ex
Ex/Mem
Mem/WB
forward unit
Notes: See where the hazard detection is. Forward unit is in the execute stage, because that is where you actually need the data.

## Slide 11: Forwarding Datapath
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
forward unit
detect hazard
Three types of forwarding/bypass
Forwarding from Ex/Mem registers to Ex stage (MEx)
Forwarding from Mem/WB register to Ex stage (W  Ex)
RegisterFile Bypass
IF/ID
ID/Ex
Ex/Mem
Mem/WB
Notes: Why is the forward unit here. Because it does not need to be earlier.

## Slide 12: Forwarding Datapath 1
Ex/MEM to EX Bypass
  EX needs ALU result that is still in MEM stage
  Resolve:
  Add a bypass from EX/MEM.D to start of EX
How to detect? Logic in Ex Stage:
forward = (Ex/M.WE && EX/M.Rd != 0 &&
ID/Ex.Ra == Ex/M.Rd)
|| (same for Rb)
“earlier” = started earlier
= stage right
stage left
  destination reg of earlier instruction == source reg of current
Notes: assumes (WE=0 implies rD=0) everywhere, similar for rA needed, rB needed (can ensure this in ID stage)

## Slide 13: Forwarding Datapath 2
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r1 |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
IF
ID
Ex
M
W
IF
ID
IF
W
Ex
M
W
ID
Ex
M

## Slide 14: Forwarding Datapath 2
Mem/WB to EX Bypass
  EX needs value being written by WB
  Resolve:
  Add bypass from WB final value to start of EX
How to detect? Logic in Ex Stage:
forward = (M/WB.WE && M/WB.Rd != 0 &&
ID/Ex.Ra == M/WB.Rd &&
|| (same for Rb)
Is this it?
Not quite!
“earlier” = started earlier
= stage right
stage left
  destination reg of earlier instruction == source reg of current
Notes: assumes (WE=0 implies rD=0) everywhere, similar for rA needed, rB needed (can ensure this in ID stage)

## Slide 15: Forwarding Datapath 2
How to detect? Logic in Ex Stage:
M/WB (WE on, Rd != 0) and (M/WB.Rd == ID/Ex.Ra)
also NOT(Ex/M.Rd == ID/Ex.Ra) and (WE, Rd!= 0))
Rb same as Ra
“earlier” = started earlier
= stage right
stage left
  destination reg of earlier instruction == source reg of current
add r3, r1, r2
sub r3, r3, r5
or r6, r3, r4
add r6, r3, r8
add r3, r1, r2
sub r5, r3, r5
or r6, r3, r4
add r6, r3, r8
Notes: assumes (WE=0 implies rD=0) everywhere, similar for rA needed, rB needed (can ensure this in ID stage)

## Slide 16: Register File Bypass
Register File Bypass
  Reading a value that is currently being written
Detect:
((Ra == MEM/WB.Rd) or (Rb == MEM/WB.Rd)) and (WB is writing a register)
Resolve:
Add a bypass around register file (WB to ID)
Better: just negate register file clock
    writes happen at end of first half of each clock cycle
    reads happen during second half of each clock cycle

## Slide 17: Register File Bypass
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r1 |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
add r6, r3, r8 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
IF
ID
Ex
M
W
IF
ID
IF
W
Ex
M
W
ID
Ex
M
IF
ID
Ex
M
W

## Slide 18: Are we done yet?
add r3, r1, r2
lw r4, 20(r8)
or r6, r3, r4
add r6, r3, r8

## Slide 19: Memory Load Data Hazard
What happens if data dependency after a load word instruction?
Memory Load Data Hazard
  Value not available until after the M stage
  So: next instruction can’t proceed if hazard detected
Notes: often see lw …; nop; …
we will stall for our project 2

## Slide 20: Memory Load Data Hazard
Ex
lw r4, 20(r8) |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
IF
ID
Ex
M
W
IF
ID
Ex
M
W
ID
Stall
load-use stall
Notes: requires one bubble

## Slide 21: Memory Load Data Hazard
Ex
lw r4, 20(r8) |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
IF
ID
Ex
M
W
IF
ID
Ex
M
W
ID
Stall
load-use stall
lw r4, 20(r8)
or r6,r4,r1
Notes: Need to go back in time

## Slide 22: Memory Load Data Hazard
data mem
inst mem
D
B
A
NOP
sub r6,r4,r1
lw r4, 20(r8)
Ex
lw r4, 20(r8) |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
IF
ID
Ex
M
W
IF
ID
Ex
M
W
ID
Stall
load-use stall
Notes: requires one bubble

## Slide 23: Memory Load Data Hazard
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
forward unit
detect hazard
IF/ID
ID/Ex
Ex/Mem
Mem/WB
Stall =
If(ID/Ex.MemRead &&
IF/ID.Ra == ID/Ex.Rd
Rd
MC
Notes: It happens in an earlier stage. You stall since you don’t want to go ahead from the ID stage unless you are ready.
Walk through what happens with a

## Slide 24: Memory Load Data Hazard
Load Data Hazard
  Value not available until WB stage
  So: next instruction can’t proceed if hazard detected
Resolution:
  MIPS 2000/3000: one delay slot
    ISA says results of loads are not available until one cycle later
    Assembler inserts nop, or reorders to fill delay slot
  MIPS 4000 onwards: stall
    But really, programmer/compiler reorders to avoid stalling in the load delay slot
For stall, how to detect? Logic in ID Stage
    Stall = ID/Ex.MemRead &&
    (IF/ID.Ra == ID/Ex.Rd || IF/ID.Rb == ID/Ex.Rd)
Notes: often see lw …; nop; …
we will stall for our project 2

## Slide 25: Quiz
add r3, r1, r2
nand r5, r3, r4
add r2, r6, r3
lw r6, 24(r3)
sw r6, 12(r2)
Notes: Find all hazards, and say how they are resolved

## Slide 26: Quiz
add r3, r1, r2
nand r5, r3, r4
add r2, r6, r3
lw r6, 24(r3)
sw r6, 12(r2)
5 Hazards
Notes: Find all hazards, and say how they are resolved

## Slide 27: Quiz
add r3, r1, r2
nand r5, r3, r4
add r2, r6, r3
lw r6, 24(r3)
sw r6, 12(r2)
Forwarding from Ex/MID/Ex (MEx)
Forwarding from M/WID/Ex (WEx)
RegisterFile (RF) Bypass
Forwarding from M/WID/Ex (WEx)
Stall
+ Forwarding from M/WID/Ex (WEx)
5 Hazards
Notes: Find all hazards, and say how they are resolved

## Slide 28: Data Hazard Recap
Delay Slot(s)
  Modify ISA to match implementation
Stall
  Pause current and all subsequent instructions
Forward/Bypass
  Try to steal correct value from elsewhere in pipeline
  Otherwise, fall back to stalling or require a delay slot
Notes: 1: ISA tied to impl; messy asm; impl easy & cheap; perf depends on asm.
2: ISA correctness not tied to impl; clean+slow asm, or messy+fast asm; impl easy and cheap; same perf as 1. 3: ISA perf not tied to impl; clean+fast asm; impl is tricky; best perf

## Slide 29: Why are we learning about this?
Logic and gates
Numbers & arithmetic
States & FSMs
Memory
A simple CPU
Performance
Pipelining
Hazards: Data and Control

## Slide 30: Control Hazards
What about branches?
A control hazard occurs if there is a control instruction (e.g. BEQ) and the program counter (PC) following the control instruction is not known until the control instruction computes if the branch should be taken
e.g.
0x10: beq r1, r2, L
0x14: add r3, r0, r3
0x18: sub r5, r4, r6
0x1C: L: or r3, r2, r4
Notes: Q: what happens with branch/jump in branch delay slot?
A: bad stuff, so forbidden
Q: why one, not two?
A: can move branch calc from EX to ID; will require new bypasses into ID stage; or can just zap the second instruction
Q: performance?
A: stall is bad

## Slide 31: Control Hazards
Control Hazards
  instructions are fetched in stage 1 (IF)
  branch and jump decisions occur in stage 3 (EX)
  i.e. next PC is not known until 2 cycles after branch/jump
What happens to instr following a branch, if branch taken?
Stall (+ Zap/Flush)
  prevent PC update
  clear IF/ID pipeline register
    instruction just fetched might be wrong, so convert to nop
  allow branch to continue into EX stage
Notes: Q: what happens with branch/jump in branch delay slot?
A: bad stuff, so forbidden
Q: why one, not two?
A: can move branch calc from EX to ID; will require new bypasses into ID stage; or can just zap the second instruction
Q: performance?
A: stall is bad

## Slide 32: Control Hazards
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 33: Control Hazards
beq r1, r2, L |  |  |  |  |  |  |  |  | 
add r3, r0, r3 |  |  |  |  |  |  |  |  | 
sub r5, r4, r6 |  |  |  |  |  |  |  |  | 
L: or r3, r2, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
PC
+4
NOP
IF
ID
Ex
M
W
IF
ID
NOP
NOP
NOP
IF
NOP
NOP
NOP
branch calc
decide branch
IF
ID
Ex
M
W
10:
14:
18:
1C:
If branch Taken
New PC = 1C
Zap
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 34: Control Hazards
beq r1, r2, L |  |  |  |  |  |  |  |  | 
add r3, r0, r3 |  |  |  |  |  |  |  |  | 
sub r5, r4, r6 |  |  |  |  |  |  |  |  | 
L: or r3, r2, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
PC
+4
NOP
IF
ID
Ex
M
W
IF
ID
NOP
NOP
NOP
IF
NOP
NOP
NOP
branch calc
decide branch
IF
ID
Ex
M
W
10:
14:
18:
1C:
If branch Taken
New PC = 1C
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 35: Control Hazards
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
14: add r3,r0,r3
10: beq r1, r2, L
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 36: Control Hazards
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
14: add r3,r0,r3
10: beq r1, r2, L
18: sub r5,r4,r6
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 37: Control Hazards
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
NOP
10: beq r1, r2, L
1C: or r3,r2,r4
NOP
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 38: Control Hazards
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
NOP
10: beq r1, r2, L
1C: or r3,r2,r4
NOP
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 39: Reduce the cost of control hazard?
Can we forward/bypass values for branches?
  We can move branch calc from EX to ID
  will require new bypasses into ID stage; or can just zap the second instruction
What happens to instructions following a branch, if branch taken?
  Still need to zap/flush instructions
Is there still a performance penalty for branches
  Yes, need to stall, then may need to zap (flush) subsequent instructions that have already been fetched
Notes: Q: what happens with branch/jump in branch delay slot?
A: bad stuff, so forbidden
Q: why one, not two?
A: can move branch calc from EX to ID; will require new bypasses into ID stage; or can just zap the second instruction
Q: performance?
A: stall is bad

## Slide 40: Control Hazards
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 41: Control Hazards
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 42: Control Hazards
beq r1, r2, L |  |  |  |  |  |  |  |  | 
add r3, r0, r3 |  |  |  |  |  |  |  |  | 
sub r5, r4, r6 |  |  |  |  |  |  |  |  | 
L: or r3, r2, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
PC
+4
NOP
IF
ID
Ex
M
W
IF
NOP
NOP
NOP
IF
ID
Ex
M
W
10:
14:
18:
1C:
If branch Taken
New PC = 1C
Zap
branch calc
decide branch
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 43: Control Hazards
beq r1, r2, L |  |  |  |  |  |  |  |  | 
add r3, r0, r3 |  |  |  |  |  |  |  |  | 
sub r5, r4, r6 |  |  |  |  |  |  |  |  | 
L: or r3, r2, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
PC
+4
NOP
IF
ID
Ex
M
W
IF
NOP
NOP
NOP
IF
ID
Ex
M
W
10:
14:
18:
1C:
If branch Taken
New PC = 1C
Zap
branch calc
decide branch
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 44: Control Hazards
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
10: beq r1,r2,L
10
14
14
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 45: Control Hazards
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
14: add r3,r0,r3
10: beq r1, r2, L
14
1C
18
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 46: Control Hazards
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
1C: or r3,r2,r4
NOP
10: beq r1, r2, L
1C
20
20
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 47: Control Hazards
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
1C: or r3,r2,r4
NOP
10: beq r1, r2, L
20
24
24
20:
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 48: Control Hazards
Control Hazards
  instructions are fetched in stage 1 (IF)
  branch and jump decisions occur in stage 3 (EX)
  i.e. next PC is not known until 2 cycles after branch/jump
  Can optimize and move branch and jump decision to stage 2 (ID)
  i.e. next PC is not known until 1 cycles after branch/jump
Stall (+ Zap)
  prevent PC update
  clear IF/ID pipeline register
    instruction just fetched might be wrong one, so convert to nop
  allow branch to continue into EX stage
Notes: Q: what happens with branch/jump in branch delay slot?
A: bad stuff, so forbidden
Q: why one, not two?
A: can move branch calc from EX to ID; will require new bypasses into ID stage; or can just zap the second instruction
Q: performance?
A: stall is bad

## Slide 49: Takeaway
Control hazards occur because the PC following a control instruction is not known until control instruction computes if branch should be taken or not
If branch taken, then need to zap/flush instructions. There still a performance penalty for branches: Need to stall, then may need to zap (flush) subsequent instructions that have already been fetched
We can reduce cost of a control hazard by moving branch decision and calculation from Ex stage to ID stage. This reduces the cost from flushing two instructions to only flushing one.

## Slide 50: Reduce cost of control hazard more?
Delay Slot
  ISA says N instructions after branch/jump always executed
    MIPS has 1 branch delay slot
    i.e. whether branch taken or not, instruction following branch is always executed

## Slide 51: Delay Slot
beq r1, r2, L |  |  |  |  |  |  |  |  | 
add r3, r0, r3 |  |  |  |  |  |  |  |  | 
sub r5, r4, r6 |  |  |  |  |  |  |  |  | 
L: or r3, r2, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
PC
+4
IF
ID
Ex
M
W
IF
IF
ID
Ex
M
W
10:
14:
18:
1C:
Delay slot
If branch taken next instr still exec'd
branch calc
decide branch
ID
Ex
M
W
Notes: Pipeline is humming

## Slide 52: Delay Slot
beq r1, r2, L |  |  |  |  |  |  |  |  | 
add r3, r0, r3 |  |  |  |  |  |  |  |  | 
sub r5, r4, r6 |  |  |  |  |  |  |  |  | 
L: or r3, r2, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
PC
+4
IF
ID
Ex
M
W
IF
IF
ID
Ex
M
W
10:
14:
18:
1C:
branch calc
decide branch
ID
Ex
M
W
IF
ID
Ex
M
W
Delay slot
If branch not taken next instr still exec’d
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 53: Control Hazards
Control Hazards
  instructions are fetched in stage 1 (IF)
  branch and jump decisions occur in stage 3 (EX)
  i.e. next PC is not known until 2 cycles after branch/jump
  Can optimize and move branch and jump decision to stage 2 (ID)
  i.e. next PC is not known until 1 cycles after branch/jump
Stall (+ Zap)
  prevent PC update
  clear IF/ID pipeline register
    instruction just fetched might be wrong one, so convert to nop
  allow branch to continue into EX stage
Delay Slot
  ISA says N instructions after branch/jump always executed
    MIPS has 1 branch delay slot
Notes: Q: what happens with branch/jump in branch delay slot?
A: bad stuff, so forbidden
Q: why one, not two?
A: can move branch calc from EX to ID; will require new bypasses into ID stage; or can just zap the second instruction
Q: performance?
A: stall is bad
GPUs have such long pipelines it is just not realistic to add delay slots. So the penalty of branching is very high typically. Various architectural approaches to address that.

## Slide 54: Takeaway
Control hazards occur because the PC following a control instruction is not known until control instruction computes if branch should be taken or not. If branch taken, then need to zap/flush instructions. There still a performance penalty for branches: Need to stall, then may need to zap (flush) subsequent instructions that have already been fetched.
We can reduce cost of a control hazard by moving branch decision and calculation from Ex stage to ID stage. This reduces the cost from flushing two instructions to only flushing one.
Delay Slots can potentially increase performance due to control hazards by putting a useful instruction in the delay slot since the instruction in the delay slot will always be executed. Requires software (compiler) to make use of delay slot. Put nop in delay slot if not able to put useful instruction in delay slot.

## Slide 55: Reduce cost of Ctrl Haz even further?
Speculative Execution
  “Guess” direction of the branch
    Allow instructions to move through pipeline
    Zap them later if wrong guess
  Useful for long pipelines
Notes: Q: How to guess?
A: constant; hint; branch prediction; random; …

## Slide 56: Speculative Execution: Loops
Pipeline so far
  “Guess” (predict) that the branch will not be taken
We can do better!
  Make prediction based on last branch
  Predict “take branch” if last branch “taken”
  Or Predict “do not take branch” if last branch “not taken”
  Need one bit to keep track of last branch

## Slide 57: Speculative Execution: Loops
While (r3 ≠ 0) {…. r3--;}
Top: BEQZ r3, End
J Top
End:
What is accuracy of branch predictor?
Wrong twice per loop!
Once on loop enter and exit
We can do better with 2 bits

## Slide 58: Speculative Execution: Branch Execution
Predict Taken 2 (PT2)
Branch Taken (T)
Predict Taken 1 (PT1)
Predict Not Taken 1 (PT1)
Predict Not Taken 2 (PT2)
Branch Not Taken (NT)
Branch Taken (T)
Branch Not Taken (NT)
Branch Taken (T)
Branch Not Taken (NT)
Notes: Sates is a 2 bit prediction scheme

## Slide 59: Summary
Control hazards
  Is branch taken or not?
  Performance penalty: stall and flush
Reduce cost of control hazards
  Move branch decision from Ex to ID
    2 nops to 1 nop
  Delay slot
    Compiler puts useful work in delay slot. ISA level.
  Branch prediction
    Correct. Great!
    Wrong. Flush pipeline. Performance penalty

## Slide 60: Hazards Summary
Data hazards
Control hazards
Structural hazards
  resource contention
  so far: impossible because of ISA and pipeline design
Notes: Q: what if we had a “copy 0(r3), 4(r3)” instruction, as the x86 does, or “add r4, r4, 0(r3)”?
A: structural hazard