## Slide 1: Traps, Exceptions, System Calls, & Privileged Mode
Prof. Kavita Bala and Prof. Hakim Weatherspoon
CS 3410, Spring 2014
Computer Science
Cornell University
P&H Chapter 4.9, pages 445–452, appendix A.7

## Slide 2: Heartbleed Security Bug
“…worst vulnerability found since commercial traffic began to flow over the internet.” Forbes, “massive Internet Security Vulnerability—Here’s where you need to do,” Apr 10 2014
17% (0.5million) secure web servers
vulnerable to bug—Netcraft, Ltd, Apr 8, 2014
  Amazon, Akamai, GitHub, Wikipedia, etc
Notes: How did such a severe security bug occur

## Slide 3: Heartbleed Security Bug
How does it work?
  Lack of bounds checking
  “Buffer over-read”
  SW allows more data to be read than should be allowed
  Malloc/Free did not clear memory
  Req with a large “length” field could return sensitive data
  Unauthenticated user can send a “heartbeat” and receive sensitive data
Notes: How did such a severe security bug occur

## Slide 4: Heartbleed Security Bug
How does it work?
  Lack of bounds checking
  “Buffer over-read”
http://en.wikipedia.org/wiki/Heartbleed
Notes: How did such a severe security bug occur

## Slide 5: Heartbleed Security Bug
How does it work?
  Lack of bounds checking
  “Buffer over-read”
Similar bug/vulnerability due to “Buffer overflow”
  Lab3
  Browser implementation lacks bounds checking
Notes: How did such a severe security bug occur

## Slide 6: Heartbleed Security Bug
sp
arguments
saved ra
saved regs
local variables
arguments
saved regs
saved ra
Buffer Overflow from lec12 and lab3
blue() {
pink(0,1,2,3,4,5);
}
pink(int a, int b, int c, int d, int e, int f) {
orange(10,11,12,13,14);
}
orange(int a, int b, int c, int, d, int e) {
char buf[100];
gets(buf); // read string, no check!
}
local variables
saved fp
saved ra
saved fp
saved fp
fp
What happens if more than 100 bytes
is written to buf?
buf[100]

## Slide 7: Takeaway
Worst Internet security vulnerability found yet due systems practices 101 that we learn in CS3410, lack of bounds checking!

## Slide 8: Big Picture
How do we protect programs from one another? How do we protect the operating system (OS) from programs?
How does the CPU (and software [OS]) handle exceptional conditions. E.g. Div by 0, page fault, syscall, etc?

## Slide 9: Goals for Today
Operating System
Privileged mode
Hardware/Software Boundary
Exceptions vs Interrupts vs Traps vs Systems calls

## Slide 10: Next Goal
How do we protect programs from one another? How do we protect the operating system (OS) from programs?
Notes: E.g. what stops firefox from writing all over the address space of Skype?

## Slide 11
Privileged Mode
aka Kernel Mode

## Slide 12: Operating System
Some things not available to untrusted programs:
  MMU instructions, Exception registers, HALT instruction, talk to I/O devices, OS memory, ...
Need trusted mediator: Operating System (OS)
  Safe control transfer
  Data isolation
P1
P2
P3
P4
VM
filesystem
net
driver
driver
disk
eth
MMU
untrusted
Notes: user/kernel/hardware

## Slide 13: Operating System
Trusted mediator is useless without a “privileged mode”:
  Any program can muck with TLB, PageTables, OS code…
  A program can intercept exceptions of other programs
  OS can crash if program messes up $sp, $fp, $gp, …
Wrong: Make these instructions and registers available only to “OS Code”
  “OS Code” == any code above 0x80000000
  Program can still JAL into middle of OS functions
  Program can still muck with OS memory, pagetables, …

## Slide 14: Privilege Mode
CPU Mode Bit / Privilege Level Status Register
Mode 0 = untrusted = user domain
  “Privileged” instructions and registers are disabled by CPU
Mode 1 = trusted = kernel domain
  All instructions and registers are enabled
Boot sequence:
  load first sector of disk (containing OS code) to well known address in memory
  Mode  1; PC  well known address
OS takes over…
  initialize devices, MMU, timers, etc.
  loads programs from disk, sets up pagetables, etc.
  Mode  0; PC  program entry point
(note: x86 has 4 levels x 3 dimensions, but only virtual machines uses any the middle)
Notes: boot sequence

## Slide 15: Terminology
Trap: Any kind of a control transfer to the OS
Syscall: Synchronous (planned), program-to-kernel transfer
  SYSCALL instruction in MIPS (various on x86)
Exception: Synchronous, program-to-kernel transfer
  exceptional events: div by zero, page fault, page protection err, …
Interrupt: Aysnchronous, device-initiated transfer
  e.g. Network packet arrived, keyboard event, timer ticks
* real mechanisms, but nobody agrees on these terms

## Slide 16: Sample System Calls
System call examples:
putc(): Print character to screen
  Need to multiplex screen between competing programs
send(): Send a packet on the network
  Need to manipulate the internals of a device
sbrk(): Allocate a page
  Needs to update page tables & MMU
sleep(): put current prog to sleep, wake other
  Need to update page table base register

## Slide 17: System Calls
System call: Not just a function call
  Don’t let program jump just anywhere in OS code
  OS can’t trust program’s registers (sp, fp, gp, etc.)
SYSCALL instruction: safe transfer of control to OS
  Mode  0; Cause  syscall; PC  exception vector
MIPS system call convention:
  user program mostly normal (save temps, save ra, …)
  but: $v0 = system call number, which specifies the operation the application is requesting

## Slide 18: Invoking System Calls
int getc() {
asm("addiu $2, $0, 4");
asm("syscall");
}
char *gets(char *buf) {
while (...) {
buf[i] = getc();
}
}

## Slide 19: Libraries and Wrappers
Compilers do not emit SYSCALL instructions
  Compiler doesn’t know OS interface
Libraries implement standard API from system API
libc (standard C library):
  getc()  syscall
  sbrk()  syscall
  write()  syscall
  gets()  getc()
  printf()  write()
  malloc()  sbrk()
  …

## Slide 21: Where does OS live?
In its own address space?
  But then syscall would have to switch to a different address space
  Also harder to deal with syscall arguments passed as pointers
So in the same address space as process
  Use protection bits to prevent user code from writing kernel
  Higher part of VM, lower part of physical memory

## Slide 22: Anatomy of an Executing Program
0xfffffffc
0x00000000
top
bottom
0x7ffffffc
0x80000000
0x10000000
0x00400000
system reserved
(stack grows down)
(heap grows up)
text
reserved
(static) data
(.stack)
.data
.text
system reserved
stack
system reserved
code (text)
static data
dynamic data (heap)
.data
.text

## Slide 23: Full System Layout
Typically all kernel text, most data
  At same VA in every address space
  Map kernel in contiguous physical memory when boot loader puts kernel into physical memory
The OS is omnipresent and steps in where necessary to aid application execution
  Typically resides in high memory
When an application needs to perform a privileged operation, it needs to invoke the OS
OS Text
Stack
Heap
Data
Text
OS Data
OS Heap
OS Stack
0x000…0
0x7ff…f
0xfff…f
0x800…0
Memory

## Slide 24: SYSCALL instruction
SYSCALL instruction does an atomic jump to a controlled location (i.e. MIPS 0x8000 0180)
  Switches the sp to the kernel stack
  Saves the old (user) SP value
  Saves the old (user) PC value (= return address)
  Saves the old privilege mode
  Sets the new privilege mode to 1
  Sets the new PC to the kernel syscall handler

## Slide 25: SYSCALL instruction
Kernel system call handler carries out the desired system call
  Saves callee-save registers
  Examines the syscall number
  Checks arguments for sanity
  Performs operation
  Stores result in v0
  Restores callee-save registers
  Performs a “return from syscall” (ERET) instruction, which restores the privilege mode, SP and PC

## Slide 26: Takeaway
Worst Internet security vulnerability found yet due systems practices 101 that we learn in CS3410, lack of bounds checking!
It is necessary to have a privileged mode (aka kernel mode) where a trusted mediator, the Operating System (OS), provides isolation between programs, protects shared resources, and provides safe control transfer.

## Slide 27: Next Goal
How do we protect programs from one another? How do we protect the operating system (OS) from programs?
How does the CPU (and software [OS]) handle exceptional conditions? E.g. syscall, Div by 0, page fault, etc?
What are exceptions and how are they handled?

## Slide 28: Exceptions
Exceptions are any unexpected change in control flow.
Interrupt -> cause of control flow change external
Exception -> cause of control flow change internal
  Exception: Divide by 0, overflow
  Exception: Bad memory address
  Exception: Page fault
  Interrupt: Hardware interrupt (e.g. keyboard stroke)
We need software to help resolve exceptions
  Exceptions are at the hardware/software boundary
Notes: What is a syscall? An (planned) exception.

## Slide 29: Exceptions
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard
Stack, Data, Code
Stored in Memory
$0 (zero)
$1 ($at)
$29 ($sp)
$31 ($ra)
Code Stored in Memory
(also, data and stack)
$$
$$

## Slide 30: Exceptions
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard
Stack, Data, Code
Stored in Memory
$0 (zero)
$1 ($at)
$29 ($sp)
$31 ($ra)
Code Stored in Memory
(also, data and stack)
$$
$$
EPC
Cause

## Slide 31: Hardware/Software Boundary
Hardware support for exceptions
  Exception program counter (EPC)
  Cause register
  Special instructions to load TLB
    Only do-able by kernel
Precise and imprecise exceptions
  In pipelined architecture
    Have to correctly identify PC of exception
    MIPS and modern processors support this

## Slide 32: Hardware/Software Boundary
Precise exceptions: Hardware guarantees
  (similar to a branch)
  Previous instructions complete
  Later instructions are flushed
  EPC and cause register are set
  Jump to prearranged address in OS
  When you come back, restart instruction
  Disable exceptions while responding to one
    Otherwise can overwrite EPC and cause

## Slide 33: Hardware/Software Boundary
Virtual to physical address translation is assisted by hardware
Need both hardware and software support
Software
  Page table storage, fault detection and updating
    Page faults result in interrupts that are then handled by the OS
    Must update appropriately Dirty and Reference bits (e.g., ~LRU) in the Page Tables

## Slide 34: Hardware/Software Boundary
OS has to keep TLB valid
Keep TLB valid on context switch
  Flush TLB when new process runs (x86)
  Store process id (MIPs)
Also, store pids with cache to avoid flushing cache on context switches
Hardware support
  Page table register
  Process id register

## Slide 35: Anatomy of an Executing Program
0xfffffffc
0x00000000
top
bottom
0x7ffffffc
0x80000000
0x10000000
0x00400000
system reserved
(stack grows down)
(heap grows up)
text
reserved
(static) data
(.stack)
.data
.text
system reserved
stack
system reserved
code (text)
static data
dynamic data (heap)
.data
.text

## Slide 36: Takeaway
Worst Internet security vulnerability found yet due systems practices 101 that we learn in CS3410, lack of bounds checking!
It is necessary to have a privileged mode (aka kernel mode) where a trusted mediator, the Operating System (OS), provides isolation between programs, protects shared resources, and provides safe control transfer.
Exceptions are any unexpected change in control flow. Precise exceptions are necessary to identify the exceptional instructional, cause of exception, and where to start to continue execution.
We need help of both hardware and software (e.g. OS) to resolve exceptions. Finally, we need some type of protected mode to prevent programs from modifying OS or other programs.

## Slide 37: Next Goal
What is the difference between traps, exceptions, interrupts, and system calls?

## Slide 38: Recap: Traps
 Map kernel into every process using supervisor PTEs
 Switch to kernel mode on trap, user mode on return
Trap: Any kind of a control transfer to the OS
Syscall: Synchronous, program-to-kernel transfer
  user does caller-saves, invokes kernel via syscall
  kernel handles request, puts result in v0, and returns
Exception: Synchronous, program-to-kernel transfer
  user div/load/store/… faults, CPU invokes kernel
  kernel saves everything, handles fault, restores, and returns
Interrupt: Aysnchronous, device-initiated transfer
  e.g. Network packet arrived, keyboard event, timer ticks
  kernel saves everything, handles event, restores, and returns

## Slide 39: Exceptions
Traps (System calls) are control transfers to the OS, performed under the control of the user program
Sometimes, need to transfer control to the OS at a time when the user program least expects it
  Division by zero,
  Alert from power supply that electricity is going out
  Alert from network device that a packet just arrived
  Clock notifying the processor that clock just ticked
Some of these causes for interruption of execution have nothing to do with the user application
Need a (slightly) different mechanism, that allows resuming the user application

## Slide 40: Interrupts & Exceptions
On an interrupt or exception
  CPU saves PC of exception instruction (EPC)
  CPU Saves cause of the interrupt/privilege (Cause register)
  Switches the sp to the kernel stack
  Saves the old (user) SP value
  Saves the old (user) PC value
  Saves the old privilege mode
  Sets the new privilege mode to 1
  Sets the new PC to the kernel interrupt/exception handler

## Slide 41: Interrupts & Exceptions
Kernel interrupt/exception handler handles the event
  Saves all registers
  Examines the cause
  Performs operation required
  Restores all registers
  Performs a “return from interrupt” instruction, which restores the privilege mode, SP and PC

## Slide 42: Example: Clock Interrupt
Example: Clock Interrupt*
  Every N cycles, CPU causes exception with Cause = CLOCK_TICK
  OS can select N to get e.g. 1000 TICKs per second
.ktext 0x8000 0180
# (step 1) save *everything* but $k0, $k1 to 0xB0000000
# (step 2) set up a usable OS context
# (step 3) examine Cause register, take action
if (Cause == PAGE_FAULT) handle_pfault(BadVaddr)
else if (Cause == SYSCALL) dispatch_syscall($v0)
else if (Cause == CLOCK_TICK) schedule()
# (step 4) restore registers and return to where program left off
* not the CPU clock, but a programmable timer clock

## Slide 43: Scheduler
struct regs context[];
int ptbr[];
schedule() {
i = current_process;
j = pick_some_process();
if (i != j) {
current_process = j;
memcpy(context[i], 0xB0000000);
memcpy(0xB0000000, context[j]);
asm(“mtc0 Context, ptbr[j]”);
}
}

## Slide 44: Syscall vs. Interrupt
Syscall vs. Exceptions vs. Interrupts
Same mechanisms, but…
Syscall saves and restores much less state
Others save and restore full processor state
Interrupt arrival is unrelated to user code
Notes: most state

## Slide 45: Takeaway
It is necessary to have a privileged mode (aka kernel mode) where a trusted mediator, the Operating System (OS), provides isolation between programs, protects shared resources, and provides safe control transfer.
Exceptions are any unexpected change in control flow. Precise exceptions are necessary to identify the exceptional instructional, cause of exception, and where to start to continue execution.
We need help of both hardware and software (e.g. OS) to resolve exceptions. Finally, we need some type of protected mode to prevent programs from modifying OS or other programs.
To handle any exception or interrupt, OS analyzes the Cause register to vector into the appropriate exception handler. The OS kernel then handles the exception, and returns control to the same process, killing the current process, or possibly scheduling another process.

## Slide 46: Summary
Trap
  Any kind of a control transfer to the OS
Syscall
  Synchronous, program-initiated control transfer from user to the OS to obtain service from the OS
  e.g. SYSCALL
Exception
  Synchronous, program-initiated control transfer from user to the OS in response to an exceptional event
  e.g. Divide by zero, TLB miss, Page fault
Interrupt
  Asynchronous, device-initiated control transfer from user to the OS
  e.g. Network packet, I/O complete

## Slide 47: Administrivia
Lab3 due tomorrow, Wednesday
  Take Home Lab, finish within day or two of your Lab
  Work alone
HW2 Help Session on tonight, Tuesday, April 15th, at 7:30pm in Kimball B11 and Thursday, April 17th.

## Slide 48: Administrivia
Next five weeks
  Week 11 (Apr 15): Proj3 release, Lab3 due Wed, HW2 due Sat
  Week 12 (Apr 22): Lab4 release and Proj3 due Fri
  Week 13 (Apr 29): Proj4 release, Lab4 due Tue, Prelim2
  Week 14 (May 6): Proj3 tournament Mon, Proj4 design doc due
Final Project for class
  Week 15 (May 13): Proj4 due Wed

## Slide 49: Administrivia
Lab3 is due this week, Thursday, April 11th
Project3 available now
  Design Doc due next week, Monday, April 15th
  Schedule a Design Doc review Mtg now, by this Friday, April 12th
  Whole project due Monday, April 22nd
  Competition/Games night Friday, April 26th, 5-7pm. Location: B17 Upson
Homework4 is available now
  Work alone
  Due next week, Wednesday, April 17th
  Question1 on Virtual Memory is pre-lab question for in-class Lab4
  HW Help Session Thurs (Apr 11) and Mon (Apr 15), 6-7:30pm in B17 Upson
Prelim3 is in two and a half weeks, Thursday, April 25th
  Time and Location: 7:30pm in Phillips 101 and Upson B17
  Old prelims are online in CMS