## Slide 1: CS 3410 - Spring 2014 Prelim 2 Review

## Slide 2: Prelim 2 Coverage
Calling Conventions
Linkers
Caches
Virtual Memory
Traps
Multicore Architectures
Synchronization

## Slide 3: Calling Convention
Prelim 2, 2013sp, Q5:
  Translate the following C code to MIPS assembly:
int foo(int a, int b, int c, int d, int e) {
int tmp = (a|b) – (d&e);
int q = littlefoo(tmp);
int z = bigfoo(q,tmp,a,b,c);
return tmp + q – z;
}

## Slide 4: Calling Convention (cont.)
int foo(int a, int b, int c, int d, int e) {
int tmp = (a|b) – (d&e);
int q = littlefoo(tmp);
int z = bigfoo(q,tmp,a,b,c);
return tmp + q – z;
}
Question 1: how many caller/callee save registers for which variables?
Callee save (need the original value after a function call):
a, b, c, tmp, q
Caller save (do not need to preserve in a function call):
d ($a3), e, z ($v0)
Question 2: how many outgoing arguments we should leave space for?
5: bigfoo(q, tmp, a, b, c)
Question 3: what is the stack frame size?
ra + fp + 5 callee-save + 5 outgoing args = 12 words = 48 bytes

## Slide 5: Calling Convention (cont.)
int foo(int a, int b, int c, int d, int e) {
int tmp = (a|b) – (d&e);
int q = littlefoo(tmp);
int z = bigfoo(q,tmp,a,b,c);
return tmp + q – z;
}
#prolog
ADDIU $sp, $sp, -48 # (== 5x outgoing args, 5x $sxx, $ra, $fp)
SW $ra, 44($sp)
SW $fp, 40($sp)
SW $s0, 36($sp) # store, then $s0 = a
SW $s1, 32($sp) # store, then $s1 = b
SW $s2, 28($sp) # store, then $s2 = c
SW $s3, 24($sp) # store, then $s3 = tmp = (a|b) – (d&e)
SW $s4, 20($sp) # store, then $s4 = q = littlefoo(tmp)
ADDIU $fp, $sp, 44

## Slide 6: Calling Convention (cont.)
int foo(int a, int b, int c, int d, int e) {
int tmp = (a|b) – (d&e);
int q = littlefoo(tmp);
int z = bigfoo(q,tmp,a,b,c);
return tmp + q – z;
}
#Initializing local variables
MOVE $s0, $a0
MOVE $s1, $a1
MOVE $s2, $a2
OR $t0, $s0, $s1 # $t0 = (a|b)
LW $t1, 64($sp) # 64 = 48(own stack) + 16(5th arg in parent)
AND $t1, $a3, $t1 # $t1 = (d&e)
SUB $s3, $t0, $t1 # $s3 = tmp = (a|b) – (d&e)

## Slide 7: Calling Convention (cont.)
int foo(int a, int b, int c, int d, int e) {
int tmp = (a|b) – (d&e);
int q = littlefoo(tmp);
int z = bigfoo(q,tmp,a,b,c);
return tmp + q – z;
}
#Calling littlefoo
MOVE $a0, $s3 # $a0 = tmp
JAL littlefoo
NOP
#Calling bigfoo
MOVE $s4, $v0 # $s4 = q = littlefoo(tmp)
MOVE $a0, $s4 # $a0 = $s4 = q
MOVE $a1, $s3 # $a1 = $s3 = tmp
MOVE $a2, $s0 # $a2 = $s0 = a
MOVE $a3, $s2 # $a3 = $s1 = b
SW $s2, 16($sp) # 5th arg = $s2 = c
JAL bigfoo # bigfoo(q,tmp,a,b,c)
NOP

## Slide 8: Calling Convention (cont.)
int foo(int a, int b, int c, int d, int e) {
int tmp = (a|b) – (d&e);
int q = littlefoo(tmp);
int z = bigfoo(q,tmp,a,b,c);
return tmp + q – z;
}
#Generating return value
ADD $t0, $s3, $s4 # $t0 = tmp + q
SUB $v0, $t0, $v0 # $v0 = $t0 – z = (tmp + q) – z
#epilog
LW $s4, 20($sp)
LW $s3, 24($sp)
LW $s2, 28($sp)
LW $s1, 32($sp)
LW $s0, 36($sp)
LW $fp, 40($sp)
LW $ra, 44($sp)
ADDIU $sp, $sp, 48
JR $ra
NOP

## Slide 9: Linkers and Program Layout
Prelim 2, 2012sp, Q2b:
  The global pointer, $gp, is usually initialized to the middle of the global data segment. Why the middle?
  Load and store instructions use signed offsets. Having $gp point to the middle of the data segment allows a full 2^16 byte range of memory to be accessed using positive and negative offsets from $gp.

## Slide 10: Linkers and Program Layout
Prelim 2, 2012sp, Q2c:
  Bob links his Hello World program against 9001 static libraries. Amazingly, this works without any collisions. Why?
  The linker chooses addresses for each library and fills in all the absolute addresses in each with the numbers that it chose.

## Slide 11: Caches
Prelim 2, 2013sp, Q4:
  Assume that we have a byte-addressed 32-bit processor with 32-bit words (i.e. a word is 4 bytes). Assume further that we have a cache consisting of eight 16-byte lines

## Slide 12: Caches (cont.)
How many bits are needed for the tag, index, and offset for the following cache architectures?
  Direct Mapped
    Tag: 25, Index: 3, Offset: 4
  2-way Set Associative
    Tag: 26, Index: 2, Offset: 4
  4-way Set Associative
    Tag: 27, Index: 1, Offset: 4
  Fully Associative
    Tag: 28, Index: 0, Offset: 4
Offset is only determined by the size of the cache line.
Index is determined by how caches are organized.
Tag = 32 – index - offset

## Slide 13: Caches (cont.)
For each access and for each specified cache organization, indicate whether there is a cache hit, a cold (compulsory) miss, conflict miss, or capacity miss.

## Slide 15: Virtual Memory (2012 Prelim3, Q4)
Stack
Heap
Data
Code
Memory layout of a single process
8 kB
8 kB
8 kB
8 kB
Virtual Address: 32-bit
Page Size: 16 kB
Single level page table
Each page table entry is 4 bytes.
Each process segment requires a separate physical page.
Bits for page Offset?
Bits for page table index?
Physical memory?
16 kB = 2^14 B
So we need 14 bits
32-14 bits = 18 bits
Each segment size < one page size
4*16 kB = 64 kB
2^18 (PTE’s) * 4 bytes = 1 MB
Total: 64kB + 1MB

## Slide 16: Virtual Memory (2012 Prelim3, Q4)
Two level page table
Assume there are enough page table entries to fill a second-level page table.
(which means every entry in a second level page table will be used)
……
Bits for page offset?
Bits for second level page table?
Bits for page directory?
14 bits
16kB/4B=2^12
So we need 12 bits
32-14-12 bits=6 bits
Physical memory(each process segment requires a separate second-level page table)?
1st: 2^6 * 4B < 2^14B=> 16 kB
2nd: 4 * 16 kB
Pages: 4 * 16 kB
Total: 16kB+4*16kB+4*16kB

## Slide 17: Syscall
User Program
main(){
…
syscall(arg1,arg2);
…
}
User Stub
syscall(arg1,arg2){
trap
return
}
handler(){
copy arguments from user memory
check arguments
syscall(arg1,arg2);
copy return value into user memory
return
}
Kernel Stub
Kernel
syscall(arg1,arg2){
do operation
}
Hardware Trap
Trap Return

## Slide 18: Exceptions
  On an interrupt or exception
    CPU saves PC of exception instruction (EPC)
    CPU Saves cause of the interrupt/privilege (Cause register)
    Switches the sp to the kernel stack
    Saves the old (user) SP value
    Saves the old (user) PC value
    Saves the old privilege mode
    Sets the new privilege mode to 1
    Sets the new PC to the kernel interrupt/exception handler
  Kernel interrupt/exception handler handles the event
    Saves all registers
    Examines the cause
    Performs operation required
    Restores all registers
    Performs a “return from interrupt” instruction, which restores the privilege mode, SP and PC

## Slide 19: Syscall V.S. Exceptions

## Slide 20: Concurrency (2012 Prelim3, Q5)
mutex_lock(&m)
operation
mutex_unlock(&m)
mutex_lock
try:
LI $t1, 1
LL $t0, 0($a0)
BNEZ $t0, try
SC $t1, 0($a0)
BEQZ $t1, try
mutex_unlock
SW $zero, 0($a0)
Load-link returns the current value of a memory location, while a subsequent store-conditional to the same memory location will store a new value only if no updates have occurred to that location since the load-link. Together, this implements a lock-free atomic read-modify-write operation.

## Slide 21: Concurrency (2012 Prelim3, Q5)
Critical Section:x = max(x, y)
x: global variable, shared; y: local variable
&x: $a1
y: $a2
Implement critical section using LL/SC without using mutex_lock and mutex_unlock
try:
LL $t0, 0($a1)
BGE $t0, $a2, next
NOP
MOVE $t0, $a2
next:
SC $t0, 0($a1)
BEQZ $t0, try
NOP

## Slide 22: Concurrency(Homework2 Q8)
c[0]?
A: LW $t0, 0($s0)
ADDIU $t0, $t0, 2
SW $t0, 0($s0)
B: SW $zero, 0($s0)
=>0
B: SW $zero, 0($s0)
A: LW $t0, 0($s0)
ADDIU $t0, $t0, 2
SW $t0, 0($s0)
=>2
A: LW $t0, 0($s0)
ADDIU $t0, $t0, 2
B: SW $zero, 0($s0)
A: SW $t0, 0($s0)
=>3

## Slide 23: Concurrency(Homework2 Q8)