## Slide 1: Lab 2: Finite State Machines CS 3410 Spring 2015

## Slide 2: Mealy Machines and Moore Machines
In Mealy Machines, output and next state both depend on current state and input.
Next State
Current State
Input
Output
Comb. Logic
Registers

## Slide 3: Mealy Machines and Moore Machines
In Moore Machines, output only depends on current state (next state still depends on both current state and input).
Current State
Input
Output
Registers
Comb. Logic
Comb. Logic

## Slide 4: Mealy Machines FSM
Legend
state
input/output
start state
A
B
C
D
down/on
up/off
down/on
up/off
up/off
up/off
down/off
up/off
Input: up or down
Output: on or off
States: A, B, C, or D

## Slide 5: Moore Machines FSM
Legend
state out
input
startout
A off
B on
C off
D off
down
up
down
up
up
up
down
up
Input: up or down
Output: on or off
States: A, B, C, or D

## Slide 6: Representing State in Logisim
In electric circuits, state must be represented by devices like Flip-Flops and Registers.
Maintaining and changing their values requires a clock!
Changing the input pin and “ticking” the clock once is equivalent to a new input to the FSM (you can use this to simulate a stream of input).

## Slide 7: Lab 2
The lab is available at http://www.cs.cornell.edu/courses/CS3410/2015sp/lab/lab2.html
Your first task will be to draw out the FSM on paper.
After your FSM has been checked off then you can begin creating it in Logisim.
Strategy:
  Draw a state diagram (e.g. Mealy Machine)
  Write output and next-state tables
  Encode states, inputs, and outputs as bits
  Determine logic equations for next state and outputs

## Slide 8: FSM Solution 1
Mealy Machine
String Progress

## Slide 9: FSM Solution 2