## Slide 1: Numbers and Arithmetic
Prof. Hakim Weatherspoon
CS 3410, Spring 2015
Computer Science
Cornell University
See: P&H Chapter 2.4, 3.2, B.2, B.5, B.6

## Slide 2: Big Picture: Building a Processor
PC
imm
memory
target
offset
cmp
control
=?
new pc
memory
din
dout
addr
register file
inst
extend
+4
+4
A Single cycle processor
alu

## Slide 3: Goals for Today
Binary Operations
  Number representations
  One-bit and four-bit adders
  Negative numbers and two’s compliment
  Addition (two’s compliment)
  Subtraction (two’s compliment)

## Slide 4: Number Representations
Recall: Binary
  Two symbols (base 2): true and false; 1 and 0
  Basis of Logic Circuits and all digital computers
So, how do we represent numbers in Binary (base 2)?
Notes: Add takeways at end of a block. Possibly build on takeaways throughout lecture

## Slide 5: Number Representations
Recall: Binary
  Two symbols (base 2): true and false; 1 and 0
  Basis of Logic Circuits and all digital computers
So, how do we represent numbers in Binary (base 2)?
  We know represent numbers in Decimal (base 10).
    E.g. 6 3 7
  Can just as easily use other bases
    Base 2 — Binary
    Base 8 — Octal
    Base 16 — Hexadecimal
102 101 100
1 0 0 1 1 1 1 1 0 1
29 28 27 26 25 24 23 22 21 20
0x 2 7 d
162161160
0o 1 1 7 5
83 82 81 80
Notes:     637 has a 1’s place , 10’s place and 100’s place
    Show how to go from

## Slide 6: Number Representations
Recall: Binary
  Two symbols (base 2): true and false; 1 and 0
  Basis of Logic Circuits and all digital computers
So, how do we represent numbers in Binary (base 2)?
  We know represent numbers in Decimal (base 10).
    E.g. 6 3 7
  Can just as easily use other bases
    Base 2 — Binary
    Base 8 — Octal
    Base 16 — Hexadecimal
102 101 100
6∙102 + 3∙101 + 7∙100 = 637
1∙29+1∙26+1∙25+1∙24+1∙23+1∙22+1∙20 = 637
1∙83 + 1∙82 + 7∙81 + 5∙80 = 637
2∙162 + 7∙161 + d∙160 = 637
2∙162 + 7∙161 + 13∙160 = 637
Notes:     637 has a 1’s place , 10’s place and 100’s place
    Show how to go from

## Slide 7: Number Representations: Activity #1 Counting
0
1
2
3
4
5
6
7
8
9
a
b
c
d
e
f
How do we count in different bases?
  Dec (base 10) Bin (base 2) Oct (base 8) Hex (base 16)
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
.
.
99
100
0
1
2
3
4
5
6
7
10
11
12
13
14
15
16
17
20
21
22
.
.
0
1
2
3
4
5
6
7
8
9
a
b
c
d
e
f
10
11
12
.
.
0
1
10
11
100
101
110
111
1000
1001
1010
1011
1100
1101
1110
1111
1 0000
1 0001
1 0010
.
.
Notes: Place location of question better in slide
The base represents the number of unique symbols (decimal has 10, octal has 8, hexadecimal has 16, and binary has 2 unique symbols)
Every group of four bits is called a nibble, every group of 8 bits is a byte

## Slide 8: Number Representations
How to convert a number between different bases?
Base conversion via repetitive division
  Divide by base, write remainder, move left with quotient
  637  8 = 79 remainder 5
  79  8 = 9 remainder 7
  9  8 = 1 remainder 1
  1  8 = 0 remainder 1
637 = 0o 1175
lsb (least significant bit)
msb (most significant bit)
lsb
msb
Notes: **Convert to a different base instead of same base**
637 = 0o1175 = 0b1001111101 = 0x27D
oct: 637 : 79 : 9 : 1 : 0
bin: 637 : 318 : 159 : 79 : 39 : 19 : 9 : 4 : 2 : 1 : 0
hex: 637 : 39 : 2 : 0

## Slide 9: Number Representations
Convert a base 10 number to a base 2 number
Base conversion via repetitive division
  Divide by base, write remainder, move left with quotient
  637  2 = 318 remainder 1
  318  2 = 159 remainder 0
  159  2 = 79 remainder 1
  79  2 = 39 remainder 1
  39  2 = 19 remainder 1
  19  2 = 9 remainder 1
  9  2 = 4 remainder 1
  4  2 = 2 remainder 0
  2  2 = 1 remainder 0
  1  2 = 0 remainder 1
637 = 10 0111 1101 (can also be written as 0b10 0111 1101)
lsb (least significant bit)
msb (most significant bit)
lsb
msb
Notes: Ask students to write down binary number after we figure it out. The question is did they writ the MSB on the left?
637 = 0o1175 = 0b10 0111 1101 = 0x27D
oct: 637 : 79 : 9 : 1 : 0
bin: 637 : 318 : 159 : 79 : 39 : 19 : 9 : 4 : 2 : 1 : 0
hex: 637 : 39 : 2 : 0

## Slide 10: Number Representations
Convert a base 10 number to a base 16 number
Base conversion via repetitive division
  Divide by base, write remainder, move left with quotient
  637  16 = 39 remainder 13
  39  16 = 2 remainder 7
  2  16 = 0 remainder 2
637 = 0x 2 7 13 = 0x 2 7 d
Thus, 637 = 0x27d
lsb
msb
dec = hex
10 = 0xa
11 = 0xb
12 = 0xc
13 = 0xd
14 = 0xe
15 = 0xf
= bin
= 1010
= 1011
= 1100
= 1101
= 1110
= 1111
?
Notes: Is 637 same as 0x 637 ?
637 = 0o1175 = 0b10 0111 1101 = 0x27D
oct: 637 : 79 : 9 : 1 : 0
bin: 637 : 318 : 159 : 79 : 39 : 19 : 9 : 4 : 2 : 1 : 0
hex: 637 : 39 : 2 : 0

## Slide 11: Number Representations
How to convert a number between different bases?
Base conversion via repetitive division
  Divide by base, write remainder, move left with quotient
  637  10 = 63 remainder 7
  63  10 = 6 remainder 3
  6  10 = 0 remainder 6
lsb (least significant bit)
msb (most significant bit)
Notes: **Convert to a different base instead of same base**
637 = 0o1175 = 0b1001111101 = 0x27D
oct: 637 : 79 : 9 : 1 : 0
bin: 637 : 318 : 159 : 79 : 39 : 19 : 9 : 4 : 2 : 1 : 0
hex: 637 : 39 : 2 : 0

## Slide 12: Number Representations
Convert a base 2 number to base 8 (oct) or 16 (hex)
Binary to Hexadecimal
  Convert each nibble (group of four bits) from binary to hex
  A nibble (four bits) ranges in value from 0…15, which is one hex digit
    Range: 0000…1111 (binary) => 0x0 …0xF (hex) => 0…15 (decimal)
  E.g. 0b10 0111 1101
    0b10 = 0x2
    0b0111 = 0x7
    0b1101 = 0xd
    Thus, 637 = 0x27d = 0b10 0111 1101
Binary to Octal
  Convert each group of three bits from binary to oct
  Three bits range in value from 0…7, which is one octal digit
    Range: 0000…1111 (binary) => 0x0 …0xF (hex) => 0…15 (decimal)
  E.g. 0b1 001 111 101
    0b1 = 0x1
    0b001 = 0x1
    0b111 = 0x7
    0b101 = 0x5
    Thus, 637 = 0o1175 = 0b10 0111 1101
Notes: Ask class to convert from binary to octal
637 = 0o1175 = 0b10 0111 1101 = 0x27D
oct: 637 : 79 : 9 : 1 : 0
bin: 637 : 318 : 159 : 79 : 39 : 19 : 9 : 4 : 2 : 1 : 0
hex: 637 : 39 : 2 : 0

## Slide 13: Number Representations Summary
We can represent any number in any base
  Base 10 – Decimal
  Base 2 — Binary
  Base 8 — Octal
  Base 16 — Hexadecimal
102 101 100
1 0 0 1 1 1 1 1 0 1
29 28 27 26 25 24 23 22 21 20
0x 2 7 d
162161160
0o 1 1 7 5
83 82 81 80
6 3 7
6∙102 + 3∙101 + 7∙100 = 637
1∙29+1∙26+1∙25+1∙24+1∙23+1∙22+1∙20 = 637
1∙83 + 1∙82 + 7∙81 + 5∙80 = 637
2∙162 + 7∙161 + d∙160 = 637
2∙162 + 7∙161 + 13∙160 = 637
Notes:     637 has a 1’s place , 10’s place and 100’s place

## Slide 14: Takeaway
Digital computers are implemented via logic circuits and thus represent all numbers in binary (base 2).
We (humans) often write numbers as decimal and hexadecimal for convenience, so need to be able to convert to binary and back (to understand what computer is doing!).
Notes: We can write any number in any base we like. The most natural base for computers is binary, which is hard to read, which is the reason we use hex and octal. Decimal..

## Slide 15: Next Goal
Binary Arithmetic: Add and Subtract two binary numbers

## Slide 16: Binary Addition
Addition works the same way regardless of base
  Add the digits in each position
  Propagate the carry
  Unsigned binary addition is pretty easy
  Combine two bits at a time
  Along with a carry
183 + 254
001110
+ 011100
How do we do arithmetic in binary?
1
4
3
7
1
1
1
0
0
0
1
1
1
Carry-out
Carry-in
Notes: Talk about Cin (carry in) and Cout (carry out)
Animate this better
Add another slide
So we need two numbers, the sum, carry in, and carry out

## Slide 17: Binary Addition
Addition works the same way regardless of base
  Add the digits in each position
  Propagate the carry
  Unsigned binary addition is pretty easy
  Combine two bits at a time
  Along with a carry
183 + 254
001110
+ 011100
How do we do arithmetic in binary?
437
1
101010
111
Notes: Talk about Cin (carry in) and Cout (carry out)
Animate this better
Add another slide
So we need two numbers, the sum, carry in, and carry out

## Slide 18: Binary Addition
Binary addition requires
  Add of two bits PLUS carry-in
  Also, carry-out if necessary
Notes: Talk about Cin (carry in) and Cout (carry out)
Animate this better
Add another slide
So we need two numbers, the sum, carry in, and carry out

## Slide 19: 1-bit Adder
Half Adder
Adds two 1-bit numbers
Computes 1-bit result and 1-bit carry
No carry-in
A
B
S
Cout
A | B | Cout | S
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
Notes: Adds two 1-bit numbers, computes 1-bit result and carry out
Useful for the rightmost binary digit, not much else

## Slide 20: 1-bit Adder with Carry
A
B
S
Cin
A | B | Cin | Cout | S
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 
Cout
Full Adder
Adds three 1-bit numbers
Computes 1-bit result and 1-bit carry
Can be cascaded
Activity: Truth Table and Sum-of-Product.
Logic minimization via Karnaugh Maps and algebraic minimization.
Draw Logic Circuits

## Slide 21: 4-bit Adder
4-Bit Full Adder
Adds two 4-bit numbers and carry in
Computes 4-bit result and carry out
Can be cascaded
A[4]
B[4]
S[4]
Cout
Cin
Notes: Adds two 1-bit numbers, along with carry-in, computes 1-bit result and carry out
Can be cascaded to add N-bit numbers

## Slide 22: 4-bit Adder
Adds two 4-bit numbers, along with carry-in
Computes 4-bit result and carry out
Carry-out = overflow indicates result does not fit in 4 bits
A0 B0
S0
A1 B1
S1
A2 B2
S2
A3 B3
S3
Cout
Cin
Notes: Transition: to do subtraction, just add, but negate one number

## Slide 23: Takeaway
Digital computers are implemented via logic circuits and thus represent all numbers in binary (base 2).
We (humans) often write numbers as decimal and hexadecimal for convenience, so need to be able to convert to binary and back (to understand what computer is doing!).
Adding two 1-bit numbers generalizes to adding two numbers of any size since 1-bit full adders can be cascaded.

## Slide 24: Next Goal
How do we subtract two binary numbers?
Equivalent to adding with a negative number
How do we represent negative numbers?

## Slide 25: First Attempt: Sign/Magnitude Representation
First Attempt: Sign/Magnitude Representation
  1 bit for sign (0=positive, 1=negative)
  N-1 bits for magnitude
Problem?
  Two zero’s: +0 different than -0
  Complicated circuits
IBM 7090
0111 =
1111 =
0111 = 7
1111 = -7
0000 = +0
1000 = -0
Notes: problems? two zeros, circuit still complicated
e.g. the existence of two forms of the same value (-0 and +0) necessitates two rather than a single comparison when checking for equality with zero.
The IBM 7090 was based in sign-magnitude representation.
The CDC 6000 series and UNIVAC 1100 series computers were based on ones' complement.
Also, in one’s complement, in addition to two zero’s, there is a crazy phenomenon called "end-around carry“: If the carry extends past the end of the word it is said to have "wrapped" around, a condition called an "end-around carry". When this occurs, the bit must be added back in at the right-most bit. This phenomenon does not occur in two's complement arithmetic.
Subtraction is similar, except that borrows are propagated to the left instead of carries. If the borrow extends past the end of the word it is said to have "wrapped" around, a condition called an "end-around borrow". When this occurs, the bit must be subtracted back in at the right-most bit. This phenomenon does not occur in two's complement arithmetic.
The CDC 6000 series and UNIVAC 1100 series computers were based on ones' complement.

## Slide 26: Second Attempt: One’s complement
Second Attempt: One’s complement
  Leading 0’s for positive and 1’s for negative
  Negative numbers: complement the positive number
Problem?
  Two zero’s still: +0 different than -0
  -1 if offset from two’s complement
  Complicated circuits
    Carry is difficult
PDP 1
0111 =
1000 =
0111 = 7
1000 = -7
0000 = +0
1111 = -0
Notes: problems? two zeros, circuit still complicated
e.g. the existence of two forms of the same value (-0 and +0) necessitates two rather than a single comparison when checking for equality with zero.
The IBM 7090 was based in sign-magnitude representation.
The CDC 6000 series and UNIVAC 1100 series computers were based on ones' complement.
Also, in one’s complement, in addition to two zero’s, there is a crazy phenomenon called "end-around carry“: If the carry extends past the end of the word it is said to have "wrapped" around, a condition called an "end-around carry". When this occurs, the bit must be added back in at the right-most bit. This phenomenon does not occur in two's complement arithmetic.
Subtraction is similar, except that borrows are propagated to the left instead of carries. If the borrow extends past the end of the word it is said to have "wrapped" around, a condition called an "end-around borrow". When this occurs, the bit must be subtracted back in at the right-most bit. This phenomenon does not occur in two's complement arithmetic.
The CDC 6000 series and UNIVAC 1100 series computers were based on ones' complement.

## Slide 27: Two’s Complement Representation
What is used: Two’s Complement Representation
Nonnegative numbers are represented as usual
  0 = 0000, 1 = 0001, 3 = 0011, 7 = 0111
Leading 1’s for negative numbers
To negate any number:
  complement all the bits (i.e. flip all the bits)
  then add 1
  -1: 1  0001  1110  1111
  -3: 3  0011  1100  1101
  -7: 7  0111  1000  1001
  -8: 8  1000  0111  1000
  -0: 0  0000  1111  0000 (this is good, -0 = +0)
Notes: add 1 and *discard carry*
Add a “Did you know box”
The two's complement of an N-bit number is defined as the *complement* with respect to 2^N, in other words the result of subtracting the number from 2^N. This is also equivalent to taking the *ones' complement* and then adding one, since the sum of a number and its ones' complement is all 1 bits. The two's complement of a number behaves like the negative of the original number in most arithmetic, and positive and negative numbers can coexist in a natural way.
Two's complement is the easiest to implement in hardware, which may be the ultimate reason for its widespread popularity[citation needed]. Remember that processors on the early mainframes often consisted of thousands of transistors – eliminating a significant number of transistors was a significant cost savings. The architects of the early integrated circuit based CPUs (Intel 8080, etc.) chose to use two's complement math. As IC technology advanced, virtually all adopted two's complement technology. Intel, AMD, and IBM POWER chips are all two's complement.[

## Slide 28: Two’s Complement
Negatives
(two’s complement: flip then add 1):
= 1111 -0 = 0000
= 1110 -1 = 1111
= 1101 -2 = 1110
= 1100 -3 = 1101
= 1011 -4 = 1100
= 1010 -5 = 1011
= 1001 -6 = 1010
= 1000 -7 = 1001
= 0111 -8 = 1000
Non-negatives
(as usual):
+0 = 0000
+1 = 0001
+2 = 0010
+3 = 0011
+4 = 0100
+5 = 0101
+6 = 0110
+7 = 0111
+8 = 1000
Notes: choose -8 so we have a sign bit
+0 = -0
wraps from +7 to -8
asymmetric: no +8

## Slide 29: Two’s Complement
Non-negatives
(as usual):
+0 = 0000
+1 = 0001
+2 = 0010
+3 = 0011
+4 = 0100
+5 = 0101
+6 = 0110
+7 = 0111
+8 = 1000
Negatives
(two’s complement: flip then add 1):
= 1111 -0 = 0000
= 1110 -1 = 1111
= 1101 -2 = 1110
= 1100 -3 = 1101
= 1011 -4 = 1100
= 1010 -5 = 1011
= 1001 -6 = 1010
= 1000 -7 = 1001
= 0111 -8 = 1000
Notes: choose -8 so we have a sign bit
+0 = -0
wraps from +7 to -8
asymmetric: no +8

## Slide 30: Two’s Complement Facts
Signed two’s complement
  Negative numbers have leading 1’s
  zero is unique: +0 = - 0
  wraps from largest positive to largest negative
N bits can be used to represent
  unsigned: range 0…2N-1
    eg: 8 bits  0…255
  signed (two’s complement): -(2N-1)…(2N-1 - 1)
    E.g.: 8 bits  (1000 000) … (0111 1111)
    -128 … 127
Notes: Why two’s complement works:
Given a set of all possible N-bit values, we can assign the lower (by binary value) half to be the integers from 0 to (2^[N−1]−1) inclusive and the upper half to be −2^[N−1] to −1 inclusive. The upper half can be used to represent negative integers from −2^[N−1] to −1 because, under addition modulo 2^N they behave the same way as those negative integers. That is to say that because i + j mod 2^N = i + (j + 2^N) mod 2^N any value in the set { j + k2^N | k is an integer } can be used in place of j.
For example, with eight bits, the unsigned bytes are 0 to 255. Subtracting 256 from the top half (128 to 255) yields the signed bytes −128 to −1.
The relationship to two's complement is realised by noting that 256 = 255 + 1, and (255 − x) is the ones' complement of x.
http://en.wikipedia.org/wiki/Two%27s_complement

## Slide 31: Sign Extension & Truncation
Extending to larger size
  1111 = -1
  1111 1111 = -1
  0111 = 7
  0000 0111 = 7
Truncate to smaller size
  0000 1111 = 15
  BUT, 0000 1111 = 1111 = -1
  Copy the leftmost bit into new leading bits
    For positive number, put 0’s in new leading bits
    For negative number, put 1’s in new leading bits
  Drop leading bits so long as sign doesn’t change

## Slide 32: Two’s Complement Addition
Addition with two’s complement signed numbers
Perform addition as usual, regardless of sign (it just works)
Examples
  1 + -1 =
  -3 + -1 =
  -7 + 3 =
  7 + (-3) =
  What is wrong with the following additions?
    7 + 1 -7 + -3 -7 + -1
Notes: 1 + (-1)
(-3) + (-1)
(-7) + 3
7 + (-3)
7 + 1 : overflow
(-7) + (-3) : overflow
(-7) + (-1)
7 + 1 = 0111+0001 = 1000 = -8 (OVERFLOW)! (Had a carry in to the MSB!) Sign of out != sign of in
7 + (-3) 0111+ 1101 = 1100 = -4
-7+-3 = 1001 + 1101 = 0110 (cout = 1) (Did not have a carry in to the MSB)
-7+-1 = 1001 + 1111 = 1000 (cout = 1)

## Slide 33: Binary Subtraction
Why create a new circuit?
Just use addition using two’s complement math
  How?
Notes: a – b, where b is so large that –B overflows
B must be -8, so that –B = -8
last bit will change
if a >= 0, will correctly signal overflow
if a < 0, will correctly subtract and not signal overflow

## Slide 34: Binary Subtraction
Two’s Complement Subtraction
  Subtraction is simply addition,
  where one of the operands has been negated
    Negation is done by inverting all bits and adding one
    A – B = A + (-B) = A + ( + 1)
S0
S1
S2
S3
A0
B0
A1
B1
A2
B2
A3
B3
Cout
Notes: a – b, where b is so large that –B overflows
B must be -8, so that –B = -8
last bit will change
if a >= 0, will correctly signal overflow
if a < 0, will correctly subtract and not signal overflow

## Slide 35: Binary Subtraction
Two’s Complement Subtraction
  Subtraction is simply addition,
  where one of the operands has been negated
    Negation is done by inverting all bits and adding one
    A – B = A + (-B) = A + ( + 1)
Q: What if (-B) overflows?
S0
S1
S2
S3
1
A0
B0
A1
B1
A2
B2
A3
B3
Q: How do we detect and handle overflows?
Cout
Notes: a – b, where b is so large that –B overflows
B must be -8, so that –B = -8
last bit will change
if a >= 0, will correctly signal overflow
if a < 0, will correctly subtract and not signal overflow

## Slide 36: Takeaway
Digital computers are implemented via logic circuits and thus represent all numbers in binary (base 2).
We (humans) often write numbers as decimal and hexadecimal for convenience, so need to be able to convert to binary and back (to understand what computer is doing!).
Adding two 1-bit numbers generalizes to adding two numbers of any size since 1-bit full adders can be cascaded.
Using Two’s complement number representation simplifies adder Logic circuit design (0 is unique, easy to negate).
Subtraction is simply adding, where one operand is negated (two’s complement; to negate just flip the bits and add 1).
.

## Slide 37: Next Goal
In general, how do we detect and handle overflow?

## Slide 38: Overflow
When can overflow occur?
  adding a negative and a positive?
  adding two positives?
  adding two negatives?

## Slide 39: Takeaway
Digital computers are implemented via logic circuits and thus represent all numbers in binary (base 2).
We (humans) often write numbers as decimal and hexadecimal for convenience, so need to be able to convert to binary and back (to understand what computer is doing!).
Adding two 1-bit numbers generalizes to adding two numbers of any size since 1-bit full adders can be cascaded.
Using Two’s complement number representation simplifies adder Logic circuit design (0 is unique, easy to negate). Subtraction is simply adding, where one operand is negated (two’s complement; to negate just flip the bits and add 1).
Overflow if sign of operands A and B != sign of result S.
Can detect overflow by testing Cin != Cout of the most significant bit (msb), which only occurs when previous statement is true.

## Slide 40: Administrivia
Make sure you are
Registered for class, can access CMS
Have a Section you can go to.
Lab Sections are required.
  “Make up” lab sections only 8:40am Wed, Thur, or Fri
  Bring laptop to Labs
Have project partner in same Lab Section, if possible
HW1 will be out soon out
Do problem with lecture
Work alone
But, use your resources
  Lab Section, Piazza.com, Office Hours, Homework Help Session,
  Class notes, book, Sections, CSUGLab

## Slide 41: Administrivia
Check online syllabus/schedule
  http://www.cs.cornell.edu/Courses/CS3410/2015sp/schedule.html
Slides and Reading for lectures
Office Hours
Pictures of all TAs
Homework and Programming Assignments
Dates to keep in Mind
  Prelims: Tue Mar 3rd and Thur April 30th
  Lab 1: Due Fri Feb 13th before Winter break
  Proj2: Due Thur Mar 26th before Spring break
  Final Project: Due when final would be (not known until Feb 14th)
Schedule is subject to change

## Slide 42: Summary
We can now implement combinational logic circuits
  Design each block
    Binary encoded numbers for compactness
  Decompose large circuit into manageable blocks
    1-bit Half Adders, 1-bit Full Adders,
    n-bit Adders via cascaded 1-bit Full Adders, ...
  Can implement circuits using NAND or NOR gates
  Can implement gates using use PMOS and NMOS-transistors
  And can add and subtract numbers (in two’s compliment)!
  Next time, state and finite state machines…