## Slide 1: State and Finite State Machines
Prof. Hakim Weatherspoon
CS 3410, Spring 2015
Computer Science
Cornell University
See P&H Appendix B.7. B.8, B.10, B.11

## Slide 2: Announcements
Make sure you are
Registered for class, can access CMS
Have a Section you can go to.
Lab Sections are required.
  “Make up” lab sections only 8:40am Wed, Thur, or Fri
  Bring laptop to Labs
Project partners are required for projects.
  Have project partner in same Lab Section, if possible
HW1 and Lab1 available today, after lecture
Do HW1 problems with lecture, i.e. finish part1 and 2 this week
Work alone on both
But, use your resources
  Lab Section, Piazza.com, Office Hours, Homework Help Session,
  Class notes, book, Sections, CSUGLab

## Slide 3: Announcements
Make sure to go to your Lab Section this week
Completed Lab1 due before winter break, Friday, Feb 13th
Note, a Design Document is due when you submit Lab1 final circuit
Work alone
Homework1 is out
Due a week before prelim1, Monday, February 23rd
Work on problems incrementally, as we cover them in lecture
Office Hours for help
Work alone
Work alone, BUT use your resources
  Lab Section, Piazza.com, Office Hours
  Class notes, book, Sections, CSUGLab

## Slide 4: Announcements
Check online syllabus/schedule
  http://www.cs.cornell.edu/Courses/CS3410/2015sp/schedule.html
Slides and Reading for lectures
Office Hours
Pictures of all TAs
Homework and Programming Assignments
Dates to keep in Mind
  Prelims: Tue Mar 3rd and Thur April 30th
  Lab 1: Due next Friday, Feb 13th before Winter break
  Proj2: Due Thur Mar 26th before Spring break
  Final Project: Due when final would be (not known until Feb 14th)
Schedule is subject to change

## Slide 5: Collaboration, Late, Re-grading Policies
“Black Board” Collaboration Policy
  Can discuss approach together on a “black board”
  Leave and write up solution independently
  Do not copy solutions
  Late Policy
  Each person has a total of four “slip days”
  Max of two slip days for any individual assignment
  Slip days deducted first for any late assignment,
  cannot selectively apply slip days
  For projects, slip days are deducted from all partners
  25% deducted per day late after slip days are exhausted
  Regrade policy
  Submit written request to lead TA,
  and lead TA will pick a different grader
  Submit another written request,
  lead TA will regrade directly
  Submit yet another written request for professor to regrade.

## Slide 6: Stateful Components
Until now is combinationial logic
  Output is computed when inputs are present
  System has no internal state
  Nothing computed in the present can depend on what happened in the past!
Need a way to record data
Need a way to build stateful circuits
Need a state-holding device
Finite State Machines
Inputs
Combinational circuit
Outputs
N
M
Notes: How are we going to stably store state

## Slide 7: Goals for Today
State
  How do we store one bit?
  Attempts at storing (and changing) one bit
    Set-Reset Latch
    D Latch
    D Flip-Flops
    Master-Slave Flip-Flops
  Register: storing more than one bit, N-bits
Basic Building Blocks
  Decoders and Encoders
Finite State Machines (FSM)
  How do we design logic circuits with state?
  Types of FSMs: Mealy and Moore Machines
  Examples: Serial Adder and a Digital Door Lock

## Slide 8: Goal
How do we store store one bit?

## Slide 9: First Attempt: Unstable Devices
B
A
C

## Slide 10: Second Attempt: Bistable Devices
A
B
A Simple Device
Stable and unstable equilibria?
Notes: How to create state? Feedback.
Show how the signal works

## Slide 11: Third Attempt: Set-Reset Latch
B
R
Q
A
S
Notes: Can you store a value (with this circuit)?
Can you change its value?
Q is comes from Latin language "quiscens" or "the present particle" or "what is present available" or "present output"
How to create state? Feedback.
Show how the signal works

## Slide 12: Third Attempt: Set-Reset Latch
Set-Reset (S-R) Latch
Stores a value Q and its complement
S | R | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
S | R | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
S
R
Q
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0

## Slide 13: Third Attempt: Set-Reset Latch
Set-Reset (S-R) Latch
Stores a value Q and its complement
S
R
Q
S
R
Q
S | R | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
S | R | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
Notes: Start with 0, 1 => 0, 1
then 0, 0 => 0, 1
then 1, 0 => 1, 0
then 0, 0 => 1, 0, better yet “stay”
1, 1 is forbidden, b/c going to 0, 0 after goes haywire
i.e.
Start 1,1 => 0,0
Alright. Now change S,R to 0, 0, what happens.
1, 1=>0, 0 -> 0, 0=> 0, 0 -> 0, 0=>1, 1 -> 0, 0=> 0, 0 -> oscillations.
S R=>Q,!Q -> S,R=>Q,!Q -> S, R=>Q,!Q -> S,R => Q,!Q

## Slide 14: Takeaway
Set-Reset (SR) Latch can store one bit and we can change the value of the stored bit. But, SR Latch has a forbidden state.

## Slide 15: Next Goal
How do we avoid the forbidden state of S-R Latch?

## Slide 16: Fourth Attempt: (Unclocked) D Latch
Fill in the truth table?
D
S
R
Q
Q
D
D | Q | 
0 |  | 
1 |  | 
D | Q | 
0 |  | 
1 |  | 
S
R
Q
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
Notes: Start in 0, 0, 1
Change to D = 1
After NOT gate, R = 0
After OR+NOT gates, /Q = 0 (R is already ready then), Q goes to 1
Problem: No way to hold state

## Slide 17: Takeaway
Set-Reset (SR) Latch can store one bit and we can change the value of the stored bit. But, SR Latch has a forbidden state.
(Unclocked) D Latch can store and change a bit like an SR Latch while avoiding the forbidden state.

## Slide 18: Next Goal
How do we coordinate state changes to a D Latch?

## Slide 19: Clocks
Clock helps coordinate state changes
  Usually generated by an oscillating crystal
  Fixed period; frequency = 1/period
period
high
low
1
0
falling edge
rising edge
clock
period
clock
high
clock
low
rising edge
falling edge

## Slide 20: Clock Disciplines
Level sensitive
  State changes when clock is high (or low)
Edge triggered
  State changes at clock edge
positive edge-triggered
negative edge-triggered

## Slide 21: Clock Methodology
Clock Methodology
Negative edge, synchronous
    Edge-Triggered: Signals must be stable near falling clock edge
Positive edge synchronous
clk
compute
save
tsetup
thold
compute
save
compute
tcombinational

## Slide 22: Fifth Attempt: D Latch with Clock
S
R
D
Q
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables

## Slide 23: Fifth Attempt: D Latch with Clock
S
R
D
clk
Q
clk | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
clk | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
Fill in the truth table
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables

## Slide 24: Fifth Attempt: D Latch with Clock
clk | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
clk | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
S
R
D
clk
Q
S | R | Q |  | 
0 | 0 | Q |  | hold
0 | 1 | 0 | 1 | reset
1 | 0 | 1 | 0 | set
1 | 1 | forbidden |  | 
S | R | Q |  | 
0 | 0 | Q |  | hold
0 | 1 | 0 | 1 | reset
1 | 0 | 1 | 0 | set
1 | 1 | forbidden |  | 
clk | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
clk | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
Fill in the truth table
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables

## Slide 25: Fifth Attempt: D Latch with Clock
S
R
D
clk
Q
clk
D
Q
Level Sensitive D Latch
Clock high: set/reset (according to D)
Clock low: keep state (ignore D)
clk | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
clk | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
Fill output signal for Q
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables

## Slide 26: Sixth Attempt: Edge-Triggered D Flip-Flop
D Flip-Flop
Edge-Triggered
Data captured when clock is high
Output changes only on falling edges
D
Q
D
Q
L
L
clk
D
X
Q
c
X
c
Q
D
clk
0
0
1
0
1
Activity#1: Fill in timing graph and values for X and Q
Notes: Master-Slave Flip Flop
- Outputs change only on falling edges
- Data is captured on rising edges
1 cycle delay
but works out perfectly – data for the next stage is ready 1 cycle ahead of time

## Slide 27: Takeaway
Set-Reset (SR) Latch can store one bit and we can change the value of the stored bit. But, SR Latch has a forbidden state.
(Unclocked) D Latch can store and change a bit like an SR Latch while avoiding a forbidden state.
An Edge-Triggered D Flip-Flip (aka Master-Slave D Flip-Flip) stores one bit. The bit can be changed in a synchronized fashion on the edge of a clock signal.

## Slide 28: Next Goal
How do we store more than one bit, N bits?

## Slide 29: Registers
Register
D flip-flops in parallel
shared clock
extra clocked inputs: write_enable, reset, …
clk
D0
D3
D1
D2
4
4
4-bit
reg
clk

## Slide 30: Takeaway
Set-Reset (SR) Latch can store one bit and we can change the value of the stored bit. But, SR Latch has a forbidden state.
(Unclocked) D Latch can store and change a bit like an SR Latch while avoiding a forbidden state.
An Edge-Triggered D Flip-Flip (aka Master-Slave D Flip-Flip) stores one bit. The bit can be changed in a synchronized fashion on the edge of a clock signal.
An N-bit register stores N-bits. It is be created with N D-Flip-Flops in parallel along with a shared clock.

## Slide 31: An Example: What will this circuit do?
4-bit
reg
Clk
Decoder
+1
4
4
4
16
4

## Slide 32: Decoder Example: 7-Segment LED
7-Segment LED
  photons emitted when electrons fall into holes
d7
d6
d5
d4
d3
d2
d1
d0
Notes: Previous slide would need to display up to 16, so would need a 16-segment LED decoder

## Slide 33: Decoder Example: 7-Segment LED Decoder
3 inputs
encode 0 – 7 in binary
7 outputs
one for each LED
7LED decode

## Slide 34: 7 Segment LED Decoder Implementation
b2 | b1 | b0 | d6 | d5 | d4 | d3 | d2 | d1 | d0
0 | 0 | 0 |  |  |  |  |  |  | 
0 | 0 | 1 |  |  |  |  |  |  | 
0 | 1 | 0 |  |  |  |  |  |  | 
0 | 1 | 1 |  |  |  |  |  |  | 
1 | 0 | 0 |  |  |  |  |  |  | 
1 | 0 | 1 |  |  |  |  |  |  | 
1 | 1 | 0 |  |  |  |  |  |  | 
1 | 1 | 1 |  |  |  |  |  |  | 
d0
d1
d2
d3
d4
d5
d6
b2 | b1 | b0 | d6 | d5 | d4 | d3 | d2 | d1 | d0
0 | 0 | 0 |  |  |  |  |  |  | 
0 | 0 | 1 |  |  |  |  |  |  | 
0 | 1 | 0 |  |  |  |  |  |  | 
0 | 1 | 1 |  |  |  |  |  |  | 
1 | 0 | 0 |  |  |  |  |  |  | 
1 | 0 | 1 |  |  |  |  |  |  | 
1 | 1 | 0 |  |  |  |  |  |  | 
1 | 1 | 1 |  |  |  |  |  |  | 

## Slide 35: 7 Segment LED Decoder Implementation
d0
d1
d2
d3
d4
d5
d6
b2 | b1 | b0 | d6 | d5 | d4 | d3 | d2 | d1 | d0
0 | 0 | 0 |  |  |  |  |  |  | 
0 | 0 | 1 |  |  |  |  |  |  | 
0 | 1 | 0 |  |  |  |  |  |  | 
0 | 1 | 1 |  |  |  |  |  |  | 
1 | 0 | 0 |  |  |  |  |  |  | 
1 | 0 | 1 |  |  |  |  |  |  | 
1 | 1 | 0 |  |  |  |  |  |  | 
1 | 1 | 1 |  |  |  |  |  |  | 
1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0 | 1 | 1

## Slide 36: Basic Building Blocks We have Seen
binary
encoder
2N
N
binary
decoder
N
2N
Multiplexor
N
M
N
N
N
N
. . .
0
1
2
2M-1

## Slide 37: Encoders
1
2
3
4
5
6
7
0
encoder
N
. . .
. . .
Log2(N) outputs wires
N Input wires
e.g. Voting:
Can only vote for one out of N
candidates, so N inputs.
But can encode vote efficiently
with binary encoding.
Notes: N possible inputs -> log2(N) wires to encode

## Slide 38: Example Encoder Truth Table
a
b
1
c
d
2
3
4
o1
A 3-bit
encoder
with 4 inputs for simplicity
a | b | c | d |  |  |  | 
0 | 0 | 0 | 0 |  |  |  | 
1 | 0 | 0 | 0 |  |  |  | 
0 | 1 | 0 | 0 |  |  |  | 
0 | 0 | 1 | 0 |  |  |  | 
0 | 0 | 0 | 1 |  |  |  | 
o0
o1
o2
Notes: Implementation . . .
assume 8 choices, exactly one mark detected

## Slide 39: Basic Building Blocks Example: Voting
Ballots
The 3410 optical scan
vote reader
machine
detect
enc
8
3
7
7LED decode

## Slide 40: Recap
We can now build interesting devices with sensors
  Using combinationial logic
We can also store data values (aka Sequential Logic)
  In state-holding elements
  Coupled with clocks

## Slide 41: Goals for Today
State
  How do we store one bit?
  Attempts at storing (and changing) one bit
    Set-Reset Latch
    D Latch
    D Flip-Flops
    Master-Slave Flip-Flops
  Register: storing more than one bit, N-bits
Basic Building Blocks
  Decoders and Encoders
Finite State Machines (FSM)
  How do we design logic circuits with state?
  Types of FSMs: Mealy and Moore Machines
  Examples: Serial Adder and a Digital Door Lock

## Slide 42: Finite State Machines

## Slide 43: Next Goal
How do we design logic circuits with state?

## Slide 44: Finite State Machines
An electronic machine which has
  external inputs
  externally visible outputs
  internal state
Output and next state depend on
  inputs
  current state

## Slide 45: Abstract Model of FSM
Machine is
M = ( S, I, O,  )
S: Finite set of states
I: Finite set of inputs
O: Finite set of outputs
: State transition function
Next state depends on present input and present state

## Slide 46: Automata Model
Finite State Machine
  inputs from external world
  outputs to external world
  internal state
  combinational logic
Next State
Current State
Input
Output
Registers
Comb. Logic
Notes: Put sequential logic term on slide

## Slide 47: FSM Example
Legend
state
input/output
start state
A
B
C
D
down/on
up/off
down/on
down/off
up/off
up/off
down/off
up/off
Input: up or down
Output: on or off
States: A, B, C, or D

## Slide 48: FSM Example
Legend
state
input/output
start state
A
B
C
D
down/on
up/off
down/on
down/off
up/off
up/off
down/off
up/off
Input: = up or = down
Output: = on or = off
States: = A, = B, = C, or = D
Notes: Say left of slash is input and right is output

## Slide 49: FSM Example
Legend
S1S0
i0i1i2…/o0o1o2…
S1S0
00
01
10
11
1/1
0/0
1/1
1/0
0/0
1/0
0/0
0/0
Input: 0=up or 1=down
Output: 1=on or 0=off
States: 00=A, 01=B, 10=C, or 11=D

## Slide 50: Mealy Machine
General Case: Mealy Machine
Outputs and next state depend on both current state and input
Next State
Current State
Input
Output
Registers
Comb. Logic

## Slide 51: Moore Machine
Special Case: Moore Machine
Outputs depend only on current state
Next State
Current State
Input
Output
Registers
Comb. Logic
Comb. Logic

## Slide 52: Moore Machine FSM Example
Legend
state out
input
startout
A off
B on
C off
D off
down
up
down
down
up
up
down
up
Input: up or down
Output: on or off
States: A, B, C, or D
Notes: Also show a mealy machine

## Slide 53: Mealy Machine FSM Example
Legend
state
input/output
start state
A
B
C
D
down/on
up/off
down/on
down/off
up/off
up/off
down/off
up/off
Input: up or down
Output: on or off
States: A, B, C, or D

## Slide 54: Activity#2: Create a Logic Circuit for a Serial Adder
Add two infinite input bit streams
  streams are sent with least-significant-bit (lsb) first
  How many states are needed to represent FSM?
  Draw and Fill in FSM diagram
…10110
…01111
…00101
Strategy:
(1) Draw a state diagram (e.g. Mealy Machine)
(2) Write output and next-state tables
(3) Encode states, inputs, and outputs as bits
(4) Determine logic equations for next state and outputs
Notes: Ask as a clicker question

## Slide 55: FSM: State Diagram
states:
Inputs: ??? and ???
Output: ???
  .
…10110
…01111
…00101
Notes: Is this a mealy or moore machine, maybe clicker

## Slide 56: FSM: State Diagram
states:
Inputs: ??? and ???
Output: ???
  .
S0
S1
__/_
__/_
__/_
__/_
__/_
__/_
__/_
__/_
…10110
…01111
…00101
Notes: Is this a mealy or moore machine, maybe clicker

## Slide 57: FSM: State Diagram
?? | ?? | Current state | ? | Next state
(2) Write down all input and state combinations
S0
S1
__/_
__/_
__/_
__/_
__/_
__/_
__/_
__/_

## Slide 58: FSM: State Diagram
?? | ?? | Current state | ? | Next state
(3) Encode states, inputs, and outputs as bits
S0
S1
__/_
__/_
__/_
__/_
__/_
__/_
__/_
__/_

## Slide 59: FSM: State Diagram
?? | ?? | Current state | ? | Next state
(4) Determine logic equations for next state and outputs

## Slide 60: Summary
We can now build interesting devices with sensors
  Using combinational logic
We can also store data values
  Stateful circuit elements (D Flip Flops, Registers, …)
  Clock to synchronize state changes
  State Machines or Ad-Hoc Circuits