## Slide 1: Processor
Prof. Hakim Weatherspoon
CS 3410, Spring 2015
Computer Science
Cornell University
See P&H Chapter: 4.1-4.4, 1.6, Appendix B

## Slide 2: Announcements
Project Partner finding assignment on CMS
No official office hours over break
Lab1 due tomorrow
HW1 Help Sessions Wed, Feb 18 and Sun, Feb 21

## Slide 3: Announcements
Make sure to go to your Lab Section this week
Lab2 due in class this week (it is not homework)
Lab1: Completed Lab1 due tomorrow Friday, Feb 13th, before winter break
Note, a Design Document is due when you submit Lab1 final circuit
Work alone
Save your work!
  Save often. Verify file is non-zero. Periodically save to Dropbox, email.
  Beware of MacOSX 10.5 (leopard) and 10.6 (snow-leopard)
Homework1 is out
Due a week before prelim1, Monday, February 23rd
Work on problems incrementally, as we cover them in lecture (i.e. part 1)
Office Hours for help
Work alone
Work alone, BUT use your resources
  Lab Section, Piazza.com, Office Hours
  Class notes, book, Sections, CSUGLab

## Slide 4: Announcements
Check online syllabus/schedule
  http://www.cs.cornell.edu/Courses/CS3410/2015sp/schedule.html
Slides and Reading for lectures
Office Hours
Pictures of all TAs
Homework and Programming Assignments
Dates to keep in Mind
  Prelims: Tue Mar 3rd and Thur April 30th
  Lab 1: Due this Friday, Feb 13th before Winter break
  Proj2: Due Thur Mar 26th before Spring break
  Final Project: Due when final would be (not known until Feb 14th)
Schedule is subject to change

## Slide 5: Collaboration, Late, Re-grading Policies
“Black Board” Collaboration Policy
  Can discuss approach together on a “black board”
  Leave and write up solution independently
  Do not copy solutions
  Late Policy
  Each person has a total of four “slip days”
  Max of two slip days for any individual assignment
  Slip days deducted first for any late assignment,
  cannot selectively apply slip days
  For projects, slip days are deducted from all partners
  25% deducted per day late after slip days are exhausted
  Regrade policy
  Submit written request to lead TA,
  and lead TA will pick a different grader
  Submit another written request,
  lead TA will regrade directly
  Submit yet another written request for professor to regrade.

## Slide 6: Goals for today
MIPS Datapath
  Memory layout
  Control Instructions
Performance
  How fast can we make it?
  CPI (Cycles Per Instruction)
  MIPS (Instructions Per Cycle)
  Clock Frequency

## Slide 7: MIPS Instruction Types
Arithmetic/Logical
  R-type: result and two source registers, shift amount
  I-type: 16-bit immediate with sign/zero extension
Memory Access
  load/store between registers and memory
  word, half-word and byte operations
Control flow
  conditional branches: pc-relative addresses
  jumps: fixed offsets, register absolute

## Slide 8: Memory Instructions
op | mnemonic | description
0x23 | LW rd, offset(rs) | R[rd] = Mem[offset+R[rs]]
0x2b | SW rd, offset(rs) | Mem[offset+R[rs]] = R[rd]
op | rs | rd | offset
6 bits | 5 bits | 5 bits | 16 bits
10101100101000010000000000000100
base + offset addressing
I-Type
signed offsets

## Slide 9: Memory Operations
Data Mem
addr
ext
+4
5
imm
5
5
control
Reg. File
PC
Prog.
Mem
ALU
inst

## Slide 10: Memory Instructions
op | mnemonic | description
0x20 | LB rd, offset(rs) | R[rd] = sign_ext(Mem[offset+R[rs]])
0x24 | LBU rd, offset(rs) | R[rd] = zero_ext(Mem[offset+R[rs]])
0x21 | LH rd, offset(rs) | R[rd] = sign_ext(Mem[offset+R[rs]])
0x25 | LHU rd, offset(rs) | R[rd] = zero_ext(Mem[offset+R[rs]])
0x23 | LW rd, offset(rs) | R[rd] = Mem[offset+R[rs]]
0x28 | SB rd, offset(rs) | Mem[offset+R[rs]] = R[rd]
0x29 | SH rd, offset(rs) | Mem[offset+R[rs]] = R[rd]
0x2b | SW rd, offset(rs) | Mem[offset+R[rs]] = R[rd]
op | rs | rd | offset
6 bits | 5 bits | 5 bits | 16 bits
10101100101000010000000000000100
Notes: sw r1 4(r5)
sb r1, 3(r5)
If you don’t make sure half word accesses are half word aligned, or word accesses are word aligned, there will be an error signaled. We will talk about traps and exceptions later.

## Slide 11: Endianness
Endianness: Ordering of bytes within a memory word
1000 | 1001 | 1002 | 1003
0x12345678
Big Endian = most significant part first (MIPS, networks)
Little Endian = least significant part first (MIPS, x86)
as 4 bytes
as 2 halfwords
as 1 word
1000 | 1001 | 1002 | 1003
0x12345678
as 4 bytes
as 2 halfwords
as 1 word
Notes: Comes from Gulliver travels

## Slide 12: Memory Layout
Examples (big/little endian):
# r5 contains 5 (0x00000005)
SB r5, 2(r0)
LB r6, 2(r0)
SW r5, 8(r0)
LB r7, 8(r0)
LB r8, 11(r0)
 | 0x00000000
 | 0x00000001
 | 0x00000002
 | 0x00000003
 | 0x00000004
 | 0x00000005
 | 0x00000006
 | 0x00000007
 | 0x00000008
 | 0x00000009
 | 0x0000000a
 | 0x0000000b
 | ...
 | 0xffffffff
Notes: Big Endian means store MSB (most significant byte) first

## Slide 13: MIPS Instruction Types
Arithmetic/Logical
  R-type: result and two source registers, shift amount
  I-type: 16-bit immediate with sign/zero extension
Memory Access
  load/store between registers and memory
  word, half-word and byte operations
Control flow
  conditional branches: pc-relative addresses
  jumps: fixed offsets, register absolute

## Slide 14: Control Flow: Absolute Jump
op | Mnemonic | Description
0x2 | J target | PC = target  00
op | immediate
6 bits | 26 bits
00001001000000000000000000000001
J-Type
op | Mnemonic | Description
0x2 | J target | PC = (PC+4)31..28  target  00
Notes: Where  is used to concatenate
Why should the offset be left shifted by 2. To keep the jump address word aligned.
AND to not waste two bits that we *know* are going to be 0.

## Slide 15: Absolute Jump
long jump? computed jump?
tgt
+4

Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm

## Slide 16: Control Flow: Jump Register
op | rs | - | - | - | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
00000000011000000000000000001000
op | func | mnemonic | description
0x0 | 0x08 | JR rs | PC = R[rs]
R-Type

## Slide 17: Jump Register
+4

tgt
Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
JR

## Slide 18: Examples
E.g. Use Jump or Jump Register instruction to
jump to 0xabcd1234
But, what about a jump based on a condition?
# assume 0 <= r3 <= 1
if (r3 == 0) jump to 0xdecafe00
else jump to 0xabcd1234

## Slide 19: Control Flow: Branches
op | mnemonic | description
0x4 | BEQ rs, rd, offset | if R[rs] == R[rd] then PC = PC+4 + (offset<<2)
0x5 | BNE rs, rd, offset | if R[rs] != R[rd] then PC = PC+4 + (offset<<2)
op | rs | rd | offset
6 bits | 5 bits | 5 bits | 16 bits
00010000101000010000000000000011
signed offsets
I-Type
Notes: Why should the offset be left shifted by 2. To keep the jump address word aligned.
AND to not waste two bits that we *know* are going to be 0.

## Slide 20: Control Flow: Branches
tgt
+4

Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
offset
+
=?
Notes: In the book, the ALU is used to determine the branch comparison. We are choosing to do it separately.
Anyway, can’t use ALU for both branc comparison and PC determination. At most, we can use it once. The book uses it for branch

## Slide 21: Control Flow: More Branches
op | rs | subop | offset
6 bits | 5 bits | 5 bits | 16 bits
00000100101000010000000000000010
signed offsets
almost I-Type
op | subop | mnemonic | description
0x1 | 0x0 | BLTZ rs, offset | if R[rs] < 0 then PC = PC+4+ (offset<<2)
0x1 | 0x1 | BGEZ rs, offset | if R[rs] ≥ 0 then PC = PC+4+ (offset<<2)
0x6 | 0x0 | BLEZ rs, offset | if R[rs] ≤ 0 then PC = PC+4+ (offset<<2)
0x7 | 0x0 | BGTZ rs, offset | if R[rs] > 0 then PC = PC+4+ (offset<<2)
Conditional Jumps (cont.)

## Slide 22: Control Flow: More Branches
tgt
+4

Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
offset
+
=?
cmp

## Slide 23: Control Flow: Jump and Link
op | mnemonic | description
0x3 | JAL target | r31 = PC+8 (+8 due to branch delay slot) PC = (PC+4)31..28  target  00
op | immediate
6 bits | 26 bits
00001101000000000000000000000001
J-Type
Discuss later
Function/procedure calls
Why?
Notes: 0x0121808 == 1185800

## Slide 24: Jump and Link
tgt
+4

Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
offset
+
=?
cmp
+4

## Slide 25: Goals for today
MIPS Datapath
  Memory layout
  Control Instructions
Performance
  How to get it?
  CPI (Cycles Per Instruction)
  MIPS (Instructions Per Cycle)
  Clock Frequency
Pipelining
  Latency vs throughput

## Slide 26: Questions
How do we measure performance?
What is the performance of a single cycle CPU?
How do I get performance?
See: P&H 1.6

## Slide 27: Performance
How do I get it?
Parallelism
Pipelining
Both!

## Slide 28: Performance: Aside
Speed of a circuit is affected by the number of gates in series (on the critical path or the deepest level of logic)
combinatorial
Logic
tcombinatorial
inputs arrive
outputs expected

## Slide 29: 4-bit Ripple Carry Adder
A3
B3
S3
C4
A1
B1
S1
A2
B2
S2
A0
B0
C0
S0
C1
C2
C3
First full adder, 2 gate delay
Second full adder, 2 gate delay
…
Carry ripples from lsb to msb

## Slide 30: Adding
Main ALU, slows us down
Does it need to be this slow?
Observations
Have to wait for Cin
Can we compute in parallel in some way?
CLA carry look-ahead adder

## Slide 31: Carry Look Ahead Logic
Can we reason Cout independent of Cin?
  Just based on (A,B) only
When is Cout == 1, irrespective of Cin?
If Cin == 1, when is Cout also == 1

## Slide 32: 1-bit Adder with Carry
A
B
S
Cin
Cout
A | B | Cin | Cout | S
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 1 | 1 | 1
Full Adder
Adds three 1-bit numbers
Computes 1-bit result and 1-bit carry
Can be cascaded

## Slide 33: 1-bit CLA adder
A
B
Cin
S
p
g
Create two terms: propagator, generator
g = 1, generates Cout: g = AB
  Irrespective of Cin
p = 1, propagates Cin to Cout: p = A + B
p and g generated in 1 gate delay
S is 2 gate delay after we get Cin

## Slide 34: 4-bit CLA
A
B
C0
p
g
A
B
p
g
A
B
p
g
A
B
p
g
CLA (carry look-ahead logic)
C1
C2
C3
C4
S

## Slide 35: Performance
How do I get it?
Parallelism
Pipelining
Both!

## Slide 36: Goals for today
MIPS Datapath
  Memory layout
  Control Instructions
Performance
  How to get it? Parallelism and Pipeline!
  CPI (Cycles Per Instruction)
  MIPS (Instructions Per Cycle)
  Clock Frequency
Pipelining
  Latency vs throughput
Next Time