## Slide 1: Performance and Pipelining
Prof. Hakim Weatherspoon
CS 3410, Spring 2015
Computer Science
Cornell University
See P&H Chapter: 1.6, 4.5-4.6

## Slide 3: Announcements
HW 1
Quite long. Do not wait till the end.
Project 1 design doc
Critical to do this, else Project 1 will be hard
HW 1 review session
Wed (2/18) @ 7:30pm and Sun (2/22) @ 5:00pm
Locations: Both in Upson B17
Prelim 1 review session
Next Tue (2/24) and Sun(2/28). 7:30pm.
Location: Olin 255 and Upson B17, respectively.

## Slide 4: Goals for today
Performance
  What is performance?
  How to get it?
Pipelining

## Slide 5: Performance
Complex question
  How fast is the processor?
  How fast your application runs?
  How quickly does it respond to you?
  How fast can you process a big batch of jobs?
  How much power does your machine use?

## Slide 6: Measures of Performance
Clock speed
  1 KHz, 103 Hz: cycle is 1 millisecond, ms, (10-6)
  1 MHz, 106 Hz: cycle is 1 microsecond, us, (10-6)
  1 Ghz, 109 Hz: cycle is 1 nanosecond, ns, (10-9)
  1 Thz, 1012 Hz: cycle is 1 picosecond, ps, (10-12)
Instruction/application performance
  MIPs (Millions of instructions per second)
  FLOPs (Floating point instructions per second)
    GPUs: GeForce GTX Titan (2,688 cores, 4.5 Tera flops, 7.1 billion transistors, 42 Gigapixel/sec fill rate, 288 GB/sec)
  Benchmarks (SPEC)
Notes: Peta: 10^(-15)
Exa: 10^(-18)
Zotta: 10^(-21)
Yotta: 10^(-24)
Benchmarks like SPEC are used to compare across architectures

## Slide 7: Measures of Performance
Latency
  How long to finish my program
    Response time, elapsed time, wall clock time
    CPU time: user and system time
Throughput
  How much work finished per unit time
Ideal: Want high throughput, low latency
… also, low power, cheap ($$) etc.

## Slide 8: How to make the computer faster?
Decrease latency
Critical Path
  Longest path determining the minimum time needed for an operation
  Determines minimum length of clock cycle i.e. determines maximum clock frequency
Optimize for latency on the critical path
    Parallelism (like carry look ahead adder)
    Pipelining
    Both
Notes: Is the the AND path or the 32 bit adder path that is going to determine your performance in your ALU from Lab1?
Critical path is what determines what is the slowest path through the logic. And therefore, it determines the minimum length of the cycle. That in turn determines the maximum clock frequency.
For example if the critical path is 1 nanosecond, the clock frequency is at most 1 GHz.

## Slide 9: Latency: Optimize Delay on Critical Path
E.g. Adder performance
32 Bit Adder Design | Space | Time
Ripple Carry | ≈ 300 gates | ≈ 64 gate delays
2-Way Carry-Skip | ≈ 360 gates | ≈ 35 gate delays
3-Way Carry-Skip | ≈ 500 gates | ≈ 22 gate delays
4-Way Carry-Skip | ≈ 600 gates | ≈ 18 gate delays
2-Way Look-Ahead | ≈ 550 gates | ≈ 16 gate delays
Split Look-Ahead | ≈ 800 gates | ≈ 10 gate delays
Full Look-Ahead | ≈ 1200 gates | ≈ 5 gate delays

## Slide 10: Multi-Cycle Instructions
But what to do when operations take diff. times?
E.g: Assume:
  load/store: 100 ns
  arithmetic: 50 ns
  branches: 33 ns
  Single-Cycle CPU
  10 MHz (100 ns cycle) with
    1 cycle per instruction
ms = 10-3 second
us = 10-6 seconds
ns = 10-9 seconds
ps = 10-12 seconds
10 MHz
20 MHz
30 MHz
Notes: 100ns = 10MHz; 50ns = 20MHz; 33ns = 30 MHz

## Slide 11: Multi-Cycle Instructions
  Multiple cycles to complete a single instruction
E.g: Assume:
  load/store: 100 ns
  arithmetic: 50 ns
  branches: 33 ns
  Multi-Cycle CPU
  30 MHz (33 ns cycle) with
    3 cycles per load/store
    2 cycles per arithmetic
    1 cycle per branch
ms = 10-3 second
us = 10-6 seconds
ns = 10-9 seconds
ps = 10-12 seconds
10 MHz
20 MHz
30 MHz
  Single-Cycle CPU
  10 MHz (100 ns cycle) with
    1 cycle per instruction
Which one is faster: Single- or Multi-Cycle CPU?
Notes: 100ns = 10MHz; 50ns = 20MHz; 33ns = 30 MHz

## Slide 12: Cycles Per Instruction (CPI)
Instruction mix for some program P, assume:
  25% load/store ( 3 cycles / instruction)
  60% arithmetic ( 2 cycles / instruction)
  15% branches ( 1 cycle / instruction)
Multi-Cycle performance for program P:
3 * .25 + 2 * .60 + 1 * .15 = 2.1
average cycles per instruction (CPI) = 2.1
Multi-Cycle @ 30 MHz
Single-Cycle @ 10 MHz
30M cycles/sec 2.1 cycles/instr ≈15 MIPS
vs
10 MIPS
MIPS = millions of instructions per second
= 10M cycles/sec  1 cycle/instr
Notes: 0.25 x 3 + 0.6 x 2 + 0.1 x 1 = 0.75 + 1.2 + .15 = 2.1

## Slide 13: Total Time
CPU Time = # Instructions x CPI x Clock Cycle Time
E.g. Say for a program with 400k instructions, 30 MHz:
CPU [Execution] Time = ?
= Instr x cycles/instr x seconds/cycle

## Slide 14: Total Time
CPU Time = # Instructions x CPI x Clock Cycle Time
E.g. Say for a program with 400k instructions, 30 MHz:
CPU [Execution] Time = 400k x 2.1 x 33 ns = 27 ms
= Instr x cycles/instr x seconds/cycle

## Slide 15: Total Time
CPU Time = # Instructions x CPI x Clock Cycle Time
E.g. Say for a program with 400k instructions, 30 MHz:
CPU [Execution] Time = 400k x 2.1 x 33 ns = 27 ms
How do we increase performance?
Need to reduce CPU time
  Reduce #instructions
  Reduce CPI
  Reduce Clock Cycle Time
= Instr x cycles/instr x seconds/cycle

## Slide 16: Example
Goal: Make Multi-Cycle @ 30 MHz CPU (15MIPS) run 2x faster by making arithmetic instructions faster
Instruction mix (for P):
  25% load/store, CPI = 3
  60% arithmetic, CPI = 2
  15% branches, CPI = 1
CPI = 0.25 x 3 + 0.6 x 2 + 0.15 x 1
= 2.1
Goal: Make processor run 2x faster,
i.e. 30 MIPS instead of 15 MIPS
Notes: So the goal is to make it run at 30 MIPs.
CPI = (.25 x 3 + .6 x 2 + .15 x 1)/1 = 2.1
MIPS = 30 MHz/2.1 = 14.28 MIPS. Call it 15 MIPS
Want to double MIPS from 15 MIPS (14.28 MIPS) to 30 MIPS (28.56 MIPS)

## Slide 17: Example
Goal: Make Multi-Cycle @ 30 MHz CPU (15MIPS) run 2x faster by making arithmetic instructions faster
Instruction mix (for P):
  25% load/store, CPI = 3
  60% arithmetic, CPI = 2 1
  15% branches, CPI = 1
First lets try CPI of 1 for arithmetic.
Is that 2x faster overall?
How much does it improve performance?
CPI = 0.25 x 3 + 0.6 x 1 + 0.15 x 1
= 1.5
No
Notes: So the goal is to make it run at approximately 30 MIPs.
Original CPI = (.25 x 3 + .6 x 2 + .15 x 1)/1 = 2.1
MIPS = 30 MHz/2.1 = 14.28 MIPS. Call it 15 MIPS
Say you drop the CPI for the arithmetic operation to 1. Will that double it? No.
.25 x 3 + .6 + .15 = 1.5
30 MHz/1.5 = 20MIPS

## Slide 18: Example
Goal: Make Multi-Cycle @ 30 MHz CPU (15MIPS) run 2x faster by making arithmetic instructions faster
Instruction mix (for P):
  25% load/store, CPI = 3
  60% arithmetic, CPI = 2 X
  15% branches, CPI = 1
But, want to half our CPI from 2.1 to 1.05.
Let new arithmetic operation have a CPI of X. X =?
Then, X = 0.25, which is a significant improvement
CPI = 1.05 = 0.25 x 3 + 0.6 x X + 0.15 x 1
1.05 = .75 + 0.6X + 0.15
X = 0.25
Notes: But we want to half our CPI. Let the new arithmetic operation have a CPI of x.
3 x .25 + x * 0.6 + .15 = 1.05
.75 + .15 + x * 0.6 = 1.05
x = 0.25
That’s a big improvement you need!

## Slide 19: Example
Goal: Make Multi-Cycle @ 30 MHz CPU (15MIPS) run 2x faster by making arithmetic instructions faster
Instruction mix (for P):
  25% load/store, CPI = 3
  60% arithmetic, CPI = 2 0.25
  15% branches, CPI = 1
To double performance CPI for arithmetic operations have to go from 2 to 0.25

## Slide 20: Amdahl’s Law
Amdahl’s Law
Execution time after improvement =
Or: Speedup is limited by popularity of improved feature
Corollary: Make the common case fast
Caveat: Law of diminishing returns
execution time affected by improvement
amount of improvement
+ execution time unaffected
contribution to execution time
Notes: Consider our GPU example with 2k cores.
Say we have a program that takes 2000 seconds to run: 200 seconds is the start up time (reading data), and 1800 is the “main” algorithm.! This doesn’t seem so bad. 200/2000 = 10% only of startup and 90% of the program is in the slow algorithm.
We want to speed it up by running on a GPU with 2000 cores! Ideally we would get 2000x speedup and the program will run in 1 second.
But when we port it to the GPU, we can only improve the “main” algorithm which is highly parallelizable. You can improve the 1800 seconds down to < 1 second say, because you can fully parallelize the algorithm on 2000 cores.
But still the time for the whole program is 201 seconds. So you threw 2000 cores at the problem, but your speedup is 2000/201 which is approximately 10x. So with 2000 cores you only got 10x speedup. Amdahl’s law expresses that “unfortunate” relation.

## Slide 21: Review: Single Cycle Processor
alu
PC
imm
memory
memory
din
dout
addr
target
offset
cmp
control
=?
new pc
register file
inst
extend
+4
+4

## Slide 22: Review: Single Cycle Processor
Advantages
  Single cycle per instruction make logic and clock simple
Disadvantages
  Since instructions take different time to finish, memory and functional unit are not efficiently utilized
  Cycle time is the longest delay
    Load instruction
  Best possible CPI is 1 (actually < 1 w parallelism)
    However, lower MIPS and longer clock period (lower clock frequency); hence, lower performance

## Slide 23: Review: Multi Cycle Processor
Advantages
  Better MIPS and smaller clock period (higher clock frequency)
  Hence, better performance than Single Cycle processor
Disadvantages
  Higher CPI than single cycle processor
Pipelining: Want better Performance
  want small CPI (close to 1) with high MIPS and short clock period (high clock frequency)

## Slide 24: Improving Performance
Parallelism
Pipelining
Both!

## Slide 25
Single Cycle vs Pipelined Processor
See: P&H Chapter 4.5

## Slide 26: The Kids
Alice
Bob
They don’t always get along…

## Slide 27: The Bicycle

## Slide 28: The Materials
Saw
Drill
Glue
Paint

## Slide 29: The Instructions
N pieces, each built following same sequence:
Saw
Drill
Glue
Paint

## Slide 30: Design 1: Sequential Schedule
Alice owns the room
Bob can enter when Alice is finished
Repeat for remaining tasks
No possibility for conflicts

## Slide 31: Sequential Performance
Elapsed Time for Alice: 4
Elapsed Time for Bob: 4
Total elapsed time: 4*N
Can we do better?
time 1 2 3 4 5 6 7 8 …
Latency:
Throughput:
Concurrency:
CPI =
Latency: 4 hours/task
Throughput: 1 task/4 hrs
Concurrency: 1
CPI = 4
Notes: Latency = 4
CPI = 4 (here the instruction is the construction of the bike)
Throughput = 2 bikes in 8 hrs. So 1 task in 4 hrs. So ¼ throughput
Concurrency: 1 (i.e. 1 task at a time)

## Slide 32: Design 2: Pipelined Design
Partition room into stages of a pipeline
One person owns a stage at a time
4 stages
4 people working simultaneously
Everyone moves right in lockstep
Alice
Bob
Carol
Dave

## Slide 33: Design 2: Pipelined Design
Partition room into stages of a pipeline
Alice
One person owns a stage at a time
4 stages
4 people working simultaneously
Everyone moves right in lockstep
It still takes all four stages for one job to complete

## Slide 34: Design 2: Pipelined Design
Partition room into stages of a pipeline
Alice
Bob
One person owns a stage at a time
4 stages
4 people working simultaneously
Everyone moves right in lockstep
It still takes all four stages for one job to complete

## Slide 35: Design 2: Pipelined Design
Partition room into stages of a pipeline
Alice
Bob
Carol
One person owns a stage at a time
4 stages
4 people working simultaneously
Everyone moves right in lockstep
It still takes all four stages for one job to complete

## Slide 36: Design 2: Pipelined Design
Partition room into stages of a pipeline
Alice
Bob
Carol
Dave
One person owns a stage at a time
4 stages
4 people working simultaneously
Everyone moves right in lockstep
It still takes all four stages for one job to complete

## Slide 37: Design 2: Pipelined Design
Partition room into stages of a pipeline
Alice
Alice
Alice
Alice
One person owns a stage at a time
4 stages
4 people working simultaneously
Everyone moves right in lockstep
It still takes all four stages for one job to complete

## Slide 38: Pipelined Performance
time 1 2 3 4 5 6 7…
What if some tasks don’t need drill?
Latency:
Throughput:
Concurrency:
Latency: 4 hrs/task
Throughput: 1 task/hr
Concurrency: 4
CPI = 1
Notes: Latency (Delay): 4 cycles / task
Throughput: 1 task / cycle (huge improvement) after your initial startup of filling the pipeline.
Parallelism: 4 concurrent tasks

## Slide 39: Pipelined Performance
Time
1 2 3 4 5 6 7 8 9 10
What if some tasks don’t need drill?
Latency:
Throughput:
CPI =
What if drilling takes twice as long, but gluing and paint take ½ as long?
Notes: Now what if drilling is twice as long but the gluing and paint are ½ each.

## Slide 40: Pipelined Performance
Time
1 2 3 4 5 6 7 8 9 10
What if some tasks don’t need drill?
Latency: 4 cycles/task
Throughput: 1 task/2 cycles
Done: 4 cycles
Done: 6 cycles
CPI = 2
Latency:
Throughput:
CPI =
What if drilling takes twice as long, but gluing and paint take ½ as long?
Done: 8 cycles
Notes: So total latency is still the same: 4
Throughput: 1 task / 2 cycle, First task out at cycle 4, second at 6, third at 8, fourth at 10. So ½. Not 1!
CPI: 2 cycles / task

## Slide 41: Lessons
Principle:
Throughput increased by parallel execution
Balanced pipeline very important
Else slowest stage dominates performance
Pipelining:
  Identify pipeline stages
  Isolate stages from each other
  Resolve pipeline hazards (next lecture)

## Slide 42: MIPs designed for pipelining
Instructions same length
  32 bits, easy to fetch and then decode
3 types of instruction formats
  Easy to route bits between stages
  Can read a register source before even knowing what the instruction is
Memory access through lw and sw only
  Access memory after ALU

## Slide 43: Basic Pipeline
Five stage “RISC” load-store architecture
  Instruction fetch (IF)
    get instruction from memory, increment PC
  Instruction Decode (ID)
    translate opcode into control signals and read registers
  Execute (EX)
    perform ALU operation, compute jump/branch targets
  Memory (MEM)
    access memory if needed
  Writeback (WB)
    update register file
Notes: This is simpler than the MIPS, but we’re using it to get the concepts across – everything you see here applies to MIPS, but we have to deal w/ fewer bits in these examples (that’s why I like them)

## Slide 44: A Processor
alu
PC
imm
memory
memory
din
dout
addr
target
offset
cmp
control
=?
new pc
register file
inst
extend
+4
+4
Review: Single cycle processor

## Slide 45: A Processor
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
register file
control
alu
imm
memory
din
dout
addr
inst
PC
memory
compute jump/branch targets
new pc
+4
extend
Notes: What does that do to a clock cycle. It is the time for 1 stage. So 5 times faster in this case (ASSUMING all stages are approximately equal sized)
Left to right flow except for the write-back phase and the branch targets that can change the PC. Otherwise left to right.

## Slide 46: A Processor
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
register file
control
alu
imm
memory
din
dout
addr
inst
PC
memory
compute jump/branch targets
new pc
+4
extend
Notes: What does that do to a clock cycle. It is the time for 1 stage. So 5 times faster in this case (ASSUMING all stages are approximately equal sized)
Left to right flow except for the write-back phase and the branch targets that can change the PC. Otherwise left to right.

## Slide 47: Time Graphs
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Clock cycle
Latency:
Throughput:
Concurrency:
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
Latency: 5 cycles
Throughput: 1 instr/cycle
Concurrency: 5
CPI = 1
add
lw
Notes: CPI = 1 (inverse of throughput)

## Slide 48: Principles of Pipelined Implementation
Break instructions across multiple clock cycles (five, in this case)
Design a separate stage for the execution performed during each clock cycle
Add pipeline registers (flip-flops) to isolate signals between different stages

## Slide 49: Pipelined Processor
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4

## Slide 50: IF
Stage 1: Instruction Fetch
Fetch a new instruction every cycle
  Current PC is index to instruction memory
  Increment the PC at end of cycle (assume no branches for now)
Write values of interest to pipeline register (IF/ID)
  Instruction bits (for later decoding)
  PC+4 (for later computing branch targets)
  Next stage will read this pipeline register
  Anything needed by later pipeline stages

## Slide 51: IF
PC
instruction memory
new pc
addr
mc
+4
- PC+4
- pcrel (PC-relative); e.g. BEQ, BNE
- pcabs (PC absolute); e.g. J and JAL
. (PC+4)31..28 • target • 00
- pcreg (PC registers); e.g. JR

## Slide 52: IF
PC
instruction memory
new pc
inst
addr
mc
00 = read word
IF/ID
Rest of pipeline
+4
PC+4
pcsel
pcreg
pcrel
pcabs

## Slide 53: ID
Stage 2: Instruction Decode
On every cycle:
  Read IF/ID pipeline register to get instruction bits
  Decode instruction, generate control signals
  Read from register file
Write values of interest to pipeline register (ID/EX)
  Control information, Rd index, immediates, offsets, …
  Contents of Ra, Rb
  PC+4 (for computing branch targets later)

## Slide 54: ID
ctrl
ID/EX
Rest of pipeline
PC+4
inst
IF/ID
PC+4
Stage 1: Instruction Fetch
register file
WE
Rd
Ra
Rb
D
B
A
B
A
imm
Notes: Early decode: decode all instr in ID, pass control signals to later stages
Late decode: decode some instr in ID, pass instr so each stage computes its own control signals

## Slide 55: ID
ctrl
ID/EX
Rest of pipeline
PC+4
inst
IF/ID
PC+4
Stage 1: Instruction Fetch
register file
WE
Rd
Ra
Rb
D
B
A
B
A
extend
imm
decode
result
dest
Notes: Early decode: decode all instr in ID, pass control signals to later stages
Late decode: decode some instr in ID, pass instr so each stage computes its own control signals

## Slide 56: EX
Stage 3: Execute
On every cycle:
  Read ID/EX pipeline register to get values and control bits
  Perform ALU operation
  Compute targets (PC+4+offset, etc.) in case this is a branch
  Decide if jump/branch should be taken
Write values of interest to pipeline register (EX/MEM)
  Control information, Rd index, …
  Result of ALU operation
  Value in case this is a memory store instruction

## Slide 57: EX
Stage 2: Instruction Decode
ctrl
EX/MEM
Rest of pipeline
B
D
ctrl
ID/EX
PC+4
B
A
alu
imm
target

## Slide 58: EX
Stage 2: Instruction Decode
pcrel
pcabs
ctrl
EX/MEM
Rest of pipeline
B
D
ctrl
ID/EX
PC+4
B
A
alu
+

branch?
imm
pcsel
pcreg
target

## Slide 59: MEM
Stage 4: Memory
On every cycle:
  Read EX/MEM pipeline register to get values and control bits
  Perform memory load/store if needed
    address is ALU result
Write values of interest to pipeline register (MEM/WB)
  Control information, Rd index, …
  Result of memory operation
  Pass result of ALU operation

## Slide 60: MEM
ctrl
MEM/WB
Rest of pipeline
Stage 3: Execute
M
D
ctrl
EX/MEM
B
D
memory
din
dout
addr
mc
target

## Slide 61: MEM
ctrl
MEM/WB
Rest of pipeline
Stage 3: Execute
M
D
ctrl
EX/MEM
B
D
memory
din
dout
addr
mc
target
branch?
pcsel
pcrel
pcabs
pcreg

## Slide 62: WB
Stage 5: Write-back
On every cycle:
  Read MEM/WB pipeline register to get values and control bits
  Select value and write to register file

## Slide 63: WB
Stage 4: Memory
ctrl
MEM/WB
M
D

## Slide 64: WB
Stage 4: Memory
ctrl
MEM/WB
M
D
result
dest

## Slide 65
IF/ID
+4
ID/EX
EX/MEM
MEM/WB
mem
din
dout
addr
inst
PC+4
OP
B
A
Rt
B
D
M
D
PC+4
imm
OP
Rd
OP
Rd
PC
inst mem
Rd
Ra
Rb
D
B
A
Rd

## Slide 66: Pipelining Recap
Pipelining is a powerful technique to mask latencies and increase throughput
  Logically, instructions execute one at a time
  Physically, instructions execute in parallel
    Instruction level parallelism
Abstraction promotes decoupling
  Interface (ISA) vs. implementation (Pipeline)