## Slide 1: Pipelining and Hazards
Prof. Hakim Weatherspoon
CS 3410, Spring 2015
Computer Science
Cornell University
See P&H Chapter: 4.6-4.8

## Slide 2: Announcements
Prelim next week
Tuesday at 7:30.
Go to location based on netid
[a-g]* → MRS146: Morrison Hall 146
[h-l]* → RRB125: Riley-Robb Hall 125
[m-n]*→ RRB105: Riley-Robb Hall 105
[o-s]* → MVRG71: M Van Rensselaer Hall G71
[t-z]* → MVRG73: M Van Rensselaer Hall G73
Prelim reviews
TODAY, Tue, Feb 24 @ 7:30pm in Olin 255
Sat, Feb 28 @ 7:30pm in Upson B17
Prelim conflicts
Contact Deniz Altinbuken <deniz@cs.cornell.edu>

## Slide 3: Announcements
Prelim1:
  Time: We will start at 7:30pm sharp, so come early
  Location: on previous slide
  Closed Book
    Cannot use electronic device or outside material
  Practice prelims are online in CMS
  Material covered everything up to end of this week
    Everything up to and including data hazards
    Appendix B (logic, gates, FSMs, memory, ALUs)
    Chapter 4 (pipelined [and non] MIPS processor with hazards)
    Chapters 2 (Numbers / Arithmetic, simple MIPS instructions)
    Chapter 1 (Performance)
    HW1, Lab0, Lab1, Lab2, C-Lab0, C-Lab1

## Slide 4: Goals for Today
RISC and Pipelined Processor: Putting it all together
Data Hazards
  Data dependencies
  Problem, detection, and solutions
    (delaying, stalling, forwarding, bypass, etc)
  Hazard detection unit
  Forwarding unit
Next time
  Control Hazards
  What is the next instruction to execute if
  a branch is taken? Not taken?

## Slide 5: MIPS Design Principles
Simplicity favors regularity
  32 bit instructions
Smaller is faster
  Small register file
Make the common case fast
  Include support for constants
Good design demands good compromises
  Support for different type of interpretations/classes

## Slide 6: Recall: MIPS instruction formats
All MIPS instructions are 32 bits long, has 3 formats
R-type
I-type
J-type
op | rs | rt | rd | shamt | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
op | rs | rt | immediate
6 bits | 5 bits | 5 bits | 16 bits
op | immediate (target address)
6 bits | 26 bits

## Slide 7: Recall: MIPS Instruction Types
Arithmetic/Logical
  R-type: result and two source registers, shift amount
  I-type: 16-bit immediate with sign/zero extension
Memory Access
  load/store between registers and memory
  word, half-word and byte operations
Control flow
  conditional branches: pc-relative addresses
  jumps: fixed offsets, register absolute

## Slide 8: Recall: MIPS Instruction Types
Arithmetic/Logical
  ADD, ADDU, SUB, SUBU, AND, OR, XOR, NOR, SLT, SLTU
  ADDI, ADDIU, ANDI, ORI, XORI, LUI, SLL, SRL, SLLV, SRLV, SRAV, SLTI, SLTIU
  MULT, DIV, MFLO, MTLO, MFHI, MTHI
Memory Access
  LW, LH, LB, LHU, LBU, LWL, LWR
  SW, SH, SB, SWL, SWR
Control flow
  BEQ, BNE, BLEZ, BLTZ, BGEZ, BGTZ
  J, JR, JAL, JALR, BEQL, BNEL, BLEZL, BGTZL
Special
  LL, SC, SYSCALL, BREAK, SYNC, COPROC

## Slide 9: Pipelining
Principle:
Throughput increased by parallel execution
Balanced pipeline very important
Else slowest stage dominates performance
Pipelining:
  Identify pipeline stages
  Isolate stages from each other
  Resolve pipeline hazards (this and next lecture)

## Slide 10: Basic Pipeline
Five stage “RISC” load-store architecture
  Instruction fetch (IF)
    get instruction from memory, increment PC
  Instruction Decode (ID)
    translate opcode into control signals and read registers
  Execute (EX)
    perform ALU operation, compute jump/branch targets
  Memory (MEM)
    access memory if needed
  Writeback (WB)
    update register file
Notes: This is simpler than the MIPS, but we’re using it to get the concepts across – everything you see here applies to MIPS, but we have to deal w/ fewer bits in these examples (that’s why I like them)

## Slide 11: Pipelined Implementation
Each instruction goes through the 5 stages
  Each stage takes one clock cycle
    So slowest stage determines clock cycle time

## Slide 12: Time Graphs
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Clock cycle
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
add
lw
Notes: CPI = 1 (inverse of throughput)

## Slide 13: Pipelined Implementation
Each instruction goes through the 5 stages
  Each stage takes one clock cycle
    So slowest stage determines clock cycle time
Stages must share information. How?
  Add pipeline registers (flip-flops) to pass results between different stages

## Slide 14: Pipelined Processor
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
compute jump/branch targets
+4
Fetch
Decode
Execute
Memory
WB

## Slide 15: Pipelined Processor
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4

## Slide 16: Pipelined Implementation
Each instruction goes through the 5 stages
  Each stage takes one clock cycle
    So slowest stage determines clock cycle time
Stages must share information. How?
  Add pipeline registers (flip-flops) to pass results between different stages
  And is this it?
  Not quite….

## Slide 17: Hazards
3 kinds
  Structural hazards
    Multiple instructions want to use same unit
  Data hazards
    Results of instruction needed before ready
  Control hazards
    Don’t know which side of branch to take
Will get back to this
First, how to pipeline when no hazards
Notes: Structural: say only 1 memory for instruction read and the MEM stage. That is a structural hazard. We have designed the MIPS ISA and our implementation of separate memory for instruction and data to avoid this problem. MIPS is designed very carefully to not have any structural hazards.
Data hazards arise when data needed by one instruction has not yet been computed (because it is further down the pipeline). We need a solution for this.
Control hazards arise when we don’t know what the PC will be. This makes it not possible to push the next instruction down the pipeline. Till we know what the issue is.

## Slide 18: Pipelined Processor
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4

## Slide 19: Example: : Sample Code (Simple)
add r3, r1, r2; nand r6, r4, r5; lw r4, 20(r2); add r5, r2, r5; sw r7, 12(r3);

## Slide 20: Example: Sample Code (Simple)
Assume eight-register machine
Run the following code on a pipelined datapath
  add r3 r1 r2 ; reg 3 = reg 1 + reg 2
  nand r6 r4 r5 ; reg 6 = ~(reg 4 & reg 5)
  lw r4 20 (r2) ; reg 4 = Mem[reg2+20]
  add r5 r2 r5 ; reg 5 = reg 2 + reg 5
  sw r7 12(r3) ; Mem[reg3+12] = reg 7
Slides thanks to Sally McKee

## Slide 21
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 11-15
Bits 16-20
op
Rt
imm
valB
valA
PC+4
PC+4
target
ALU
result
op
dest
valB
op
dest
ALU
result
mdata
instruction
0
R2
R3
R4
R5
R1
R6
R0
R7
regA
regB
Bits 26-31
data
dest
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
M
U
X
Rd

## Slide 22
PC
Inst
mem
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 11-15
Bits 16-20
nop
0
0
0
0
0
0
0
nop
0
0
nop
0
0
0
0
nop
9
12
18
7
36
41
0
22
R2
R3
R4
R5
R1
R6
R0
R7
Bits 26-31
data
dest
Initial
State
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
0
M
U
X
0
At time 1,
Fetch
add r3 r1 r2
0
Time: 0
4

## Slide 23: Takeaway
Pipelining is a powerful technique to mask latencies and increase throughput
  Logically, instructions execute one at a time
  Physically, instructions execute in parallel
    Instruction level parallelism
Abstraction promotes decoupling
  Interface (ISA) vs. implementation (Pipeline)

## Slide 24: Hazards
See P&H Chapter: 4.7-4.8

## Slide 25: Hazards
3 kinds
  Structural hazards
    Multiple instructions want to use same unit
  Data hazards
    Results of instruction needed before
  Control hazards
    Don’t know which side of branch to take
Notes: Structural: say only 1 memory for instruction read and the MEM stage. That is a structural hazard. We have designed the MIPS ISA and our implementation of separate memory for instruction and data to avoid this problem. MIPS is designed very carefully to not have any structural hazards.
Data hazards arise when data needed by one instruction has not yet been computed (because it is further down the pipeline). We need a solution for this.
Control hazards arise when we don’t know what the PC will be. This makes it not possible to push the next instruction down the pipeline. Till we know what the issue is.

## Slide 26: Next Goal
What about data dependencies (also known as a data hazard in a pipelined processor)?
i.e. add r3, r1, r2
sub r5, r3, r4
Need to detect and then fix such hazards

## Slide 27: Data Hazards
Data Hazards
  register file reads occur in stage 2 (ID)
  register file writes occur in stage 5 (WB)
  next instructions may read values about to be written
    i.e instruction may need values that are being computed further down the pipeline
    in fact, this is quite common
“earlier” = started earlier
= stage right
stage left
  destination reg of earlier instruction == source reg of current
Notes: assumes (WE=0 implies rD=0) everywhere, similar for rA needed, rB needed (can ensure this in ID stage)

## Slide 28: Data Hazards
Clock cycle
1 2 3 4 5 6 7 8 9
sub r5, r3, r4
lw r6, 4(r3)
or r5, r3, r5
sw r6, 12(r3)
add r3, r1, r2
time

## Slide 29: Data Hazards
Data Hazards
  register file reads occur in stage 2 (ID)
  register file writes occur in stage 5 (WB)
  next instructions may read values about to be written
i.e. add r3, r1, r2
sub r5, r3, r4
How to detect?
“earlier” = started earlier
= stage right
stage left
  destination reg of earlier instruction == source reg of current
Notes: assumes (WE=0 implies rD=0) everywhere, similar for rA needed, rB needed (can ensure this in ID stage)

## Slide 30
IF/ID
+4
ID/EX
EX/MEM
MEM/WB
mem
din
dout
addr
inst
PC+4
OP
B
A
Rt
B
D
M
D
PC+4
imm
OP
Rd
OP
Rd
PC
inst mem
Rd
Ra
Rb
D
B
A
Rd
Detecting Data Hazards
IF/ID.Ra ≠ 0 &&
(IF/ID.Ra==ID/Ex.Rd
IF/ID.Ra==Ex/M.Rd
IF/ID.Ra==M/W.Rd)

## Slide 31: Data Hazards
Data Hazards
  register file reads occur in stage 2 (ID)
  register file writes occur in stage 5 (WB)
  next instructions may read values about to be written
How to detect? Logic in ID stage:
stall = (IF/ID.Ra != 0 &&
(IF/ID.Ra == ID/EX.Rd || IF/ID.Ra == EX/M.Rd || IF/ID.Ra == M/WB.Rd))
|| (same for Rb)
“earlier” = started earlier
= stage right
stage left
  destination reg of earlier instruction == source reg of current
Notes: assumes (WE=0 implies rD=0) everywhere, similar for rA needed, rB needed (can ensure this in ID stage)

## Slide 32: Detecting Data Hazards
IF/ID
+4
ID/EX
EX/MEM
MEM/WB
mem
din
dout
addr
PC
inst mem
Rd
Ra
Rb
D
B
A
detect hazard
Rd
add r3, r1, r2
sub r5, r3, r5
or r6, r3, r4
add r6, r3, r8
inst
PC+4
OP
B
A
Rt
B
D
M
D
PC+4
imm
OP
Rd
OP
Rd

## Slide 33: Takeaway
Data hazards occur when a operand (register) depends on the result of a previous instruction that may not be computed yet. A pipelined processor needs to detect data hazards.

## Slide 34: Next Goal
What to do if data hazard detected?
Notes: Nothing: Modify ISA to match implementation
Stall: Pause current and all subsequent instruction
Forward/Bypass: Steal correct value from elsewhere in pipeline

## Slide 35: Stalling
How to stall an instruction in ID stage
  prevent IF/ID pipeline register update
    stalls the ID stage instruction
  convert ID stage instr into nop for later stages
    innocuous “bubble” passes through pipeline
  prevent PC update
    stalls the next (IF stage) instruction
Notes: prev slide:
Q: what happens if branch in EX?
A: bad stuff: we miss the branch
So: lets try not to stall

## Slide 36: Detecting Data Hazards
IF/ID
+4
ID/EX
EX/MEM
MEM/WB
mem
din
dout
addr
PC
inst mem
Rd
Ra
Rb
D
B
A
detect hazard
Rd
add r3, r1, r2
sub r5, r3, r5
or r6, r3, r4
add r6, r3, r8
inst
PC+4
OP
B
A
Rt
B
D
M
D
PC+4
imm
OP
Rd
OP
Rd
If detect hazard
WE=0
MemWr=0
RegWr=0

## Slide 37: Stalling
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r5 |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
add r6, r3, r8 |  |  |  |  |  |  |  |  | 
IF | ID 11=r1 22=r2 | EX D=33 | MEM D=33 | WB r3=33 |  |  |  | 
 | IF | ID ?=r3 | ID ?=r3 | ID ?=r3 | ID 33=r3 | EX | MEM | WB
 |  | IF | IF | IF | IF | ID 33=r3 | EX | M
 |  |  |  |  |  | IF | ID 33=r3 | EX
time
Notes: find hazards first, then draw

## Slide 38: Stalling
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r5 |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
add r6, r3, r8 |  |  |  |  |  |  |  |  | 
IF | ID 11=r1 22=r2 | EX D=33 | MEM D=33 | WB r3=33 |  |  |  | 
 | IF | ID ?=r3 | ID ?=r3 | ID ?=r3 | ID 33=r3 | EX | MEM | WB
 |  | IF | IF | IF | IF | ID 33=r3 | EX | M
 |  |  |  |  |  | IF | ID 33=r3 | EX
r3 = 10
r3 = 20
time
IF
ID
Ex
M
W
IF
ID
Ex
M
W
IF
ID
Ex
M
ID
ID
ID
IF
IF
IF
IF
ID
Ex
Stalls
3
Stall
Notes: find hazards first, then draw

## Slide 39: Stalling
data mem
B
A
B
D
M
D
inst mem
D rD
B
A
Rd
Rd
Rd
WE
WE
Op
WE
Op
rA rB
PC
+4
Op
nop
inst
/stall
add r3,r1,r2
(MemWr=0
RegWr=0)
NOP = If(IF/ID.rA ≠ 0 &&
(IF/ID.rA==ID/Ex.Rd
IF/ID.rA==Ex/M.Rd
IF/ID.rA==M/W.Rd))
sub r5,r3,r5
or r6,r3,r4
(WE=0)
Notes: draw control signals for /stall
Q: what happens if branch in EX?
A: bad stuff: we miss the branch
So: lets try not to stall

## Slide 40: Stalling
data mem
B
A
B
D
M
D
inst mem
D rD
B
A
Rd
Rd
Rd
WE
WE
Op
WE
Op
rA rB
PC
+4
Op
nop
inst
/stall
nop
(MemWr=0
RegWr=0)
NOP = If(IF/ID.rA ≠ 0 &&
(IF/ID.rA==ID/Ex.Rd
IF/ID.rA==Ex/M.Rd
IF/ID.rA==M/W.Rd))
add r3,r1,r2
sub r5,r3,r5
(MemWr=0
RegWr=0)
or r6,r3,r4
(WE=0)
Notes: draw control signals for /stall
Q: what happens if branch in EX?
A: bad stuff: we miss the branch
So: lets try not to stall

## Slide 41: Stalling
data mem
B
A
B
D
M
D
inst mem
D rD
B
A
Rd
Rd
Rd
WE
WE
Op
WE
Op
rA rB
PC
+4
Op
nop
inst
/stall
(MemWr=0
RegWr=0)
NOP = If(IF/ID.rA ≠ 0 &&
(IF/ID.rA==ID/Ex.Rd
IF/ID.rA==Ex/M.Rd
IF/ID.rA==M/W.Rd))
add r3,r1,r2
sub r5,r3,r5
nop
nop
(MemWr=0
RegWr=0)
(MemWr=0
RegWr=0)
or r6,r3,r4
(WE=0)
Notes: draw control signals for /stall
Q: what happens if branch in EX?
A: bad stuff: we miss the branch
So: lets try not to stall

## Slide 42: Stalling
How to stall an instruction in ID stage
  prevent IF/ID pipeline register update
    stalls the ID stage instruction
  convert ID stage instr into nop for later stages
    innocuous “bubble” passes through pipeline
  prevent PC update
    stalls the next (IF stage) instruction
Notes: prev slide:
Q: what happens if branch in EX?
A: bad stuff: we miss the branch
So: lets try not to stall

## Slide 43: Takeaway
Data hazards occur when a operand (register) depends on the result of a previous instruction that may not be computed yet. A pipelined processor needs to detect data hazards.
Stalling, preventing a dependent instruction from advancing, is one way to resolve data hazards.
Stalling introduces NOPs (“bubbles”) into a pipeline. Introduce NOPs by (1) preventing the PC from updating, (2) preventing writes to IF/ID registers from changing, and (3) preventing writes to memory and register file.
*Bubbles in pipeline significantly decrease performance.

## Slide 44: Next Goal: Resolving Data Hazards via Forwarding
What to do if data hazard detected?
Wait/Stall
Reorder in Software (SW)
Forward/Bypass
Notes: Nothing: Modify ISA to match implementation
Stall: Pause current and all subsequent instruction
Forward/Bypass: Steal correct value from elsewhere in pipeline

## Slide 45: Forwarding
Forwarding bypasses some pipelined stages forwarding a result to a dependent instruction operand (register).
Three types of forwarding/bypass
  Forwarding from Ex/Mem registers to Ex stage (MEx)
  Forwarding from Mem/WB register to Ex stage (WEx)
  RegisterFile Bypass

## Slide 46: Forwarding Datapath
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
detect hazard
Three types of forwarding/bypass
Forwarding from Ex/Mem registers to Ex stage (MEx)
Forwarding from Mem/WB register to Ex stage (W  Ex)
RegisterFile Bypass
IF/ID
ID/Ex
Ex/Mem
Mem/WB
forward unit
Notes: draw control signals

## Slide 47: Forwarding Datapath
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
forward unit
detect hazard
Three types of forwarding/bypass
Forwarding from Ex/Mem registers to Ex stage (MEx)
Forwarding from Mem/WB register to Ex stage (W  Ex)
RegisterFile Bypass
IF/ID
ID/Ex
Ex/Mem
Mem/WB
Notes: draw control signals

## Slide 48: Forwarding Datapath 1
Ex/MEM to EX Bypass
  EX needs ALU result that is still in MEM stage
  Resolve:
  Add a bypass from EX/MEM.D to start of EX
How to detect? Logic in Ex Stage:
forward = (Ex/M.WE && EX/M.Rd != 0 &&
ID/Ex.Ra == Ex/M.Rd)
|| (same for Rb)
“earlier” = started earlier
= stage right
stage left
  destination reg of earlier instruction == source reg of current
Notes: assumes (WE=0 implies rD=0) everywhere, similar for rA needed, rB needed (can ensure this in ID stage)

## Slide 49: Forwarding Datapath
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
forward unit
detect hazard
Three types of forwarding/bypass
Forwarding from Ex/Mem registers to Ex stage (MEx)
Forwarding from Mem/WB register to Ex stage (W  Ex)
RegisterFile Bypass
IF/ID
ID/Ex
Ex/Mem
Mem/WB
Notes: draw control signals

## Slide 50: Forwarding Datapath 1
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r1 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A

## Slide 51: Forwarding Datapath 2
Mem/WB to EX Bypass
  EX needs value being written by WB
  Resolve:
  Add bypass from WB final value to start of EX
How to detect? Logic in Ex Stage:
forward = (M/WB.WE && M/WB.Rd != 0 &&
ID/Ex.Ra == M/WB.Rd &&
not (Ex/M.WE && Ex/M.Rd != 0 &&
ID/Ex.Ra == Ex/M.Rd)
|| (same for Rb)
“earlier” = started earlier
= stage right
stage left
  destination reg of earlier instruction == source reg of current
Check pg. 311
Notes: assumes (WE=0 implies rD=0) everywhere, similar for rA needed, rB needed (can ensure this in ID stage)

## Slide 52: Forwarding Datapath
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
forward unit
detect hazard
Three types of forwarding/bypass
Forwarding from Ex/Mem registers to Ex stage (MEx)
Forwarding from Mem/WB register to Ex stage (W  Ex)
RegisterFile Bypass
IF/ID
ID/Ex
Ex/Mem
Mem/WB
Notes: draw control signals

## Slide 53: Forwarding Datapath 2
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r1 |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A

## Slide 54: Register File Bypass
Register File Bypass
  Reading a value that is currently being written
Detect:
((Ra == MEM/WB.Rd) or (Rb == MEM/WB.Rd)) and (WB is writing a register)
Resolve:
Add a bypass around register file (WB to ID)
Better: (Hack) just negate register file clock
    writes happen at end of first half of each clock cycle
    reads happen during second half of each clock cycle

## Slide 55: Forwarding Datapath
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
forward unit
detect hazard
Three types of forwarding/bypass
Forwarding from Ex/Mem registers to Ex stage (MEx)
Forwarding from Mem/WB register to Ex stage (W  Ex)
RegisterFile Bypass
IF/ID
ID/Ex
Ex/Mem
Mem/WB
Notes: draw control signals

## Slide 56: Register File Bypass
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r1 |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
add r6, r3, r8 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A

## Slide 57: Forwarding Example
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r5 |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
add r6, r3, r8 |  |  |  |  |  |  |  |  | 
IF | ID 11=r1 22=r2 | EX D=33 | MEM D=33 | WB r3=33 |  |  |  | 
 | IF | ID 33=r3 | EX | MEM | WB |  |  | 
 |  | IF | ID 33=r3 | EX | MEM | WB |  | 
 |  |  | IF | ID 33=r3 | EX | MEM | WB | 
r3 = 10
r3 = 20
time

## Slide 58: Forwarding Example 2
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r4 |  |  |  |  |  |  |  |  | 
lw r6, 4(r3) |  |  |  |  |  |  |  |  | 
or r5, r3, r5 |  |  |  |  |  |  |  |  | 
sw r6, 12(r3) |  |  |  |  |  |  |  |  | 
IF | ID 11=r1 22=r2 | EX D=33 | MEM D=33 | WB r3=33 |  |  |  | 
 | IF | ID 33=r3 | EX D=55 | MEM D=55 | WB r5=55 |  |  | 
 |  | IF | ID 33=r3 | EX D=? | MEM D=66 | WB r6=66 |  | 
 |  |  | IF | ID 33=r3 55=r5 | EX | MEM | WB | 
 |  |  |  | IF | ID 33=r3 66=r6 | EX | MEM | 
IF
ID
Ex
M
W
IF
ID
Ex
M
W
time
Notes: identify hazards then draw; if “or” had used r6, would have needed to stall

## Slide 59: Forwarding Datapath
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
forward unit
detect hazard
Three types of forwarding/bypass
Forwarding from Ex/Mem registers to Ex stage (MEx)
Forwarding from Mem/WB register to Ex stage (W  Ex)
Register File Bypass
IF/ID
ID/Ex
Ex/Mem
Mem/WB
Notes: draw control signals

## Slide 60: Takeaway
Data hazards occur when a operand (register) depends on the result of a previous instruction that may not be computed yet. A pipelined processor needs to detect data hazards.
Stalling, preventing a dependent instruction from advancing, is one way to resolve data hazards. Stalling introduces NOPs (“bubbles”) into a pipeline. Introduce NOPs by (1) preventing the PC from updating, (2) preventing writes to IF/ID registers from changing, and (3) preventing writes to memory and register file. Bubbles (nops) in pipeline significantly decrease performance.
Forwarding bypasses some pipelined stages forwarding a result to a dependent instruction operand (register). Better performance than stalling.

## Slide 61: Data Hazard Recap
Stall
  Pause current and all subsequent instructions
Forward/Bypass
  Try to steal correct value from elsewhere in pipeline
  Otherwise, fall back to stalling or require a delay slot
Tradeoffs?
Notes: 1: ISA tied to impl; messy asm; impl easy & cheap; perf depends on asm.
2: ISA correctness not tied to impl; clean+slow asm, or messy+fast asm; impl easy and cheap; same perf as 1. 3: ISA perf not tied to impl; clean+fast asm; impl is tricky; best perf