## Slide 1: Data and Control Hazards
Prof. Hakim Weatherspoon
CS 3410, Spring 2015
Computer Science
Cornell University
See P&H Chapter: 4.6-4.8

## Slide 2: Announcements
Prelim next week
Tuesday at 7:30.
Go to location based on netid
[a-g]* → MRS146: Morrison Hall 146
[h-l]* → RRB125: Riley-Robb Hall 125
[m-n]*→ RRB105: Riley-Robb Hall 105
[o-s]* → MVRG71: M Van Rensselaer Hall G71
[t-z]* → MVRG73: M Van Rensselaer Hall G73
Prelim reviews
Yesterday, Tue, Feb 24 @ 7:30pm in Olin 255
SATURDAY, Feb 28 @ 7:30pm in Upson B17
Prelim conflicts
Contact Deniz Altinbuken <deniz@cs.cornell.edu>

## Slide 3: Announcements
Prelim1:
  Time: We will start at 7:30pm sharp, so come early
  Location: on previous slide
  Closed Book
    Cannot use electronic device or outside material
  Practice prelims are online in CMS
Material covered everything up to end of this week
  Everything up to and including data hazards
  Appendix B (logic, gates, FSMs, memory, ALUs)
  Chapter 4 (pipelined [and non] MIPS processor with hazards)
  Chapters 2 (Numbers / Arithmetic, simple MIPS instructions)
  Chapter 1 (Performance)
  HW1, Lab0, Lab1, Lab2, C-Lab0, C-Lab1

## Slide 4: Goals for Today
Data Hazards
  Data dependencies
  Problem, detection, and solutions
    (delaying, stalling, forwarding, bypass, etc)
  Hazard detection unit
  Forwarding unit
Control Hazards
  What is the next instruction to execute if a branch is taken? Not taken?
  How to resolve control hazards
  Optimizations

## Slide 5: Hazards
3 kinds
  Structural hazards
    Multiple instructions want to use same unit
  Data hazards
    Results of instruction needed before
  Control hazards
    Don’t know which side of branch to take
Notes: Structural: say only 1 memory for instruction read and the MEM stage. That is a structural hazard. We have designed the MIPS ISA and our implementation of separate memory for instruction and data to avoid this problem. MIPS is designed very carefully to not have any structural hazards.
Data hazards arise when data needed by one instruction has not yet been computed (because it is further down the pipeline). We need a solution for this.
Control hazards arise when we don’t know what the PC will be. This makes it not possible to push the next instruction down the pipeline. Till we know what the issue is.

## Slide 6: How to handle data hazards
What to do if data hazard detected?
i.e. add r3, r1, r2
sub r5, r3, r4
Options
  Nothing
    Change the ISA to match implementation
  Stall
    Pause current and subsequent instructions till safe
      Slow down the pipeline (add bubbles to pipeline)
  Forward/bypass
    Forward data value to where it is needed
Notes: Nothing: Modify ISA to match implementation (not great as an option, violates abstraction. Requires restructuring by application. Might not always be possible).
Stall: Pause current and all subsequent instruction
Forward/Bypass: Steal correct value from elsewhere in pipeline

## Slide 7: Data Hazards
Data Hazards
  register file reads occur in stage 2 (ID)
  register file writes occur in stage 5 (WB)
  next instructions may read values about to be written
“earlier” = started earlier
= stage right
stage left
  destination reg of earlier instruction == source reg of current
Notes: assumes (WE=0 implies rD=0) everywhere, similar for rA needed, rB needed (can ensure this in ID stage)

## Slide 8: Data Hazards
Stall
  Pause current and all subsequent instructions
Forward/Bypass
  Try to steal correct value from elsewhere in pipeline
  Otherwise, fall back to stalling or require a delay slot
Tradeoffs?
Notes: 1: ISA tied to impl; messy asm; impl easy & cheap; perf depends on asm.
2: ISA correctness not tied to impl; clean+slow asm, or messy+fast asm; impl easy and cheap; same perf as 1. 3: ISA perf not tied to impl; clean+fast asm; impl is tricky; best perf

## Slide 9: Data Hazards
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
detect hazard
IF/ID
ID/Ex
Ex/Mem
Mem/WB
forward unit
stall = If(IF/ID.Ra ≠ 0 &&
(IF/ID.Ra == ID/Ex.Rd
IF/ID.Ra == Ex/M.Rd
IF/ID.Ra == M/W.Rd))
Rd
Notes: draw control signals

## Slide 10: Data Hazards
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
forward unit
detect hazard
Three types of forwarding/bypass
Forwarding from Ex/Mem registers to Ex stage (MEx)
Forwarding from Mem/WB register to Ex stage (W  Ex)
RegisterFile Bypass
IF/ID
ID/Ex
Ex/Mem
Mem/WB
Notes: draw control signals

## Slide 11: Stalling
  Pause current and all subsequent instructions
“slow down the pipeline”

## Slide 12: Stalling
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r5 |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
add r6, r3, r8 |  |  |  |  |  |  |  |  | 
IF | ID 11=r1 22=r2 | EX D=33 | MEM D=33 | WB r3=33 |  |  |  | 
 | IF | ID ?=r3 | ID ?=r3 | ID ?=r3 | ID 33=r3 | EX | MEM | WB
 |  | IF | IF | IF | IF | ID 33=r3 | EX | M
 |  |  |  |  |  | IF | ID 33=r3 | EX
r3 = 10
r3 = 20
time
IF
ID
Ex
M
W
IF
ID
Ex
M
W
IF
ID
Ex
M
ID
ID
ID
IF
IF
IF
IF
ID
Ex
Stalls
3
Stall
Notes: find hazards first, then draw

## Slide 13: Stalling
data mem
B
A
B
D
M
D
inst mem
D rD
B
A
Rd
Rd
Rd
WE
WE
Op
WE
Op
rA rB
PC
+4
Op
nop
inst
/stall
add r3,r1,r2
(MemWr=0
RegWr=0)
NOP = If(IF/ID.rA ≠ 0 &&
(IF/ID.rA==ID/Ex.Rd
IF/ID.rA==Ex/M.Rd
IF/ID.rA==M/W.Rd))
sub r5,r3,r5
or r6,r3,r4
(WE=0)
Notes: draw control signals for /stall
Q: what happens if branch in EX?
A: bad stuff: we miss the branch
So: lets try not to stall

## Slide 14: Stalling
data mem
B
A
B
D
M
D
inst mem
D rD
B
A
Rd
Rd
Rd
WE
WE
Op
WE
Op
rA rB
PC
+4
Op
nop
inst
/stall
nop
(MemWr=0
RegWr=0)
NOP = If(IF/ID.rA ≠ 0 &&
(IF/ID.rA==ID/Ex.Rd
IF/ID.rA==Ex/M.Rd
IF/ID.rA==M/W.Rd))
add r3,r1,r2
sub r5,r3,r5
(MemWr=0
RegWr=0)
or r6,r3,r4
(WE=0)
Notes: draw control signals for /stall
Q: what happens if branch in EX?
A: bad stuff: we miss the branch
So: lets try not to stall

## Slide 15: Stalling
data mem
B
A
B
D
M
D
inst mem
D rD
B
A
Rd
Rd
Rd
WE
WE
Op
WE
Op
rA rB
PC
+4
Op
nop
inst
/stall
(MemWr=0
RegWr=0)
NOP = If(IF/ID.rA ≠ 0 &&
(IF/ID.rA==ID/Ex.Rd
IF/ID.rA==Ex/M.Rd
IF/ID.rA==M/W.Rd))
add r3,r1,r2
sub r5,r3,r5
nop
nop
(MemWr=0
RegWr=0)
(MemWr=0
RegWr=0)
or r6,r3,r4
(WE=0)
Notes: draw control signals for /stall
Q: what happens if branch in EX?
A: bad stuff: we miss the branch
So: lets try not to stall

## Slide 16: Stalling
How to stall an instruction in ID stage
  prevent IF/ID pipeline register update
    stalls the ID stage instruction
  convert ID stage instr into nop for later stages
    innocuous “bubble” passes through pipeline
  prevent PC update
    stalls the next (IF stage) instruction
Notes: prev slide:
Q: what happens if branch in EX?
A: bad stuff: we miss the branch
So: lets try not to stall

## Slide 17: Forwarding
Alternative to stalling, we can forward
Forwarding bypasses some pipelined stages forwarding a result to a dependent instruction operand (register)
Three types of forwarding/bypass
  Forwarding from Ex/Mem registers to Ex stage (MEx)
  Forwarding from Mem/WB register to Ex stage (WEx)
  RegisterFile Bypass

## Slide 18: Forwarding Example
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r5 |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
add r6, r3, r8 |  |  |  |  |  |  |  |  | 
IF | ID 11=r1 22=r2 | EX D=33 | MEM D=33 | WB r3=33 |  |  |  | 
 | IF | ID 33=r3 | EX | MEM | WB |  |  | 
 |  | IF | ID 33=r3 | EX | MEM | WB |  | 
 |  |  | IF | ID 33=r3 | EX | MEM | WB | 
IF
ID
Ex
M
W
IF
ID
IF
W
Ex
M
W
ID
Ex
M
IF
ID
Ex
r3 = 10
r3 = 20
time
M
W

## Slide 19: Forwarding
Alternative to stalling, we can forward
Forwarding bypasses some pipelined stages forwarding a result to a dependent instruction operand (register)
Three types of forwarding/bypass
  Forwarding from Ex/Mem registers to Ex stage (MEx)
  Forwarding from Mem/WB register to Ex stage (WEx)
  RegisterFile Bypass

## Slide 20: Forwarding Datapath 1
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r1 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
M
W
IF
ID
Ex
IF
ID
Ex
M
W
Notes: Note that the arrow is not going backward in time.

## Slide 21: Forwarding Datapath
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
detect hazard
Three types of forwarding/bypass
Forwarding from Ex/Mem registers to Ex stage (MEx)
Forwarding from Mem/WB register to Ex stage (W  Ex)
RegisterFile Bypass
IF/ID
ID/Ex
Ex/Mem
Mem/WB
forward unit
Notes: See where the hazard detection is. Forward unit is in the execute stage, because that is where you actually need the data.

## Slide 22: Forwarding Datapath
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
forward unit
detect hazard
Three types of forwarding/bypass
Forwarding from Ex/Mem registers to Ex stage (MEx)
Forwarding from Mem/WB register to Ex stage (W  Ex)
RegisterFile Bypass
IF/ID
ID/Ex
Ex/Mem
Mem/WB
Notes: Why is the forward unit here. Because it does not need to be earlier.

## Slide 23: Forwarding Datapath 1
Ex/MEM to EX Bypass
  EX needs ALU result that is still in MEM stage
  Resolve:
  Add a bypass from EX/MEM.D to start of EX
How to detect? Logic in Ex Stage:
forward = (Ex/M.WE && EX/M.Rd != 0 &&
ID/Ex.Ra == Ex/M.Rd)
|| (same for Rb)
“earlier” = started earlier
= stage right
stage left
  destination reg of earlier instruction == source reg of current
Notes: assumes (WE=0 implies rD=0) everywhere, similar for rA needed, rB needed (can ensure this in ID stage)

## Slide 24: Forwarding Datapath 2
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r1 |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
IF
ID
Ex
M
W
IF
ID
IF
W
Ex
M
W
ID
Ex
M

## Slide 25: Forwarding Datapath 2
Mem/WB to EX Bypass
  EX needs value being written by WB
  Resolve:
  Add bypass from WB final value to start of EX
How to detect? Logic in Ex Stage:
forward = (M/WB.WE && M/WB.Rd != 0 &&
ID/Ex.Ra == M/WB.Rd &&
|| (same for Rb)
Is this it?
Not quite!
“earlier” = started earlier
= stage right
stage left
  destination reg of earlier instruction == source reg of current
Notes: assumes (WE=0 implies rD=0) everywhere, similar for rA needed, rB needed (can ensure this in ID stage)

## Slide 26: Forwarding Datapath 2
How to detect? Logic in Ex Stage. Forward from M/WB reg if:
M/WB (WE on, Rd != 0) and (M/WB.Rd == ID/Ex.Ra)
also NOT(Ex/M.Rd == ID/Ex.Ra) and (WE, Rd!= 0))
Rb same as Ra
“earlier” = started earlier
= stage right
stage left
  destination reg of earlier instruction == source reg of current
add r3, r1, r2
sub r3, r3, r5
or r6, r3, r4
add r6, r3, r8
add r3, r1, r2
sub r5, r3, r5
or r6, r3, r4
add r6, r3, r8
Check pg. 311
Notes: assumes (WE=0 implies rD=0) everywhere, similar for rA needed, rB needed (can ensure this in ID stage)

## Slide 27: Register File Bypass
Register File Bypass
  Reading a value that is currently being written
Detect:
((Ra == MEM/WB.Rd) or (Rb == MEM/WB.Rd)) and (WB is writing a register)
Resolve:
Add a bypass around register file (WB to ID)
Better: just negate register file clock
    writes happen at end of first half of each clock cycle
    reads happen during second half of each clock cycle

## Slide 28: Register File Bypass
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r1 |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
add r6, r3, r8 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
IF
ID
Ex
M
W
IF
ID
IF
W
Ex
M
W
ID
Ex
M
IF
ID
Ex
M
W

## Slide 29: Are we done yet?
add r3, r1, r2
lw r4, 20(r8)
or r6, r3, r4
add r6, r3, r8
Memory “Load-Use Data Hazard”

## Slide 30: Memory Load Data Hazard
What happens if data dependency after a load word instruction?
Memory Load Data Hazard
  Value not available until after the M stage
  So: next instruction can’t proceed if hazard detected
Notes: often see lw …; nop; …
we will stall for our project 2

## Slide 31: Memory Load Data Hazard
Ex
lw r4, 20(r8) |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
IF
ID
Ex
M
W
IF
ID
Ex
M
W
ID
Stall
load-use stall
Notes: requires one bubble

## Slide 32: Memory Load Data Hazard
Ex
lw r4, 20(r8) |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
IF
ID
Ex
M
W
IF
ID
Ex
M
W
ID
Stall
load-use stall
lw r4, 20(r8)
or r6,r4,r1
Notes: Need to go back in time

## Slide 33: Memory Load Data Hazard
data mem
inst mem
D
B
A
NOP
or r6,r4,r1
lw r4, 20(r8)
Ex
lw r4, 20(r8) |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
IF
ID
Ex
M
W
IF
ID
Ex
M
W
ID
Stall
load-use stall
Notes: requires one bubble

## Slide 34: Memory Load Data Hazard
data mem
inst mem
D
B
A
NOP
or r6,r4,r1
lw r4, 20(r8)
Ex
lw r4, 20(r8) |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
IF
ID
Ex
M
W
IF
ID
Ex
M
W
ID
Stall
load-use stall
Notes: requires one bubble

## Slide 35: Memory Load Data Hazard
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
forward unit
detect hazard
IF/ID
ID/Ex
Ex/Mem
Mem/WB
Stall =
If(ID/Ex.MemRead &&
IF/ID.Ra == ID/Ex.Rd
Rd
MC
Notes: It happens in an earlier stage. You stall since you don’t want to go ahead from the ID stage unless you are ready.
Walk through what happens with a

## Slide 36: Memory Load Data Hazard
Load Data Hazard
  Value not available until WB stage
  So: next instruction can’t proceed if hazard detected
Resolution:
  MIPS 2000/3000: one delay slot
    ISA says results of loads are not available until one cycle later
    Assembler inserts nop, or reorders to fill delay slot
  MIPS 4000 onwards: stall
    But really, programmer/compiler reorders to avoid stalling in the load delay slot
For stall, how to detect? Logic in ID Stage
    Stall = ID/Ex.MemRead &&
    (IF/ID.Ra == ID/Ex.Rd || IF/ID.Rb == ID/Ex.Rd)
Notes: often see lw …; nop; …
we will stall for our project 2

## Slide 37: Quiz
Find all hazards, and say how they are resolved:
add r3, r1, r2
nand r5, r3, r4
add r2, r6, r3
lw r6, 24(r3)
sw r6, 12(r2)
Notes: Find all hazards, and say how they are resolved

## Slide 38: Quiz
Find all hazards, and say how they are resolved:
add r3, r1, r2
nand r5, r3, r4
add r2, r6, r3
lw r6, 24(r3)
sw r6, 12(r2)
5 Hazards
Notes: Find all hazards, and say how they are resolved

## Slide 39: Quiz
Find all hazards, and say how they are resolved:
add r3, r1, r2
nand r5, r3, r4
add r2, r6, r3
lw r6, 24(r3)
sw r6, 12(r2)
Forwarding from Ex/MID/Ex (MEx)
Forwarding from M/WID/Ex (WEx)
RegisterFile (RF) Bypass
Forwarding from M/WID/Ex (WEx)
Stall
+ Forwarding from M/WID/Ex (WEx)
5 Hazards
Notes: Find all hazards, and say how they are resolved

## Slide 40: Quiz
Find all hazards, and say how they are resolved: add r3, r1, r2 sub r3, r2, r1 nand r4, r3, r1 or r0, r3, r4 xor r1, r4, r3 sb r4, 1(r0)
Notes: 6 hazards
be careful of store (no rD)
be careful or r0 (never a hazard)

## Slide 41: Quiz 2
Find all hazards, and say how they are resolved: add r3, r1, r2 sub r3, r2, r1 nand r4, r3, r1 or r0, r3, r4 xor r1, r4, r3 sb r4, 1(r0)
Hours and hours of debugging!
Notes: 6 hazards
be careful of store (no rD)
be careful or r0 (never a hazard)

## Slide 42: Data Hazard Recap
Delay Slot(s)
  Modify ISA to match implementation
Stall
  Pause current and all subsequent instructions
Forward/Bypass
  Try to steal correct value from elsewhere in pipeline
  Otherwise, fall back to stalling or require a delay slot
Notes: 1: ISA tied to impl; messy asm; impl easy & cheap; perf depends on asm.
2: ISA correctness not tied to impl; clean+slow asm, or messy+fast asm; impl easy and cheap; same perf as 1. 3: ISA perf not tied to impl; clean+fast asm; impl is tricky; best perf

## Slide 43: Why are we learning about this?
Logic and gates
Numbers & arithmetic
States & FSMs
Memory
A simple CPU
Performance
Pipelining
Hazards: Data and Control

## Slide 44: Why are we learning about this?
Logic and gates
Numbers & arithmetic
States & FSMs
Memory
A simple CPU
Performance
Pipelining
Hazards: Data and Control
Computer Organization is fundamental to CS

## Slide 45: Control Hazards
What about branches?
A control hazard occurs if there is a control instruction (e.g. BEQ) and the program counter (PC) following the control instruction is not known until the control instruction computes if the branch should be taken
e.g.
0x10: beq r1, r2, L
0x14: add r3, r0, r3
0x18: sub r5, r4, r6
0x1C: L: or r3, r2, r4
Notes: Q: what happens with branch/jump in branch delay slot?
A: bad stuff, so forbidden
Q: why one, not two?
A: can move branch calc from EX to ID; will require new bypasses into ID stage; or can just zap the second instruction
Q: performance?
A: stall is bad

## Slide 46: Control Hazards
Control Hazards
  instructions are fetched in stage 1 (IF)
  branch and jump decisions occur in stage 3 (EX)
  i.e. next PC is not known until 2 cycles after branch/jump
What happens to instr following a branch, if branch not taken?
Stall
Forward/Bypass
Zap/Flush
All the above
None of the above
e.g.
0x10: beq r1, r2, L
0x14: add r3, r0, r3
0x18: sub r5, r4, r6
0x1C: L: or r3, r2, r4
Notes: Q: what happens with branch/jump in branch delay slot?
A: bad stuff, so forbidden
Q: why one, not two?
A: can move branch calc from EX to ID; will require new bypasses into ID stage; or can just zap the second instruction
Q: performance?
A: stall is bad

## Slide 47: Control Hazards
Control Hazards
  instructions are fetched in stage 1 (IF)
  branch and jump decisions occur in stage 3 (EX)
  i.e. next PC is not known until 2 cycles after branch/jump
What happens to instr following a branch, if branch taken?
Stall
Forward/Bypass
Zap/Flush
All the above
None of the above
e.g.
0x10: beq r1, r2, L
0x14: add r3, r0, r3
0x18: sub r5, r4, r6
0x1C: L: or r3, r2, r4
Notes: Q: what happens with branch/jump in branch delay slot?
A: bad stuff, so forbidden
Q: why one, not two?
A: can move branch calc from EX to ID; will require new bypasses into ID stage; or can just zap the second instruction
Q: performance?
A: stall is bad

## Slide 48: Control Hazards
Control Hazards
  instructions are fetched in stage 1 (IF)
  branch and jump decisions occur in stage 3 (EX)
  i.e. next PC is not known until 2 cycles after branch/jump
What happens to instr following a branch, if branch taken?
Stall (+ Zap/Flush)
  prevent PC update
  clear IF/ID pipeline register
    instruction just fetched might be wrong one, so convert to nop
  allow branch to continue into EX stage
Notes: Q: what happens with branch/jump in branch delay slot?
A: bad stuff, so forbidden
Q: why one, not two?
A: can move branch calc from EX to ID; will require new bypasses into ID stage; or can just zap the second instruction
Q: performance?
A: stall is bad

## Slide 49: Control Hazards
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 50: Control Hazards
beq r1, r2, L |  |  |  |  |  |  |  |  | 
add r3, r0, r3 |  |  |  |  |  |  |  |  | 
sub r5, r4, r6 |  |  |  |  |  |  |  |  | 
L: or r3, r2, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
PC
+4
NOP
IF
ID
Ex
M
W
IF
ID
NOP
NOP
NOP
IF
NOP
NOP
NOP
branch calc
decide branch
IF
ID
Ex
M
W
10:
14:
18:
1C:
If branch Taken
New PC = 1C
Zap
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 51: Control Hazards
beq r1, r2, L |  |  |  |  |  |  |  |  | 
add r3, r0, r3 |  |  |  |  |  |  |  |  | 
sub r5, r4, r6 |  |  |  |  |  |  |  |  | 
L: or r3, r2, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
PC
+4
NOP
IF
ID
Ex
M
W
IF
ID
NOP
NOP
NOP
IF
NOP
NOP
NOP
branch calc
decide branch
IF
ID
Ex
M
W
10:
14:
18:
1C:
If branch Taken
New PC = 1C
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 52: Control Hazards
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
14: add r3,r0,r3
10: beq r1, r2, L
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 53: Control Hazards
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
14: add r3,r0,r3
10: beq r1, r2, L
18: sub r5,r4,r6
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 54: Control Hazards
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
NOP
10: beq r1, r2, L
1C: or r3,r2,r4
NOP
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 55: Control Hazards
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
NOP
10: beq r1, r2, L
1C: or r3,r2,r4
NOP
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 56: Takeaway
Control hazards occur because the PC following a control instruction is not known until control instruction computes if branch should be taken or not.
If branch taken, then need to zap/flush instructions.
There is a performance penalty for branches:
Need to stall, then may need to zap (flush) subsequent instructions that have already been fetched.

## Slide 57: Next Goal
Can we reduce the cost of a control hazard?

## Slide 58: Reduce the cost of control hazard?
Can we forward/bypass values for branches?
  We can move branch calc from EX to ID
  will require new bypasses into ID stage; or can just zap the second instruction
What happens to instructions following a branch, if branch taken?
  Still need to zap/flush instructions
Is there still a performance penalty for branches
  Yes, need to stall, then may need to zap (flush) subsequent instructions that have already been fetched
Notes: Q: what happens with branch/jump in branch delay slot?
A: bad stuff, so forbidden
Q: why one, not two?
A: can move branch calc from EX to ID; will require new bypasses into ID stage; or can just zap the second instruction
Q: performance?
A: stall is bad

## Slide 59: Control Hazards
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 60: Control Hazards
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 61: Control Hazards
beq r1, r2, L |  |  |  |  |  |  |  |  | 
add r3, r0, r3 |  |  |  |  |  |  |  |  | 
sub r5, r4, r6 |  |  |  |  |  |  |  |  | 
L: or r3, r2, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
PC
+4
NOP
IF
ID
Ex
M
W
IF
NOP
NOP
NOP
IF
ID
Ex
M
W
10:
14:
18:
1C:
If branch Taken
New PC = 1C
Zap
branch calc
decide branch
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 62: Control Hazards
beq r1, r2, L |  |  |  |  |  |  |  |  | 
add r3, r0, r3 |  |  |  |  |  |  |  |  | 
sub r5, r4, r6 |  |  |  |  |  |  |  |  | 
L: or r3, r2, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
PC
+4
NOP
IF
ID
Ex
M
W
IF
NOP
NOP
NOP
IF
ID
Ex
M
W
10:
14:
18:
1C:
If branch Taken
New PC = 1C
Zap
branch calc
decide branch
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 63: Control Hazards
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
10: beq r1,r2,L
10
14
14
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 64: Control Hazards
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
14: add r3,r0,r3
10: beq r1, r2, L
14
1C
18
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 65: Control Hazards
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
1C: or r3,r2,r4
NOP
10: beq r1, r2, L
1C
20
20
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 66: Control Hazards
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
1C: or r3,r2,r4
NOP
10: beq r1, r2, L
20
24
24
20:
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 67: Control Hazards
Control Hazards
  instructions are fetched in stage 1 (IF)
  branch and jump decisions occur in stage 3 (EX)
  i.e. next PC is not known until 2 cycles after branch/jump
  Can optimize and move branch and jump decision to stage 2 (ID)
  i.e. next PC is not known until 1 cycles after branch/jump
Stall (+ Zap)
  prevent PC update
  clear IF/ID pipeline register
    instruction just fetched might be wrong one, so convert to nop
  allow branch to continue into EX stage
Notes: Q: what happens with branch/jump in branch delay slot?
A: bad stuff, so forbidden
Q: why one, not two?
A: can move branch calc from EX to ID; will require new bypasses into ID stage; or can just zap the second instruction
Q: performance?
A: stall is bad

## Slide 68: Takeaway
Control hazards occur because the PC following a control instruction is not known until control instruction computes if branch should be taken or not
If branch taken, then need to zap/flush instructions. There still a performance penalty for branches: Need to stall, then may need to zap (flush) subsequent instructions that have already been fetched
We can reduce cost of a control hazard by moving branch decision and calculation from Ex stage to ID stage. This reduces the cost from flushing two instructions to only flushing one.

## Slide 69: Reduce cost of Control Hazards More
Delay Slot
  ISA says N instructions after branch/jump always executed
    MIPS has 1 branch delay slot
    i.e. Whether branch taken or not, instruction following branch is always executed

## Slide 70: Delay Slot
beq r1, r2, L |  |  |  |  |  |  |  |  | 
add r3, r0, r3 |  |  |  |  |  |  |  |  | 
sub r5, r4, r6 |  |  |  |  |  |  |  |  | 
L: or r3, r2, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
PC
+4
IF
ID
Ex
M
W
IF
IF
ID
Ex
M
W
10:
14:
18:
1C:
Delay slot
If branch taken next instr still exec'd
branch calc
decide branch
ID
Ex
M
W
Notes: Pipeline is humming

## Slide 71: Delay Slot
beq r1, r2, L |  |  |  |  |  |  |  |  | 
add r3, r0, r3 |  |  |  |  |  |  |  |  | 
sub r5, r4, r6 |  |  |  |  |  |  |  |  | 
L: or r3, r2, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
PC
+4
IF
ID
Ex
M
W
IF
IF
ID
Ex
M
W
10:
14:
18:
1C:
branch calc
decide branch
ID
Ex
M
W
IF
ID
Ex
M
W
Delay slot
If branch not taken next instr still exec’d
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 72: Control Hazards
Control Hazards
  instructions are fetched in stage 1 (IF)
  branch and jump decisions occur in stage 3 (EX)
  i.e. next PC is not known until 2 cycles after branch/jump
  Can optimize and move branch and jump decision to stage 2 (ID)
  i.e. next PC is not known until 1 cycles after branch/jump
Stall (+ Zap)
  prevent PC update
  clear IF/ID pipeline register
    instruction just fetched might be wrong one, so convert to nop
  allow branch to continue into EX stage
Delay Slot
  ISA says N instructions after branch/jump always executed
    MIPS has 1 branch delay slot
Notes: Q: what happens with branch/jump in branch delay slot?
A: bad stuff, so forbidden
Q: why one, not two?
A: can move branch calc from EX to ID; will require new bypasses into ID stage; or can just zap the second instruction
Q: performance?
A: stall is bad
GPUs have such long pipelines it is just not realistic to add delay slots. So the penalty of branching is very high typically. Various architectural approaches to address that.

## Slide 73: Takeaway
Control hazards occur because the PC following a control instruction is not known until control instruction computes if branch should be taken or not. If branch taken, then need to zap/flush instructions. There still a performance penalty for branches: Need to stall, then may need to zap (flush) subsequent instructions that have already been fetched.
We can reduce cost of a control hazard by moving branch decision and calculation from Ex stage to ID stage. This reduces the cost from flushing two instructions to only flushing one.
Delay Slots can potentially increase performance due to control hazards by putting a useful instruction in the delay slot since the instruction in the delay slot will always be executed. Requires software (compiler) to make use of delay slot. Put nop in delay slot if not able to put useful instruction in delay slot.

## Slide 74: Reduce cost of Ctrl Haz even further?
Speculative Execution
  “Guess” direction of the branch
    Allow instructions to move through pipeline
    Zap them later if wrong guess
  Useful for long pipelines
Notes: Q: How to guess?
A: constant; hint; branch prediction; random; …

## Slide 75: Speculative Execution: Loops
Pipeline so far
  “Guess” (predict) that the branch will not be taken
We can do better!
  Make prediction based on last branch
  Predict “take branch” if last branch “taken”
  Or Predict “do not take branch” if last branch “not taken”
  Need one bit to keep track of last branch

## Slide 76: Speculative Execution: Loops
While (r3 ≠ 0) {…. r3--;}
Top: BEQZ r3, End
J Top
End:
While (r3 ≠ 0) {…. r3--;}
Top2: BEQZ r3, End2
J Top
End2:
What is accuracy of branch predictor?
Wrong twice per loop!
Once on loop enter and exit
We can do better with 2 bits

## Slide 77: Speculative Execution: Branch Execution
Predict Taken 2 (PT2)
Branch Taken (T)
Predict Taken 1 (PT1)
Predict Not Taken 1 (PT1)
Predict Not Taken 2 (PT2)
Branch Not Taken (NT)
Branch Taken (T)
Branch Not Taken (NT)
Branch Taken (T)
Branch Not Taken (NT)
Notes: Sates is a 2 bit prediction scheme

## Slide 78: Summary
Control hazards
  Is branch taken or not?
  Performance penalty: stall and flush
Reduce cost of control hazards
  Move branch decision from Ex to ID
    2 nops to 1 nop
  Delay slot
    Compiler puts useful work in delay slot. ISA level.
  Branch prediction
    Correct. Great!
    Wrong. Flush pipeline. Performance penalty

## Slide 79: Hazards Summary
Data hazards
Control hazards
Structural hazards
  resource contention
  so far: impossible because of ISA and pipeline design
Notes: Q: what if we had a “copy 0(r3), 4(r3)” instruction, as the x86 does, or “add r4, r4, 0(r3)”?
A: structural hazard

## Slide 80: Hazards Summary
Data hazards
  register file reads occur in stage 2 (IF)
  register file writes occur in stage 5 (WB)
  next instructions may read values soon to be written
Control hazards
  branch instruction may change the PC in stage 3 (EX)
  next instructions have already started executing
Structural hazards
  resource contention
  so far: impossible because of ISA and pipeline design
Notes: Q: what if we had a “copy 0(r3), 4(r3)” instruction, as the x86 does, or “add r4, r4, 0(r3)”?
A: structural hazard