## Slide 1: Calling Conventions
Prof. Hakim Weatherspoon
CS 3410, Spring 2015
Computer Science
Cornell University
See P&H 2.8 and A.5-A.6

## Slide 2: Big Picture: Where are we now?
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard

## Slide 3: Big Picture: Where are we going?
int x = 10;
x = 2 * x + 15;
C
compiler
addi r5, r0, 10
muli r5, r5, 2
addi r5, r5, 15
MIPS
assembly
00100000000001010000000000001010
00000000000001010010100001000000
00100000101001010000000000001111
machine code
assembler
CPU
Circuits
Gates
Transistors
Silicon
op = addi r0 r5 10
op = addi r5 r5 15
op = r-type r5 r5 shamt=1 func=sll
r0 = 0
r5 = r0 + 10
r5 = r5<<1 #r5 = r5 * 2
r5 = r15 + 15
Notes: 32 bits, 4 bytes

## Slide 4: Goals for Today
Calling Convention for Procedure Calls
Enable code to be reused by allowing code snippets to be invoked
Will need a way to
  call the routine (i.e. transfer control to procedure)
  pass arguments
    fixed length, variable length, recursively
  return to the caller
    Putting results in a place where caller can find them
  Manage register

## Slide 5: Cheat Sheet and Mental Model for Today
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard
How do we share registers and use memory when making procedure calls?

## Slide 6: Cheat Sheet and Mental Model for Today
  first four arg words passed in $a0, $a1, $a2, $a3
  remaining arg words passed in parent’s stack frame
  return value (if any) in $v0, $v1
  stack frame at $sp
    contains $ra (clobbered on JAL
    to sub-functions)
    contains local vars (possibly
    clobbered by sub-functions)
    contains extra arguments to sub-functions
    contains space for first 4 arguments
    to sub-functions
  callee save regs are preserved
  caller save regs are not
  Global data accessed via $gp
saved ra
saved fp
saved regs ($s0 ... $s7)
locals
outgoing args
$fp 
$sp 
Notes: Q: Minimum frame size?
A: 24 bytes (ra+fp+4args)
Q: What if this function makes no sub-calls?

## Slide 7: MIPS Register
Return address: $31 (ra)
Stack pointer: $29 (sp)
Frame pointer: $30 (fp)
First four arguments: $4-$7 (a0-a3)
Return result: $2-$3 (v0-v1)
Callee-save free regs: $16-$23 (s0-s7)
Caller-save free regs: $8-$15,$24,$25 (t0-t9)
Reserved: $26, $27
Global pointer: $28 (gp)
Assembler temporary: $1 (at)

## Slide 8: MIPS Register Conventions
r0 | $zero | zero
r1 | $at | assembler temp
r2 | $v0 | function return values
r3 | $v1 | 
r4 | $a0 | function arguments
r5 | $a1 | 
r6 | $a2 | 
r7 | $a3 | 
r8 | $t0 | temps (caller save)
r9 | $t1 | 
r10 | $t2 | 
r11 | $t3 | 
r12 | $t4 | 
r13 | $t5 | 
r14 | $t6 | 
r15 | $t7 | 
r16 | $s0 | saved (callee save)
r17 | $s1 | 
r18 | $s2 | 
r19 | $s3 | 
r20 | $s4 | 
r21 | $s5 | 
r22 | $s6 | 
r23 | $s7 | 
r24 | $t8 | more temps (caller save)
r25 | $t9 | 
r26 | $k0 | reserved for kernel
r27 | $k1 | 
r28 | $gp | global data pointer
r29 | $sp | stack pointer
r30 | $fp | frame pointer
r31 | $ra | return address

## Slide 9: Goals for Today
Calling Convention for Procedure Calls
Enable code to be reused by allowing code snippets to be invoked
Will need a way to
  call the routine (i.e. transfer control to procedure)
  pass arguments
    fixed length, variable length, recursively
  return to the caller
    Putting results in a place where caller can find them
  Manage register

## Slide 10: What is the convention to call a subroutine?
int main (int argc, char* argv[ ]) {
int n = 9;
int result = multi(n);
}
int multi(int n) {
int f = 1;
int i = 1;
int j = n – 1;
while(j >= 0) {
f *= i;
i++;
j = n - i;
}
return f;
}

## Slide 11: Procedure Call – Attempt #1: Use Jumps
main:
j mult
Laftercall1:
add $1,$2,$3
mult:
…
…
j Laftercall1
Jumps and branches can transfer control to the callee (called procedure)
Jumps and branches can transfer control back

## Slide 12: Procedure Call – Attempt #1: Use Jumps
main:
j mult
Laftercall1:
add $1,$2,$3
j mult
Laftercall2:
sub $3,$4,$5
mult:
…
…
j Laftercall1
j Laftercall2
Jumps and branches can transfer control to the callee (called procedure)
Jumps and branches can transfer control back
What happens when there are multiple calls from different call sites?
Not correct. How do
We know what location
to return to?

## Slide 13: Takeaway1: Need Jump And Link
JAL (Jump And Link) instruction moves a new value into the PC, and simultaneously saves the old value in register $31 (aka $ra or return address)
Thus, can get back from the subroutine to the instruction immediately following the jump by transferring control back to PC in register $31

## Slide 14: Procedure Call – Attempt #2: JAL/JR
main:
jal mult
Laftercall1:
add $1,$2,$3
jal mult
Laftercall2:
sub $3,$4,$5
mult:
…
…
jr $31
JAL saves the PC in register $31
Subroutine returns by jumping to $31
What happens for recursive invocations?

## Slide 15: Procedure Call – Attempt #2: JAL/JR
main:
jal mult
Laftercall1:
add $1,$2,$3
jal mult
Laftercall2:
sub $3,$4,$5
mult:
…
…
jr $31
JAL saves the PC in register $31
Subroutine returns by jumping to $31
What happens for recursive invocations?

## Slide 16: Procedure Call – Attempt #2: JAL/JR
int main (int argc, char* argv[ ]) {
int n = 9;
int result = multi(n);
}
int multi(int n) {
int f = 1;
int i = 1;
int j = n – 1;
while(j >= 0) {
f *= i;
i++;
j = n - i;
}
return f;
}

## Slide 17: Procedure Call – Attempt #2: JAL/JR
int main (int argc, char* argv[ ]) {
int n = 9;
int result = multi(n);
}
What happens for recursive invocations?
int multi(int n) {
if(n == 0) {
return 1;
} else {
return n * multi(n - 1);
}
}

## Slide 18: Procedure Call – Attempt #2: JAL/JR
main:
jal mult
Laftercall1:
add $1,$2,$3
jal mult
Laftercall2:
sub $3,$4,$5
mult:
…
beq $4, $0, Lout
...
jal mult
Linside:
…
Lout:
jr $31
What happens for recursive invocations?
Recursion overwrites contents of $31
Need to save and restore the register contents

## Slide 19: Need a “Call Stack”
Call stack
  contains activation records (aka stack frames)
Each activation record contains
  the return address for that invocation
  the local variables for that procedure
A stack pointer (sp) keeps track of the top of the stack
  dedicated register ($29) on the MIPS
Manipulated by push/pop operations
  push: move sp down, store
  pop: load, move sp up
Laftercall1
high mem
low mem
$31 =
sp

## Slide 20: Cheat Sheet and Mental Model for Today
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard

## Slide 21: Need a “Call Stack”
Call stack
  contains activation records (aka stack frames)
Each activation record contains
  the return address for that invocation
  the local variables for that procedure
A stack pointer (sp) keeps track of the top of the stack
  dedicated register ($29) on the MIPS
Manipulated by push/pop operations
  push: move sp down, store
  pop: load, move sp up
sp
Laftercall1
Linside
high mem
low mem
Push: ADDIU $sp, $sp, -4
SW $31, 0 ($sp)
$31 =
$31 =
sp

## Slide 22: Need a “Call Stack”
Call stack
  contains activation records (aka stack frames)
Each activation record contains
  the return address for that invocation
  the local variables for that procedure
A stack pointer (sp) keeps track of the top of the stack
  dedicated register ($29) on the MIPS
Manipulated by push/pop operations
  push: move sp down, store
  pop: load, move sp up
sp
Laftercall1
Linside
high mem
low mem
Push: ADDIU $sp, $sp, -4
SW $31, 0 ($sp)
Pop: LW $31, 0 ($sp)
ADDIU $sp, $sp, 4
JR $31
$31 =
$31 =
sp

## Slide 23: Stack Growth
(Call) Stacks start at a high address in memory
Stacks grow down as frames are pushed on
  Note: data region starts at a low address and grows up
  The growth potential of stacks and data region are not artificially limited

## Slide 24: Anatomy of an executing program
0xfffffffc
0x00000000
top
bottom
0x7ffffffc
0x80000000
0x10000000
0x00400000
system reserved
(stack grows down)
(heap grows up)
text
reserved
(static) data
(.stack)
.data
.text
system reserved
stack
system reserved
code (text)
static data
dynamic data (heap)
.data
.text

## Slide 25: Anatomy of an executing program
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard
Stack, Data, Code
Stored in Memory
$29 ($sp)
$31 ($ra)

## Slide 26: Takeaway2: Need a Call Stack
JAL (Jump And Link) instruction moves a new value into the PC, and simultaneously saves the old value in register $31 (aka $ra or return address) Thus, can get back from the subroutine to the instruction immediately following the jump by transferring control back to PC in register $31
Need a Call Stack to return to correct calling procedure. To maintain a stack, need to store an activation record (aka a “stack frame”) in memory. Stacks keep track of the correct return address by storing the contents of $31 in memory (the stack).

## Slide 27: Attempt #3: JAL/JR with Activation Records
main:
jal mult
Laftercall1:
add $1,$2,$3
jal mult
Laftercall2:
sub $3,$4,$5
mult:
addiu $sp,$sp,-4
sw $31, 0($sp)
beq $4, $0, Lout
...
jal mult
Linside:
…
Lout:
lw $31, 0($sp)
addiu $sp,$sp,4
jr $31
Stack used to save and restore contents of $31
sp
Laftercall1
Linside
high mem
low mem
Linside
Linside
sp
sp

## Slide 28: Attempt #3: JAL/JR with Activation Records
Stack used to save and restore contents of $31
How about arguments?
sp
Laftercall1
Linside
high mem
low mem
Linside
Linside
sp
sp
main:
jal mult
Laftercall1:
add $1,$2,$3
jal mult
Laftercall2:
sub $3,$4,$5
mult:
addiu $sp,$sp,-4
sw $31, 0($sp)
beq $4, $0, Lout
...
jal mult
Linside:
…
Lout:
lw $31, 0($sp)
addiu $sp,$sp,4
jr $31

## Slide 29: Next Goal
Need consistent way of passing arguments and getting the result of a subroutine invocation

## Slide 30: Attempt #4: Arguments & Return Values
Need consistent way of passing arguments and getting the result of a subroutine invocation
Given a procedure signature, need to know where arguments should be placed
  int min(int a, int b);
  int subf(int a, int b, int c, int d, int e);
  int isalpha(char c);
  int treesort(struct Tree *root);
  struct Node *createNode();
  struct Node mynode();
Too many combinations of char, short, int, void *, struct, etc.
  MIPS treats char, short, int and void * identically
$a0, $a1
stack
$a0
$v0, $v1
$v0

## Slide 31: Simple Argument Passing
First four arguments are passed in registers
  Specifically, $4, $5, $6 and $7, aka $a0, $a1, $a2, $a3
The returned result is passed back in a register
  Specifically, $2, aka $v0
main:
li $a0, 6
li $a1, 7
jal min
// result in $v0

## Slide 32: Conventions so far:
  args passed in $a0, $a1, $a2, $a3
  return value (if any) in $v0, $v1
  stack frame at $sp
    contains $ra (clobbered on JAL to sub-functions)
Q: What about argument lists?

## Slide 33: Many Arguments
What if there are more than 4 arguments?
main:
li $a0, 0
li $a1, 1
li $a2, 2
li $a3, 3
jal subf
// result in $v0

## Slide 34: Many Arguments
What if there are more than 4 arguments?
Use the stack for the additional arguments
  “spill”
main:
li $a0, 0
li $a1, 1
li $a2, 2
li $a3, 3
li $8, 4
addiu $sp,$sp,-4
sw $8, 0($sp)
jal subf
// result in $v0
sp
4

## Slide 35: Many Arguments
What if there are more than 4 arguments?
Use the stack for the additional arguments
  “spill”
main:
li $a0, 0
li $a1, 1
li $a2, 2
li $a3, 3
addiu $sp,$sp,-8
li $8, 4
sw $8, 0($sp)
li $8, 5
sw $8, 4($sp)
jal subf
// result in $v0
sp
5
4

## Slide 36: Variable Length Arguments
printf(“Coordinates are: %d %d %d\n”, 1, 2, 3);
Could just use the regular calling convention, placing first four arguments in registers, spilling the rest onto the stack
  Callee requires special-case code
  if(argno == 1) use a0, … else if (argno == 4) use a3, else use stack offset
Best to use an (initially confusing but ultimately simpler) approach:
  Pass the first four arguments in registers, as usual
  Pass the rest on the stack
  Reserve space on the stack for all arguments, including the first four
Simplifies functions that use variable-length arguments
  Store a0-a3 on the slots allocated on the stack, refer to all arguments through the stack

## Slide 37: Register Layout on Stack
First four arguments are in registers
The rest are on the stack
There is room on the stack for the first four arguments, just in case
main:
li $a0, 0
li $a1, 1
li $a2, 2
li $a3, 3
addiu $sp,s$p,-24
li $8, 4
sw $8, 16($sp)
li $8, 5
sw $8, 20($sp)
jal subf
// result in$ v0
sp
4
space for $a3
space for $a2
space for $a1
space for $a0
5
0($sp)
4($sp)
8($sp)
12($sp)
16($sp)
20($sp)

## Slide 38: Frame Layout on Stack
sp
4
space for $a3
space for $a2
space for $a1
space for $a0
5
blue() {
pink(0,1,2,3,4,5);
}
sp
return address

## Slide 39: Frame Layout on Stack
sp
4
space for $a3
space for $a2
space for $a1
space for $a0
5
return address
blue() {
pink(0,1,2,3,4,5);
}
pink(int a, int b, int c, int d, int e, int f) {
…
}
sp
return address

## Slide 40: Frame Layout on Stack
sp
4
space for $a3
space for $a2
space for $a1
space for $a0
5
return address
blue() {
pink(0,1,2,3,4,5);
}
pink(int a, int b, int c, int d, int e, int f) {
…
}
return address
blue
pink

## Slide 41: Conventions so far:
  first four arg words passed in $a0, $a1, $a2, $a3
  remaining arg words passed on the stack
  return value (if any) in $v0, $v1
  stack frame at $sp
    contains $ra (clobbered on JAL to sub-functions)
    contains extra arguments to sub-functions
    contains space for first 4 arguments to sub-functions
Notes: note: arguments are in caller’s frame, not callee

## Slide 42: MIPS Register Conventions so far:
r0 | $zero | zero
r1 | $at | assembler temp
r2 |  | 
r3 |  | 
r4 |  | 
r5 |  | 
r6 |  | 
r7 |  | 
r8 |  | 
r9 |  | 
r10 |  | 
r11 |  | 
r12 |  | 
r13 |  | 
r14 |  | 
r15 |  | 
r16 |  | 
r17 |  | 
r18 |  | 
r19 |  | 
r20 |  | 
r21 |  | 
r22 |  | 
r23 |  | 
r24 |  | 
r25 |  | 
r26 | $k0 | reserved for OS kernel
r27 | $k1 | 
r28 |  | 
r29 |  | 
r30 |  | 
r31 | $ra | return address
 | $v0 | function return values
 | $v1 | 
 | $a0 | function arguments
 | $a1 | 
 | $a2 | 
 | $a3 | 
Pseudo-Instructions
e.g. BLZ
SLT $at
BNE $at, 0, L
Notes: why $at? BLT psuedo-instruction and others

## Slide 43: Java vs C: Pointers and Structures
Pointers are 32-bits, treat just like ints
Pointers to structs are pointers
C allows passing whole structs
  int distance(struct Point p1, struct Point p2);
  Treat like a collection of consecutive 32-bit arguments, use registers for first 4 words, stack for rest
  Of course, Inefficient and to be avoided, better to use int distance(struct Point *p1, struct Point *p2); in all cases
$a0, $a1
$a2, $a3
$a0
$a1

## Slide 44: Globals and Locals
Global variables are allocated in the “data” region of the program
  Exist for all time, accessible to all routines
Local variables are allocated within the stack frame
  Exist solely for the duration of the stack frame
Dangling pointers are pointers into a destroyed stack frame
  C lets you create these, Java does not
  int *foo() { int a; return &a; }
Return the address of a,
But a is stored on stack, so will be removed
when call returns and point will be invalid

## Slide 45: Global and Locals
How does a function load global data?
  global variables are just above 0x10000000
Convention: global pointer
  $28 is $gp (pointer into middle of global data section) $gp = 0x10008000
  Access most global data using LW at $gp +/- offset LW $v0, 0x8000($gp) LW $v1, 0x7FFF($gp)
Notes: # data at 0x10000000
# data at 0x1000FFFF
(64KB range)

## Slide 46: Anatomy of an executing program
0xfffffffc
0x00000000
top
bottom
0x7ffffffc
0x80000000
0x10000000
0x00400000
system reserved
(stack grows down)
(heap grows up)
text
reserved
(static) data
(.stack)
.data
.text
system reserved
stack
system reserved
code (text)
static data
dynamic data (heap)
$gp

## Slide 47: Frame Pointer
It is often cumbersome to keep track of location of data on the stack
  The offsets change as new values are pushed onto and popped off of the stack
Keep a pointer to the bottom of the top stack frame
  Simplifies the task of referring to items on the stack
A frame pointer, $30, aka $fp
  Value of $sp upon procedure entry
  Can be used to restore $sp on exit

## Slide 48: Conventions so far
  first four arg words passed in $a0, $a1, $a2, $a3
  remaining arg words passed in parent’s stack frame
  return value (if any) in $v0, $v1
  stack frame at $sp
    contains $ra (clobbered on JAL
    to sub-functions)
    contains extra arguments to sub-functions
    contains space for first 4 arguments
    to sub-functions
Notes: Q: Minimum frame size?
A: 24 bytes (ra+fp+4args)
Q: What if this function makes no sub-calls?

## Slide 49: Next Goal
What convention should we use to share use of registers across procedure calls?

## Slide 50: Register Usage
Suppose a routine would like to store a value in a register
Two options: callee-save and caller-save
Callee-save:
  Assume that one of the callers is already using that register to hold a value of interest
  Save the previous contents of the register on procedure entry, restore just before procedure return
  E.g. $31
Caller-save:
  Assume that a caller can clobber any one of the registers
  Save the previous contents of the register before proc call
  Restore after the call
MIPS calling convention supports both

## Slide 51: Callee-Save
Assume caller is using the registers
Save on entry, restore on exit
Pays off if caller is actually using the registers, else the save and restore are wasted
main:
addiu $sp,$sp,-32
sw $31,28($sp)
sw $30, 24($sp)
sw $17, 20($sp)
sw $16, 16($sp)
addiu $30, $sp, 28
…
[use $16 and $17]
…
lw $31,28($sp)
lw $30,24($sp)
lw $17, 20$sp)
lw $16, 16($sp)
addiu $sp,$sp,32
jr $31

## Slide 52: Callee-Save
Assume caller is using the registers
Save on entry, restore on exit
Pays off if caller is actually using the registers, else the save and restore are wasted
main:
addiu $sp,$sp,-32
sw $ra,28($sp)
sw $fp, 24($sp)
sw $s1, 20($sp)
sw $s0, 16($sp)
addiu $fp, $sp, 28
…
[use $s0 and $s1]
…
lw $ra,28($sp)
lw $fp,24($sp)
lw $s1, 20$sp)
lw $s0, 16($sp)
addiu $sp,$sp,32
jr $ra

## Slide 53: Caller-Save
Assume the registers are free for the taking, clobber them
But since other subroutines will do the same, must protect values that will be used later
By saving and restoring them before and after subroutine invocations
Pays off if a routine makes few calls to other routines with values that need to be preserved
main:
…
[use $8 & $9]
…
addiu $sp,$sp,-8
sw $9, 4($sp)
sw $8, 0($sp)
jal mult
lw $9, 4($sp)
lw $8, 0($sp)
addiu $sp,$sp,8
…
[use $8 & $9]

## Slide 54: Caller-Save
Assume the registers are free for the taking, clobber them
But since other subroutines will do the same, must protect values that will be used later
By saving and restoring them before and after subroutine invocations
Pays off if a routine makes few calls to other routines with values that need to be preserved
main:
…
[use $t0 & $t1]
…
addiu $sp,$sp,-8
sw $t1, 4($sp)
sw $t0, 0($sp)
jal mult
lw $t1, 4($sp)
lw $t0, 0($sp)
addiu $sp,$sp,8
…
[use $t0 & $t1]

## Slide 55: Frame Layout on Stack
saved ra
saved fp
saved regs ($s0 ... $s7)
locals
outgoing args
fp
sp
ADDIU $sp, $sp, -32 # allocate frame
SW $ra, 28($sp) # save $ra
SW $fp, 24($sp) # save old $fp
SW $s1, 20($sp) # save ...
SW $s0, 16($sp) # save ...
ADDIU $fp, $sp, 28 # set new frame ptr
… ...
BODY
… ...
LW $s0, 16($sp) # restore …
LW $s1, 20($sp) # restore …
LW $fp, 24($sp) # restore old $fp
LW $ra, 28($sp) # restore $ra
ADDIU $sp,$sp, 32 # dealloc frame
JR $ra

## Slide 56: Frame Layout on Stack
sp
blue() {
pink(0,1,2,3,4,5);
}
saved fp
saved ra
fp
arguments
saved regs
blue

## Slide 57: Frame Layout on Stack
sp
arguments
saved ra
saved regs
local variables
arguments
saved regs
blue() {
pink(0,1,2,3,4,5);
}
pink(int a, int b, int c, int d, int e, int f) {
orange(10,11,12,13,14);
}
saved fp
saved ra
saved fp
fp
blue
pink

## Slide 58: Frame Layout on Stack
sp
arguments
saved ra
saved regs
local variables
arguments
saved regs
saved ra
blue() {
pink(0,1,2,3,4,5);
}
pink(int a, int b, int c, int d, int e, int f) {
orange(10,11,12,13,14);
}
orange(int a, int b, int c, int, d, int e) {
char buf[100];
gets(buf); // read string, no check!
}
local variables
saved fp
saved ra
saved fp
saved fp
fp
blue
pink
orange
buf[100]

## Slide 59: Buffer Overflow
sp
arguments
saved ra
saved regs
local variables
arguments
saved regs
saved ra
blue() {
pink(0,1,2,3,4,5);
}
pink(int a, int b, int c, int d, int e, int f) {
orange(10,11,12,13,14);
}
orange(int a, int b, int c, int, d, int e) {
char buf[100];
gets(buf); // read string, no check!
}
local variables
saved fp
saved ra
saved fp
saved fp
fp
What happens if more than 100 bytes
is written to buf?
buf[100]

## Slide 60: MIPS Register Recap
Return address: $31 (ra)
Stack pointer: $29 (sp)
Frame pointer: $30 (fp)
First four arguments: $4-$7 (a0-a3)
Return result: $2-$3 (v0-v1)
Callee-save free regs: $16-$23 (s0-s7)
Caller-save free regs: $8-$15,$24,$25 (t0-t9)
Reserved: $26, $27
Global pointer: $28 (gp)
Assembler temporary: $1 (at)

## Slide 61: MIPS Register Conventions
r0 | $zero | zero
r1 | $at | assembler temp
r2 | $v0 | function return values
r3 | $v1 | 
r4 | $a0 | function arguments
r5 | $a1 | 
r6 | $a2 | 
r7 | $a3 | 
r8 | $t0 | temps (caller save)
r9 | $t1 | 
r10 | $t2 | 
r11 | $t3 | 
r12 | $t4 | 
r13 | $t5 | 
r14 | $t6 | 
r15 | $t7 | 
r16 | $s0 | saved (callee save)
r17 | $s1 | 
r18 | $s2 | 
r19 | $s3 | 
r20 | $s4 | 
r21 | $s5 | 
r22 | $s6 | 
r23 | $s7 | 
r24 | $t8 | more temps (caller save)
r25 | $t9 | 
r26 | $k0 | reserved for kernel
r27 | $k1 | 
r28 | $gp | global data pointer
r29 | $sp | stack pointer
r30 | $fp | frame pointer
r31 | $ra | return address

## Slide 62: Recap: Conventions so far
  first four arg words passed in $a0, $a1, $a2, $a3
  remaining arg words passed in parent’s stack frame
  return value (if any) in $v0, $v1
  stack frame at $sp
    contains $ra (clobbered on JAL
    to sub-functions)
    contains local vars (possibly
    clobbered by sub-functions)
    contains extra arguments to sub-functions
    contains space for first 4 arguments
    to sub-functions
  callee save regs are preserved
  caller save regs are not
  Global data accessed via $gp
saved ra
saved fp
saved regs ($s0 ... $s7)
locals
outgoing args
$fp 
$sp 
Notes: Q: Minimum frame size?
A: 24 bytes (ra+fp+4args)
Q: What if this function makes no sub-calls?