## Slide 1: Calling Conventions
Prof. Hakim Weatherspoon
CS 3410, Spring 2015
Computer Science
Cornell University
See P&H 2.8 and 2.12, and A.5-6

## Slide 2: Announcement
Upcoming agenda
  PA1 due yesterday
  PA2 available and discussed during lab section this week
  PA2 Work-in-Progress due Monday, March 16th
  PA2 due Thursday, March 26th
  HW2 available next week, due before Prelim2 in April
  Spring break: Saturday, March 28th to Sunday, April 5th

## Slide 3: Goals for Today
Review: Calling Conventions
  call a routine (i.e. transfer control to procedure)
  pass arguments
    fixed length, variable length, recursively
  return to the caller
    Putting results in a place where caller can find them
  Manage register
  Today
  More on Calling Conventions
  globals vs local accessible data
  callee vs caller saved registers
  Calling Convention examples and debugging

## Slide 4: Goals for Today
Review: Calling Conventions
  call a routine (i.e. transfer control to procedure)
  pass arguments
    fixed length, variable length, recursively
  return to the caller
    Putting results in a place where caller can find them
  Manage register
  Today
  More on Calling Conventions
  globals vs local accessible data
  callee vs caller saved registers
  Calling Convention examples and debugging
Warning: There is no one true MIPS calling convention.
lecture != book != gcc != spim != web

## Slide 5: MIPS Register Recap
Return address: $31 (ra)
Stack pointer: $29 (sp)
Frame pointer: $30 (fp)
First four arguments: $4-$7 (a0-a3)
Return result: $2-$3 (v0-v1)
Callee-save free regs: $16-$23 (s0-s7)
Caller-save free regs: $8-$15,$24,$25 (t0-t9)
Reserved: $26, $27 (k0-k1)
Global pointer: $28 (gp)
Assembler temporary: $1 (at)

## Slide 6: MIPS Register Conventions
r0 | $zero | zero
r1 | $at | assembler temp
r2 | $v0 | function return values
r3 | $v1 | 
r4 | $a0 | function arguments
r5 | $a1 | 
r6 | $a2 | 
r7 | $a3 | 
r8 | $t0 | temps (caller save)
r9 | $t1 | 
r10 | $t2 | 
r11 | $t3 | 
r12 | $t4 | 
r13 | $t5 | 
r14 | $t6 | 
r15 | $t7 | 
r16 | $s0 | saved (callee save)
r17 | $s1 | 
r18 | $s2 | 
r19 | $s3 | 
r20 | $s4 | 
r21 | $s5 | 
r22 | $s6 | 
r23 | $s7 | 
r24 | $t8 | more temps (caller save)
r25 | $t9 | 
r26 | $k0 | reserved for kernel
r27 | $k1 | 
r28 | $gp | global data pointer
r29 | $sp | stack pointer
r30 | $fp | frame pointer
r31 | $ra | return address

## Slide 7: Recap: Conventions so far
  first four arg words passed in $a0, $a1, $a2, $a3
  remaining arg words passed in parent’s stack frame
  return value (if any) in $v0, $v1
  stack frame at $sp
    contains $ra (clobbered on JAL to sub-functions)
    contains $fp
    contains local vars (possibly
    clobbered by sub-functions)
    contains extra arguments to sub-functions
    (i.e. argument “spilling”)
    contains space for first 4 arguments
    to sub-functions
  callee save regs are preserved
  caller save regs are not preserved
  Global data accessed via $gp
saved ra
saved fp
saved regs ($s0 ... $s7)
locals
outgoing args
$fp 
$sp 
Bottom of
current
stack frame
Top of
the stack
Notes: Q: Minimum frame size?
A: 24 bytes (ra+fp+4args)
Q: What if this function makes no sub-calls?

## Slide 8: Globals and Locals
Global variables in data segment
  Exist for all time, accessible to all routines
Dynamic variables in heap segment
  Exist between malloc() and free()
Local variables in stack frame
  Exist solely for the duration of the stack frame
Dangling pointers into freed heap mem are bad
Dangling pointers into old stack frames are bad
  C lets you create these, Java does not
  E.g. int *foo() { int a; return &a; }

## Slide 9: Anatomy of an executing program
0xfffffffc
0x00000000
top
bottom
0x7ffffffc
0x80000000
0x10000000
0x00400000
system reserved
(stack grows down)
(heap grows up)
text
reserved
(static) data
(.stack)
.data
.text
system reserved
stack
system reserved
code (text)
static data
dynamic data (heap)
.data
.text
PC
Notes: Refer to previous global vs local slide

## Slide 10: MIPS Register Recap
Return address: $31 (ra)
Stack pointer: $29 (sp)
Frame pointer: $30 (fp)
First four arguments: $4-$7 (a0-a3)
Return result: $2-$3 (v0-v1)
Callee-save free regs: $16-$23 (s0-s7)
Caller-save free regs: $8-$15,$24,$25 (t0-t9)
Reserved: $26, $27
Global pointer: $28 (gp)
Assembler temporary: $1 (at)

## Slide 11: Caller-saved vs. Callee-saved
Callee-save register:
  Assumes register not changed across procedure call
  Thus, callee must save the previous contents of the register on procedure entry, restore just before procedure return
  E.g. $ra, $fp, $s0-s7
Caller-save register:
  Assumes that a caller can clobber contents of register
  Thus, caller must save the previous contents of the register before proc call
  Caller, then, restores after the call to subroutine returns
  E.g. $a0-a3, $v0-$v1, $t0-$t9
MIPS calling convention supports both
Notes: Also, $gp is a callee save register

## Slide 12: Caller-saved vs. Callee-saved
Callee-save register:
  Assumes register not changed across procedure call
  Thus, callee must save the previous contents of the register on procedure entry, restore just before procedure return
  E.g. $ra, $fp, $s0-s7, $gp
  Also, $sp
Caller-save register:
  Assumes that a caller can clobber contents of register
  Thus, caller must save the previous contents of the register before proc call
  Caller, then, restores after the call to subroutine returns
  E.g. $a0-a3, $v0-$v1, $t0-$t9
MIPS calling convention supports both
Notes: Also, $gp is a callee save register

## Slide 13: Caller-saved vs. Callee-saved
Caller-save: If necessary… ($t0 .. $t9)
  save before calling anything; restore after it returns
Callee-save: Always… ($s0 .. $s7)
  save before modifying; restore before returning
Caller-save registers are responsibility of the caller
  Caller-save register values saved only if used after call/return
  The callee function can use caller-saved registers
Callee-save register are the responsibility of the callee
  Values must be saved by callee before they can be used
  Caller can assume that these registers will be restored
Save if want to
use after a call
Save before use

## Slide 14: Caller-saved vs. Callee-saved
Caller-save: If necessary… ($t0 .. $t9)
  save before calling anything; restore after it returns
Callee-save: Always… ($s0 .. $s7)
  save before modifying; restore before returning
MIPS ($t0-$t9), x86 (eax, ecx, and edx) are caller-save…
  … a function can freely modify these registers
  … but must assume that their contents have been destroyed if it in turns calls a function.
MIPS ($s0 - $s7), x86 (ebx, esi, edi, ebp, esp) are callee-save
  A function may call another function and know that the callee-save registers have not been modified
  However, if it modifies these registers itself, it must restore them to their original values before returning.

## Slide 15: Caller-saved vs. Callee-saved
Caller-save: If necessary… ($t0 .. $t9)
  save before calling anything; restore after it returns
Callee-save: Always… ($s0 .. $s7)
  save before modifying; restore before returning
A caller-save register must be saved and restored around any call to a subroutine.
In contrast, for a callee-save register, a caller does not need to do any extra work at a call site (b/c the callee saves and restores the register if it is used).

## Slide 16: Caller-saved vs. Callee-saved
Caller-save: If necessary… ($t0 .. $t9)
  save before calling anything; restore after it returns
Callee-save: Always… ($s0 .. $s7)
  save before modifying; restore before returning
CALLER SAVED: MIPS calls these temporary registers, $t0-t9
  the calling routine saves the registers that it does not want a called procedure to overwrite
  register values are NOT preserved across procedure calls
CALLEE SAVED: MIPS calls these saved registers, $s0-s8
  register values are preserved across procedure calls
  the called procedure saves register values in its Activation Record (AR), uses the registers for local variables, restores register values before it returns.

## Slide 17: Caller-saved vs. Callee-saved
Caller-save: If necessary… ($t0 .. $t9)
  save before calling anything; restore after it returns
Callee-save: Always… ($s0 .. $s7)
  save before modifying; restore before returning
Registers $t0-$t9 are caller-saved registers
  … that are used to hold temporary quantities
  … that need not be preserved across calls
Registers $s0-s8 are callee-saved registers
  … that hold long-lived values
  … that should be preserved across calls

## Slide 18: Callee-Save
Assume caller is using the registers
Callee must save on entry, restore on exit
Pays off if caller is actually using the registers, else the save and restore are wasted
main:
addiu $sp,$sp,-32
sw $31,28($sp)
sw $30, 24($sp)
sw $17, 20($sp)
sw $16, 16($sp)
addiu $30, $sp, 28
…
[use $16 and $17]
…
lw $31,28($sp)
lw $30,24($sp)
lw $17, 20$sp)
lw $16, 16($sp)
addiu $sp,$sp,32
jr $31

## Slide 19: Callee-Save
Assume caller is using the registers
Callee must save on entry, restore on exit
Pays off if caller is actually using the registers, else the save and restore are wasted
main:
addiu $sp,$sp,-32
sw $ra,28($sp)
sw $fp, 24($sp)
sw $s1, 20($sp)
sw $s0, 16($sp)
addiu $fp, $sp, 28
…
[use $s0 and $s1]
…
lw $ra,28($sp)
lw $fp,24($sp)
lw $s1, 20$sp)
lw $s0, 16($sp)
addiu $sp,$sp,32
jr $ra

## Slide 20: Caller-Save
Assume the registers are free for the taking, clobber them
But since other subroutines will do the same, must protect values that will be used later
By saving and restoring them before and after subroutine invocations
Pays off if a routine makes few calls to other routines with values that need to be preserved
main:
…
[use $8 & $9]
…
addiu $sp,$sp,-8
sw $9, 4($sp)
sw $8, 0($sp)
jal mult
lw $9, 4($sp)
lw $8, 0($sp)
addiu $sp,$sp,8
…
[use $8 & $9]

## Slide 21: Caller-Save
Assume the registers are free for the taking, clobber them
But since other subroutines will do the same, must protect values that will be used later
By saving and restoring them before and after subroutine invocations
Pays off if a routine makes few calls to other routines with values that need to be preserved
main:
…
[use $t0 & $t1]
…
addiu $sp,$sp,-8
sw $t1, 4($sp)
sw $t0, 0($sp)
jal mult
lw $t1, 4($sp)
lw $t0, 0($sp)
addiu $sp,$sp,8
…
[use $t0 & $t1]

## Slide 22: MIPS Register Recap
Return address: $31 (ra)
Stack pointer: $29 (sp)
Frame pointer: $30 (fp)
First four arguments: $4-$7 (a0-a3)
Return result: $2-$3 (v0-v1)
Callee-save free regs: $16-$23 (s0-s7)
Caller-save free regs: $8-$15,$24,$25 (t0-t9)
Reserved: $26, $27
Global pointer: $28 (gp)
Assembler temporary: $1 (at)

## Slide 23: Recap: Conventions so far
  first four arg words passed in $a0, $a1, $a2, $a3
  remaining arg words passed in parent’s stack frame
  return value (if any) in $v0, $v1
  stack frame at $sp
    contains $ra (clobbered on JAL to sub-functions)
    contains $fp
    contains local vars (possibly
    clobbered by sub-functions)
    contains extra arguments to sub-functions
    (i.e. argument “spilling)
    contains space for first 4 arguments
    to sub-functions
  callee save regs are preserved
  caller save regs are not
  Global data accessed via $gp
saved ra
saved fp
saved regs ($s0 ... $s7)
locals
outgoing args
$fp 
$sp 
Bottom of
current
stack frame
Top of
the stack
Notes: Q: Minimum frame size?
A: 24 bytes (ra+fp+4args)
Q: What if this function makes no sub-calls?

## Slide 24: Frame Layout on Stack
saved ra
saved fp
saved regs ($s0 ... $s7)
locals
outgoing args
fp
sp
Assume a function uses two callee-save registers.
How do we allocate a stack frame? How large is the stack frame?
What should be stored in the stack frame?
Where should everything be stored?

## Slide 25: Frame Layout on Stack
saved ra
saved fp
saved regs ($s0 ... $s7)
locals
outgoing args
fp
sp
ADDIU $sp, $sp, -32 # allocate frame
SW $ra, 28($sp) # save $ra
SW $fp, 24($sp) # save old $fp
SW $s1, 20($sp) # save ...
SW $s0, 16($sp) # save ...
ADDIU $fp, $sp, 28 # set new frame ptr
… ...
BODY
… ...
LW $s0, 16($sp) # restore …
LW $s1, 20($sp) # restore …
LW $fp, 24($sp) # restore old $fp
LW $ra, 28($sp) # restore $ra
ADDIU $sp,$sp, 32 # dealloc frame
JR $ra

## Slide 26: Frame Layout on Stack
sp
blue() {
pink(0,1,2,3,4,5);
}
saved fp
saved ra
fp
arguments
saved regs
blue

## Slide 27: Frame Layout on Stack
sp
arguments
saved ra
saved regs
local variables
arguments
saved regs
blue() {
pink(0,1,2,3,4,5);
}
pink(int a, int b, int c, int d, int e, int f) {
orange(10,11,12,13,14);
}
saved fp
saved ra
saved fp
fp
blue
pink

## Slide 28: Frame Layout on Stack
sp
arguments
saved ra
saved regs
local variables
arguments
saved regs
saved ra
blue() {
pink(0,1,2,3,4,5);
}
pink(int a, int b, int c, int d, int e, int f) {
orange(10,11,12,13,14);
}
orange(int a, int b, int c, int, d, int e) {
char buf[100];
gets(buf); // read string, no check!
}
local variables
saved fp
saved ra
saved fp
saved fp
fp
blue
pink
orange
buf[100]

## Slide 29: Buffer Overflow
sp
arguments
saved ra
saved regs
local variables
arguments
saved regs
saved ra
blue() {
pink(0,1,2,3,4,5);
}
pink(int a, int b, int c, int d, int e, int f) {
orange(10,11,12,13,14);
}
orange(int a, int b, int c, int, d, int e) {
char buf[100];
gets(buf); // read string, no check!
}
local variables
saved fp
saved ra
saved fp
saved fp
fp
What happens if more than 100 bytes
is written to buf?
buf[100]

## Slide 30: Activity #1: Calling Convention Example
int test(int a, int b) {
int tmp = (a&b)+(a|b);
int s = sum(tmp,1,2,3,4,5);
int u = sum(s,tmp,b,a,b,a);
return u + a + b;
}
s0 = a0
s1 = a1
t0 = a & b
t1 = a | b
t0 = t0 + t1
SW t0, 24(sp) # tmp
a0 = t0
a1 = 1
a2 = 2
a3 = 3
SW 4, 0(sp)
SW 5, 4(sp)
JAL sum
NOP
LW t0, 24(sp)
a0 = v0
a1 = t0
a2 = s1
a3 = s0
SW s1, 0(sp)
SW s0, 4(sp)
JAL sum
NOP
v0 = v0 + s0 + s1

## Slide 31: Activity #1: Calling Convention Example
int test(int a, int b) {
int tmp = (a&b)+(a|b);
int s = sum(tmp,1,2,3,4,5);
int u = sum(s,tmp,b,a,b,a);
return u + a + b;
}
s0 = a0
s1 = a1
t0 = a & b
t1 = a | b
t0 = t0 + t1
SW t0, 24(sp) # tmp
a0 = t0
a1 = 1
a2 = 2
a3 = 3
SW 4, 0(sp)
SW 5, 4(sp)
JAL sum
NOP
LW t0, 24(sp)
a0 = v0
a1 = t0
a2 = s1
a3 = s0
SW s1, 0(sp)
SW s0, 4(sp)
JAL sum
NOP
v0 = v0 + s0 + s1
test:
MOVE $s0, $a0
MOVE $s1, $a1
AND $t0, $a0, $a1
OR $t1, $a0, $a1
ADD $t0, $t0, $t1
MOVE $a0, $t0
LI $a1, 1
LI $a2, 2
LI $a3, 3
LI $t1, 4
SW $t1 16($sp)
LI $t1, 5
SW $t1, 20($sp)
SW $t0, 24($sp)
JAL sum
NOP
LW $t0, 24($sp)
MOVE $a0, $v0 # s
MOVE $a1, $t0 # tmp
MOVE $a2, $s1 # b
MOVE $a3, $s0 # a
SW $s1, 16($sp)
SW $s0, 20($sp)
JAL sum
NOP
# add u (v0) and a (s0)
ADD $v0, $v0, $s0
ADD $v0, $v0, $s1
# $v0 = u + a + b
Prologue
Epilogue

## Slide 32: Activity #1: Calling Convention Example
int test(int a, int b) {
int tmp = (a&b)+(a|b);
int s = sum(tmp,1,2,3,4,5);
int u = sum(s,tmp,b,a,b,a);
return u + a + b;
}
s0 = a0
s1 = a1
t0 = a & b
t1 = a | b
t0 = t0 + t1
SW t0, 24(sp) # tmp
a0 = t0
a1 = 1
a2 = 2
a3 = 3
SW 4, 0(sp)
SW 5, 4(sp)
JAL sum
NOP
LW t0, 24(sp)
a0 = v0
a1 = t0
a2 = s1
a3 = s0
SW s1, 0(sp)
SW s0, 4(sp)
JAL sum
NOP
v0 = v0 + s0 + s1
test:
MOVE $s0, $a0
MOVE $s1, $a1
AND $t0, $a0, $a1
OR $t1, $a0, $a1
ADD $t0, $t0, $t1
MOVE $a0, $t0
LI $a1, 1
LI $a2, 2
LI $a3, 3
LI $t1, 4
SW $t1 16($sp)
LI $t1, 5
SW $t1, 20($sp)
SW $t0, 24($sp)
JAL sum
NOP
LW $t0, 24($sp)
MOVE $a0, $v0 # s
MOVE $a1, $t0 # tmp
MOVE $a2, $s1 # b
MOVE $a3, $s0 # a
SW $s1, 16($sp)
SW $s0, 20($sp)
JAL sum
NOP
# add u (v0) and a (s0)
ADD $v0, $v0, $s0
ADD $v0, $v0, $s1
# $v0 = u + a + b
Prologue
Epilogue
How many bytes do we
need to allocate for the
stack frame?
24
32
40
44
48

## Slide 33: Activity #1: Calling Convention Example
int test(int a, int b) {
int tmp = (a&b)+(a|b);
int s = sum(tmp,1,2,3,4,5);
int u = sum(s,tmp,b,a,b,a);
return u + a + b;
}
s0 = a0
s1 = a1
t0 = a & b
t1 = a | b
t0 = t0 + t1
SW t0, 24(sp) # tmp
a0 = t0
a1 = 1
a2 = 2
a3 = 3
SW 4, 0(sp)
SW 5, 4(sp)
JAL sum
NOP
LW t0, 24(sp)
a0 = v0
a1 = t0
a2 = s1
a3 = s0
SW s1, 0(sp)
SW s0, 4(sp)
JAL sum
NOP
v0 = v0 + s0 + s1
test:
MOVE $s0, $a0
MOVE $s1, $a1
AND $t0, $a0, $a1
OR $t1, $a0, $a1
ADD $t0, $t0, $t1
MOVE $a0, $t0
LI $a1, 1
LI $a2, 2
LI $a3, 3
LI $t1, 4
SW $t1 16($sp)
LI $t1, 5
SW $t1, 20($sp)
SW $t0, 24($sp)
JAL sum
NOP
LW $t0, 24($sp)
MOVE $a0, $v0 # s
MOVE $a1, $t0 # tmp
MOVE $a2, $s1 # b
MOVE $a3, $s0 # a
SW $s1, 16($sp)
SW $s0, 20($sp)
JAL sum
NOP
# add u (v0) and a (s0)
ADD $v0, $v0, $s0
ADD $v0, $v0, $s1
# $v0 = u + a + b
saved ra
saved fp
saved regs ($s0 and $s1)
locals
($t0)
outgoing args
space for a0 - a3
and 5th and 6th arg
$fp 
$sp 
Prologue
Epilogue

## Slide 34: Activity #1: Calling Convention Example
int test(int a, int b) {
int tmp = (a&b)+(a|b);
int s = sum(tmp,1,2,3,4,5);
int u = sum(s,tmp,b,a,b,a);
return u + a + b;
}
s0 = a0
s1 = a1
t0 = a & b
t1 = a | b
t0 = t0 + t1
SW t0, 24(sp) # tmp
a0 = t0
a1 = 1
a2 = 2
a3 = 3
SW 4, 0(sp)
SW 5, 4(sp)
JAL sum
NOP
LW t0, 24(sp)
a0 = v0
a1 = t0
a2 = s1
a3 = s0
SW s1, 0(sp)
SW s0, 4(sp)
JAL sum
NOP
v0 = v0 + s0 + s1
test:
MOVE $s0, $a0
MOVE $s1, $a1
AND $t0, $a0, $a1
OR $t1, $a0, $a1
ADD $t0, $t0, $t1
MOVE $a0, $t0
LI $a1, 1
LI $a2, 2
LI $a3, 3
LI $t1, 4
SW $t1 16($sp)
LI $t1, 5
SW $t1, 20($sp)
SW $t0, 24($sp)
JAL sum
NOP
LW $t0, 24($sp)
MOVE $a0, $v0 # s
MOVE $a1, $t0 # tmp
MOVE $a2, $s1 # b
MOVE $a3, $s0 # a
SW $s1, 16($sp)
SW $s0, 20($sp)
JAL sum
NOP
# add u (v0) and a (s0)
ADD $v0, $v0, $s0
ADD $v0, $v0, $s1
# $v0 = u + a + b
saved ra
saved fp
$fp 
$sp 
Prologue
Epilogue
saved reg $s1
saved reg $s0
local $t0
outgoing 6th arg
outgoing 5th arg
space for $a3
space for $a2
space for $a1
space for $a0
4
8
12
16
0
20
24
28
32
36
40

## Slide 35: Activity #2: Calling Convention Example: Prologue, Epilogue
ADDIU $sp, $sp, -40
SW $ra, 36($sp)
SW $fp, 32($sp)
SW $s0, 28($sp)
SW $s5, 24($sp)
ADDIU $fp, $sp, 40
...
...
LW $s5, 24($sp)
LW $s0, 28($sp)
LW $fp, 32($sp)
LW $ra, 36($sp)
ADDIU $sp, $sp, 40
JR $ra
# allocate frame
# save $ra
# save old $fp
# callee save ...
# callee save ...
# set new frame ptr
...
...
# restore …
# restore …
# restore old $fp
# restore $ra
# dealloc frame
test:
saved ra
saved fp
$fp 
$sp 
saved reg $s1
saved reg $s0
local $t0
outgoing 6th arg
outgoing 5th arg
space for $a3
space for $a2
space for $a1
space for $a0
4
8
12
16
0
20
24
28
32
36
40

## Slide 36: Activity #2: Calling Convention Example: Prologue, Epilogue
# allocate frame
# save $ra
# save old $fp
# callee save ...
# callee save ...
# set new frame ptr
...
...
# restore …
# restore …
# restore old $fp
# restore $ra
# dealloc frame
ADDIU $sp, $sp, -40
SW $ra, 36($sp)
SW $fp, 32($sp)
SW $s0, 28($sp)
SW $s5, 24($sp)
ADDIU $fp, $sp, 40
...
...
LW $s5, 24($sp)
LW $s0, 28($sp)
LW $fp, 32($sp)
LW $ra, 36($sp)
ADDIU $sp, $sp, 40
JR $ra
test:
ADDIU $sp, $sp, -44
SW $ra, 40($sp)
SW $fp, 36($sp)
SW $s1, 32($sp)
SW $s0, 28($sp)
ADDIU $fp, $sp, 40
LW $s0, 28($sp)
LW $s1, 32($sp)
LW $fp, 36($sp)
LW $ra, 40($sp)
ADDIU $sp, $sp, 44
JR $ra
NOP
Body
(previous slide, Activity #1)
saved ra
saved fp
$fp 
$sp 
saved reg $s1
saved reg $s0
local $t0
outgoing 6th arg
outgoing 5th arg
space for $a3
space for $a2
space for $a1
space for $a0
4
8
12
16
0
20
24
28
32
36
40
Space for $t0
and six args
to pass to
subroutine

## Slide 37: Next Goal
Can we optimize the assembly code at all?

## Slide 38: Activity #3: Calling Convention Example
int test(int a, int b) {
int tmp = (a&b)+(a|b);
int s = sum(tmp,1,2,3,4,5);
int u = sum(s,tmp,b,a,b,a);
return u + a + b;
}
s0 = a0
s1 = a1
t0 = a & b
t1 = a | b
t0 = t0 + t1
SW t0, 24(sp) # tmp
a0 = t0
a1 = 1
a2 = 2
a3 = 3
SW 4, 0(sp)
SW 5, 4(sp)
JAL sum
NOP
LW t0, 24(sp)
a0 = v0
a1 = t0
a2 = s1
a3 = s0
SW s1, 0(sp)
SW s0, 4(sp)
JAL sum
NOP
v0 = v0 + s0 + s1
test:
MOVE $s0, $a0
MOVE $s1, $a1
AND $t0, $a0, $a1
OR $t1, $a0, $a1
ADD $t0, $t0, $t1
MOVE $a0, $t0
LI $a1, 1
LI $a2, 2
LI $a3, 3
LI $t1, 4
SW $t1 16($sp)
LI $t1, 5
SW $t1, 20($sp)
SW $t0, 24($sp)
JAL sum
NOP
LW $t0, 24($sp)
MOVE $a0, $v0 # s
MOVE $a1, $t0 # tmp
MOVE $a2, $s1 # b
MOVE $a3, $s0 # a
SW $s1, 16($sp)
SW $s0, 20($sp)
JAL sum
NOP
# add u (v0) and a (s0)
ADD $v0, $v0, $s0
ADD $v0, $v0, $s1
# $v0 = u + a + b
Prologue
Epilogue
How can we optimize
the assembly code?
Notes: Optimize by removing the NOPs. That is, putting a independent instruction in the delay slot

## Slide 39: Activity #3: Calling Convention Example: Prologue, Epilogue
# allocate frame
# save $ra
# save old $fp
# callee save ...
# callee save ...
# set new frame ptr
...
...
# restore …
# restore …
# restore old $fp
# restore $ra
# dealloc frame
ADDIU $sp, $sp, -40
SW $ra, 36($sp)
SW $fp, 32($sp)
SW $s0, 28($sp)
SW $s5, 24($sp)
ADDIU $fp, $sp, 40
...
...
LW $s5, 24($sp)
LW $s0, 28($sp)
LW $fp, 32($sp)
LW $ra, 36($sp)
ADDIU $sp, $sp, 40
JR $ra
test:
ADDIU $sp, $sp, -44
SW $ra, 40($sp)
SW $fp, 36($sp)
SW $s1, 32($sp)
SW $s0, 28($sp)
ADDIU $fp, $sp, 40
LW $s0, 28($sp)
LW $s1, 32($sp)
LW $fp, 36($sp)
LW $ra, 40($sp)
ADDIU $sp, $sp, 44
JR $ra
NOP
Body

## Slide 40: Minimum stack size for a standard function?
Notes: Q: Minimum frame size?
A: 24 bytes (ra+fp+4args)
Q: What if this function makes no sub-calls?

## Slide 41: Minimum stack size for a standard function?
24 bytes = 6x 4 bytes ($ra + $fp + 4 args)
saved ra
saved fp
saved regs ($s0 ... $s7)
locals
outgoing args
$fp 
$sp 
Notes: Q: Minimum frame size?
A: 24 bytes (ra+fp+4args)
Q: What if this function makes no sub-calls?

## Slide 42: Leaf Functions
Leaf function does not invoke any other functions
int f(int x, int y) { return (x+y); }
Optimizations?
No saved regs (or locals)
No outgoing args
Don’t push $ra
No frame at all?
Maybe.
saved ra
saved fp
saved regs ($s0 ... $s7)
locals
outgoing args
$fp 
$sp 

## Slide 43: Next Goal
Given a running program (a process), how do we know what is going on (what function is executing, what arguments were passed to where, where is the stack and current stack frame, where is the code and data, etc)?

## Slide 44: Anatomy of an executing program
0xfffffffc
0x00000000
top
bottom
0x7ffffffc
0x80000000
0x10000000
0x00400000
system reserved
(stack grows down)
(heap grows up)
text
reserved
(static) data
(.stack)
.data
.text
system reserved
stack
system reserved
code (text)
static data
dynamic data (heap)
.data
.text
PC

## Slide 45: Activity #4: Debugging
init(): 0x400000
printf(s, …): 0x4002B4
vnorm(a,b): 0x40107C
main(a,b): 0x4010A0
pi: 0x10000000
str1: 0x10000004
0x00000000
0x004010c4
0x00000000
0x00000000
0x7FFFFFF4
0x00000000
0x00000000
0x0040010c
0x00000015
0x10000004
0x00401090
0x00000000
0x00000000
CPU:
$pc=0x004003C0
$sp=0x7FFFFFAC
$ra=0x00401090
0x7FFFFFB0
What func is running?
Who called it?
Has it called anything?
Will it?
Args?
Stack depth?
Call trace?
0x7FFFFFDC
Notes: pc  in printf
ra  called from vnorm? or called vnorm?
0(sp)  looks like in printf, called by vnorm, and not going to call anything else
4,8(sp)  looks like args are str1 and 0x15
20(sp)  looks like a return address, probably main called vnorm with less than 4 args
44(sp)  looks like a return address, probably init called main
how large is init’s stack frame?

## Slide 46: Activity #4: Debugging
init(): 0x400000
printf(s, …): 0x4002B4
vnorm(a,b): 0x40107C
main(a,b): 0x4010A0
pi: 0x10000000
str1: 0x10000004
0x00000000
0x004010c4
0x00000000
0x00000000
0x7FFFFFF4
0x00000000
0x00000000
0x0040010c
0x00000015
0x10000004
0x00401090
0x00000000
0x00000000
CPU:
$pc=0x004003C0
$sp=0x7FFFFFAC
$ra=0x00401090
0x7FFFFFB0
What func is running?
Who called it?
Has it called anything?
Will it?
Args?
Stack depth?
Call trace?
0x7FFFFFDC
printf
vnorm
no
no
printf, vnorm, main, init
Str1 and 0x15
4
0x7FFFFFAC
0x7FFFFFB4
0x7FFFFFB8
0x7FFFFFBC
0x7FFFFFC0
0x7FFFFFC4
0x7FFFFFC8
0x7FFFFFCA
0x7FFFFFD0
0x7FFFFFD4
0x7 …D8
DC
E0
Memory
ra
fp
a3
a2
a1
a0
ra
fp
a3
a2
a1
a0
a0
ra
E4
E8
EA
…F0
…F4
a1
a2
a3
fp
ra
b/c no space for
outgoing args
0x7FFFFFA8
main
vnorm
0x7FFFFFC4
printf
Notes: pc  in printf
ra  called from vnorm? or called vnorm?
0(sp)  looks like in printf, called by vnorm, and not going to call anything else
4,8(sp)  looks like args are str1 and 0x15
20(sp)  looks like a return address, probably main called vnorm with less than 4 args
44(sp)  looks like a return address, probably init called main
how large is init’s stack frame?

## Slide 47: Recap
  How to write and Debug a MIPS program using calling convention
  first four arg words passed in $a0, $a1, $a2, $a3
  remaining arg words passed in parent’s stack frame
  return value (if any) in $v0, $v1
  stack frame at $sp
    contains $ra (clobbered on JAL to sub-functions)
    contains $fp
    contains local vars (possibly
    clobbered by sub-functions)
    contains extra arguments to sub-functions
    (i.e. argument “spilling)
    contains space for first 4 arguments
    to sub-functions
  callee save regs are preserved
  caller save regs are not
  Global data accessed via $gp
saved ra
saved fp
saved regs ($s0 ... $s7)
locals
outgoing args
$fp 
$sp 
Notes: Q: Minimum frame size?
A: 24 bytes (ra+fp+4args)
Q: What if this function makes no sub-calls?