## Slide 1
CS 3410, Spring 2015
Computer Science
Cornell University
See P&H Chapter: 5.1-5.3 (except writes)
  Caches and Memory

## Slide 2: Big Picture: Memory
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
ALU
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard
Stack, Data, Code
Stored in Memory
Code Stored in Memory
(also, data and stack)

## Slide 3: What is in Memory?
int n = 4;
int k[] = {3, 14, 0, 10};
int fib(int i) {
  if (i <= 2) return i;
  else return fib(i-1)+fib(i-2);
}
int main(int ac, char **av) {
for (int i = 0; i < n; i++) {
printi(fib(k[i]));
prints("\n");
}
}

## Slide 4: Problem
Main memory is very very very slow!
DRAM
  1 transistor, cheaper/bit, slower, needs refresh
SRAM
  6-8 transistors, costlier/bit, faster, no refresh
D-Flip Flop, Registers
  10-100s of transistors, very expensive, very fast
Notes: LW to access and read variables
SW to change the variable

## Slide 5: Problem
CPU clock rates ~0.33ns – 2ns (3GHz-500MHz)
Memory technology | Access time in nanosecs (ns) | Access time in cycles | $ per GIB in 2012 | Capacity
SRAM (on chip) | 0.5-2.5 ns | 1-3 cycles | $4k | 256 KB
SRAM (off chip) | 1.5-30 ns | 5-15 cycles | $4k | 32 MB
DRAM | 50-70 ns | 150-200 cycles | $10-$20 | 8 GB
SSD (Flash) | 5k-50k ns | Tens of thousands | $0.75-$1 | 512 GB
Disk | 5M-20M ns | Millions | $0.05-$0.1 | 4 TB
Notes: Capacity and latency are closely coupled
Cost is inversely proportional

## Slide 6: Memory Hierarchy
RegFile
100s bytes
< 1 cycle access
*These are rough numbers, mileage may vary.
1,000,000+ cycle access
Disk (Many GB – few TB)
150-200 cycle access
Memory (128MB – few GB)
Notes: Registers part of CPU, Memory much larger, much slower to access
Get rid of DISK

## Slide 7: Goal
Can we create an illusion of fast, cheap and large memory?
YES! Caches!
  Using fast technology (SRAM)
  Being smart about access and placement of data
    Temporal locality
    Spatial locality
Notes: Caches and taking advantage of temporal and spatial locality!!

## Slide 8: Memory Hierarchy
< 1 cycle access
L2 Cache (½-32MB)
5-15 cycle access
150-200 cycle access
L3 becoming more common
*These are rough numbers, mileage may vary.
1-3 cycle access
L1 Cache
(several KB)
1000000+ cycle access
Disk (Many GB – few TB)
Memory (128MB – few GB)
RegFile
100s bytes

## Slide 9: Caches on Today’s CPUs
L1
L1
L1
L1
L2
L2
L2
L2
This Core i7 CPU has 4 cores, a memory controller and the QuickPath Interconnect (QPI at bottom left and right) on a single chip (die).

## Slide 10: Just like your Contacts!
* Will refer to this analogy using BLUE in the slides.
5-15 clicks
Favorites
1-3 clicks
Speed
Dial
Bunch of clicks
Google / Facebook / White Pages
~ 1 click
Last
Called
More clicks
Contacts

## Slide 11: Memory Hierarchy
Storage (memory/DRAM) farther from processor
  big & slow
  stores inactive data
  contacts
Storage (cache/SRAM) closer to processor
  small & fast
  stores active data
  speed dial & favorites

## Slide 12: Memory Hierarchy
L2/L3 Cache
SRAM
9% of data is
“active”
Memory DRAM
90% of data
inactive
(not accessed)
L1 Cache
SRAM-on-chip
1% of data most accessed
Favorites
9% of people called
Contacts
90% people rarely called
Speed Dial
1% most called people

## Slide 13: Insight for Caches
If Mem[x] was accessed recently...
… then Mem[x] is likely to be accessed soon
  Exploit temporal locality:
    Put recently accessed Mem[x] higher in memory hierarchy since it will likely be accessed again soon
    If you call a contact, you are more likely to call them again soon
… then Mem[x ± ε] is likely to be accessed soon
  Exploit spatial locality:
    Put entire block containing Mem[x] and surrounding addresses higher in memory hierarchy since nearby address will likely be accessed
    If you call a member of a family, you are more likely to call other members
put entire block containing Mem[x] higher in the pyramid
put recently accessed Mem[x] higher in the pyramid
A: Data that will be used soon
Notes: Copy the data that is accessed recently, or around data that is accessed recently closer to the CPU!

## Slide 14: What is in Memory?
int n = 4;
int k[] = {3, 14, 0, 10};
int fib(int i) {
  if (i <= 2) return i;
  else return fib(i-1)+fib(i-2);
}
int main(int ac, char **av) {
for (int i = 0; i < n; i++) {
printi(fib(k[i]));
prints("\n");
}
}
Temporal Locality
Spatial Locality

## Slide 15: Cache Lookups (Read)
Processor tries to access Mem[x]
You try to speed dial “Smith, Paul”
Check: is block containing Mem[x] in the cache?
Check: is Smith in your Speed Dial?
Yes: cache hit!
  return requested data from cache line!
  call Smith, P.!

## Slide 16: Cache Lookups (Read)
No: cache miss
  read block from memory (or lower level cache)
  find Smith, P. in Contacts (or Favorites)
  (evict an existing cache line to make room)
  (delete a speed dial number to make room for Smith, P.)
  place new block in cache
  store Smith, P. in speed dial
  return requested data
  call Smith, P.!
   and stall the pipeline while all of this happens
Processor tries to access Mem[x]
You try to speed dial “Smith, Paul”
Check: is block containing Mem[x] in the cache?
Check: is Smith in your Speed Dial?
Notes: Fix animation!

## Slide 17: Definitions and Terms
Block (or cacheline or line)
  Minimum unit of information that is present/or not in the cache
  Minimum # of contact numbers that is either present or not
Cache hit
  Contact in Speed Dial
Cache miss
  Contact not in Speed Dial
Hit rate
  The fraction of memory accesses found in a level of the memory hierarchy
  The fraction of contacts found in Speed Dial
Miss rate
  The fraction of memory accesses not found in a level of the memory hierarchy
  The fraction of contacts not found in Speed Dial

## Slide 18: Cache Questions
What structure to use?
  Where to place a block?
  How to find a block?
When miss, which block to replace?
What happens on write?
  Next lecture

## Slide 19: Three common designs
A given data block can be placed…
  … in exactly one cache line  Direct Mapped
  … in any cache line  Fully Associative
  … in a small set of cache lines  Set Associative
Notes: Give Address Book reference

## Slide 20: Direct Mapped Cache
Each contact can be mapped to a single digit
Contacts
Baker, J. | 111-111-1111
Baker, S. | 222-222-2222
Dunn, A. | 333-333-3333
Foster, D. | 444-444-4444
Gill, D. | 555-555-5555
Harris, F. | 666-666-6666
Jones, N. | 777-777-7777
Lee, V. | 888-888-8888
Mann, B. | 111-111-1119
Moore, F. | 222-222-2229
Powell, C. | 333-333-3339
Sam, J. | 444-444-4449
Taylor, B. | 555-555-5559
Taylor, O. | 666-666-6669
Wright, T. | 777-777-7779
Zhang, W. | 888-888-8889
Notes: 4 bytes each, 8 bytes per line, show tags

## Slide 21: Direct Mapped Cache
Each contact can be mapped to a single digit
Baker, J.
ABC  2
2  111-111-1111
Your brain is doing indexing!
Contacts
Baker, J. | 111-111-1111
Baker, S. | 222-222-2222
Dunn, A. | 333-333-3333
Foster, D. | 444-444-4444
Gill, D. | 555-555-5555
Harris, F. | 666-666-6666
Jones, N. | 777-777-7777
Lee, V. | 888-888-8888
Mann, B. | 111-111-1119
Moore, F. | 222-222-2229
Powell, C. | 333-333-3339
Sam, J. | 444-444-4449
Taylor, B. | 555-555-5559
Taylor, O. | 666-666-6669
Wright, T. | 777-777-7779
Zhang, W. | 888-888-8889
Notes: 4 bytes each, 8 bytes per line, show tags

## Slide 22: Direct Mapped Cache
Speed Dial
Use the first letter to index!
Block Size: 1 Contact Number
Contacts
2 | ABC | Baker, J.
3 | DEF | Dunn, A.
4 | GHI | Gill, S.
5 | JKL | Jones, N.
6 | MNO | Mann, B.
7 | PQRS | Powell, J.
8 | TUV | Taylor, B.
9 | WXYZ | Wright, T.
Baker, J. | 111-111-1111
Baker, S. | 222-222-2222
Dunn, A. | 333-333-3333
Foster, D. | 444-444-4444
Gill, D. | 555-555-5555
Harris, F. | 666-666-6666
Jones, N. | 777-777-7777
Lee, V. | 888-888-8888
Mann, B. | 111-111-1119
Moore, F. | 222-222-2229
Powell, C. | 333-333-3339
Sam, J. | 444-444-4449
Taylor, B. | 555-555-5559
Taylor, O. | 666-666-6669
Wright, T. | 777-777-7779
Zhang, W. | 888-888-8889
Notes: 4 bytes each, 8 bytes per line, show tags

## Slide 23: Direct Mapped Cache
Speed Dial
2 | ABC | Baker, J. | Baker, S.
3 | DEF | Dunn, A. | Foster, D.
4 | GHI | Gill, D. | Harris, F.
5 | JKL | Jones, N. | Lee, V.
6 | MNO | Mann, B. | Moore, F.
7 | PQRS | Powell, C. | Sam, J.
8 | TUV | Taylor, B. | Taylor, O.
9 | WXYZ | Wright, T. | Zhang, W.
Use the first letter to index!
Use the initial to offset!
Contacts
Block Size: 2 Contact Numbers
Baker, J. | 111-111-1111
Baker, S. | 222-222-2222
Dunn, A. | 333-333-3333
Foster, D. | 444-444-4444
Gill, D. | 555-555-5555
Harris, F. | 666-666-6666
Jones, N. | 777-777-7777
Lee, V. | 888-888-8888
Mann, B. | 111-111-1119
Moore, F. | 222-222-2229
Powell, C. | 333-333-3339
Sam, J. | 444-444-4449
Taylor, B. | 555-555-5559
Taylor, O. | 666-666-6669
Wright, T. | 777-777-7779
Zhang, W. | 888-888-8889
Notes: 4 bytes each, 8 bytes per line, show tags

## Slide 24: Direct Mapped Cache
Cache
4 cachelines
2 words per cacheline
0x000004
0x000000
line 0
line 1
line 2
line 3
line 0
line 1
line 2
line 3
Memory
tag
index
offset
32-bit addr
3-bits
2-bits
27-bits
line 0 |  | 
line 1 |  | 
line 2 |  | 
line 3 |  | 
0x000000 | 
0x000004 | 
0x000008 | 
0x00000c | 
0x000010 | 
0x000014 | 
0x000018 | 
0x00001c | 
0x000020 | 
0x000024 | 
0x000028 | 
0x00002c | 
0x000030 | 
0x000034 | 
0x000038 | 
0x00003c | 
Each block number mapped to a single cache line index
Simplest hardware
Notes: 4 bytes each, 8 bytes per line, show tags

## Slide 25: Direct Mapped Cache
line 0 |  |  |  | 
line 1 |  |  |  | 
0x000000 | 
0x000004 | 
0x000008 | 
0x00000c | 
0x000010 | 
0x000014 | 
0x000018 | 
0x00001c | 
0x000020 | 
0x000024 | 
0x000028 | 
0x00002c | 
0x000030 | 
0x000034 | 
0x000038 | 
0x00003c | 
Memory
Cache
2 cachelines
4 words per cacheline
We need 4 bits to offset into 16 (24) bytes!
We need 1 bit to index into 2 lines!
Notes: 4 bytes each, 8 bytes per line, show tags

## Slide 26: Direct Mapped Cache
addr
line 0 |  |  |  | 
line 1 |  |  |  | 
0x000004
0x000000
0x000008
0x00000c
Cache
tag
index
offset
4-bits
1-bit
27-bits
Memory
2 cachelines
4-words per cacheline
0000 0000 0000 0000 0000 0000 0000 0100
0x000000 | 
0x000004 | 
0x000008 | 
0x00000c | 
0x000010 | 
0x000014 | 
0x000018 | 
0x00001c | 
0x000020 | 
0x000024 | 
0x000028 | 
0x00002c | 
0x000030 | 
0x000034 | 
0x000038 | 
0x00003c | 
32-bit addr
Notes: Animate!

## Slide 27: Direct Mapped Cache
line 0 |  |  |  | 
line 1 |  |  |  | 
0x000004
0x000000
0x000008
0x00000c
Cache
tag
index
offset
4-bits
1-bit
27-bits
Memory
2 cachelines
4-words per cacheline
line 0
line 1
0x000000 | 
0x000004 | 
0x000008 | 
0x00000c | 
0x000010 | 
0x000014 | 
0x000018 | 
0x00001c | 
0x000020 | 
0x000024 | 
0x000028 | 
0x00002c | 
0x000030 | 
0x000034 | 
0x000038 | 
0x00003c | 
32-bit addr

## Slide 28: Direct Mapped Cache
line 0 |  |  |  | 
line 1 |  |  |  | 
0x000004
0x000000
0x000008
0x00000c
Cache
tag
index
offset
4-bits
1-bit
27-bits
Memory
2 cachelines
4-words per cacheline
line 0
line 1
0x000000 | 
0x000004 | 
0x000008 | 
0x00000c | 
0x000010 | 
0x000014 | 
0x000018 | 
0x00001c | 
0x000020 | 
0x000024 | 
0x000028 | 
0x00002c | 
0x000030 | 
0x000034 | 
0x000038 | 
0x00003c | 
32-bit addr
line 0
line 1

## Slide 29: Direct Mapped Cache (Reading)
V
Tag
Block
=
Tag Index Offset
word select
hit?
data
=
hit?
data
word select
32bits
Byte offset

## Slide 30: Direct Mapped Cache (Reading)
V
Tag
=
word select
hit?
data
n bit index, m bit offset
Q: How big is the cache (data only)?
n
m
data
Tag
Index
Offset
32-bit addr
Cache

## Slide 31: Direct Mapped Cache (Reading)
=
word select
hit?
data
n bit index, m bit offset
Q: How much SRAM is needed (data + overhead)?
V
Tag
n
m
Tag
Index
Offset
data
overhead
32-bit addr
Cache

## Slide 32: Example: Direct Mapped Cache
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
Processor
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
4 cache lines
2 word block
Using byte addresses in this example! Addr Bus = 5 bits
0
0
0
0
V
tag data

## Slide 33: Example: Direct Mapped Cache
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
Processor
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
4 cache lines
2 word block
2 bit tag field
2 bit index field
1 bit offset
0
0
0
0
V
tag data
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 34: 1st Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Cache
Processor
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
0
0
0
0
V
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
tag data
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 35: 1st Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Cache
Processor
00
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
100
110
110
Misses: 1
Hits: 0
Addr: 00001
offset
1
0
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
V
M
0
0
tag data
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 36: 2nd Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Cache
Processor
00
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
100
110
110
Misses: 1
Hits: 0
1
0
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
V
M
0
0
tag data
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 37: 2nd Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Cache
Processor
00
$0
$1
$2
$3
Memory
00
100
120
140
170
190
210
230
250
100
110
110
Misses: 2
Hits: 0
150
140
150
Addr: 00101
offset
1
0
1
0
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
V
M
M
tag data
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 38: 3rd Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Cache
Processor
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
110
Misses: 2
Hits: 0
150
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
00
00
100
110
150
140
1
0
1
0
V
M
M
tag data
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 39: 3rd Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Cache
Processor
00
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
100
110
110
Misses: 2
Hits: 1
150
110
1
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
0
00
150
140
1
0
V
Addr: 00001
M
M
H
tag data
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 40: 4th Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Cache
Processor
00
$0
$1
$2
$3
Memory
2
100
120
140
170
190
210
230
250
100
110
110
Misses: 2
Hits: 1
150
140
150
110
1
1
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
0
0
0
00
150
140
1
0
V
M
M
H
tag data
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 41: 4th Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
110
Misses: 2
Hits: 2
150
140
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
00
2
100
110
150
140
1
1
0
0
0
00
150
140
1
0
V
Addr: 00100
offset
M
M
H
H
tag data
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 42: 5th Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
110
Misses: 2
Hits: 2
150
140
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
00
2
100
110
150
140
1
1
0
0
0
00
140
1
0
V
150
M
M
H
H
tag data
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 43: 5th Access
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
110
Misses: 2
Hits: 3
140
100
140
Cache
00
2
150
140
1
1
0
0
0
00
1
0
V
Addr: 00000
M
M
H
H
H
100
110
150
140
tag data
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 44: 6th Access
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 10 ]
LB $2  M[ 15 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
110
Misses: 2
Hits: 3
140
100
140
Cache
00
2
100
110
150
140
1
1
0
0
0
00
150
140
1
0
V
M
M
H
H
H
tag data
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 45: 6th Access
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 10 ]
LB $2  M[ 15 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
110
Misses: 3
Hits: 3
140
200
140
Addr: 01010
Cache
00
2
100
110
150
140
1
1
0
0
0
1
1
01
00
150
140
200
210
V
M
M
H
H
H
M
tag data
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 46: 7th Access
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 10 ]
LB $2  M[ 15 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
110
Misses: 3
Hits: 3
140
200
140
Cache
00
2
100
110
150
140
1
1
0
0
0
1
1
01
00
150
140
200
210
V
M
M
H
H
H
M
tag data
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 47: 7th Access
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 10 ]
LB $2  M[ 15 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
110
Misses: 4
Hits: 3
140
250
140
Addr: 01111
Cache
00
2
100
110
150
140
1
1
0
0
1
1
1
01
00
150
140
200
210
240
250
01
V
M
M
H
H
H
M
M
tag data
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 48: 8th Access
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 10 ]
LB $2  M[ 15 ]
LB $2  M[ 8 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
110
Misses: 4
Hits: 3
140
250
140
Cache
00
2
100
110
150
140
1
1
0
0
1
1
1
01
00
150
140
200
210
240
250
01
V
M
M
H
H
H
M
M
tag data
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 49: 8th Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
110
Misses: 5
Hits: 3
140
180
140
Addr: 01000
Cache
01
2
100
110
150
140
1
1
0
0
1
1
1
01
00
150
140
200
210
240
250
01
180
190
V
M
M
H
H
H
M
M
M
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 10 ]
LB $2  M[ 15 ]
LB $2  M[ 8 ]
tag data
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 50: Misses
Three types of misses
  Cold (aka Compulsory)
    The line is being referenced for the first time
  Capacity
    The line was evicted because the cache was not large enough
  Conflict
    The line was evicted because of another access whose index conflicted

## Slide 51: Misses
How to avoid…
Cold Misses
  Unavoidable? The data was never in the cache…
  Prefetching!
Capacity Misses
  Buy more SRAM
Conflict Misses
  Use a more flexible cache design

## Slide 52: 6th Access
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 8 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
110
Misses: 2
Hits: 3
140
100
140
Cache
00
2
100
110
150
140
1
1
0
0
0
00
150
140
1
0
V
M
M
H
H
H
tag data
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 53: 6th Access
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 8 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
110
Misses: 3
Hits: 3
140
220
140
Addr: 01100
Cache
00
2
150
140
1
1
0
0
0
1
0
V
M
M
H
H
H
M
100
110
01
230
220
tag data
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 54: 7th Access
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 8 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
110
Misses: 3
Hits: 3
140
220
140
Cache
00
2
150
140
1
1
0
0
0
1
0
V
M
M
H
H
H
M
100
110
01
230
220
tag data
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 55: 7th Access
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 8 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
180
Misses: 4
Hits: 3
140
220
140
Addr: 01000
Cache
01
2
100
110
150
140
1
1
0
0
0
01
230
220
1
0
180
190
V
M
M
H
H
H
M
M
tag data
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 56: 8th and 9th Accesses
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 8 ]
LB $2  M[ 4 ]
LB $2  M[ 0 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
180
Misses: 4
Hits: 3
140
220
140
Cache
01
2
100
110
150
140
1
1
0
0
0
01
230
220
1
0
180
190
V
M
M
H
H
H
M
M
tag data
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 57: 8th and 9th Accesses
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 8 ]
LB $2  M[ 4 ]
LB $2  M[ 0 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses: 4+2
Hits: 3
Cache
00
2
100
110
150
140
1
1
0
0
0
00
230
220
1
0
180
190
150
140
110
100
V
M
M
H
H
H
M
M
M
M
$0
$1
$2
$3
180
140
100
tag data
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 58: 10th and 11th Accesses
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 8 ]
LB $2  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 8 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses: 4+2
Hits: 3
Cache
00
2
100
110
150
140
1
1
0
0
0
00
230
220
1
0
180
190
150
140
110
100
V
M
M
H
H
H
M
M
M
M
tag data
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 59: 10th and 11th Accesses
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 8 ]
LB $2  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 8 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Cache
1
2
100
110
150
140
1
1
0
0
0
1
230
220
1
0
180
190
V
M
M
H
H
H
M
M
M
M
M
M
Misses: 4+2+2
Hits: 3
tag data
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 60: Cache Organization
How to avoid Conflict Misses?!
Three common designs
  Direct mapped: Block can only be in one line in the cache
    Contact numbers are assigned in the Speed Dial by first letter.
  Fully associative: Block can be anywhere in the cache
    Contact numbers are assigned without any rules.
  Set-associative: Block can be in a few (2 to 8) places in the cache
    Every digit in the Speed Dial maps to a new Speed Dial

## Slide 61: Direct Mapped Cache
Speed Dial
Use the first letter to index!
Block Size: 1 Contact Number
Contacts
2 | ABC | Baker, J.
3 | DEF | Dunn, A.
4 | GHI | Gill, S.
5 | JKL | Jones, N.
6 | MNO | Mann, B.
7 | PQRS | Powell, J.
8 | TUV | Taylor, B.
9 | WXYZ | Wright, T.
Baker, J. | 111-111-1111
Baker, S. | 222-222-2222
Dunn, A. | 333-333-3333
Foster, D. | 444-444-4444
Gill, D. | 555-555-5555
Harris, F. | 666-666-6666
Jones, N. | 777-777-7777
Lee, V. | 888-888-8888
Mann, B. | 111-111-1119
Moore, F. | 222-222-2229
Powell, C. | 333-333-3339
Sam, J. | 444-444-4449
Taylor, B. | 555-555-5559
Taylor, O. | 666-666-6669
Wright, T. | 777-777-7779
Zhang, W. | 888-888-8889
Notes: 4 bytes each, 8 bytes per line, show tags

## Slide 62: Fully Associative Cache
Speed Dial
No index!
Block Size: 1 Contact Number
Contacts
Mann, B.
Dunn, A.
Taylor, B.
Wright, T.
Baker, J.
Powell, J.
Gill, S.
Jones, N.
Baker, J. | 111-111-1111
Baker, S. | 222-222-2222
Dunn, A. | 333-333-3333
Foster, D. | 444-444-4444
Gill, D. | 555-555-5555
Harris, F. | 666-666-6666
Jones, N. | 777-777-7777
Lee, V. | 888-888-8888
Mann, B. | 111-111-1119
Moore, F. | 222-222-2229
Powell, C. | 333-333-3339
Sam, J. | 444-444-4449
Taylor, B. | 555-555-5559
Taylor, O. | 666-666-6669
Wright, T. | 777-777-7779
Zhang, W. | 888-888-8889
2
3
4
5
6
7
8
9
Notes: 4 bytes each, 8 bytes per line, show tags

## Slide 63: Fully Associative Cache
Speed Dial
Mann, B. | Moore, F.
Powell, C. | Sam, J.
Gill, D. | Harris, F.
Wright, T. | Zhang, W.
Baker, J. | Baker, S.
Dunn, A. | Foster, D.
Taylor, B. | Taylor, O.
Jones, N. | Lee, V.
No index!
Use the initial to offset!
Contacts
Block Size: 2 Contact Numbers
Baker, J. | 111-111-1111
Baker, S. | 222-222-2222
Dunn, A. | 333-333-3333
Foster, D. | 444-444-4444
Gill, D. | 555-555-5555
Harris, F. | 666-666-6666
Jones, N. | 777-777-7777
Lee, V. | 888-888-8888
Mann, B. | 111-111-1119
Moore, F. | 222-222-2229
Powell, C. | 333-333-3339
Sam, J. | 444-444-4449
Taylor, B. | 555-555-5559
Taylor, O. | 666-666-6669
Wright, T. | 777-777-7779
Zhang, W. | 888-888-8889
2
3
4
5
6
7
8
9
Notes: 4 bytes each, 8 bytes per line, show tags

## Slide 64: Fully Associative Cache (Reading)
V
Tag
Block
word select
hit?
data
line select
=
=
=
=
32bits
64bytes
Tag Offset
Notes: “way” = line

## Slide 65: Fully Associative Cache (Reading)
V
Tag
Block
Cache
m
Tag
Offset
32-bit addr
m bit offset, 2n blocks (cache lines)
Q: How big is the cache (data only)?
Notes: “way” = line

## Slide 66: Fully Associative Cache (Reading)
V
Tag
Block
Cache
m
Tag
Offset
32-bit addr
m bit offset, 2n blocks (cache lines)
Q: How much SRAM needed (data + overhead)?
Notes: “way” = line

## Slide 67: Example: Fully Associative Cache
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
Processor
tag data
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
4 cache lines
2 word block
4 bit tag field
1 bit block offset
V
V
V
V
V
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 68: 1st Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
Processor
tag data
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
0
0
0
0
V
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 69: 1st Access
0
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
Processor
0000
tag data
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
100
110
110
Misses: 1
Hits: 0
Addr: 00001
offset
1
0
0
M
lru
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 70: 2nd Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
Processor
0000
tag data
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
100
110
110
Misses: 1
Hits: 0
lru
1
0
0
0
M
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 71: 2nd Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
Processor
0000
tag data
$0
$1
$2
$3
Memory
0010
100
120
140
170
190
210
230
250
100
110
110
Misses: 2
Hits: 0
150
140
150
Addr: 00101
offset
1
1
0
0
M
M
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 72: 3rd Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
Processor
0000
tag data
$0
$1
$2
$3
Memory
0010
100
120
140
170
190
210
230
250
100
110
110
Misses: 2
Hits: 0
150
140
150
1
1
0
0
M
M
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 73: 3rd Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
Processor
0000
tag data
$0
$1
$2
$3
Memory
0010
100
120
140
170
190
210
230
250
100
110
110
Misses: 2
Hits: 1
150
140
150
110
1
1
0
0
Addr: 00001
offset
M
M
H
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 74: 4th Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
Processor
0000
tag data
$0
$1
$2
$3
Memory
0010
100
120
140
170
190
210
230
250
100
110
110
Misses: 2
Hits: 1
150
140
150
110
1
1
0
0
M
M
H
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 75: 4th Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
Processor
0000
tag data
$0
$1
$2
$3
Memory
0010
100
120
140
170
190
210
230
250
100
110
110
Misses: 2
Hits: 2
150
140
150
140
1
1
0
0
Addr: 00100
offset
M
M
H
H
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 76: 5th Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
Processor
0000
tag data
$0
$1
$2
$3
Memory
0010
100
120
140
170
190
210
230
250
100
110
110
Misses: 2
Hits: 2
150
140
150
140
1
1
0
0
M
M
H
H
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 77: 5th Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
Cache
Processor
0
tag data
$0
$1
$2
$3
Memory
2
100
120
140
170
190
210
230
250
100
110
110
Misses: 2
Hits: 3
150
140
140
100
140
1
1
0
0
Addr: 00000
offset
M
M
H
H
H
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 78: 6th Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Cache
Processor
0
tag data
$0
$1
$2
$3
Memory
2
100
120
140
170
190
210
230
250
100
110
110
Misses: 2
Hits: 3
150
140
140
100
140
1
1
0
0
M
M
H
H
H
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 8 ]
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 79: 6th Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
110
Misses: 3
Hits: 3
140
220
140
Addr: 01100
Cache
0000
tag data
0010
100
110
150
140
1
1
1
0
0
0110
220
230
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 8 ]
M
M
H
H
H
M
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 80: 7th Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
110
Misses: 3
Hits: 3
140
220
140
Cache
0000
tag data
0010
100
110
150
140
1
1
1
0
0
0110
220
230
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 8 ]
M
M
H
H
H
M
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 81: 7th Access
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
110
Misses: 4
Hits: 3
140
100
140
Addr: 01000
Cache
0000
tag data
0010
100
110
150
140
1
1
1
0
1
0110
220
230
180
190
0100
180
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 8 ]
M
M
H
H
H
M
M
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 82: 8th and 9th Accesses
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
$0
$1
$2
$3
Memory
100
120
140
170
190
210
230
250
110
Misses: 4
Hits: 3
140
100
140
Cache
0000
tag data
0010
100
110
150
140
1
1
1
0
1
0110
220
230
180
190
0100
180
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 8 ]
LB $2  M[ 4 ]
LB $2  M[ 0 ]
M
M
H
H
H
M
M
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 83: 8th and 9th Accesses
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses: 4
Hits: 3+2
Cache
0000
tag data
0010
100
110
150
140
1
1
1
0
1
0110
220
230
180
190
0100
$0
$1
$2
$3
110
140
100
140
180
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 8 ]
LB $2  M[ 4 ]
LB $2  M[ 0 ]
M
M
H
H
H
M
M
H
H
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 84: 10th and 11th Accesses
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses: 4
Hits: 3+2
Cache
0000
tag data
0010
100
110
150
140
1
1
1
0
1
0110
220
230
180
190
0100
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 8 ]
LB $2  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 8 ]
M
M
H
H
H
M
M
H
H
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 85: 10th and 11th Accesses
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses: 4
Hits: 3+2+2
Cache
0000
tag data
0010
100
110
150
140
1
1
1
0
1
0110
220
230
180
190
0100
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 8 ]
LB $2  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 8 ]
M
M
H
H
H
M
M
H
H
H
H
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 86: Eviction
Which cache line should be evicted from the cache to make room for a new line?
  Direct-mapped
    no choice, must evict line selected by index
  Associative caches
    Random: select one of the lines at random
    Round-Robin: similar to random
    FIFO: replace oldest line
    LRU: replace line that has not been used in the longest time

## Slide 87: Cache Tradeoffs
 | Direct Mapped | Fully Associative
Tag Size | Smaller | Larger
SRAM Overhead | Less | More
Controller Logic | Less | More
Speed | Faster | Slower
Price | Less | More
Scalability | Very | Not Very
# of conflict misses | Lots | Zero
Hit Rate | Low | High
Pathological Cases | Common | ?

## Slide 88: Hybrid Approach
Set-associative cache!
Like a direct-mapped cache
  Index into a location
  Fast
Like a fully-associative cache
  Can store multiple entries
    decreases thrashing in cache
  Search in each element

## Slide 89: 3-Way Set Associative Cache
word select
hit?
data
line select
=
=
=
32bits
64bytes
Tag Index Offset

## Slide 90: Comparison: Direct Mapped
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses:
Hits:
Cache
tag data
2
100
110
150
140
1
0
0
4 cache lines
2 word block
2 bit tag field
2 bit index field
1 bit block offset field
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 91: Comparison: Direct Mapped
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses: 8
Hits: 3
Cache
00
tag data
2
100
110
150
140
1
1
0
0
0
00
230
220
1
0
180
190
150
140
110
100
4 cache lines
2 word block
2 bit tag field
2 bit index field
1 bit block offset field
M
M
H
H
H
M
M
M
M
M
M
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 92: Comparison: Fully Associative
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses:
Hits:
Cache
tag data
0
4 cache lines
2 word block
4 bit tag field
1 bit block offset field
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 93: Comparison: Fully Associative
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses: 3
Hits: 8
Cache
0000
tag data
0010
100
110
150
140
1
1
1
0
0110
220
230
4 cache lines
2 word block
4 bit tag field
1 bit block offset field
M
M
H
H
H
M
H
H
H
H
H
Using byte addresses in this example! Addr Bus = 5 bits

## Slide 94: Comparison: 2-Way Set Associative
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses:
Hits:
Cache
tag data
0
0
0
0
2 sets
2 word block
3 bit tag field
1 bit set index field
1 bit block offset field
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
Using byte addresses in this example! Addr Bus = 5 bits
tag data
Notes: 0001 M: 1, H: 0
0101 M: 2, H: 0
0001 M: 2, H: 3 01/45/00/00
1100 M: 3, H: 3 12,13/01/00/00
1000 M:4, H:3 12,13/4,5/00/00
0100 M:5, H:3 8,9/45/00/00
0000 M:5, H:4 01/45/00/00
1100 M: 3, H: 3 12,13/01/00/00
1000 M:4, H:3 8,9/12,13/00/00
M:7,H:4

## Slide 95: Comparison: 2-Way Set Associative
110
130
150
160
180
200
220
240
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Processor
Memory
100
120
140
170
190
210
230
250
Misses: 4
Hits: 7
Cache
0
0
0
0
2 sets
2 word block
3 bit tag field
1 bit set index field
1 bit block offset field
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
M
M
H
H
H
M
M
H
H
H
H
Using byte addresses in this example! Addr Bus = 5 bits
tag data
tag data
Notes: 0001 M: 1, H: 0
0101 M: 2, H: 0
0001 M: 2, H: 3 01/45/00/00
1100 M: 3, H: 3 12,13/01/00/00
1000 M:4, H:3 12,13/4,5/00/00
0100 M:5, H:3 8,9/45/00/00
0000 M:5, H:4 01/45/00/00
1100 M: 3, H: 3 12,13/01/00/00
1000 M:4, H:3 8,9/12,13/00/00
M:7,H:4

## Slide 96: Summary
Caching assumptions
  small working set: 90/10 rule
  can predict future: spatial & temporal locality
Benefits
  big & fast memory built from (big & slow) + (small & fast)
Tradeoffs: associativity, line size, hit cost, miss penalty, hit rate
  Fully Associative  higher hit cost, higher hit rate
  Larger block size  lower hit cost, higher miss penalty

## Slide 97: Remaining Issues
To Do:
  Evicting cache lines
  Picking cache parameters
  Writing using the cache