## Slide 1: Caches 3
Prof. Hakim Weatherspoon
CS 3410, Spring 2015
Computer Science
Cornell University
See P&H Chapter: 5.1-5.4, 5.8, 5.10, 5.15; Also, 5.13 & 5.17

## Slide 2: Overview
Writing to caches: policies, performance
Cache tradeoffs and performance

## Slide 3: What about Stores?
Where should you write the result of a store?
  If that memory location is in the cache?
    Send it to the cache
    Should we also send it to memory right away?
    (write-through policy)
    Wait until we evict the block (write-back policy)
  If it is not in the cache?
    Allocate the line (put it in the cache)?
    (write allocate policy)
    Write it directly to memory without allocation?
    (no write allocate policy)

## Slide 4: Cache Write Policies
Q: How to write data?
CPU
Cache
SRAM
Memory
DRAM
addr
data
If data is already in the cache…
No-Write
  writes invalidate the cache and go directly to memory
Write-Through
  writes go to main memory and cache
Write-Back
  CPU writes only to cache
  cache writes to main memory later (when block is evicted)

## Slide 5: Write Allocation Policies
Q: How to write data?
CPU
Cache
SRAM
Memory
DRAM
addr
data
If data is not in the cache…
Write-Allocate
  allocate a cache line for new data (and maybe write-through)
No-Write-Allocate
  ignore cache, just go to main memory

## Slide 6: Next Goal
How does a write-through cache work?
Assume write-allocate

## Slide 7: Handling Stores (Write-Through)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
Cache
Processor
V tag data
$0
$1
$2
$3
Memory
78
120
71
173
21
28
200
225
Misses: 0
Hits: 0
0
0
Assume write-allocate
policy
Using byte addresses in this example! Addr Bus = 5 bits
Fully Associative Cache
2 cache lines
2 word block
4 bit tag field
1 bit block offset field

## Slide 8: Write-Through (REF 1)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
Cache
Processor
V tag data
$0
$1
$2
$3
Memory
78
120
71
173
21
28
200
225
Misses: 0
Hits: 0
0
0

## Slide 9: How Many Memory References?
Write-through performance
Each miss (read or write) reads a block from mem
Each store writes an item to mem
Evictions don’t need to write to mem

## Slide 10: Summary: Write Through
Write-through policy with write allocate
Cache miss: read entire block from memory
Write: write only updated item to memory
Eviction: no need to write to memory

## Slide 11: Write-Through vs. Write-Back
Can we also design the cache NOT to write all stores immediately to memory?
  Keep the most current copy in cache, and update memory when that data is evicted (write-back policy)
  Do we need to write-back all evicted lines?
    No, only blocks that have been stored into (written)

## Slide 12: Write-Back Meta-Data
V = 1 means the line has valid data
D = 1 means the bytes are newer than main memory
When allocating line:
  Set V = 1, D = 0, fill in Tag and Data
When writing line:
  Set D = 1
When evicting line:
  If D = 0: just set V = 0
  If D = 1: write-back Data, then set D = 0, V = 0
V | D | Tag | Byte 1 | Byte 2 | … Byte N

## Slide 13: Write-back Example
Example: How does a write-back cache work?
Assume write-allocate

## Slide 14: Handling Stores (Write-Back)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
Cache
Processor
V d tag data
$0
$1
$2
$3
Memory
78
120
71
173
21
28
200
225
Misses: 0
Hits: 0
0
0
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
Using byte addresses in this example! Addr Bus = 5 bits
Assume write-allocate
policy
Fully Associative Cache
2 cache lines
2 word block
3 bit tag field
1 bit block offset field

## Slide 15: Write-Back (REF 1)
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
Cache
Processor
V d tag data
$0
$1
$2
$3
Memory
78
120
71
173
21
28
200
225
Misses: 0
Hits: 0
0
0
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]

## Slide 16: How Many Memory References?
Write-back performance
Each miss (read or write) reads a block from mem
Some evictions write a block to mem

## Slide 17: So is write back just better?
What are other performance tradeoffs between write-through and write-back?
How can we further reduce penalty for cost of writes to memory?

## Slide 18: Performance: An Example
Performance: Write-back versus Write-through
Assume: large associative cache, 16-byte lines
for (i=1; i<n; i++)
A[0] += A[i];
for (i=0; i<n; i++)
B[i] = A[i]
Notes: Q: direct, or associative? A: associative definitely (w/ LRU or LFU, etc.)
A) reads: miss every W’th A[i]
A) writes: n for write-through, 1 eviction for write-back
B) reads: miss every W’th A[i] or B[i]
B) writes: n for write-through, n for write-back

## Slide 19: Performance Tradeoffs
Q: Hit time: write-through vs. write-back?
Q: Miss penalty: write-through vs. write-back?

## Slide 20: Write Buffering
Q: Writes to main memory are slow!
Q: When does it help?

## Slide 21: Write-through vs. Write-back
Write-through is slower
  But simpler (memory always consistent)
Write-back is almost always faster
  write-back buffer hides large eviction cost
  But what about multiple cores with separate caches but sharing memory?
Write-back requires a cache coherency protocol
  Inconsistent views of memory
  Need to “snoop” in each other’s caches
  Extremely complex protocols, very hard to get right

## Slide 22: Cache-coherency
Q: Multiple readers and writers?
  A: Potentially inconsistent views of memory
Mem
L2
L1
L1
Cache coherency protocol
  May need to snoop on other CPU’s cache activity
  Invalidate cache line when other CPU writes
  Flush write-back caches before other CPU reads
  Or the reverse: Before writing/reading…
  Extremely complex protocols, very hard to get right
CPU
L1
L1
CPU
L2
L1
L1
CPU
L1
L1
CPU
disk
net
A
A
A
A
A’
A

## Slide 23
Write-through policy with write allocate
  Cache miss: read entire block from memory
  Write: write only updated item to memory
  Eviction: no need to write to memory
  Slower, but cleaner
Write-back policy with write allocate
  Cache miss: read entire block from memory
    But may need to write dirty cacheline first
  Write: nothing to memory
  Eviction: have to write to memory, entire cacheline because don’t know what is dirty (only 1 dirty bit)
  Faster, but complicated with multicore
Summary: Write Through

## Slide 24: Next Goal
Performance: What is the average memory access time (AMAT) for a cache?
AMAT = %hit x hit time + % miss x miss time

## Slide 25: Cache Performance Example
Average Memory Access Time (AMAT)
Cache Performance (very simplified):
L1 (SRAM): 512 x 64 byte cache lines, direct mapped
Data cost: 3 cycle per word access
Lookup cost: 2 cycle
Mem (DRAM): 4GB
Data cost: 50 cycle for first word, plus 3 cycles per subsequent word
16 words (i.e. 64 / 4 = 16)
Notes: Hit rate 90%
.90 *5 + .10*(2+50+16*3) = 4.5 + 10.0 = 14.5 cycles on average
Hit rate 95 %  9.5 cycles on average

## Slide 26: Cache Performance Example
Average Memory Access Time (AMAT)
Cache Performance (very simplified):
L1 (SRAM): 512 x 64 byte cache lines, direct mapped
Data cost: 3 cycle per word access
Lookup cost: 2 cycle
Mem (DRAM): 4GB
Data cost: 50 cycle for first word, plus 3 cycles per subsequent word
16 words (i.e. 64 / 4 = 16)
Notes: Hit rate 90%
.90 *5 + .10*(2+50+16*3) = 4.5 + 10.0 = 14.5 cycles on average
Hit rate 95 %  9.5 cycles on average

## Slide 27: Multi Level Caching
Cache Performance (very simplified):
L1 (SRAM): 512 x 64 byte cache lines, direct mapped
Hit time: 5 cycles
L2 cache: bigger
Hit time = 20 cycles
Mem (DRAM): 4GB
Hit rate: 90% in L1, 90% in L2
Often: L1 fast and direct mapped, L2 bigger and higher associativity

## Slide 28: Performance Summary
Average memory access time (AMAT)
depends on cache architecture and size
access time for hit,
miss penalty, miss rate
Cache design a very complex problem:
  Cache size, block size (aka line size)
  Number of ways of set-associativity (1, N, )
  Eviction policy
  Number of levels of caching, parameters for each
  Separate I-cache from D-cache, or Unified cache
  Prefetching policies / instructions
  Write policy

## Slide 29: Cache Conscious Programming
// H = 12, W = 10
int A[H][W];
for(x=0; x < W; x++)
for(y=0; y < H; y++)
sum += A[y][x];

## Slide 30: Cache Conscious Programming
// H = 12, W = 10
int A[H][W];
for(y=0; y < H; y++)
for(x=0; x < W; x++)
sum += A[y][x];

## Slide 31: A Real Example
> dmidecode -t cache
Cache Information
Configuration: Enabled, Not Socketed, Level 1
Operational Mode: Write Back
Installed Size: 128 KB
Error Correction Type: None
Cache Information
Configuration: Enabled, Not Socketed, Level 2
Operational Mode: Varies With Memory Address
Installed Size: 6144 KB
Error Correction Type: Single-bit ECC
> cd /sys/devices/system/cpu/cpu0; grep cache/*/*
cache/index0/level:1
cache/index0/type:Data
cache/index0/ways_of_associativity:8
cache/index0/number_of_sets:64
cache/index0/coherency_line_size:64
cache/index0/size:32K
cache/index1/level:1
cache/index1/type:Instruction
cache/index1/ways_of_associativity:8
cache/index1/number_of_sets:64
cache/index1/coherency_line_size:64
cache/index1/size:32K
cache/index2/level:2
cache/index2/type:Unified
cache/index2/shared_cpu_list:0-1
cache/index2/ways_of_associativity:24
cache/index2/number_of_sets:4096
cache/index2/coherency_line_size:64
cache/index2/size:6144K
Dual-core 3.16GHz Intel (purchased in 2011)

## Slide 32: A Real Example
Dual 32K L1 Instruction caches
  8-way set associative
  64 sets
  64 byte line size
Dual 32K L1 Data caches
  Same as above
Single 6M L2 Unified cache
  24-way set associative (!!!)
  4096 sets
  64 byte line size
4GB Main memory
1TB Disk
Dual-core 3.16GHz Intel (purchased in 2009)

## Slide 34: Summary
Memory performance matters!
  often more than CPU performance
  … because it is the bottleneck, and not improving much
  … because most programs move a LOT of data
Design space is huge
  Gambling against program behavior
  Cuts across all layers: users  programs  os  hardware
Multi-core / Multi-Processor is complicated
  Inconsistent views of memory
  Extremely complex protocols, very hard to get right