## Slide 1: Virtual Memory
Prof. Hakim Weatherspoon
CS 3410, Spring 2015
Computer Science
Cornell University
P & H Chapter 5.7 (up to TLBs)

## Slide 2: Announcements
Lab3: Available, and due next Wednesday
HW2: Do up to Problem5 this week. Do it now.
Do problem9, coding a hashtable in C, now.

## Slide 3: Announcements
Next five weeks
  Week 10 (Apr 7): Lab3 (calling convention) release
  Week 11 (Apr 14): Proj3 (caches) release, Lab3 due Wed
  Week 12 (Apr 21): Lab4 (virtual memory) release, due in-class, Proj3 due Fri, HW2 due Sat
  Week 13 (Apr 28): Proj4 (multi-core/parallelism) release, Lab4 due in-class, Prelim2 Thurs Apr 30th
  Week 14 (May 5): Proj3 Tournament Mon May 4th, Proj4 design doc due
Final Project for class
  Week 15 (May 12): Proj4 due Wed, Presentations Tu/Wed

## Slide 4: Big Picture: (Virtual) Memory
0xfffffffc
0x00000000
top
bottom
0x7ffffffc
0x80000000
0x10000000
0x00400000
system reserved
(stack grows down)
(heap grows up)
text
reserved
(static) data
(.stack)
.data
.text
system reserved
stack
system reserved
code (text)
static data
dynamic data (heap)
.data
.text
Notes: Add a clicker question. How many programs do you typically run at a time? How many programs can we run at once on a quad-core processor? How do we execute more than one process at a time.

## Slide 5: Big Picture: (Virtual) Memory
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard
Stack, Data, Code
Stored in Memory
$0 (zero)
$1 ($at)
$29 ($sp)
$31 ($ra)
Code Stored in Memory
(also, data and stack)
$$
$$

## Slide 6: Big Picture: (Virtual) Memory
How do we execute more than one program at a time?

## Slide 7: Big Picture: (Virtual) Memory
How do we execute more than one program at a time?
A: Abstraction – Virtual Memory
  Memory that appears to exist as main memory (although most of it is supported by data held in secondary storage, transfer between the two being made automatically as required—i.e. ”paging”)
  Abstraction that supports multi-tasking---the ability to run more than one process at a time

## Slide 8: Goals for Today: Virtual Memory
What is Virtual Memory?
How does Virtual memory Work?
  Address Translation
    Pages, page tables, and memory mgmt unit
  Paging
  Role of Operating System
    Context switches, working set, shared memory
  Performance
    How slow is it
    Making virtual memory fast
    Translation lookaside buffer (TLB)
  Virtual Memory Meets Caching

## Slide 9: Virtual Memory

## Slide 10: Big Picture: Multiple Processes
How to Run multiple processes?
Time-multiplex a single CPU core (multi-tasking)
  Web browser, skype, office, … all must co-exist
Many cores per processor (multi-core) or many processors (multi-processor)
  Multiple programs run simultaneously

## Slide 11: Big Picture: (Virtual) Memory
LB $1  M[ 1 ]
LB $2  M[ 5 ]
LB $3  M[ 1 ]
LB $3  M[ 4 ]
LB $2  M[ 0 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
LB $2  M[ 12 ]
LB $2  M[ 5 ]
Processor
Memory
Misses:
Hits:
Cache
tag data
2
100
110
150
140
1
0
0
Text
Data
Stack
Heap
0x000…0
0x7ff…f
0xfff…f
Memory: big & slow vs Caches: small & fast
$0
$1
$2
$3

## Slide 12: Processor & Memory
CPU address/data bus...
… routed through caches
… to main memory
  Simple, fast, but…
Q: What happens for LW/SW to an invalid location?
  0x000000000 (NULL)
  uninitialized pointer
.
CPU
Text
Data
Stack
Heap
Memory
0x000…0
0x7ff…f
0xfff…f
Memory
$$

## Slide 13: Multiple Processes
Q: What happens when another program is executed concurrently on another processor?
  .
CPU
Text
Data
Stack
Heap
Memory
CPU
Text
Data
Stack
Heap
0x000…0
0x7ff…f
0xfff…f
$$
$$

## Slide 14: Multiple Processes
Q: Can we relocate second program?
CPU
Text
Data
Stack
Heap
Memory
CPU
Text
Data
Stack
Heap
0x000…0
0x7ff…f
0xfff…f

## Slide 15: Solution? Multiple processes/processors
Q: Can we relocate second program?
CPU
Text
Data
Stack
Heap
Memory
CPU
Text
Data
Stack
Heap

## Slide 16: Takeaway
All problems in computer science can be solved by another level of indirection.
– David Wheeler
– or, Butler Lampson
– or, Leslie Lamport
– or, Steve Bellovin

## Slide 17: Takeaway
All problems in computer science can be solved by another level of indirection.
– David Wheeler
– or, Butler Lampson
– or, Leslie Lamport
– or, Steve Bellovin
Solution: Need a MAP
To map a Virtual Address (generated by CPU)
to a Physical Address (in memory)

## Slide 18: Next Goal
How does Virtual Memory work?
i.e. How do we create that “map” that maps a virtual address generated by the CPU to a physical address used by main memory?

## Slide 19: Virtual Memory
Virtual Memory: A Solution for All Problems
  Program/CPU can access any address from 0…2N
  (e.g. N=32)
Each process has its own virtual address space
  A process is a program being executed
  Programmer can code as if they own all of memory
On-the-fly at runtime, for each memory access
  all access is indirect through a virtual address
  translate fake virtual address to a real physical address
  redirect load/store to the physical address
map

## Slide 20: Address Space
Programs load/store to virtual addresses
Actual memory uses physical addresses
Memory Management Unit (MMU)
  Responsible for translating on the fly
  Essentially, just a big array of integers: paddr = PageTable[vaddr];
CPU
MMU
A
B
C
X
Y
Z
X
Y
Z
C
B
A
CPU
MMU
0x1000
0x1000
Virtual Address
Space
Physical Address Space
Virtual Address
Space
Notes: each mmu has own mappings
Easy relocation
Higher memory utilization
Easy sharing

## Slide 21: Virtual Memory Advantages
Advantages
Easy relocation
  Loader puts code anywhere in physical memory
  Creates virtual mappings to give illusion of correct layout
Higher memory utilization
  Provide illusion of contiguous memory
  Use all physical memory, even physical address 0x0
Easy sharing
  Different mappings for different programs / cores
And more to come…

## Slide 22: Takeaway
All problems in computer science can be solved by another level of indirection.
Need a map to translate a “fake” virtual address (generated by CPU) to a “real” physical Address (in memory)
Virtual memory is implemented via a “Map”, a PageTage, that maps a vaddr (a virtual address) to a paddr (physical address):
paddr = PageTable[vaddr]

## Slide 23: Next Goal
How do we implement that translation from a virtual address (vaddr) to a physical address (paddr)?
paddr = PageTable[vaddr]
i.e. How do we implement the PageTable??

## Slide 24
Address Translation
Pages, Page Tables, and
the Memory Management Unit (MMU)

## Slide 25: Attempt#1: Address Translation
How large should a PageTable be for a MMU?
paddr = PageTable[vaddr];
Granularity?
  Per word…
  Per block…
  Variable..…
Typical:
  4KB – 16KB pages
  4MB – 256MB jumbo pages
Notes: per word … too expensive: 4GB PageTable arrray
per block… ?
Variable … complicated hardware
We will stick to 4kb pages

## Slide 26: Attempt #1: Address Translation
Attempt #1: For any access to virtual address:
  Calculate virtual page number and page offset
  Lookup physical page number at PageTable[vpn]
  Calculate physical address as ppn:offset
vaddr
Page Offset
Virtual page number
Page offset
Physical page number
Lookup in PageTable
paddr
31 12 11 0
12 11 0
CPU
generated
Main
Memory
e.g. Page size
4 kB = 212
Notes: 4kb pages = 12 bits for page offset, 20 bits for VPN

## Slide 27: Takeaway
All problems in computer science can be solved by another level of indirection.
Need a map to translate a “fake” virtual address (generated by CPU) to a “real” physical Address (in memory)
Virtual memory is implemented via a “Map”, a PageTage, that maps a vaddr (a virtual address) to a paddr (physical address):
paddr = PageTable[vaddr]
A page is constant size block of virtual memory. Often, the page size will be around 4kB to reduce the number of entries in a PageTable.

## Slide 28: Next Goal
Example
How to translate a vaddr (virtual address) generated by the CPU to a paddr (physical address) used by main memory using the PageTable managed by the memory management unit (MMU).

## Slide 29: Next Goal
Example
How to translate a vaddr (virtual address) generated by the CPU to a paddr (physical address) used by main memory using the PageTable managed by the memory management unit (MMU).
Q: Where is the PageTable stored??

## Slide 30: Simple PageTable
Q: Where to store page tables?
CPU
MMU
Data
Read Mem[0x4123B538]
0x00000000
0x90000000
0x10045000
0x4123B000
0xC20A3000
0x10044000
PageOffset
VPN: virtual page number
PTBR
Notes: VADDR = 0x00401538
PFN = VADDR/4kb = VADDR>>12 = 0x401
PageTableEntry at 0x90000804 contains 0x4123B000
Data at 0x4123B538

## Slide 31: Simple PageTable
vpn | pgoff
 | Physical Page Number
 | 0x10045
 | 0xC20A3
 | 0x4123B
 | 0x10044
vaddr
PTBR
0x00000000
0x90000000
0x10045000
0xC20A3000
0x10044000
0x4123B000

## Slide 32: Invalid Pages
Cool Trick #1: Don’t map all pages
Need valid bit for each page table entry
Q: Why?
.
V |  | Physical Page Number
0 |  | 
1 |  | 0x10045
0 |  | 
0 |  | 
1 |  | 0xC20A3
1 |  | 0x4123B
1 |  | 0x10044
0 |  | 
0x00000000
0x90000000
0x10045000
0x4123B000
0xC20A3000
0x10044000

## Slide 33: Page Permissions
Cool Trick #2: Page permissions!
Keep R, W, X permission bits for each page table entry
Q: Why?
.
V | R | W | X |  | Physical Page Number
0 |  |  |  |  | 
1 |  |  |  |  | 0x10045
0 |  |  |  |  | 
0 |  |  |  |  | 
1 |  |  |  |  | 0xC20A3
1 |  |  |  |  | 0x4123B
1 |  |  |  |  | 0x10044
0 |  |  |  |  | 
0x00000000
0x90000000
0x10045000
0x4123B000
0xC20A3000
0x10044000

## Slide 34: Aliasing
Cool Trick #3: Aliasing
Map the same physical page at several virtual addresses
Q: Why?
.
V | R | W | X |  | Physical Page Number
0 |  |  |  |  | 
1 |  |  |  |  | 0xC20A3
0 |  |  |  |  | 
0 |  |  |  |  | 
1 |  |  |  |  | 0xC20A3
1 |  |  |  |  | 0x4123B
1 |  |  |  |  | 0x10044
0 |  |  |  |  | 
0x00000000
0x90000000
0x10045000
0x4123B000
0xC20A3000
0x10044000

## Slide 35: Page Size Example
Overhead for VM Attempt #1 (example)
Virtual address space (for each process):
  total memory: 232 bytes = 4GB
  page size: 212 bytes = 4KB
  entries in PageTable?
  size of PageTable?
Physical address space:
  total memory: 229 bytes = 512MB
  overhead for 10 processes?

## Slide 36: Takeaway
All problems in computer science can be solved by another level of indirection.
Need a map to translate a “fake” virtual address (generated by CPU) to a “real” physical Address (in memory)
Virtual memory is implemented via a “Map”, a PageTage, that maps a vaddr (a virtual address) to a paddr (physical address):
paddr = PageTable[vaddr]
A page is constant size block of virtual memory. Often, the page size will be around 4kB to reduce the number of entries in a PageTable.
We can use the PageTable to set Read/Write/Execute permission on a per page basis. Can allocate memory on a per page basis. Need a valid bit, as well as Read/Write/Execute and other bits.
But, overhead due to PageTable is significant.

## Slide 37: Next Goal
How do we reduce the size (overhead) of the PageTable?

## Slide 38: Next Goal
How do we reduce the size (overhead) of the PageTable?
A: Another level of indirection!!

## Slide 39: Beyond Flat Page Tables
Assume most of PageTable is empty
How to translate addresses?
10 bits
PTBR
10 bits
10 bits
vaddr
PDEntry
Page Directory
Page Table
PTEntry
Page
Word
2
Multi-level PageTable
* x86 does exactly this
Notes: Q: Benefits?
A1: Don’t need 4MB contiguous physical memory
A2: Don’t need to allocate every PageTable, only those containing valid PTEs
Q: Drawbacks?
A: Longer lookups.

## Slide 40: Beyond Flat Page Tables
Assume most of PageTable is empty
How to translate addresses? Multi-level PageTable
Q: Benefits?
Q: Drawbacks
Notes: Q: Benefits?
A1: Don’t need 4MB contiguous physical memory
A2: Don’t need to allocate every PageTable, only those containing valid PTEs
Q: Drawbacks?
A: Longer lookups.

## Slide 41: Takeaway
All problems in computer science can be solved by another level of indirection.
Need a map to translate a “fake” virtual address (generated by CPU) to a “real” physical Address (in memory)
Virtual memory is implemented via a “Map”, a PageTage, that maps a vaddr (a virtual address) to a paddr (physical address):
paddr = PageTable[vaddr]
A page is constant size block of virtual memory. Often, the page size will be around 4kB to reduce the number of entries in a PageTable.
We can use the PageTable to set Read/Write/Execute permission on a per page basis. Can allocate memory on a per page basis. Need a valid bit, as well as Read/Write/Execute and other bits.
But, overhead due to PageTable is significant.
Another level of indirection, two levels of PageTables and significantly reduce the overhead due to PageTables.

## Slide 42: Next Goal
Can we run process larger than physical memory?

## Slide 43
Paging

## Slide 44: Paging
Can we run process larger than physical memory?
  The “virtual” in “virtual memory”
View memory as a “cache” for secondary storage
  Swap memory pages out to disk when not in use
  Page them back in when needed
Assumes Temporal/Spatial Locality
  Pages used recently most likely to be used again soon

## Slide 45: Paging
Cool Trick #4: Paging/Swapping
Need more bits:
Dirty, RecentlyUsed, …
V | R | W | X | D | Physical Page Number
0 |  |  |  |  | invalid
1 |  |  |  | 0 | 0x10045
0 |  |  |  |  | invalid
0 |  |  |  |  | invalid
0 |  |  |  | 0 | disk sector 200
0 |  |  |  | 0 | disk sector 25
1 |  |  |  | 1 | 0x00000
0 |  |  |  |  | invalid
0x00000000
0x90000000
0x10045000
0x4123B000
0xC20A3000
25
200
Notes: A: can make code read-only, executable; make data read-write but not executable; etc.

## Slide 46: Summary
Virtual Memory
  Address Translation
    Pages, page tables, and memory mgmt unit
  Paging
Next time
  Role of Operating System
    Context switches, working set, shared memory
  Performance
    How slow is it
    Making virtual memory fast
    Translation lookaside buffer (TLB)
  Virtual Memory Meets Caching