## Slide 1: Virtual Memory 2
Prof. Hakim Weatherspoon
CS 3410, Spring 2015
Computer Science
Cornell University
P & H Chapter 5.7

## Slide 2: Announcements
Lab3: Available today, and due by next Wednesday
HW2: Do up to Problem5 this week. Do it now.
Do Problem9, coding a hashtable in C, now.

## Slide 3: Announcements
Next five weeks
  Week 10 (Apr 7): Lab3 (calling convention) release
  Week 11 (Apr 14): Proj3 (caches) release, Lab3 due Wed
  Week 12 (Apr 21): Lab4 (virtual memory) release, due in-class, Proj3 due Fri, HW2 due Sat
  Week 13 (Apr 28): Proj4 (multi-core/parallelism) release, Lab4 due in-class, Prelim2
  Week 14 (May 5): Proj3 Tournament, Proj4 design doc due
Final Project for class
  Week 15 (May 12): Proj4 due Wed

## Slide 4: Goals for Today
Virtual Memory
  Address Translation
    Pages, page tables, and memory mgmt unit
  Paging
  Performance
    How slow is it
    Making virtual memory fast
    Translation lookaside buffer (TLB)
  Virtual Memory Meets Caching
  Role of Operating System
    Context switches, working set, shared memory

## Slide 5: Virtual Memory
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard
Stack, Data, Code
Stored in Memory
$0 (zero)
$1 ($at)
$29 ($sp)
$31 ($ra)
Code Stored in Memory
(also, data and stack)
$$
$$

## Slide 6: Virtual Memory Summary
All problems in computer science can be solved by another level of indirection.
Need a map to translate a “fake” virtual address (generated by CPU) to a “real” physical Address (in memory)
Virtual memory is implemented via a “Map”, a PageTage, that maps a vaddr (a virtual address) to a paddr (physical address):
paddr = PageTable[vaddr]
A page is constant size block of virtual memory. Often, the page size will be around 4kB to reduce the number of entries in a PageTable.
We can use the PageTable to set Read/Write/Execute permission on a per page basis. Can allocate memory on a per page basis. Need a valid bit, as well as Read/Write/Execute and other bits.
But, overhead due to PageTable is significant.

## Slide 7: Next Goal
How do we reduce the size (overhead) of the PageTable?

## Slide 8: Next Goal
How do we reduce the size (overhead) of the PageTable?
A: Another level of indirection!!

## Slide 9: Beyond Flat Page Tables
V | R | W | X |  | Physical Page Number
0 |  |  |  |  | 
1 |  |  |  |  | 0xC20A3
0 |  |  |  |  | 
0 |  |  |  |  | 
1 |  |  |  |  | 0xC20A3
1 |  |  |  |  | 0x4123B
1 |  |  |  |  | 0x10044
0 |  |  |  |  | 
0x00000000
0x90000000
0x10045000
0x4123B000
0xC20A3000
0x10044000
Memory
Notes: A: can make different views of same data with different permissions

## Slide 10: Multi-level Page Tables
Assume most of PageTable is empty
How to translate addresses?
10 bits
PTBR
10 bits
10 bits
vaddr
PDEntry
Page Directory
Page Table
PTEntry
Page
Word
2
Multi-level PageTable
* x86 does exactly this
31 22 21 12 11 2 1 0
Notes: Q: Benefits?
A1: Don’t need 4MB contiguous physical memory
A2: Don’t need to allocate every PageTable, only those containing valid PTEs
Q: Drawbacks?
A: Longer lookups.

## Slide 11: Multi-level Page Tables
Assume most of PageTable is empty
How to translate addresses? Multi-level PageTable
Q: Benefits?
A: Don’t need 4MB contiguous physical memory
A: Don’t need to allocate every PageTable, only those containing valid PTEs
Q: Drawbacks
A: Performance: Longer lookups
Notes: Q: Benefits?
A1: Don’t need 4MB contiguous physical memory
A2: Don’t need to allocate every PageTable, only those containing valid PTEs
Q: Drawbacks?
A: Longer lookups.

## Slide 12: Takeaway
All problems in computer science can be solved by another level of indirection.
Need a map to translate a “fake” virtual address (generated by CPU) to a “real” physical Address (in memory)
Virtual memory is implemented via a “Map”, a PageTage, that maps a vaddr (a virtual address) to a paddr (physical address):
paddr = PageTable[vaddr]
A page is constant size block of virtual memory. Often, the page size will be around 4kB to reduce the number of entries in a PageTable.
We can use the PageTable to set Read/Write/Execute permission on a per page basis. Can allocate memory on a per page basis. Need a valid bit, as well as Read/Write/Execute and other bits.
But, overhead due to PageTable is significant.
Another level of indirection, two levels of PageTables, can significantly reduce the overhead due to PageTables.

## Slide 13: Next Goal
Can we run process larger than physical memory?

## Slide 14
Paging

## Slide 15: Paging
Can we run process larger than physical memory?
  The “virtual” in “virtual memory”
View memory as a “cache” for secondary storage
  Swap memory pages out to disk when not in use
  Page them back in when needed
Assumes Temporal/Spatial Locality
  Pages used recently most likely to be used again soon

## Slide 16: Paging
Cool Trick #4: Paging/Swapping
Need more bits:
Dirty, RecentlyUsed, …
V | R | W | X | D | Physical Page Number
0 |  |  |  |  | invalid
1 |  |  |  | 0 | 0x10045
0 |  |  |  |  | invalid
0 |  |  |  |  | invalid
0 |  |  |  | 0 | disk sector 200
0 |  |  |  | 0 | disk sector 25
1 |  |  |  | 1 | 0x00000
0 |  |  |  |  | invalid
0x00000000
0x90000000
0x10045000
0x4123B000
0xC20A3000
25
200
Notes: A: can make code read-only, executable; make data read-write but not executable; etc.

## Slide 17
Performance

## Slide 18: Performance
Virtual Memory Summary
PageTable for each process:
  Page table tradeoffs
    Single-level (e.g. 4MB contiguous in physical memory)
    or multi-level (e.g. less mem overhead due to page table),
    …
  every load/store translated to physical addresses
  page table miss = page fault
    load the swapped-out page and retry instruction, or kill program if the page really doesn’t exist, or tell the program it made a mistake

## Slide 19: Page Table Review
x86 Example: 2 level page tables, assume… 32 bit vaddr, 32 bit paddr 4k PDir, 4k PTables, 4k Pages
Q:How many bits for a physical page number?
A: 20
Q: What is stored in each PageTableEntry?
A: ppn, valid/dirty/r/w/x/…
Q: What is stored in each PageDirEntry?
A: ppn, valid/?/…
Q: How many entries in a PageDirectory?
A: 1024 four-byte PDEs
Q: How many entires in each PageTable?
A: 1024 four-byte PTEs
PDE
PTBR
PDE
PDE
PDE
PTE
PTE
PTE
PTE

## Slide 20: Page Table Example
x86 Example: 2 level page tables, assume… 32 bit vaddr, 32 bit paddr 4k PDir, 4k PTables, 4k Pages PTBR = 0x10005000 (physical)
Write to virtual address, vaddr= 0x7192a44c… Q: Byte offset in page? PT Index? PD Index?
(1) PageDir is at 0x10005000, so… Fetch PDE from physical address 0x1005000+(4*PDI)
  suppose we get {0x12345, v=1, …}
(2) PageTable is at 0x12345000, so… Fetch PTE from physical address 0x12345000+(4*PTI)
  suppose we get {0x14817, v=1, d=0, r=1, w=1, x=0, …}
(3) Page is at 0x14817000, so… Write data to physical address? Also: update PTE with d=1
PDE
PTBR
PDE
PDE
PDE
PTE
PTE
PTE
PTE
0x1481744c
0x44c
(vaddr<<10)>>22
vaddr>>22
0x1c6
0x12a
Notes: byte offset = 0x44c
PTI = 0x12a
PDI = (0x719 >> 2) = 0x1c6

## Slide 21: Performance
Virtual Memory Summary
PageTable for each process:
  Page
    Single-level (e.g. 4MB contiguous in physical memory)
    or multi-level (e.g. less mem overhead due to page table),
    …
  every load/store translated to physical addresses
  page table miss: load a swapped-out page and retry instruction, or kill program
Performance?
  How many memory references required to access memory? a) 1 b) 2
c) 3 d) 4
  e) 5
Notes: 4x slower!
Pipelining? No. Parallelization? No.

## Slide 22: Performance
Virtual Memory Summary
PageTable for each process:
  Page
    Single-level (e.g. 4MB contiguous in physical memory)
    or multi-level (e.g. less mem overhead due to page table),
    …
  every load/store translated to physical addresses
  page table miss: load a swapped-out page and retry instruction, or kill program
Performance?
  terrible: memory is already slow translation makes it slower
Solution?
  A cache, of course
Notes: 4x slower!
Pipelining? No. Parallelization? No.

## Slide 23: Next Goal
How do we speedup address translation?

## Slide 24
Making Virtual Memory Fast
  The Translation Lookaside Buffer (TLB)

## Slide 25: Translation Lookaside Buffer (TLB)
Hardware Translation Lookaside Buffer (TLB)
A small, very fast cache of recent address mappings
  TLB hit: avoids PageTable lookup
  TLB miss: do PageTable lookup, cache result for later

## Slide 26: TLB Diagram
V | R | W | X | D | 
0 |  |  |  |  | invalid
1 |  |  |  | 0 | 
0 |  |  |  |  | invalid
0 |  |  |  |  | invalid
1 |  |  |  | 0 | 
0 |  |  |  | 0 | 
1 |  |  |  | 1 | 
0 |  |  |  |  | invalid
V | R | W | X | D | tag | ppn
V |  | 
0 |  | invalid
0 |  | invalid
0 |  | invalid
1 |  | 
0 |  | invalid
1 |  | 
1 |  | 
0 |  | invalid

## Slide 27: A TLB in the Memory Hierarchy
(1) Check TLB for vaddr (~ 1 cycle)
(2) TLB Miss: traverse PageTables for vaddr
(3a) PageTable has valid entry for in-memory page
  Load PageTable entry into TLB; try again (tens of cycles)
(3b) PageTable has entry for swapped-out (on-disk) page
  Page Fault: load from disk, fix PageTable, try again (millions of cycles)
(3c) PageTable has invalid entry
  Page Fault: kill process
CPU
TLB
Lookup
Cache
Mem
Disk
PageTable
Lookup
(2) TLB Hit
  compute paddr, send to cache
Notes: TLB miss in hardware usually, but not always
PageTable stuff in software

## Slide 28: Takeaway
The TLB is a fast cache for address translations.
A TLB hit is fast, miss is slow.

## Slide 29: Next Goal
How do we keep TLB, PageTable, and Cache consistent?

## Slide 30: TLB Coherency
TLB Coherency: What can go wrong?
A: PageTable or PageDir contents change
  swapping/paging activity, new shared pages, …
A: Page Table Base Register changes
  context switch between processes
Notes: Fully transparent

## Slide 31: Translation Lookaside Buffers (TLBs)
When PTE changes, PDE changes, PTBR changes….
Full Transparency: TLB coherency in hardware
  Flush TLB whenever PTBR register changes [easy – why?]
  Invalidate entries whenever PTE or PDE changes [hard – why?]
TLB coherency in software
If TLB has a no-write policy…
  OS invalidates entry after OS modifies page tables
  OS flushes TLB whenever OS does context switch
Notes: process ID could just be the PTBR for the process

## Slide 32: TLB Parameters
TLB parameters (typical)
  very small (64 – 256 entries), so very fast
  fully associative, or at least set associative
  tiny block size: why?
Intel Nehalem TLB (example)
  128-entry L1 Instruction TLB, 4-way LRU
  64-entry L1 Data TLB, 4-way LRU
  512-entry L2 Unified TLB, 4-way LRU
Notes: Tiny block size because there is no spacial locality

## Slide 33: Takeaway
The TLB is a fast cache for address translations.
A TLB hit is fast, miss is slow.
TLB Coherency –
  in HW – flush TLB when PTBR changes (context switch) and invalidate entry when PTE or PDE changes (may need processID).
  In SW–OS invalidates TLB entry after change page tables or OS flushes TLB whenever OS does context switch

## Slide 34: Next Goal
Virtual Memory meets Caching
Virtually vs. physically addressed caches
Virtually vs. physically tagged caches

## Slide 35
Virtual Memory meets Caching
  Virtually vs. physically addressed caches
  Virtually vs. physically tagged caches

## Slide 36: Recall TLB in the Memory Hierarchy
CPU
TLB
Lookup
Cache
Mem
Disk
PageTable
Lookup
TLB is passing a physical address so we can load
from memory.
What if the data is in the cache?

## Slide 37: Virtually Addressed Caching
Q: Can we remove the TLB from the critical path?
A: Virtually-Addressed Caches
CPU
TLB
Lookup
Virtually
Addressed
Cache
Mem
Disk
PageTable
Lookup
Notes: A: have to flush entire cache on context switch
A:
Doing synonym updates requires significant hardware – essentially an associative lookup on the physical address tags to see if you have multiple hits

## Slide 38: Virtual vs. Physical Caches
CPU
Cache
SRAM
Memory
DRAM
addr
data
MMU
Cache
SRAM
MMU
CPU
Memory
DRAM
addr
data
Cache works on physical addresses
Cache works on virtual addresses
Q: What happens on context switch?
Q: What about virtual memory aliasing?
Q: So what’s wrong with physically addressed caches?
Notes: A1: Physically-addressed: nothing; Virtually-addressed: need to flush cache
A2: Physically-addressed: nothing; Virtually-addressed: problems

## Slide 39: Indexing vs. Tagging
Physically-Addressed Cache
  slow: requires TLB (and maybe PageTable) lookup first
Virtually-Indexed, Virtually Tagged Cache
  fast: start TLB lookup before cache lookup finishes
  PageTable changes (paging, context switch, etc.)
     need to purge stale cache lines (how?)
  Synonyms (two virtual mappings for one physical page)
     could end up in cache twice (very bad!)
Virtually-Indexed, Physically Tagged Cache
  ~fast: TLB lookup in parallel with cache lookup
  PageTable changes  no problem: phys. tag mismatch
  Synonyms  search and evict lines with same phys. tag
Virtually-Addressed Cache

## Slide 40: Typical Cache Setup
CPU
L2 Cache
SRAM
Memory
DRAM
addr
data
MMU
Typical L1: On-chip virtually addressed, physically tagged
Typical L2: On-chip physically addressed
Typical L3: On-chip …
L1 Cache
SRAM
TLB SRAM

## Slide 41: Design Decisions of Caches/TLBs/VM
Caches, Virtual Memory, & TLBs
Where can block be placed?
  Direct, n-way, fully associative
What block is replaced on miss?
  LRU, Random, LFU, …
How are writes handled?
  No-write (w/ or w/o automatic invalidation)
  Write-back (fast, block at time)
  Write-through (simple, reason about consistency)
Notes: Where?
Caches: direct/n-way/fa
VM: fa, but with a table of contents to eliminate searches
TLB: fa
Replacement?
varied
Writes?
Caches: usually write-back, or maybe write-through, or maybe no-write w/ invalidation
VM: write-back
TLB: usually no-write

## Slide 42: Summary of Caches/TLBs/VM
Caches, Virtual Memory, & TLBs
Where can block be placed?
  Caches: direct/n-way/fully associative (fa)
  VM: fa, but with a table of contents to eliminate searches
  TLB: fa
What block is replaced on miss?
  varied
How are writes handled?
  Caches: usually write-back, or maybe write-through, or maybe no-write w/ invalidation
  VM: write-back
  TLB: usually no-write
Notes: Where?
Caches: direct/n-way/fa
VM: fa, but with a table of contents to eliminate searches
TLB: fa
Replacement?
varied
Writes?
Caches: usually write-back, or maybe write-through, or maybe no-write w/ invalidation
VM: write-back
TLB: usually no-write

## Slide 43: Summary of Cache Design Parameters
 | L1 | Paged Memory | TLB
Size (blocks) | 1/4k to 4k | 16k to 1M | 64 to 4k
Size (kB) | 16 to 64 | 1M to 4G | 2 to 16
Block size (B) | 16-64 | 4k to 64k | 4-32
Miss rates | 2%-5% | 10-4 to 10-5% | 0.01% to 2%
Miss penalty | 10-25 | 10M-100M | 100-1000

## Slide 44
Role of the Operating System
Context switches, working set,
shared memory

## Slide 45: Next Goal
How many programs do you run at once?
How does the Operating System (OS) help?

## Slide 46: Role of the Operating System
The operating systems (OS) manages and multiplexes memory between process. It…
  Enables processes to (explicitly) increase memory:
    sbrk and (implicitly) decrease memory
  Enables sharing of physical memory:
    multiplexing memory via context switching, sharing memory, and paging
  Enables and limits the number of processes that can run simultaneously

## Slide 47: sbrk (more memory)
Suppose Firefox needs a new page of memory
(1) Invoke the Operating System
  void *sbrk(int nbytes);
(2) OS finds a free page of physical memory
  clear the page (fill with zeros)
  add a new entry to Firefox’s PageTable

## Slide 48: Context Switch (sharing CPU)
Suppose Firefox is idle, but Skype wants to run
(1) Firefox invokes the Operating System
  int sleep(int nseconds);
(2) OS saves Firefox’s registers, load Skype’s
  (more on this later)
(3) OS changes the CPU’s Page Table Base Register
  Cop0:ContextRegister / CR3:PDBR
(4) OS returns to Skype

## Slide 49: Shared Memory
Suppose Firefox and Skype want to share data
(1) OS finds a free page of physical memory
  clear the page (fill with zeros)
  add a new entry to Firefox’s PageTable
  add a new entry to Skype’s PageTable
    can be same or different vaddr
    can be same or different page permissions

## Slide 50: Multiplexing
Suppose Skype needs a new page of memory, but Firefox is hogging it all
(1) Invoke the Operating System
  void *sbrk(int nbytes);
(2) OS can’t find a free page of physical memory
  Pick a page from Firefox instead (or other process)
(3) If page table entry has dirty bit set…
  Copy the page contents to disk
(4) Mark Firefox’s page table entry as “on disk”
  Firefox will fault if it tries to access the page
(5) Give the newly freed physical page to Skype
  clear the page (fill with zeros)
  add a new entry to Skype’s PageTable

## Slide 51: Takeaway
The OS assists with the Virtual Memory abstraction
  sbrk
  Context switches
  Shared memory
  Multiplexing memory

## Slide 52
How can the OS optimize the use of physical memory?
What does the OS need to beware of?

## Slide 53: Paging Assumption 1
OS multiplexes physical memory among processes
  assumption # 1: processes use only a few pages at a time
  working set = set of process’s recently actively pages
# recent accesses
0x00000000
0x90000000
code
data
stack
memory
disk

## Slide 54: Thrashing (excessive paging)
Q: What if working set is too large?
Case 1: Single process using too many pages
Case 2: Too many processes
working set
mem
disk
swapped
P1
working set
mem
disk
swapped
ws
mem
disk
ws
ws
ws
ws
ws

## Slide 55: Thrashing
Thrashing b/c working set of process (or processes) greater than physical memory available
    Firefox steals page from Skype
    Skype steals page from Firefox
  I/O (disk activity) at 100% utilization
    But no useful work is getting done
Ideal: Size of disk, speed of memory (or cache)
Non-ideal: Speed of disk

## Slide 56: Paging Assumption 2
OS multiplexes physical memory among processes
  assumption # 2: recent accesses predict future accesses
  working set usually changes slowly over time
working set
time 

## Slide 57: More Thrashing
Q: What if working set changes rapidly or unpredictably?
A: Thrashing b/c recent accesses don’t predict future accesses
working set
time 

## Slide 58: Preventing Thrashing
How to prevent thrashing?
  User: Don’t run too many apps
  Process: efficient and predictable mem usage
  OS: Don’t over-commit memory, memory-aware scheduling policies, etc.

## Slide 59: Takeaway
The OS assists with the Virtual Memory abstraction
  sbrk
  Context switches
  Shared memory
  Multiplexing memory
  Working set
  Thrashing

## Slide 60: Virtual Memory Summary
All problems in computer science can be solved by another level of indirection.
Need a map to translate a “fake” virtual address (generated by CPU) to a “real” physical Address (in memory)
Virtual memory is implemented via a “Map”, a PageTage, that maps a vaddr (a virtual address) to a paddr (physical address):
paddr = PageTable[vaddr]
A page is constant size block of virtual memory. Often, the page size will be around 4kB to reduce the number of entries in a PageTable.
We can use the PageTable to set Read/Write/Execute permission on a per page basis. Can allocate memory on a per page basis. Need a valid bit, as well as Read/Write/Execute and other bits.
But, overhead due to PageTable is significant.

## Slide 61: Summary of Caches/TLBs/VM
Caches, Virtual Memory, & TLBs
Where can block be placed?
  Caches: direct/n-way/fully associative (fa)
  VM: fa, but with a table of contents to eliminate searches
  TLB: fa
What block is replaced on miss?
  varied
How are writes handled?
  Caches: usually write-back, or maybe write-through, or maybe no-write w/ invalidation
  VM: write-back
  TLB: usually no-write
Notes: Where?
Caches: direct/n-way/fa
VM: fa, but with a table of contents to eliminate searches
TLB: fa
Replacement?
varied
Writes?
Caches: usually write-back, or maybe write-through, or maybe no-write w/ invalidation
VM: write-back
TLB: usually no-write

## Slide 62: Summary of Cache Design Parameters
 | L1 | Paged Memory | TLB
Size (blocks) | 1/4k to 4k | 16k to 1M | 64 to 4k
Size (kB) | 16 to 64 | 1M to 4G | 2 to 16
Block size (B) | 16-64 | 4k to 64k | 4-32
Miss rates | 2%-5% | 10-4 to 10-5% | 0.01% to 2%
Miss penalty | 10-25 | 10M-100M | 100-1000