## Slide 1: Traps, Exceptions, System Calls, & Privileged Mode
Deniz ALTINBUKEN
CS 3410, Spring 2015
Computer Science
Cornell University
P&H Chapter 4.9, pages 445–452, appendix A.7

## Slide 2: Heartbleed Security Bug

## Slide 3: Heartbleed Security Bug
Heartbleed is a security bug disclosed in April 2014 in the open-source OpenSSL cryptography library, widely used to implement the Internet's Transport Layer Security (TLS) protocol.
“…worst vulnerability found since commercial traffic began to flow over the internet.” — Forbes; Apr 10, 2014
“17% (0.5 million) secure web servers vulnerable to bug.” — Netcraft Ltd.; Apr 8, 2014
Amazon, Akamai, GitHub, Wikipedia, etc. affected!

## Slide 4: Heartbleed Security Bug
How does it work?
  Keep-alive heartbeat lacked bounds checking!
  “Buffer over-read”
Send me this 5 letter word if you are alive: “Phone”
Phone
Send me this 1000 letter word if you are alive: “Phone”
Phone Alice passwd 123456 Bob passwd 654321 Server passwd …

## Slide 5: Heartbleed Security Bug
Heartbeat Protocol:
  Client sends buffer and the length of buffer
  Server writes buffer in memory
  Returns length of characters from memory
Server did not check length of buffer
Malloc/Free did not clear memory
Unauthenticated users can send a heartbeat
Server can return sensitive information present in memory!

## Slide 6: Takeaway
Worst Internet security vulnerability found
yet due systems practices 101 that we learn in CS3410, lack of bounds checking!
Lab 3: Similar bug/vulnerability due to “Buffer overflow”
  Browser implementation lacks bounds checking
  Overwrite return address in memory using a smart input!

## Slide 7: Outline for Today
How do we protect processes from one another?
  Skype should not crash Chrome.
How do we protect the operating system (OS) from other processes?
  Chrome should not crash the computer!
How does the CPU and OS (software) handle exceptional conditions?
  Division by 0, Page Fault, Syscall, etc.

## Slide 8: Outline for Today
How do we protect processes from one another?
  Skype should not crash Chrome.
How do we protect the operating system (OS) from other processes?
  Chrome should not crash the computer!
How does the CPU and OS (software) handle exceptional conditions?
  Division by 0, Page Fault, Syscall, etc.
Operating System
Privileged Mode
Traps, System calls, Exceptions, Interrupts

## Slide 9
Operating System

## Slide 10: Operating System
Manages all of the software and hardware on the computer.
Many processes running at the same time, requiring resources
  CPU, Memory, Storage, etc.
The Operating System multiplexes these resources amongst different processes, and isolates and protects processes from one another!

## Slide 11: Operating System
Operating System (OS) is a trusted mediator:
  Safe control transfer between processes
  Isolation (memory, registers) of processes
P1
P2
P3
P4
VM
filesystem
net
driver
driver
untrusted
disk
netw
card
MMU
CPU
trusted
software
hardware
OS

## Slide 12: Which statement is FALSE?
A) OS is always in the Hard Disk.
B) OS is always in Memory.
C) All processes can access the OS code.
D) OS provides a consistent API to be used by other processes.
E) OS manages the CPU, Memory, Devices, and Storage.

## Slide 13: Outline for Today
How do we protect processes from one another?
  Skype should not crash Chrome.
How do we protect the operating system (OS) from other processes?
  Chrome should not crash the computer!
How does the CPU and OS (software) handle exceptional conditions?
  Division by 0, Page Fault, Syscall, etc.
Operating System
Privileged Mode
Traps, System calls, Exceptions, Interrupts

## Slide 14
Privileged (Kernel) Mode
Notes: How do you ENFORCE this trusted abstraction?

## Slide 15: Privileged Mode
Only privileged (and trusted!) processes can access & change important things.
  Editing TLB, Page Tables, OS code, $sp, $fp…
If an untrusted process could change $sp, $fp, and $gp, OS would crash!

## Slide 16: Privileged Mode
How can we get the privileged mode to work?
Attempt #1:
Make privileged instructions and registers available only to “OS Code”!
  “OS Code” resides in memory at preset virtual address

## Slide 17: Privileged Mode
Would making privileged instructions and registers available only to “OS Code” work?
A) Will work great!
B) Will work, but performance will be slow!
C) Will not work because any process can jump into OS code
D) Will not work because process can access all registers
E) Whatever, I am bored!

## Slide 18: Privileged Mode
How can we get the privileged mode to work?
Attempt #1:
Make privileged instructions and registers available only to “OS Code”
  “OS Code” resides in memory at preset virtual address
Does not work:
  Process can still JAL into middle of OS functions
  Process can still access and change memory, page tables, …

## Slide 19: Privileged Mode
How can we get the privileged mode to work?
Attempt #2:
CPU Mode Bit in Privilege Level Status Register
Mode 0 = untrusted = user mode
  “Privileged” instructions and registers are disabled by CPU
Mode 1 = trusted = kernel mode
  All instructions and registers are enabled

## Slide 20: Privileged Mode
How can we get the privileged mode to work?
Boot sequence:
  load first sector of disk (containing OS code) to predetermined address in memory
  Mode  1; PC  predetermined address
OS takes over…
  initializes devices, MMU, timers, etc.
  loads programs from disk, sets up page tables, etc.
  Mode  0; PC  program entry point

## Slide 21: Privileged Mode
If an untrusted process does not have privileges to use system resources, how can it
  Use the screen to print?
  Send message on the network?
  Allocate pages?
  Schedule processes?
System Calls

## Slide 22: System Calls
System call: Not just a function call
  Don’t let process ram jump just anywhere in OS code
  OS can’t trust process’ registers (sp, fp, gp, etc.)
SYSCALL instruction: safe transfer of control to OS
  Mode  0; Cause  syscall; PC  exception vector
MIPS system call convention:
  Exception handler saves temp regs, saves ra, …
  but: $v0 = system call number, which specifies the operation the application is requesting

## Slide 23
User Application
0xfffffffc
0x00000000
top
bottom
0x7ffffffc
0x80000000
0x10000000
0x00400000
system reserved
stack
system reserved
code (text)
static data
dynamic data (heap)
.data
.text
User Mode
Privileged (Kernel) Mode
System Call Interface
printf()
printf.c
Implementation
of printf() syscall!
SYSCALL!

## Slide 24: System Calls
System call examples:
putc(): Print character to screen
  Need to multiplex screen between competing processes
send(): Send a packet on the network
  Need to manipulate the internals of a device
sbrk(): Allocate a page
  Needs to update page tables & MMU
sleep(): put current prog to sleep, wake other
  Need to update page table base register

## Slide 25: Invoking System Calls
int getc() {
asm("addiu $v0, $0, 4");
asm("syscall");
}
char *gets(char *buf) {
while (...) {
buf[i] = getc();
}
}
Notes: Inline assembly
4 is getc syscall name!

## Slide 26: Libraries and Wrappers
Compilers do not emit SYSCALL instructions
  Compiler doesn’t know OS interface
Libraries implement standard API from system API
libc (standard C library):
  getc()  syscall
  sbrk()  syscall
  write()  syscall
  gets()  getc()
  printf()  write()
  malloc()  sbrk()
  …

## Slide 27: Where does the OS live?
In its own address space?
  But then syscall would have to switch to a different address space
  Also harder to deal with syscall arguments passed as pointers
So in the same address space as process
  Use protection bits to prevent user code from writing kernel
  Higher part of virtual memory, lower part of physical memory

## Slide 28: Anatomy of a Process
system reserved
(stack grows down)
(heap grows up)
text
reserved
(static) data
(.stack)
.data
.text
0xfffffffc
0x00000000
top
bottom
0x7ffffffc
0x80000000
0x10000000
0x00400000
system reserved
stack
system reserved
code (text)
static data
dynamic data (heap)
.data
.text

## Slide 29: Full System Layout
Typically all kernel text, most data
  At same virtual address in every address space
  Map kernel in contiguous physical memory when boot loader puts kernel into physical memory
The OS is omnipresent and steps in where necessary to aid application execution
  Typically resides in high memory
When an application needs to perform a privileged operation, it needs to invoke the OS
Virtual Memory
0xfffffffc
0x00000000
0x7ffffffc
0x80000000
0x10000000
0x00400000
stack
system reserved
code (text)
static data
dynamic data (heap)
OS Heap
OS Data
OS Stack
OS Text

## Slide 30: Full System Layout
Virtual Memory
OS Text
OS Data
OS Heap
OS Stack
Physical Memory
0xfffffffc
0x00000000
0x7ffffffc
0x80000000
0x10000000
0x00400000
stack
system reserved
code (text)
static data
dynamic data (heap)
OS Heap
OS Data
OS Stack
OS Text
0x00...00

## Slide 31: SYSCALL instruction
SYSCALL instruction does an atomic jump to a controlled location (i.e. MIPS 0x8000 0180)
  Switches the sp to the kernel stack
  Saves the old (user) SP value
  Saves the old (user) PC value (= return address)
  Saves the old privilege mode
  Sets the new privilege mode to 1
  Sets the new PC to the kernel syscall handler

## Slide 32: SYSCALL instruction
Kernel system call handler carries out the desired system call
  Saves callee-save registers
  Examines the syscall number
  Checks arguments for sanity
  Performs operation
  Stores result in v0
  Restores callee-save registers
  Performs a “return from syscall” (ERET) instruction, which restores the privilege mode, SP and PC

## Slide 33: Takeaway
It is necessary to have a privileged (kernel) mode to enable the Operating System (OS):
  provides isolation between processes
  protects shared resources
  provides safe control transfer

## Slide 34: Outline for Today
How do we protect processes from one another?
  Skype should not crash Chrome.
How do we protect the operating system (OS) from other processes?
  Chrome should not crash the computer!
How does the CPU and OS (software) handle exceptional conditions?
  Division by 0, Page Fault, Syscall, etc.
Operating System
Privileged Mode
Traps, System calls, Exceptions, Interrupts

## Slide 35: Terminology
Trap: Any kind of a control transfer to the OS
Syscall: Synchronous and planned, process-to-kernel transfer
  SYSCALL instruction in MIPS (various on x86)
Exception: Synchronous but unplanned, process-to-kernel transfer
  exceptional events: div by zero, page fault, page protection err, …
Interrupt: Asynchronous, device-initiated transfer
  e.g. Network packet arrived, keyboard event, timer ticks

## Slide 36: Exceptions
Exceptions are any unexpected change in control flow.
Interrupt -> cause of control flow change external
Exception -> cause of control flow change internal
  Exception: Divide by 0, overflow
  Exception: Bad memory address
  Exception: Page fault
  Interrupt: I/O interrupt (e.g. keyboard stroke)
We need both HW and SW to help resolve exceptions
  Exceptions are at the hardware/software boundary

## Slide 37: Hardware/Software Boundary
Hardware support for exceptions
  Exception program counter (EPC)
    A 32-bit register to hold the addr of the affected instruction.
    Syscall case: Address of SYSCALL
  Cause register
    A register to hold the cause of the exception.
    Syscall case: 8, Sys
  Special instructions to load TLB
    Only do-able by kernel
Precise and imprecise exceptions
  In pipelined architecture
    Have to correctly identify PC of exception
    MIPS and modern processors support this

## Slide 38: Exceptions
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard
Stack, Data, Code
Stored in Memory
$0 (zero)
$1 ($at)
$29 ($sp)
$31 ($ra)
Code Stored in Memory
(also, data and stack)
EPC
Cause

## Slide 39: Hardware/Software Boundary
Precise exceptions: Hardware guarantees
  (similar to a branch)
  Previous instructions complete
  Later instructions are flushed
  EPC and cause register are set
  Jump to prearranged address in OS
  When you come back, restart instruction
  Disable exceptions while responding to one
    Otherwise can overwrite EPC and cause

## Slide 40: Hardware/Software Boundary
What else requires both Hardware and Software?
A) Virtual to Physical Address Translation
B) Branching and Jumping
C) Clearing the contents of a register
D) Pipelining instructions in the CPU
E) What are we even talking about?

## Slide 41: Hardware/Software Boundary
Virtual to physical address translation!
Hardware
CPU has a concept of operating in physical or virtual mode.
CPU helps manage the TLB.
CPU raises page faults.
CPU keeps Page Table Base Register (PTBR) and ProcessID
Software
OS manages Page Table storage
OS handles Page Faults
OS updates Dirty and Reference bits in the Page Tables
OS keeps TLB valid on context switch:
  Flush TLB when new process runs (x86)
  Store process id (MIPS)

## Slide 42: Summary
Trap
  Any kind of a control transfer to the OS
Syscall
  Synchronous, process-initiated control transfer from user to the OS to obtain service from the OS
  e.g. SYSCALL
Exception
  Synchronous, process-initiated control transfer from user to the OS in response to an exceptional event
  e.g. Divide by zero, TLB miss, Page fault
Interrupt
  Asynchronous, device-initiated control transfer from user to the OS
  e.g. Network packet, I/O complete

## Slide 43
What is the difference between traps, exceptions, interrupts, and system calls?

## Slide 44: Interrupts & Exceptions
Hardware
  CPU saves PC of exception instruction (EPC)
  CPU Saves cause of the interrupt/privilege (Cause register)
  Switches the sp to the kernel stack
  Saves the old (user) SP value
  Saves the old (user) PC value
  Saves the old privilege mode
  Sets the new privilege mode to 1
  Sets the new PC to the kernel interrupt/exception handler

## Slide 45: Interrupts & Exceptions
Software
Kernel interrupt/exception handler handles the event
  Saves all registers
  Examines the cause
  Performs operation required
  Restores all registers
  Performs a “return from interrupt” instruction, which restores the privilege mode, SP and PC

## Slide 46: Example: Clock Interrupt
Example: Clock Interrupt*
  Every N cycles, CPU causes exception with Cause = CLOCK_TICK
  OS can select N to get e.g. 1000 TICKs per second
.ktext 0x8000 0180
# (step 1) save *everything* but $k0, $k1 to 0xB0000000
# (step 2) set up a usable OS context
# (step 3) examine Cause register, take action
if (Cause == PAGE_FAULT) handle_pfault(BadVaddr)
else if (Cause == SYSCALL) dispatch_syscall($v0)
else if (Cause == CLOCK_TICK) schedule()
# (step 4) restore registers and return to where process left off
* not the CPU clock, but a programmable timer clock

## Slide 47: Scheduler
struct regs context[];
int ptbr[];
schedule() {
i = current_process;
j = pick_some_process();
if (i != j) {
current_process = j;
memcpy(context[i], 0xB0000000);
memcpy(0xB0000000, context[j]);
asm(“mtc0 Context, ptbr[j]”);
}
}

## Slide 48: Syscall vs. Exception vs. Interrupt
Same mechanisms, but…
Syscall saves and restores much less state
Others save and restore full processor state
Interrupt arrival is unrelated to user code

## Slide 49: Takeaway
Traps are any transfer of control to the OS.
Exceptions are any unexpected change in control flow.
Precise exceptions are necessary to identify the exceptional instructions, cause of exception, and where to continue execution.
We need help of both hardware and software (e.g. OS) to resolve exceptions.

## Slide 50: Takeaway
To handle any exception or interrupt:
OS analyzes the Cause register
OS vectors into the appropriate exception handler.
OS kernel handles the exception
Returns control to the same process
  Possibly kills the current process
  Possibly schedules another process