## Slide 1: Multicore and Parallelism
Prof. Hakim Weatherspoon
CS 3410, Spring 2015
Computer Science
Cornell University
P & H Chapter 4.10, 1.7, 1.8, 5.10, 6

## Slide 2: Announcements
HW2 Review Sessions!
  Saturday, April 18th, Hollister B14@7pm
  Tuesday, April 21st, Hollister B14@7pm
Lab3 is due yesterday!
  Wednesday, April 15th
PA3 started this week!
  The Lord of the Cache!
  Due Friday, April 24th

## Slide 3: Announcements
HW2-P5 (Pre-Lab4) due next week!
  Monday, April 20th
  Don’t forget to submit on CMS!
  Designed for you to look over the code and understand virtual memory before coming to Lab 4.

## Slide 4: Announcements
Prelim 2 is on April 30th at 7 PM at Statler Hall!
If you have a conflict e-mail me:
deniz@cs.cornell.edu

## Slide 5: Announcements
Next three weeks
  Week 12 (Apr 21): Lab4 due in-class, Proj3 due Fri, HW2 due Sat
  Week 13 (Apr 28): Proj4 release, Prelim2
  Week 14 (May 5): Proj3 tournament Mon, Proj4 design doc due
Final Project for class
  Week 15 (May 12): Proj4 due Wed

## Slide 6: Today
Many ways to improve performance
Instruction Level Parallelism
Multicore
Performance in multicore
Next 2 lectures: synchronization

## Slide 7: xkcd/619

## Slide 8: Pitfall: Amdahl’s Law
affected execution time
amount of improvement
+ execution time unaffected
Execution time after improvement =
Notes: Amdahl’s Law

## Slide 9: Pitfall: Amdahl’s Law
Improving an aspect of a computer and expecting a proportional improvement in overall performance
Example: multiply accounts for 80s out of 100s
Notes: Clicker question

## Slide 10: Scaling Example
Workload: sum of 10 scalars, and 10 × 10 matrix sum
  Speed up from 10 to 100 processors?
Single processor: Time = (10 + 100) × tadd
10 processors
100 processors
.
Notes: Pair up question

## Slide 11: Scaling Example
What if matrix size is 100 × 100?
Single processor: Time = (10 + 10000) × tadd
10 processors
100 processors
.

## Slide 12: Goals for Today
How to improve System Performance?
  Instruction Level Parallelism (ILP)
  Multicore
    Increase clock frequency vs multicore
  Beware of Amdahls Law
Next time:
  Concurrency, programming, and synchronization

## Slide 13: Problem Statement
Q: How to improve system performance?
 Increase CPU clock rate?
 But I/O speeds are limited
Disk, Memory, Networks, etc.
Recall: Amdahl’s Law
Solution: Parallelism

## Slide 14: Instruction-Level Parallelism (ILP)
Pipelining: execute multiple instructions in parallel
Q: How to get more instruction level parallelism?
A: Deeper pipeline
    E.g. 250MHz 1-stage; 500Mhz 2-stage; 1GHz 4-stage; 4GHz 16-stage
Pipeline depth limited by…
    max clock speed (less work per stage  shorter clock cycle)
    min unit of work
    dependencies, hazards / forwarding logic
Notes: Draw pictures: 250MHz 1-stage; 500Mhz 2-stage; 1GHz 4-stage; 4GHz 16-stage

## Slide 15: Instruction-Level Parallelism (ILP)
Pipelining: execute multiple instructions in parallel
Q: How to get more instruction level parallelism?
Notes: Draw picture; 4 stage, 4-way * 4GHz = 16B inst/cycles Next: Static issue

## Slide 16: Static Multiple Issue
Static Multiple Issue
a.k.a. Very Long Instruction Word (VLIW)
Compiler groups instructions to be issued together
  Packages them into “issue slots”
Q: How does HW detect and resolve hazards?
Notes: show program, decode stage
Ideal CPI = 0.5

## Slide 17: MIPS with Static Dual Issue
Two-issue packets
  One ALU/branch instruction
  One load/store instruction
  64-bit aligned
    ALU/branch, then load/store
    Pad an unused instruction with nop
Address | Instruction type | Pipeline Stages |  |  |  |  |  | 
n | ALU/branch | IF | ID | EX | MEM | WB |  | 
n + 4 | Load/store | IF | ID | EX | MEM | WB |  | 
n + 8 | ALU/branch |  | IF | ID | EX | MEM | WB | 
n + 12 | Load/store |  | IF | ID | EX | MEM | WB | 
n + 16 | ALU/branch |  |  | IF | ID | EX | MEM | WB
n + 20 | Load/store |  |  | IF | ID | EX | MEM | WB

## Slide 18: Scheduling Example
Loop: lw $t0, 0($s1) # $t0=array element addu $t0, $t0, $s2 # add scalar in $s2 sw $t0, 0($s1) # store result addi $s1, $s1,–4 # decrement pointer bne $s1, $zero, Loop # branch $s1!=0
Schedule this for dual-issue MIPS
 | ALU/branch | Load/store | cycle

## Slide 19: Scheduling Example
Compiler scheduling for dual-issue MIPS…
Loop: lw $t0, 0($s1) # $t0 = A[i]
lw $t1, 4($s1) # $t1 = A[i+1] addu $t0, $t0, $s2 # add $s2 addu $t1, $t1, $s2 # add $s2 sw $t0, 0($s1) # store A[i] sw $t1, 4($s1) # store A[i+1] addi $s1, $s1, +8 # increment pointer bne $s1, $s3, TOP # continue if $s1!=end
ALU/branch slot Load/store slot cycle
Loop: nop lw $t0, 0($s1) 1
nop lw $t1, 4($s1) 2
addu $t0, $t0, $s2 nop 3
addu $t1, $t1, $s2 sw $t0, 0($s1) 4
addi $s1, $s1, +8 sw $t1, 4($s1) 5
bne $s1, $s3, TOP nop 6
Notes:   assume 1 delay slot for loads
  can move addi earlier
  CPI = 6 cycles / 8 instructions = 0.75
  CPI = 5 cycles / 8 instructions = 0.625

## Slide 20: Scheduling Example
Compiler scheduling for dual-issue MIPS…
Loop: lw $t0, 0($s1) # $t0 = A[i]
lw $t1, 4($s1) # $t1 = A[i+1] addu $t0, $t0, $s2 # add $s2 addu $t1, $t1, $s2 # add $s2 sw $t0, 0($s1) # store A[i] sw $t1, 4($s1) # store A[i+1] addi $s1, $s1, +8 # increment pointer bne $s1, $s3, TOP # continue if $s1!=end
ALU/branch slot Load/store slot cycle
Loop: nop lw $t0, 0($s1) 1
addi $s1, $s1, +8 lw $t1, 4($s1) 2
addu $t0, $t0, $s2 nop 3
addu $t1, $t1, $s2 sw $t0, -8($s1) 4
bne $s1, $s3, Loop sw $t1, -4($s1) 5
Notes:   assume 1 delay slot for loads
  can move addi earlier
  CPI = 6 cycles / 8 instructions = 0.75
  CPI = 5 cycles / 8 instructions = 0.625

## Slide 21: Limits of Static Scheduling
Compiler scheduling for dual-issue MIPS…
lw $t0, 0($s1) # load A
addi $t0, $t0, +1 # increment A
sw $t0, 0($s1) # store A
lw $t0, 0($s2) # load B
addi $t0, $t0, +1 # increment B
sw $t0, 0($s2) # store B
ALU/branch slot Load/store slot cycle
nop lw $t0, 0($s1) 1
nop nop 2
addi $t0, $t0, +1 nop 3
nop sw $t0, 0($s1) 4
nop lw $t0, 0($s2) 5
nop nop 6
addi $t0, $t0, +1 nop 7
nop sw $t0, 0($s2) 8
Notes: Rename registers, move load B up, eliminate delay slot
But! s1 and s2 might be equal => Aliasing!

## Slide 22: Limits of Static Scheduling
Compiler scheduling for dual-issue MIPS…
lw $t0, 0($s1) # load A
addi $t0, $t0, +1 # increment A
sw $t0, 0($s1) # store A
lw $t1, 0($s2) # load B
addi $t1, $t1, +1 # increment B
sw $t0, 0($s2) # store B
ALU/branch slot Load/store slot cycle
nop lw $t0, 0($s1) 1
nop lw $t1, 0($s2) 2
addi $t0, $t0, +1 nop 3
addi $t1, $t1, +1 sw $t0, 0($s1) 4
nop sw $t1, 0($s2) 5
Notes: Rename registers, move load B up, eliminate delay slot
But! s1 and s2 might be equal => Aliasing!

## Slide 23: Dynamic Multiple Issue
Dynamic Multiple Issue
a.k.a. SuperScalar Processor (c.f. Intel)
  CPU examines instruction stream and chooses multiple instructions to issue each cycle
  Compiler can help by reordering instructions….
  … but CPU is responsible for resolving hazards
Even better: Speculation/Out-of-order Execution
  Execute instructions as early as possible
  Aggressive register renaming
  Guess results of branches, loads, etc.
  Roll back if guesses were wrong
  Don’t commit results until all previous insts. are retired

## Slide 24: Dynamic Multiple Issue

## Slide 25: Does Multiple Issue Work?
Q: Does multiple issue / ILP work?

## Slide 26: Power Efficiency
Q: Does multiple issue / ILP cost much?

## Slide 27: Moore’s Law
486
286
8088
8080
8008
4004
386
Pentium
Atom
P4
Itanium 2
K8
K10
Dual-core Itanium 2
Notes: NVIDIA GF100 has 3B transistors

## Slide 28: Why Multicore?
Moore’s law
  A law about transistors
  Smaller means more transistors per die
  And smaller means faster too
But: Power consumption growing too…

## Slide 29: Power Limits
Hot Plate
Rocket Nozzle
Nuclear Reactor
Surface of Sun
Xeon
Notes: Intel Westmere: 32 nm = 0.032u, 130W / 240mm^2 = 54 W/cm^2

## Slide 30: Power Wall
Power = capacitance * voltage2 * frequency
In practice: Power ~ voltage3
Reducing voltage helps (a lot)
... so does reducing clock speed
Better cooling helps
The power wall
  We can’t reduce voltage further
  We can’t remove more heat

## Slide 31: Why Multicore?
Power
1.0x
1.0x
Performance
Single-Core
Power
1.2x
1.7x
Performance
Single-Core Overclocked +20%
Power
0.8x
0.51x
Performance
Single-Core
Underclocked -20%
1.6x
1.02x
Dual-Core
Underclocked -20%

## Slide 32: Inside the Processor
AMD Barcelona Quad-Core: 4 processor cores

## Slide 33: Inside the Processor
Intel Nehalem Hex-Core

## Slide 34: Hyperthreading
Multi-Core vs. Multi-Issue
Programs:
Num. Pipelines:
Pipeline Width:
.
vs. HT
Notes: HT = MultiIssue + extra PCs and registers – dependency logic
HT = MultiCore – redundant functional units + hazard avoidance

## Slide 35: Example: All of the above
Notes: MultiCore: 8 processors dies * 8 cores per processor die
Hyperthreading: 2 HT per core
Dynamic Multi-Issue: 4 issue
Pipeline: 16 stages

## Slide 36: Parallel Programming
Q: So lets just all use multicore from now on!
A: Software must be written as parallel program
Multicore difficulties
  Partitioning work
  Coordination & synchronization
  Communications overhead
  Balancing load over cores
  How do you write parallel programs?
    ... without knowing exact underlying architecture?
Notes: Or hyperthreads

## Slide 37: Work Partitioning
Partition work so all cores have something to do

## Slide 38: Load Balancing
Load Balancing
Need to partition so all cores are actually working

## Slide 39: Amdahl’s Law
If tasks have a serial part and a parallel part…
Example:
step 1: divide input data into n pieces
step 2: do work on each piece
step 3: combine all results
Recall: Amdahl’s Law
As number of cores increases …
  time to execute parallel part?
  time to execute serial part?
  Serial part eventually dominates
goes to zero
Remains the same

## Slide 40: Amdahl’s Law
Notes: Underclocking messes up the ratios completely. Work through a 8x slowdown example.

## Slide 41: Parallel Programming
Q: So lets just all use multicore from now on!
Multicore difficulties
  Partitioning work
  Coordination & synchronization
  Communications overhead
  Balancing load over cores
  How do you write parallel programs?
    ... without knowing exact underlying architecture?
Notes: Most is software, but hardware can help:
- communications (fast core-to-core interconnect)
- coordination and synchronization primitives (next time)