## Slide 1: Multicore, Parallelism, and Synchronization
Hakim Weatherspoon
CS 3410, Spring 2015
Computer Science
Cornell University
P&H Chapter 2.11, 5.10, and 6.5

## Slide 2: Announcements
HW2 Review Sessions!
  TODAY, Tue, April 21st, Hollister B14@7pm
HW2-P5 (Pre-Lab4) was due yesterday!
PA3 due Friday, April 24th
  The Lord of the Cache!
  Tournament, Monday, May 4, 5-7pm

## Slide 3: Announcements
Prelim 2 is next week on April 30th at 7 PM at Statler Hall!
If you have a conflict e-mail me:
deniz@cs.cornell.edu

## Slide 4: Announcements
Next three weeks
  Week 12 (Apr 21): Lab4 due in-class, Proj3 due Fri, HW2 due Sat
  Week 13 (Apr 28): Proj4 release, Prelim2
  Week 14 (May 5): Proj3 tournament Mon, Proj4 design doc due
Final Project for class
  Week 15 (May 12): Proj4 due Wed

## Slide 5: Big Picture: Parallelism and Synchronization
How do I take advantage of parallelism?
How do I write (correct) parallel programs?
What primitives do I need to implement correct parallel programs?

## Slide 6: Topics: Goals for Today
Understand Cache Coherency
Synchronizing parallel programs
  Atomic Instructions
  HW support for synchronization
How to write parallel programs
  Threads and processes
  Critical sections, race conditions, and mutexes

## Slide 7: Parallelism and Synchronization
Cache Coherency Problem: What happens when to two or more processors cache shared data?

## Slide 8: Parallelism and Synchronization
Cache Coherency Problem: What happens when to two or more processors cache shared data?
i.e. the view of memory held by two different processors is through their individual caches.
As a result, processors can see different (incoherent) values to the same memory location.

## Slide 9: Parallelism and Synchronization

## Slide 10: Parallelism and Synchronization
Each processor core has its own L1 cache

## Slide 11: Parallelism and Synchronization
Each processor core has its own L1 cache

## Slide 12: Parallelism and Synchronization
Each processor core has its own L1 cache
Core0
Cache
Memory
I/O
Interconnect
Core1
Cache
Core3
Cache
Core2
Cache

## Slide 13: Shared Memory Multiprocessors
Shared Memory Multiprocessor (SMP)
  Typical (today): 2 – 4 processor dies, 2 – 8 cores each
  HW provides single physical address space for all processors
  Assume physical addresses (ignore virtual memory)
  Assume uniform memory access (ignore NUMA)
Core0
Cache
Memory
I/O
Interconnect
Core1
Cache
Core3
Cache
Core2
Cache
Notes: How do they share data? How do they coordinate? How do they scale?

## Slide 14: Shared Memory Multiprocessors
Shared Memory Multiprocessor (SMP)
  Typical (today): 2 – 4 processor dies, 2 – 8 cores each
  HW provides single physical address space for all processors
  Assume physical addresses (ignore virtual memory)
  Assume uniform memory access (ignore NUMA)
...
Core0
Cache
Memory
I/O
Interconnect
Core1
Cache
CoreN
Cache
...
...
Notes: How do they share data? How do they coordinate? How do they scale?

## Slide 15: Cache Coherency Problem
...
Core0
Cache
Memory
I/O
Interconnect
Core1
Cache
CoreN
Cache
...
...
Thread A (on Core0) Thread B (on Core1) for(int i = 0, i < 5; i++) { for(int j = 0; j < 5; j++) { x = x + 1; x = x + 1; } }
What will the value of x be after both loops finish?
Notes: How do they share data? How do they coordinate? How do they scale?

## Slide 16: Cache Coherence Problem
Time step | Event | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  | 0
Suppose two CPU cores share a physical address space
  Write-through caches
...
Core0
Cache
Memory
I/O
Interconnect
Core1
Cache
CoreN
Cache
...
...

## Slide 17: Two issues
Coherence
What values can be returned by a read
Consistency
When a written value will be returned by a read

## Slide 18: Coherence Defined
Informal: Reads return most recently written value
Formal: For concurrent processes P1 and P2
  P writes X before P reads X (with no intervening writes)  read returns written value
    (preserve program order)
  P1 writes X before P2 reads X  read returns written value
    (coherent memory view, can’t read old value forever)
  P1 writes X and P2 writes X  all processors see writes in the same order
    all see the same final value for X
    Aka write serialization
    (else PA can see P2’s write before P1’s and PB can see the opposite; their final understanding of state is wrong)
Notes: second case: for some definition of “before”
third case: see relativity
complication: clocks are not synchronized across cores
1 light nanosecond = 30cm, so 3GHz can do 1 instruction per 10cm

## Slide 19: Cache Coherence Protocols
Operations performed by caches in multiprocessors to ensure coherence
  Migration of data to local caches
    Reduces bandwidth for shared memory
  Replication of read-shared data
    Reduces contention for access
Snooping protocols
  Each cache monitors bus reads/writes

## Slide 20: Snooping
Snooping for Hardware Cache Coherence
  All caches monitor bus and all other caches
  Bus read: respond if you have dirty data
  Bus write: update/invalidate your copy of data
Snoop
Snoop
Snoop
...
Core0
Cache
Memory
I/O
Interconnect
...
...
Snoop
Core1
Cache
Snoop
CoreN
Cache
Snoop
Notes: In reality: very complicated, lots of corner cases

## Slide 21: Invalidating Snooping Protocols
Cache gets exclusive access to a block when it is to be written
  Broadcasts an invalidate message on the bus
  Subsequent read in another cache misses
    Owning cache supplies updated value
Time Step | CPU activity | Bus activity | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  |  | 0
1 | CPU A reads X |  |  |  | 
2 | CPU B reads X |  |  |  | 
3 | CPU A writes 1 to X |  |  |  | 
4 | CPU B read X |  |  |  | 

## Slide 22: Writing
Write-back policies for bandwidth
Write-invalidate coherence policy
  First invalidate all other copies of data
  Then write it in cache line
  Anybody else can read it
Permits one writer, multiple readers
In reality: many coherence protocols
  Snooping doesn’t scale
  Directory-based protocols
    Caches and memory record sharing status of blocks in a directory

## Slide 23: Takeaway: Summary of cache coherence
Informally, Cache Coherency requires that reads return most recently written value
Cache coherence hard problem
Snooping protocols are one approach

## Slide 24: Next Goal: Synchronization
Is cache coherency sufficient?
i.e. Is cache coherency (what values are read) sufficient to maintain consistency (when a written value will be returned to a read). Both coherency and consistency are required to maintain consistency in shared memory programs.

## Slide 25: Is Cache Coherency Sufficient?
...
Core0
Cache
Memory
I/O
Interconnect
Core1
Cache
CoreN
Cache
...
...
Thread A (on Core0) Thread B (on Core1) for(int i = 0, i < 5; i++) { for(int j = 0; j < 5; j++) { LW $t0, addr(x) LW $t0, addr(x)
ADDIU $t0, $t0, 1 ADDIU $t0, $t0, 1
SW $t0, addr(x) SW $t0, addr(x) } }
Very expensive and difficult to maintain consistency
Notes: Is cache coherence enough? Maybe?
read (1) 40 read (3) 40
Inc (2) 41 inc (4) 41
Write (5) 41 write (6) 41
second case: for some definition of “before”
third case: see relativity
complication: clocks are not synchronized across cores
1 light nanosecond = 30cm, so 3GHz can do 1 instruction per 10cm

## Slide 26: Synchronization
  Threads
  Critical sections, race conditions, and mutexes
  Atomic Instructions
    HW support for synchronization
    Using sync primitives to build concurrency-safe data structures
  Example: thread-safe data structures
  Language level synchronization
  Threads and processes

## Slide 27: Programming with Threads
Need it to exploit multiple processing units
…to parallelize for multicore
…to write servers that handle many clients
Problem: hard even for experienced programmers
  Behavior can depend on subtle timing differences
  Bugs may be impossible to reproduce
Needed: synchronization of threads

## Slide 28: Programming with threads
Within a thread: execution is sequential
Between threads?
  No ordering or timing guarantees
  Might even run on different cores at the same time
Problem: hard to program, hard to reason about
  Behavior can depend on subtle timing differences
  Bugs may be impossible to reproduce
Cache coherency is not sufficient…
Need explicit synchronization to make sense of concurrency!

## Slide 29: Programming with Threads
Concurrency poses challenges for:
Correctness
  Threads accessing shared memory should not interfere with each other
Liveness
  Threads should not get stuck, should make forward progress
Efficiency
  Program should make good use of available computing resources (e.g., processors).
Fairness
  Resources apportioned fairly between threads

## Slide 30: Example: Multi-Threaded Program
Apache web server
void main() { setup();
while (c = accept_connection()) {
req = read_request(c);
hits[req]++; send_response(c, req);
}
cleanup();
}
Notes: Use fork
Use threads

## Slide 31: Example: web server
Each client request handled by a separate thread (in parallel)
  Some shared state: hit counter, ...
(look familiar?)
Timing-dependent failure  race condition
  hard to reproduce  hard to debug
Thread 52
...
hits = hits + 1;
...
Thread 205
...
hits = hits + 1;
...
Thread 52
read hits
addiu
write hits
Thread 205
read hits
addiu
write hits
Notes: What happens when two threads execute concurrently?
sequential with threads
between threads is unsynchronized

## Slide 32: Two threads, one counter
Possible result: lost update!
Timing-dependent failure  race condition
  Very hard to reproduce  Difficult to debug
ADDIU/SW: hits = 0 + 1
LW (0)
ADDIU/SW: hits = 0 + 1
LW (0)
T1
T2
hits = 1
hits = 0
time

## Slide 33: Race conditions
Def: timing-dependent error involving access to shared state
Whether a race condition happens depends on
  how threads scheduled
  i.e. who wins “races” to instruction that updates state vs. instruction that accesses state
Challenges about Race conditions
  Races are intermittent, may occur rarely
  Timing dependent = small changes can hide bug
A program is correct only if all possible schedules are safe
  Number of possible schedule permutations is huge
  Need to imagine an adversary who switches contexts at the worst possible time

## Slide 34: Critical sections
What if we can designate parts of the execution as critical sections
  Rule: only one thread can be “inside” a critical section
Thread 52
read hits
addi
write hits
Thread 205
read hits
addi
write hits
Thread 52
CSEnter()
read hits
addi
write hits
CSExit()
Thread 205
CSEnter()
read hits
addi
write hits
CSExit()
Notes: Show picture

## Slide 35: Critical Sections
To eliminate races: use critical sections that only one thread can be in
  Contending threads must wait to enter
CSEnter();
  Critical section
CSExit();
T1
T2
time
CSEnter();
  # wait
  # wait
  Critical section
CSExit();
T1
T2

## Slide 36: Mutexes
Q: How to implement critical sections in code?
A: Lots of approaches….
Mutual Exclusion Lock (mutex)
lock(m): wait till it becomes free, then lock it
unlock(m): unlock it
safe_increment() {
pthread_mutex_lock(&m);
hits = hits + 1;
pthread_mutex_unlock(&m);
}

## Slide 37: Mutexes
Only one thread can hold a given mutex at a time
Acquire (lock) mutex on entry to critical section
  Or block if another thread already holds it
Release (unlock) mutex on exit
  Allow one waiting thread (if any) to acquire & proceed
pthread_mutex_lock(&m);
  hits = hits+1;
pthread_mutex_unlock(&m);
T1
T2
pthread_mutex_lock(&m);
# wait
# wait
  hits = hits+1;
pthread_mutex_unlock(&m);
pthread_mutex_init(&m);

## Slide 38: Next Goal
How to implement mutex locks?
What are the hardware primitives?
Then, use these mutex locks to implement critical sections, and use critical sections to write parallel safe programs

## Slide 39: Synchronization
Synchronization requires hardware support
  Atomic read/write memory operation
  No other access to the location allowed between the read and write
  Could be a single instruction
    E.g., atomic swap of register ↔ memory (e.g. ATS, BTS; x86)
  Or an atomic pair of instructions (e.g. LL and SC; MIPS)

## Slide 41: Synchronization in MIPS
Load linked: LL rt, offset(rs)
Store conditional: SC rt, offset(rs)
  Succeeds if location not changed since the LL
    Returns 1 in rt
  Fails if location is changed
    Returns 0 in rt
Any time a processor intervenes and modifies the value in memory between the LL and SC instruction, the SC returns 0 in $t0, causing the code to try again.
i.e. use this value 0 in $t0 to try again.

## Slide 42: Synchronization in MIPS
Time Step | Thread A | Thread B | Thread A $t0 | Thread B $t0 | Memory M[$s0]
0 |  |  |  |  | 0
1 | try: LL $t0, 0($s0) | try: LL $t0, 0($s0) |  |  | 
2 | ADDIU $t0, $t0, 1 | ADDIU $t0, $t0, 1 |  |  | 
3 | SC $t0, 0($s0) | SC $t0, 0 ($s0) |  |  | 
4 | BEQZ $t0, try | BEQZ $t0, try |  |  | 
Load linked: LL rt, offset(rs)
Store conditional: SC rt, offset(rs)
  Succeeds if location not changed since the LL
    Returns 1 in rt
  Fails if location is changed
    Returns 0 in rt
Example: atomic incrementor

## Slide 43: Mutex from LL and SC
Linked load / Store Conditional
m = 0; // m=0 means lock is free; otherwise, if m=1, then lock locked
mutex_lock(int *m) {
while(test_and_set(m)){}
}
int test_and_set(int *m) {
old = *m;
*m = 1;
return old;
}
LL Atomic
SC
Notes: LL just like LW
SC jus like SW, but overwrites src register with 1 “success” or 0 “fail”

## Slide 44: Mutex from LL and SC
Linked load / Store Conditional
m = 0; // m=0 means lock is free; otherwise, if m=1, then lock locked
mutex_lock(int *m) {
while(test_and_set(m)){}
}
int test_and_set(int *m) {
LI $t0, 1
LL $t1, 0($a0)
SC $t0, 0($a0)
MOVE $v0, $t1
}
BEQZ $t0, try
try:
Notes: LL just like LW
SC jus like SW, but overwrites src register with 1 “success” or 0 “fail”

## Slide 45: Mutex from LL and SC
Linked load / Store Conditional
m = 0; // m=0 means lock is free; otherwise, if m=1, then lock locked
mutex_lock(int *m) {
while(test_and_set(m)){}
}
int test_and_set(int *m) {
try:
LI $t0, 1
LL $t1, 0($a0)
SC $t0, 0($a0)
BEQZ $t0, try
MOVE $v0, $t1
}
Notes: LL just like LW
SC jus like SW, but overwrites src register with 1 “success” or 0 “fail”

## Slide 46: Mutex from LL and SC
Linked load / Store Conditional
m = 0;
mutex_lock(int *m) {
test_and_set:
LI $t0, 1
LL $t1, 0($a0)
BNEZ $t1, test_and_set
SC $t0, 0($a0)
BEQZ $t0, test_and_set
}
mutex_unlock(int *m) {
*m = 0;
}
Notes: LL just like LW
SC jus like SW, but overwrites src register with 1 “success” or 0 “fail”

## Slide 47: Mutex from LL and SC
Linked load / Store Conditional
m = 0;
mutex_lock(int *m) {
test_and_set:
LI $t0, 1
LL $t1, 0($a0)
BNEZ $t1, test_and_set
SC $t0, 0($a0)
BEQZ $t0, test_and_set
}
mutex_unlock(int *m) {
SW $zero, 0($a0)
}
This is called a
Spin lock
Aka spin waiting
Notes: LL just like LW
SC jus like SW, but overwrites src register with 1 “success” or 0 “fail”

## Slide 48: Mutex from LL and SC
Linked load / Store Conditional
m = 0;
mutex_lock(int *m) {
Time Step | Thread A | Thread B | ThreadA $t0 | ThreadA $t1 | ThreadB $t0 | ThreadB $t1 | Mem M[$a0]
0 |  |  |  |  |  |  | 0
1 | try: LI $t0, 1 | try: LI $t0, 1 |  |  |  |  | 
2 | LL $t1, 0($a0) | LL $t1, 0($a0) |  |  |  |  | 
3 | BNEZ $t1, try | BNEZ $t1, try |  |  |  |  | 
4 | SC $t0, 0($a0) | SC $t0, 0 ($a0) |  |  |  |  | 
5 | BEQZ $t0, try | BEQZ $t0, try |  |  |  |  | 
6 |  |  |  |  |  |  | 
Notes: LL just like LW
SC jus like SW, but overwrites src register with 1 “success” or 0 “fail”

## Slide 49: Mutex from LL and SC
Linked load / Store Conditional
m = 0;
mutex_lock(int *m) {
test_and_set:
LI $t0, 1
LL $t1, 0($a0)
BNEZ $t1, test_and_set
SC $t0, 0($a0)
BEQZ $t0, test_and_set
}
mutex_unlock(int *m) {
SW $zero, 0($a0)
}
This is called a
Spin lock
Aka spin waiting
Notes: LL just like LW
SC jus like SW, but overwrites src register with 1 “success” or 0 “fail”

## Slide 50: Mutex from LL and SC
Linked load / Store Conditional
m = 0;
mutex_lock(int *m) {
Time Step | Thread A | Thread B | ThreadA $t0 | ThreadA $t1 | ThreadB $t0 | ThreadB $t1 | Mem M[$a0]
0 |  |  |  |  |  |  | 1
1 | try: LI $t0, 1 | try: LI $t0, 1 |  |  |  |  | 
2 |  |  |  |  |  |  | 
3 |  |  |  |  |  |  | 
4 |  |  |  |  |  |  | 
5 |  |  |  |  |  |  | 
6 |  |  |  |  |  |  | 
7 |  |  |  |  |  |  | 
8 |  |  |  |  |  |  | 
9 |  |  |  |  |  |  | 
Notes: LL just like LW
SC jus like SW, but overwrites src register with 1 “success” or 0 “fail”

## Slide 51: Now we can write parallel and correct programs
Thread A Thread B for(int i = 0, i < 5; i++) { for(int j = 0; j < 5; j++) {
x = x + 1; x = x + 1;
} }
mutex_lock(m); mutex_lock(m);
mutex_unlock(m); mutex_unlock(m);
Notes: Can be done using lock,
Also can be done using atomic increment.

## Slide 52: Alternative Atomic Instructions
Other atomic hardware primitives
- test and set (x86)
- atomic increment (x86)
- bus lock prefix (x86)
- compare and exchange (x86, ARM deprecated)
- linked load / store conditional (MIPS, ARM, PowerPC, DEC Alpha, …)
Notes: hardware implementation: lock bus while read-modify-write cycle happens, very expensive

## Slide 53: Synchronization
Synchronization techniques
clever code
  must work despite adversarial scheduler/interrupts
  used by: hackers
  also: noobs
disable interrupts
  used by: exception handler, scheduler, device drivers, …
disable preemption
  dangerous for user code, but okay for some kernel code
mutual exclusion locks (mutex)
  general purpose, except for some interrupt-related cases
Notes: device drivers if interrupts always go to same core

## Slide 54: Summary
Need parallel abstractions, especially for multicore
Writing correct programs is hard
Need to prevent data races
Need critical sections to prevent data races
Mutex, mutual exclusion, implements critical section
Mutex often implemented using a lock abstraction
Hardware provides synchronization primitives such as LL and SC (load linked and store conditional) instructions to efficiently implement locks