## Slide 1: Back to the Future: A Historical Perspective
Prof. Hakim Weatherspoon
CS 3410, Spring 2015
Computer Science
Cornell University

## Slide 2: Announcements
Project3 Cache Race Games night Monday, May 4th, 5pm
  Come, eat, drink, have fun and be merry!
  Location: B17 Upson Hall
Prelim2: Thursday, April 30th in evening
  Time and Location: 7:30pm sharp in Statler Auditorium
  Old prelims are online in CMS
  Prelim Review Session:
  TODAY, Tuesday, April 28, 7-9pm in B14 Hollister Hall
Project4:
  Design Doc due May 5th, bring design doc to mtg May 4-6
  Demos: May 12 and 13
  Will not be able to use slip days

## Slide 3: Announcements
Prelim2 Topics
  Lecture: Lectures 10 to 24
  Data and Control Hazards (Chapters 4.7-4.8)
  RISC/CISC (Chapters 2.16-2.18, 2.21)
  Calling conventions and linkers (Chapters 2.8, 2.12, Appendix A.1-6)
  Caching and Virtual Memory (Chapter 5)
  Multicore/parallelism (Chapter 6)
  Synchronization (Chapter 2.11)
  Traps, Exceptions, OS (Chapter 4.9, Appendix A.7, pp 445-452)
  HW2, Labs 3/4, C-Labs 2/3, PA2/3
  Topics from Prelim1 (not the focus, but some possible questions)

## Slide 4: Survey
Are you a gamer?
PC Games (NVIDIA card, etc)
Xbox One/PlayStation 4/etc
Mobile phone
Online games (minecraft, etc)
You do not play games!

## Slide 5: GPUs

## Slide 6: The supercomputer in your laptop
GPU: Graphics processing unit
Very basic till about 1999
Specialized device to accelerate display
Then started changing into a full processor
2000-…: Frontier times

## Slide 7: Parallelism
CPU: Central Processing Unit
GPU: Graphics Processing Unit

## Slide 8: Parallelism
GPU parallelism is similar to multicore parallelism
Key: How to gang schedule thousands of threads on thousands of cores?
Hardware multithreading with thousands of register sets
GPU Hardware multithreads (like multicore Hyperthreads)
  MultiIssue + extra PCs and registers – dependency logic
  Illusion of thousands of cores
  Fine grain hardware multithreading - Easier to keep pipelines full
Notes: HT = MultiIssue + extra PCs and registers – dependency logic
HT = MultiCore – redundant functional units + hazard avoidance

## Slide 10: GPU Architectures
Processing is highly data-parallel
  GPUs are highly multithreaded
  Use thread switching to hide memory latency
    Less reliance on multi-level caches
  Graphics memory is wide and high-bandwidth
Trend toward general purpose GPUs
  Heterogeneous CPU/GPU systems
  CPU for sequential code, GPU for parallel code
Programming languages/APIs
  DirectX, OpenGL
  C for Graphics (Cg), High Level Shader Language (HLSL)
  Compute Unified Device Architecture (CUDA)

## Slide 12: GPUs: Faster than Moore’s Law Moore’s Law is for Wimps?!
Peak
Performance
(polygons’s/sec)
Year
HP CRX
SGI Iris
SGI GT
HP VRX
Stellar GS1000
SGI VGX
HP TVRX
SGI SkyWriter
SGI
E&S
F300
One-pixel polygons (~10M polygons @ 30Hz)
SGI
RE2
RE1
Megatek
86
88
90
92
94
96
98
00
10
4
10
5
10
6
10
7
10
8
10
9
UNC Pxpl4
UNC Pxpl5
UNC/HP PixelFlow
Flat
shading
Gouraud
shading
Antialiasing
Slope ~2.4x/year
(Moore's Law ~ 1.7x/year)
SGI
IR
E&S
Harmony
SGI
R-Monster
Division VPX
E&S Freedom
Accel/VSIS
Voodoo
Glint
Division
Pxpl6
PC Graphics
Textures
SGI
Cobalt
Nvidia TNT
3DLabs
Graph courtesy of Professor John Poulton (from Eric Haines)
GeForce
10
4
10
5
10
6
10
7
10
8
10
9
ATI
Radeon 256
nVidia
G70

## Slide 13: Programmable Hardware
Started in 1999
Flexible, programmable
  Vertex, Geometry, Fragment Shaders
And much faster, of course
    1999 GeForce256: 0.35 Gigapixel peak fill rate
    2001 GeForce3: 0.8 Gigapixel peak fill rate
    2003 GeForceFX Ultra: 2.0 Gigapixel peak fill rate
    ATI Radeon 9800 Pro : 3.0 Gigapixel peak fill rate
    2006 NV60: ... Gigapixel peak fill rate
    2009 GeForce GTX 285: 10 Gigapixel peak fill rate
    2011
      GeForce GTC 590: 56 Gigapixel peak fill rate
      Radeon HD 6990: 2x26.5
    2012
      GeForce GTC 690: 62 Gigapixel/s peak fill rate

## Slide 14: Evolution of GPU

## Slide 15: Around 2000
Fixed function pipeline

## Slide 16: Around 2005
Programmable vertex and pixel processors

## Slide 17: Post 2006: Unified Architecture
nVIDIA Kepler

## Slide 18: Why?
Parallelism: thousands of cores
Pipelining
Hardware multithreading
Not multiscale caching
  Streaming caches
Throughput, not latency

## Slide 19: Flynn’s Taxonomy
Single Instruction Single Data (SISD) | Multiple Instruction Single Data (MISD)
Single Instruction Multiple Data (SIMD) | Multiple Instruction Multiple Data (MIMD)

## Slide 20: MIMD array of SIMD procs
nVIDIA Kepler

## Slide 21: Grids, Blocks, and Threads

## Slide 22: CUDA Memory
Fastest, per-thread
Faster, per-block
Slower, global
Read-only, cached

## Slide 23: Heterogeneous Computing
Host: the CPU and its memory
Device: the GPU and its memory

## Slide 24: Programming using CUDA
Compute Unified Device Architecture
do_something_on_host();
kernel<<<nBlk, nTid>>>(args);
cudaDeviceSynchronize();
do_something_else_on_host();
…
Highly parallel

## Slide 25: Hardware Thread Organization
Threads in a block are partitioned into warps
  All threads in a warp execute in a Single Instruction Multiple Data, or SIMD, fashion
  All paths of conditional branches will be taken
  Warp size varies, many graphics cards have 32
NO guaranteed execution ordering between warps

## Slide 26: Branch Divergence
Threads in one warp execute very different branches
Significantly harms the performance!
Simple solution:
  Reordering the threads so that all threads in each block are more likely to take the same branch
  Not always possible

## Slide 27: Example: NVIDIA Tesla
Streaming multiprocessor
8 × Streaming processors

## Slide 28: Example: NVIDIA Tesla
Streaming Processors
  Single-precision FP and integer units
  Each SP is fine-grained multithreaded
Warp: group of 32 threads
  Executed in parallel, SIMD style
    8 SPs × 4 clock cycles
  Hardware contexts for 24 warps
    Registers, PCs, …

## Slide 31: Historical Perspective

## Slide 32: Goal for Today: Back to the Future
Can multiple entities interact with processor at once?

## Slide 33: Back to the Future: Timesharing
Can multiple entities interact with processor at once?
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard

## Slide 34: Back to the Future: Timesharing
Fernando J. Corbató (MIT)
  Known for pioneering time sharing systems and MULTICS operating system (later influence UNIX)
  Influences: Turing Award Recipient (1990).
    "for his pioneering work in organizing the concepts and leading the development of the general-purpose, large-scale, time-sharing and resource-sharing computer systems“
        Corbató's Law: "Regardless of whether one is dealing with assembly language or compiler language, the number of debugged lines of source code per day is about the same!"
IBM 7090

## Slide 35: Back to the Future: Timesharing
1963 Timesharing: A Solution to Computer Bottlenecks
  http://www.youtube.com/watch?v=Q07PhW5sCEk&feature=youtu.be
  Reporter John Fitch at the MIT Computation Center in an extended interview with MIT professor of computer science Fernando J. Corbato
  The prime focus of the film is timesharing, one of the most important developments in computing
IBM 7090
Notes: http://www.youtube.com/watch?v=Q07PhW5sCEk&feature=youtu.be
[Recorded: May 9, 1963]
This vintage film features MIT Science Reporter John Fitch at the MIT Computation Center in an extended interview with MIT professor of computer science Fernando J. Corbato. The film was co-produced by WGBH (Boston) and MIT.
The prime focus of the film is timesharing, one of the most important developments in computing, and one which has come in and out of favor several times over the last several decades as the dichotomy between remote and centrally-managed computing resources played out; the latest incarnation for centrally-managed computing resources is known as cloud computing.
Timesharing as shown in this film, was a novel concept in the early 1960s. Driven by a desire to more efficiently use expensive computer resources while increasing the interactivity between user and computer (man and machine), timesharing was eventually taken up by industry in the form of special timesharing hardware for mainframe and minicomputer computer systems as well as in sophisticated operating systems to manage multiple users and resources.
Corbato describes how after the mid-1950s, when computers began to become reliable, the next big challenge to improve productivity and efficiency was the development of computer languages, FORTRAN being an example. One of the next bottlenecks in computing, according to Corabto, was the traditional batch processing method of combining many peoples computer jobs into one large single job for the computer to process at one time. He compares batch processing to a group of people catching a bus, all being moved at once.
Timesharing, on the other hand, involves attaching a large number of consoles to the central computer, each of which is given a time-slice of the computers time. While the computer is rapidly switching among user applications and problems, it appears to the user that s/he has complete access to the central computer.
Corbato then describes in technical detail a complex description of timesharing before showing some examples of timesharing from a terminal using a simple program to calculate a simple geometric problem (Pythagorean theorem).
In the long run, Corbato says, timesharing will help address the increasing need for computer time and ease-of-use.