## Slide 1: GPUs
Prof. Hakim Weatherspoon
CS 3410, Spring 2015
Computer Science
Cornell University

## Slide 2: Announcements
Project3 Cache Race Games night Monday, May 4th, 5pm
  Come, eat, drink, have fun and be merry!
  Location: B17 Upson Hall
Prelim2: Thursday, April 30th in evening
  Time and Location: 7:30pm sharp in Statler Auditorium
  Old prelims are online in CMS
  Prelim Review Session:
  TODAY, Tuesday, April 28, 7-9pm in B14 Hollister Hall
Project4:
  Design Doc due May 5th, bring design doc to mtg May 4-6
  Demos: May 12 and 13
  Will not be able to use slip days

## Slide 3: Announcements
Prelim2 Topics
  Lecture: Lectures 10 to 24
  Data and Control Hazards (Chapters 4.7-4.8)
  RISC/CISC (Chapters 2.16-2.18, 2.21)
  Calling conventions and linkers (Chapters 2.8, 2.12, Appendix A.1-6)
  Caching and Virtual Memory (Chapter 5)
  Multicore/parallelism (Chapter 6)
  Synchronization (Chapter 2.11)
  Traps, Exceptions, OS (Chapter 4.9, Appendix A.7, pp 445-452)
  HW2, Labs 3/4, C-Labs 2/3, PA2/3
  Topics from Prelim1 (not the focus, but some possible questions)

## Slide 4: GPUs

## Slide 5: The supercomputer in your laptop
GPU: Graphics processing unit
Very basic till about 1999
Specialized device to accelerate display
Then started changing into a full processor
2000-…: Frontier times

## Slide 6: Parallelism
CPU: Central Processing Unit
GPU: Graphics Processing Unit

## Slide 7: Parallelism
GPU parallelism is similar to multicore parallelism
Key: How to gang schedule thousands of threads on thousands of cores?
Hardware multithreading with thousands of register sets
GPU Hardware multithreads (like multicore Hyperthreads)
  MultiIssue + extra PCs and registers – dependency logic
  Illusion of thousands of cores
  Fine grain hardware multithreading - Easier to keep pipelines full
Notes: HT = MultiIssue + extra PCs and registers – dependency logic
HT = MultiCore – redundant functional units + hazard avoidance

## Slide 9: GPU Architectures
Processing is highly data-parallel
  GPUs are highly multithreaded
  Use thread switching to hide memory latency
    Less reliance on multi-level caches
  Graphics memory is wide and high-bandwidth
Trend toward general purpose GPUs
  Heterogeneous CPU/GPU systems
  CPU for sequential code, GPU for parallel code
Programming languages/APIs
  DirectX, OpenGL
  C for Graphics (Cg), High Level Shader Language (HLSL)
  Compute Unified Device Architecture (CUDA)

## Slide 11: GPUs: Faster than Moore’s Law Moore’s Law is for Wimps?!
Peak
Performance
(polygons’s/sec)
Year
HP CRX
SGI Iris
SGI GT
HP VRX
Stellar GS1000
SGI VGX
HP TVRX
SGI SkyWriter
SGI
E&S
F300
One-pixel polygons (~10M polygons @ 30Hz)
SGI
RE2
RE1
Megatek
86
88
90
92
94
96
98
00
10
4
10
5
10
6
10
7
10
8
10
9
UNC Pxpl4
UNC Pxpl5
UNC/HP PixelFlow
Flat
shading
Gouraud
shading
Antialiasing
Slope ~2.4x/year
(Moore's Law ~ 1.7x/year)
SGI
IR
E&S
Harmony
SGI
R-Monster
Division VPX
E&S Freedom
Accel/VSIS
Voodoo
Glint
Division
Pxpl6
PC Graphics
Textures
SGI
Cobalt
Nvidia TNT
3DLabs
Graph courtesy of Professor John Poulton (from Eric Haines)
GeForce
10
4
10
5
10
6
10
7
10
8
10
9
ATI
Radeon 256
nVidia
G70

## Slide 12: Programmable Hardware
Started in 1999
Flexible, programmable
  Vertex, Geometry, Fragment Shaders
And much faster, of course
    1999 GeForce256: 0.35 Gigapixel peak fill rate
    2001 GeForce3: 0.8 Gigapixel peak fill rate
    2003 GeForceFX Ultra: 2.0 Gigapixel peak fill rate
    ATI Radeon 9800 Pro : 3.0 Gigapixel peak fill rate
    2006 NV60: ... Gigapixel peak fill rate
    2009 GeForce GTX 285: 10 Gigapixel peak fill rate
    2011
      GeForce GTC 590: 56 Gigapixel peak fill rate
      Radeon HD 6990: 2x26.5
    2012
      GeForce GTC 690: 62 Gigapixel/s peak fill rate

## Slide 13: Evolution of GPU

## Slide 14: Around 2000
Fixed function pipeline

## Slide 15: Around 2005
Programmable vertex and pixel processors

## Slide 16: Post 2006: Unified Architecture
nVIDIA Kepler

## Slide 17: Why?
Parallelism: thousands of cores
Pipelining
Hardware multithreading
Not multiscale caching
  Streaming caches
Throughput, not latency

## Slide 18: Flynn’s Taxonomy
Single Instruction Single Data (SISD) | Multiple Instruction Single Data (MISD)
Single Instruction Multiple Data (SIMD) | Multiple Instruction Multiple Data (MIMD)

## Slide 19: MIMD array of SIMD procs
nVIDIA Kepler

## Slide 20: Grids, Blocks, and Threads

## Slide 21: CUDA Memory
Fastest, per-thread
Faster, per-block
Slower, global
Read-only, cached

## Slide 22: Heterogeneous Computing
Host: the CPU and its memory
Device: the GPU and its memory

## Slide 23: Programming using CUDA
Compute Unified Device Architecture
do_something_on_host();
kernel<<<nBlk, nTid>>>(args);
cudaDeviceSynchronize();
do_something_else_on_host();
…
Highly parallel

## Slide 24: Hardware Thread Organization
Threads in a block are partitioned into warps
  All threads in a warp execute in a Single Instruction Multiple Data, or SIMD, fashion
  All paths of conditional branches will be taken
  Warp size varies, many graphics cards have 32
NO guaranteed execution ordering between warps

## Slide 25: Branch Divergence
Threads in one warp execute very different branches
Significantly harms the performance!
Simple solution:
  Reordering the threads so that all threads in each block are more likely to take the same branch
  Not always possible

## Slide 26: Example: NVIDIA Tesla
Streaming multiprocessor
8 × Streaming processors

## Slide 27: Example: NVIDIA Tesla
Streaming Processors
  Single-precision FP and integer units
  Each SP is fine-grained multithreaded
Warp: group of 32 threads
  Executed in parallel, SIMD style
    8 SPs × 4 clock cycles
  Hardware contexts for 24 warps
    Registers, PCs, …