## Slide 1: State
Hakim Weatherspoon
CS 3410
Computer Science
Cornell University
The slides are the product of many rounds of teaching CS 3410 by Professors Weatherspoon, Bala, Bracy, and Sirer.

## Slide 2: Announcements
Make sure you are
Registered for class, can access CMS
Have a Section you can go to.
Lab Sections are required.
  “Make up” lab sections only Friday 11:40am or 1:25pm
  Bring laptop to Labs
Project partners are required for projects starting w/ project 2
  Have project partner in same Lab Section, if possible
  WICC hosting a partner finding event Feb 12 @ 6pm in 3rd floor lounge of Gates

## Slide 3: Announcements
Make sure to go to your Lab Section this week
Completed Proj1 due before winter break, Friday, Feb 16th
Note, a Design Document is due when you submit Proj1 final circuit
Work alone
Work alone, BUT use your resources
  Lab Section, Piazza.com, Office Hours
  Class notes, book, Sections, CSUGLab

## Slide 4: Announcements
Check online syllabus/schedule
  http://www.cs.cornell.edu/Courses/CS3410/2018sp/schedule
Slides and Reading for lectures
Office Hours
Pictures of all TAs
Project and Reading Assignments
Dates to keep in Mind
  Prelims: Thur Mar 15th and Thur May 3rd
  Proj 1: Due next Friday, Feb 16th before Winter break
  Proj3: Due before Spring break
  Final Project: May 15th
Schedule is subject to change

## Slide 5: Collaboration, Late, Re-grading Policies
“White Board” Collaboration Policy
  Can discuss approach together on a “white board”
  Leave, watch a movie (e.g. Strange Things), and write up solution independently
  Do not copy solutions
  Late Policy
  Each person has a total of four “slip days”
  Max of two slip days for any individual assignment
  Slip days deducted first for any late assignment,
  cannot selectively apply slip days
  For projects, slip days are deducted from all partners
  25% deducted per day late after slip days are exhausted
  Regrade policy
  Submit written regrade request within a week of receiving score

## Slide 6: Big Picture: Building a Processor
PC
imm
memory
memory
din
dout
addr
target
offset
cmp
control
=?
new pc
register file
inst
extend
+4
+4
A Single cycle processor
alu

## Slide 7: Review
  We can generalize 1-bit Full Adders to 32 bits, 64 bits …
A0 B0
S0
A1 B1
S1
A2 B2
S2
A3 B3
S3
C0

## Slide 8: Review
  We can generalize 1-bit Full Adders to 32 bits, 64 bits …
S0
S1
S2
S3
over flow
A0
B0
A1
B1
A2
B2
A3
B3
mux
mux
mux
mux
0=add
1=sub

## Slide 9: Example: A Calculator
decoder
8
8
S
A
B
8
0=add
1=sub
Notes: red herring? constants into mux

## Slide 10: Example: A Calculator
adder
mux
decoder
8
8
8
8
8
S
A
B
8
0=add
1=sub
Notes: red herring? constants into mux

## Slide 11: Example: A Calculator
adder
mux
decoder
8
8
8
8
8
S
A
B
8
0=add
1=sub
128
128
0b1000 0000
0b1000 0000
Notes: red herring? constants into mux

## Slide 12: Example: A Calculator
adder
mux
decoder
8
8
8
8
8
S
A
B
8
0=add
1=sub
128
128
0b1000 0000
0b1000 0000
Notes: red herring? constants into mux

## Slide 13: Review: Efficiency and Generality
  We can generalize 1-bit Full Adders to 32 bits, 64 bits …
  How long does it take to compute a result?
S0
S1
S2
S3
over flow
A0
B0
A1
B1
A2
B2
A3
B3
mux
mux
mux
mux
0=add
1=sub

## Slide 14: Review: Efficiency and Generality
  We can generalize 1-bit Full Adders to 32 bits, 64 bits …
  How long does it take to compute a result?
  A) 2 ns
  B) 2 gate delays
  C) 10 ns
  D) 10 gate delays
  E) 8 gate delays

## Slide 15: Review: Efficiency and Generality
  We can generalize 1-bit Full Adders to 32 bits, 64 bits …
  How long does it take to compute a result?
S0
S1
S2
S3
over flow
A0
B0
A1
B1
A2
B2
A3
B3
mux
mux
mux
mux
0=add
1=sub
t=10
t=8
t=6
t=4
t=2
t=0

## Slide 16: Review: Efficiency and Generality
  We can generalize 1-bit Full Adders to 32 bits, 64 bits …
  How long does it take to compute a result?
  Can we store the result?
S0
S1
S2
S3
over flow
A0
B0
A1
B1
A2
B2
A3
B3
mux
mux
mux
mux
0=add
1=sub
t=10
t=8
t=6
t=4
t=2
t=0

## Slide 17: Performance
Speed of a circuit is affected by the number of gates in series (on the critical path or the deepest level of logic)
Combinational
Logic
tcombinational
inputs arrive
outputs expected

## Slide 18: 4-bit Ripple Carry Adder
A3
B3
S3
C4
A1
B1
S1
A2
B2
S2
A0
B0
C0
S0
C1
C2
C3
First full adder, 2 gate delay
Second full adder, 2 gate delay
…
Carry ripples from lsb to msb
Notes: Carry-lookahead adders would be more efficient performance wise (i.e. lower gate delay), but more expense hardware wise (i.e. more logic gates)

## Slide 19: Stateful Components
Until now is combinationial logic
  Output is computed when inputs are present
  System has no internal state
  Nothing computed in the present can depend on what happened in the past!
Need a way to record data
Need a way to build stateful circuits
Need a state-holding device
Inputs
Combinational circuit
Outputs
N
M
Notes: How are we going to stably store state

## Slide 20: Goals for Today
State
  How do we store one bit?
  Attempts at storing (and changing) one bit
    Set-Reset Latch
    D Latch
    D Flip-Flops
    Master-Slave Flip-Flops
  Register: storing more than one bit, N-bits
Basic Building Blocks
  Decoders and Encoders

## Slide 21: Goal
How do we store store one bit?

## Slide 22: First Attempt: Unstable Devices
B
A
C

## Slide 23: First Attempt: Unstable Devices
0
1
Does not work!
  Unstable
  Oscillates wildly!
B
A
C
1
0
0
1

## Slide 24: Second Attempt: Bistable Devices
In stable state, A = B
How do we change the state?
A
B
A
B
1
A
B
1
0
0
A Simple Device
Stable and unstable equilibria?
Notes: How to create state? Feedback.
Show how the signal works

## Slide 25: Third Attempt: Set-Reset Latch
B
R
Q
A
S
Notes: Can you store a value (with this circuit)?
Can you change its value?
Q is comes from Latin language "quiscens" or "the present particle" or "what is present available" or "present output"
How to create state? Feedback.
Show how the signal works

## Slide 26: Third Attempt: Set-Reset Latch
Set-Reset (S-R) Latch
Stores a value Q and its complement
S | R | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
S | R | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
S
R
Q
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0

## Slide 27: Third Attempt: Set-Reset Latch
Set-Reset (S-R) Latch
Stores a value Q and its complement
S | R | Q | 
0 | 0 |  | 
0 | 1 | ? | ?
1 | 0 |  | 
1 | 1 |  | 
S | R | Q | 
0 | 0 |  | 
0 | 1 | ? | ?
1 | 0 |  | 
1 | 1 |  | 
S
R
Q
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
0
1
0
Q will be 0 if R is 1
1
will be 1
S | R | Q | 
0 | 0 |  | 
0 | 1 | 0 | 1
1 | 0 |  | 
1 | 1 |  | 
S | R | Q | 
0 | 0 |  | 
0 | 1 | 0 | 1
1 | 0 |  | 
1 | 1 |  | 

## Slide 28: Third Attempt: Set-Reset Latch
Set-Reset (S-R) Latch
Stores a value Q and its complement
S | R | Q | 
0 | 0 |  | 
0 | 1 | 0 | 1
1 | 0 | ? | ?
1 | 1 |  | 
S | R | Q | 
0 | 0 |  | 
0 | 1 | 0 | 1
1 | 0 | ? | ?
1 | 1 |  | 
S
R
Q
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
1
0
1
Q will be 1
0
will be 0 if S is 1
S | R | Q | 
0 | 0 |  | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 |  | 
S | R | Q | 
0 | 0 |  | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 |  | 
What are the values for Q and ?
0 and 0
0 and 1
1 and 0
1 and 1
iClicker Question
Notes: Ask a clicker question about Q and !Q

## Slide 29: Third Attempt: Set-Reset Latch
Set-Reset (S-R) Latch
Stores a value Q and its complement
S | R | Q | 
0 | 0 | ? | ?
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 |  | 
S | R | Q | 
0 | 0 | ? | ?
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 |  | 
S
R
Q
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
0
0
1
If Q is 1, will stay 1
if Q is 0, will stay 0
0
If is 0 will stay 0
If is 1 will stay 1
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 |  | 
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 |  | 
1

Notes: Since the set and reset input are both 0, the Q and !Q determine the output, which will hold.

## Slide 30: Third Attempt: Set-Reset Latch
Set-Reset (S-R) Latch
Stores a value Q and its complement
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | ? | ?
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | ? | ?
S
R
Q
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
1
1
0
Q will be 0 since R is 1
0
will be 0 since S is 1
What happens when S,R changes from 1,1 to 0,0?
Notes: Start with 0, 1 => 0, 1
then 0, 0 => 0, 1
then 1, 0 => 1, 0
then 0, 0 => 1, 0, better yet “stay”
1, 1 is forbidden, b/c going to 0, 0 after goes haywire
i.e.
Start 1,1 => 0,0
Alright. Now change S,R to 0, 0, what happens.
1, 1=>0, 0 -> 0, 0=> 0, 0 -> 0, 0=>1, 1 -> 0, 0=> 0, 0 -> oscillations.
S R=>Q,!Q -> S,R=>Q,!Q -> S, R=>Q,!Q -> S,R => Q,!Q

## Slide 31: iClicker Question
What’s wrong with the SR Latch?
Q is undefined when S=1 and R=1
(That’s why this is called the forbidden state.)
Q oscillates between 0 and 1 when the inputs transition from 1,1  0,0
The SR Latch is problematic b/c it has two outputs to store a single bit.
There is nothing wrong with the SR Latch!
Notes: Answer:

## Slide 32: Third Attempt: Set-Reset Latch
Set-Reset (S-R) Latch
Stores a value Q and its complement
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | ? | ?
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | ? | ?
S
R
Q
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
10
1 0
01
0 1
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | forbidden | 
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | forbidden | 
What happens when S,R changes from 1,1 to 0,0?
Q and become unstable and will oscillate wildly
between values 0,0 to 1,1 to 0,0 to 1,1 …
0 1 0
01 0
0 1 0 1
01 0 1
0
0
Notes: Start with 0, 1 => 0, 1
then 0, 0 => 0, 1
then 1, 0 => 1, 0
then 0, 0 => 1, 0, better yet “stay”
1, 1 is forbidden, b/c going to 0, 0 after goes haywire
i.e.
Start 1,1 => 0,0
Alright. Now change S,R to 0, 0, what happens.
1, 1=>0, 0 -> 0, 0=> 0, 0 -> 0, 0=>1, 1 -> 0, 0=> 0, 0 -> oscillations.
S R=>Q,!Q -> S,R=>Q,!Q -> S, R=>Q,!Q -> S,R => Q,!Q

## Slide 33: Third Attempt: Set-Reset Latch
Set-Reset (S-R) Latch
Stores a value Q and its complement
S
R
Q
S
R
Q
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | forbidden | 
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | forbidden | 
S | R | Q |  | 
0 | 0 | Q |  | hold
0 | 1 | 0 | 1 | reset
1 | 0 | 1 | 0 | set
1 | 1 | forbidden |  | 
S | R | Q |  | 
0 | 0 | Q |  | hold
0 | 1 | 0 | 1 | reset
1 | 0 | 1 | 0 | set
1 | 1 | forbidden |  | 
Notes: Start with 0, 1 => 0, 1
then 0, 0 => 0, 1
then 1, 0 => 1, 0
then 0, 0 => 1, 0, better yet “stay”
1, 1 is forbidden, b/c going to 0, 0 after goes haywire
i.e.
Start 1,1 => 0,0
Alright. Now change S,R to 0, 0, what happens.
1, 1=>0, 0 -> 0, 0=> 0, 0 -> 0, 0=>1, 1 -> 0, 0=> 0, 0 -> oscillations.
S R=>Q,!Q -> S,R=>Q,!Q -> S, R=>Q,!Q -> S,R => Q,!Q

## Slide 34: Takeaway
Set-Reset (SR) Latch can store one bit and we can change the value of the stored bit. But, SR Latch has a forbidden state.

## Slide 35: Next Goal
How do we avoid the forbidden state of S-R Latch?

## Slide 36: Fourth Attempt: (Unclocked) D Latch
Fill in the truth table?
D
S
R
Q
Q
D
D | Q | 
0 |  | 
1 |  | 
D | Q | 
0 |  | 
1 |  | 
S
R
Q
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
Notes: Start in 0, 0, 1
Change to D = 1
After NOT gate, R = 0
After OR+NOT gates, /Q = 0 (R is already ready then), Q goes to 1
Problem: No way to hold state

## Slide 37: Fourth Attempt: (Unclocked) D Latch
D
S
R
Q
Q
D
D | Q | 
0 | 0 | 1
1 | 1 | 0
D | Q | 
0 | 0 | 1
1 | 1 | 0
S
R
Q
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
Fill in the truth table?
Data (D) Latch
  Easier to use than an SR latch
  No possibility of entering an undefined state
When D changes, Q changes
    … immediately (…after a delay of 2 Ors and 2 NOTs)
Need to control when the output changes
Notes: Start in 0, 0, 1
Change to D = 1
After NOT gate, R = 0
After OR+NOT gates, /Q = 0 (R is already ready then), Q goes to 1
Problem: No way to hold state

## Slide 38: Takeaway
Set-Reset (SR) Latch can store one bit and we can change the value of the stored bit. But, SR Latch has a forbidden state.
(Unclocked) D Latch can store and change a bit like an SR Latch while avoiding the forbidden state.

## Slide 39: Next Goal
How do we coordinate state changes to a D Latch?

## Slide 40: Aside: Clocks
Clock helps coordinate state changes
  Usually generated by an oscillating crystal
  Fixed period
  Frequency = 1/period
period
high
low
1
0
falling edge
rising edge
clock
period
clock
high
clock
low
rising edge
falling edge

## Slide 41: Clock Disciplines
Level sensitive
  State changes when clock is high (or low)
Edge triggered
  State changes at clock edge
positive edge-triggered
negative edge-triggered

## Slide 42: Clock Methodology
Clock Methodology
Negative edge, synchronous
Edge-Triggered  signals must be stable near falling edge
“near” = before and after
tsetup thold
clk
compute
save
tsetup
thold
compute
save
compute
tcombinational

## Slide 43: Round 2: D Latch (1)
S
R
D
Q
C | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
C | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
D
Q
C
Set
Reset
Inverter prevents SR Latch from entering 1,1 state
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables
Answer:
Q
Q
0
1

## Slide 44: Round 2: D Latch (1)
S
R
D
Q
C | D | Q | 
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 |  | 
1 | 1 |  | 
C | D | Q | 
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 |  | 
1 | 1 |  | 
D
Q
C
Set
Reset
Inverter prevents SR Latch from entering 1,1 state
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables
Answer:
Q
Q
0
1

## Slide 45: Round 2: D Latch (1)
S
R
D
Q
C | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
C | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
Level sensitive
Inverter prevents SR Latch from entering 1,1 state
C enables changes
D
Q
C
Set
Reset
C = 1, D Latch transparent: set/reset (according to D)
C = 0, D Latch opaque: keep state (ignore D)
No
Change
C
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables
Answer:
Q
Q
0
1

## Slide 46: Round 2: D Latch (1)
S
R
D
Q
C | D | Q | 
0 | 0 | Q | 
0 | 1 | Q | 
1 | 0 | 0 | 1
1 | 1 | 1 | 0
C | D | Q | 
0 | 0 | Q | 
0 | 1 | Q | 
1 | 0 | 0 | 1
1 | 1 | 1 | 0
D
Q
C
Set
Reset
C = 1, D Latch transparent: set/reset (according to D)
C = 0, D Latch opaque: keep state (ignore D)
No
Change
S | R | Q |  | 
0 | 0 | Q |  | hold
0 | 1 | 0 | 1 | reset
1 | 0 | 1 | 0 | set
1 | 1 | forbidden |  | 
S | R | Q |  | 
0 | 0 | Q |  | hold
0 | 1 | 0 | 1 | reset
1 | 0 | 1 | 0 | set
1 | 1 | forbidden |  | 
Level sensitive
Inverter prevents SR Latch from entering 1,1 state
C enables changes
C
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables
Answer:
Q
Q
0
1

## Slide 47: iClicker Question
clk
D
Q
clk | D | Q | 
0 | 0 | Q | 
0 | 1 | Q | 
1 | 0 | 0 | 1
1 | 1 | 1 | 0
clk | D | Q | 
0 | 0 | Q | 
0 | 1 | Q | 
1 | 0 | 0 | 1
1 | 1 | 1 | 0
A
B
D
Q
clk
What is the value of Q at A & B?
A = 0, B = 0
A = 0, B = 1
A = 1, B = 0
A = 1, B = 1
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables

## Slide 48: iClicker Question
clk
D
Q
clk | D | Q | 
0 | 0 | Q | 
0 | 1 | Q | 
1 | 0 | 0 | 1
1 | 1 | 1 | 0
clk | D | Q | 
0 | 0 | Q | 
0 | 1 | Q | 
1 | 0 | 0 | 1
1 | 1 | 1 | 0
A
B
D
Q
clk
What is the value of Q at A & B?
A = 0, B = 0
A = 0, B = 1
A = 1, B = 0
A = 1, B = 1
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables

## Slide 49: iClicker Question
clk
D
Q
Level Sensitive D Latch
Clock high: set/reset (according to D)
Clock low: keep state (ignore D)
clk | D | Q | 
0 | 0 | Q | 
0 | 1 | Q | 
1 | 0 | 0 | 1
1 | 1 | 1 | 0
clk | D | Q | 
0 | 0 | Q | 
0 | 1 | Q | 
1 | 0 | 0 | 1
1 | 1 | 1 | 0
A
B
D
Q
clk
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables

## Slide 50: Round 3: D Flip-Flop
Edge-Triggered
Data captured when clock high
Output changes only on falling edges
D
Q
D
Q
C
C
X
Q
D
clk
L1
L2
Notes: Master-Slave Flip Flop
- Outputs change only on falling edges
- Data is captured on rising edges
1 cycle delay
but works out perfectly – data for the next stage is ready 1 cycle ahead of time

## Slide 51: Round 3: D Flip-Flop
Clock = 1: L1 transparent L2 opaque
D
Q
D
Q
C
C
X
Q
D
clk
0
1
L1
L2
X
D
D passes through L1 to X
X
Clock = 0: L1 opaque L2 transparent
D
Q
D
Q
C
C
X
Q
D
clk
1
0
L1
L2
X
Q
X passes through L2 to Q
X
When CLK falls (10),
Q gets X, X cannot change
When CLK rises (01),
now X can change,
Q does not change
Notes: Master-Slave Flip Flop
- Outputs change only on falling edges
- Data is captured on rising edges
1 cycle delay
but works out perfectly – data for the next stage is ready 1 cycle ahead of time

## Slide 52: iClicker Question – start here
D
Q
D
Q
C
C
clk
D
X
Q
X
Q
D
clk
1
L1
L2
What is the value of Q
at A & B?
A = 0, B = 0
A = 0, B = 1
A = 1, B = 0
A = 1, B = 1
B
A
Notes: A=1, B=0

## Slide 53: iClicker Question – start here
D
Q
D
Q
C
C
clk
D
X
Q
X
Q
D
clk
1
L1
L2
What is the value of Q
at A & B?
A = 0, B = 0
A = 0, B = 1
A = 1, B = 0
A = 1, B = 1
B
A
Notes: A=1, B=0

## Slide 54: Edge-Triggered D Flip-Flop
D Flip-Flop
Edge-Triggered
Data captured when clock is high
Output changes only on falling edges
D
Q
D
Q
C
C
clk
D
X
Q
c
X
c
Q
D
clk
1
0
1
0
0
1
1
0
0
1
A
B
Notes: Master-Slave Flip Flop
- Outputs change only on falling edges
- Data is captured on rising edges
1 cycle delay
but works out perfectly – data for the next stage is ready 1 cycle ahead of time

## Slide 55: Edge-Triggered D Flip-Flop
D Flip-Flop
Edge-Triggered
Data captured when clock is high
Output changes only on falling edges
D
Q
D
Q
C
C
clk
D
X
Q
c
X
c
Q
D
clk
1
0
1
0
0
1
1
0
0
1
A
B
Notes: Master-Slave Flip Flop
- Outputs change only on falling edges
- Data is captured on rising edges
1 cycle delay
but works out perfectly – data for the next stage is ready 1 cycle ahead of time

## Slide 56: Takeaway
Set-Reset (SR) Latch can store one bit and we can change the value of the stored bit. But, SR Latch has a forbidden state.
(Unclocked) D Latch can store and change a bit like an SR Latch while avoiding a forbidden state.
An Edge-Triggered D Flip-Flip (aka Master-Slave D Flip-Flip) stores one bit. The bit can be changed in a synchronized fashion on the edge of a clock signal.

## Slide 57: Next Goal
How do we store more than one bit, N bits?

## Slide 58: Registers
Register
D flip-flops in parallel
shared clock
extra clocked inputs: write_enable, reset, …
clk
D0
D3
D1
D2
4
4
4-bit
reg
clk

## Slide 59: Takeaway
Set-Reset (SR) Latch can store one bit and we can change the value of the stored bit. But, SR Latch has a forbidden state.
(Unclocked) D Latch can store and change a bit like an SR Latch while avoiding a forbidden state.
An Edge-Triggered D Flip-Flip (aka Master-Slave D Flip-Flip) stores one bit. The bit can be changed in a synchronized fashion on the edge of a clock signal.
An N-bit register stores N-bits. It is created with N D-Flip-Flops in parallel along with a shared clock.

## Slide 60: An Example: What will this circuit do?
4-bit
reg
Clk
Decoder
+1
4
4
4
16
4

## Slide 61: An Example: What will this circuit do?
4-bit
reg
Clk
Run
WE
R
Reset
Decoder
A[4]
1 = 0001 =B[4]
S[4]
Cout
+1
4
4
4
16
4

## Slide 62: Decoder Example: 7-Segment LED
7-Segment LED
  photons emitted when electrons fall into holes
d7
d6
d5
d4
d3
d2
d1
d0
Notes: Previous slide would need to display up to 16, so would need a 16-segment LED decoder

## Slide 63: Decoder Example: 7-Segment LED
7-Segment LED
  photons emitted when electrons fall into holes
d7
d6
d5
d4
d3
d2
d1
d0

## Slide 64: Decoder Example: 7-Segment LED Decoder
3 inputs
encode 0 – 7 in binary
7 outputs
one for each LED
7LED decode

## Slide 65: 7 Segment LED Decoder Implementation
b2 | b1 | b0 | d6 | d5 | d4 | d3 | d2 | d1 | d0
0 | 0 | 0 |  |  |  |  |  |  | 
0 | 0 | 1 |  |  |  |  |  |  | 
0 | 1 | 0 |  |  |  |  |  |  | 
0 | 1 | 1 |  |  |  |  |  |  | 
1 | 0 | 0 |  |  |  |  |  |  | 
1 | 0 | 1 |  |  |  |  |  |  | 
1 | 1 | 0 |  |  |  |  |  |  | 
1 | 1 | 1 |  |  |  |  |  |  | 
d0
d1
d2
d3
d4
d5
d6
b2 | b1 | b0 | d6 | d5 | d4 | d3 | d2 | d1 | d0
0 | 0 | 0 |  |  |  |  |  |  | 
0 | 0 | 1 |  |  |  |  |  |  | 
0 | 1 | 0 |  |  |  |  |  |  | 
0 | 1 | 1 |  |  |  |  |  |  | 
1 | 0 | 0 |  |  |  |  |  |  | 
1 | 0 | 1 |  |  |  |  |  |  | 
1 | 1 | 0 |  |  |  |  |  |  | 
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1

## Slide 66: 7 Segment LED Decoder Implementation
d0
d1
d2
d3
d4
d5
d6
b2 | b1 | b0 | d6 | d5 | d4 | d3 | d2 | d1 | d0
0 | 0 | 0 |  |  |  |  |  |  | 
0 | 0 | 1 |  |  |  |  |  |  | 
0 | 1 | 0 |  |  |  |  |  |  | 
0 | 1 | 1 |  |  |  |  |  |  | 
1 | 0 | 0 |  |  |  |  |  |  | 
1 | 0 | 1 |  |  |  |  |  |  | 
1 | 1 | 0 |  |  |  |  |  |  | 
1 | 1 | 1 |  |  |  |  |  |  | 
1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0 | 1 | 1

## Slide 67: Basic Building Blocks We have Seen
binary
encoder
2N
N
binary
decoder
N
2N
Multiplexor
N
M
N
N
N
N
. . .
0
1
2
2M-1

## Slide 68: Encoders
1
2
3
4
5
6
7
0
encoder
N
. . .
. . .
Log2(N) outputs wires
N Input wires
e.g. Voting:
Can only vote for one out of N
candidates, so N inputs.
But can encode vote efficiently
with binary encoding.
Notes: N possible inputs -> log2(N) wires to encode

## Slide 69: Example Encoder Truth Table
a
b
1
c
d
2
3
4
o1
A 3-bit
encoder
with 4 inputs for simplicity
a | b | c | d |  |  |  | 
0 | 0 | 0 | 0 |  |  |  | 
1 | 0 | 0 | 0 |  |  |  | 
0 | 1 | 0 | 0 |  |  |  | 
0 | 0 | 1 | 0 |  |  |  | 
0 | 0 | 0 | 1 |  |  |  | 
o0
o1
o2
Notes: Implementation . . .
assume 8 choices, exactly one mark detected

## Slide 70: Example Encoder Truth Table
a
b
1
c
d
2
3
4
o1
A 3-bit
encoder
with 4 inputs for simplicity
a | b | c | d |  | o2 | o1 | o0
0 | 0 | 0 | 0 |  | 0 | 0 | 0
1 | 0 | 0 | 0 |  | 0 | 0 | 1
0 | 1 | 0 | 0 |  | 0 | 1 | 0
0 | 0 | 1 | 0 |  | 0 | 1 | 1
0 | 0 | 0 | 1 |  | 1 | 0 | 0
o0
o1
o2
o2 = abcd
o1 = abcd + abcd
o0 = abcd + abcd
Notes: Implementation . . .
assume 8 choices, exactly one mark detected

## Slide 71: Basic Building Blocks Example: Voting
Ballots
The 3410 optical scan
vote reader
machine
detect
enc
8
3
7
7LED decode

## Slide 72: Basic Building Blocks We have Seen
binary
encoder
2N
N
binary
decoder
N
2N
Multiplexor
N
M
N
N
N
N
. . .
0
1
2
2M-1

## Slide 73: Recap
We can now build interesting devices with sensors
  Using combinationial logic
We can also store data values (aka Sequential Logic)
  In state-holding elements
  Coupled with clocks

## Slide 74: Summary
We can now build interesting devices with sensors
  Using combinational logic
We can also store data values
  Stateful circuit elements (D Flip Flops, Registers, …)
  Clock to synchronize state changes