## Slide 1: State
Hakim Weatherspoon
CS 3410
Computer Science
Cornell University
The slides are the product of many rounds of teaching CS 3410 by Professors Weatherspoon, Bala, Bracy, and Sirer.

## Slide 2: Announcements
Make sure you are
Registered for class, can access CMS
Have a Section you can go to.
Lab Sections are required.
  “Make up” lab sections only Friday 11:40am or 1:25pm
  Bring laptop to Labs
Project partners are required for projects starting w/ project 2
  Have project partner in same Lab Section, if possible
  WICC hosting a partner finding event Feb 12 @ 6pm in 3rd floor lounge of Gates

## Slide 3: Announcements
Make sure to go to your Lab Section this week
Completed Proj1 due before winter break, Friday, Feb 16th
Note, a Design Document is due when you submit Proj1 final circuit
Work alone
Work alone, BUT use your resources
  Lab Section, Piazza.com, Office Hours
  Class notes, book, Sections, CSUGLab

## Slide 4: Announcements
Check online syllabus/schedule
  http://www.cs.cornell.edu/Courses/CS3410/2018sp/schedule
Slides and Reading for lectures
Office Hours
Pictures of all TAs
Project and Reading Assignments
Dates to keep in Mind
  Prelims: Thur Mar 15th and Thur May 3rd
  Proj 1: Due next Friday, Feb 16th before Winter break
  Proj3: Due before Spring break
  Final Project: May 15th
Schedule is subject to change

## Slide 5: Collaboration, Late, Re-grading Policies
“White Board” Collaboration Policy
  Can discuss approach together on a “white board”
  Leave , watch a movie (e.g. Strange Things), and write up solution independently
  Do not copy solutions
  Late Policy
  Each person has a total of four “slip days”
  Max of two slip days for any individual assignment
  Slip days deducted first for any late assignment,
  cannot selectively apply slip days
  For projects, slip days are deducted from all partners
  25% deducted per day late after slip days are exhausted
  Regrade policy
  Submit regrade within a week of receiving score

## Slide 6: Goals for Today
State
  How do we store one bit?
  Attempts at storing (and changing) one bit
    Set-Reset Latch
    D Latch
    D Flip-Flops
    Master-Slave Flip-Flops
  Register: storing more than one bit, N-bits
Basic Building Blocks
  Decoders and Encoders

## Slide 7: Goal
How do we store store one bit?

## Slide 8: First Attempt: Unstable Devices
B
A
C

## Slide 9: Second Attempt: Bistable Devices
A
B
A Simple Device
Stable and unstable equilibria?
Notes: How to create state? Feedback.
Show how the signal works

## Slide 10: Third Attempt: Set-Reset Latch
B
R
Q
A
S
Notes: Can you store a value (with this circuit)?
Can you change its value?
Q is comes from Latin language "quiscens" or "the present particle" or "what is present available" or "present output"
How to create state? Feedback.
Show how the signal works

## Slide 11: Third Attempt: Set-Reset Latch
Set-Reset (S-R) Latch
Stores a value Q and its complement
S | R | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
S | R | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
S
R
Q
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0

## Slide 12: Third Attempt: Set-Reset Latch
Set-Reset (S-R) Latch
Stores a value Q and its complement
S
R
Q
S
R
Q
S | R | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
S | R | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
Notes: Start with 0, 1 => 0, 1
then 0, 0 => 0, 1
then 1, 0 => 1, 0
then 0, 0 => 1, 0, better yet “stay”
1, 1 is forbidden, b/c going to 0, 0 after goes haywire
i.e.
Start 1,1 => 0,0
Alright. Now change S,R to 0, 0, what happens.
1, 1=>0, 0 -> 0, 0=> 0, 0 -> 0, 0=>1, 1 -> 0, 0=> 0, 0 -> oscillations.
S R=>Q,!Q -> S,R=>Q,!Q -> S, R=>Q,!Q -> S,R => Q,!Q

## Slide 13: Takeaway
Set-Reset (SR) Latch can store one bit and we can change the value of the stored bit. But, SR Latch has a forbidden state.

## Slide 14: Next Goal
How do we avoid the forbidden state of S-R Latch?

## Slide 15: Fourth Attempt: (Unclocked) D Latch
Fill in the truth table?
D
S
R
Q
Q
D
D | Q | 
0 |  | 
1 |  | 
D | Q | 
0 |  | 
1 |  | 
S
R
Q
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
Notes: Start in 0, 0, 1
Change to D = 1
After NOT gate, R = 0
After OR+NOT gates, /Q = 0 (R is already ready then), Q goes to 1
Problem: No way to hold state

## Slide 16: Takeaway
Set-Reset (SR) Latch can store one bit and we can change the value of the stored bit. But, SR Latch has a forbidden state.
(Unclocked) D Latch can store and change a bit like an SR Latch while avoiding the forbidden state.

## Slide 17: Next Goal
How do we coordinate state changes to a D Latch?

## Slide 18: Aside: Clocks
Clock helps coordinate state changes
  Usually generated by an oscillating crystal
  Fixed period
  Frequency = 1/period
period
high
low
1
0
falling edge
rising edge
clock
period
clock
high
clock
low
rising edge
falling edge

## Slide 19: Clock Disciplines
Level sensitive
  State changes when clock is high (or low)
Edge triggered
  State changes at clock edge
positive edge-triggered
negative edge-triggered

## Slide 20: Clock Methodology
Clock Methodology
Negative edge, synchronous
Edge-Triggered  signals must be stable near falling edge
“near” = before and after
tsetup thold
clk
compute
save
tsetup
thold
compute
save
compute
tcombinational

## Slide 21: Round 2: D Latch (1)
S
R
D
Q
C | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
C | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
D
Q
C
Set
Reset
Inverter prevents SR Latch from entering 1,1 state
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables
Answer:
Q
Q
0
1

## Slide 22: Round 2: D Latch (1)
S
R
D
Q
C | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
C | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
Level sensitive
Inverter prevents SR Latch from entering 1,1 state
C enables changes
D
Q
C
Set
Reset
C = 1, D Latch transparent: set/reset (according to D)
C = 0, D Latch opaque: keep state (ignore D)
No
Change
C
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables
Answer:
Q
Q
0
1

## Slide 23: Round 2: D Latch (1)
S
R
D
Q
C | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
C | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
D
Q
C
Set
Reset
C = 1, D Latch transparent: set/reset (according to D)
C = 0, D Latch opaque: keep state (ignore D)
No
Change
S | R | Q |  | 
0 | 0 | Q |  | hold
0 | 1 | 0 | 1 | reset
1 | 0 | 1 | 0 | set
1 | 1 | forbidden |  | 
S | R | Q |  | 
0 | 0 | Q |  | hold
0 | 1 | 0 | 1 | reset
1 | 0 | 1 | 0 | set
1 | 1 | forbidden |  | 
Level sensitive
Inverter prevents SR Latch from entering 1,1 state
C enables changes
C
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables
Answer:
Q
Q
0
1

## Slide 24: Round 2: D Latch (1)
clk
D
Q
Level Sensitive D Latch
Clock high: set/reset (according to D)
Clock low: keep state (ignore D)
clk | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
clk | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
D
Q
clk
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables

## Slide 25: Round 3: D Flip-Flop
Edge-Triggered
Data captured when clock high
Output changes only on falling edges
D
Q
D
Q
C
C
X
Q
D
clk
L1
L2
Notes: Master-Slave Flip Flop
- Outputs change only on falling edges
- Data is captured on rising edges
1 cycle delay
but works out perfectly – data for the next stage is ready 1 cycle ahead of time

## Slide 26: Round 3: D Flip-Flop
Clock = 1: L1 transparent L2 opaque
D
Q
D
Q
C
C
X
Q
D
clk
0
1
L1
L2
X
D
D passes through L1 to X
X
Clock = 0: L1 opaque L2 transparent
D
Q
D
Q
C
C
X
Q
D
clk
1
0
L1
L2
X
Q
X passes through L2 to Q
X
When CLK falls (10),
Q gets X, X cannot change
When CLK rises (01),
now X can change,
Q does not change
Notes: Master-Slave Flip Flop
- Outputs change only on falling edges
- Data is captured on rising edges
1 cycle delay
but works out perfectly – data for the next stage is ready 1 cycle ahead of time

## Slide 27: Edge-Triggered D Flip-Flop
D
Q
D
Q
C
C
clk
D
X
Q
X
Q
D
clk
1
L1
L2
D Flip-Flop
Edge-Triggered
Data captured when clock is high
Output changes only on falling edges
Notes: A=1, B=0

## Slide 28: Takeaway
Set-Reset (SR) Latch can store one bit and we can change the value of the stored bit. But, SR Latch has a forbidden state.
(Unclocked) D Latch can store and change a bit like an SR Latch while avoiding a forbidden state.
An Edge-Triggered D Flip-Flip (aka Master-Slave D Flip-Flip) stores one bit. The bit can be changed in a synchronized fashion on the edge of a clock signal.

## Slide 29: Next Goal
How do we store more than one bit, N bits?

## Slide 30: Registers
Register
D flip-flops in parallel
shared clock
extra clocked inputs: write_enable, reset, …
clk
D0
D3
D1
D2
4
4
4-bit
reg
clk

## Slide 31: Takeaway
Set-Reset (SR) Latch can store one bit and we can change the value of the stored bit. But, SR Latch has a forbidden state.
(Unclocked) D Latch can store and change a bit like an SR Latch while avoiding a forbidden state.
An Edge-Triggered D Flip-Flip (aka Master-Slave D Flip-Flip) stores one bit. The bit can be changed in a synchronized fashion on the edge of a clock signal.
An N-bit register stores N-bits. It is created with N D-Flip-Flops in parallel along with a shared clock.

## Slide 32: An Example: What will this circuit do?
4-bit
reg
Clk
Decoder
+1
4
4
4
16
4

## Slide 33: Decoder Example: 7-Segment LED
7-Segment LED
  photons emitted when electrons fall into holes
d7
d6
d5
d4
d3
d2
d1
d0
Notes: Previous slide would need to display up to 16, so would need a 16-segment LED decoder

## Slide 34: Decoder Example: 7-Segment LED Decoder
3 inputs
encode 0 – 7 in binary
7 outputs
one for each LED
7LED decode

## Slide 35: 7 Segment LED Decoder Implementation
b2 | b1 | b0 | d6 | d5 | d4 | d3 | d2 | d1 | d0
0 | 0 | 0 |  |  |  |  |  |  | 
0 | 0 | 1 |  |  |  |  |  |  | 
0 | 1 | 0 |  |  |  |  |  |  | 
0 | 1 | 1 |  |  |  |  |  |  | 
1 | 0 | 0 |  |  |  |  |  |  | 
1 | 0 | 1 |  |  |  |  |  |  | 
1 | 1 | 0 |  |  |  |  |  |  | 
1 | 1 | 1 |  |  |  |  |  |  | 
d0
d1
d2
d3
d4
d5
d6
b2 | b1 | b0 | d6 | d5 | d4 | d3 | d2 | d1 | d0
0 | 0 | 0 |  |  |  |  |  |  | 
0 | 0 | 1 |  |  |  |  |  |  | 
0 | 1 | 0 |  |  |  |  |  |  | 
0 | 1 | 1 |  |  |  |  |  |  | 
1 | 0 | 0 |  |  |  |  |  |  | 
1 | 0 | 1 |  |  |  |  |  |  | 
1 | 1 | 0 |  |  |  |  |  |  | 
1 | 1 | 1 |  |  |  |  |  |  | 

## Slide 36: Basic Building Blocks We have Seen
binary
encoder
2N
N
binary
decoder
N
2N
Multiplexor
N
M
N
N
N
N
. . .
0
1
2
2M-1

## Slide 37: Encoders
1
2
3
4
5
6
7
0
encoder
N
. . .
. . .
Log2(N) outputs wires
N Input wires
e.g. Voting:
Can only vote for one out of N
candidates, so N inputs.
But can encode vote efficiently
with binary encoding.
Notes: N possible inputs -> log2(N) wires to encode

## Slide 38: Example Encoder Truth Table
a
b
1
c
d
2
3
4
o1
A 3-bit
encoder
with 4 inputs for simplicity
a | b | c | d |  |  |  | 
0 | 0 | 0 | 0 |  |  |  | 
1 | 0 | 0 | 0 |  |  |  | 
0 | 1 | 0 | 0 |  |  |  | 
0 | 0 | 1 | 0 |  |  |  | 
0 | 0 | 0 | 1 |  |  |  | 
o0
o1
o2
Notes: Implementation . . .
assume 8 choices, exactly one mark detected

## Slide 39: Basic Building Blocks Example: Voting
Ballots
The 3410 optical scan
vote reader
machine
detect
enc
8
3
7
7LED decode

## Slide 40: Recap
We can now build interesting devices with sensors
  Using combinationial logic
We can also store data values (aka Sequential Logic)
  In state-holding elements
  Coupled with clocks

## Slide 41: Summary
We can now build interesting devices with sensors
  Using combinational logic
We can also store data values
  Stateful circuit elements (D Flip Flops, Registers, …)
  Clock to synchronize state changes