## Slide 1: Finite State Machines
Hakim Weatherspoon
CS 3410
Computer Science
Cornell University
The slides are the product of many rounds of teaching CS 3410 by Professors Weatherspoon, Bala, Bracy, and Sirer.

## Slide 2: Goals for Today
Finite State Machines (FSM)
  How do we design logic circuits with state?
  Types of FSMs: Mealy and Moore Machines
  Examples: Serial Adder and a Digital Door Lock

## Slide 3: Finite State Machines

## Slide 4: Next Goal
How do we design logic circuits with state?

## Slide 5: Finite State Machines
An electronic machine which has
  external inputs
  externally visible outputs
  internal state
Output and next state depend on
  inputs
  current state

## Slide 6: Abstract Model of FSM
Machine is
M = ( S, I, O,  )
S: Finite set of states
I: Finite set of inputs
O: Finite set of outputs
: State transition function
Next state depends on present input and present state

## Slide 7: Automata Model
Finite State Machine
  inputs from external world
  outputs to external world
  internal state
  combinational logic
Next State
Current State
Input
Output
Registers
Comb. Logic
Notes: Put sequential logic term on slide

## Slide 8: FSM Example
Legend
state
input/output
start state
A
B
C
D
down/on
up/off
down/on
down/off
up/off
down/off
up/off
up/off
Input: up or down
Output: on or off
States: A, B, C, or D

## Slide 9: FSM Example
Legend
state
input/output
start state
A
B
C
D
down/on
up/off
down/on
down/off
up/off
down/off
up/off
up/off
Input: = up or = down
Output: = on or = off
States: = A, = B, = C, or = D
Notes: Say left of slash is input and right is output

## Slide 10: FSM Example
Legend
S1S0
i0i1i2…/o0o1o2…
S1S0
00
01
10
11
1/1
0/0
1/1
1/0
0/0
1/0
0/0
0/0
Input: 0=up or 1=down
Output: 1=on or 0=off
States: 00=A, 01=B, 10=C, or 11=D

## Slide 11: Mealy Machine
General Case: Mealy Machine
Outputs and next state depend on both current state and input
Next State
Current State
Input
Output
Registers
Comb. Logic

## Slide 12: Moore Machine
Special Case: Moore Machine
Outputs depend only on current state
Next State
Current State
Input
Output
Registers
Comb. Logic
Comb. Logic

## Slide 13: Moore Machine FSM Example
Legend
state out
input
startout
A off
B on
C off
D off
down
up
down
down
up
up
down
up
Input: up or down
Output: on or off
States: A, B, C, or D
Notes: Also show a mealy machine

## Slide 14: Mealy Machine FSM Example
Legend
state
input/output
start state
A
B
C
D
down/on
up/off
down/on
down/off
up/off
up/off
down/off
up/off
Input: up or down
Output: on or off
States: A, B, C, or D

## Slide 15: Activity#2: Create a Logic Circuit for a Serial Adder
Add two infinite input bit streams
  streams are sent with least-significant-bit (lsb) first
  How many states are needed to represent FSM?
  Draw and Fill in FSM diagram
…10110
…01111
…00101
Strategy:
(1) Draw a state diagram (e.g. Mealy Machine)
(2) Write output and next-state tables
(3) Encode states, inputs, and outputs as bits
(4) Determine logic equations for next state and outputs
Sum: output
Notes: Ask as a clicker question

## Slide 16: FSM: State Diagram
states:
Inputs: ??? and ???
Output: ???
  .
…10110
…01111
…00101
Notes: Is this a mealy or moore machine, maybe clicker

## Slide 17: FSM: State Diagram
S0
S1
__/_
__/_
__/_
__/_
__/_
__/_
__/_
__/_
…10110
…01111
…00101
states:
Inputs: ??? and ???
Output: ???
  .
Notes: Is this a mealy or moore machine, maybe clicker

## Slide 18: FSM: State Diagram
?? | ?? | Current state | ? | Next state
(2) Write down all input and state combinations
S0
S1
__/_
__/_
__/_
__/_
__/_
__/_
__/_
__/_

## Slide 19: FSM: State Diagram
?? | ?? | Current state | ? | Next state
(3) Encode states, inputs, and outputs as bits
S0
S1
__/_
__/_
__/_
__/_
__/_
__/_
__/_
__/_

## Slide 20: FSM: State Diagram
?? | ?? | Current state | ? | Next state
(4) Determine logic equations for next state and outputs

## Slide 21: Example: Digital Door Lock
Digital Door Lock
Inputs:
  keycodes from keypad
  clock
Outputs:
  “unlock” signal
  display how many keys pressed so far

## Slide 22: Door Lock: Inputs
Assumptions:
  signals are synchronized to clock
  Password is B-A-B
K
A
B
K | A | B | Meaning
0 | 0 | 0 | Ø (no key)
1 | 1 | 0 | ‘A’ pressed
1 | 0 | 1 | ‘B’ pressed
Notes: How many states, another clicker question

## Slide 23: Door Lock: Outputs
Assumptions:
  High pulse on U unlocks door
U
D3D2D1D0
4
LED dec
8
Strategy:
(1) Draw a state diagram (e.g. Moore Machine)
(2) Write output and next-state tables
(3) Encode states, inputs, and outputs as bits
(4) Determine logic equations for next state and outputs

## Slide 24: Door Lock: Simplified State Diagram
(1) Draw a state diagram (e.g. Moore Machine)

## Slide 25: Door Lock: Simplified State Diagram
any
Cur. State | Output
(2) Write output and next-state tables

## Slide 26: Door Lock: Simplified State Diagram
G2
G3
”2”
”3”, U
Ø
“B”
any
else
Cur. State | Input | Next State
Cur. State | Input | Next State
(2) Write output and next-state tables

## Slide 27: Door Lock: Implementation
4
dec
3bit Reg
clk
U
D3-0
S2-0
S’2-0
S2-0
K
A
B
D3 | D2 | D1 | D0 | U
S2 | S1 | S0
(4) Determine logic equations for next state and outputs

## Slide 28: Door Lock: Implementation
4
dec
3bit Reg
clk
U
D3-0
S2-0
S’2-0
S2-0
K
A
B
S2 | S1 | S0 |  | S’2 | S’1 | S’0
K | A | B
(4) Determine logic equations for next state and outputs
Notes: Write down and compare S2’

## Slide 29: Door Lock: Implementation
4
dec
3bit Reg
clk
U
D3-0
S2-0
S’2-0
S2-0
K
A
B
Strategy:
(1) Draw a state diagram (e.g. Moore Machine)
(2) Write output and next-state tables
(3) Encode states, inputs, and outputs as bits
(4) Determine logic equations for next state and outputs

## Slide 30: Door Lock: Implementation
Strategy:
(1) Draw a state diagram (e.g. Moore Machine)
(2) Write output and next-state tables
(3) Encode states, inputs, and outputs as bits
(4) Determine logic equations for next state and outputs
Next State
Current State
Input
Output
Registers
Comb. Logic
Comb. Logic
Moore Machine

## Slide 31: Goals for today
Review
  Finite State Machines

## Slide 32: Summary
We can now build interesting devices with sensors
  Using combinational logic
We can also store data values
  Stateful circuit elements (D Flip Flops, Registers, …)
  State Machines or Ad-Hoc Circuits