## Slide 1: Memory
Hakim Weatherspoon
CS 3410
Computer Science
Cornell University
The slides are the product of many rounds of teaching CS 3410 by Professors Weatherspoon, Bala, Bracy, and Sirer.

## Slide 2: Goals for today
Memory
  CPU: Register Files (i.e. Memory w/in the CPU)
  Scaling Memory: Tri-state devices
  Cache: SRAM (Static RAM—random access memory)
  Memory: DRAM (Dynamic RAM)

## Slide 3: Last time: How do we store one bit
D Flip Flop stores 1 bit
Q
D
clk
Notes: Put a matching box around both

## Slide 4: Goal for today
How do we store results from ALU computations?

## Slide 5: Big Picture: Building a Processor
PC
imm
memory
target
offset
cmp
control
=?
new pc
memory
din
dout
addr
register file
inst
extend
+4
+4
A Single cycle processor
alu

## Slide 6: Big Picture: Building a Processor
PC
imm
memory
target
offset
cmp
control
=?
new pc
memory
din
dout
addr
register file
inst
extend
+4
+4
A Single cycle processor
alu

## Slide 7: Goal for today
How do we store results from ALU computations?
How do we use stored results in subsequent operations?
Register File
How does a Register File work? How do we design it?

## Slide 8: Register File
Register File
  N read/write registers
  Indexed by register number
Dual-Read-Port Single-Write-Port
32 x 32 Register File
QA
QB
DW
RW
RA
RB
W
32
32
32
1
5
5
5

## Slide 9: Register File
Recall: Register
D flip-flops in parallel
shared clock
extra clocked inputs: write_enable, reset, …
clk
D0
D3
D1
D2
4
4
4-bit
reg
clk
Notes: Put a matching box around both

## Slide 10: Register File
Recall: Register
D flip-flops in parallel
shared clock
extra clocked inputs: write_enable, reset, …
clk
D0
D3
D1
D2
32
32
32-bit
reg
clk
Notes: Put a matching box around both

## Slide 11: Register File
Register File
  N read/write registers
  Indexed by register number
How to write to one register in the register file?
  Need a decoder
Reg 0
….
Reg 30
Reg 31
Reg 1
5-to-32
decoder
5
RW
W
D
32
addi r1, r0, 10
00001
Notes: Ask class to describe/design a decoder?
How to distinguish a wrote from a read?

## Slide 12: Aside: 3-to-8 decoder truth table & circuit
i2 | i1 | i0 | o0 | o1 | o2 | o3 | o4 | o5 | o6 | o7
0 | 0 | 0 |  |  |  |  |  |  |  | 
0 | 0 | 1 |  |  |  |  |  |  |  | 
0 | 1 | 0 |  |  |  |  |  |  |  | 
0 | 1 | 1 |  |  |  |  |  |  |  | 
1 | 0 | 0 |  |  |  |  |  |  |  | 
1 | 0 | 1 |  |  |  |  |  |  |  | 
1 | 1 | 0 |  |  |  |  |  |  |  | 
1 | 1 | 1 |  |  |  |  |  |  |  | 
3-to-8
decoder
3
RW
…
001
Notes: Ask class to describe/design a decoder?
How to distinguish a wrote from a read?

## Slide 13: Aside: 3-to-8 decoder truth table & circuit
i2 | i1 | i0 | o0 | o1 | o2 | o3 | o4 | o5 | o6 | o7
0 | 0 | 0 | 1 |  |  |  |  |  |  | 
0 | 0 | 1 |  | 1 |  |  |  |  |  | 
0 | 1 | 0 |  |  | 1 |  |  |  |  | 
0 | 1 | 1 |  |  |  | 1 |  |  |  | 
1 | 0 | 0 |  |  |  |  | 1 |  |  | 
1 | 0 | 1 |  |  |  |  |  | 1 |  | 
1 | 1 | 0 |  |  |  |  |  |  | 1 | 
1 | 1 | 1 |  |  |  |  |  |  |  | 1
3-to-8
decoder
3
RW
…
001
i2
i1
i0
o0
i2
i1
i0
o5
Notes: Ask class to describe/design a decoder?
How to distinguish a wrote from a read?

## Slide 14: Register File
Register File
  N read/write registers
  Indexed by register number
How to read from two registers?
  Need a multiplexor
32
Reg 0
Reg 1
….
Reg 30
Reg 31
M
U
X
M
U
X
32
QA
32
QB
5
5
RB
RA
….
….
add r1, r0, r5
Notes: Ask class how do we select a register to read?
Ask class to describe/design a multiplexor?

## Slide 15: Register File
Register File
  N read/write registers
  Indexed by register number
Implementation:
  D flip flops to store bits
  Decoder for each write port
  Mux for each read port
32
Reg 0
Reg 1
….
Reg 30
Reg 31
M
U
X
M
U
X
32
QA
32
QB
5
5
RB
RA
….
….
5-to-32
decoder
5
RW
W
D
32

## Slide 16: Register File
Register File
  N read/write registers
  Indexed by register number
Implementation:
  D flip flops to store bits
  Decoder for each write port
  Mux for each read port
Dual-Read-Port Single-Write-Port
32 x 32 Register File
QA
QB
DW
RW
RA
RB
W
32
32
32
1
5
5
5

## Slide 17: Register File
Register File
  N read/write registers
  Indexed by register number
Implementation:
  D flip flops to store bits
  Decoder for each write port
  Mux for each read port
What happens if same register read and written during same clock cycle?
Notes: Is this a good clicker question

## Slide 18: Tradeoffs
Register File tradeoffs
  + Very fast (a few gate delays for
  both read and write)
  + Adding extra ports is
  straightforward
  – Doesn’t scale
  e.g. 32Mb register file with
  32 bit registers
  Need 32x 1M-to-1 multiplexor
  and 32x 20-to-1M decoder
  How many logic gates/transistors?
a
b
c
d
e
f
g
h
s2
s1
s0
8-to-1 mux
Notes: Need two transistors per input of a logic gate
How does a n-input Mux grow in transistors? 2n + 4 transistors per input.
e.g. 2^20 input Mux will have 2x20+4=44 transistors per input, so 44M total transistors.
20 = 1024 = 1k
220 = 1M
230 = 1G
240 = 1T

## Slide 19: Takeway
Register files are very fast storage (only a few gate delays), but does not scale to large memory sizes.

## Slide 20: Goals for today
Memory
  CPU: Register Files (i.e. Memory w/in the CPU)
  Scaling Memory: Tri-state devices
  Cache: SRAM (Static RAM—random access memory)
  Memory: DRAM (Dynamic RAM)

## Slide 21: Next Goal
How do we scale/build larger memories?

## Slide 22: Building Large Memories
Need a shared bus (or shared bit line)
  Many FlipFlops/outputs/etc. connected to single wire
  Only one output drives the bus at a time
  How do we build such a device?
S0
D0
shared line
S1
D1
S2
D2
S3
D3
S1023
D1023

## Slide 23: Tri-State Devices
E
E | D | Q
0 | 0 | z
0 | 1 | z
1 | 0 | 0
1 | 1 | 1
D
Q
Tri-State Buffers
  If enabled (E=1), then Q = D
  Otherwise, Q is not connected (z = high impedance)
Notes: z, z 0, 1

## Slide 24: Tri-State Devices
Q
Vsupply
Gnd
D
E
E | D | Q
0 | 0 | z
0 | 1 | z
1 | 0 | 0
1 | 1 | 1
D
Q
Tri-State Buffers
  If enabled (E=1), then Q = D
  Otherwise, Q is not connected (z = high impedance)
Notes: z, z 0, 1

## Slide 25: Tri-State Devices
D
Q
E
Vsupply
Gnd
D
E
E | D | Q
0 | 0 | z
0 | 1 | z
1 | 0 | 0
1 | 1 | 1
D
Q
Tri-State Buffers
  If enabled (E=1), then Q = D
  Otherwise, Q is not connected (z = high impedance)
Notes: z, z 0, 1

## Slide 26: Tri-State Devices
D
Q
E
Vsupply
Gnd
E
E | D | Q
0 | 0 | z
0 | 1 | z
1 | 0 | 0
1 | 1 | 1
D
Q
Tri-State Buffers
  If enabled (E=1), then Q = D
  Otherwise, Q is not connected (z = high impedance)
0
0
1
0
off
off
z
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
A | B | AND | NAND
0 | 0 | 0 | 1
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
Notes: z, z 0, 1

## Slide 27: Tri-State Devices
D
Q
E
Vsupply
Gnd
E
E | D | Q
0 | 0 | z
0 | 1 | z
1 | 0 | 0
1 | 1 | 1
D
Q
Tri-State Buffers
  If enabled (E=1), then Q = D
  Otherwise, Q is not connected (z = high impedance)
1
1
1
1
off
on
0
0
0
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
A | B | AND | NAND
0 | 0 | 0 | 1
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
0
Notes: z, z 0, 1

## Slide 28: Tri-State Devices
D
Q
E
Vsupply
Gnd
E
E | D | Q
0 | 0 | z
0 | 1 | z
1 | 0 | 0
1 | 1 | 1
D
Q
Tri-State Buffers
  If enabled (E=1), then Q = D
  Otherwise, Q is not connected (z = high impedance)
1
1
0
0
off
on
1
1
1
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
A | B | AND | NAND
0 | 0 | 0 | 1
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
1
Notes: z, z 0, 1

## Slide 29: Shared Bus
S0
D0
shared line
S1
D1
S2
D2
S3
D3
S1023
D1023

## Slide 30: Takeway
Register files are very fast storage (only a few gate delays), but does not scale to large memory sizes.
Tri-state Buffers allow scaling since multiple registers can be connected to a single output, while only one register actually drives the output.

## Slide 31: Goals for today
Memory
  CPU: Register Files (i.e. Memory w/in the CPU)
  Scaling Memory: Tri-state devices
  Cache: SRAM (Static RAM—random access memory)
  Memory: DRAM (Dynamic RAM)

## Slide 32: Next Goal
How do we build large memories?
Use similar designs as Tri-state Buffers to connect multiple registers to output line. Only one register will drive output line.
Notes: Tri-State buffers, plus we need denser designs.

## Slide 33: Memory
  Storage Cells + bus
  Inputs: Address, Data (for writes)
  Outputs: Data (for reads)
  Also need R/W signal (not shown)
  N address bits  2N words total
  M data bits  each word M bits
M
N
Address
Data
Notes: How many address bits are necessary for a 4M x 8 SRAM module? (i.e. 4M word lines that are each 8 bits wide)?

## Slide 34: Memory
  Storage Cells + bus
  Decoder selects a word line
  R/W selector determines access type
  Word line is then coupled to the data lines
Data
Address
Decoder
R/W
Notes: Essentially just D-Latches plus Tri-State Buffers
A decoder selects which line of memory to access
(i.e. word line)
A R/W selector determines the
type of access
That line is then coupled to
the data lines

## Slide 35: Memory
  Storage Cells + bus
  Decoder selects a word line
  R/W selector determines access type
  Word line is then coupled to the data lines
Din
8
Dout
8
22
Address
Chip Select
Write Enable
Output Enable
Memory
4M x 8
Notes: How many address bits are necessary for a 4M x 8 SRAM module? (i.e. 4M word lines that are each 8 bits wide)?

## Slide 36: Memory
E.g. How do we design
a 4 x 2 Memory Module?
(i.e. 4 word lines that are
each 2 bits wide)?
2-to-4
decoder
2
Address
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
Dout[1]
Dout[2]
Din[1]
Din[2]
enable
enable
enable
enable
enable
enable
enable
enable
0
1
2
3
Write Enable
Output Enable
4 x 2 SRAM
Notes: How many address bits are necessary for a 4 x 2 SRAM module? (i.e. 4 word lines that are each 2 bits wide)?

## Slide 37: Memory
2-to-4
decoder
2
Address
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
Dout[1]
Dout[2]
Din[1]
Din[2]
enable
enable
enable
enable
enable
enable
enable
enable
0
1
2
3
Write Enable
Output Enable
E.g. How do we design
a 4 x 2 Memory Module?
(i.e. 4 word lines that are
each 2 bits wide)?
Notes: How do we design a 4 x 2 SRAM Module?
Caption on B.9.1 is incorrect
Output enable is useful for connecting multiple memories to a single-output bus and using Output enable to determine which memory drives the bus.

## Slide 38: Memory
2-to-4
decoder
2
Address
Dout[1]
Dout[2]
Din[1]
Din[2]
enable
enable
enable
enable
enable
enable
enable
enable
0
1
2
3
Write Enable
Output Enable
E.g. How do we design
a 4 x 2 Memory Module?
(i.e. 4 word lines that are
each 2 bits wide)?
Word lines
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
Notes: How do we design a 4 x 2 SRAM Module?
Caption on B.9.1 is incorrect
Output enable is useful for connecting multiple memories to a single-output bus and using Output enable to determine which memory drives the bus.

## Slide 39: Memory
2-to-4
decoder
2
Address
Dout[1]
Dout[2]
Din[1]
Din[2]
enable
enable
enable
enable
enable
enable
enable
enable
0
1
2
3
Write Enable
Output Enable
E.g. How do we design
a 4 x 2 Memory Module?
(i.e. 4 word lines that are
each 2 bits wide)?
Bit lines
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
Notes: How do we design a 4 x 2 SRAM Module?
Caption on B.9.1 is incorrect
Output enable is useful for connecting multiple memories to a single-output bus and using Output enable to determine which memory drives the bus.

## Slide 40: iClicker Question
What’s your familiarity with memory (SRAM, DRAM)?
I’ve never heard of any of this.
I’ve heard the words SRAM and DRAM, but I have no idea what they are.
I know that DRAM means main memory.
I know the difference between SRAM and DRAM and where they are used in a computer system.

## Slide 41: SRAM Cell
Typical SRAM Cell
B
word line
bit line
Each cell stores one bit, and requires 4 – 8 transistors (6 is typical)
Pass-Through
Transistors
Notes: Typical
read access times for SRAMs in 2004 varied from about 2–4 ns for the fastest CMOS
parts, which tend to be somewhat smaller and narrower, to 8–20 ns for the typical
largest parts, which in 2004 had more than 32 million bits of data.

## Slide 42: SRAM Cell
Disabled (wordline = 0)
Typical SRAM Cell
B
word line
bit line
Each cell stores one bit, and requires 4 – 8 transistors (6 is typical)
Read:
pre-charge B and to Vsupply/2
pull word line high
cell pulls B or low, sense amp detects voltage difference
1
0
on
on
2) Enable (wordline = 1)
Pre-charge
B = Vsupply/2
off
off
3) Cell pulls B low
i.e. B = 0
Pre-charge
= Vsupply/2
3) Cell pulls high
i.e. = 1
Notes: Typical
read access times for SRAMs in 2004 varied from about 2–4 ns for the fastest CMOS
parts, which tend to be somewhat smaller and narrower, to 8–20 ns for the typical
largest parts, which in 2004 had more than 32 million bits of data.

## Slide 43: SRAM Cell
Disabled (wordline = 0)
Typical SRAM Cell
B
word line
bit line
Each cell stores one bit, and requires 4 – 8 transistors (6 is typical)
Read:
pre-charge B and to Vsupply/2
pull word line high
cell pulls B or low, sense amp detects voltage difference
Write:
pull word line high
drive B and to flip cell
1
0
on
on
1) Enable (wordline = 1)
off
off
2) Drive B high
i.e. B = 1
2) Drive low
i.e. = 0
1
0
→
→
Notes: Typical
read access times for SRAMs in 2004 varied from about 2–4 ns for the fastest CMOS
parts, which tend to be somewhat smaller and narrower, to 8–20 ns for the typical
largest parts, which in 2004 had more than 32 million bits of data.

## Slide 44: SRAM
2-to-4
decoder
2
Address
Dout[1]
Dout[2]
Din[1]
Din[2]
enable
enable
enable
enable
enable
enable
enable
enable
0
1
2
3
Write Enable
Output Enable
E.g. How do we design
a 4 x 2 SRAM Module?
(i.e. 4 word lines that are
each 2 bits wide)?
Word lines
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
Bit Line
Notes: How do we design a 4 x 2 SRAM Module?
Caption on B.9.1 is incorrect
Output enable is useful for connecting multiple memories to a single-output bus and using Output enable to determine which memory drives the bus.

## Slide 45: SRAM
2-to-4
decoder
2
Address
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
Dout[1]
Dout[2]
Din[1]
Din[2]
enable
enable
enable
enable
enable
enable
enable
enable
0
1
2
3
Write Enable
Output Enable
4 x 2 SRAM
E.g. How do we design
a 4 x 2 SRAM Module?
(i.e. 4 word lines that are
each 2 bits wide)?
Notes: Caption on B.9.1 is incorrect
Output enable is useful for connecting multiple memories to a single-output bus and using Output enable to determine which memory drives the bus.

## Slide 46: SRAM
22
Address
Dout
Din
Write Enable
Output Enable
4M x 8 SRAM
8
8
E.g. How do we design
a 4M x 8 SRAM Module?
(i.e. 4M word lines that
are each 8 bits wide)?
Chip Select
Notes: Caption on B.9.1 is incorrect
Output enable is useful for connecting multiple memories to a single-output bus and using Output enable to determine which memory drives the bus.

## Slide 47: SRAM
12
Address [21-10]
4k x
1024
SRAM
4k x
1024
SRAM
4k x
1024
SRAM
4k x
1024
SRAM
4k x
1024
SRAM
4k x
1024
SRAM
4k x
1024
SRAM
4k x
1024
SRAM
12 x
4096
decoder
mux
1024
mux
1024
mux
1024
mux
1024
mux
mux
1024
1024
mux
1024
mux
1024
Dout[7]
1
Dout[6]
1
Dout[5]
1
Dout[4]
1
Dout[3]
1
Dout[2]
1
Dout[1]
1
Dout[0]
1
Address [9-0]
10
4M x 8 SRAM
E.g. How do we design
a 4M x 8 SRAM Module?
Notes: Caption on B.9.1 is incorrect
Output enable is useful for connecting multiple memories to a single-output bus and using Output enable to determine which memory drives the bus.

## Slide 48: SRAM
12
Address [21-10]
4k x
1024
SRAM
4k x
1024
SRAM
4k x
1024
SRAM
4k x
1024
SRAM
4k x
1024
SRAM
4k x
1024
SRAM
4k x
1024
SRAM
4k x
1024
SRAM
Row
decoder
1024
1024
1024
1024
1024
1024
1024
1024
Address [9-0]
10
4M x 8 SRAM
column selector, sense amp, and I/O circuits
Shared Data Bus
Chip Select (CS)
R/W Enable
8
E.g. How do we design
a 4M x 8 SRAM Module?
Notes: Caption on B.9.1 is incorrect
Output enable is useful for connecting multiple memories to a single-output bus and using Output enable to determine which memory drives the bus.

## Slide 49: SRAM Modules and Arrays
A21-0
Bank 2
Bank 3
Bank 4
4M x 8 SRAM
4M x 8 SRAM
4M x 8 SRAM
4M x 8 SRAM
R/W
msb
lsb
CS
CS
CS
CS
Notes: 2, 3, or more step address decode
The first decoder generates the addresses for eight 4M x 4 arrays; then a set of multiplexors is used to select 1 bit from each 4-bit-wide array. This is a much easier design than a single-level decode that would need either an enormous decoder or a gigantic multiplexor. In practice, a modern SRAM of
this size would probably use an even larger number of blocks, each somewhat smaller.

## Slide 50: SRAM Summary
SRAM
A few transistors (~6) per cell
Used for working memory (caches)
But for even higher density…

## Slide 51: Dynamic RAM: DRAM
Dynamic-RAM (DRAM)
  Data values require constant refresh
Gnd
word line
bit line
Capacitor
Each cell stores one bit, and requires 1 transistors
Notes: value kept in a cell is stored as a charge in a capacitor
To refresh the cell, we merely read its contents and write it back.
Because DRAMs store the charge on a capacitor, it cannot be kept indefinitely and must periodically be refreshed. That is why this memory structure is called dynamic, as opposed to the static storage in an SRAM cell.
The pass transistor acts like a switch: when the signal on the word line is asserted, the switch is closed (on), connecting the capacitor to the bit line. If the operation is a write, then the value to be written is placed on the bit line. If the value is a 1, the capacitor will be charged. If the value is a 0, then the capacitor will be discharged. Reading is slightly more complex, since the DRAM must detect a very small charge stored in the capacitor. Before activating the word line for a read, the bit line is charged to the voltage that is halfway between the low and high voltage. Then, by activating the word line, the charge on the capacitor is read out onto the bit line. This causes the bit line to move slightly toward the high or low direction, and this change is detected with a sense amplifier, which can detect small changes in voltage.

## Slide 52: Dynamic RAM: DRAM
Dynamic-RAM (DRAM)
  Data values require constant refresh
Gnd
word line
bit line
Capacitor
Pass-Through
Transistors
Each cell stores one bit, and requires 1 transistors
Notes: value kept in a cell is stored as a charge in a capacitor
To refresh the cell, we merely read its contents and write it back.
Because DRAMs store the charge on a capacitor, it cannot be kept indefinitely and must periodically be refreshed. That is why this memory structure is called dynamic, as opposed to the static storage in an SRAM cell.
The pass transistor acts like a switch: when the signal on the word line is asserted, the switch is closed, connecting the capacitor to the bit line. If the operation is a write, then the value to be written is placed on the bit line. If the value is a 1, the capacitor will be charged. If the value is a 0, then the capacitor will be discharged. Reading is slightly more complex, since the DRAM must detect a very small charge stored in the capacitor. Before activating the word line for a read, the bit line is charged to the voltage that is halfway between the low and high voltage. Then, by activating the word line, the charge on the capacitor is read out onto the bit line. This causes the bit line to move slightly toward the high or low direction, and this change is detected with a sense amplifier, which can detect small changes in voltage.

## Slide 53: Dynamic RAM: DRAM
on
Dynamic-RAM (DRAM)
Gnd
word line
bit line
Capacitor
Disabled (wordline = 0)
Each cell stores one bit, and requires 1 transistors
Read:
pre-charge B and to Vsupply/2
pull word line high
cell pulls B low, sense amp detects voltage difference
0
2) Enable (wordline = 1)
Pre-charge
B = Vsupply/2
off
3) Cell pulls B low
i.e. B = 0
Notes: value kept in a cell is stored as a charge in a capacitor
To refresh the cell, we merely read its contents and write it back.
Because DRAMs store the charge on a capacitor, it cannot be kept indefinitely and must periodically be refreshed. That is why this memory structure is called dynamic, as opposed to the static storage in an SRAM cell.
The pass transistor acts like a switch: when the signal on the word line is asserted, the switch is closed (on), connecting the capacitor to the bit line. If the operation is a write, then the value to be written is placed on the bit line. If the value is a 1, the capacitor will be charged. If the value is a 0, then the capacitor will be discharged. Reading is slightly more complex, since the DRAM must detect a very small charge stored in the capacitor. Before activating the word line for a read, the bit line is charged to the voltage that is halfway between the low and high voltage. Then, by activating the word line, the charge on the capacitor is read out onto the bit line. This causes the bit line to move slightly toward the high or low direction, and this change is detected with a sense amplifier, which can detect small changes in voltage.

## Slide 54: Dynamic RAM: DRAM
Dynamic-RAM (DRAM)
on
Gnd
word line
bit line
Capacitor
Disabled (wordline = 0)
Each cell stores one bit, and requires 4 – 8 transistors (6 is typical)
Read:
pre-charge B and to Vsupply/2
pull word line high
cell pulls B or low, sense amp detects voltage difference
Write:
pull word line high
drive B charges capacitor
0
1) Enable (wordline = 1)
off
2) Drive B high
i.e. B = 1
Charges capacitor
1
→
Notes: value kept in a cell is stored as a charge in a capacitor
To refresh the cell, we merely read its contents and write it back.
Because DRAMs store the charge on a capacitor, it cannot be kept indefinitely and must periodically be refreshed. That is why this memory structure is called dynamic, as opposed to the static storage in an SRAM cell.
The pass transistor acts like a switch: when the signal on the word line is asserted, the switch is closed, connecting the capacitor to the bit line. If the operation is a write, then the value to be written is placed on the bit line. If the value is a 1, the capacitor will be charged. If the value is a 0, then the capacitor will be discharged. Reading is slightly more complex, since the DRAM must detect a very small charge stored in the capacitor. Before activating the word line for a read, the bit line is charged to the voltage that is halfway between the low and high voltage. Then, by activating the word line, the charge on the capacitor is read out onto the bit line. This causes the bit line to move slightly toward the high or low direction, and this change is detected with a sense amplifier, which can detect small changes in voltage.

## Slide 55: DRAM vs. SRAM
Single transistor vs. many gates
  Denser, cheaper ($30/1GB vs. $30/2MB)
  But more complicated, and has analog sensing
Also needs refresh
  Read and write back…
  …every few milliseconds
  Organized in 2D grid, so can do rows at a time
  Chip can do refresh internally
Hence… slower and energy inefficient

## Slide 56: Memory
Register File tradeoffs
  + Very fast (a few gate delays for both read and write)
  + Adding extra ports is straightforward
  – Expensive, doesn’t scale
  – Volatile
Volatile Memory alternatives: SRAM, DRAM, …
  – Slower
  + Cheaper, and scales well
  – Volatile
  Non-Volatile Memory (NV-RAM): Flash, EEPROM, …
  + Scales well
  – Limited lifetime; degrades after 100000 to 1M writes

## Slide 57: Summary
We now have enough building blocks to build machines that can perform non-trivial computational tasks
Register File: Tens of words of working memory
SRAM: Millions of words of working memory
DRAM: Billions of words of working memory
NVRAM: long term storage (usb fob, solid state disks, BIOS, …)
Next time we will build a simple processor!