## Slide 1: The MIPS Processor
Hakim Weatherspoon
CS 3410
Computer Science
Cornell University
The slides are the product of many rounds of teaching CS 3410 by Professors Weatherspoon, Bala, Bracy, and Sirer.
Notes: Old See P&H Chapter 2.16-20, 4.1-4

## Slide 2: Announcements
Project Partner finding assignment on CMS
Practice C programming assignment
No official office hours over break

## Slide 3: Announcements
Make sure to go to your Lab Section this week
Lab3 due in class this week (it is not homework)
Proj1: Completed Proj1 due this Friday, Feb 16th, before winter break
Note, a Design Document is due when you submit Proj1 final circuit
Work alone
Save your work!
  Save often. Verify file is non-zero. Periodically save to Dropbox, email.
  Beware of MacOSX 10.5 (leopard) and 10.6 (snow-leopard)
C programming assignment is out
Due Monday, February 26th
Office Hours for help
Work alone
Work alone, BUT use your resources
  Lab Section, Piazza.com, Office Hours
  Class notes, book, Sections, CSUGLab

## Slide 4: Announcements
Check online syllabus/schedule
  http://www.cs.cornell.edu/Courses/CS3410/2018sp/schedule
Slides and Reading for lectures
Office Hours
Pictures of all TAs
Dates to keep in Mind
  Prelims: Thur Mar 15th and Thur May 3rd
  Proj 1: Due this Friday, Feb 16th before Winter break
  Proj3: Due before Spring break
  Final Project: Due when final would be Feb 15th
Schedule is subject to change

## Slide 5: Collaboration, Late, Re-grading Policies
“White Board” Collaboration Policy
  Can discuss approach together on a “white board”
  Leave, watch a movie such as Stranger Things, then write up solution independently
  Do not copy solutions
  Late Policy
  Each person has a total of four “slip days”
  Max of two slip days for any individual assignment
  Slip days deducted first for any late assignment,
  cannot selectively apply slip days
  For projects, slip days are deducted from all partners
  25% deducted per day late after slip days are exhausted
  Regrade policy
  Submit written request within a week of receiving score

## Slide 6: Big Picture: Building a Processor
PC
imm
memory
target
offset
cmp
control
=?
new pc
memory
din
dout
addr
register file
inst
extend
+4
+4
A Single cycle processor
alu

## Slide 7: Goal for the next 2 lectures
Understanding the basics of a processor
  We now have the technology to build a CPU!
Putting it all together:
  Arithmetic Logic Unit (ALU)
  Register File
  Memory
    SRAM: cache
    DRAM: main memory
  MIPS Instructions & how they are executed

## Slide 8: MIPS Register File
PC
imm
memory
target
offset
cmp
control
=?
new pc
memory
din
dout
addr
register file
inst
extend
+4
+4
A Single cycle processor
alu

## Slide 9: MIPS Register File
MIPS register file
  32 registers, 32-bits each
  r0 wired to zero
  Write port indexed via RW
    on falling edge when WE=1
  Read ports indexed via RA, RB
Dual-Read-Port Single-Write-Port
32 x 32 Register File
QA
QB
DW
RW
RA
RB
WE
32
32
32
1
5
5
5

## Slide 10: MIPS Register File
MIPS register file
  32 registers, 32-bits each
  r0 wired to zero
  Write port indexed via RW
    on falling edge when WE=1
  Read ports indexed via RA, RB
MIPS register file
  Numbered from 0 to 31.
  Can be referred by number: $0, $1, $2, … $31
  Convention, each register also has a name:
    $16 - $23  $s0 - $s7, $8 - $15  $t0 - $t7
    [P&H p105]
A
B
W
RW
RA
RB
WE
32
32
32
1
5
5
5
r0
r1
…
r31

## Slide 11: iClicker Question
If we wanted to support 64 registers, what would change?
  W, A, B → 64
  RW, Ra, Rb 5 → 6
  W 32 → 64, Rw 5 → 6
  A & B only
A
B
W
RW
RA
RB
WE
32
32
32
1
5
5
5
r0
r1
…
r31

## Slide 12: iClicker Question
If we wanted to support 64 registers, what would change?
  W, A, B → 64
  RW, Ra, Rb 5 → 6
  W 32 → 64, Rw 5 → 6
  A & B only
A
B
W
RW
RA
RB
WE
32
32
32
1
5
5
5
r0
r1
…
r31

## Slide 13: MIPS Memory
PC
imm
memory
target
offset
cmp
control
=?
new pc
memory
din
dout
addr
register file
inst
extend
+4
+4
A Single cycle processor
alu

## Slide 14: MIPS Memory
32-bit address
32-bit data (but byte addressed)
Enable + 2 bit memory control (mc)
  00: read word (4 byte aligned)
  01: write byte
  10: write halfword (2 byte aligned)
  11: write word (4 byte aligned)
memory
32
addr
2
mc
32
32
E
Din
Dout
 | 0xffffffff
 | . . .
 | 0x0000000b
 | 0x0000000a
 | 0x00000009
 | 0x00000008
 | 0x00000007
 | 0x00000006
 | 0x00000005
 | 0x00000004
 | 0x00000003
 | 0x00000002
 | 0x00000001
 | 0x00000000
0x05
1 byte
address

## Slide 15: Putting it all together: Basic Processor
PC
imm
memory
target
offset
cmp
control
=?
new pc
memory
din
dout
addr
register file
inst
extend
+4
+4
A Single cycle processor
alu
Notes: A processor executes instructions
  Processor has some internal state in storage elements (registers)
A memory holds instructions and data
  Harvard architecture: separate insts and data
  von Neumann architecture: combined inst and data
A bus connects the two

## Slide 16: To make a computer
Need a program
Stored program computer
Architectures
von Neumann architecture
Harvard (modified) architecture
Notes: A stored-program computer is one which stores program instructions in electronic memory. Often the definition is extended with the requirement that the treatment of programs and data in

## Slide 17: To make a computer
Need a program
Stored program computer
(a Universal Turing Machine)
Architectures
von Neumann architecture
Harvard (modified) architecture
Notes: A stored-program computer is one which stores program instructions in electronic memory. Often the definition is extended with the requirement that the treatment of programs and data in
http://en.wikipedia.org/wiki/Universal_Turing_machine#Stored-program_computer
Davis makes a persuasive argument that Turing's conception of what is now known as "the stored-program computer", of placing the "action table"—the instructions for the machine—in the same "memory" as the input data, strongly influenced John von Neumann's conception of the first American discrete-symbol (as opposed to analog) computer—the EDVAC (Electronic Discrete Variable Automatic Computer) [previous machine, ENIAC (Electronic Numerical Integrator And Computer), was not a stored-program computer, and was not even in binary, it was in decimal].
See video on von Neumann describe the stored-program computer, 34 minutes into video, https://www.youtube.com/watch?v=VTS9O0CoVng
Also, see clip on Turing in the movie The Imitation Game where Turing states that the Bombe will work in breaking the Enigma machine: https://www.youtube.com/watch?v=MM47hsaYWZE

## Slide 18: Putting it all together: Basic Processor
A MIPS CPU with a (modified) Harvard architecture
  Modified: instructions & data in common address space, separate instr/data caches can be accessed in parallel
CPU
Registers
Data Memory
data, address,
control
ALU
Control
00100000001
00100000010
00010000100
...
Program Memory
10100010000
10110000011
00100010101
...
Notes: The Harvard architecture is a computer architecture with physically separate storage and signal pathways for instructions and data. --- http://en.wikipedia.org/wiki/Harvard_architecture
Under pure von Neumann architecture the CPU can be either reading an instruction or reading/writing data from/to the memory. Both cannot occur at the same time since the instructions and data use the same bus system. In a computer using the Harvard architecture, the CPU can both read an instruction and perform a data memory access at the same time, even without a cache. A Harvard architecture computer can thus be faster for a given circuit complexity because instruction fetches and data access do not contend for a single memory pathway .
Also, a Harvard architecture machine has distinct code and data address spaces: instruction address zero is not the same as data address zero. Instruction address zero might identify a twenty-four bit value, while data address zero might indicate an eight bit byte that isn't part of that twenty-four bit value.
A modified Harvard architecture machine is very much like a Harvard architecture machine, but it relaxes the strict separation between instruction and data while still letting the CPU concurrently access two (or more) memory buses. The most common modification includes separate instruction and data caches backed by a common address space. While the CPU executes from cache, it acts as a pure Harvard machine. When accessing backing memory, it acts like a von Neumann machine (where code can be moved around like data, a powerful technique). This modification is widespread in modern processors such as the ARM architecture and X86 processors. It is sometimes loosely called a Harvard architecture, overlooking the fact that it is actually "modified".

## Slide 19: Takeaway
A processor executes instructions
  Processor has some internal state in storage elements (registers)
A memory holds instructions and data
  (modified) Harvard architecture: separate insts and data
  von Neumann architecture: combined inst and data
A bus connects the two
  We now have enough building blocks to build machines that can perform non-trivial computational tasks

## Slide 20: Next Goal
How to program and execute instructions on a MIPS processor?

## Slide 21: Instruction Usage
Instructions are stored in memory, encoded in binary
A basic processor
  fetches
  decodes
  executes
one instruction at a time
pc
adder
cur inst
decode
regs
execute
addr
data
00100000000000100000000000001010
00100000000000010000000000000000
00000000001000100001100000101010
op=addi r0 r2 10

## Slide 22: Instruction Processing
A basic processor
  fetches
  decodes
  executes
one instruction at a time
00100000000000100000000000001010
00100000000000010000000000000000
00000000001000100001100000101010
5
ALU
5
5
control
Reg. File
PC
Prog
Mem
inst
+4
Data
Mem
Instructions:
stored in memory, encoded in binary

## Slide 23: Levels of Interpretation: Instructions
High Level Language
  C, Java, Python, ADA, …
  Loops, control flow, variables
for (i = 0; i < 10; i++) printf(“go cucs”);
main: addi r2, r0, 10
addi r1, r0, 0
loop: slt r3, r1, r2
...
Assembly Language
  No symbols (except labels)
  One operation per statement
  “human readable machine language”
00100000000000100000000000001010
00100000000000010000000000000000
00000000001000100001100000101010
Machine Language
  Binary-encoded assembly
  Labels become addresses
  The language of the CPU
op=addi r0 r2 10
ALU, Control, Register File, …
Machine Implementation
(Microarchitecture)
Instruction Set Architecture

## Slide 24: Instruction Set Architecture (ISA)
Different CPU architectures specify different instructions
Two classes of ISAs
  Reduced Instruction Set Computers (RISC)
  IBM Power PC, Sun Sparc, MIPS, Alpha
  Complex Instruction Set Computers (CISC)
  Intel x86, PDP-11, VAX
Another ISA classification: Load/Store Architecture
  Data must be in registers to be operated on
  For example: array[x] = array[y] + array[z]
  1 add ? OR 2 loads, an add, and a store ?
  Keeps HW simple  many RISC ISAs are load/store

## Slide 25: iClicker Question
What does it mean for an architecture to be called a load/store architecture?
Load and Store instructions are supported by the ISA.
Load and Store instructions can also perform arithmetic instructions on data in memory.
Data must first be loaded into a register before it can be operated on.
Every load must have an accompanying store at some later point in the program.

## Slide 26: iClicker Question
What does it mean for an architecture to be called a load/store architecture?
Load and Store instructions are supported by the ISA.
Load and Store instructions can also perform arithmetic instructions on data in memory.
Data must first be loaded into a register before it can be operated on.
Every load must have an accompanying store at some later point in the program.

## Slide 27: Takeaway
A MIPS processor and ISA (instruction set architecture) is an example a Reduced Instruction Set Computers (RISC) where simplicity is key, thus enabling us to build it!!

## Slide 28: Next Goal
How are instructions executed?
What is the general datapath to execute an instruction?

## Slide 29: Five Stages of MIPS Datapath
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
Fetch
Decode
Execute
Memory
WB
A Single cycle processor – this diagram is not 100% spatial

## Slide 30: Five Stages of MIPS datapath
Basic CPU execution loop
  Instruction Fetch
  Instruction Decode
  Execution (ALU)
  Memory Access
  Register Writeback

## Slide 31: Stage 1: Instruction Fetch
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
Fetch
Decode
Execute
Memory
WB
  Fetch 32-bit instruction from memory
  Increment PC = PC + 4

## Slide 32: Stage 2: Instruction Decode
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
Fetch
Decode
Execute
Memory
WB
  Gather data from the instruction
  Read opcode; determine instruction type, field lengths
  Read in data from register file
  (0, 1, or 2 reads for jump, addi, or add, respectively)

## Slide 33: Stage 3: Execution (ALU)
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
Fetch
Decode
Execute
Memory
WB
  Useful work done here (+, -, *, /), shift, logic operation, comparison (slt)
  Load/Store? lw $t2, 32($t3)  Compute address

## Slide 34: Stage 4: Memory access
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
Fetch
Decode
Execute
Memory
WB
  Used by load and store instructions only
  Other instructions will skip this stage
addr
Data
Data
R/W

## Slide 35: Stage 5: Writeback
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
Fetch
Decode
Execute
Memory
WB
  Write to register file
    For arithmetic ops, logic, shift, etc, load. What about stores?
  Update PC
    For branches, jumps

## Slide 36: iClicker Question
Which of the following statements is true?
All instructions require an access to Program Memory.
All instructions require an access to Data Memory.
All instructions write to the register file.
Some MIPS instructions are shorter than 32 bits.
A & C

## Slide 37: iClicker Question
Which of the following statements is true?
All instructions require an access to Program Memory.
All instructions require an access to Data Memory.
All instructions write to the register file.
Some MIPS instructions are shorter than 32 bits.
A & C

## Slide 38: Takeaway
The datapath for a MIPS processor has five stages:
  Instruction Fetch
  Instruction Decode
  Execution (ALU)
  Memory Access
  Register Writeback
This five stage datapath is used to execute all MIPS instructions

## Slide 39: Next Goal
Specific datapaths MIPS Instructions

## Slide 40: MIPS Design Principles
Simplicity favors regularity
  32 bit instructions
Smaller is faster
  Small register file
Make the common case fast
  Include support for constants
Good design demands good compromises
  Support for different type of interpretations/classes

## Slide 41: Instruction Types
Arithmetic
  add, subtract, shift left, shift right, multiply, divide
Memory
  load value from memory to a register
  store value to memory from a register
Control flow
  unconditional jumps
  conditional jumps (branches)
  jump and link (subroutine call)
Many other instructions are possible
  vector add/sub/mul/div, string operations
  manipulate coprocessor
  I/O

## Slide 42: MIPS Instruction Types
Arithmetic/Logical
  R-type: result and two source registers, shift amount
  I-type: 16-bit immediate with sign/zero extension
Memory Access
  I-type
  load/store between registers and memory
  word, half-word and byte operations
Control flow
  J-type: fixed offset jumps, jump-and-link
  R-type: register absolute jumps
  I-type: conditional branches: pc-relative addresses

## Slide 43: MIPS instruction formats
All MIPS instructions are 32 bits long, has 3 formats
R-type
I-type
J-type
op | rs | rt | rd | shamt | func
6 bits | 5 bits | 5 bits | 5 bits | 5 bits | 6 bits
op | rs | rt | immediate
6 bits | 5 bits | 5 bits | 16 bits
op | immediate (target address)
6 bits | 26 bits

## Slide 44: R-Type (1): Arithmetic and Logic
op | rs | rt | rd | - | func
6 | 5 | 5 | 5 | 5 | 6 bits
op | func | mnemonic | description
0x0 | 0x21 | ADDU rd, rs, rt | R[rd] = R[rs] + R[rt]
0x0 | 0x23 | SUBU rd, rs, rt | R[rd] = R[rs] – R[rt]
0x0 | 0x25 | OR rd, rs, rt | R[rd] = R[rs] ¦ R[rt]
0x0 | 0x26 | XOR rd, rs, rt | R[rd] = R[rs]  R[rt]
0x0 | 0x27 | NOR rd, rs rt | R[rd] = ~ ( R[rs] ¦ R[rt] )
00000001000001100010000000100110

## Slide 45: R-Type (1): Arithmetic and Logic
op | rs | rt | rd | - | func
6 | 5 | 5 | 5 | 5 | 6 bits
op | func | mnemonic | description
0x0 | 0x21 | ADDU rd, rs, rt | R[rd] = R[rs] + R[rt]
0x0 | 0x23 | SUBU rd, rs, rt | R[rd] = R[rs] – R[rt]
0x0 | 0x25 | OR rd, rs, rt | R[rd] = R[rs] ¦ R[rt]
0x0 | 0x26 | XOR rd, rs, rt | R[rd] = R[rs]  R[rt]
0x0 | 0x27 | NOR rd, rs rt | R[rd] = ~ ( R[rs] ¦ R[rt] )
00000001000001100010000000100110
Example: r4 = r8  r6 # XOR r4, r8, r6
rd, rs, rt

## Slide 46: Arithmetic and Logic
ALU
PC
Prog.
Mem
+4
5
5
5
Reg. File
control
Fetch
Decode
Execute
WB
Memory
skip
r4
XOR
r8
r6
r8  r6
Example: r4 = r8  r6 # XOR r4, r8, r6

## Slide 47: R-Type (2): Shift Instructions
op | - | rt | rd | shamt | func
6 | 5 | 5 | 5 | 5 | 6 bits
op | func | mnemonic | description
0x0 | 0x0 | SLL rd, rt, shamt | R[rd] = R[rt] << shamt
0x0 | 0x2 | SRL rd, rt, shamt | R[rd] = R[rt] >>> shamt (zero ext.)
0x0 | 0x3 | SRA rd, rt, shamt | R[rd] = R[rt] >> shamt (sign ext.)
00000000000001000100000110000000

## Slide 48: R-Type (2): Shift Instructions
op | - | rt | rd | shamt | func
6 | 5 | 5 | 5 | 5 | 6 bits
op | func | mnemonic | description
0x0 | 0x0 | SLL rd, rt, shamt | R[rd] = R[rt] << shamt
0x0 | 0x2 | SRL rd, rt, shamt | R[rd] = R[rt] >>> shamt (zero ext.)
0x0 | 0x3 | SRA rd, rt, shamt | R[rd] = R[rt] >> shamt (sign ext.)
00000000000001000100000110000000
Example: r8 = r4 * 64 # SLL r8, r4, 6
r8 = r4 << 6

## Slide 49: Shift
5
ALU
5
5
Reg. File
PC
Prog.
Mem
+4
control
Fetch
Decode
Execute
Memory
WB
skip
r8
SLL
r4
6
r4 << 6
Example: r8 = r4 * 64 # SLL r8, r4, 6
r8 = r4 << 6

## Slide 50: I-Type (1): Arithmetic w/immediates
op | mnemonic | description
0x9 | ADDIU rd, rs, imm | R[rd] = R[rs] + imm)
0xc | ANDI rd, rs, imm | R[rd] = R[rs] & zero_extend(imm)
0xd | ORI rd, rs, imm | R[rd] = R[rs] ¦ zero_extend(imm)
op | rs | rd | immediate
6 | 5 | 5 | 16 bits
00100100101001010000000000000101

## Slide 51: I-Type (1): Arithmetic w/immediates
op | mnemonic | description
0x9 | ADDIU rd, rs, imm | R[rd] = R[rs] + imm
0xc | ANDI rd, rs, imm | R[rd] = R[rs] & imm
0xd | ORI rd, rs, imm | R[rd] = R[rs] ¦ imm
op | rs | rd | immediate
6 | 5 | 5 | 16 bits
00100100101001010000000000000101
r5 += -1
r5 += 65535
Example: r5 = r5 + 5 # ADDIU r5, r5, 5
r5 += 5
What if immediate is negative?
Unsigned means no overflow detection.
The immediate can be negative!
op | mnemonic | description
0x9 | ADDIU rd, rs, imm | R[rd] = R[rs] + sign_extend(imm)
0xc | ANDI rd, rs, imm | R[rd] = R[rs] & zero_extend(imm)
0xd | ORI rd, rs, imm | R[rd] = R[rs] ¦ zero_extend(imm)

## Slide 52: Arithmetic w/immediates
5
imm
5
5
extend
+4
shamt
Reg. File
PC
Prog.
Mem
ALU
control
Fetch
Decode
Execute
Memory
WB
skip
Example: r5 = r5 + 5 # ADDIU r5, r5, 5
16
32

## Slide 53: Arithmetic w/immediates
5
imm
5
5
extend
+4
shamt
Reg. File
PC
Prog.
Mem
ALU
control
Fetch
Decode
Execute
Memory
WB
skip
Example: r5 = r5 + 5 # ADDIU r5, r5, 5
16
32

## Slide 54: Arithmetic w/immediates
5
imm
5
5
extend
+4
shamt
Reg. File
PC
Prog.
Mem
ALU
control
Example: r5 = r5 + 5 # ADDIU r5, r5, 5
Fetch
Decode
Execute
Memory
WB
skip
r5
ADDIU
r5
5
r5 + 5
16
32

## Slide 55: I-Type (2): Load Upper Immediate
op | mnemonic | description
0xF | LUI rd, imm | R[rd] = imm << 16
op | - | rd | immediate
6 | 5 | 5 | 16 bits
00111100000001010000000000000101
Example: LUI r5, 0xdead
ORI r5, r5 0xbeef
What does r5 = ?
example: r5 = 0x50000 # LUI r5, 5
WORST
NAME
EVER !
“
”

## Slide 56: I-Type (2): Load Upper Immediate
op | mnemonic | description
0xF | LUI rd, imm | R[rd] = imm << 16
op | - | rd | immediate
6 | 5 | 5 | 16 bits
00111100000001010000000000000101
Example: LUI r5, 0xdead
ORI r5, r5 0xbeef
What does r5 = 0xdeadbeef
Example: r5 = 0x50000 # LUI r5, 5
WORST
NAME
EVER !
“
”

## Slide 57: Load Upper Immediate
5
imm
5
5
extend
+4
shamt
Reg. File
PC
Prog.
Mem
ALU
control
Fetch
Decode
Execute
Memory
WB
skip
Example: r5 = 0x50000 # LUI r5, 5
32
16
Notes: or, extra input to alu B mux from before/after extend
(or, extra mux after alu)

## Slide 58: Load Upper Immediate
5
imm
5
5
extend
+4
shamt
Reg. File
PC
Prog.
Mem
ALU
16
control
Example: r5 = 0x50000 # LUI r5, 5
Fetch
Decode
Execute
Memory
WB
skip
r5
LUI
5
0x50000
32
16
Notes: or, extra input to alu B mux from before/after extend
(or, extra mux after alu)

## Slide 59: MIPS Instruction Types
Arithmetic/Logical
  R-type: result and two source registers, shift amount
  I-type: 16-bit immediate with sign/zero extension
Memory Access
  I-type
  load/store between registers and memory
  word, half-word and byte operations
Control flow
  J-type: fixed offset jumps, jump-and-link
  R-type: register absolute jumps
  I-type: conditional branches: pc-relative addresses

## Slide 60: Memory Layout Options
# r5 contains 5 (0x00000005)
SB r5, 0(r0)
SB r5, 2(r0)
SW r5, 8(r0)
Two ways to store a word in memory.
 | 0xffffffff
 | ...
 | 0x0000000b
 | 0x0000000a
 | 0x00000009
 | 0x00000008
 | 0x00000007
 | 0x00000006
 | 0x00000005
 | 0x00000004
 | 0x00000003
 | 0x00000002
 | 0x00000001
 | 0x00000000
Notes: Big Endian means store MSB (most significant byte) first

## Slide 61: Little Endian
Endianness: Ordering of bytes within a memory word
1000 | 1001 | 1002 | 1003
0x12345678
Little Endian = least significant part first (MIPS, x86)
as 4 bytes
as 2 halfwords
as 1 word
Clicker Question: What values go in the byte-sized boxes with addresses 1000 and 1001?
a) d)
b) e)
c)
0x8, 0x7
0x78, 0x56
0x1, 0x2
0x12, 0x34
0x87, 0x65
THIS IS WHAT YOUR PROJECTS WILL BE
Notes: Comes from Gulliver travels
Answer: B

## Slide 62: Little Endian
Endianness: Ordering of bytes within a memory word
1000 | 1001 | 1002 | 1003
0x12345678
Little Endian = least significant part first (MIPS, x86)
as 4 bytes
as 2 halfwords
as 1 word
Clicker Question: What values go in the byte-sized boxes with addresses 1000 and 1001?
a) d)
b) e)
c)
0x8, 0x7
0x78, 0x56
0x1, 0x2
0x12, 0x34
0x87, 0x65
THIS IS WHAT YOUR PROJECTS WILL BE
Notes: Comes from Gulliver travels
Answer: B

## Slide 63: Big Endian
Endianness: Ordering of bytes within a memory word
Big Endian = most significant part first (MIPS, networks)
1000 | 1001 | 1002 | 1003
0x12345678
as 4 bytes
as 2 halfwords
as 1 word
Clicker Question: What value goes in the half-word sized box with address 1000?
a) d)
b) e)
c)
0x1
0x12
0x5678
0x4321
0x1234
Notes: Comes from Gulliver travels
Answer: B

## Slide 64: Big Endian
Endianness: Ordering of bytes within a memory word
Big Endian = most significant part first (MIPS, networks)
1000 | 1001 | 1002 | 1003
0x12345678
as 4 bytes
as 2 halfwords
as 1 word
Clicker Question: What value goes in the half-word sized box with address 1000?
a) d)
b) e)
c)
0x1
0x12
0x5678
0x4321
0x1234
Notes: Comes from Gulliver travels
Answer: B

## Slide 65: Big Endian Memory Layout
 | 0xffffffff
 | ...
 | 0x0000000b
 | 0x0000000a
 | 0x00000009
 | 0x00000008
 | 0x00000007
 | 0x00000006
 | 0x00000005
 | 0x00000004
 | 0x00000003
 | 0x00000002
 | 0x00000001
 | 0x00000000
SB r5, 2(r0)
LB r6, 2(r0)
SW r5, 8(r0)
LB r7, 8(r0)
LB r8, 11(r0)
0x05
0x00
0x00
0x00
0x05
 | r0
 | ...
0x00000005 | r5
 | r6
 | r7
 | r8
0x00000005
0x00000000
0x00000005
Notes: Big Endian means store MSB (most significant byte) first

## Slide 66: I-Type (3): Memory Instructions
op | mnemonic | description
0x23 | LW rd, offset(rs) | R[rd] = Mem[offset+R[rs]]
0x2b | SW rd, offset(rs) | Mem[offset+R[rs]] = R[rd]
op | rs | rd | offset
6 | 5 | 5 | 16 bits
10101100101000010000000000000100

## Slide 67: I-Type (3): Memory Instructions
op | mnemonic | description
0x23 | LW rd, offset(rs) | R[rd] = Mem[offset+R[rs]]
0x2b | SW rd, offset(rs) | Mem[offset+R[rs]] = R[rd]
op | rs | rd | offset
6 | 5 | 5 | 16 bits
10101100101000010000000000000100
Example: = Mem[4+r5] = r1 # SW r1, 4(r5)
signed offsets
base + offset addressing

## Slide 68: Memory Operations
Data Mem
addr
ext
+4
5
imm
5
5
control
Reg. File
PC
Prog.
Mem
ALU
Example: = Mem[4+r5] = r1 # SW r1, 4(r5)
Write Enable

## Slide 69: Memory Operations
Data Mem
addr
ext
+4
5
imm
5
5
control
Reg. File
PC
Prog.
Mem
ALU
Write Enable
r1
SW
r5
4
r5+4
Example: = Mem[4+r5] = r1 # SW r1, 4(r5)

## Slide 70: More Memory Instructions
op | mnemonic | description
0x20 | LB rd, offset(rs) | R[rd] = sign_ext(Mem[offset+R[rs]])
0x24 | LBU rd, offset(rs) | R[rd] = zero_ext(Mem[offset+R[rs]])
0x21 | LH rd, offset(rs) | R[rd] = sign_ext(Mem[offset+R[rs]])
0x25 | LHU rd, offset(rs) | R[rd] = zero_ext(Mem[offset+R[rs]])
0x23 | LW rd, offset(rs) | R[rd] = Mem[offset+R[rs]]
0x28 | SB rd, offset(rs) | Mem[offset+R[rs]] = R[rd]
0x29 | SH rd, offset(rs) | Mem[offset+R[rs]] = R[rd]
0x2b | SW rd, offset(rs) | Mem[offset+R[rs]] = R[rd]
op | rs | rd | offset
6 | 5 | 5 | 16 bits
10101100101000010000000000000100
Notes: sw r1 4(r5)
sb r1, 3(r5)
If you don’t make sure half word accesses are half word aligned, or word accesses are word aligned, there will be an error signaled. We will talk about traps and exceptions later.

## Slide 71: MIPS Instruction Types
Arithmetic/Logical
  R-type: result and two source registers, shift amount
  I-type: 16-bit immediate with sign/zero extension
Memory Access
  I-type
  load/store between registers and memory
  word, half-word and byte operations
Control flow
  J-type: fixed offset jumps, jump-and-link
  R-type: register absolute jumps
  I-type: conditional branches: pc-relative addresses

## Slide 72: J-Type (1): Absolute Jump
00001001000000000000000000000001
op | immediate
6 | 26 bits
op | Mnemonic | Description
0x2 | J target | PC = (PC+4)31..28  target  00
““= concatenate
(PC+4)31..28 target 00
4 bits | 26 bits | 2 bits
(PC+4)31..28 01000000000000000000000001 00
MIPS Quirk:
  jump targets computed using already incremented PC
Notes: Where  is used to concatenate
Why should the offset be left shifted by 2. To keep the jump address word aligned.
AND to not waste two bits that we *know* are going to be 0.

## Slide 73: Absolute Jump
long jump? computed jump?
target
+4

Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
J
(PC+4)31..28 0x100000100
(PC+4)31..280x4000004
Example: PC = (PC+4)31..28  target  00 # J 0x1000001
ex: J 0x1000001
PC = ((PC+4) & 0xf0000000) | 0x04000004
26
32

## Slide 74: R-Type (3): Jump Register
op | rs | - | - | - | func
6 | 5 | 5 | 5 | 5 | 6 bits
00000000011000000000000000001000
op | func | mnemonic | description
0x0 | 0x08 | JR rs | PC = R[rs]
ex: JR r3

## Slide 75: Jump Register
+4

tgt
Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
op | func | mnemonic | description
0x0 | 0x08 | JR rs | PC = R[rs]
R[r3]
JR
ex: JR r3

## Slide 76: iClicker Question
What is a good trait about the Jump Register instruction?
Since registers are 32 bits, you can specify any address.
The address you’re jumping to is programmable. It doesn’t have to be hard-coded in the instruction because it lives in a register.
It allows you to jump to an instruction with an address ending in something other than 00, which is very useful.
Both A and B.
A, B, and C.

## Slide 77: iClicker Question
What is a good trait about the Jump Register instruction?
Since registers are 32 bits, you can specify any address.
The address you’re jumping to is programmable. It doesn’t have to be hard-coded in the instruction because it lives in a register.
It allows you to jump to an instruction with an address ending in something other than 00, which is very useful.
Both A and B.
A, B, and C.

## Slide 78: Moving Beyond Jumps
Can use Jump or Jump Register instruction to
jump to 0xabcd1234
What about a jump based on a condition?
# assume 0 <= r3 <= 1
if (r3 == 0) jump to 0xdecafe00
else jump to 0xabcd1234

## Slide 79: I-Type (4): Branches
op | mnemonic | description
0x4 | BEQ rs, rd, offset | if R[rs] == R[rd] then PC = PC+4 + (offset<<2)
0x5 | BNE rs, rd, offset | if R[rs] != R[rd] then PC = PC+4 + (offset<<2)
op | rs | rd | offset
6 | 5 | 5 | 16 bits
00010000101000010000000000000011
Notes: Why should the offset be left shifted by 2. To keep the jump address word aligned.
AND to not waste two bits that we *know* are going to be 0.

## Slide 80: I-Type (4): Branches
op | mnemonic | description
0x4 | BEQ rs, rd, offset | if R[rs] == R[rd] then PC = PC+4 + (offset<<2)
0x5 | BNE rs, rd, offset | if R[rs] != R[rd] then PC = PC+4 + (offset<<2)
op | rs | rd | offset
6 | 5 | 5 | 16 bits
00010000101000010000000000000011
Example: BEQ r5, r1, 3
if(R[r5]==R[r1])
PC = PC+4 + 12 (i.e. 12 == 3<<2)
A word about all these +’s…
signed
Notes: Why should the offset be left shifted by 2. To keep the jump address word aligned.
AND to not waste two bits that we *know* are going to be 0.

## Slide 81: Control Flow: Branches
tgt
+4

Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
offset
+
Could have used ALU for branch add
=?
op | mnemonic | description
0x4 | BEQ rs, rd, offset | if R[rs] == R[rd] then PC = PC+4 + (offset<<2)
0x5 | BNE rs, rd, offset | if R[rs] != R[rd] then PC = PC+4 + (offset<<2)
R[r5]
BEQ
R[r1]
Could have used ALU for branch cmp
ex: BEQ r5, r1, 3
(PC+4)+3<<2
Notes: In the book, the ALU is used to determine the branch comparison. We are choosing to do it separately.
Anyway, can’t use ALU for both branc comparison and PC determination. At most, we can use it once. The book uses it for branch

## Slide 82: I-Type (5): Conditional Jumps
op | rs | subop | offset
6 bits | 5 bits | 5 bits | 16 bits
00000100101000010000000000000010
op | subop | mnemonic | description
0x1 | 0x0 | BLTZ rs, offset | if R[rs] < 0 then PC = PC+4+ (offset<<2)
0x1 | 0x1 | BGEZ rs, offset | if R[rs] ≥ 0 then PC = PC+4+ (offset<<2)
0x6 | 0x0 | BLEZ rs, offset | if R[rs] ≤ 0 then PC = PC+4+ (offset<<2)
0x7 | 0x0 | BGTZ rs, offset | if R[rs] > 0 then PC = PC+4+ (offset<<2)
signed

## Slide 83: I-Type (5): Conditional Jumps
op | rs | subop | offset
6 bits | 5 bits | 5 bits | 16 bits
00000100101000010000000000000010
op | subop | mnemonic | description
0x1 | 0x0 | BLTZ rs, offset | if R[rs] < 0 then PC = PC+4+ (offset<<2)
0x1 | 0x1 | BGEZ rs, offset | if R[rs] ≥ 0 then PC = PC+4+ (offset<<2)
0x6 | 0x0 | BLEZ rs, offset | if R[rs] ≤ 0 then PC = PC+4+ (offset<<2)
0x7 | 0x0 | BGTZ rs, offset | if R[rs] > 0 then PC = PC+4+ (offset<<2)
Example: BGEZ r5, 2
if(R[r5] ≥ 0)
PC = PC+4 + 8 (i.e. 8 == 2<<2)
signed

## Slide 84: Control Flow: More Branches
tgt
+4

Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
offset
+
Could have used ALU for branch cmp
=?
cmp
R[r5]
BEQZ
ex: BGEZ r5, 2
(PC+4)+2<<2
op | subop | mnemonic | description
0x1 | 0x1 | BGEZ rs, offset | if R[rs] ≥ 0 then PC = PC+4+ (offset<<2)

## Slide 85: J-Type (2): Jump and Link
op | mnemonic | description
0x3 | JAL target | r31 = PC+8 (+8 due to branch delay slot) PC = (PC+4)31..28  target  00
op | immediate
6 bits | 26 bits
00001101000000000000000000000001
Discuss later
Function/procedure calls
Why?
Notes: 0x0121808 == 1185800

## Slide 86: Jump and Link
tgt
+4

Data Mem
addr
ext
5
5
5
Reg. File
PC
Prog.
Mem
ALU
inst
control
imm
offset
+
=?
cmp
Could have used ALU for link add
+4
op | mnemonic | description
0x3 | JAL target | r31 = PC+8 (+8 due to branch delay slot) PC = (PC+4)31..28  (target << 2)
R[r31]
PC+8
ex: JAL 0x1000001
r31 = PC+8
PC = (PC+4)31..28 0x4000004

## Slide 87: MIPS Instruction Types
Arithmetic/Logical
  R-type: result and two source registers, shift amount
  I-type: 16-bit immediate with sign/zero extension
Memory Access
  I-type
  load/store between registers and memory
  word, half-word and byte operations
Control flow
  J-type: fixed offset jumps, jump-and-link
  R-type: register absolute jumps
  I-type: conditional branches: pc-relative addresses
Many other instructions possible:
  vector add/sub/mul/div, string operations
  manipulate coprocessor
  I/O
  ✔
  ✔
  ✔

## Slide 88: iClicker Question
What MIPS instruction would you use for a:
1. For loop?
2. While loop?
3. Function call?
4. If statement?
5. Return statement?
Jump Absolute (J 0x000FFFF)
Jump Register (J r1)
Branch Equals (BEQ r1, r2, 0xAAAA)
Branch Less Than (BLT r1, r2, 0xAAAA)
Jump and Link (JAL 0x000FFFF)
Notes: Add a “leave the if clause” option next time.

## Slide 89: iClicker Question
What is the one topic you’re most uncertain about at this point in the class?
Gates & Logic
Circuit Simplification
Finite State Machines
MIPS Processor
MIPS Assembly

## Slide 90: Summary
We have all that it takes to build a processor!
  Arithmetic Logic Unit (ALU)
  Register File
  Memory
MIPS processor and ISA is an example of a Reduced Instruction Set Computers (RISC).
Simplicity is key, thus enabling us to build it!
We now know the data path for the MIPS ISA:
register, memory and control instructions