## Slide 1: Pipelining
Hakim Weatherspoon
CS 3410
Computer Science
Cornell University
The slides are the product of many rounds of teaching CS 3410 by Professors Weatherspoon, Bala, Bracy, McKee, and Sirer.

## Slide 2: Announcements
C Programming Practice Assignment due next Tuesday
Short. Do not wait till the end.
Project 2 design doc
Critical to do this, else Project 2 will be hard

## Slide 3
Single Cycle vs Pipelined Processor

## Slide 4: Review: Single Cycle Processor
alu
PC
imm
memory
memory
din
dout
addr
target
offset
cmp
control
=?
new pc
register file
inst
extend
+4
+4

## Slide 5: Review: Single Cycle Processor
Advantages
  Single cycle per instruction make logic and clock simple
Disadvantages
  Since instructions take different time to finish, memory and functional unit are not efficiently utilized
  Cycle time is the longest delay
    Load instruction
  Best possible CPI is 1 (actually < 1 w parallelism)
    However, lower MIPS and longer clock period (lower clock frequency); hence, lower performance

## Slide 6: The Kids
Alice
Bob
They don’t always get along…

## Slide 7: The Bicycle

## Slide 8: The Materials
Saw
Drill
Glue
Paint

## Slide 9: The Instructions
N pieces, each built following same sequence:
Saw
Drill
Glue
Paint

## Slide 10: Design 1: Sequential Schedule
Alice owns the room
Bob can enter when Alice is finished
Repeat for remaining tasks
No possibility for conflicts

## Slide 11: Sequential Performance
Elapsed Time for Alice: 4
Elapsed Time for Bob: 4
Total elapsed time: 4*N
Can we do better?
time 1 2 3 4 5 6 7 8 …
Latency:
Throughput:
Concurrency:
CPI =
Latency:
Throughput:
Concurrency:
CPI =
Notes: Latency = 4
CPI = 4 (here the instruction is the construction of the bike)
Throughput = 2 bikes in 8 hrs. So 1 task in 4 hrs. So ¼ throughput
Concurrency: 1 (i.e. 1 task at a time)

## Slide 12: Design 2: Pipelined Design
Partition room into stages of a pipeline
Alice
Bob
Carol
Dave
One person owns a stage at a time
4 stages
4 people working simultaneously
Everyone moves right in lockstep
It still takes all four stages for one job to complete

## Slide 13: Pipelined Performance
time 1 2 3 4 5 6 7…
What if some tasks don’t need drill?
Latency:
Throughput:
Concurrency:
Latency:
Throughput:
Concurrency:
CPI =
Notes: Latency (Delay): 4 cycles / task
Throughput: 1 task / cycle (huge improvement) after your initial startup of filling the pipeline.
Parallelism: 4 concurrent tasks

## Slide 14: Pipelined Performance
Time
1 2 3 4 5 6 7 8 9 10
What if some tasks don’t need drill?
Latency:
Throughput:
CPI =
What if drilling takes twice as long, but gluing and paint take ½ as long?
Notes: Now what if drilling is twice as long but the gluing and paint are ½ each.

## Slide 15: Lessons
Principle:
Throughput increased by parallel execution
Balanced pipeline very important
Else slowest stage dominates performance
Pipelining:
  Identify pipeline stages
  Isolate stages from each other
  Resolve pipeline hazards (next lecture)

## Slide 16
Single Cycle vs Pipelined Processor

## Slide 17: Single Cycle  Pipelining
insn0.fetch, dec, exec
Single-cycle
insn1.fetch, dec, exec
Pipelined
insn0.dec
insn0.fetch
insn1.dec
insn1.fetch
insn0.exec
insn1.exec

## Slide 18: Agenda
5-stage Pipeline
Implementation
Working Example
Hazards
Structural
Data Hazards
Control Hazards

## Slide 19: A Processor
alu
PC
imm
memory
memory
din
dout
addr
target
offset
cmp
control
=?
new pc
register file
inst
extend
+4
+4
Review: Single cycle processor

## Slide 20: A Processor
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
register file
control
alu
imm
memory
din
dout
addr
inst
PC
memory
compute jump/branch targets
new pc
+4
extend
Notes: What does that do to a clock cycle. It is the time for 1 stage. So 5 times faster in this case (ASSUMING all stages are approximately equal sized)
Left to right flow except for the write-back phase and the branch targets that can change the PC. Otherwise left to right.

## Slide 21: Pipelined Processor
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
compute jump/branch targets
+4
Fetch
Decode
Execute
Memory
WB

## Slide 22: Pipelined Processor
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4

## Slide 23: Time Graphs
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Cycle
Latency:
Throughput:
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
Latency:
Throughput:
Concurrency:
CPI =
add
nand
lw
add
sw
Notes: CPI = 1 (inverse of throughput)

## Slide 24: Principles of Pipelined Implementation
Break datapath into multiple cycles (here 5)
  Parallel execution increases throughput
  Balanced pipeline very important
    Slowest stage determines clock rate
    Imbalance kills performance
Add pipeline registers (flip-flops) for isolation
  Each stage begins by reading values from latch
  Each stage ends by writing values to latch
Resolve hazards

## Slide 25: Pipelined Processor
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4

## Slide 26: Pipeline Stages
  Next stage will read this pipeline register
  Anything needed by later pipeline stages
Stage | Perform Functionality | Latch values of interest
Fetch | Use PC to index Program Memory, increment PC | Instruction bits (to be decoded) PC + 4 (to compute branch targets)
Decode | Decode instruction, generate control signals, read register file | Control information, Rd index, immediates, offsets, register values (Ra, Rb), PC+4 (to compute branch targets)
Execute | Perform ALU operation Compute targets (PC+4+offset, etc.) in case this is a branch, decide if branch taken | Control information, Rd index, etc. Result of ALU operation, value in case this is a store instruction
Memory | Perform load/store if needed, address is ALU result | Control information, Rd index, etc. Result of load, pass result from execute
Writeback | Select value, write to register file | 

## Slide 27: Instruction Fetch (IF)
Stage 1: Instruction Fetch
Fetch a new instruction every cycle
  Current PC is index to instruction memory
  Increment the PC at end of cycle (assume no branches for now)
Write values of interest to pipeline register (IF/ID)
  Instruction bits (for later decoding)
  PC+4 (for later computing branch targets)
  Next stage will read this pipeline register
  Anything needed by later pipeline stages

## Slide 28: Instruction Fetch (IF)
PC
instruction memory
new pc
addr
mc
+4

## Slide 29: Decode
Stage 2: Instruction Decode
On every cycle:
  Read IF/ID pipeline register to get instruction bits
  Decode instruction, generate control signals
  Read from register file
Write values of interest to pipeline register (ID/EX)
  Control information, Rd index, immediates, offsets, …
  Contents of Ra, Rb
  PC+4 (for computing branch targets later)

## Slide 30: Decode
ctrl
ID/EX
Rest of pipeline
PC+4
inst
IF/ID
PC+4
Stage 1: Instruction Fetch
register file
WE
Rd
Ra
Rb
D
B
A
B
A
imm
Notes: Early decode: decode all instr in ID, pass control signals to later stages
Late decode: decode some instr in ID, pass instr so each stage computes its own control signals

## Slide 31: Execute (EX)
Stage 3: Execute
On every cycle:
  Read ID/EX pipeline register to get values and control bits
  Perform ALU operation
  Compute targets (PC+4+offset, etc.) in case this is a branch
  Decide if jump/branch should be taken
Write values of interest to pipeline register (EX/MEM)
  Control information, Rd index, …
  Result of ALU operation
  Value in case this is a memory store instruction

## Slide 32: Execute (EX)
Stage 2: Instruction Decode
ctrl
EX/MEM
Rest of pipeline
B
D
ctrl
ID/EX
PC+4
B
A
alu
imm
target

## Slide 33: MEM
Stage 4: Memory
On every cycle:
  Read EX/MEM pipeline register to get values and control bits
  Perform memory load/store if needed
    address is ALU result
Write values of interest to pipeline register (MEM/WB)
  Control information, Rd index, …
  Result of memory operation
  Pass result of ALU operation

## Slide 34: MEM
ctrl
MEM/WB
Rest of pipeline
Stage 3: Execute
M
D
ctrl
EX/MEM
B
D
memory
din
dout
addr
mc
target

## Slide 35: WB
Stage 5: Write-back
On every cycle:
  Read MEM/WB pipeline register to get values and control bits
  Select value and write to register file

## Slide 36: WB
Stage 4: Memory
ctrl
MEM/WB
M
D

## Slide 37
IF/ID
+4
ID/EX
EX/MEM
MEM/WB
mem
din
dout
addr
inst
PC+4
B
A
Rt
B
D
M
D
PC+4
imm
OP
Rd
OP
Rd
OP
PC
inst mem
Rd
Ra
Rb
D
B
A
Rd
Putting it all together!

## Slide 38: Takeaway
Pipelining is a powerful technique to mask latencies and increase throughput
  Logically, instructions execute one at a time
  Physically, instructions execute in parallel
    Instruction level parallelism
Abstraction promotes decoupling
  Interface (ISA) vs. implementation (Pipeline)

## Slide 39: MIPS is designed for pipelining
Instructions same length
  32 bits, easy to fetch and then decode
3 types of instruction formats
  Easy to route bits between stages
  Can read a register source before even knowing what the instruction is
Memory access through lw and sw only
  Access memory after ALU

## Slide 40: Agenda
5-stage Pipeline
Implementation
Working Example
Hazards
Structural
Data Hazards
Control Hazards

## Slide 41: Example: : Sample Code (Simple)
add r3  r1, r2 nand r6  r4, r5 lw r4  20(r2) add r5  r2, r5 sw r7  12(r3)
Assume 8-register machine

## Slide 42
PC
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 11-15
Bits 16-20
op
Rt
imm
valB
valA
PC+4
PC+4
target
ALU
result
op
dest
valB
op
dest
ALU
result
mdata
instruction
0
R2
R3
R4
R5
R1
R6
R0
R7
regA
regB
Bits 26-31
data
dest
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
M
U
X
Rd
Inst
mem

## Slide 43: Example: Start State @ Cycle 0
PC
add
nand
lw
add
sw
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 11-15
Bits 16-20
nop
0
0
0
0
0
0
0
nop
0
0
nop
0
0
0
0
nop
9
12
18
7
36
41
0
22
R2
R3
R4
R5
R1
R6
R0
R7
Bits 26-31
data
dest
Initial
State
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
0
M
U
X
0
At time 1,
Fetch
add r3 r1 r2
0
Time: 0
4

## Slide 44: Agenda
5-stage Pipeline
Implementation
Working Example
Hazards
Structural
Data Hazards
Control Hazards

## Slide 45: Hazards
Correctness problems associated w/processor design
  Structural hazards
  Same resource needed for different purposes at the same time (Possible: ALU, Register File, Memory)
  Data hazards
    Instruction output needed before it’s available
  Control hazards
    Next instruction PC unknown at time of Fetch
Notes: Structural: say only 1 memory for instruction read and the MEM stage. That is a structural hazard. We have designed the MIPS ISA and our implementation of separate memory for instruction and data to avoid this problem. MIPS is designed very carefully to not have any structural hazards.
Data hazards arise when data needed by one instruction has not yet been computed (because it is further down the pipeline). We need a solution for this.
Control hazards arise when we don’t know what the PC will be. This makes it not possible to push the next instruction down the pipeline. Till we know what the issue is.

## Slide 46: Dependences and Hazards
Dependence: relationship between two insns
  Data: two insns use same storage location
  Control: 1 insn affects whether another executes at all
  Not a bad thing, programs would be boring otherwise
  Enforced by making older insn go before younger one
    Happens naturally in single-/multi-cycle designs
    But not in a pipeline
Hazard: dependence & possibility of wrong insn order
  Effects of wrong insn order cannot be externally visible
  Hazards are a bad thing: most solutions either complicate the hardware or reduce performance

## Slide 47: Data Hazards
Data Hazards
  register file reads occur in stage 2 (ID)
  register file writes occur in stage 5 (WB)
  next instructions may read values about to be written
    i.e instruction may need values that are being computed further down the pipeline
    in fact, this is quite common
“earlier” = started earlier
= stage right
stage left
  destination reg of earlier instruction == source reg of current
Notes: assumes (WE=0 implies rD=0) everywhere, similar for rA needed, rB needed (can ensure this in ID stage)

## Slide 48: Where are the Data Hazards?
Clock cycle
1 2 3 4 5 6 7 8 9
sub r5, r3, r4
lw r6, 4(r3)
or r5, r3, r5
sw r6, 12(r3)
add r3, r1, r2
time

## Slide 49: Data Hazards
Data Hazards
  register file reads occur in stage 2 (ID)
  register file writes occur in stage 5 (WB)
  next instructions may read values about to be written
i.e. add r3, r1, r2
sub r5, r3, r4
How to detect?
“earlier” = started earlier
= stage right
stage left
  destination reg of earlier instruction == source reg of current
Notes: assumes (WE=0 implies rD=0) everywhere, similar for rA needed, rB needed (can ensure this in ID stage)

## Slide 50
IF/ID
+4
ID/EX
EX/MEM
MEM/WB
mem
din
dout
addr
inst
PC+4
OP
B
A
Rt
B
D
M
D
PC+4
imm
OP
Rd
OP
Rd
PC
inst mem
Rd
Ra
Rb
D
B
A
Rd
Detecting Data Hazards
IF/ID.Ra ≠ 0 &&
(IF/ID.Ra==ID/Ex.Rd
IF/ID.Ra==Ex/M.Rd
IF/ID.Ra==M/W.Rd)
repeat for Rb
add r3, r1, r2
sub r5,r3,r4

## Slide 51: Data Hazards
Data Hazards
  register file reads occur in stage 2 (ID)
  register file writes occur in stage 5 (WB)
  next instructions may read values about to be written
How to detect? Logic in ID stage:
stall = (IF/ID.Ra != 0 &&
(IF/ID.Ra == ID/EX.Rd || IF/ID.Ra == EX/M.Rd || IF/ID.Ra == M/WB.Rd))
|| (same for Rb)
“earlier” = started earlier
= stage right
stage left
  destination reg of earlier instruction == source reg of current
Notes: assumes (WE=0 implies rD=0) everywhere, similar for rA needed, rB needed (can ensure this in ID stage)

## Slide 52: Detecting Data Hazards
IF/ID
+4
ID/EX
EX/MEM
MEM/WB
mem
din
dout
addr
PC
inst mem
Rd
Ra
Rb
D
B
A
detect hazard
Rd
add r3, r1, r2
sub r5, r3, r5
or r6, r3, r4
add r6, r3, r8
inst
PC+4
OP
B
A
Rt
B
D
M
D
PC+4
imm
OP
Rd
OP
Rd

## Slide 53: Takeaway
Data hazards occur when a operand (register) depends on the result of a previous instruction that may not be computed yet. A pipelined processor needs to detect data hazards.

## Slide 54: Next Goal
What to do if data hazard detected?
Notes: Nothing: Modify ISA to match implementation
Stall: Pause current and all subsequent instruction
Forward/Bypass: Steal correct value from elsewhere in pipeline

## Slide 55: Possible Responses to Data Hazards
Do Nothing
  Change the ISA to match implementation
  “Hey compiler: don’t create code w/data hazards!”
  (We can do better than this)
Stall
  Pause current and subsequent instructions till safe
Forward/bypass
  Forward data value to where it is needed
  (Only works if value actually exists already)
Notes: Nothing: Modify ISA to match implementation
Stall: Pause current and all subsequent instruction
Forward/Bypass: Steal correct value from elsewhere in pipeline

## Slide 56: Stalling
How to stall an instruction in ID stage
  prevent IF/ID pipeline register update
    stalls the ID stage instruction
  convert ID stage instr into nop for later stages
    innocuous “bubble” passes through pipeline
  prevent PC update
    stalls the next (IF stage) instruction
Notes: prev slide:
Q: what happens if branch in EX?
A: bad stuff: we miss the branch
So: lets try not to stall

## Slide 57: Detecting Data Hazards
IF/ID
+4
ID/EX
EX/MEM
MEM/WB
mem
din
dout
addr
PC
inst mem
Rd
Ra
Rb
D
B
A
detect hazard
Rd
add r3, r1, r2
sub r5, r3, r5
or r6, r3, r4
add r6, r3, r8
inst
PC+4
OP
B
A
Rt
B
D
M
D
PC+4
imm
OP
Rd
OP
Rd
If detect hazard
WE=0
MemWr=0
RegWr=0

## Slide 58: Stalling
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r5 |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
add r6, r3, r8 |  |  |  |  |  |  |  |  | 
IF | ID 11=r1 22=r2 | EX D=33 | MEM D=33 | WB r3=33 |  |  |  | 
 | IF | ID ?=r3 | ID ?=r3 | ID ?=r3 | ID 33=r3 | EX | MEM | WB
 |  | IF | IF | IF | IF | ID 33=r3 | EX | M
 |  |  |  |  |  | IF | ID 33=r3 | EX
time
Notes: find hazards first, then draw

## Slide 59: Stalling
data mem
B
A
B
D
M
D
inst mem
D rD
B
A
Rd
Rd
Rd
WE
WE
Op
WE
Op
rA rB
PC
+4
Op
nop
inst
/stall
add r3,r1,r2
(MemWr=0
RegWr=0)
NOP = If(IF/ID.rA ≠ 0 &&
(IF/ID.rA==ID/Ex.Rd
IF/ID.rA==Ex/M.Rd
IF/ID.rA==M/W.Rd))
sub r5,r3,r5
or r6,r3,r4
(WE=0)
STALL CONDITION MET
Notes: draw control signals for /stall
Q: what happens if branch in EX?
A: bad stuff: we miss the branch
So: lets try not to stall

## Slide 60: Stalling
data mem
B
A
B
D
M
D
inst mem
D rD
B
A
Rd
Rd
Rd
WE
WE
Op
WE
Op
rA rB
PC
+4
Op
nop
inst
/stall
nop
(MemWr=0
RegWr=0)
NOP = If(IF/ID.rA ≠ 0 &&
(IF/ID.rA==ID/Ex.Rd
IF/ID.rA==Ex/M.Rd
IF/ID.rA==M/W.Rd))
add r3,r1,r2
sub r5,r3,r5
(MemWr=0
RegWr=0)
or r6,r3,r4
(WE=0)
STALL CONDITION MET
Notes: draw control signals for /stall
Q: what happens if branch in EX?
A: bad stuff: we miss the branch
So: lets try not to stall

## Slide 61: Stalling
data mem
B
A
B
D
M
D
inst mem
D rD
B
A
Rd
Rd
Rd
WE
WE
Op
WE
Op
rA rB
PC
+4
Op
nop
inst
/stall
(MemWr=0
RegWr=0)
NOP = If(IF/ID.rA ≠ 0 &&
(IF/ID.rA==ID/Ex.Rd
IF/ID.rA==Ex/M.Rd
IF/ID.rA==M/W.Rd))
add r3,r1,r2
sub r5,r3,r5
nop
nop
(MemWr=0
RegWr=0)
(MemWr=0
RegWr=0)
or r6,r3,r4
(WE=0)
STALL CONDITION MET
Notes: draw control signals for /stall
Q: what happens if branch in EX?
A: bad stuff: we miss the branch
So: lets try not to stall

## Slide 62: Stalling
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r5 |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
add r6, r3, r8 |  |  |  |  |  |  |  |  | 
IF | ID 11=r1 22=r2 | EX D=33 | MEM D=33 | WB r3=33 |  |  |  | 
 | IF | ID ?=r3 | ID ?=r3 | ID ?=r3 | ID 33=r3 | EX | MEM | WB
 |  | IF | IF | IF | IF | ID 33=r3 | EX | M
 |  |  |  |  |  | IF | ID 33=r3 | EX
r3 = 10
r3 = 20
time
Notes: find hazards first, then draw

## Slide 63: Stalling
How to stall an instruction in ID stage
  prevent IF/ID pipeline register update
    stalls the ID stage instruction
  convert ID stage instr into nop for later stages
    innocuous “bubble” passes through pipeline
  prevent PC update
    stalls the next (IF stage) instruction
Notes: prev slide:
Q: what happens if branch in EX?
A: bad stuff: we miss the branch
So: lets try not to stall

## Slide 64: Takeaway
Data hazards occur when a operand (register) depends on the result of a previous instruction that may not be computed yet. A pipelined processor needs to detect data hazards.
Stalling, preventing a dependent instruction from advancing, is one way to resolve data hazards.
Stalling introduces NOPs (“bubbles”) into a pipeline. Introduce NOPs by (1) preventing the PC from updating, (2) preventing writes to IF/ID registers from changing, and (3) preventing writes to memory and register file.
*Bubbles in pipeline significantly decrease performance.

## Slide 65: Possible Responses to Data Hazards
Do Nothing
  Change the ISA to match implementation
  “Compiler: don’t create code with data hazards!”
  (Nice try, we can do better than this)
Stall
  Pause current and subsequent instructions till safe
Forward/bypass
  Forward data value to where it is needed
  (Only works if value actually exists already)
Notes: Nothing: Modify ISA to match implementation
Stall: Pause current and all subsequent instruction
Forward/Bypass: Steal correct value from elsewhere in pipeline

## Slide 66: Forwarding
Forwarding bypasses some pipelined stages forwarding a result to a dependent instruction operand (register).
Three types of forwarding/bypass
  Forwarding from Ex/Mem registers to Ex stage (MEx)
  Forwarding from Mem/WB register to Ex stage (WEx)
  RegisterFile Bypass

## Slide 67: Add the Forwarding Datapath
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
forward unit
detect hazard
IF/ID
ID/Ex
Ex/Mem
Mem/WB
Notes: draw control signals

## Slide 68: Forwarding Datapath
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
forward unit
detect hazard
Three types of forwarding/bypass
Forwarding from Ex/Mem registers to Ex stage (MEx)
Forwarding from Mem/WB register to Ex stage (W  Ex)
RegisterFile Bypass
IF/ID
ID/Ex
Ex/Mem
Mem/WB
Notes: draw control signals

## Slide 69: Forwarding Datapath 1: Ex/MEM  EX
add r3, r1, r2 |  |  |  |  |  |  | 
sub r5, r3, r1 |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
add r3, r1, r2
sub r5, r3, r1
Problem: EX needs ALU result that is in MEM stage
Solution: add a bypass from EX/MEM.D to start of EX
Ex/Mem

## Slide 70: Forwarding Datapath 1: Ex/MEM  EX
data mem
inst mem
D
B
A
Detection Logic in Ex Stage:
forward = (Ex/M.WE && EX/M.Rd != 0 &&
ID/Ex.Ra == Ex/M.Rd)
|| (same for Rb)
add r3, r1, r2
sub r5, r3, r1
Ex/Mem

## Slide 71: Forwarding Datapath 2: Mem/WB  EX
add r3, r1, r2 |  |  |  |  |  |  |  | 
sub r5, r3, r1 |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
Problem: EX needs value being written by WB
Solution: Add bypass from WB final value to start of EX
Mem/WB
add r3, r1,r2
sub r5, r3, r1
or r6, r3, r4

## Slide 72: Forwarding Datapath 2: Mem/WB  EX
data mem
inst mem
D
B
A
Detection Logic:
forward = (M/WB.WE && M/WB.Rd != 0 &&
ID/Ex.Ra == M/WB.Rd &&
not (ID/Ex.WE && Ex/M.Rd != 0 &&
ID/Ex.Ra == Ex/M.Rd)
|| (same for Rb)
Mem/WB
add r3, r1,r2
sub r5, r3, r1
or r6, r3, r4

## Slide 73: Register File Bypass
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r1 |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
add r6, r3, r8 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
add r3, r1,r2
sub r5, r3, r1
or r6, r3, r4
add r6, r3, r8

## Slide 74: Register File Bypass
data mem
inst mem
D
B
A
Problem: Reading a value that is currently being written
Solution: just negate register file clock
  writes happen at end of first half of each clock cycle
  reads happen during second half of each clock cycle
add r3, r1,r2
sub r5, r3, r1
or r6, r3, r4
add r6, r3, r8

## Slide 75: Forwarding Example 2
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r4 |  |  |  |  |  |  |  |  | 
lw r6, 4(r3) |  |  |  |  |  |  |  |  | 
or r5, r3, r5 |  |  |  |  |  |  |  |  | 
sw r6, 12(r3) |  |  |  |  |  |  |  |  | 
IF | ID 11=r1 22=r2 | EX D=33 | MEM D=33 | WB r3=33 |  |  |  | 
 | IF | ID 33=r3 | EX D=55 | MEM D=55 | WB r5=55 |  |  | 
 |  | IF | ID 33=r3 | EX D=? | MEM D=66 | WB r6=66 |  | 
 |  |  | IF | ID 33=r3 55=r5 | EX | MEM | WB | 
 |  |  |  | IF | ID 33=r3 66=r6 | EX | MEM | 
time
Notes: identify hazards then draw; if “or” had used r6, would have needed to stall

## Slide 76: Forwarding Example 2
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add r3, r1, r2 |  |  |  |  |  |  |  |  | 
sub r5, r3, r4 |  |  |  |  |  |  |  |  | 
lw r6, 4(r3) |  |  |  |  |  |  |  |  | 
or r5, r3, r5 |  |  |  |  |  |  |  |  | 
sw r6, 12(r3) |  |  |  |  |  |  |  |  | 
IF | ID 11=r1 22=r2 | EX D=33 | MEM D=33 | WB r3=33 |  |  |  | 
 | IF | ID 33=r3 | EX D=55 | MEM D=55 | WB r5=55 |  |  | 
 |  | IF | ID 33=r3 | EX D=? | MEM D=66 | WB r6=66 |  | 
 |  |  | IF | ID 33=r3 55=r5 | EX | MEM | WB | 
 |  |  |  | IF | ID 33=r3 66=r6 | EX | MEM | 
IF
ID
Ex
M
W
IF
ID
Ex
M
W
time
Notes: identify hazards then draw; if “or” had used r6, would have needed to stall

## Slide 77: Load-Use Hazard Explained
Data dependency after a load instruction:
  Value not available until after the M stage
  Next instruction cannot proceed if dependent
THE KILLER HAZARD
data mem
inst mem
D
B
A
lw r4, 20(r8)
or r6, r3, r4
Notes: often see lw …; nop; …
we will stall for our project 2

## Slide 78: Load-Use Stall
lw r4, 20(r8) |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
lw r4, 20(r8)
or r6,r4,r1
load-use stall
Notes: Need to go back in time

## Slide 79: Load-Use Stall (1)
lw r4, 20(r8) |  |  |  |  |  |  |  |  | 
or r6, r3, r4 |  |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
IF
ID
Ex
IF
ID
lw r4, 20(r8)
or r6,r4,r1
load-use stall
Notes: Need to go back in time

## Slide 80: Load-Use Detection
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
forward unit
detect hazard
IF/ID
ID/Ex
Ex/Mem
Mem/WB
Stall = If(ID/Ex.MemRead &&
IF/ID.Ra == ID/Ex.Rd
Rd
MC
Notes: It happens in an earlier stage. You stall since you don’t want to go ahead from the ID stage unless you are ready.
Walk through what happens with a

## Slide 81: Resolving Load-Use Hazards
Two MIPS Solutions:
  MIPS 2000/3000: delay slot
    ISA says results of loads are not available until one cycle later
    Assembler inserts nop, or reorders to fill delay slot
  MIPS 4000 onwards: stall
    But really, programmer/compiler reorders to avoid stalling in the load delay slot
Notes: often see lw …; nop; …
we will stall for our project 2

## Slide 82: Takeaway
Data hazards occur when a operand (register) depends on the result of a previous instruction that may not be computed yet. A pipelined processor needs to detect data hazards.
Stalling, preventing a dependent instruction from advancing, is one way to resolve data hazards. Stalling introduces NOPs (“bubbles”) into a pipeline. Introduce NOPs by (1) preventing the PC from updating, (2) preventing writes to IF/ID registers from changing, and (3) preventing writes to memory and register file. Bubbles (nops) in pipeline significantly decrease performance.
Forwarding bypasses some pipelined stages forwarding a result to a dependent instruction operand (register). Better performance than stalling.

## Slide 83: Quiz
Find all hazards, and say how they are resolved:
add r3, r1, r2
nand r5, r3, r4
add r2, r6, r3
lw r6, 24(r3)
sw r6, 12(r2)
Notes: Find all hazards, and say how they are resolved

## Slide 84: Quiz
Find all hazards, and say how they are resolved: add r3, r1, r2 sub r3, r2, r1 nand r4, r3, r1 or r0, r3, r4 xor r1, r4, r3 sb r4, 1(r0)
Notes: 6 hazards
be careful of store (no rD)
be careful or r0 (never a hazard)

## Slide 85: Data Hazard Recap
Delay Slot(s)
  Modify ISA to match implementation
Stall
  Pause current and all subsequent instructions
Forward/Bypass
  Try to steal correct value from elsewhere in pipeline
  Otherwise, fall back to stalling or require a delay slot
Tradeoffs?
Notes: 1: ISA tied to impl; messy asm; impl easy & cheap; perf depends on asm.
2: ISA correctness not tied to impl; clean+slow asm, or messy+fast asm; impl easy and cheap; same perf as 1. 3: ISA perf not tied to impl; clean+fast asm; impl is tricky; best perf

## Slide 86: Agenda
5-stage Pipeline
Implementation
Working Example
Hazards
Structural
Data Hazards
Control Hazards

## Slide 87: A bit of Context
i = 0;
do {
n += 2;
i++;
} while(i < max)
i = 7;
n--;
x10 addi r1, r0, 0 # i=0
x14 Loop: addi r2, r2, 2 # n += 2
x18 addi r1, r1, 1 # i++
x1C blt r1, r3, Loop # i<max?
x20 addi r1, r0, 7 # i = 7
x24 subi r2, r2, 1 # n--
i  r1
Assume:
n  r2
max  r3

## Slide 88: Control Hazards
Control Hazards
  instructions are fetched in stage 1 (IF)
  branch and jump decisions occur in stage 3 (EX)
   next PC not known until 2 cycles after branch/jump
x1C blt r1, r3, Loop
x20 addi r1, r0, 7
x24 subi r2, r2, 1
Branch not taken?
Branch taken?
Notes: Q: what happens with branch/jump in branch delay slot?
A: bad stuff, so forbidden
Q: why one, not two?
A: can move branch calc from EX to ID; will require new bypasses into ID stage; or can just zap the second instruction
Q: performance?
A: stall is bad

## Slide 89: Zap & Flush
1C | blt r1,r3,L |  |  |  |  |  |  |  | 
20 | addi r1,r0,7 |  |  |  |  |  |  |  | 
24 | subi r2,r2,1 |  |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
If branch Taken
Zap
prevent PC update
clear IF/ID latch
branch continues
New PC = 14
14 L:addi r2,r2,2
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 90: Reducing the cost of control hazard
Delay Slot
  You MUST do this
  MIPS ISA: 1 insn after ctrl insn always executed
    Whether branch taken or not
Resolve Branch at Decode
  Some groups do this for Project 3, your choice
  Move branch calc from EX to ID
  Alternative: just zap 2nd instruction when branch taken
Branch Prediction
  Not in 3410, but every processor worth anything does this (no offense!)
Notes: Q: what happens with branch/jump in branch delay slot?
A: bad stuff, so forbidden
Q: why one, not two?
A: can move branch calc from EX to ID; will require new bypasses into ID stage; or can just zap the second instruction
Q: performance?
A: stall is bad

## Slide 91: Problem: Zapping 2 insns/branch
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
New PC = 1C
1C | blt r1, r3, Loop |  |  |  |  |  |  |  | 
20 | addi r1, r0, 7 |  |  |  |  |  |  |  | 
24 | subi r2, r2, 1 |  |  |  |  |  |  |  | 
Notes: Pipeline is humming

## Slide 92: Solution #1: Delay Slot
i = 0;
do {
n += 2;
i++;
} while(i < max)
i = 7;
n--;
x10 addi r1, r0, 0 # i=0
x14 Loop: addi r2, r2, 2 # n += 2
x18 addi r1, r1, 1 # i++
x1C blt r1, r3, Loop # i<max?
x20 nop
x24 addi r1, r0, 7 # i = 7
x28 subi r2, r2, 1 # n++
i  r1
Assume:
n  r2
max  r3

## Slide 93: Delay Slot in Action
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
New PC = 1C
1C | blt r1, r3, Loop |  |  |  |  |  |  |  | 
20 | nop |  |  |  |  |  |  |  | 
24 | addi r1, r0, 7 |  |  |  |  |  |  |  | 
Notes: Pipeline is humming

## Slide 94: Soln #2: Resolve Branches @ Decode
data mem
inst mem
D
B
A
PC
+4
New PC = 1C
branch calc
decide branch
1C | blt r1, r3, Loop |  |  |  |  |  |  |  | 
20 | nop |  |  |  |  |  |  |  | 
14 | Loop:addi r2,r2,2 |  |  |  |  |  |  |  | 
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 95: Optimization: Fill the Delay Slot
x10 addi r1, r0, 0 # i=0
x14 Loop: addi r2, r2, 2 # n += 2
x18 addi r1, r1, 1 # i++
x1C blt r1, r3, Loop # i<max?
x20 nop
x10 addi r1, r0, 0 # i=0
x14 Loop: addi r1, r1, 1 # i++
x18 blt r1, r3, Loop # i<max?
x1C addi r2, r2, 2 # n += 2
Compiler transforms code

## Slide 96: Optimization In Action!
data mem
inst mem
D
B
A
PC
+4
New PC = 1C
branch calc
decide branch
1C | blt r1, r3, Loop |  |  |  |  |  |  |  | 
20 | addi r2,r2,2 |  |  |  |  |  |  |  | 
14 | Loop:addi r1,r1,1 |  |  |  |  |  |  |  | 
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 97: Branch Prediction
Most processor support Speculative Execution
  Guess direction of the branch
    Allow instructions to move through pipeline
    Zap them later if guess turns out to be wrong
  A must for long pipelines
Notes: Q: How to guess?
A: constant; hint; branch prediction; random; …

## Slide 98: Data Hazard Takeaways
Data hazards occur when a operand (register) depends on the result of a previous instruction that may not be computed yet. Pipelined processors need to detect data hazards.
Stalling, preventing a dependent instruction from advancing, is one way to resolve data hazards. Stalling introduces NOPs (“bubbles”) into a pipeline. Introduce NOPs by (1) preventing the PC from updating, (2) preventing writes to IF/ID registers from changing, and (3) preventing writes to memory and register file. Nops significantly decrease performance.
Forwarding bypasses some pipelined stages forwarding a result to a dependent instruction operand (register). Better performance than stalling.

## Slide 99: Control Hazard Takeaways
Control hazards occur because the PC following a control instruction is not known until control instruction is executed. If branch is taken  need to zap instructions. 1 cycle performance penalty.
Delay Slots can potentially increase performance due to control hazards. The instruction in the delay slot will always be executed. Requires software (compiler) to make use of delay slot. Put nop in delay slot if not able to put useful instruction in delay slot.
We can reduce cost of a control hazard by moving branch decision and calculation from Ex stage to ID stage. With a delay slot, this removes the need to flush instructions on taken branches.