## Slide 1: Calling Conventions
Hakim Weatherspoon
CS 3410
Computer Science
Cornell University
The slides are the product of many rounds of teaching CS 3410 by Professors Weatherspoon, Bala, Bracy, McKee, and Sirer.

## Slide 2: Big Picture: Where are we now?
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard

## Slide 3: Big Picture: Where are we going?
int x = 10;
x = 2 * x + 15;
C
compiler
addiu r5, r0, 10
muli r5, r5, 2
addiu r5, r5, 15
MIPS
assembly
00100000000001010000000000001010
00000000000001010010100001000000
00100000101001010000000000001111
machine code
assembler
CPU
Circuits
Gates
Transistors
Silicon
op = addiu r0 r5 10
op = addiu r5 r5 15
op = r-type r5 r5 shamt=1 func=sll
r0 = 0
r5 = r0 + 10
r5 = r5<<1 #r5 = r5 * 2
r5 = r15 + 15
Notes: 32 bits, 4 bytes

## Slide 4: Big Picture: Where are we going?
SandyBridge Motherboard, 2011
http://news.softpedia.com
CPU
Main Memory
(DRAM)

## Slide 5: Goals for this week
Calling Convention for Procedure Calls
Enable code to be reused by allowing code snippets to be invoked
Will need a way to
  call the routine (i.e. transfer control to procedure)
  pass arguments
    fixed length, variable length, recursively
  return to the caller
    Putting results in a place where caller can find them
  Manage register
Notes: Ninja example from book

## Slide 6: Calling Convention for Procedure Calls
Transfer Control
  Caller  Routine
  Routine  Caller
Pass Arguments to and from the routine
  fixed length, variable length, recursively
  Get return value back to the caller
Manage Registers
  Allow each routine to use registers
  Prevent routines from clobbering each others’ data
What is a Convention?
Warning: There is no one true MIPS calling convention.
lecture != book != gcc != spim != web

## Slide 7: Cheat Sheet and Mental Model for Today
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard
How do we share registers and use memory when making procedure calls?

## Slide 8: Cheat Sheet and Mental Model for Today
  first four arg words passed in $a0, $a1, $a2, $a3
  remaining arg words passed in parent’s stack frame
  return value (if any) in $v0, $v1
  stack frame at $sp
    contains $ra (clobbered on JAL
    to sub-functions)
    contains local vars (possibly
    clobbered by sub-functions)
    contains extra arguments to sub-functions
    contains space for first 4 arguments
    to sub-functions
  callee save regs are preserved
  caller save regs are not
  Global data accessed via $gp
saved ra
saved fp
saved regs ($s0 ... $s7)
locals
outgoing args
$fp 
$sp 
Notes: Q: Minimum frame size?
A: 24 bytes (ra+fp+4args)
Q: What if this function makes no sub-calls?

## Slide 9: MIPS Register
Return address: $31 (ra)
Stack pointer: $29 (sp)
Frame pointer: $30 (fp)
First four arguments: $4-$7 (a0-a3)
Return result: $2-$3 (v0-v1)
Callee-save free regs: $16-$23 (s0-s7)
Caller-save free regs: $8-$15,$24,$25 (t0-t9)
Reserved: $26, $27
Global pointer: $28 (gp)
Assembler temporary: $1 (at)

## Slide 10: MIPS Register Conventions
r0 | $zero | zero
r1 | $at | assembler temp
r2 | $v0 | function return values
r3 | $v1 | 
r4 | $a0 | function arguments
r5 | $a1 | 
r6 | $a2 | 
r7 | $a3 | 
r8 | $t0 | temps (caller save)
r9 | $t1 | 
r10 | $t2 | 
r11 | $t3 | 
r12 | $t4 | 
r13 | $t5 | 
r14 | $t6 | 
r15 | $t7 | 
r16 | $s0 | saved (callee save)
r17 | $s1 | 
r18 | $s2 | 
r19 | $s3 | 
r20 | $s4 | 
r21 | $s5 | 
r22 | $s6 | 
r23 | $s7 | 
r24 | $t8 | more temps (caller save)
r25 | $t9 | 
r26 | $k0 | reserved for kernel
r27 | $k1 | 
r28 | $gp | global data pointer
r29 | $sp | stack pointer
r30 | $fp | frame pointer
r31 | $ra | return address

## Slide 11: Calling Convention for Procedure Calls
Transfer Control
  Caller  Routine
  Routine  Caller
Pass Arguments to and from the routine
  fixed length, variable length, recursively
  Get return value back to the caller
Manage Registers
  Allow each routine to use registers
  Prevent routines from clobbering each others’ data
What is a Convention?
Warning: There is no one true MIPS calling convention.
lecture != book != gcc != spim != web

## Slide 12: How does a function call work?
int main (int argc, char* argv[ ]) {
int n = 9;
int result = myfn(n);
}
int myfn(int n) {
int f = 1;
int i = 1;
int j = n – 1;
while(j >= 0) {
f *= i;
i++;
j = n - i;
}
return f;
}

## Slide 13: Jumps are not enough
main:
j myfn
after1:
add $1,$2,$3
myfn:
…
…
j after1
Jumps to the callee
Jumps back
1
2
Notes: Jumps and branches can transfer control to the callee (called procedure)
Jumps and branches can transfer control back

## Slide 14: Jumps are not enough
main:
j myfn
after1:
add $1,$2,$3
j myfn
after2:
sub $3,$4,$5
myfn:
…
…
j after1
Jumps to the callee
Jumps back
What about multiple sites?
??? Change target
on the fly ???
j after2
1
2
3
4
Notes: Jumps and branches can transfer control to the callee (called procedure)
Jumps and branches can transfer control back

## Slide 15: Takeaway1: Need Jump And Link
JAL (Jump And Link) instruction moves a new value into the PC, and simultaneously saves the old value in register $31 (aka $ra or return address)
Thus, can get back from the subroutine to the instruction immediately following the jump by transferring control back to PC in register $31

## Slide 16: Jump-and-Link / Jump Register
JAL saves the PC in register $31
Subroutine returns by jumping to $31
r31
main:
jal myfn
after1:
add $1,$2,$3
jal myfn
after2:
sub $3,$4,$5
myfn:
…
…
jr $31
after1
1
2
First call

## Slide 17: Jump-and-Link / Jump Register
JAL saves the PC in register $31
Subroutine returns by jumping to $31
What happens for recursive invocations?
r31
main:
jal myfn
after1:
add $1,$2,$3
jal myfn
after2:
sub $3,$4,$5
myfn:
…
…
jr $31
1
2
4
3
Second call
after1
after2

## Slide 18: JAL / JR for Recursion?
int main (int argc, char* argv[ ]) {
int n = 9;
int result = myfn(n);
}
int myfn(int n) {
int f = 1;
int i = 1;
int j = n – 1;
while(j >= 0) {
f *= i;
i++;
j = n - i;
}
return f;
}

## Slide 19: JAL / JR for Recursion?
int main (int argc, char* argv[ ]) {
int n = 9;
int result = myfn(n);
}
int myfn(int n) {
if(n > 0) {
return n * myfn(n - 1);
} else {
return 1;
}
}

## Slide 20: JAL / JR for Recursion?
Problems with recursion:
overwrites contents of $31
r31
main:
jal myfn
after1:
add $1,$2,$3
myfn:
if (test)
jal myfn
after2:
jr $31
after1
1
First call

## Slide 21: JAL / JR for Recursion?
Problems with recursion:
overwrites contents of $31
r31
main:
jal myfn
after1:
add $1,$2,$3
myfn:
if (test)
jal myfn
after2:
jr $31
1
2
Recursive Call
after1
after2

## Slide 22: JAL / JR for Recursion?
Problems with recursion:
overwrites contents of $31
r31
main:
jal myfn
after1:
add $1,$2,$3
myfn:
if (test)
jal myfn
after2:
jr $31
1
2
3
Return from Recursive Call
after2

## Slide 23: JAL / JR for Recursion?
Problems with recursion:
overwrites contents of $31
r31
main:
jal myfn
after1:
add $1,$2,$3
myfn:
if (test)
jal myfn
after2:
jr $31
1
2
3
4
Stuck!
Return from Original Call ???
after2

## Slide 24: JAL / JR for Recursion?
Problems with recursion:
overwrites contents of $31
Need a way to save and restore register contents
r31
main:
jal myfn
after1:
add $1,$2,$3
myfn:
if (test)
jal myfn
after2:
jr $31
1
2
3
4
Stuck!
Return from Original Call ???
after2

## Slide 25: Need a “Call Stack”
Call stack
  contains activation records (aka stack frames)
Each activation record contains
  the return address for that invocation
  the local variables for that procedure
A stack pointer (sp) keeps track of the top of the stack
  dedicated register ($29) on the MIPS
Manipulated by push/pop operations
  push: move sp down, store
  pop: load, move sp up
after1
high mem
low mem
$31 =
sp

## Slide 26: Cheat Sheet and Mental Model for Today
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard

## Slide 27: Need a “Call Stack”
Call stack
  contains activation records (aka stack frames)
Each activation record contains
  the return address for that invocation
  the local variables for that procedure
A stack pointer (sp) keeps track of the top of the stack
  dedicated register ($29) on the MIPS
Manipulated by push/pop operations
  push: move sp down, store
  pop: load, move sp up
sp
after1
after2
high mem
low mem
Push: ADDIU $sp, $sp, -4
SW $31, 0 ($sp)
$31 =
$31 =
sp

## Slide 28: Need a “Call Stack”
Call stack
  contains activation records (aka stack frames)
Each activation record contains
  the return address for that invocation
  the local variables for that procedure
A stack pointer (sp) keeps track of the top of the stack
  dedicated register ($29) on the MIPS
Manipulated by push/pop operations
  push: move sp down, store
  pop: load, move sp up
sp
after1
after2
high mem
low mem
Push: ADDIU $sp, $sp, -4
SW $31, 0 ($sp)
Pop: LW $31, 0 ($sp)
ADDIU $sp, $sp, 4
JR $31
$31 =
$31 =
sp

## Slide 29: Need a “Call Stack”
Stack used to save and restore contents of $31
sp
after1
after2
high mem
low mem
after2
after2
sp
sp
main:
jal myfn
after1:
add $1,$2,$3
myfn:
addiu $sp,$sp,-4
sw $31, 0($sp)
if (test)
jal myfn
after2:
lw $31, 0($sp)
addiu $sp,$sp,4
jr $31
2
1

## Slide 30: Need a “Call Stack”
Stack used to save and restore contents of $31
sp
after1
after2
high mem
low mem
after2
after2
sp
sp
main:
jal myfn
after1:
add $1,$2,$3
myfn:
addiu $sp,$sp,-4
sw $31, 0($sp)
if (test)
jal myfn
after2:
lw $31, 0($sp)
addiu $sp,$sp,4
jr $31
2
1

## Slide 31: Stack Growth
(Call) Stacks start at a high address in memory
Stacks grow down as frames are pushed on
  Note: data region starts at a low address and grows up
  The growth potential of stacks and data region are not artificially limited

## Slide 32: An executing program in memory
top
bottom
system reserved
(stack grows down)
(heap grows up)
text
reserved
(static) data
(.stack)
.data
.text
system reserved
stack
system reserved
.data
.text
0xfffffffc
0x00000000
0x7ffffffc
0x80000000
0x10000000
0x00400000
code (text)
static data
dynamic data (heap)

## Slide 33: An executing program in memory
0xfffffffc
0x00000000
top
bottom
0x7ffffffc
0x80000000
0x10000000
0x00400000
system reserved
(stack grows down)
(heap grows up)
text
reserved
(static) data
(.stack)
.data
.text
system reserved
stack
system reserved
code (text)
static data
dynamic data (heap)
“Data Memory”
“Program Memory”

## Slide 34: Anatomy of an executing program
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard
Stack, Data, Code
Stored in Memory
$29 ($sp)
$31 ($ra)
Stack, Data, Code
Stored in Memory

## Slide 35: An executing program in memory
0xfffffffc
0x00000000
top
bottom
0x7ffffffc
0x80000000
0x10000000
0x00400000
system reserved
(stack grows down)
(heap grows up)
text
reserved
(static) data
(.stack)
.data
.text
system reserved
stack
system reserved
code (text)
static data
dynamic data (heap)
“Data Memory”
“Program Memory”

## Slide 36: Return Address lives in Stack Frame
x2000
x1FD0
Stack Manipulated by push/pop operations
Context: after 2nd JAL to myfn (from myfn)
PUSH: ADDIU $sp, $sp, -20 // move sp down
SW $31, 16($sp) // store retn PC 1st
Context: 2nd myfn is done (r31 == ???)
POP: LW $31, 16($sp) // restore retn PC r31 ADDIU $sp, $sp, 20 // move sp up
JR $31 // return
myfn stack frame
main stack frame
myfn stack frame
after2
r31
r29
x2000
For now: Assume each frame = x20 bytes
(just to make this example concrete)
x1FD0
after2
XXXX

## Slide 37: The Stack
Stack contains stack frames (aka “activation records”)
  1 stack frame per dynamic function
  Exists only for the duration of function
Grows down, “top” of stack is $sp, r29
Example: lw $r1, 0($sp) puts word at top of stack into $r1
Each stack frame contains:
  Local variables, return address (later), register
  backups (later)
myfn stack frame
myfn stack frame
system reserved
stack
system reserved
code
static data
heap
main stack frame
int main(…) {
...
myfn(x);
}
int myfn(int n) {
...
myfn();
}
$sp

## Slide 38: The Heap
Heap holds dynamically allocated memory
Program must maintain pointers to anything allocated
  Example: if $r3 holds x
  lw $r1, 0($r3) gets first word x points to
Data exists from malloc() to free()
2000 bytes
1000 bytes
system reserved
stack
x
y
z
system reserved
code
static data
heap
3000 bytes
void some_function() {
int *x = malloc(1000);
int *y = malloc(2000);
free(y);
int *z = malloc(3000);
}

## Slide 39: Data Segment
Data segment contains global variables
  Exist for all time, accessible to all routines
Accessed w/global pointer
  $gp, r28, points to middle of segment
  Example: lw $r1, 0($gp) gets middle-most word
  (here, max_players)
system reserved
stack
system reserved
code
static data
heap
int max_players = 4;
int main(...) {
...
}
gp
4

## Slide 40: Globals and Locals
int n = 100;
int main (int argc, char* argv[ ]) {
int i, m = n, sum = 0;
int* A = malloc(4*m + 4);
for (i = 1; i <= m; i++) {
sum += i; A[i] = sum; }
printf ("Sum 1 to %d is %d\n", n, sum);
}
Variables Visibility Lifetime Location
Function-Local
Global
Dynamic
Where is i ?
Stack
Heap
Global Data
Text
Where is n ?
Stack
Heap
Global Data
Text
Where is main ?
Stack
Heap
Global Data
Text
Notes: function / func invocation / stack
file or prog / prog execution / data segment
undef / malloc to free / heap
bug in this code

## Slide 41: Globals and Locals
Variables Visibility Lifetime Location
Function-Local
Global
Dynamic
i, m, sum, A
n, str
w/in function
function
invocation
stack
whole program
program
execution
.data
b/w malloc
and free
heap
Anywhere that
has a pointer
*A
int n = 100;
int main (int argc, char* argv[ ]) {
int i, m = n, sum = 0;
int* A = malloc(4*m + 4);
for (i = 1; i <= m; i++) {
sum += i; A[i] = sum; }
printf ("Sum 1 to %d is %d\n", n, sum);
}
Notes: function / func invocation / stack
file or prog / prog execution / data segment
undef / malloc to free / heap
bug in this code

## Slide 42: Takeaway2: Need a Call Stack
JAL (Jump And Link) instruction moves a new value into the PC, and simultaneously saves the old value in register $31 (aka $ra or return address) Thus, can get back from the subroutine to the instruction immediately following the jump by transferring control back to PC in register $31
Need a Call Stack to return to correct calling procedure. To maintain a stack, need to store an activation record (aka a “stack frame”) in memory. Stacks keep track of the correct return address by storing the contents of $31 in memory (the stack).

## Slide 43: Calling Convention for Procedure Calls
Transfer Control
  Caller  Routine
  Routine  Caller
Pass Arguments to and from the routine
  fixed length, variable length, recursively
  Get return value back to the caller
Manage Registers
  Allow each routine to use registers
  Prevent routines from clobbering each others’ data

## Slide 44: Next Goal
Need consistent way of passing arguments and getting the result of a subroutine invocation

## Slide 45: Arguments & Return Values
Need consistent way of passing arguments and getting the result of a subroutine invocation
Given a procedure signature, need to know where arguments should be placed
  int min(int a, int b);
  int subf(int a, int b, int c, int d, int e);
  int isalpha(char c);
  int treesort(struct Tree *root);
  struct Node *createNode();
  struct Node mynode();
Too many combinations of char, short, int, void *, struct, etc.
  MIPS treats char, short, int and void * identically
$a0, $a1
stack?
$a0
$v0, $v1
$v0

## Slide 46: Simple Argument Passing (1-4 args)
First four arguments:
passed in registers $4-$7
  aka $a0, $a1, $a2, $a3
Returned result:
passed back in a register
  Specifically, $2, aka $v0
main:
li $a0, 6
li $a1, 7
jal myfn
addiu $r1, $v0, 2
main() {
int x = myfn(6, 7);
x = x + 2;
}
Note: This is not the entire story for 1-4 arguments.
Please see the Full Story slides.

## Slide 47: Conventions so far:
  args passed in $a0, $a1, $a2, $a3
  return value (if any) in $v0, $v1
  stack frame at $sp
    contains $ra (clobbered on JAL to sub-functions)
Q: What about argument lists?

## Slide 48: Many Arguments (5+ args)
First four arguments:
passed in $4-$7
  aka $a0-$a3
Subsequent arguments:
”spill” onto the stack
main:
li $a0, 0
li $a1, 1
li $a2, 2
li $a3, 3
addiu $sp,$sp,-8
li $8, 4
sw $8, 0($sp)
li $8, 5
sw $8, 4($sp)
jal myfn
main() {
myfn(0,1,2,3,4,5);
…
}
Note: This is not the entire story for 5+ arguments.
Please see the Full Story slides.
sp
5
4
sp

## Slide 49: Argument Passing: the Full Story
Arguments 1-4:
passed in $4-$7
room on stack
Arguments 5+:
placed on stack
main:
li $a0, 0
li $a1, 1
li $a2, 2
li $a3, 3
addiu $sp,$sp,-24
li $8, 4
sw $8, 16($sp)
li $8, 5
sw $8, 20($sp)
jal myfn
main() {
myfn(0,1,2,3,4,5);
…
}
sp
sp
4
space for a3
space for a2
space for a1
space for a0
5
0($sp)
4($sp)
8($sp)
12($sp)
16($sp)
20($sp)
Stack decremented by
max(16, #args x 4)
Here: max (16, 24) = 24

## Slide 50: Pros of Argument Passing Convention
Consistent way of passing arguments to and from subroutines
Creates single location for all arguments
  Caller makes room for $a0-$a3 on stack
  Callee must copy values from $a0-$a3 to stack
   callee may treat all args as an array in memory
  Particularly helpful for functions w/ variable length inputs: printf(“Scores: %d %d %d\n”, 1, 2, 3);
Aside: not a bad place to store inputs if callee needs to call a function (your input cannot stay in $a0 if you need to call another function!)

## Slide 51: iClicker Question
  Which is a true statement about the arguments to the function
  void sub(int a, int b, int c, int d, int e);
Arguments a-e are all passed in registers.
Arguments a-e are all stored on the stack.
Only e is stored on the stack, but space is allocated for all 5 arguments.
Only a-d are stored on the stack, but space is allocated for all 5 arguments.

## Slide 52: iClicker Question
  Which is a true statement about the arguments to the function
  void sub(int a, int b, int c, int d, int e);
Arguments a-e are all passed in registers.
Arguments a-e are all stored on the stack.
Only e is stored on the stack, but space is allocated for all 5 arguments.
Only a-d are stored on the stack, but space is allocated for all 5 arguments.

## Slide 53: Frame Layout & the Frame Pointer
4
space for a3
space for a2
space for a1
space for a0
5
blue() {
pink(0,1,2,3,4,5);
}
blue’s Ret Addr
sp
blue’s stack frame
sp

## Slide 54: Frame Layout & the Frame Pointer
4
space for a3
space for a2
space for a1
space for a0
5
pink’s Ret Addr
blue() {
pink(0,1,2,3,4,5);
}
pink(int a, int b, int c, int d, int e, int f) {
…
}
blue’s Ret Addr
pink’s stack frame
sp
sp
blue’s stack frame
Notice
Pink’s arguments are on blue’s stack
sp changes as functions call other functions, complicates accesses
 Convenient to keep pointer to bottom of stack == frame pointer
$30, aka $fp
can be used to restore $sp on exit
 fp

## Slide 55: Conventions so far
  first four arg words passed in $a0, $a1, $a2, $a3
  remaining arg words passed in parent’s stack frame
  return value (if any) in $v0, $v1
  stack frame ($fp to $sp) contains:
    $ra (clobbered on JAL to sub-functions)
    space for 4 arguments to Callees
    arguments 5+ to Callees
Notes: Q: Minimum frame size?
A: 24 bytes (ra+fp+4args)
Q: What if this function makes no sub-calls?

## Slide 56: MIPS Register Conventions so far:
r0 | $zero | zero
r1 | $at | assembler temp
r2 |  | 
r3 |  | 
r4 |  | 
r5 |  | 
r6 |  | 
r7 |  | 
r8 |  | 
r9 |  | 
r10 |  | 
r11 |  | 
r12 |  | 
r13 |  | 
r14 |  | 
r15 |  | 
r16 |  | 
r17 |  | 
r18 |  | 
r19 |  | 
r20 |  | 
r21 |  | 
r22 |  | 
r23 |  | 
r24 |  | 
r25 |  | 
r26 | $k0 | reserved for OS kernel
r27 | $k1 | 
r28 |  | 
r29 |  | 
r30 |  | 
r31 | $ra | return address
 | $v0 | function return values
 | $v1 | 
 | $a0 | function arguments
 | $a1 | 
 | $a2 | 
 | $a3 | 
Pseudo-Instructions
e.g. BLZ
SLT $at
BNE $at, 0, L
Notes: why $at? BLT psuedo-instruction and others

## Slide 57: C & MIPS: the fine print
C allows passing whole structs
  int dist(struct Point p1, struct Point p2);
  Treated as collection of consecutive 32-bit arguments
    Registers for first 4 words, stack for rest
  Better: int dist(struct Point *p1, struct Point *p2);
Where are the arguments to:
  void sub(int a, int b, int c, int d, int e);
  void isalpha(char c);
  void treesort(struct Tree *root);
Where are the return values from:
  struct Node *createNode();
  struct Node mynode();
Many combinations of char, short, int, void *, struct, etc.
  MIPS treats char, short, int and void * identically
$a0, $a1
$a2, $a3
$a0
$a1
$a0, $a1
stack
$a0
$v0, $v1
$v0

## Slide 58: Globals and Locals
Global variables are allocated in the “data” region of the program
  Exist for all time, accessible to all routines
Local variables are allocated within the stack frame
  Exist solely for the duration of the stack frame
Dangling pointers are pointers into a destroyed stack frame
  C lets you create these, Java does not
  int *foo() { int a; return &a; }
Return the address of a,
But a is stored on stack, so will be removed
when call returns and point will be invalid

## Slide 59: Global and Locals
How does a function load global data?
  global variables are just above 0x10000000
Convention: global pointer
  $28 is $gp (pointer into middle of global data section) $gp = 0x10008000
  Access most global data using LW at $gp +/- offset LW $v0, 0x8000($gp) LW $v1, 0x7FFF($gp)
Notes: # data at 0x10000000
# data at 0x1000FFFF
(64KB range)

## Slide 60: Anatomy of an executing program
0xfffffffc
0x00000000
top
bottom
0x7ffffffc
0x80000000
0x10000000
0x00400000
system reserved
(stack grows down)
(heap grows up)
text
reserved
(static) data
(.stack)
.data
.text
system reserved
stack
system reserved
$gp
code (text)
static data
dynamic data (heap)

## Slide 61: Frame Pointer
It is often cumbersome to keep track of location of data on the stack
  The offsets change as new values are pushed onto and popped off of the stack
Keep a pointer to the bottom of the top stack frame
  Simplifies the task of referring to items on the stack
A frame pointer, $30, aka $fp
  Value of $sp upon procedure entry
  Can be used to restore $sp on exit

## Slide 62: Conventions so far
first four arg words passed in $a0-$a3
remaining args passed in parent’s stack frame
return value (if any) in $v0, $v1
stack frame ($fp to $sp) contains:
  $ra (clobbered on JALs)
  space for 4 arguments to Callees
  arguments 5+ to Callees
global data accessed via $gp
Notes: Q: Minimum frame size?
A: 24 bytes (ra+fp+4args)
Q: What if this function makes no sub-calls?

## Slide 63: Calling Convention for Procedure Calls
Transfer Control
  Caller  Routine
  Routine  Caller
Pass Arguments to and from the routine
  fixed length, variable length, recursively
  Get return value back to the caller
Manage Registers
  Allow each routine to use registers
  Prevent routines from clobbering each others’ data

## Slide 64: Next Goal
What convention should we use to share use of registers across procedure calls?

## Slide 65: Register Management
Functions:
Are compiled in isolation
Make use of general purpose registers
Call other functions in the middle of their execution
  These functions also use general purpose registers!
  No way to coordinate between caller & callee
 Need a convention for register management
Notes: Also, $gp is a callee save register

## Slide 66: Register Usage
Suppose a routine would like to store a value in a register
Two options: callee-save and caller-save
Callee-save:
  Assume that one of the callers is already using that register to hold a value of interest
  Save the previous contents of the register on procedure entry, restore just before procedure return
  E.g. $31
Caller-save:
  Assume that a caller can clobber any one of the registers
  Save the previous contents of the register before proc call
  Restore after the call
MIPS calling convention supports both

## Slide 67: Caller-saved
Registers that the caller cares about: $t0… $t9
About to call a function?
Need value in a t-register after function returns?
 save it to the stack before fn call
 restore it from the stack after fn returns
Don’t need value?  do nothing
Functions
  Can freely use these registers
  Must assume that their contents
  are destroyed by other functions
void myfn(int a) {
int x = 10;
int y = max(x, a);
int z = some_fn(y);
return (z + y);
}
Suppose:
$t0 holds x
$t1 holds y
$t2 holds z
Where do we save and restore?

## Slide 68: Callee-saved
Registers a function intends to use: $s0… $s9
About to use an s-register? You MUST:
Save the current value on the stack before using
Restore the old value from the stack before fn returns
Functions
  Must save these registers before
  using them
  May assume that their contents
  are preserved even across fn calls
void myfn(int a) {
int x = 10;
int y = max(x, a);
int z = some_fn(y);
return (z + y);
}
Suppose:
$t0 holds x
$s1 holds y
$s2 holds z
Where do we save and restore?

## Slide 69: Caller-Saved Registers in Practice
Assume the registers are free for the taking, use with no overhead
Since subroutines will do the same, must protect values needed later:
  Save before fn call
  Restore after fn call
Notice: Good registers to use if you don’t call too many functions or if the values don’t matter later on anyway.
main:
…
[use $8 & $9]
…
addiu $sp,$sp,-8
sw $9, 4($sp)
sw $8, 0($sp)
jal mult
lw $9, 4($sp)
lw $8, 0($sp)
addiu $sp,$sp,8
…
[use $8 & $9]

## Slide 70: Caller-Saved Registers in Practice
Assume the registers are free for the taking, use with no overhead
Since subroutines will do the same, must protect values needed later:
  Save before fn call
  Restore after fn call
Notice: Good registers to use if you don’t call too many functions or if the values don’t matter later on anyway.
main:
…
[use $t0 & $t1]
…
addiu $sp,$sp,-8
sw $t1, 4($sp)
sw $t0, 0($sp)
jal mult
lw $t1, 4($sp)
lw $t0, 0($sp)
addiu $sp,$sp,8
…
[use $t0 & $t1]

## Slide 71: Callee-Saved Registers in Practice
Assume caller is using the registers
Save on entry
Restore on exit
Notice: Good registers to use if you make a lot of function calls and need values that are preserved across all of them.
Also, good if caller is actually using the registers, otherwise the save and restores are wasted. But hard to know this.
main:
addiu $sp,$sp,-32
sw $31,28($sp)
sw $30, 24($sp)
sw $17, 20($sp)
sw $16, 16($sp)
addiu $fp, $sp, 28
…
[use $16 and $17]
…
lw $31,28($sp)
lw $30,24($sp)
lw $17, 20$sp)
lw $16, 16($sp)
addiu $sp,$sp,32
jr $31

## Slide 72: Callee-Saved Registers in Practice
Assume caller is using the registers
Save on entry
Restore on exit
Notice: Good registers to use if you make a lot of function calls and need values that are preserved across all of them.
Also, good if caller is actually using the registers, otherwise the save and restores are wasted. But hard to know this.
main:
addiu $sp,$sp,-32
sw $ra,28($sp)
sw $fp, 24($sp)
sw $s1, 20($sp)
sw $s0, 16($sp)
addiu $fp, $sp, 28
…
[use $s0 and $s1]
…
lw $ra,28($sp)
lw $fp,24($sp)
lw $s1, 20$sp)
lw $s0, 16($sp)
addiu $sp,$sp,32
jr $ra

## Slide 73: Caller-saved vs. Callee-saved
Callee-save register:
  Assumes register not changed across procedure call
  Thus, callee must save the previous contents of the register on procedure entry, restore just before procedure return
  E.g. $ra, $fp, $s0-s7
Caller-save register:
  Assumes that a caller can clobber contents of register
  Thus, caller must save the previous contents of the register before proc call
  Caller, then, restores after the call to subroutine returns
  E.g. $a0-a3, $v0-$v1, $t0-$t9
MIPS calling convention supports both
Notes: Also, $gp is a callee save register

## Slide 74: Caller-saved vs. Callee-saved
Callee-save register:
  Assumes register not changed across procedure call
  Thus, callee must save the previous contents of the register on procedure entry, restore just before procedure return
  E.g. $ra, $fp, $s0-s7, $gp
  Also, $sp
Caller-save register:
  Assumes that a caller can clobber contents of register
  Thus, caller must save the previous contents of the register before proc call
  Caller, then, restores after the call to subroutine returns
  E.g. $a0-a3, $v0-$v1, $t0-$t9
MIPS calling convention supports both
Notes: Also, $gp is a callee save register

## Slide 75: Clicker Question
You are a compiler. Do you choose to put a in a:
Caller-saved register (t)
Callee-saved register (s)
Depends on where we put the other variables in this fn
Both are equally valid
.

## Slide 76: Clicker Question
You are a compiler. Do you choose to put a in a:
Caller-saved register (t)
Callee-saved register (s)
Depends on where we put the other variables in this fn
Both are equally valid
.

## Slide 77: Clicker Question
You are a compiler. Do you choose to put a in a:
Caller-saved register (t)
Callee-saved register (s)
Depends on where we put the other variables in this fn
Both are equally valid
Repeat but assume that foo is recursive (bar/baz  foo)

## Slide 78: Clicker Question
You are a compiler. Do you choose to put a in a:
Caller-saved register (t)
Callee-saved register (s)
Depends on where we put the other variables in this fn
Both are equally valid
Repeat but assume that foo is recursive (bar/baz  foo)

## Slide 79: Frame Layout on Stack
Assume a function uses two callee-save registers.
How do we allocate a stack frame? How large is the stack frame?
What should be stored in the stack frame?
Where should everything be stored?
saved ra
saved fp
saved regs ($s0 ... $s7)
locals
outgoing args
fp 
sp 
Notes: Q: Minimum frame size?
A: 24 bytes (ra+fp+4args)
Q: What if this function makes no sub-calls?

## Slide 80: Frame Layout on Stack
ADDIU $sp, $sp, -32 # allocate frame
SW $ra, 28($sp) # save $ra
SW $fp, 24($sp) # save old $fp
SW $s1, 20($sp) # save ...
SW $s0, 16($sp) # save ...
ADDIU $fp, $sp, 28 # set new frame ptr
… ...
BODY
… ...
LW $s0, 16($sp) # restore …
LW $s1, 20($sp) # restore …
LW $fp, 24($sp) # restore old $fp
LW $ra, 28($sp) # restore $ra
ADDIU $sp,$sp, 32 # dealloc frame
JR $ra
saved ra
saved fp
saved regs ($s0 ... $s7)
locals
outgoing args
fp 
sp 

## Slide 81: Frame Layout on Stack
blue() {
pink(0,1,2,3,4,5);
}
saved regs
args for pink
saved fp
blue’s ra
fp
blue’s stack frame
sp

## Slide 82: Frame Layout on Stack
pink’s ra
blue() {
pink(0,1,2,3,4,5);
}
pink(int a, int b, int c, int d, int e, int f) {
int x;
orange(10,11,12,13,14);
}
saved regs
args for pink
blue’s fp
saved fp
saved regs
blue’s ra
pink’s stack frame
fp
blue’s stack frame
x
args for orange
sp

## Slide 83: Frame Layout on Stack
pink’s ra
blue() {
pink(0,1,2,3,4,5);
}
pink(int a, int b, int c, int d, int e, int f) {
int x;
orange(10,11,12,13,14);
}
orange(int a, int b, int c, int, d, int e) {
char buf[100];
gets(buf); // no bounds check!
}
What happens if more than 100 bytes
is written to buf?
saved regs
args for pink
blue’s fp
saved fp
saved regs
blue’s ra
pink’s stack frame
fp
blue’s stack frame
x
args for orange
sp
orange’s ra
pink’s fp
saved regs
orange
stack frame
buf[100]

## Slide 84: Buffer Overflow
pink’s ra
blue() {
pink(0,1,2,3,4,5);
}
pink(int a, int b, int c, int d, int e, int f) {
int x;
orange(10,11,12,13,14);
}
orange(int a, int b, int c, int, d, int e) {
char buf[100];
gets(buf); // no bounds check!
}
What happens if more than 100 bytes
is written to buf?
saved regs
args for pink
blue’s fp
saved fp
saved regs
blue’s ra
pink’s stack frame
fp
blue’s stack frame
x
args for orange
sp
orange’s ra
pink’s fp
saved regs
orange
stack frame
buf[100]

## Slide 85: MIPS Register Recap
Return address: $31 (ra)
Stack pointer: $29 (sp)
Frame pointer: $30 (fp)
First four arguments: $4-$7 (a0-a3)
Return result: $2-$3 (v0-v1)
Callee-save free regs: $16-$23 (s0-s7)
Caller-save free regs: $8-$15,$24,$25 (t0-t9)
Reserved: $26, $27
Global pointer: $28 (gp)
Assembler temporary: $1 (at)

## Slide 86: MIPS Register Conventions
r0 | $zero | zero
r1 | $at | assembler temp
r2 | $v0 | function return values
r3 | $v1 | 
r4 | $a0 | function arguments
r5 | $a1 | 
r6 | $a2 | 
r7 | $a3 | 
r8 | $t0 | temps (caller save)
r9 | $t1 | 
r10 | $t2 | 
r11 | $t3 | 
r12 | $t4 | 
r13 | $t5 | 
r14 | $t6 | 
r15 | $t7 | 
r16 | $s0 | saved (callee save)
r17 | $s1 | 
r18 | $s2 | 
r19 | $s3 | 
r20 | $s4 | 
r21 | $s5 | 
r22 | $s6 | 
r23 | $s7 | 
r24 | $t8 | more temps (caller save)
r25 | $t9 | 
r26 | $k0 | reserved for kernel
r27 | $k1 | 
r28 | $gp | global data pointer
r29 | $sp | stack pointer
r30 | $fp | frame pointer
r31 | $ra | return address

## Slide 87: Convention Summary
first four arg words passed in $a0-$a3
remaining args passed in parent’s stack frame
return value (if any) in $v0, $v1
stack frame ($fp to $sp) contains:
  $ra (clobbered on JALs)
  local variables
  space for 4 arguments to Callees
  arguments 5+ to Callees
callee save regs: preserved
caller save regs: not preserved
global data accessed via $gp
saved ra
saved fp
saved regs ($s0 ... $s7)
locals
outgoing args
$fp 
$sp 
Notes: Q: Minimum frame size?
A: 24 bytes (ra+fp+4args)
Q: What if this function makes no sub-calls?

## Slide 88: Activity #1: Calling Convention Example
s0 = a0
s1 = a1
t0 = a & b
t1 = a | b
t0 = t0 + t1
SW t0, 24(sp) # tmp
a0 = t0
a1 = 1
a2 = 2
a3 = 3
SW 4, 0(sp)
SW 5, 4(sp)
JAL sum
NOP
LW t0, 24(sp)
a0 = v0
a1 = t0
a2 = s1
a3 = s0
SW s1, 0(sp)
SW s0, 4(sp)
JAL sum
NOP
v0 = v0 + s0 + s1
int test(int a, int b) {
int tmp = (a&b)+(a|b);
int s = sum(tmp,1,2,3,4,5);
int u = sum(s,tmp,b,a,b,a);
return u + a + b;
}
Correct Order:
Body First
Determine stack frame size
Complete Prologue/Epilogue

## Slide 89: Activity #1: Calling Convention Example
int test(int a, int b) {
int tmp = (a&b)+(a|b);
int s = sum(tmp,1,2,3,4,5);
int u = sum(s,tmp,b,a,b,a);
return u + a + b;
}
s0 = a0
s1 = a1
t0 = a & b
t1 = a | b
t0 = t0 + t1
SW t0, 24(sp) # tmp
a0 = t0
a1 = 1
a2 = 2
a3 = 3
SW 4, 0(sp)
SW 5, 4(sp)
JAL sum
NOP
LW t0, 24(sp)
a0 = v0
a1 = t0
a2 = s1
a3 = s0
SW s1, 0(sp)
SW s0, 4(sp)
JAL sum
NOP
v0 = v0 + s0 + s1
test:
MOVE $s0, $a0
MOVE $s1, $a1
AND $t0, $a0, $a1
OR $t1, $a0, $a1
ADD $t0, $t0, $t1
MOVE $a0, $t0
LI $a1, 1
LI $a2, 2
LI $a3, 3
LI $t1, 4
SW $t1 16($sp)
LI $t1, 5
SW $t1, 20($sp)
SW $t0, 24($sp)
JAL sum
NOP
LW $t0, 24($sp)
MOVE $a0, $v0 # s
MOVE $a1, $t0 # tmp
MOVE $a2, $s1 # b
MOVE $a3, $s0 # a
SW $s1, 16($sp)
SW $s0, 20($sp)
JAL sum
NOP
# add u (v0) and a (s0)
ADD $v0, $v0, $s0
ADD $v0, $v0, $s1
# $v0 = u + a + b
Prologue
Epilogue

## Slide 90: Activity #1: Calling Convention Example
int test(int a, int b) {
int tmp = (a&b)+(a|b);
int s = sum(tmp,1,2,3,4,5);
int u = sum(s,tmp,b,a,b,a);
return u + a + b;
}
s0 = a0
s1 = a1
t0 = a & b
t1 = a | b
t0 = t0 + t1
SW t0, 24(sp) # tmp
a0 = t0
a1 = 1
a2 = 2
a3 = 3
SW 4, 0(sp)
SW 5, 4(sp)
JAL sum
NOP
LW t0, 24(sp)
a0 = v0
a1 = t0
a2 = s1
a3 = s0
SW s1, 0(sp)
SW s0, 4(sp)
JAL sum
NOP
v0 = v0 + s0 + s1
test:
MOVE $s0, $a0
MOVE $s1, $a1
AND $t0, $a0, $a1
OR $t1, $a0, $a1
ADD $t0, $t0, $t1
MOVE $a0, $t0
LI $a1, 1
LI $a2, 2
LI $a3, 3
LI $t1, 4
SW $t1 16($sp)
LI $t1, 5
SW $t1, 20($sp)
SW $t0, 24($sp)
JAL sum
NOP
LW $t0, 24($sp)
MOVE $a0, $v0 # s
MOVE $a1, $t0 # tmp
MOVE $a2, $s1 # b
MOVE $a3, $s0 # a
SW $s1, 16($sp)
SW $s0, 20($sp)
JAL sum
NOP
# add u (v0) and a (s0)
ADD $v0, $v0, $s0
ADD $v0, $v0, $s1
# $v0 = u + a + b
Prologue
Epilogue
How many bytes do we
need to allocate for the
stack frame?
24
32
40
44
48

## Slide 91: Activity #1: Calling Convention Example
int test(int a, int b) {
int tmp = (a&b)+(a|b);
int s = sum(tmp,1,2,3,4,5);
int u = sum(s,tmp,b,a,b,a);
return u + a + b;
}
s0 = a0
s1 = a1
t0 = a & b
t1 = a | b
t0 = t0 + t1
SW t0, 24(sp) # tmp
a0 = t0
a1 = 1
a2 = 2
a3 = 3
SW 4, 0(sp)
SW 5, 4(sp)
JAL sum
NOP
LW t0, 24(sp)
a0 = v0
a1 = t0
a2 = s1
a3 = s0
SW s1, 0(sp)
SW s0, 4(sp)
JAL sum
NOP
v0 = v0 + s0 + s1
test:
MOVE $s0, $a0
MOVE $s1, $a1
AND $t0, $a0, $a1
OR $t1, $a0, $a1
ADD $t0, $t0, $t1
MOVE $a0, $t0
LI $a1, 1
LI $a2, 2
LI $a3, 3
LI $t1, 4
SW $t1 16($sp)
LI $t1, 5
SW $t1, 20($sp)
SW $t0, 24($sp)
JAL sum
NOP
LW $t0, 24($sp)
MOVE $a0, $v0 # s
MOVE $a1, $t0 # tmp
MOVE $a2, $s1 # b
MOVE $a3, $s0 # a
SW $s1, 16($sp)
SW $s0, 20($sp)
JAL sum
NOP
# add u (v0) and a (s0)
ADD $v0, $v0, $s0
ADD $v0, $v0, $s1
# $v0 = u + a + b
saved ra
saved fp
saved regs ($s0 and $s1)
locals
($t0)
outgoing args
space for a0 - a3
and 5th and 6th arg
$fp 
$sp 
Prologue
Epilogue

## Slide 92: Activity #1: Calling Convention Example
int test(int a, int b) {
int tmp = (a&b)+(a|b);
int s = sum(tmp,1,2,3,4,5);
int u = sum(s,tmp,b,a,b,a);
return u + a + b;
}
s0 = a0
s1 = a1
t0 = a & b
t1 = a | b
t0 = t0 + t1
SW t0, 24(sp) # tmp
a0 = t0
a1 = 1
a2 = 2
a3 = 3
SW 4, 0(sp)
SW 5, 4(sp)
JAL sum
NOP
LW t0, 24(sp)
a0 = v0
a1 = t0
a2 = s1
a3 = s0
SW s1, 0(sp)
SW s0, 4(sp)
JAL sum
NOP
v0 = v0 + s0 + s1
test:
MOVE $s0, $a0
MOVE $s1, $a1
AND $t0, $a0, $a1
OR $t1, $a0, $a1
ADD $t0, $t0, $t1
MOVE $a0, $t0
LI $a1, 1
LI $a2, 2
LI $a3, 3
LI $t1, 4
SW $t1 16($sp)
LI $t1, 5
SW $t1, 20($sp)
SW $t0, 24($sp)
JAL sum
NOP
LW $t0, 24($sp)
MOVE $a0, $v0 # s
MOVE $a1, $t0 # tmp
MOVE $a2, $s1 # b
MOVE $a3, $s0 # a
SW $s1, 16($sp)
SW $s0, 20($sp)
JAL sum
NOP
# add u (v0) and a (s0)
ADD $v0, $v0, $s0
ADD $v0, $v0, $s1
# $v0 = u + a + b
saved ra
saved fp
$fp 
$sp 
Prologue
Epilogue
saved reg $s1
saved reg $s0
local $t0
outgoing 6th arg
outgoing 5th arg
space for $a3
space for $a2
space for $a1
space for $a0
4
8
12
16
0
20
24
28
32
36
40

## Slide 93: Activity #2: Calling Convention Example: Prologue, Epilogue
ADDIU $sp, $sp, -40
SW $ra, 36($sp)
SW $fp, 32($sp)
SW $s0, 28($sp)
SW $s5, 24($sp)
ADDIU $fp, $sp, 40
...
...
LW $s5, 24($sp)
LW $s0, 28($sp)
LW $fp, 32($sp)
LW $ra, 36($sp)
ADDIU $sp, $sp, 40
JR $ra
# allocate frame
# save $ra
# save old $fp
# callee save ...
# callee save ...
# set new frame ptr
...
...
# restore …
# restore …
# restore old $fp
# restore $ra
# dealloc frame
test:
saved ra
saved fp
$fp 
$sp 
saved reg $s1
saved reg $s0
local $t0
outgoing 6th arg
outgoing 5th arg
space for $a3
space for $a2
space for $a1
space for $a0
4
8
12
16
0
20
24
28
32
36
40

## Slide 94: Activity #2: Calling Convention Example: Prologue, Epilogue
# allocate frame
# save $ra
# save old $fp
# callee save ...
# callee save ...
# set new frame ptr
...
...
# restore …
# restore …
# restore old $fp
# restore $ra
# dealloc frame
ADDIU $sp, $sp, -40
SW $ra, 36($sp)
SW $fp, 32($sp)
SW $s0, 28($sp)
SW $s5, 24($sp)
ADDIU $fp, $sp, 40
...
...
LW $s5, 24($sp)
LW $s0, 28($sp)
LW $fp, 32($sp)
LW $ra, 36($sp)
ADDIU $sp, $sp, 40
JR $ra
test:
ADDIU $sp, $sp, -44
SW $ra, 40($sp)
SW $fp, 36($sp)
SW $s1, 32($sp)
SW $s0, 28($sp)
ADDIU $fp, $sp, 40
LW $s0, 28($sp)
LW $s1, 32($sp)
LW $fp, 36($sp)
LW $ra, 40($sp)
ADDIU $sp, $sp, 44
JR $ra
NOP
Body
(previous slide, Activity #1)
saved ra
saved fp
$fp 
$sp 
saved reg $s1
saved reg $s0
local $t0
outgoing 6th arg
outgoing 5th arg
space for $a3
space for $a2
space for $a1
space for $a0
4
8
12
16
0
20
24
28
32
36
40
Space for $t0
and six args
to pass to
subroutine

## Slide 95: Next Goal
Can we optimize the assembly code at all?

## Slide 96: Activity #3: Calling Convention Example
int test(int a, int b) {
int tmp = (a&b)+(a|b);
int s = sum(tmp,1,2,3,4,5);
int u = sum(s,tmp,b,a,b,a);
return u + a + b;
}
s0 = a0
s1 = a1
t0 = a & b
t1 = a | b
t0 = t0 + t1
SW t0, 24(sp) # tmp
a0 = t0
a1 = 1
a2 = 2
a3 = 3
SW 4, 0(sp)
SW 5, 4(sp)
JAL sum
NOP
LW t0, 24(sp)
a0 = v0
a1 = t0
a2 = s1
a3 = s0
SW s1, 0(sp)
SW s0, 4(sp)
JAL sum
NOP
v0 = v0 + s0 + s1
test:
MOVE $s0, $a0
MOVE $s1, $a1
AND $t0, $a0, $a1
OR $t1, $a0, $a1
ADD $t0, $t0, $t1
MOVE $a0, $t0
LI $a1, 1
LI $a2, 2
LI $a3, 3
LI $t1, 4
SW $t1 16($sp)
LI $t1, 5
SW $t1, 20($sp)
SW $t0, 24($sp)
JAL sum
NOP
LW $t0, 24($sp)
MOVE $a0, $v0 # s
MOVE $a1, $t0 # tmp
MOVE $a2, $s1 # b
MOVE $a3, $s0 # a
SW $s1, 16($sp)
SW $s0, 20($sp)
JAL sum
NOP
# add u (v0) and a (s0)
ADD $v0, $v0, $s0
ADD $v0, $v0, $s1
# $v0 = u + a + b
Prologue
Epilogue
How can we optimize
the assembly code?
Notes: Optimize by removing the NOPs. That is, putting a independent instruction in the delay slot

## Slide 97: Activity #3: Calling Convention Example: Prologue, Epilogue
# allocate frame
# save $ra
# save old $fp
# callee save ...
# callee save ...
# set new frame ptr
...
...
# restore …
# restore …
# restore old $fp
# restore $ra
# dealloc frame
ADDIU $sp, $sp, -40
SW $ra, 36($sp)
SW $fp, 32($sp)
SW $s0, 28($sp)
SW $s5, 24($sp)
ADDIU $fp, $sp, 40
...
...
LW $s5, 24($sp)
LW $s0, 28($sp)
LW $fp, 32($sp)
LW $ra, 36($sp)
ADDIU $sp, $sp, 40
JR $ra
test:
ADDIU $sp, $sp, -44
SW $ra, 40($sp)
SW $fp, 36($sp)
SW $s1, 32($sp)
SW $s0, 28($sp)
ADDIU $fp, $sp, 40
LW $s0, 28($sp)
LW $s1, 32($sp)
LW $fp, 36($sp)
LW $ra, 40($sp)
ADDIU $sp, $sp, 44
JR $ra
NOP
Body

## Slide 98: Minimum stack size for a standard function?
Notes: Q: Minimum frame size?
A: 24 bytes (ra+fp+4args)
Q: What if this function makes no sub-calls?

## Slide 99: Minimum stack size for a standard function?
24 bytes = 6x 4 bytes ($ra + $fp + 4 args)
saved ra
saved fp
saved regs ($s0 ... $s7)
locals
outgoing args
$fp 
$sp 
Notes: Q: Minimum frame size?
A: 24 bytes (ra+fp+4args)
Q: What if this function makes no sub-calls?

## Slide 100: Leaf Functions
Leaf function does not invoke any other functions
int f(int x, int y) { return (x+y); }
Optimizations?
No saved regs (or locals)
No outgoing args
Don’t push $ra
No frame at all?
Maybe.
saved ra
saved fp
saved regs ($s0 ... $s7)
locals
outgoing args
$fp 
$sp 

## Slide 101: Next Goal
Given a running program (a process), how do we know what is going on (what function is executing, what arguments were passed to where, where is the stack and current stack frame, where is the code and data, etc)?

## Slide 102: Anatomy of an executing program
0xfffffffc
0x00000000
top
bottom
0x7ffffffc
0x80000000
0x10000000
0x00400000
system reserved
(stack grows down)
(heap grows up)
text
reserved
(static) data
(.stack)
.data
.text
system reserved
stack
system reserved
.data
.text
PC
code (text)
static data
dynamic data (heap)

## Slide 103: Activity #4: Debugging
init(): 0x400000
printf(s, …): 0x4002B4
vnorm(a,b): 0x40107C
main(a,b): 0x4010A0
pi: 0x10000000
str1: 0x10000004
0x00000000
0x004010c4
0x00000000
0x00000000
0x7FFFFFF4
0x00000000
0x00000000
0x0040010c
0x00000015
0x10000004
0x00401090
0x00000000
0x00000000
CPU:
$pc=0x004003C0
$sp=0x7FFFFFAC
$ra=0x00401090
0x7FFFFFB0
What func is running?
Who called it?
Has it called anything?
Will it?
Args?
Stack depth?
Call trace?
0x7FFFFFDC
Notes: pc  in printf
ra  called from vnorm? or called vnorm?
0(sp)  looks like in printf, called by vnorm, and not going to call anything else
4,8(sp)  looks like args are str1 and 0x15
20(sp)  looks like a return address, probably main called vnorm with less than 4 args
44(sp)  looks like a return address, probably init called main
how large is init’s stack frame?

## Slide 104: Activity #4: Debugging
init(): 0x400000
printf(s, …): 0x4002B4
vnorm(a,b): 0x40107C
main(a,b): 0x4010A0
pi: 0x10000000
str1: 0x10000004
0x00000000
0x004010c4
0x00000000
0x00000000
0x7FFFFFF4
0x00000000
0x00000000
0x0040010c
0x00000015
0x10000004
0x00401090
0x00000000
0x00000000
CPU:
$pc=0x004003C0
$sp=0x7FFFFFAC
$ra=0x00401090
0x7FFFFFB0
What func is running?
Who called it?
Has it called anything?
Will it?
Args?
Stack depth?
Call trace?
0x7FFFFFDC
printf
vnorm
no
no
printf, vnorm, main, init
Str1 and 0x15
4
0x7FFFFFAC
0x7FFFFFB4
0x7FFFFFB8
0x7FFFFFBC
0x7FFFFFC0
0x7FFFFFC4
0x7FFFFFC8
0x7FFFFFCA
0x7FFFFFD0
0x7FFFFFD4
0x7 …D8
DC
E0
Memory
ra
fp
a3
a2
a1
a0
ra
fp
a3
a2
a1
a0
a0
ra
E4
E8
EA
…F0
…F4
a1
a2
a3
fp
ra
b/c no space for
outgoing args
0x7FFFFFA8
main
vnorm
0x7FFFFFC4
printf
Notes: pc  in printf
ra  called from vnorm? or called vnorm?
0(sp)  looks like in printf, called by vnorm, and not going to call anything else
4,8(sp)  looks like args are str1 and 0x15
20(sp)  looks like a return address, probably main called vnorm with less than 4 args
44(sp)  looks like a return address, probably init called main
how large is init’s stack frame?

## Slide 105: Recap
  How to write and Debug a MIPS program using calling convention
  first four arg words passed in $a0, $a1, $a2, $a3
  remaining arg words passed in parent’s stack frame
  return value (if any) in $v0, $v1
  stack frame ($fp to $sp) contains:
    $ra (clobbered on JAL to sub-functions)
    $fp
    local vars (possibly clobbered by sub-functions)
    contains extra arguments to sub-functions
    (i.e. argument “spilling)
    contains space for first 4 arguments
    to sub-functions
  callee save regs are preserved
  caller save regs are not
  Global data accessed via $gp
saved ra
saved fp
saved regs ($s0 ... $s7)
locals
outgoing args
$fp 
$sp 
Notes: Q: Minimum frame size?
A: 24 bytes (ra+fp+4args)
Q: What if this function makes no sub-calls?