## Slide 1: Performance
Hakim Weatherspoon
CS 3410
Computer Science
Cornell University
The slides are the product of many rounds of teaching CS 3410 by Professors Weatherspoon, Bala, Bracy, and Sirer.

## Slide 2: Goals for today
Performance
  What is performance?
  How to get it?

## Slide 3: Performance
Complex question
  How fast is the processor?
  How fast your application runs?
  How quickly does it respond to you?
  How fast can you process a big batch of jobs?
  How much power does your machine use?

## Slide 4: Measures of Performance
Clock speed
  1 KHz, 103 Hz: cycle is 1 millisecond, ms, (10-6)
  1 MHz, 106 Hz: cycle is 1 microsecond, us, (10-6)
  1 Ghz, 109 Hz: cycle is 1 nanosecond, ns, (10-9)
  1 Thz, 1012 Hz: cycle is 1 picosecond, ps, (10-12)
Instruction/application performance
  MIPs (Millions of instructions per second)
  FLOPs (Floating point instructions per second)
    GPUs: GeForce GTX Titan (2,688 cores, 4.5 Tera flops, 7.1 billion transistors, 42 Gigapixel/sec fill rate, 288 GB/sec)
  Benchmarks (SPEC)
Notes: Peta: 10^(-15)
Exa: 10^(-18)
Zotta: 10^(-21)
Yotta: 10^(-24)
Benchmarks like SPEC are used to compare across architectures

## Slide 5: Measures of Performance
CPI: “Cycles per instruction”→Cycle/instruction for on average
  IPC = 1/CPI
    Used more frequently than CPI
    Favored because “bigger is better”, but harder to compute with
  Different instructions have different cycle costs
    E.g., “add” typically takes 1 cycle, “divide” takes >10 cycles
  Depends on relative instruction frequencies
CPI example
  Program has equal ratio: integer, memory, floating point
  Cycles per insn type: integer = 1, memory = 2, FP = 3
  What is the CPI? (33% * 1) + (33% * 2) + (33% * 3) = 2
  Caveat: calculation ignores many effects
    Back-of-the-envelope arguments only

## Slide 6: Measures of Performance
General public (mostly) ignores CPI
  Equates clock frequency with performance!
Which processor would you buy?
  Processor A: CPI = 2, clock = 5 GHz
  Processor B: CPI = 1, clock = 3 GHz
  Probably A, but B is faster (assuming same ISA/compiler)
Classic example
  800 MHz PentiumIII faster than 1 GHz Pentium4!
  Example: Core i7 faster clock-per-clock than Core 2
  Same ISA and compiler!
Meta-point: danger of partial performance metrics!

## Slide 7: Measures of Performance
Latency
  How long to finish my program
    Response time, elapsed time, wall clock time
    CPU time: user and system time
Throughput
  How much work finished per unit time
Ideal: Want high throughput, low latency
… also, low power, cheap ($$) etc.

## Slide 8: iClicker Question #1: Car vs. Bus
#2 Bus Throughput
Car: speed = 60 miles/hour, capacity = 5
Bus: speed = 20 miles/hour, capacity = 60
Task: transport passengers 10 miles
 | Latency (min) | Throughput (PPH)
Car |  | 
Bus |  | 
A. 10
B. 15
C. 20
D. 60
E. 120
CLICKER
QUESTIONS:
#1 Car Throughput
10 min
30 min
Notes: 10, 15
30, 60

## Slide 9: iClicker Question #1: Car vs. Bus
Car: speed = 60 miles/hour, capacity = 5
Bus: speed = 20 miles/hour, capacity = 60
Task: transport passengers 10 miles
 | Latency (min) | Throughput (PPH)
Car |  | 
Bus |  | 
10 min
30 min
15 PPH
60 PPH

## Slide 10: How to make the computer faster?
Decrease latency
Critical Path
  Longest path determining the minimum time needed for an operation
  Determines minimum length of clock cycle i.e. determines maximum clock frequency
Optimize for latency on the critical path
    Parallelism (like carry look ahead adder)
    Pipelining
    Both
Notes: Is the the AND path or the 32 bit adder path that is going to determine your performance in your ALU from Lab1?
Critical path is what determines what is the slowest path through the logic. And therefore, it determines the minimum length of the cycle. That in turn determines the maximum clock frequency.
For example if the critical path is 1 nanosecond, the clock frequency is at most 1 GHz.

## Slide 11: Latency: Optimize Delay on Critical Path
E.g. Adder performance
32 Bit Adder Design | Space | Time
Ripple Carry | ≈ 300 gates | ≈ 64 gate delays
2-Way Carry-Skip | ≈ 360 gates | ≈ 35 gate delays
3-Way Carry-Skip | ≈ 500 gates | ≈ 22 gate delays
4-Way Carry-Skip | ≈ 600 gates | ≈ 18 gate delays
2-Way Look-Ahead | ≈ 550 gates | ≈ 16 gate delays
Split Look-Ahead | ≈ 800 gates | ≈ 10 gate delays
Full Look-Ahead | ≈ 1200 gates | ≈ 5 gate delays

## Slide 12: Review: Single-Cycle Datapath
Single-cycle datapath: true “atomic” F/EX loop
Fetch, decode, execute one instruction/cycle
Low CPI (later): 1 by definition
Long clock period: accommodate slowest insn
(PC  I$  RF  ALU  D$  RF)
PC
I$
Register
File
s1
s2
d
D$
+
4

## Slide 13: New: Multi-Cycle Datapath
Multi-cycle datapath: attacks slow clock
Fetch, decode, execute one insn over multiple cycles
Allows insns to take different number of cycles
Opposite of single-cycle: short clock period, high CPI
PC
I$
Register
File
s1
s2
d
D$
+
4
D
O
B
A

## Slide 14: Single- vs. Multi-cycle Performance
Single-cycle
  Clock period = 50ns, CPI = 1
  Performance = 50ns/insn
Multi-cycle: opposite performance split
  Shorter clock period
  Higher CPI
Example
  branch: 20% (3 cycles), ld: 20% (5 cycles), ALU: 60% (4 cycle)
  Clock period = 11ns, CPI = (20%*3)+(20%*5)+(60%*4) = 4
    Why is clock period 11ns and not 10ns?
  Performance = 44ns/insn
Aside: CISC makes perfect sense in multi-cycle datapath
Notes: Why 11ns and not 10ns? Extra “latch” overhead

## Slide 15: Multi-Cycle Instructions
But what to do when operations take diff. times?
E.g: Assume:
  load/store: 100 ns
  arithmetic: 50 ns
  branches: 33 ns
  Single-Cycle CPU
  10 MHz (100 ns cycle) with
    1 cycle per instruction
ms = 10-3 second
us = 10-6 seconds
ns = 10-9 seconds
ps = 10-12 seconds
10 MHz
20 MHz
30 MHz
Notes: 100ns = 10MHz; 50ns = 20MHz; 33ns = 30 MHz

## Slide 16: Multi-Cycle Instructions
  Multiple cycles to complete a single instruction
E.g: Assume:
  load/store: 100 ns
  arithmetic: 50 ns
  branches: 33 ns
  Multi-Cycle CPU
  30 MHz (33 ns cycle) with
    3 cycles per load/store
    2 cycles per arithmetic
    1 cycle per branch
ms = 10-3 second
us = 10-6 seconds
ns = 10-9 seconds
ps = 10-12 seconds
10 MHz
20 MHz
30 MHz
  Single-Cycle CPU
  10 MHz (100 ns cycle) with
    1 cycle per instruction
Which one is faster: Single- or Multi-Cycle CPU?
Notes: 100ns = 10MHz; 50ns = 20MHz; 33ns = 30 MHz

## Slide 17: Cycles Per Instruction (CPI)
Instruction mix for some program P, assume:
  25% load/store ( 3 cycles / instruction)
  60% arithmetic ( 2 cycles / instruction)
  15% branches ( 1 cycle / instruction)
Multi-Cycle performance for program P:
3 * .25 + 2 * .60 + 1 * .15 = 2.1
average cycles per instruction (CPI) = 2.1
Multi-Cycle @ 30 MHz
Single-Cycle @ 10 MHz
30M cycles/sec 2.1 cycles/instr ≈15 MIPS
vs
10 MIPS
MIPS = millions of instructions per second
= 10M cycles/sec  1 cycle/instr
Notes: 0.25 x 3 + 0.6 x 2 + 0.1 x 1 = 0.75 + 1.2 + .15 = 2.1

## Slide 18: Total Time
CPU Time = # Instructions x CPI x Clock Cycle Time
sec/prgrm = Instr/prgm x cycles/instr x seconds/cycle
Instructions per program: “dynamic instruction count”
  Runtime count of instructions executed by the program
  Determined by program, compiler, ISA
Cycles per instruction: “CPI” (typical range: 2 to 0.5)
  How many cycles does an instruction take to execute?
  Determined by program, compiler, ISA, micro-architecture
Seconds per cycle: clock period, length of each cycle
  Inverse metric: cycles/second (Hertz) or cycles/ns (Ghz)
  Determined by micro-architecture, technology parameters
For lower latency (=better performance) minimize all three
  Difficult: often pull against one another

## Slide 19: Total Time
CPU Time = # Instructions x CPI x Clock Cycle Time
E.g. Say for a program with 400k instructions, 30 MHz:
CPU [Execution] Time = ?
sec/prgrm = Instr/prgm x cycles/instr x seconds/cycle

## Slide 20: Total Time
CPU Time = # Instructions x CPI x Clock Cycle Time
E.g. Say for a program with 400k instructions, 30 MHz:
CPU [Execution] Time = 400k x 2.1 x 33 ns = 27 ms
sec/prgrm = Instr/prgm x cycles/instr x seconds/cycle

## Slide 21: Total Time
CPU Time = # Instructions x CPI x Clock Cycle Time
E.g. Say for a program with 400k instructions, 30 MHz:
CPU [Execution] Time = 400k x 2.1 x 33 ns = 27 ms
How do we increase performance?
Need to reduce CPU time
  Reduce #instructions
  Reduce CPI
  Reduce Clock Cycle Time
sec/prgrm = Instr/prgm x cycles/instr x seconds/cycle

## Slide 22: Example
Goal: Make Multi-Cycle @ 30 MHz CPU (15MIPS) run 2x faster by making arithmetic instructions faster
Instruction mix (for P):
  25% load/store, CPI = 3
  60% arithmetic, CPI = 2
  15% branches, CPI = 1
CPI = 0.25 x 3 + 0.6 x 2 + 0.15 x 1
= 2.1
Goal: Make processor run 2x faster,
i.e. 30 MIPS instead of 15 MIPS
Notes: So the goal is to make it run at 30 MIPs.
CPI = (.25 x 3 + .6 x 2 + .15 x 1)/1 = 2.1
MIPS = 30 MHz/2.1 = 14.28 MIPS. Call it 15 MIPS
Want to double MIPS from 15 MIPS (14.28 MIPS) to 30 MIPS (28.56 MIPS)

## Slide 23: Example
Goal: Make Multi-Cycle @ 30 MHz CPU (15MIPS) run 2x faster by making arithmetic instructions faster
Instruction mix (for P):
  25% load/store, CPI = 3
  60% arithmetic, CPI = 2 1
  15% branches, CPI = 1
First lets try CPI of 1 for arithmetic.
Is that 2x faster overall?
How much does it improve performance?
CPI = 0.25 x 3 + 0.6 x 1 + 0.15 x 1
= 1.5
No
Notes: So the goal is to make it run at approximately 30 MIPs.
Original CPI = (.25 x 3 + .6 x 2 + .15 x 1)/1 = 2.1
MIPS = 30 MHz/2.1 = 14.28 MIPS. Call it 15 MIPS
Say you drop the CPI for the arithmetic operation to 1. Will that double it? No.
.25 x 3 + .6 + .15 = 1.5
30 MHz/1.5 = 20MIPS

## Slide 24: Example
Goal: Make Multi-Cycle @ 30 MHz CPU (15MIPS) run 2x faster by making arithmetic instructions faster
Instruction mix (for P):
  25% load/store, CPI = 3
  60% arithmetic, CPI = 2 X
  15% branches, CPI = 1
But, want to half our CPI from 2.1 to 1.05.
Let new arithmetic operation have a CPI of X. X =?
Then, X = 0.25, which is a significant improvement
CPI = 1.05 = 0.25 x 3 + 0.6 x X + 0.15 x 1
1.05 = .75 + 0.6X + 0.15
X = 0.25
Notes: But we want to half our CPI. Let the new arithmetic operation have a CPI of x.
3 x .25 + x * 0.6 + .15 = 1.05
.75 + .15 + x * 0.6 = 1.05
x = 0.25
That’s a big improvement you need!

## Slide 25: Example
Goal: Make Multi-Cycle @ 30 MHz CPU (15MIPS) run 2x faster by making arithmetic instructions faster
Instruction mix (for P):
  25% load/store, CPI = 3
  60% arithmetic, CPI = 2 0.25
  15% branches, CPI = 1
To double performance CPI for arithmetic operations have to go from 2 to 0.25

## Slide 26: Amdahl’s Law
Amdahl’s Law
Execution time after improvement =
Or: Speedup is limited by popularity of improved feature
Corollary: Make the common case fast
Don’t optimize 1% to the detriment of other 99%
Don’t over-engineer capabilities that cannot be utilized
Caveat: Law of diminishing returns
execution time affected by improvement
amount of improvement
+ execution time unaffected
contribution to execution time
Notes: Consider our GPU example with 2k cores.
Say we have a program that takes 2000 seconds to run: 200 seconds is the start up time (reading data), and 1800 is the “main” algorithm.! This doesn’t seem so bad. 200/2000 = 10% only of startup and 90% of the program is in the slow algorithm.
We want to speed it up by running on a GPU with 2000 cores! Ideally we would get 2000x speedup and the program will run in 1 second.
But when we port it to the GPU, we can only improve the “main” algorithm which is highly parallelizable. You can improve the 1800 seconds down to < 1 second say, because you can fully parallelize the algorithm on 2000 cores.
But still the time for the whole program is 201 seconds. So you threw 2000 cores at the problem, but your speedup is 2000/201 which is approximately 10x. So with 2000 cores you only got 10x speedup. Amdahl’s law expresses that “unfortunate” relation.

## Slide 27: Performance Recap

## Slide 28: iClicker Question
What is the minimal, additional metric(s) that you need to decide which processor is faster?
(If 1 metric is enough, only list 1. Include more if needed.)
MIPS
CPI
Dynamic Instruction Count
Clock Rate
Nothing. Enough information has been given
Processor A and Processor B execute the program in the same number of cycles
Notes: Additional Metric: D

## Slide 29: iClicker Question
What is the minimal, additional metric(s) that you need to decide which processor is faster?
(If 1 metric is enough, only list 1. Include more if needed.)
MIPS
CPI
Dynamic Instruction Count
Clock Rate
Nothing. Enough information has been given
Processor A and Processor B execute the program in the same number of cycles
Notes: Additional Metric: D

## Slide 30: iClicker Question
What is the minimal, additional metric(s) that you need to decide which processor is faster?
(If 1 metric is enough, only list 1. Include more if needed.)
MIPS
CPI
Dynamic Instruction Count
Clock Rate
Nothing. Enough information has been given
Processor A and Processor B have the same clock rate, but support different ISAs
Notes: Additional Metric: B,C

## Slide 31: iClicker Question
What is the minimal, additional metric(s) that you need to decide which processor is faster?
(If 1 metric is enough, only list 1. Include more if needed.)
MIPS
CPI
Dynamic Instruction Count
Clock Rate
Nothing. Enough information has been given
Processor A and Processor B have the same clock rate, but support different ISAs
Notes: Additional Metric: B,C

## Slide 32: iClicker Question
What is the minimal, additional metric(s) that you need to decide which processor is faster?
(If 1 metric is enough, only list 1. Include more if needed.)
MIPS
CPI
Dynamic Instruction Count
Clock Rate
Nothing. Enough information has been given
Processor A and Processor B support the same ISA
Notes: Additional Metric: A

## Slide 33: iClicker Question
What is the minimal, additional metric(s) that you need to decide which processor is faster?
(If 1 metric is enough, only list 1. Include more if needed.)
MIPS
CPI
Dynamic Instruction Count
Clock Rate
Nothing. Enough information has been given
Processor A and Processor B support the same ISA
Notes: Additional Metric: A