## Slide 1: Assemblers, Linkers, and Loaders
CS 3410
Computer System Organization & Programming
These slides are the product of many rounds of teaching CS 3410 by Professors Weatherspoon, Bala, Bracy, and Sirer.

## Slide 2: Big Picture: Where are we going?
int x = 10;
x = x + 15;
C
compiler
addi r5, r0, 10
addi r5, r5, 15
MIPS
assembly
00100000000001010000000000001010
00100000101001010000000000001111
machine
code
assembler
CPU
Circuits
Gates
Transistors
Silicon
loader
addi r0 r5 10
r0 = 0
r5 = r0 + 10
r5 = r15 + 15
A
B
32
32
RF
Notes: 32 bits, 4 bytes
Add a line to represent the instruction set architecture
Another line for assembly
Another line, high level language

## Slide 3: Big Picture: Where are we going?
addi r5, r0, 10
muli r5, r5, 2
addi r5, r5, 15
int x = 10;
x = 2 * x + 15;
C
compiler
MIPS
assembly
machine
code
assembler
CPU
Circuits
Gates
Transistors
Silicon
loader
00100000000001010000000000001010
00000000000001010010100001000000
00100000101001010000000000001111
High Level Languages
Instruction Set
Architecture (ISA)
Notes: 32 bits, 4 bytes
Add a line to represent the instruction set architecture
Another line for assembly
Another line, high level language

## Slide 4: From Writing to Running
sum.c
sum.s
Compiler
C source
files
assembly
files
sum.o
Assembler
obj files
sum
Linker
executable
program
Executing
in
Memory
loader
process
exists on
disk
When most people say “compile” they mean
the entire process:
compile + assemble + link
“It’s alive!”
gcc -S
gcc -c
gcc -o
Notes: C compiler produces assembly files (contain MIPS assembly, pseudo-instructions, directives, etc.)
MIPS assembler produces object files (contain MIPS machine code, missing symbols, some layout information, etc.)
MIPS linker produces executable file (contains MIPS machine code, no missing symbols, some layout information)
OS loader gets it into memory and jumps to first instruction (machine code)

## Slide 5: Example: sum.c
Compiler output is assembly files
Assembler output is obj files
Linker joins object files into one executable
Loader brings it into memory and starts execution

## Slide 6: Example: sum.c
#include <stdio.h>
int n = 100;
int main (int argc, char* argv[ ]) {
int i;
int m = n;
int sum = 0;
for (i = 1; i <= m; i++) {
sum += i;
}
printf ("Sum 1 to %d is %d\n", n, sum);
}

## Slide 7: Compiler
Input: Code File (.c)
Source code
#includes, function declarations & definitions, global variables, etc.
Output: Assembly File (MIPS)
  MIPS assembly instructions
(.s file)
for (i = 1; i <= m; i++) {
sum += i;
}
li $2,1
lw $3,28($fp)
slt $2,$3,$2

## Slide 8: sum.s (abridged)
.globl n
.data
.type n, @object
n: .word 100
.rdata
$str0: .ascii "Sum 1 to %d is %d\n"
.text
.globl main
.type main, @function
main: addiu $sp,$sp,-48
sw $31,44($sp)
sw $fp,40($sp)
move $fp,$sp
sw $4,48($fp)
sw $5,52($fp)
la $2,n
lw $2,0($2)
sw $2,28($fp)
sw $0,32($fp)
li $2,1
sw $2,24($fp)
$L2: lw $2,24($fp)
lw $3,28($fp)
slt $2,$3,$2
bne $2,$0,$L3
lw $3,32($fp)
lw $2,24($fp)
addu $2,$3,$2
sw $2,32($fp)
lw $2,24($fp)
addiu $2,$2,1
sw $2,24($fp)
b $L2
$L3: la $4,$str0
lw $5,28($fp)
lw $6,32($fp)
jal printf
move $sp,$fp
lw $31,44($sp)
lw $fp,40($sp)
addiu $sp,$sp,48
j $31
Notes: note:
funny label names
alignment directives
.data versus .rdata
frame pointer equals stack pointer
totally unoptimized
use of LA

## Slide 9: Assembler
Input: Assembly File (.s)
assembly instructions, pseudo-instructions
program data (strings, variables), layout directives
Output: Object File in binary machine code MIPS instructions in executable form
(.o file in Unix, .obj in Windows)
00100000000001010000000000001010
00000000000001010010100001000000
00100000101001010000000000001111
addi r5, r0, 10
muli r5, r5, 2
addi r5, r5, 15

## Slide 10: MIPS Assembly Instructions
Arithmetic/Logical
  ADD, ADDU, SUB, SUBU, AND, OR, XOR, NOR, SLT, SLTU
  ADDI, ADDIU, ANDI, ORI, XORI, LUI, SLL, SRL, SLLV, SRLV, SRAV, SLTI, SLTIU
  MULT, DIV, MFLO, MTLO, MFHI, MTHI
Memory Access
  LW, LH, LB, LHU, LBU, LWL, LWR
  SW, SH, SB, SWL, SWR
Control flow
  BEQ, BNE, BLEZ, BLTZ, BGEZ, BGTZ
  J, JR, JAL, JALR, BEQL, BNEL, BLEZL, BGTZL
Special
  LL, SC, SYSCALL, BREAK, SYNC, COPROC

## Slide 11: Pseudo-Instructions
Assembly shorthand, technically not machine instructions, but easily converted into 1+ instructions that are
Pseudo-Insns Actual Insns Functionality
NOP SLL r0, r0, 0 # do nothing
MOVE reg, reg ADD r2, r0, r1 # copy between regs
LI reg, 0x45678 LUI reg, 0x4 #load immediate
ORI reg, reg, 0x5678
LA reg, label # load address (32 bits)
B # unconditional branch
BLT reg, reg, label SLT r1, rA, rB # branch less than
BNE r1, r0, label
+ a few more…
Notes: BLT rA, rB, label
becomes
SLT r1, rA, rB
BNE r1, r0, label
--------------------
Pseudo-Instructions
NOP # do nothing
SLL r0, r0, 0
MOVE reg, reg # copy between regs
ADD r2, r0, r1 # copies contents of r1 to r2
LI reg, imm # load immediate (up to 32 bits)
LA reg, label # load address (32 bits)
B label # unconditional branch
BLT reg, reg, label # branch less than
SLT r1, rA, rB # r1 = 1 if R[rA] < R[rB]; o.w. r1 = 0
BNE r1, r0, label # go to address label if r1!=r0; i.t. rA < rB

## Slide 12: Program Layout
Programs consist of segments used for different purposes
  Text: holds instructions
  Data: holds statically allocated program data such as variables, strings, etc.
add r1,r2,r3
ori r2, r4, 3
...
“cornell cs”
13
25
data
text

## Slide 13: Assembling Programs
Assembly files consist of a mix of
+ instructions
+ pseudo-instructions
+ assembler (data/layout) directives
(Assembler lays out binary values
in memory based on directives)
Assembled to an Object File
  Header
  Text Segment
  Data Segment
  Relocation Information
  Symbol Table
  Debugging Information
.text
.ent main
main: la $4, Larray
li $5, 15
...
li $4, 0
jal exit
.end main
.data
Larray:
.long 51, 491, 3991
Notes: A program is made up by code and data from several object files
Each object file is generated independently
Assembler starts at some PC address, e.g. 0, in each object file, generates code as if the program were laid out starting out at location 0x0
It also generates a symbol table, and a relocation table
In case the segments need to be moved

## Slide 14: Assembling Programs
Assembly using a (modified) Harvard architecture
  Need segments since data and program stored together in memory
CPU
Registers
Data Memory
data, address,
control
ALU
Control
00100000001
00100000010
00010000100
...
Program Memory
10100010000
10110000011
00100010101
...
Notes: The Harvard architecture is a computer architecture with physically separate storage and signal pathways for instructions and data. --- http://en.wikipedia.org/wiki/Harvard_architecture
Under pure von Neumann architecture the CPU can be either reading an instruction or reading/writing data from/to the memory. Both cannot occur at the same time since the instructions and data use the same bus system. In a computer using the Harvard architecture, the CPU can both read an instruction and perform a data memory access at the same time, even without a cache. A Harvard architecture computer can thus be faster for a given circuit complexity because instruction fetches and data access do not contend for a single memory pathway .
Also, a Harvard architecture machine has distinct code and data address spaces: instruction address zero is not the same as data address zero. Instruction address zero might identify a twenty-four bit value, while data address zero might indicate an eight bit byte that isn't part of that twenty-four bit value.
A modified Harvard architecture machine is very much like a Harvard architecture machine, but it relaxes the strict separation between instruction and data while still letting the CPU concurrently access two (or more) memory buses. The most common modification includes separate instruction and data caches backed by a common address space. While the CPU executes from cache, it acts as a pure Harvard machine. When accessing backing memory, it acts like a von Neumann machine (where code can be moved around like data, a powerful technique). This modification is widespread in modern processors such as the ARM architecture and X86 processors. It is sometimes loosely called a Harvard architecture, overlooking the fact that it is actually "modified".

## Slide 15: Takeaway
Assembly is a low-level task
  Need to assemble assembly language into machine code binary. Requires
    Assembly language instructions
    pseudo-instructions
    And Specify layout and data using assembler directives
  Today, we use a modified Harvard Architecture (Von Neumann architecture) that mixes data and instructions in memory
  … but kept in separate segments
  … and has separate caches

## Slide 16: Symbols and References
Global labels: Externally visible “exported” symbols
Can be referenced from other object files
Exported functions, global variables
Examples: pi, e, userid, printf, pick_prime, pick_random
Local labels: Internally visible only symbols
Only used within this object file
static functions, static variables, loop labels, …
Examples: randomval, is_prime
int pi = 3;
int e = 2;
static int randomval = 7;
extern int usrid;
extern int printf(char *str, …);
int square(int x) { … }
static int is_prime(int x) { … }
int pick_prime() { … }
int get_n() {
return usrid;
}
math.c
(extern == defined in another file)

## Slide 17: Handling forward references
Example:
    bne $1, $2, L sll $0, $0, 0
    L: addiu $2, $3, 0x2
The assembler will change this to
    bne $1, $2, +1 sll $0, $0, 0 addiu $2, $3, $0x2
Final machine code
  0X14220001 # bne 0x00000000 # sll 0x24620002 # addiu
actually: 000101...
000000...
001001...
Looking for L
Found L
Notes: 0X14220001 = 000101 00001 00010 0000 0000 0000 0001 # bne $1, $2, 0x1 0x00000000 = 000000 00000 00000 00000 00000 000000 # sll $0, $0, $0 0x24620002 = 001001 00011 00010 0000 0000 0000 0010 # addiu $2, $3, 0x2

## Slide 18: Object file
Header
  Size and position of pieces of file
Text Segment
  instructions
Data Segment
  static data (local/global vars, strings, constants)
Debugging Information
  line number  code address map, etc.
Symbol Table
  External (exported) references
  Unresolved (imported) references
Object File

## Slide 19: Object File Formats
Unix
  a.out
  COFF: Common Object File Format
  ELF: Executable and Linking Format
Windows
  PE: Portable Executable
All support both executable and object files

## Slide 20: Objdump disassembly
> mipsel-linux-objdump --disassemble math.o
Disassembly of section .text:
00000000 <get_n>:
0: 27bdfff8 addiu sp,sp,-8
4: afbe0000 sw s8,0(sp)
8: 03a0f021 move s8,sp
c: 3c020000 lui v0,0x0
10: 8c420008 lw v0,8(v0)
14: 03c0e821 move sp,s8
18: 8fbe0000 lw s8,0(sp)
1c: 27bd0008 addiu sp,sp,8
20: 03e00008 jr ra
24: 00000000 nop
elsewhere in another file: int usrid = 41;
int get_n() {
return usrid;
}
Notes: something suspicious: a lot of zero constants in this code

## Slide 21: Objdump symbols
> mipsel-linux-objdump --syms math.o
SYMBOL TABLE:
00000000 l df *ABS* 00000000 math.c
00000000 l d .text 00000000 .text
00000000 l d .data 00000000 .data
00000000 l d .bss 00000000 .bss
00000008 l O .data 00000004 randomval
00000060 l F .text 00000028 is_prime
00000000 l d .rodata 00000000 .rodata
00000000 l d .comment 00000000 .comment
00000000 g O .data 00000004 pi
00000004 g O .data 00000004 e
00000000 g F .text 00000028 get_n
00000028 g F .text 00000038 square
00000088 g F .text 0000004c pick_prime
00000000 *UND* 00000000 usrid
00000000 *UND* 00000000 printf
[l]ocal
[g]lobal
size
segment
[F]unction
[O]bject
Notes: notice: pick_random, square, other functions; pi, e, randomval; some undefined symbols

## Slide 22: Separate Compilation & Assembly
sum.c
sum.s
Compiler
source files
assembly files
sum.o
Assembler
obj files
sum
Linker
executable
program
Executing
in
Memory
loader
process
exists on
disk
math.c
math.s
math.o
Notes: C compiler produces assembly files (contain MIPS assembly, pseudo-instructions, directives, etc.)
MIPS assembler produces object files (contain MIPS machine code, missing symbols, some layout information, etc.)
MIPS linker produces executable file (contains MIPS machine code, no missing symbols, some layout information)
OS loader gets it into memory and jumps to first instruction (machine code)

## Slide 23: Linkers
Linker combines object files into an executable file
  Resolve as-yet-unresolved symbols
  Each has illusion of own address space
   Relocate each object’s text and data segments
  Record top-level entry point in executable file
End result: a program on disk, ready to execute
  E.g. ./sum Linux
  ./sum.exe Windows
  simulate sum Class MIPS simulator

## Slide 24: Static Libraries
Static Library: Collection of object files (think: like a zip archive)
Q: Every program contains the entire library?!?

## Slide 25: Linker Example: Resolving an External Fn Call
...
21032040
0C40023C
1b301402
3C041000
34040004
...
0C40023C
21035000
1b80050c
8C048004
21047002
0C400020
...
10201000
21040330
22500102
...
sum.exe
0040 0000
0040 0100
0040 0200
1000 0000
.text
.data
main.o
...
0C000000
21035000
1b80050C
8C040000
21047002
0C000000
...
00 T main
00 D usrid
*UND* printf
*UND* pi
*UND* get_n
printf.o
...
3C T printf
.text
Symbol table
Entry:0040 0100
text: 0040 0000
data: 1000 0000
math
main
printf
40,JAL, printf
...
54,JAL, get_n
40
44
48
4C
50
54
Relocation info
math.o
...
21032040
0C000000
1b301402
3C040000
34040000
...
20 T get_n
00 D pi
*UND* printf
*UND* usrid
28,JAL, printf
24
28
2C
30
34
global variables
go here (later)
Notes: main.o
0C000000 = 0000 1100 (JAL)
21035000 = 001000 01000 00011 0101 0000 0000 0000 (ADDI $3,$8, 0x5000)
1B80050C = 000110 11100 00000 0000 0101 0000 1100 (BLEZ $28, 0x050C)
3C040000 = 001111 00000 00100 0000 0000 0000 0000 (LUI, $4, 0)
21047002 = 001000 01000 00100 0111 0000 0000 0010 (ADDI $4, $8, 0x7002)
math.o
21032040 = 001000 01000 00011 0010 0000 0100 0000 (ADDI $3,$8, 0x2040)
0C000000 = 0000 1100 (JAL)
1B301402 = 000110 11001 10000 0001 0100 0000 0010 (BLEZ $23, 0x1402)
3C040000 = 001111 000000 0100 0000 0000 0000 0000 (LUI, $4, 0)
34040000 = 001101 000000 0100 0000 0000 0000 0000 (ORI, $4, 0)
1111 f
1110 e
1101 d
1100 c
1011 b
1010 a

## Slide 26
sum.c
math.c
io.s
sum.s
math.s
Compiler
C source
files
assembly
files
libc.o
libm.o
io.o
sum.o
math.o
Assembler
obj files
sum.exe
Linker
executable
program
Executing
in
Memory
loader
process
exists on
disk
Notes: C compiler produces assembly files (contain MIPS assembly, pseudo-instructions, directives, etc.)
MIPS assembler produces object files (contain MIPS machine code, missing symbols, some layout information, etc.)
MIPS linker produces executable file (contains MIPS machine code, no missing symbols, some layout information)
OS loader gets it into memory and jumps to first instruction (machine code)

## Slide 27: Loaders
Loader reads executable from disk into memory
  Initializes registers, stack, arguments to first function
  Jumps to entry-point
Part of the Operating System (OS)

## Slide 28: Shared Libraries
Q: Every program contains parts of same library?!?
Notes: fixed address: drawbacks? advantages?
(makes linking trivial: few relocations needed)

## Slide 29: Static and Dynamic Linking
Static linking
  Big executable files (all/most of needed libraries inside)
  Don’t benefit from updates to library
  No load-time linking
Dynamic linking
  Small executable files (just point to shared library)
  Library update benefits all programs that use it
  Load-time cost to do final linking
    But dll code is probably already in memory
    And can do the linking incrementally, on-demand
Notes: cost of loading big executables
dll hell, versioning problems

## Slide 30: Takeaway
Compiler produces assembly files
  (contain MIPS assembly, pseudo-instructions,
  directives, etc.)
Assembler produces object files
  (contain MIPS machine code, missing symbols,
  some layout information, etc.)
Linker joins object files into one executable file
  (contains MIPS machine code, no missing symbols,
  some layout information)
Loader puts program into memory, jumps to
1st insn, and starts executing a process
(machine code)