## Slide 1: Caches & Memory
CS 3410
Computer System Organization & Programming
These slides are the product of many rounds of teaching CS 3410 by Professors Weatherspoon, Bala, Bracy, and Sirer.

## Slide 2: Programs 101
Load/Store Architectures:
Read data from memory (put in registers)
Manipulate it
Store it back to memory
int main (int argc, char* argv[ ]) {
int i;
int m = n;
int sum = 0;
for (i = 1; i <= m; i++) {
sum += i;
}
printf (“...”, n, sum);
}
C Code
main: addiu $sp,$sp,-48
sw $31,44($sp)
sw $fp,40($sp)
move $fp,$sp
sw $4,48($fp)
sw $5,52($fp)
la $2,n
lw $2,0($2)
sw $2,28($fp)
sw $0,32($fp)
li $2,1
sw $2,24($fp)
$L2: lw $2,24($fp)
lw $3,28($fp)
slt $2,$3,$2
bne $2,$0,$L3
. . .
MIPS Assembly
Instructions that read from
or write to memory…

## Slide 3: 1 Cycle Per Stage: the Biggest Lie (So Far)
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
ALU
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard
Stack, Data, Code
Stored in Memory
Code Stored in Memory
(also, data and stack)

## Slide 4: What’s the problem?
+ big
– slow
– far away
SandyBridge Motherboard, 2011
http://news.softpedia.com
CPU
Main Memory

## Slide 5: The Need for Speed
CPU Pipeline
Notes: I made these two slides to see if you can make everything Ampelmännchen instead of first rainbow then ampelmännchen.
Not sure if this captures what you want to say. Just wanted to throw it out there.
(Slides 7/8 would be an alternative for slides 4/5/6)

## Slide 6: The Need for Speed
Instruction speeds:
add,sub,shift: 1 cycle
mult: 3 cycles
load/store: 100 cycles
  off-chip 50(-70)ns
  2(-3) GHz processor  0.5 ns clock
CPU Pipeline
Notes: This is great, but I would re-arrange it. First say that load/store requires 100 cycles (parallel to mult, add). This is your punch-line and probably surprising to the students.
Then explain why it is the case.

## Slide 7: The Need for Speed
CPU Pipeline

## Slide 8: What’s the solution?
Level 2 $
Level 1
Data $
Level 1
Insn $
Intel Pentium 3, 1999
Caches !

## Slide 9: Aside
Go back to 04-state and 05-memory and look at how registers, SRAM and DRAM are built.

## Slide 10: What’s the solution?
What lucky data gets to go here?
Level 2 $
Level 1
Data $
Level 1
Insn $
Intel Pentium 3, 1999
Caches !

## Slide 11: Locality Locality Locality
If you ask for something, you’re likely to ask for:
the same thing again soon
 Temporal Locality
something near that thing, soon
 Spatial Locality
total = 0;
for (i = 0; i < n; i++)
total += a[i];
return total;

## Slide 12: Clicker Questions
This highlights the temporal and spatial locality of data.
Q1: Which line of code exhibits good temporal locality?
1 total = 0;
2 for (i = 0; i < n; i++) {
3 n--;
4 total += a[i];
5 return total;
1
2
3
4
5

## Slide 13: Clicker Questions
This highlights the temporal and spatial locality of data.
Q1: Which line of code exhibits good temporal locality?
1 total = 0;
2 for (i = 0; i < n; i++) {
3 n--;
4 total += a[i];
5 return total;
1
2
3
4
5

## Slide 14: Clicker Questions
This highlights the temporal and spatial locality of data.
Q1: Which line of code exhibits good temporal locality?
1 total = 0;
2 for (i = 0; i < n; i++) {
3 n--;
4 total += a[i];
5 return total;
Q2: Which line of code exhibits good spatial locality with the line after it?
1
2
3
4
5

## Slide 15: Clicker Questions
This highlights the temporal and spatial locality of data.
Q1: Which line of code exhibits good temporal locality?
1 total = 0;
2 for (i = 0; i < n; i++) {
3 n--;
4 total += a[i];
5 return total;
Q2: Which line of code exhibits good spatial locality with the line after it?
1
2
3
4
5

## Slide 16: Your life is full of Locality
Last Called
Speed Dial
Favorites
Contacts
Google/Facebook/email

## Slide 17: Your life is full of Locality

## Slide 18: The Memory Hierarchy
Registers
L1 Caches
L2 Cache
L3 Cache
Main Memory
Disk
1 cycle,
128 bytes
4 cycles,
64 KB
Intel Haswell Processor, 2013
12 cycles,
256 KB
36 cycles,
2-20 MB
50-70 ns,
512 MB – 4 GB
5-20 ms
16GB – 4 TB,
Small, Fast
Big, Slow

## Slide 19: Some Terminology
Cache hit
data is in the Cache
thit : time it takes to access the cache
Hit rate (%hit): # cache hits / # cache accesses
Cache miss
data is not in the Cache
tmiss : time it takes to get the data from below the $
Miss rate (%miss): # cache misses / # cache accesses
Cacheline or cacheblock or simply line or block
Minimum unit of info that is present/or not in the cache

## Slide 20: The Memory Hierarchy
Registers
L1 Caches
1 cycle,
128 bytes
4 cycles,
64 KB
Intel Haswell Processor, 2013
50-70 ns,
512 MB – 4 GB
5-20 ms
16GB – 4 TB,
  average access time
  tavg = thit + %miss* tmiss
  = 4 + 5% x 100
  = 9 cycles
12 cycles,
256 KB
36 cycles,
2-20 MB
L2 Cache
L3 Cache
Main Memory
Disk
Notes: There are two expressions for AMAT bolded below.
AMAT = %hit * hit time + %miss * miss time
where miss time = (hit time + miss penalty)
AMAT = %hit * hit time + %miss * (hit time + miss penalty)
AMAT = %hit * hit time + %miss * hit time + %miss * miss penalty
AMAT = hit time * (%hit + %miss) + % miss * miss penalty
AMAT = hit time + % miss * miss penalty

## Slide 21: Single Core Memory Hierarchy
Registers
L1 Caches
L2 Cache
L3 Cache
Main Memory
Disk
ON CHIP
Disk
Processor
Regs
I$
D$
L2
Main Memory

## Slide 22: Multi-Core Memory Hierarchy
ON CHIP
Main Memory
Processor
Regs
I$
D$
L2
L3
Processor
Regs
I$
D$
L2
Processor
Regs
I$
D$
L2
Processor
Regs
I$
D$
L2
Disk
Notes: This is my suggestion

## Slide 23: Memory Hierarchy by the Numbers
CPU clock rates ~0.33ns – 2ns (3GHz-500MHz)
*Registers,D-Flip Flops: 10-100’s of registers
Memory technology | Transistor count* | Access time | Access time in cycles | $ per GIB in 2012 | Capacity
SRAM (on chip) | 6-8 transistors | 0.5-2.5 ns | 1-3 cycles | $4k | 256 KB
SRAM (off chip) |  | 1.5-30 ns | 5-15 cycles | $4k | 32 MB
DRAM | 1 transistor (needs refresh) | 50-70 ns | 150-200 cycles | $10-$20 | 8 GB
SSD (Flash) |  | 5k-50k ns | Tens of thousands | $0.75-$1 | 512 GB
Disk |  | 5M-20M ns | Millions | $0.05-$0.1 | 4 TB
Notes: Capacity and latency are closely coupled
Cost is inversely proportional

## Slide 24: Basic Cache Design
Direct Mapped Caches

## Slide 25: 16 Byte Memory
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
MEMORY
Byte-addressable memory
4 address bits  16 bytes total
b addr bits  2b bytes in memory
load 1100  r1

## Slide 26: 4-Byte, Direct Mapped Cache
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
MEMORY
CACHE
data
A
B
C
D
Direct mapped:
Each address maps to 1 cache block
4 entries  2 index bits (2n  n bits)
Index with LSB:
Supports spatial locality
index
XXXX
index
00
01
10
11
Cache entry
= row
= (cache) line
= (cache) block
Block Size: 1 byte

## Slide 27: Analogy to a Spice Rack
Compared to your spice wall
  Smaller
  Faster
  More costly (per oz.)
A
B
C
D
E
F
…
Z
http://www.bedbathandbeyond.com
Spice Wall
(Memory)
Spice Rack
(Cache)
index spice

## Slide 28: Analogy to a Spice Rack
Cinnamon
How do you know what’s in the jar?
Need labels
  Tag = Ultra-minimalist label
innamon
Spice Wall
(Memory)
A
B
C
D
E
F
…
Z
Spice Rack
(Cache)
index spice
tag

## Slide 29: 4-Byte, Direct Mapped Cache
tag|index
XXXX
 | data
 | A
 | B
 | C
 | D
tag
00
00
00
00
MEMORY
CACHE
Tag: minimalist label/address
address = tag + index
index
00
01
10
11
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q

## Slide 30: 4-Byte, Direct Mapped Cache
MEMORY
CACHE
One last tweak: valid bit
V | tag | data
0 | 00 | X
0 | 00 | X
0 | 00 | X
0 | 00 | X
index
00
01
10
11
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q

## Slide 31: Simulation #1 of a 4-byte, DM Cache
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
Lookup:
Index into $
Check tag
Check valid bit
MEMORY
CACHE
V | tag | data
0 | 11 | X
0 | 11 | X
0 | 11 | X
0 | 11 | X
load 1100
Miss
tag|index
XXXX
index
00
01
10
11

## Slide 32: Simulation #1 of a 4-byte, DM Cache
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
MEMORY
CACHE
V | tag | data
1 | 11 | N
0 | xx | X
0 | xx | X
0 | xx | X
load 1100
Miss
Lookup:
Index into $
Check tag
Check valid bit
tag|index
XXXX
index
00
01
10
11

## Slide 33: Simulation #1 of a 4-byte, DM Cache
MEMORY
CACHE
V | tag | data
1 | 11 | N
0 | 11 | X
0 | 11 | X
0 | 11 | X
load 1100
...
load 1100
Miss
Hit!
Awesome!
tag|index
XXXX
Lookup:
Index into $
Check tag
Check valid bit
index
00
01
10
11
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q

## Slide 34: Clicker Questions
Processor A is a 1 GHz processor (1 cycle = 1 ns). There is an L1 cache with a 1 cycle access time and a 50% hit rate. There is an L2 cache with a 10 cycle access time and a 90% hit rate. It takes 100 ns to access memory.
Q1: What is the average memory access time of Processor A in ns? A: 5 B: 7 C: 9 D: 11 E: 13
Proc. B attempts to improve upon Proc. A by making the L1 cache larger. The new hit rate is 90%. To maintain a 1 cycle access time, Proc. B runs at 500 MHz (1 cycle = 2 ns).
Q2: What is the average memory access time of Processor B in ns? A: 5 B: 7 C: 9 D: 11 E: 13
Q3: Which processor should you buy?
A: Processor A B: Processor B C: They are equally good.
Notes: Q1:
  1 + 50% (10 + 10% x 100) =
  1 + 5 + 5 = 11 ns
Q2:
  2 + 10% (20 + 10% x 100) =
  2 + 2 + 1 = 5 ns
Processor A. Although memory access times are over 2x faster on Processor B, the frequency of Processor B is 2x slower. Since most workloads are not more than 50% memory instructions, Processor A is still likely to be the faster processor for most work- loads. (If I did have workloads that were over 50% memory instructions, Processor B might be the better choice.)

## Slide 35: Clicker Answers
Q1:
  1 + 50% (10 + 10% x 100) =
  1 + 5 + 5 = 11 ns
Q2:
  2 + 10% (20 + 10% x 100) =
  2 + 2 + 1 = 5 ns
Processor A. Although memory access times are over 2x faster on Processor B, the frequency of Processor B is 2x slower. Since most workloads are not more than 50% memory instructions, Processor A is still likely to be the faster processor for most work- loads. (If I did have workloads that were over 50% memory instructions, Processor B might be the better choice.)

## Slide 36: Block Diagram 4-entry, direct mapped Cache
CACHE
V | tag | data
1 | 00 | 1111 0000
1 | 11 | 1010 0101
0 | 01 | 1010 1010
1 | 11 | 0000 0000
tag|index
1101
2
2
2
=
Hit!
data
8
1010 0101
Great!
Are we done?

## Slide 37: Clicker: A) Hit B) Miss
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
MEMORY
CACHE
V | tag | data
0 | 11 | X
0 | 11 | X
0 | 11 | X
0 | 11 | X
load 1100
load 1101
load 0100
load 1100
Miss
Lookup:
Index into $
Check tag
Check valid bit
index
00
01
10
11
Simulation #2:
4-byte, DM Cache

## Slide 38: Simulation #2: 4-byte, DM Cache
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
MEMORY
CACHE
V | tag | data
1 | 11 | N
0 | 11 | X
0 | 11 | X
0 | 11 | X
load 1100
load 1101
load 0100
load 1100
Miss
Lookup:
Index into $
Check tag
Check valid bit
index
00
01
10
11

## Slide 39: Simulation #2: 4-byte, DM Cache
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
MEMORY
CACHE
V | tag | data
1 | 11 | N
0 | 11 | X
0 | 11 | X
0 | 11 | X
load 1100
load 1101
load 0100
load 1100
Miss
Miss
Lookup:
Index into $
Check tag
Check valid bit
index
00
01
10
11
Clicker: A) Hit B) Miss

## Slide 40: Simulation #2: 4-byte, DM Cache
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
MEMORY
CACHE
V | tag | data
1 | 11 | N
1 | 11 | O
0 | 11 | X
0 | 11 | X
load 1100
load 1101
load 0100
load 1100
Miss
Miss
tag|index
XXXX
Lookup:
Index into $
Check tag
Check valid bit
index
00
01
10
11

## Slide 41: Simulation #2: 4-byte, DM Cache
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
MEMORY
CACHE
V | tag | data
1 | 11 | N
1 | 11 | O
0 | xx | X
0 | xx | X
load 1100
load 1101
load 0100
load 1100
Miss
Miss
Miss
Lookup:
Index into $
Check tag
Check valid bit
index
00
01
10
11
Clicker: A) Hit B) Miss

## Slide 42: Simulation #2: 4-byte, DM Cache
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
MEMORY
CACHE
V | tag | data
1 | 01 | E
1 | 11 | O
0 | 11 | X
0 | 11 | X
load 1100
load 1101
load 0100
load 1100
Miss
Miss
Miss
Lookup:
Index into $
Check tag
Check valid bit
index
00
01
10
11

## Slide 43: Simulation #2: 4-byte, DM Cache
MEMORY
CACHE
V | tag | data
1 | 01 | E
1 | 11 | O
0 | 11 | X
0 | 11 | X
load 1100
load 1101
load 0100
load 1100
Miss
Miss
Miss
Miss
Lookup:
Index into $
Check tag
Check valid bit
index
00
01
10
11
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
Clicker: A) Hit B) Miss

## Slide 44: Simulation #2: 4-byte, DM Cache
MEMORY
CACHE
V | tag | data
1 | 11 | N
1 | 11 | O
0 | 11 | X
0 | 11 | X
load 1100
load 1101
load 0100
load 1100
Miss
Miss
Miss
Miss
Disappointed!

tag|index
XXXX
cold
cold
cold
index
00
01
10
11
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q

## Slide 45: Reducing Cold Misses by Increasing Block Size
Leveraging Spatial Locality

## Slide 46: Increasing Block Size
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
CACHE
V | tag | data
0 | x | A ¦ B
0 | x | C ¦ D
0 | x | E ¦ F
0 | x | G ¦ H
MEMORY
Block Size: 2 bytes
Block Offset: least significant bits indicate where you live in the block
Which bits are the index? tag?
offset
XXXX
index
00
01
10
11

## Slide 47: Simulation #3: 8-byte, DM Cache
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
MEMORY
CACHE
V | tag | data
0 | x | X ¦ X
0 | x | X ¦ X
0 | x | X ¦ X
0 | x | X ¦ X
load 1100
load 1101
load 0100
load 1100
Miss
tag| |offset
XXXX
index
Lookup:
Index into $
Check tag
Check valid bit
index
00
01
10
11

## Slide 48: Simulation #3: 8-byte, DM Cache
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
V | tag | data
0 | x | X ¦ X
0 | x | X ¦ X
1 | 1 | N ¦ O
0 | x | X ¦ X
MEMORY
CACHE
load 1100
load 1101
load 0100
load 1100
tag| |offset
XXXX
index
Miss
Lookup:
Index into $
Check tag
Check valid bit
index
00
01
10
11

## Slide 49: Simulation #3: 8-byte, DM Cache
V | tag | data
0 | x | X ¦ X
0 | x | X ¦ X
1 | 1 | N ¦ O
0 | x | X ¦ X
MEMORY
CACHE
load 1100
load 1101
load 0100
load 1100
Hit!
tag| |offset
XXXX
index
Miss
Lookup:
Index into $
Check tag
Check valid bit
index
00
01
10
11
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q

## Slide 50: Simulation #3: 8-byte, DM Cache
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
V | tag | data
0 | x | X ¦ X
0 | x | X ¦ X
1 | 1 | N ¦ O
0 | x | X ¦ X
MEMORY
CACHE
load 1100
load 1101
load 0100
load 1100
Hit!
Miss
Miss
tag| |offset
XXXX
index
Lookup:
Index into $
Check tag
Check valid bit
index
00
01
10
11

## Slide 51: Simulation #3: 8-byte, DM Cache
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
V | tag | data
0 | x | X ¦ X
0 | x | X ¦ X
1 | 0 | E ¦ F
0 | x | X ¦ X
MEMORY
CACHE
load 1100
load 1101
load 0100
load 1100
Hit!
Miss
Miss
tag| |offset
XXXX
index
Lookup:
Index into $
Check tag
Check valid bit
index
00
01
10
11

## Slide 52: Simulation #3: 8-byte, DM Cache
V | tag | data
0 | x | X ¦ X
0 | x | X ¦ X
1 | 0 | E ¦ F
0 | x | X ¦ X
MEMORY
CACHE
load 1100
load 1101
load 0100
load 1100
Hit!
Miss
Miss
Miss
tag| |offset
XXXX
index
Lookup:
Index into $
Check tag
Check valid bit
index
00
01
10
11
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q

## Slide 53: Simulation #3: 8-byte, DM Cache
V | tag | data
0 | x | X ¦ X
0 | x | X ¦ X
1 | 0 | E ¦ F
0 | x | X ¦ X
MEMORY
CACHE
load 1100
load 1101
load 0100
load 1100
Hit!
Miss
Miss
Miss
1 hit, 3 misses
3 bytes don’t fit in a 4 entry cache?
cold
cold
conflict
index
00
01
10
11
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q

## Slide 54: Removing Conflict Misses with Fully-Associative Caches

## Slide 55: 8 byte, fully-associative Cache
CACHE
MEMORY
What should the offset be?
What should the index be?
What should the tag be?
XXXX
tag|offset
XXXX
offset
XXXX
V | tag | data
0 | xxx | X ¦ X
V | tag | data
0 | xxx | X ¦ X
V | tag | data
0 | xxx | X ¦ X
V | tag | data
0 | xxx | X ¦ X
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
Clicker: A) xxxx
B) xxxx
C) xxxx
D) xxxx
E) None
Notes: Offset = A
Index = E
Tag = D

## Slide 56: Simulation #4: 8-byte, FA Cache
V | tag | data
0 | xxx | X ¦ X
V | tag | data
0 | xxx | X ¦ X
V | tag | data
0 | xxx | X ¦ X
V | tag | data
0 | xxx | X ¦ X
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
MEMORY
load 1100
load 1101
load 0100
load 1100
Miss
XXXX
tag|offset
Lookup:
Index into $
Check tags
Check valid bits
CACHE
LRU Pointer

## Slide 57: Simulation #4: 8-byte, FA Cache
V | tag | data
1 | 110 | N ¦ O
V | tag | data
0 | xxx | X ¦ X
V | tag | data
0 | xxx | X ¦ X
V | tag | data
0 | xxx | X ¦ X
MEMORY
load 1100
load 1101
load 0100
load 1100
Miss
XXXX
tag|offset
Lookup:
Index into $
Check tags
Check valid bits
CACHE
Hit!
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q

## Slide 58: Simulation #4: 8-byte, FA Cache
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
V | tag | data
1 | 110 | N ¦ O
V | tag | data
0 | xxx | X ¦ X
V | tag | data
0 | xxx | X ¦ X
V | tag | data
0 | xxx | X ¦ X
MEMORY
load 1100
load 1101
load 0100
load 1100
Miss
XXXX
tag|offset
Lookup:
Index into $
Check tags
Check valid bits
CACHE
Hit!
Miss
LRU Pointer

## Slide 59: Simulation #4: 8-byte, FA Cache
V | tag | data
1 | 110 | N ¦ O
V | tag | data
1 | 010 | E ¦ F
V | tag | data
0 | xxx | X ¦ X
V | tag | data
0 | xxx | X ¦ X
MEMORY
load 1100
load 1101
load 0100
load 1100
Miss
XXXX
tag|offset
Lookup:
Index into $
Check tags
Check valid bits
CACHE
Hit!
Miss
Hit!
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
LRU Pointer

## Slide 60: Pros and Cons of Full Associativity
+ No more conflicts!
+ Excellent utilization!
But either:
Parallel Reads
– lots of reading!
Serial Reads
– lots of waiting
  tavg = thit + %miss* tmiss
  = 4 + 5% x 100
  = 9 cycles
  = 6 + 3% x 100
  = 9 cycles

## Slide 61: Pros & Cons
 | Direct Mapped | Fully Associative
Tag Size | Smaller | Larger
SRAM Overhead | Less | More
Controller Logic | Less | More
Speed | Faster | Slower
Price | Less | More
Scalability | Very | Not Very
# of conflict misses | Lots | Zero
Hit Rate | Low | High
Pathological Cases | Common | ?

## Slide 62: Reducing Conflict Misses with Set-Associative Caches
Not too conflict-y. Not too slow.
… Just Right!

## Slide 63: 8 byte, 2-way set associative Cache
CACHE
MEMORY
What should the offset be?
What should the index be?
What should the tag be?
XXXX
tag||offset
index
XXXX
offset
V | tag | data
0 | xx | E ¦ F
0 | xx | C ¦ D
V | tag | data
0 | xx | N ¦ O
0 | xx | P ¦ Q
XXXX
index
0
1
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q

## Slide 64: Clicker Question
XXXXX
5 bit address
2 byte block size
24 byte, 3-Way Set Associative CACHE
0
1
2
3
4
V | tag | data
0 | ? | X ¦ Y
0 | ? | X ¦ Y
0 | ? | X ¦ Y
0 | ? | X ¦ Y
V | tag | data
0 | ? | X’ ¦ Y’
0 | ? | X’ ¦ Y’
0 | ? | X’ ¦ Y’
0 | ? | X’ ¦ Y’
index
00
01
10
11
V | tag | data
0 | ? | X’’ ¦ Y’’
0 | ? | X’’ ¦ Y’’
0 | ? | X’’ ¦ Y’’
0 | ? | X’’ ¦ Y’’
How many tag bits?

## Slide 65: Clicker Question
XXXXX
5 bit address
2 byte block size
24 byte, 3-Way Set Associative CACHE
0
1
2
3
4
V | tag | data
0 | ? | X ¦ Y
0 | ? | X ¦ Y
0 | ? | X ¦ Y
0 | ? | X ¦ Y
V | tag | data
0 | ? | X’ ¦ Y’
0 | ? | X’ ¦ Y’
0 | ? | X’ ¦ Y’
0 | ? | X’ ¦ Y’
index
00
01
10
11
V | tag | data
0 | ? | X’’ ¦ Y’’
0 | ? | X’’ ¦ Y’’
0 | ? | X’’ ¦ Y’’
0 | ? | X’’ ¦ Y’’
How many tag bits?

## Slide 66: 8 byte, 2-way set associative Cache
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
CACHE
index
0
1
MEMORY
XXXX
tag||offset
index
V | tag | data
0 | xx | X ¦ X
0 | xx | X ¦ X
V | tag | data
0 | xx | X ¦ X
0 | xx | X ¦ X
load 1100
load 1101
load 0100
load 1100
Miss
Lookup:
Index into $
Check tag
Check valid bit
LRU Pointer

## Slide 67: 8 byte, 2-way set associative Cache
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
CACHE
index
0
1
MEMORY
XXXX
tag||offset
index
V | tag | data
1 | 11 | N ¦ O
0 | xx | X ¦ X
V | tag | data
0 | xx | X ¦ X
0 | xx | X ¦ X
load 1100
load 1101
load 0100
load 1100
Miss
Lookup:
Index into $
Check tag
Check valid bit
Hit!
LRU Pointer

## Slide 68: 8 byte, 2-way set associative Cache
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
CACHE
index
0
1
MEMORY
XXXX
tag||offset
index
V | tag | data
1 | 11 | N ¦ O
0 | xx | X ¦ X
V | tag | data
0 | xx | X ¦ X
0 | xx | X ¦ X
load 1100
load 1101
load 0100
load 1100
Miss
Lookup:
Index into $
Check tag
Check valid bit
Hit!
Miss
LRU Pointer

## Slide 69: 8 byte, 2-way set associative Cache
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
CACHE
index
0
1
MEMORY
XXXX
tag||offset
index
V | tag | data
1 | 11 | N ¦ O
0 | xx | X ¦ X
V | tag | data
1 | 01 | E ¦ F
0 | xx | X ¦ X
load 1100
load 1101
load 0100
load 1100
Miss
Lookup:
Index into $
Check tag
Check valid bit
Hit!
Miss
Hit!
LRU Pointer

## Slide 70: Eviction Policies
Which cache line should be evicted from the cache to make room for a new line?
Direct-mapped: no choice, must evict line selected by index
Associative caches
  Random: select one of the lines at random
  Round-Robin: similar to random
  FIFO: replace oldest line
  LRU: replace line that has not been used in the longest time

## Slide 71: Misses: the Three C’s
Cold (compulsory) Miss:
never seen this address before
Conflict Miss:
cache associativity is too low
Capacity Miss:
cache is too small

## Slide 72: Miss Rate vs. Block Size

## Slide 73: Block Size Tradeoffs
For a given total cache size,
Larger block sizes mean….
  fewer lines
  so fewer tags, less overhead
  and fewer cold misses (within-block “prefetching”)
But also…
  fewer blocks available (for scattered accesses!)
  so more conflicts
  can decrease performance if working set can’t fit in $
  and larger miss penalty (time to fetch block)
Notes: Same for other parameters: experimental mostly

## Slide 74: Miss Rate vs. Associativity

## Slide 75: Clicker Question
Conflict misses decrease
Tag overhead decreases
Hit time increases
Cache stays the same size
What does NOT happen when you increase the associativity of the cache?

## Slide 76: Clicker Question
Conflict misses decrease
Tag overhead decreases
Hit time increases
Cache stays the same size
What does NOT happen when you increase the associativity of the cache?

## Slide 77: ABCs of Caches
+ Associativity:
⬇conflict misses 
⬆hit time 
+ Block Size:
⬇cold misses 
⬆conflict misses 
+ Capacity:
⬇capacity misses 
⬆hit time 
  tavg = thit + %miss* tmiss

## Slide 78: Which caches get what properties?
L1 Caches
L2 Cache
L3 Cache
Fast
Big
More Associative
Bigger Block Sizes
Larger Capacity
  tavg = thit + %miss* tmiss
Design with miss rate in mind
Design with speed in mind

## Slide 79: Roadmap
Things we have covered:
  The Need for Speed
  Locality to the Rescue!
  Calculating average memory access time
  $ Misses: Cold, Conflict, Capacity
  $ Characteristics: Associativity, Block Size, Capacity
Things we will now cover:
  Cache Figures
  Cache Performance Examples
  Writes

## Slide 80: 2-Way Set Associative Cache (Reading)
hit?
line select
64bytes
Tag Index Offset
data
word select
32bits
=
=
Tag
Tag
V
V
Data
Data

## Slide 81: 3-Way Set Associative Cache (Reading)
data
word select
hit?
line select
=
=
=
32bits
64bytes
Tag Index Offset

## Slide 82: How Big is the Cache?
n bit index, m bit offset, N-way Set Associative
Question: How big is cache?
Data only?
(what we usually mean when we ask “how big” is the cache)
Data + overhead?
Tag Index Offset

## Slide 83: How Big is the Cache?
n bit index, m bit offset, N-way Set Associative
Question: How big is cache?
How big is the cache (Data only)?
Cache of size 2n sets
Block size of 2m bytes, N-way set associative
Cache Size: 2m bytes-per-block x (2n sets x N-way-per-set)
= N x 2n+m bytes
Tag Index Offset

## Slide 84: How Big is the Cache?
n bit index, m bit offset, N-way Set Associative
Question: How big is cache?
How big is the cache (Data + overhead)?
Cache of size 2n sets
Block size of 2m bytes, N-way set associative
Tag field: 32 – (n + m), Valid bit: 1
SRAM Size: 2n sets x N-way-per-set x (block size + tag size + valid bit size)
= 2n x N-way x (2m bytes x 8 bits-per-byte + (32–n–m) + 1)
Tag Index Offset

## Slide 85: Performance Calculation with $ Hierarchy
Parameters
  Reference stream: all loads
  D$: thit = 1ns, %miss = 5%
  L2: thit = 10ns, %miss = 20% (local miss rate)
  Main memory: thit = 50ns
What is tavgD$ without an L2?
  tmissD$ =
  tavgD$ =
What is tavgD$ with an L2?
  tmissD$ =
  tavgL2 =
  tavgD$ =
  tavg = thit + %miss* tmiss

## Slide 86: Performance Calculation with $ Hierarchy
Parameters
  Reference stream: all loads
  D$: thit = 1ns, %miss = 5%
  L2: thit = 10ns, %miss = 20% (local miss rate)
  Main memory: thit = 50ns
What is tavgD$ without an L2?
  tmissD$ =
  tavgD$ =
What is tavgD$ with an L2?
  tmissD$ =
  tavgL2 =
  tavgD$ =
  thitM
  thitD$ + %missD$*thitM = 1ns+(0.05*50ns) = 3.5ns
  tavgL2
  thitL2+%missL2*thitM = 10ns+(0.2*50ns) = 20ns
  thitD$ + %missD$*tavgL2 = 1ns+(0.05*20ns) = 2ns
  tavg = thit + %miss* tmiss

## Slide 87: Performance Summary
Average memory access time (AMAT) depends on:
cache architecture and size
Hit and miss rates
Access times and miss penalty
Cache design a very complex problem:
Cache size, block size (aka line size)
Number of ways of set-associativity (1, N, )
Eviction policy
Number of levels of caching, parameters for each
Separate I-cache from D-cache, or Unified cache
Prefetching policies / instructions
Write policy

## Slide 88: Takeaway
Direct Mapped  fast, but low hit rate
Fully Associative  higher hit cost, higher hit rate
Set Associative  middleground
Line size matters. Larger cache lines can increase performance due to prefetching. BUT, can also decrease performance is working set size cannot fit in cache.
Cache performance is measured by the average memory access time (AMAT), which depends cache architecture and size, but also the access time for hit, miss penalty, hit rate.

## Slide 89: What about Stores?
We want to write to the cache.
If the data is not in the cache?
  Bring it in. (Write allocate policy)
Should we also update memory?
Yes: write-through policy
No: write-back policy

## Slide 90: Write-Through Cache
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
Cache
Register File
$0
$1
$2
$3
Memory
78
120
71
173
21
28
200
225
Misses: 0
Hits: 0
Reads: 0
Writes: 0
0
0
16 byte, byte-addressed memory
4 btye, fully-associative cache:
2-byte blocks, write-allocate
4 bit addresses:
3 bit tag, 1 bit offset
lru V tag data
1
0

## Slide 91: Write-Through (REF 1)
Cache
Register File
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
$0
$1
$2
$3
78
120
71
173
21
28
200
225
Misses: 0
Hits: 0
Reads: 0
Writes: 0
0
0
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
lru V tag data
1
0

## Slide 92: Write-Through (REF 1)
Cache
Register File
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
000
$0
$1
$2
$3
78
120
71
173
21
28
200
225
Misses: 1
Hits: 0
Reads: 2
Writes: 0
1
0
29
78
29
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
lru V tag data
M
0
1

## Slide 93: Write-Through (REF 2)
Cache
Register File
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
000
$0
$1
$2
$3
78
120
71
173
21
28
200
225
Misses: 1
Hits: 0
Reads: 2
Writes: 0
1
0
29
78
29
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
lru V tag data
M
0
1

## Slide 94: Write-Through (REF 2)
Cache
Register File
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
000
$0
$1
$2
$3
011
78
120
71
173
21
28
200
225
Misses: 2
Hits: 0
Reads: 4
Writes: 0
1
1
29
78
29
162
173
173
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
lru V tag data
M
M
0
1

## Slide 95: Write-Through (REF 3)
Cache
Register File
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
000
$0
$1
$2
$3
011
78
120
71
173
21
28
200
225
1
1
29
78
29
162
173
173
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
lru V tag data
M
M
1
0
Misses: 2
Hits: 0
Reads: 4
Writes: 0
CLICKER:
HIT
MISS

## Slide 96: Write-Through (REF 3)
Cache
Register File
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
000
$0
$1
$2
$3
011
120
71
173
21
28
200
225
1
1
29
29
162
173
173
173
173
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
lru V tag data
M
M
Hit
0
1
Misses: 2
Hits: 1
Reads: 4
Writes: 1

## Slide 97: Write-Through (REF 4)
011
Cache
Register File
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
000
$0
$1
$2
$3
173
120
71
173
21
28
200
225
1
1
29
173
29
173
162
173
150
71
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
lru V tag data
M
M
Hit
M
0
1
011
010
Misses: 2
Hits: 1
Reads: 4
Writes: 1
write-allocate

## Slide 98: Write-Through (REF 4)
Cache
Register File
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
000
$0
$1
$2
$3
010
173
120
71
173
21
28
200
225
1
1
29
173
29
173
150
71
150
29
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
lru V tag data
M
M
Hit
M
1
0
29
Misses: 3
Hits: 1
Reads: 6
Writes: 2

## Slide 99: Write-Through (REF 5)
Cache
Register File
29
123
29
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
$0
$1
$2
$3
010
173
120
71
173
21
28
200
225
1
1
29
173
29
173
29
71
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
lru V tag data
M
M
Hit
M
1
0
000
Misses: 3
Hits: 1
Reads: 6
Writes: 2
CLICKER:
HIT
MISS

## Slide 100: Write-Through (REF 5)
Cache
Register File
29
123
29
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
101
$0
$1
$2
$3
010
173
120
71
173
21
28
200
225
1
1
29
29
71
33
28
33
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
lru V tag data
M
M
Hit
M
M
0
1
Misses: 4
Hits: 1
Reads: 8
Writes: 2

## Slide 101: Write-Through (REF 6)
Cache
Register File
29
123
29
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
101
$0
$1
$2
$3
010
173
120
71
173
21
28
200
225
1
1
29
29
71
33
28
33
29
29
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
lru V tag data
M
M
Hit
M
M
0
1
Misses: 4
Hits: 1
Reads: 8
Writes: 2

## Slide 102: Write-Through (REF 6)
Cache
Register File
29
123
29
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
101
$0
$1
$2
$3
010
173
120
71
173
21
28
200
225
1
1
29
29
71
33
28
33
29
29
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
lru V tag data
M
M
Hit
M
M
Hit
0
1
Misses: 4
Hits: 2
Reads: 8
Writes: 3

## Slide 103: Write-Through (REF 7)
Cache
Register File
29
123
29
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
101
$0
$1
$2
$3
010
173
120
71
173
21
28
200
225
1
1
29
29
71
33
28
33
29
29
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
lru V tag data
M
M
Hit
M
M
Hit
0
1
Misses: 4
Hits: 2
Reads: 8
Writes: 3

## Slide 104: Write-Through (REF 7)
Cache
Register File
33
29
29
123
29
162
18
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
101
$0
$1
$2
$3
010
173
120
71
173
21
28
200
225
1
1
29
29
71
28
33
29
29
33
29
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
lru V tag data
M
M
Hit
M
M
Hit
Hit
0
1
Misses: 4
Hits: 3
Reads: 8
Writes: 4

## Slide 105: Summary: Write Through
Write-through policy with write allocate
Cache miss: read entire block from memory
Write: write only updated item to memory
Eviction: no need to write to memory

## Slide 106: Next Goal: Write-Through vs. Write-Back
What if we DON’T to write stores immediately to memory?
  Keep the current copy in cache, and update memory when data is evicted (write-back policy)
  Write-back all evicted lines?
    No, only written-to blocks

## Slide 107: Write-Back Meta-Data (Valid, Dirty Bits)
V = 1 means the line has valid data
D = 1 means the bytes are newer than main memory
When allocating line:
  Set V = 1, D = 0, fill in Tag and Data
When writing line:
  Set D = 1
When evicting line:
  If D = 0: just set V = 0
  If D = 1: write-back Data, then set D = 0, V = 0
V | D | Tag | Byte 1 | Byte 2 | … Byte N

## Slide 108: Write-back Example
Example: How does a write-back cache work?
Assume write-allocate

## Slide 109: Handling Stores (Write-Back)
Cache
Register File
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
$0
$1
$2
$3
78
120
71
173
21
28
200
225
Misses: 0
Hits: 0
Reads: 0
Writes: 0
0
0
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
lru V d tag data
16 byte, byte-addressed memory
4 btye, fully-associative cache:
2-byte blocks, write-allocate
4 bit addresses:
3 bit tag, 1 bit offset
1
0

## Slide 110: Write-Back (REF 1)
Cache
Register File
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
$0
$1
$2
$3
78
120
71
173
21
28
200
225
0
0
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
lru V d tag data
1
0
Misses: 0
Hits: 0
Reads: 0
Writes: 0

## Slide 111: Write-Back (REF 1)
Cache
Register File
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
000
$0
$1
$2
$3
78
120
71
173
21
28
200
225
0
1
0
29
78
29
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M
lru V d tag data
0
1
Misses: 1
Hits: 0
Reads: 2
Writes: 0

## Slide 112: Write-Back (REF 2)
Cache
Register File
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
000
$0
$1
$2
$3
78
120
71
173
21
28
200
225
0
1
0
29
78
29
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M
lru V d tag data
0
1
Misses: 1
Hits: 0
Reads: 2
Writes: 0

## Slide 113: Write-Back (REF 2)
Cache
Register File
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
000
$0
$1
$2
$3
011
78
120
71
173
21
28
200
225
0
0
1
1
29
78
29
162
173
173
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
1
0
M
M
lru V d tag data
Misses: 2
Hits: 0
Reads: 4
Writes: 0

## Slide 114: Write-Back (REF 3)
Cache
Register File
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
000
$0
$1
$2
$3
011
78
120
71
173
21
28
200
225
0
0
1
1
29
78
162
173
29
173
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
1
0
M
M
lru V d tag data
Misses: 2
Hits: 0
Reads: 4
Writes: 0

## Slide 115: Write-Back (REF 3)
Cache
Register File
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
000
$0
$1
$2
$3
011
78
120
71
173
21
28
200
225
1
0
1
1
29
173
29
162
173
173
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M
M
Hit
lru V d tag data
0
1
Misses: 2
Hits: 1
Reads: 4
Writes: 0

## Slide 116: Write-Back (REF 4)
Cache
Register File
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
000
$0
$1
$2
$3
011
78
120
71
173
21
28
200
225
1
0
1
1
29
173
29
162
173
173
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M
M
Hit
lru V d tag data
0
1
Misses: 2
Hits: 1
Reads: 4
Writes: 0

## Slide 117: Write-Back (REF 4)
Cache
Register File
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
000
$0
$1
$2
$3
011
78
120
71
173
21
28
200
225
1
0
1
1
29
173
29
162
173
173
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M
M
Hit
lru V d tag data
0
1
Misses: 3
Hits: 1
Reads: 6
Writes: 0

## Slide 118: Write-Back (REF 4)
Cache
Register File
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
000
$0
$1
$2
$3
010
78
120
71
173
21
28
200
225
1
1
1
1
29
173
29
173
150
71
29
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
1
0
M
M
Hit
M
lru V d tag data
Misses: 3
Hits: 1
Reads: 6
Writes: 0

## Slide 119: Write-Back (REF 5)
Cache
Register File
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
000
$0
$1
$2
$3
010
78
120
71
173
21
28
200
225
1
1
1
1
29
173
29
173
29
71
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
1
0
M
M
Hit
M
lru V d tag data
Misses: 3
Hits: 1
Reads: 6
Writes: 0

## Slide 120: Write-Back (REF 5)
Cache
Register File
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
000
$0
$1
$2
$3
010
78
120
71
173
21
28
200
225
1
1
1
1
29
173
29
173
29
71
173
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
1
0
M
M
Hit
M
lru V d tag data
Misses: 3
Hits: 1
Reads: 6
Writes: 2
Eviction, WB dirty block

## Slide 121: Write-Back (REF 5)
Cache
Register File
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
101
$0
$1
$2
$3
010
173
120
71
173
21
28
200
225
0
1
1
1
29
29
71
33
28
33
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M
M
Hit
M
M
lru V d tag data
0
1
Misses: 4
Hits: 1
Reads: 8
Writes: 2

## Slide 122: Write-Back (REF 6)
Cache
Register File
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
101
$0
$1
$2
$3
010
173
120
71
173
21
28
200
225
0
1
1
1
29
29
71
33
28
33
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M
M
Hit
M
M
lru V d tag data
0
1
Misses: 4
Hits: 1
Reads: 8
Writes: 2
CLICKER:
HIT
MISS

## Slide 123: Write-Back (REF 6)
Cache
Register File
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
101
$0
$1
$2
$3
010
173
120
71
173
21
28
200
225
0
1
1
1
29
29
71
33
28
33
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
1
0
M
M
Hit
M
M
Hit
lru V d tag data
Misses: 4
Hits: 2
Reads: 8
Writes: 2

## Slide 124: Write-Back (REF 7)
Cache
Register File
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
101
$0
$1
$2
$3
010
173
120
71
173
21
28
200
225
0
1
1
1
29
29
71
33
28
33
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
1
0
M
M
Hit
M
M
Hit
lru V d tag data
Misses: 4
Hits: 2
Reads: 8
Writes: 2

## Slide 125: Write-Back (REF 7)
Cache
Register File
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
101
$0
$1
$2
$3
010
173
120
71
173
21
28
200
225
1
1
1
1
29
29
71
29
28
33
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M
M
Hit
M
M
Hit
Hit
lru V d tag data
0
1
Misses: 4
Hits: 3
Reads: 8
Writes: 2

## Slide 126: Write-Back (REF 8,9)
Cache
Register File
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
101
$0
$1
$2
$3
010
173
120
71
173
21
28
200
225
1
1
1
1
29
29
71
29
28
33
Memory
Instructions:
...
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M
M
Hit
M
M
Hit
Hit
lru V d tag data
0
1
Misses: 4
Hits: 3
Reads: 8
Writes: 2
Cheap subsequent updates!

## Slide 127: Write-Back (REF 8,9)
Cache
Register File
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
101
$0
$1
$2
$3
010
173
120
71
173
21
28
200
225
1
1
1
1
29
29
71
29
28
33
Memory
Instructions:
...
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
M
M
Hit
M
M
Hit
Hit
Hit
Hit
lru V d tag data
0
1
Misses: 4
Hits: 3
Reads: 8
Writes: 2

## Slide 128: How Many Memory References?
Write-back performance
How many reads?
  Each miss (read or write) reads a block from mem
  4 misses  8 mem reads
How many writes?
  Some evictions write a block to mem
  1 dirty eviction  2 mem writes
  (+ 2 dirty evictions later  +4 mem writes)

## Slide 129: Write-back vs. Write-through Example
Assume: large associative cache, 16-byte lines
N 4-byte words
for (i=1; i<n; i++)
A[0] += A[i];
for (i=0; i<n; i++)
B[i] = A[i]
Write-thru: n/4 reads
n writes
Write-back: n/4 reads
1 write
Write-thru: 2 x n/4 reads
n writes
Write-back: 2 x n/4 reads
n/4 writes
Notes: Q: direct, or associative? A: associative definitely (w/ LRU or LFU, etc.)
A) reads: miss every W’th A[i]
A) writes: n for write-through, 1 eviction for write-back
B) reads: miss every W’th A[i] or B[i]
B) writes: n for write-through, n for write-back

## Slide 130: So is write back just better?
Short Answer: Yes (fewer writes is a good thing)
Long Answer: It’s complicated.
Evictions require entire line be written back to memory (vs. just the data that was written)
Write-back can lead to incoherent caches on multi-core processors (later lecture)

## Slide 131: Optimization: Write Buffering
Q: Writes to main memory are slow!
A: Use a write-back buffer
  A small queue holding dirty lines
  Add to end upon eviction
  Remove from front upon completion
Q: When does it help?
A: short bursts of writes (but not sustained writes)
A: fast eviction reduces miss penalty

## Slide 132: Write-through vs. Write-back
Write-through is slower
  But simpler (memory always consistent)
Write-back is almost always faster
  write-back buffer hides large eviction cost
  But what about multiple cores with separate caches but sharing memory?
Write-back requires a cache coherency protocol
  Inconsistent views of memory
  Need to “snoop” in each other’s caches
  Extremely complex protocols, very hard to get right

## Slide 133: Cache-coherency
Q: Multiple readers and writers?
  A: Potentially inconsistent views of memory
Mem
L2
L1
L1
Cache coherency protocol
  May need to snoop on other CPU’s cache activity
  Invalidate cache line when other CPU writes
  Flush write-back caches before other CPU reads
  Or the reverse: Before writing/reading…
  Extremely complex protocols, very hard to get right
CPU
L1
L1
CPU
L2
L1
L1
CPU
L1
L1
CPU
disk
net
A
A
A
A
A’
A

## Slide 134
Write-through policy with write allocate
  Cache miss: read entire block from memory
  Write: write only updated item to memory
  Eviction: no need to write to memory
  Slower, but cleaner
Write-back policy with write allocate
  Cache miss: read entire block from memory
    **But may need to write dirty cacheline first**
  Write: nothing to memory
  Eviction: have to write to memory entire cacheline because don’t know what is dirty (only 1 dirty bit)
  Faster, but more complicated, especially with multicore
Takeaway

## Slide 135
1 |  |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  |  | 
6 |  |  |  |  |  |  |  |  | 
Every access a cache miss! (unless entire matrix fits in cache)
// H = 6, W = 10
int A[H][W];
for(x=0; x < W; x++)
for(y=0; y < H; y++)
sum += A[y][x];
Cache Conscious Programming
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
6 |  |  | 
MEMORY
CACHE
YOUR MIND
H
W

## Slide 136
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |  | 
Cache Conscious Programming
1 | 2 | 3 | 4
5 | 6 | 7 | 8
MEMORY
CACHE
YOUR MIND
H
W
// H = 6, W = 10
int A[H][W];
for(x=0; x < H; x++)
for(y=0; y < W; y++)
sum += A[x][y];
Block size = 4  75% hit rate
Block size = 8  87.5% hit rate
Block size = 16  93.75% hit rate
And you can easily prefetch to warm the cache

## Slide 137: Clicker Question
Choose the best block size for your cache among the choices given. Assume that integers and pointers are all 4 bytes each and that the scores array is 4-byte aligned.
(a) 1 byte (b) 4 bytes (c) 8 bytes (d) 16 bytes (e) 32 bytes
int scores[NUM STUDENTS] = 0;
int sum = 0; for (i = 0; i < NUM STUDENTS; i++) {
sum += scores[i];
}
Notes: Answer: E

## Slide 138: Clicker Question
Choose the best block size for your cache among the choices given. Assume that integers and pointers are all 4 bytes each and that the scores array is 4-byte aligned.
(a) 1 byte (b) 4 bytes (c) 8 bytes (d) 16 bytes (e) 32 bytes
int scores[NUM STUDENTS] = 0;
int sum = 0; for (i = 0; i < NUM STUDENTS; i++) {
sum += scores[i];
}
Notes: Answer: E

## Slide 139: Clicker Question
Choose the best block size for your cache among the choices given. Assume integers and pointers are 4 bytes.
(a) 1 byte (b) 4 bytes (c) 8 bytes (d) 16 bytes (e) 32 bytes
int sum = 0;
item_t *curr = list_head; while (curr != NULL) {
sum += curr->value;
curr = curr->next;
}
typedef struct item_t {
int value;
struct item_t *next;
char *name;
} item_t;
Notes: Answer: C

## Slide 140: Clicker Question
Choose the best block size for your cache among the choices given. Assume integers and pointers are 4 bytes.
(a) 1 byte (b) 4 bytes (c) 8 bytes (d) 16 bytes (e) 32 bytes
int sum = 0;
item_t *curr = list_head; while (curr != NULL) {
sum += curr->value;
curr = curr->next;
}
typedef struct item_t {
int value;
struct item_t *next;
char *name;
} item_t;
Notes: Answer: C

## Slide 141: By the end of the cache lectures…

## Slide 142: A Real Example
> dmidecode -t cache
Cache Information
Socket Designation: L1 Cache
Configuration: Enabled, Not Socketed, Level 1
Operational Mode: Write Back
Location: Internal
Installed Size: 128 kB
Maximum Size: 128 kB
Supported SRAM Types:
Synchronous
Installed SRAM Type: Synchronous
Speed: Unknown
Error Correction Type: Parity
System Type: Unified
Associativity: 8-way Set-associative
Cache Information
Socket Designation: L2 Cache
Configuration: Enabled, Not Socketed,
Level 2
Operational Mode: Write Back
Location: Internal
Installed Size: 512 kB
Maximum Size: 512 kB
Supported SRAM Types:
Synchronous
Installed SRAM Type: Synchronous
Speed: Unknown
Error Correction Type: Single-bit ECC
System Type: Unified
Associativity: 4-way Set-associative
Microsoft Surfacebook
Dual core
Intel i7-6600 CPU @ 2.6 GHz (purchased in 2016)
Cache Information
Socket Designation: L3 Cache
Configuration: Enabled, Not Socketed,
Level 3
Operational Mode: Write Back
Location: Internal
Installed Size: 4096 kB
Maximum Size: 4096 kB
Supported SRAM Types:
Synchronous
Installed SRAM Type: Synchronous
Speed: Unknown
Error Correction Type: Multi-bit ECC
System Type: Unified
Associativity: 16-way Set-associative

## Slide 143: A Real Example
> sudo dmidecode -t cache
Cache Information
Configuration: Enabled, Not Socketed, Level 1
Operational Mode: Write Back
Installed Size: 128 KB
Error Correction Type: None
Cache Information
Configuration: Enabled, Not Socketed, Level 2
Operational Mode: Varies With Memory Address
Installed Size: 6144 KB
Error Correction Type: Single-bit ECC
> cd /sys/devices/system/cpu/cpu0; grep cache/*/*
cache/index0/level:1
cache/index0/type:Data
cache/index0/ways_of_associativity:8
cache/index0/number_of_sets:64
cache/index0/coherency_line_size:64
cache/index0/size:32K
cache/index1/level:1
cache/index1/type:Instruction
cache/index1/ways_of_associativity:8
cache/index1/number_of_sets:64
cache/index1/coherency_line_size:64
cache/index1/size:32K
cache/index2/level:2
cache/index2/type:Unified
cache/index2/shared_cpu_list:0-1
cache/index2/ways_of_associativity:24
cache/index2/number_of_sets:4096
cache/index2/coherency_line_size:64
cache/index2/size:6144K
Dual-core 3.16GHz Intel (purchased in 2011)

## Slide 144: A Real Example
Dual 32K L1 Instruction caches
  8-way set associative
  64 sets
  64 byte line size
Dual 32K L1 Data caches
  Same as above
Single 6M L2 Unified cache
  24-way set associative (!!!)
  4096 sets
  64 byte line size
4GB Main memory
1TB Disk
Dual-core 3.16GHz Intel (purchased in 2009)

## Slide 146: Summary
Memory performance matters!
  often more than CPU performance
  … because it is the bottleneck, and not improving much
  … because most programs move a LOT of data
Design space is huge
  Gambling against program behavior
  Cuts across all layers: users  programs  os  hardware
NEXT: Multi-core processors are complicated
  Inconsistent views of memory
  Extremely complex protocols, very hard to get right