## Slide 1: Caches & Memory
CS 3410
Computer System Organization & Programming
These slides are the product of many rounds of teaching CS 3410 by Professors Weatherspoon, Bala, Bracy, and Sirer.

## Slide 2: Programs 101
Load/Store Architectures:
Read data from memory (put in registers)
Manipulate it
Store it back to memory
int main (int argc, char* argv[ ]) {
int i;
int m = n;
int sum = 0;
for (i = 1; i <= m; i++) {
sum += i;
}
printf (“...”, n, sum);
}
C Code
main: addiu $sp,$sp,-48
sw $31,44($sp)
sw $fp,40($sp)
move $fp,$sp
sw $4,48($fp)
sw $5,52($fp)
la $2,n
lw $2,0($2)
sw $2,28($fp)
sw $0,32($fp)
li $2,1
sw $2,24($fp)
$L2: lw $2,24($fp)
lw $3,28($fp)
slt $2,$3,$2
bne $2,$0,$L3
. . .
MIPS Assembly
Instructions that read from
or write to memory…

## Slide 3: 1 Cycle Per Stage: the Biggest Lie (So Far)
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
ALU
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard
Stack, Data, Code
Stored in Memory
Code Stored in Memory
(also, data and stack)

## Slide 4: What’s the problem?
+ big
– slow
– far away
SandyBridge Motherboard, 2011
http://news.softpedia.com
CPU
Main Memory

## Slide 5: The Need for Speed
CPU Pipeline
Notes: I made these two slides to see if you can make everything Ampelmännchen instead of first rainbow then ampelmännchen.
Not sure if this captures what you want to say. Just wanted to throw it out there.
(Slides 7/8 would be an alternative for slides 4/5/6)

## Slide 6: The Need for Speed
Instruction speeds:
add,sub,shift: 1 cycle
mult: 3 cycles
load/store: 100 cycles
  off-chip 50(-70)ns
  2(-3) GHz processor  0.5 ns clock
CPU Pipeline
Notes: This is great, but I would re-arrange it. First say that load/store requires 100 cycles (parallel to mult, add). This is your punch-line and probably surprising to the students.
Then explain why it is the case.

## Slide 7: The Need for Speed
CPU Pipeline

## Slide 8: What’s the solution?
Level 2 $
Level 1
Data $
Level 1
Insn $
Intel Pentium 3, 1999
Caches !

## Slide 9: Aside
Go back to 04-state and look at how SRAM and DRAM are built.

## Slide 10: What’s the solution?
What lucky data gets to go here?
Level 2 $
Level 1
Data $
Level 1
Insn $
Intel Pentium 3, 1999
Caches !

## Slide 11: Locality Locality Locality
If you ask for something, you’re likely to ask for:
the same thing again soon
 Temporal Locality
something near that thing, soon
 Spatial Locality
total = 0;
for (i = 0; i < n; i++)
total += a[i];
return total;

## Slide 12: Your life is full of Locality
Last Called
Speed Dial
Favorites
Contacts
Google/Facebook/email

## Slide 13: Your life is full of Locality

## Slide 14: The Memory Hierarchy
Registers
L1 Caches
L2 Cache
L3 Cache
Main Memory
Disk
1 cycle,
128 bytes
4 cycles,
64 KB
Intel Haswell Processor, 2013
12 cycles,
256 KB
36 cycles,
2-20 MB
50-70 ns,
512 MB – 4 GB
5-20 ms
16GB – 4 TB,
Small, Fast
Big, Slow

## Slide 15: Some Terminology
Cache hit
data is in the Cache
thit : time it takes to access the cache
Hit rate (%hit): # cache hits / # cache accesses
Cache miss
data is not in the Cache
tmiss : time it takes to get the data from below the $
Miss rate (%miss): # cache misses / # cache accesses

## Slide 16: The Memory Hierarchy
Registers
L1 Caches
1 cycle,
128 bytes
4 cycles,
64 KB
Intel Haswell Processor, 2013
50-70 ns,
512 MB – 4 GB
5-20 ms
16GB – 4 TB,
  average access time
  tavg = thit + %miss* tmiss
  = 4 + 5% x 100
  = 9 cycles
12 cycles,
256 KB
36 cycles,
2-20 MB
L2 Cache
L3 Cache
Main Memory
Disk

## Slide 17: Single Core Memory Hierarchy
Registers
L1 Caches
L2 Cache
L3 Cache
Main Memory
Disk
ON CHIP
Disk
Processor
Regs
I$
D$
L2
Main Memory

## Slide 18: Multi-Core Memory Hierarchy
ON CHIP
Main Memory
Processor
Regs
I$
D$
L2
L3
Processor
Regs
I$
D$
L2
Processor
Regs
I$
D$
L2
Processor
Regs
I$
D$
L2
Disk
Notes: This is my suggestion

## Slide 19: Memory Hierarchy by the Numbers
CPU clock rates ~0.33ns – 2ns (3GHz-500MHz)
*Registers,D-Flip Flops: 10-100’s of registers
Memory technology | Transistor count* | Access time | Access time in cycles | $ per GIB in 2012 | Capacity
SRAM (on chip) | 6-8 transistors | 0.5-2.5 ns | 1-3 cycles | $4k | 256 KB
SRAM (off chip) |  | 1.5-30 ns | 5-15 cycles | $4k | 32 MB
DRAM | 1 transistor (needs refresh) | 50-70 ns | 150-200 cycles | $10-$20 | 8 GB
SSD (Flash) |  | 5k-50k ns | Tens of thousands | $0.75-$1 | 512 GB
Disk |  | 5M-20M ns | Millions | $0.05-$0.1 | 4 TB
Notes: Capacity and latency are closely coupled
Cost is inversely proportional

## Slide 20: Basic Cache Design
Direct Mapped Caches

## Slide 21: 16 Byte Memory
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
MEMORY
Byte-addressable memory
4 address bits  16 bytes total
b addr bits  2b bytes in memory
load 1100  r1

## Slide 22: 4-Byte, Direct Mapped Cache
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
MEMORY
CACHE
data
A
B
C
D
Direct mapped:
Each address maps to 1 cache block
4 entries  2 index bits (2n  n bits)
Index with LSB:
Supports spatial locality
index
XXXX
index
00
01
10
11
Cache entry
= row
= (cache) line
= (cache) block
Block Size: 1 byte

## Slide 23: Analogy to a Spice Rack
Compared to your spice wall
  Smaller
  Faster
  More costly (per oz.)
A
B
C
D
E
F
…
Z
http://www.bedbathandbeyond.com
Spice Wall
(Memory)
Spice Rack
(Cache)
index spice

## Slide 24: Analogy to a Spice Rack
Cinnamon
How do you know what’s in the jar?
Need labels
  Tag = Ultra-minimalist label
innamon
Spice Wall
(Memory)
A
B
C
D
E
F
…
Z
Spice Rack
(Cache)
index spice
tag

## Slide 25: 4-Byte, Direct Mapped Cache
tag|index
XXXX
 | data
 | A
 | B
 | C
 | D
tag
00
00
00
00
MEMORY
CACHE
Tag: minimalist label/address
address = tag + index
index
00
01
10
11
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q

## Slide 26: 4-Byte, Direct Mapped Cache
MEMORY
CACHE
One last tweak: valid bit
V | tag | data
0 | 00 | X
0 | 00 | X
0 | 00 | X
0 | 00 | X
index
00
01
10
11
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q

## Slide 27: Simulation #1 of a 4-byte, DM Cache
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
Lookup:
Index into $
Check tag
Check valid bit
MEMORY
CACHE
V | tag | data
0 | 11 | X
0 | 11 | X
0 | 11 | X
0 | 11 | X
tag|index
XXXX
index
00
01
10
11
load 1100
...
load 1100

## Slide 28: Block Diagram 4-entry, direct mapped Cache
CACHE
V | tag | data
1 | 00 | 1111 0000
1 | 11 | 1010 0101
0 | 01 | 1010 1010
1 | 11 | 0000 0000
tag|index
1101
2
2
2
=
Hit!
data
8
1010 0101

## Slide 29
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
MEMORY
CACHE
V | tag | data
0 | 11 | X
0 | 11 | X
0 | 11 | X
0 | 11 | X
load 1100
load 1101
load 0100
load 1100
Lookup:
Index into $
Check tag
Check valid bit
index
00
01
10
11
Simulation #2:
4-byte, DM Cache

## Slide 30: Reducing Cold Misses by Increasing Block Size
Leveraging Spatial Locality

## Slide 31: Increasing Block Size
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
CACHE
V | tag | data
0 | x | A ¦ B
0 | x | C ¦ D
0 | x | E ¦ F
0 | x | G ¦ H
MEMORY
Block Size: 2 bytes
Block Offset: least significant bits indicate where you live in the block
Which bits are the index? tag?
offset
XXXX
index
00
01
10
11

## Slide 32: Simulation #3: 8-byte, DM Cache
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
MEMORY
CACHE
V | tag | data
0 | x | X ¦ X
0 | x | X ¦ X
0 | x | X ¦ X
0 | x | X ¦ X
load 1100
load 1101
load 0100
load 1100
tag| |offset
XXXX
index
Lookup:
Index into $
Check tag
Check valid bit
index
00
01
10
11

## Slide 33: Removing Conflict Misses with Fully-Associative Caches

## Slide 34: Simulation #4: 8-byte, FA Cache
V | tag | data
0 | xxx | X ¦ X
V | tag | data
0 | xxx | X ¦ X
V | tag | data
0 | xxx | X ¦ X
V | tag | data
0 | xxx | X ¦ X
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
MEMORY
load 1100
load 1101
load 0100
load 1100
XXXX
tag|offset
Lookup:
Index into $
Check tags
Check valid bits
CACHE
LRU Pointer

## Slide 35: Pros and Cons of Full Associativity
+ No more conflicts!
+ Excellent utilization!
But either:
Parallel Reads
– lots of reading!
Serial Reads
– lots of waiting
  tavg = thit + %miss* tmiss
  = 4 + 5% x 100
  = 9 cycles
  = 6 + 3% x 100
  = 9 cycles

## Slide 36: Pros & Cons
 | Direct Mapped | Fully Associative
Tag Size | Smaller | Larger
SRAM Overhead | Less | More
Controller Logic | Less | More
Speed | Faster | Slower
Price | Less | More
Scalability | Very | Not Very
# of conflict misses | Lots | Zero
Hit Rate | Low | High
Pathological Cases | Common | ?

## Slide 37: Reducing Conflict Misses with Set-Associative Caches
Not too conflict-y. Not too slow.
… Just Right!

## Slide 38: 8 byte, 2-way set associative Cache
CACHE
MEMORY
What should the offset be?
What should the index be?
What should the tag be?
XXXX
tag||offset
index
XXXX
offset
V | tag | data
0 | xx | E ¦ F
0 | xx | C ¦ D
V | tag | data
0 | xx | N ¦ O
0 | xx | P ¦ Q
XXXX
index
0
1
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q

## Slide 39: 8 byte, 2-way set associative Cache
addr | data
0000 | A
0001 | B
0010 | C
0011 | D
0100 | E
0101 | F
0110 | G
0111 | H
1000 | J
1001 | K
1010 | L
1011 | M
1100 | N
1101 | O
1110 | P
1111 | Q
CACHE
index
0
1
MEMORY
XXXX
tag||offset
index
V | tag | data
0 | xx | X ¦ X
0 | xx | X ¦ X
V | tag | data
0 | xx | X ¦ X
0 | xx | X ¦ X
load 1100
load 1101
load 0100
load 1100
Miss
Lookup:
Index into $
Check tag
Check valid bit
LRU Pointer

## Slide 40: Eviction Policies
Which cache line should be evicted from the cache to make room for a new line?
Direct-mapped: no choice, must evict line selected by index
Associative caches
  Random: select one of the lines at random
  Round-Robin: similar to random
  FIFO: replace oldest line
  LRU: replace line that has not been used in the longest time

## Slide 41: Misses: the Three C’s
Cold (compulsory) Miss:
never seen this address before
Conflict Miss:
cache associativity is too low
Capacity Miss:
cache is too small

## Slide 42: Miss Rate vs. Block Size

## Slide 43: Block Size Tradeoffs
For a given total cache size,
Larger block sizes mean….
  fewer lines
  so fewer tags, less overhead
  and fewer cold misses (within-block “prefetching”)
But also…
  fewer blocks available (for scattered accesses!)
  so more conflicts
  can decrease performance if working set can’t fit in $
  and larger miss penalty (time to fetch block)
Notes: Same for other parameters: experimental mostly

## Slide 44: Miss Rate vs. Associativity

## Slide 45: ABCs of Caches
+ Associativity:
⬇conflict misses 
⬆hit time 
+ Block Size:
⬇cold misses 
⬆conflict misses 
+ Capacity:
⬇capacity misses 
⬆hit time 
  tavg = thit + %miss* tmiss

## Slide 46: Which caches get what properties?
L1 Caches
L2 Cache
L3 Cache
Fast
Big
More Associative
Bigger Block Sizes
Larger Capacity
  tavg = thit + %miss* tmiss
Design with miss rate in mind
Design with speed in mind

## Slide 47: Roadmap
Things we have covered:
  The Need for Speed
  Locality to the Rescue!
  Calculating average memory access time
  $ Misses: Cold, Conflict, Capacity
  $ Characteristics: Associativity, Block Size, Capacity
Things we will now cover:
  Cache Figures
  Cache Performance Examples
  Writes

## Slide 48: 2-Way Set Associative Cache (Reading)
hit?
line select
64bytes
Tag Index Offset
data
word select
32bits
=
=
Tag
Tag
V
V
Data
Data

## Slide 49: 3-Way Set Associative Cache (Reading)
data
word select
hit?
line select
=
=
=
32bits
64bytes
Tag Index Offset

## Slide 50: How Big is the Cache?
n bit index, m bit offset, N-way Set Associative
Question: How big is cache?
Data only?
(what we usually mean when we ask “how big” is the cache)
Data + overhead?
Tag Index Offset

## Slide 51: Performance Calculation with $ Hierarchy
Parameters
  Reference stream: all loads
  D$: thit = 1ns, %miss = 5%
  L2: thit = 10ns, %miss = 20% (local miss rate)
  Main memory: thit = 50ns
What is tavgD$ without an L2?
  tmissD$ =
  tavgD$ =
What is tavgD$ with an L2?
  tmissD$ =
  tavgL2 =
  tavgD$ =
  tavg = thit + %miss* tmiss

## Slide 52: Performance Summary
Average memory access time (AMAT) depends on:
cache architecture and size
Hit and miss rates
Access times and miss penalty
Cache design a very complex problem:
Cache size, block size (aka line size)
Number of ways of set-associativity (1, N, )
Eviction policy
Number of levels of caching, parameters for each
Separate I-cache from D-cache, or Unified cache
Prefetching policies / instructions
Write policy

## Slide 53: Takeaway
Direct Mapped  fast, but low hit rate
Fully Associative  higher hit cost, higher hit rate
Set Associative  middleground
Line size matters. Larger cache lines can increase performance due to prefetching. BUT, can also decrease performance is working set size cannot fit in cache.
Cache performance is measured by the average memory access time (AMAT), which depends cache architecture and size, but also the access time for hit, miss penalty, hit rate.

## Slide 54: What about Stores?
We want to write to the cache.
If the data is not in the cache?
  Bring it in. (Write allocate policy)
Should we also update memory?
Yes: write-through policy
No: write-back policy

## Slide 55: Write-Through Cache
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
Cache
Register File
$0
$1
$2
$3
Memory
78
120
71
173
21
28
200
225
Misses: 0
Hits: 0
Reads: 0
Writes: 0
0
0
16 byte, byte-addressed memory
4 btye, fully-associative cache:
2-byte blocks, write-allocate
4 bit addresses:
3 bit tag, 1 bit offset
lru V tag data
1
0

## Slide 56: Write-Through (REF 1)
Cache
Register File
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
$0
$1
$2
$3
78
120
71
173
21
28
200
225
Misses: 0
Hits: 0
Reads: 0
Writes: 0
0
0
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
lru V tag data
1
0

## Slide 57: Summary: Write Through
Write-through policy with write allocate
Cache miss: read entire block from memory
Write: write only updated item to memory
Eviction: no need to write to memory

## Slide 58: Next Goal: Write-Through vs. Write-Back
What if we DON’T to write stores immediately to memory?
  Keep the current copy in cache, and update memory when data is evicted (write-back policy)
  Write-back all evicted lines?
    No, only written-to blocks

## Slide 59: Write-Back Meta-Data (Valid, Dirty Bits)
V = 1 means the line has valid data
D = 1 means the bytes are newer than main memory
When allocating line:
  Set V = 1, D = 0, fill in Tag and Data
When writing line:
  Set D = 1
When evicting line:
  If D = 0: just set V = 0
  If D = 1: write-back Data, then set D = 0, V = 0
V | D | Tag | Byte 1 | Byte 2 | … Byte N

## Slide 60: Write-back Example
Example: How does a write-back cache work?
Assume write-allocate

## Slide 61: Handling Stores (Write-Back)
Cache
Register File
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
$0
$1
$2
$3
78
120
71
173
21
28
200
225
Misses: 0
Hits: 0
Reads: 0
Writes: 0
0
0
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
lru V d tag data
16 byte, byte-addressed memory
4 btye, fully-associative cache:
2-byte blocks, write-allocate
4 bit addresses:
3 bit tag, 1 bit offset
1
0

## Slide 62: Write-Back (REF 1)
Cache
Register File
29
123
150
162
18
33
19
210
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
$0
$1
$2
$3
78
120
71
173
21
28
200
225
0
0
Memory
Instructions:
LB $1  M[ 1 ]
LB $2  M[ 7 ]
SB $2  M[ 0 ]
SB $1  M[ 5 ]
LB $2  M[ 10 ]
SB $1  M[ 5 ]
SB $1  M[ 10 ]
lru V d tag data
1
0
Misses: 0
Hits: 0
Reads: 0
Writes: 0

## Slide 63: How Many Memory References?
Write-back performance
How many reads?
  Each miss (read or write) reads a block from mem
  4 misses  8 mem reads
How many writes?
  Some evictions write a block to mem
  1 dirty eviction  2 mem writes
  (+ 2 dirty evictions later  +4 mem writes)

## Slide 64: Write-back vs. Write-through Example
Assume: large associative cache, 16-byte lines
N 4-byte words
for (i=1; i<n; i++)
A[0] += A[i];
for (i=0; i<n; i++)
B[i] = A[i]
Notes: Q: direct, or associative? A: associative definitely (w/ LRU or LFU, etc.)
A) reads: miss every W’th A[i]
A) writes: n for write-through, 1 eviction for write-back
B) reads: miss every W’th A[i] or B[i]
B) writes: n for write-through, n for write-back

## Slide 65: So is write back just better?
Short Answer: Yes (fewer writes is a good thing)
Long Answer: It’s complicated.
Evictions require entire line be written back to memory (vs. just the data that was written)
Write-back can lead to incoherent caches on multi-core processors (later lecture)

## Slide 66
1 |  |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  |  | 
6 |  |  |  |  |  |  |  |  | 
Every access a cache miss! (unless entire matrix fits in cache)
// H = 6, W = 10
int A[H][W];
for(x=0; x < W; x++)
for(y=0; y < H; y++)
sum += A[y][x];
Cache Conscious Programming
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
6 |  |  | 
MEMORY
CACHE
YOUR MIND
H
W

## Slide 67: By the end of the cache lectures…

## Slide 69: Summary
Memory performance matters!
  often more than CPU performance
  … because it is the bottleneck, and not improving much
  … because most programs move a LOT of data
Design space is huge
  Gambling against program behavior
  Cuts across all layers: users  programs  os  hardware
NEXT: Multi-core processors are complicated
  Inconsistent views of memory
  Extremely complex protocols, very hard to get right

## Slide 70: Have a great Spring Break!!