## Slide 1: Virtual Memory
CS 3410
Computer System Organization & Programming
These slides are the product of many rounds of teaching CS 3410 by Professors Weatherspoon, Bala, Bracy, and Sirer.

## Slide 2: Announcements
Next five weeks
  Week 10 (Apr 9): Proj4 (Buffer Overflow/calling convention) release, due week later
  Week 11 (Apr 16): Proj5 (caches) release, due week and half later on Fri
  Week 12 (Apr 23): C assignment 2 due Mon
  Week 13 (Apr 30): Proj6 (multi-core/parallelism) release Prelim2 on Thur, May 3
  Week 14 (May 7): Proj5 Tournament, Monday, May 7 Proj6 design doc due
Final Project for class
  Week 15 (May 15): Proj6 due Tue May 15 at 4:30pm

## Slide 3: Where are we now and where are we going?
How many programs do you run at once?
a) 1
b) 2
c) 3-5
d) 6-10
e) 11+
Notes: Take a class poll
People often have many programs/application running at the same time such as a browser, Skype, Facetime, etc

## Slide 4: Big Picture: Multiple Processes
Can we execute more than one program at a time with our current MIPS processor?

## Slide 5: Big Picture: Multiple Processes
How to run multiple processes?
Time-multiplex a single CPU core (multi-tasking)
  Web browser, skype, office, … all must co-exist
Many cores per processor (multi-core) or many processors (multi-processor)
  Multiple programs run simultaneously

## Slide 6: Processor & Memory
CPU address/data bus...
… routed through caches
… to main memory
  Simple, fast, but…
CPU
Text
Data
Stack
Heap
Memory
0x000…0
0x7ff…f
0xfff…f
$$
Notes: Q: What happens for LW/SW to an invalid location?
  0x000000000 (NULL)
  uninitialized pointer
A: Need a memory management unit (MMU)
  Throw (and/or handle) an exception

## Slide 7: Multiple Processes
Q: What happens when another program is executed concurrently on another processor?
CPU
Text
Data
Stack
Heap
Memory
CPU
Text
Data
Stack
Heap
0x000…0
0x7ff…f
0xfff…f
$$
$$

## Slide 8: Multiple Processes
Q: Can we relocate second program?
CPU
Text
Data
Stack
Heap
Memory
CPU
Text
Data
Stack
Heap
0x000…0
0x7ff…f
0xfff…f

## Slide 9: Takeaway
All problems in computer science can be solved by another level of indirection.
– David Wheeler
– or, Butler Lampson
– or, Leslie Lamport
– or, Steve Bellovin
Solution: Need a MAP
To map a Virtual Address (generated by CPU)
to a Physical Address (in memory)

## Slide 10: Big Picture: (Virtual) Memory
How do we execute more than one program at a time?
A: Abstraction – Virtual Memory
  Memory that appears to exist as main memory
  (although most of it is supported by data held in secondary storage, transfer between the two being made automatically as required—i.e. ”paging”)
  Abstraction that supports multi-tasking---the ability to run more than one process at a time

## Slide 11: Next Goal
How does Virtual Memory work?
i.e. How do we create the “map” that maps a virtual address generated by the CPU to a physical address used by main memory?

## Slide 12: Picture Memory as… ?
addr | data
0xffffffff | xaa
 | …
 | …
 | x00
 | x00
 | xef
 | xcd
 | xab
 | xff
0x00000000 | x00
Byte Array:
0xfffffffc
0x00000000
0x7ffffffc
0x80000000
0x10000000
0x00400000
system
reserved
stack
system
reserved
text
data
heap
Segments:
0x00000000
0xffffe000
0xfffff000
0x00003000
0x00001000
page 0
Page Array:
page 1
page 2
. . .
. . .
page n
0x00002000
0x00004000
0xffffd000
each segment uses some # of pages
New!

## Slide 13: A Little More About Pages
Suppose each page = 4KB
Anything in page 2 has address: 0x00002xxx
Lower 12 bits specify which byte you are in the page:
0x00002200 = 0010 0000 0000
= byte 512
upper bits = page number
lower bits = page offset
Sound familiar?
0x00000000
0xffffe000
0xfffff000
0x00003000
0x00001000
Page Array:
…
4KB
0x00002000
0x00004000
0xffffd000

## Slide 14: Data Granularity
ISA: instruction specific: LB, LH, LW (MIPS)
Registers: 32 bits (MIPS)
Caches: cache line/block
Address bits divided into:
index: which entry in the cache
tag: sanity check for address match
offset: which byte in the line
Memory: page
Address bits divided into:
page number: which page in memory
index: which byte in the page

## Slide 15: Program’s View of Memory
These assumptions are embedded
in the executable!
If they are wrong, things will break!
Recompile? Relink?
32-bit machine:
0x00000000 – 0xffffffff to play with
(modulo system reserved)
2 Interesting/Dubious Assumptions:
The machine I’m running on has 4GB of DRAM.
I am the only one using this DRAM.
64-bits:
16 EB ???

## Slide 16: Indirection* to the Rescue!
Virtual Memory: a Solution for All Problems
Each process has its own virtual address space
  Program/CPU can access any address from 0…2N
  A process is a program being executed
  Programmer can code as if they own all of memory
On-the-fly at runtime, for each memory access
  all accesses are indirect through a virtual address
  translate fake virtual address to a real physical address
  redirect load/store to the physical address
*google David Wheeler, Butler Lampson, Leslie Lamport, and Steve Bellovin
map

## Slide 17: Virtual vs. Physical Address Spaces
A
B
C
C
B
A
Program #1’s
Virtual Address
Space
Physical Address Space
Memory (DRAM)
D
D
Address Translation
DISK
A
B
C
D
Program #2’s
Virtual Address
Space
A
B
C
D
Not contiguous
Page vs. Address?
3
2
1
0
9
8
7
6
5
4
3
2
1
0
3
2
1
0
page
page
page
Notes: each mmu has own mappings
Easy relocation
Higher memory utilization
Easy sharing

## Slide 18: Advantages of Virtual Memory
Easy relocation
Loader puts code anywhere in physical memory
Virtual mappings to give illusion of correct layout
Higher memory utilization
Provide illusion of contiguous memory
Use all physical memory, even physical address 0x0
Easy sharing
Different mappings for different programs / cores
And more to come…

## Slide 19: Takeaway
All problems in computer science can be solved by another level of indirection.
Need a map to translate a “fake” virtual address (generated by CPU) to a “real” physical Address (in memory)
Virtual memory is implemented via a “Map”, a PageTage, that maps a vaddr (a virtual address) to a paddr (physical address):
paddr = PageTable[vaddr]

## Slide 20: Next Goal
How do we implement that translation from a virtual address (vaddr) to a physical address (paddr)?
paddr = PageTable[vaddr]
i.e. How do we implement the PageTable??

## Slide 21: Virtual Memory Agenda
What is Virtual Memory?
How does Virtual memory Work?
  Address Translation
  Overhead
  Paging
  Performance
  Virtual Memory & Caches

## Slide 22: Address Translator: MMU
Programs use virtual addresses
Actual memory uses physical addresses
Memory Management Unit (MMU)
HW structure
Translates virtual  physical address on the fly
A
B
C
Program #1
D
A
B
C
D
Program #2
C
B
A
Physical Address Space
Memory (DRAM)
MMU
B
C
D
3
2
1
0
9
8
7
6
5
4
3
2
1
0
3
2
1
0
Notes: each mmu has own mappings
Easy relocation
Higher memory utilization
Easy sharing

## Slide 23: Address Translation: in Page Table
OS-Managed Mapping of Virtual  Physical Pages
int page_table[220] = { 0, 5, 4, 1, … };
. . .
ppn = page_table[vpn];
Remember:
any address 0x00001234
is x234 bytes into Page C
both virtual & physical
VP 1  PP 5
C
B
A
Physical
Address
Space
A
B
C
D
3
2
1
0
Program’s
Virtual Address
Space
9
8
7
6
5
4
3
2
1
0
Assuming each page = 4KB

## Slide 24: Page Table Basics
1 Page Table per process
Lives in Memory, i.e. in a page (or more…)
Location stored in Page Table Base Register
Part of program state (like PC)
C
B
A
Physical
Address
Space
A
B
C
D
3
2
1
0
Program’s
Virtual Address
Space
9
8
7
6
5
4
3
2
1
0
PTBR
0x00008000
Assuming each page = 4KB
. . .
00000001
00000004
00000005
00000000
0x00008000
0x00008004
0x00008008
0x0000800c
0x00008FFF

## Slide 25: Simple Address Translation
1111 1010 1111 0000 1111 0000 1111 0000
Assuming each page = 4KB
Page Offset
Virtual Page Number
Lookup in Page Table
0000 0101 1100 0011 0000 0000 1111 0000
Physical Page Number
Page Offset

## Slide 26: Simple Page Table Translation
Memory
PTBR
0x90000000
Assuming each page = 4KB
0x10045
. . .
0xC20A3
0x4123B
0x10044
0x00000
0x90000000
0x90000004
0x90000008
0x9000000c
0x00008FFF
0x00000000
0x90000000
0x10045000
0xC20A3000
0x10044000
0x4123B000
0x00002 | 0xABC
vaddr
0
11
12
31
0x4123B | 0xABC
paddr

## Slide 27: General Address Translation
What if the page size is not 4KB?
 Page offset is no longer 12 bits
What if Main Memory is not 4GB?
 Physical page number is no longer 20 bits

## Slide 28: Virtual Memory Agenda
What is Virtual Memory?
How does Virtual memory Work?
  Address Translation
  Overhead
  Paging
  Performance
  Virtual Memory & Caches

## Slide 29: Page Table Overhead
How large is PageTable?
Virtual address space (for each process):
  Given: total virtual memory: 232 bytes = 4GB
  Given: page size: 212 bytes = 4KB
  # entries in PageTable?
  size of PageTable?
  This is one, big contiguous array, by the way!
Physical address space:
  Given: total physical memory: 229 bytes = 512MB
  overhead for 10 processes?
Notes: 220 entries in pagetable, so 222 bytes = 4MB (w/ 4byte entries), so 40MB (25% of total!)
Q: Can we possibly have a “full” pagetable?
A: Not enough physical memory pages – some pagetable entries will be duplicates!

## Slide 30: But Wait... There’s more!
Page Table Entry won’t be just an integer
Meta-Data
  Valid Bits
    What PPN means “not mapped”? No such number…
    At first: not all virtual pages will be in physical memory
    Later: might not have enough physical memory to map all virtual pages
  Page Permissions
    R/W/X permission bits for each PTE
    Code: read-only, executable
    Data: writeable, not executable

## Slide 31: Less Simple Page Table
V | R | W | X | Physical Page Number
0 |  |  |  | 
1 | 1 | 1 | 0 | 0xC20A3
0 |  |  |  | 
0 |  |  |  | 
1 | 1 | 0 | 0 | 0xC20A3
1 |  |  |  | 0x4123B
1 |  |  |  | 0x10044
0 |  |  |  | 
0x00000000
0x90000000
0x10045000
0x4123B000
0xC20A3000
0x10044000
Aliasing: mapping several virtual addresses  same physical page
Process tries to access a page without proper permissions
Segmentation Fault
Example:
Write to read-only?  process killed

## Slide 32: Now how big is this Page Table?
struct pte_t page_table[220]
Each PTE = 8 bytes
How many pages in memory will the page table take up?
Assuming each page = 4KB

## Slide 33: Takeaway
All problems in computer science can be solved by another level of indirection.
Need a map to translate a “fake” virtual address (generated by CPU) to a “real” physical Address (in memory)
Virtual memory is implemented via a “Map”, a PageTage, that maps a vaddr (a virtual address) to a paddr (physical address):
paddr = PageTable[vaddr]
A page is constant size block of virtual memory. Often, the page size will be around 4kB to reduce the number of entries in a PageTable.
We can use the PageTable to set Read/Write/Execute permission on a per page basis. Can allocate memory on a per page basis. Need a valid bit, as well as Read/Write/Execute and other bits.
But, overhead due to PageTable is significant.

## Slide 34: Next Goal
How do we reduce the size (overhead) of the PageTable?

## Slide 35: Next Goal
How do we reduce the size (overhead) of the PageTable?
A: Another level of indirection!!

## Slide 36: Multi-Level Page Table
10 bits
PTBR
10 bits
10 bits
vaddr
PDEntry
Page Directory
Page Table
PTEntry
Page
Word
2
* Indirection to the Rescue, AGAIN!
31 22 21 12 11 2 1 0
PPN
Where is my translation?
Where is my physical page?
Also referred to as Level 1 and Level 2 Page Tables

## Slide 37: Multi-Level Page Table
Doesn’t this take up more memory than before?
Benefits
Don’t need 4MB contiguous physical memory
Don’t need to allocate every PageTable, only those containing valid PTEs
Drawbacks
Performance: Longer lookups
Notes: Q: Benefits?
A1: Don’t need 4MB contiguous physical memory
A2: Don’t need to allocate every PageTable, only those containing valid PTEs
Q: Drawbacks?
A: Longer lookups.

## Slide 38: Virtual Memory Agenda
What is Virtual Memory?
How does Virtual memory Work?
  Address Translation
  Overhead
  Paging
  Performance
  Virtual Memory & Caches

## Slide 39: Paging
What if process requirements > physical memory?
Virtual starts earning its name
Memory acts as a cache for secondary storage (disk)
  Swap memory pages out to disk when not in use
  Page them back in when needed
Courtesy of Temporal & Spatial Locality (again!)
  Pages used recently mostly likely to be used again
More Meta-Data:
Dirty Bit, Recently Used, etc.
OS may access this meta-data to choose a victim

## Slide 40: Paging
Example: accessing address beginning with 0x00003 (PageTable[3]) results in a Page Fault which will page the data in from disk sector 200
V | R | W | X | D | Physical Page Number
0 |  |  |  |  | --
1 | 1 | 0 | 1 | 0 | 0x10045
0 |  |  |  |  | --
0 |  |  |  |  | --
0 |  |  |  | 0 | disk sector 200
0 |  |  |  | 0 | disk sector 25
1 | 1 | 1 | 0 | 1 | 0x00000
0 |  |  |  |  | --
0x00000000
0x90000000
0x10045000
0x4123B000
0xC20A3000
25
200
Notes: A: can make code read-only, executable; make data read-write but not executable; etc.

## Slide 41: Page Fault
Valid bit in Page Table = 0
 means page is not in memory
OS takes over:
Choose a physical page to replace
  “Working set”: refined LRU, tracks page usage
If dirty, write to disk
Read missing page from disk
  Takes so long (~10ms), OS schedules another task
Performance-wise page faults are really bad!

## Slide 42: Virtual Memory Agenda
What is Virtual Memory?
How does Virtual memory Work?
  Address Translation
  Overhead
  Paging
  Performance
  Virtual Memory & Caches

## Slide 43: Watch Your Performance Tank!
For every instruction:
MMU translates address (virtual  physical)
  Uses PTBR to find Page Table in memory
  Looks up entry for that virtual page
Fetch the instruction using physical address
  Access Memory Hierarchy (I$  L2  Memory)
Repeat at Memory stage for load/store insns
  Translate address
  Now you perform the load/store

## Slide 44: Performance
Virtual Memory Summary
PageTable for each process:
  Page
    Single-level (e.g. 4MB contiguous in physical memory)
    or multi-level (e.g. less mem overhead due to page table),
    …
  every load/store translated to physical addresses
  page table miss: load a swapped-out page and retry instruction, or kill program
Performance?
Solution?
Notes: 4x slower!
Pipelining? No. Parallelization? No.

## Slide 45: Next Goal
How do we speedup address translation?

## Slide 46: Translation Lookaside Buffer (TLB)
Small, fast cache
Holds VPNPPN translations
Exploits temporal locality in pagetable
TLB Hit: huge performance savings
TLB Miss: invoke TLB miss handler
    Put translation in TLB for later
VPN
PPN
VPN
PPN
VPN
PPN
“tag”
“data”
CPU
VA
PA
VA
PA
MMU
TLB
VA

## Slide 47: TLB Parameters
Typical
very small (64 – 256 entries)  very fast
fully associative, or at least set associative
tiny block size: why?
Example: Intel Nehalem TLB
128-entry L1 Instruction TLB, 4-way LRU
64-entry L1 Data TLB, 4-way LRU
512-entry L2 Unified TLB, 4-way LRU

## Slide 48: TLB to the Rescue!
For every instruction:
Translate the address (virtual  physical)
  CPU checks TLB
  That failing, walk the Page Table
    Use PTBR to find Page Table in memory
    Look up entry for that virtual page
    Cache the result in the TLB
Fetch the instruction using physical address
  Access Memory Hierarchy (I$  L2  Memory)
Repeat at Memory stage for load/store insns
  CPU checks TLB, translate if necessary
  Now perform load/store

## Slide 49: Virtual Memory Agenda
What is Virtual Memory?
How does Virtual memory Work?
  Address Translation
  Overhead
  Paging
  Performance
  Virtual Memory & Caches
    Caches use physical addresses
    Prevents sharing except when intended
    Works beautifully!

## Slide 50: Recall TLB in the Memory Hierarchy
CPU
TLB
Lookup
Cache
Mem
Disk
PageTable
Lookup
TLB is passing a physical address so we can load
from memory.
What if the data is in the cache?

## Slide 51: Virtually Addressed Caching
Q: Can we remove the TLB from the critical path?
A: Virtually-Addressed Caches
CPU
TLB
Lookup
Virtually
Addressed
Cache
Mem
Disk
PageTable
Lookup
Notes: A: have to flush entire cache on context switch
A:
Doing synonym updates requires significant hardware – essentially an associative lookup on the physical address tags to see if you have multiple hits

## Slide 52: Virtual vs. Physical Caches
CPU
Cache
SRAM
Memory
DRAM
addr
data
MMU
Cache
SRAM
MMU
CPU
Memory
DRAM
addr
data
Cache works on physical addresses
Cache works on virtual addresses
Q: What happens on context switch?
Q: What about virtual memory aliasing?
Q: So what’s wrong with physically addressed caches?
Notes: A1: Physically-addressed: nothing; Virtually-addressed: need to flush cache
A2: Physically-addressed: nothing; Virtually-addressed: problems

## Slide 53: Indexing vs. Tagging
Physically-Addressed Cache
  slow: requires TLB (and maybe PageTable) lookup first
Virtually-Indexed, Virtually Tagged Cache
  fast: start TLB lookup before cache lookup finishes
  PageTable changes (paging, context switch, etc.)
     need to purge stale cache lines (how?)
  Synonyms (two virtual mappings for one physical page)
     could end up in cache twice (very bad!)
Virtually-Indexed, Physically Tagged Cache
  ~fast: TLB lookup in parallel with cache lookup
  PageTable changes  no problem: phys. tag mismatch
  Synonyms  search and evict lines with same phys. tag
Virtually-Addressed Cache

## Slide 54: Typical Cache Setup
CPU
L2 Cache
SRAM
Memory
DRAM
addr
data
MMU
Typical L1: On-chip virtually addressed, physically tagged
Typical L2: On-chip physically addressed
Typical L3: On-chip …
L1 Cache
SRAM
TLB SRAM

## Slide 55: Design Decisions of Caches/TLBs/VM
Caches, Virtual Memory, & TLBs
Where can block be placed?
  Direct, n-way, fully associative
What block is replaced on miss?
  LRU, Random, LFU, …
How are writes handled?
  No-write (w/ or w/o automatic invalidation)
  Write-back (fast, block at time)
  Write-through (simple, reason about consistency)
Notes: Where?
Caches: direct/n-way/fa
VM: fa, but with a table of contents to eliminate searches
TLB: fa
Replacement?
varied
Writes?
Caches: usually write-back, or maybe write-through, or maybe no-write w/ invalidation
VM: write-back
TLB: usually no-write

## Slide 56: Summary of Caches/TLBs/VM
Caches, Virtual Memory, & TLBs
Where can block be placed?
  Caches: direct/n-way/fully associative (fa)
  VM: fa, but with a table of contents to eliminate searches
  TLB: fa
What block is replaced on miss?
  varied
How are writes handled?
  Caches: usually write-back, or maybe write-through, or maybe no-write w/ invalidation
  VM: write-back
  TLB: usually no-write
Notes: Where?
Caches: direct/n-way/fa
VM: fa, but with a table of contents to eliminate searches
TLB: fa
Replacement?
varied
Writes?
Caches: usually write-back, or maybe write-through, or maybe no-write w/ invalidation
VM: write-back
TLB: usually no-write

## Slide 57: Summary of Cache Design Parameters
 | L1 | Paged Memory | TLB
Size (blocks) | 1/4k to 4k | 16k to 1M | 64 to 4k
Size (kB) | 16 to 64 | 1M to 4G | 2 to 16
Block size (B) | 16-64 | 4k to 64k | 4-32
Miss rates | 2%-5% | 10-4 to 10-5% | 0.01% to 2%
Miss penalty | 10-25 | 10M-100M | 100-1000

## Slide 58: Translation in Action
yes
Next Topic:
Exceptional Control Flow
Virtual Address
TLB Access
TLB Hit?
no
Physical Address
$ Access
$
Hit?
yes
no
deliver Data back to CPU
DRAM
Access
TLB miss handler
(HW or OS)
DRAM
Hit?
yes

## Slide 59: Takeaways
Need a map to translate a “fake” virtual address (from process) to a “real” physical Address (in memory).
The map is a Page Table: ppn = PageTable[vpn]
A page is constant size block of virtual memory. Often ~4KB to reduce the number of entries in a PageTable.
Page Table can enforce Read/Write/Execute permissions on a per page basis. Can allocate memory on a per page basis. Also need a valid bit, and a few others.
Space overhead due to Page Table is significant.
Solution: another level of indirection!
Two-level of Page Table significantly reduces overhead.
Time overhead due to Address Translations also significant.
Solution: caching! Translation Lookaside Buffer (TLB) acts as a cache for the Page Table and significantly improves performance.