## Slide 1: Syscalls, exceptions, and interrupts, …oh my!
Hakim Weatherspoon
CS 3410
Computer Science
Cornell University
The slides are the product of many rounds of teaching CS 3410 by Deniz Altinbuken, Professors Weatherspoon, Bala, Bracy, and Sirer.

## Slide 2: Announcements
C practice assignment
  Due Monday, April 23rd
P4-Buffer Overflow is due tomorrow
  Due Wednesday, April 18th
P5-Cache Collusion!
  Due Friday, April 27th

## Slide 3: Outline for Today
How do we protect processes from one another?
  Skype should not crash Chrome.
How do we protect the operating system (OS) from other processes?
  Chrome should not crash the computer!
How does the CPU and OS (software) handle exceptional conditions?
  Division by 0, Page Fault, Syscall, etc.

## Slide 4: Outline for Today
How do we protect processes from one another?
  Skype should not crash Chrome.
How do we protect the operating system (OS) from other processes?
  Chrome should not crash the computer!
How does the CPU and OS (software) handle exceptional conditions?
  Division by 0, Page Fault, Syscall, etc.
Operating System
Privileged Mode
Traps, System calls, Exceptions, Interrupts

## Slide 5: Meltdown and Spectre Security Bug

## Slide 6
Operating System

## Slide 7: Operating System
Manages all of the software and hardware on the computer.
Many processes running at the same time, requiring resources
  CPU, Memory, Storage, etc.
The Operating System multiplexes these resources amongst different processes, and isolates and protects processes from one another!

## Slide 8: Operating System
Operating System (OS) is a trusted mediator:
  Safe control transfer between processes
  Isolation (memory, registers) of processes
P1
P2
P3
P4
VM
filesystem
net
driver
driver
untrusted
disk
netw
card
MMU
CPU
trusted
software
hardware
OS

## Slide 9: Outline for Today
How do we protect processes from one another?
  Skype should not crash Chrome.
How do we protect the operating system (OS) from other processes?
  Chrome should not crash the computer!
How does the CPU and OS (software) handle exceptional conditions?
  Division by 0, Page Fault, Syscall, etc.
Operating System
Privileged Mode
Traps, System calls, Exceptions, Interrupts

## Slide 10
Privileged (Kernel) Mode
Notes: How do you ENFORCE this trusted abstraction?

## Slide 11: One Brain, Many Personalities
You are what you execute.
Personalities:
hailstone_recursive
Microsoft Word
Minecraft
Linux  yes, this is just software like
every other program
that runs on the CPU
Are they all equal?
Brain

## Slide 12: Trusted vs. Untrusted
Only trusted processes should access & change important things
  Editing TLB, Page Tables, OS code, OS $sp, OS $fp…
If an untrusted process could change the OS’ $sp/$fp/$gp/etc., OS would crash!

## Slide 13: Privileged Mode
CPU Mode Bit in Process Status Register
Many bits about the current process
Mode bit is just one of them
Mode bit:
  0 = user mode = untrusted:
  “Privileged” instructions and registers are
  disabled by CPU
  1 = kernel mode = trusted
  All instructions and registers are enabled

## Slide 14: Privileged Mode at Startup
Boot sequence
  load first sector of disk (containing OS code) to predetermined address in memory
  Mode  1; PC  predetermined address
2. OS takes over
  initializes devices, MMU, timers, etc.
  loads programs from disk, sets up page tables, etc.
  Mode  0; PC  program entry point
    User programs regularly yield control back to OS

## Slide 15: Users need access to resources
If an untrusted process does not have privileges to use system resources, how can it
  Use the screen to print?
  Send message on the network?
  Allocate pages?
  Schedule processes?
Solution: System Calls

## Slide 16: System Call Examples
putc(): Print character to screen
  Need to multiplex screen between competing processes
send(): Send a packet on the network
  Need to manipulate the internals of a device
sbrk(): Allocate a page
  Needs to update page tables & MMU
sleep(): put current prog to sleep, wake other
  Need to update page table base register

## Slide 17: System Calls
System call: Not just a function call
  Don’t let process jump just anywhere in OS code
  OS can’t trust process’ registers (sp, fp, gp, etc.)
SYSCALL instruction: safe transfer of control to OS
MIPS system call convention:
  Exception handler saves temp regs, saves ra, …
  but: $v0 = system call number, which specifies the operation the application is requesting
Notes: Mode  0; Cause  syscall; PC  exception vector

## Slide 18
User Application
0xfffffffc
0x00000000
top
bottom
0x7ffffffc
0x80000000
0x10000000
0x00400000
system reserved
stack
system reserved
code (text)
static data
dynamic data (heap)
.data
.text
User Mode
Privileged (Kernel) Mode
System Call Interface
printf()
printf.c
Implementation
of printf() syscall!
SYSCALL!

## Slide 19: Libraries and Wrappers
Compilers do not emit SYSCALL instructions
  Compiler doesn’t know OS interface
Libraries implement standard API from system API
libc (standard C library):
  getc()  syscall
  sbrk()  syscall
  write()  syscall
  gets()  getc()
  printf()  write()
  malloc()  sbrk()
  …

## Slide 20: Invoking System Calls
char *gets(char *buf) {
while (...) {
buf[i] = getc();
}
}
int getc() {
asm("addiu $v0, $0, 4");
asm("syscall");
}
4 is number for getc syscall
Notes: Inline assembly
4 is getc syscall name!

## Slide 21: Anatomy of a Process, v1
system reserved
(stack grows down)
(heap grows up)
text
reserved
(static) data
(.stack)
.data
.text
0xfffffffc
0x00000000
0x7ffffffc
0x80000000
0x10000000
0x00400000
system reserved
stack
system reserved
code
(text)
static data
dynamic data (heap)
(user) gets
(library) getc
??

## Slide 22: Where does the OS live?
In its own address space?
  Syscall has to switch to a different address space
  Hard to support syscall arguments passed as pointers
  . . . So, NOPE
In the same address space as the user process?
  Protection bits prevent user code from writing kernel
  Higher part of virtual memory
  Lower part of physical memory
  . . . Yes, this is how we do it.

## Slide 23: Anatomy of a Process
system reserved
(stack grows down)
(heap grows up)
text
reserved
(static) data
(.stack)
.data
.text
0xfffffffc
0x00000000
top
bottom
0x7ffffffc
0x80000000
0x10000000
0x00400000
system reserved
stack
system reserved
code (text)
static data
dynamic data (heap)
.data
.text

## Slide 24: Full System Layout
All kernel text & most data:
At same virtual address in every address space
OS is omnipresent, available to help user-level applications
  Typically in high memory
Virtual Memory
0xfffffffc
0x00000000
0x7ffffffc
0x80000000
0x10000000
0x00400000
stack
system reserved
code (text)
static data
dynamic data (heap)
OS Heap
OS Data
OS Stack
OS Text
Notes: When an application needs to perform a privileged operation, it needs to invoke the OS

## Slide 25: Full System Layout
Virtual Memory
OS Text
OS Data
OS Heap
OS Stack
Physical Memory
0xfffffffc
0x00000000
0x7ffffffc
0x80000000
0x10000000
0x00400000
stack
system reserved
code (text)
static data
dynamic data (heap)
OS Heap
OS Data
OS Stack
OS Text
0x00...00

## Slide 26: Anatomy of a Process, v2
system reserved
(stack grows down)
(heap grows up)
text
reserved
(static) data
(.stack)
.data
.text
0xfffffffc
0x00000000
0x7ffffffc
0x80000000
0x10000000
0x00400000
system reserved
stack
system reserved
code (text)
static data
dynamic data (heap)
gets
getc
implementation of getc() syscall

## Slide 27: Clicker Question
Which statement is FALSE?
OS manages the CPU, Memory, Devices, and Storage.
OS provides a consistent API to be used by other processes.
The OS kernel is always present on Disk.
The OS kernel is always present in Memory.
Any process can fetch and execute OS code in user mode.

## Slide 28: Clicker Question
Which statement is FALSE?
OS manages the CPU, Memory, Devices, and Storage.
OS provides a consistent API to be used by other processes.
The OS kernel is always present on Disk.
The OS kernel is always present in Memory.
Any process can fetch and execute OS code in user mode.

## Slide 29: Inside the SYSCALL instruction
SYSCALL instruction does an atomic jump to a controlled location (i.e. MIPS 0x8000 0180)
  Switches the sp to the kernel stack
  Saves the old (user) SP value
  Saves the old (user) PC value (= return address)
  Saves the old privilege mode
  Sets the new privilege mode to 1
  Sets the new PC to the kernel syscall handler

## Slide 30: Inside the SYSCALL implementation
Kernel system call handler carries out the desired system call
  Saves callee-save registers
  Examines the syscall number
  Checks arguments for sanity
  Performs operation
  Stores result in v0
  Restores callee-save registers
  Performs a “return from syscall” (ERET) instruction, which restores the privilege mode, SP and PC

## Slide 31: Takeaway
It is necessary to have a privileged (kernel) mode to enable the Operating System (OS):
  provides isolation between processes
  protects shared resources
  provides safe control transfer

## Slide 32: Outline for Today
How do we protect processes from one another?
  Skype should not crash Chrome.
How do we protect the operating system (OS) from other processes?
  Chrome should not crash the computer!
How does the CPU and OS (software) handle exceptional conditions?
  Division by 0, Page Fault, Syscall, etc.
Operating System
Privileged Mode
Traps, System calls, Exceptions, Interrupts

## Slide 33: Exceptional Control Flow
Anything that isn’t a user program executing its own user-level instructions.
System Calls:
just one type of exceptional control flow
Process requesting a service from the OS
Intentional – it’s in the executable!

## Slide 34: Software Exceptions
Trap
Intentional
  Examples:
  System call
  (OS performs service)
Breakpoint traps
Privileged instructions
Abort
Unintentional
Not recoverable
  Examples:
Parity error
Fault
Unintentional but
Possibly recoverable
  Examples:
Division by zero
Page fault
One of many ontology / terminology trees.

## Slide 35: Terminology
Trap: Any kind of a control transfer to the OS
Syscall: Synchronous and planned, process-to-kernel transfer
  SYSCALL instruction in MIPS (various on x86)
Exception: Synchronous but unplanned, process-to-kernel transfer
  exceptional events: div by zero, page fault, page protection err, …
Interrupt: Asynchronous, device-initiated transfer
  e.g. Network packet arrived, keyboard event, timer ticks

## Slide 36: Hardware support for exceptions
Exception program counter (EPC)
  32-bit register, holds addr of affected instruction
  Syscall case: Address of SYSCALL
Cause register
  Register to hold the cause of the exception
  Syscall case: 8, Sys
Special instructions to load TLB
  Only do-able by kernel
Notes: Precise and imprecise exceptions
  In pipelined architecture
    Have to correctly identify PC of exception
    MIPS and modern processors support this

## Slide 37: Hardware support for exceptions
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4
forward unit
detect hazard
Stack, Data, Code
Stored in Memory
$0 (zero)
$1 ($at)
$29 ($sp)
$31 ($ra)
Code Stored in Memory
(also, data and stack)
EPC
Cause
Notes: Precise and imprecise exceptions
  In pipelined architecture
    Have to correctly identify PC of exception
    MIPS and modern processors support this

## Slide 38: Hardware support for exceptions
Precise exceptions: Hardware guarantees
  (similar to a branch)
  Previous instructions complete
  Later instructions are flushed
  EPC and cause register are set
  Jump to prearranged address in OS
  When you come back, restart instruction
  Disable exceptions while responding to one
    Otherwise can overwrite EPC and cause
Notes: Precise and imprecise exceptions
  In pipelined architecture
    Have to correctly identify PC of exception
    MIPS and modern processors support this

## Slide 39: Exceptional Control Flow
Hardware interrupts
Asynchronous
= caused by events external to CPU
Software exceptions
Synchronous
= caused by CPU executing an instruction
Maskable
Can be turned off by CPU
Example: alert from network device that a packet just arrived, clock notifying CPU of clock tick
Unmaskable
Cannot be ignored
Example: alert from the power supply that electricity is about to go out
AKA Exceptions

## Slide 40: Interrupts & Unanticipated Exceptions
No SYSCALL instruction. Hardware steps in:
  Saves PC of exception instruction (EPC)
  Saves cause of the interrupt/privilege (Cause register)
  Switches the sp to the kernel stack
  Saves the old (user) SP value
  Saves the old (user) PC value
  Saves the old privilege mode
  Sets the new privilege mode to 1
  Sets the new PC to the kernel syscall hander interrupt/exception handler
SYSCALL

## Slide 41: Inside Interrupts & Unanticipated Exceptions
Kernel system call handler carries out system call
  all
  Saves callee-save registers
  Examines the syscall number cause
  Checks arguments for sanity
  Performs operation
  Stores result in v0
  Restores callee-save registers
  Performs a ERET instruction (restores the privilege mode, SP and PC)
interrupt/exception handler handles event
all

## Slide 42: Clicker Question
What else requires both Hardware and Software?
A) Virtual to Physical Address Translation
B) Branching and Jumping
C) Clearing the contents of a register
D) Pipelining instructions in the CPU
E) What are we even talking about?

## Slide 43: Clicker Question
What else requires both Hardware and Software?
A) Virtual to Physical Address Translation
B) Branching and Jumping
C) Clearing the contents of a register
D) Pipelining instructions in the CPU
E) What are we even talking about?

## Slide 44: Address Translation: HW/SW Division of Labor
Virtual  physical address translation!
Hardware
has a concept of operating in physical or virtual mode
helps manage the TLB
raises page faults
keeps Page Table Base Register (PTBR) and ProcessID
Software/OS
manages Page Table storage
handles Page Faults
updates Dirty and Reference bits in the Page Tables
keeps TLB valid on context switch:
  Flush TLB when new process runs (x86)
  Store process id (MIPS)

## Slide 45: Demand Paging on MIPS
TLB miss
Trap to kernel
Walk Page Table
Find page is invalid
Convert virtual address to file + offset
Allocate page frame
  Evict page if needed
Initiate disk block read into page frame
Disk interrupt when DMA complete
Mark page as valid
Load TLB entry
Resume process at faulting instruction
Execute instruction

## Slide 46: November 1988: Internet Worm
Internet Worm attacks thousands of Internet hosts
Best Wikipedia quotes:
  “According to its creator, the Morris worm was not written to cause damage, but to gauge the size of the Internet. The worm was released from MIT to disguise the fact that the worm originally came from Cornell.”
  “The worm …determined whether to invade a new computer by asking whether there was already a copy running. But just doing this would have made it trivially easy to kill: everyone could run a process that would always answer "yes”. To compensate for this possibility, Morris directed the worm to copy itself even if the response is "yes" 1 out of 7 times. This level of replication proved excessive, and the worm spread rapidly, infecting some computers multiple times. Morris remarked, when he heard of the mistake, that he "should have tried it on a simulator first”.”
Computer Virus TV News Report 1988

## Slide 47: Clicker Question
Which of the following is not a viable solution to protect against a buffer overflow attack?
(There are multiple answers, just pick one of them.)
Prohibit the execution of anything stored on the Stack.
Randomize the starting location of the Stack.
Use only library code that requires a buffer length to make sure it doesn’t overflow.
Write only to buffers on the OS Stack where they will be protected.
Compile the executable with the highest level of optimization flags.
Notes: A B and C

## Slide 48: Summary
Trap
  Any kind of a control transfer to the OS
Syscall
  Synchronous, process-initiated control transfer from user to the OS to obtain service from the OS
  e.g. SYSCALL
Exception
  Synchronous, process-initiated control transfer from user to the OS in response to an exceptional event
  e.g. Divide by zero, TLB miss, Page fault
Interrupt
  Asynchronous, device-initiated control transfer from user to the OS
  e.g. Network packet, I/O complete

## Slide 49: Example: Clock Interrupt
Example: Clock Interrupt*
  Every N cycles, CPU causes exception with Cause = CLOCK_TICK
  OS can select N to get e.g. 1000 TICKs per second
.ktext 0x8000 0180
# (step 1) save *everything* but $k0, $k1 to 0xB0000000
# (step 2) set up a usable OS context
# (step 3) examine Cause register, take action
if (Cause == PAGE_FAULT) handle_pfault(BadVaddr)
else if (Cause == SYSCALL) dispatch_syscall($v0)
else if (Cause == CLOCK_TICK) schedule()
# (step 4) restore registers and return to where process left off
* not the CPU clock, but a programmable timer clock

## Slide 50: Scheduler
struct regs context[];
int ptbr[];
schedule() {
i = current_process;
j = pick_some_process();
if (i != j) {
current_process = j;
memcpy(context[i], 0xB0000000);
memcpy(0xB0000000, context[j]);
asm(“mtc0 Context, ptbr[j]”);
}
}