## Slide 1: Storage
CS 3410
Computer System Organization & Programming
These slides are the product of many rounds of teaching CS 3410 by Deniz Altinbuke, Kevin Walsh, and Professors Weatherspoon, Bala, Bracy, and Sirer.

## Slide 2
Challenge
How do we store lots of data for a long time
  Disk (Hard disk, floppy disk, …)
  Tape (cassettes, backup, VHS, …)
  CDs/DVDs

## Slide 3
Challenge
How do we store lots of data for a long time
  Disk (Hard disk, floppy disk, …Solid State Disk (SSD)
  Tape (cassettes, backup, VHS, …)
  CDs/DVDs
  Non-Volitile Persistent Memory (NVM; e.g. 3D Xpoint)

## Slide 4
I/O System Characteristics
Dependability is important
  Particularly for storage devices
Performance measures
  Latency (response time)
  Throughput (bandwidth)
  Desktops & embedded systems
    Mainly interested in response time & diversity of devices
  Servers
    Mainly interested in throughput & expandability of devices

## Slide 5
Memory Hierarchy
Tape
Disk
DRAM
L2
registers/L1
100s, sequential access
2 ns, random access
5 ns, random access
20-80 ns, random access
2-8 ms, random access
1 TB
16 KB
512 KB
2 GB
300 GB
2006

## Slide 6
Memory Hierarchy
SSD
Disk
DRAM
L2
registers/L1
100ns-10us, random access
Millions of IOPS (I/O per sec)
2 ns, random access
5 ns, random access
20-80 ns, random access
2-8 ms, random access
30 TB
128 KB
4 MB
256 GB
6 TB

## Slide 7
Memory Hierarchy
SSD
Disk
DRAM
L2
registers/L1
100ns-10us, random access
Millions of IOPS (I/O per sec)
2 ns, random access
5 ns, random access
20-80 ns, random access
2-8 ms, random access
30 TB
128 KB
4 MB
256 GB
6 TB
Non-volatile memory
20 -100 ns, random access
1 TB
Notes: 30TB 2.5in Samsung Flash Drive https://arstechnica.com/gadgets/2018/02/samsung-crams-30tb-of-ssd-into-a-single-2-5-inch-drive/
60TB 3.5in Seagate Flash Drive https://arstechnica.com/gadgets/2016/08/seagate-unveils-60tb-ssd-the-worlds-largest-hard-drive/

## Slide 8
Memory Hierarchy
SSD
100ns-10us, random access
Millions of IOPS (I/O per sec)
30 TB
Server
10s of Disks
256 TB
Rack of Servers
10s of Servers
10 PB
Data Center
10-100s of Servers
1 EB
Cloud
10-100s of
Data Centers
0.1 YB
245B
248B
253B
260B
267B

## Slide 9: The Rise of Cloud Computing
How big is Big Data in the Cloud?
  Exabytes: Delivery of petabytes of storage daily
Titan tech boom, randy katz, 2008
Notes: Big Data: Volume (Exabytes), Velocity (Petabytes/day), variety (worlds data)
1KB: webpage (and amount of L1 [level-1] cache)
1MB: music file (and amount of L3 [level-3] cache)
1GB: movie file (and amount of memory in a computer)
1TB: genome file (and 1 hard disk drive)
1PB: 1000x genome file or million moves
1EB: million genome files, billion movies, trillion music files, quadrillion webpages

## Slide 10: The Rise of Cloud Computing
How big is Big Data in the Cloud?
  Most of the worlds data (and computation) hosted by few companies

## Slide 11: The Rise of Cloud Computing
How big is Big Data in the Cloud?
  Most of the worlds data (and computation) hosted by few companies

## Slide 12: The Rise of Cloud Computing
The promise of the Cloud
  ubiquitous, convenient, on-demand network access to a shared pool of configurable computing resources (e.g., networks, servers, storage, applications, and services) that can be rapidly provisioned and released with minimal management effort or service provider interaction.
NIST Cloud Definition
Notes: The cloud completes the commoditization process and makes storage and computation a commodity.
Public vs private
IaaS, PaaS, SaaS
On demand (self service), network access, resource pooling, rapid elasticity, measured service

## Slide 13: The Rise of Cloud Computing
The promise of the Cloud
  ubiquitous, convenient, on-demand network access to a shared pool of configurable computing resources (e.g., networks, servers, storage, applications, and services) that can be rapidly provisioned and released with minimal management effort or service provider interaction.
NIST Cloud Definition
Notes: The cloud completes the commoditization process and makes storage and computation a commodity.
Public vs private
IaaS, PaaS, SaaS
On demand (self service), network access, resource pooling, rapid elasticity, measured service

## Slide 14
Tapes
Same basic principle for 8-tracks, cassettes, VHS, ...
  Ferric Oxide Powder: ferromagnetic material
  During recording, the audio signal is sent through the coil of wire to create a magnetic field in the core.
  During playback, the motion of the tape creates a varying magnetic field in the core and therefore a signal in the coil.
0 0 1 0 1 0 1 0 1

## Slide 15
Disks & CDs
Disks use same magnetic medium as tapes
  concentric rings (not a spiral)
CDs & DVDs use optics and a single spiral track

## Slide 16
Disk Physics
Typical parameters :
1 spindle
1 arm assembly
1-4 platters
1-2 sides/platter
1 head per side
(but only 1 active head at a time)
700-20480 tracks/surface
16-1600 sectors/track

## Slide 17
Disk Accesses
Accessing a disk requires:
  specify sector: C (cylinder), H (head), and S (sector)
  specify size: number of sectors to read or write
  specify memory address
Performance:
  seek time: move the arm assembly to track
  Rotational delay: wait for sector to come around
  transfer time: get the bits off the disk
  Controller time: time for setup
Track
Sector
Seek Time
Rotation
Delay

## Slide 18
Example
Average time to read/write 512-byte sector
  Disk rotation at 10,000 RPM
  Seek time: 6ms
  Transfer rate: 50 MB/sec
  Controller overhead: 0.2 ms
Average time:
  Seek time + rotational delay + transfer time + controller overhead
  6ms + 0.5 rotation/(10,000 RPM) + 0.5KB/(50 MB/sec) + 0.2ms
  6.0 + 3.0 + 0.01 + 0.2 = 9.2ms

## Slide 19
Disk Access Example
If actual average seek time is 2ms
  Average read time = 5.2ms

## Slide 20
Disk Scheduling
Goal: minimize seek time
    secondary goal: minimize rotational latency
FCFS (First come first served)
Shortest seek time
SCAN/Elevator
  First service all requests in one direction
  Then reverse and serve in opposite direction
Circular SCAN
  Go off the edge and come to the beginning and start all over again

## Slide 21: FCFS

## Slide 22: SSTF

## Slide 23: SCAN

## Slide 24: C-SCAN

## Slide 25
Disk Geometry: LBA
New machines use logical block addressing instead of CHS
  machine presents illusion of an array of blocks, numbered 0 to N
Modern disks…
  have varying number of sectors per track
    roughly constant data density over disk
    varying throughput over disk
  remap and reorder blocks (to avoid defects)
  completely obscure their actual physical geometry
  have built-in caches to hide latencies when possible (but being careful of persistence requirements)
  have internal software running on an embedded CPU

## Slide 26
Flash Storage
Nonvolatile semiconductor storage
  100× – 1000× faster than disk
  Smaller, lower power
  But more $/GB (between disk and DRAM)
  But, price is dropping and performance is increasing faster than disk

## Slide 27
Flash Types
NOR flash: bit cell like a NOR gate
  Random read/write access
  Used for instruction memory in embedded systems
NAND flash: bit cell like a NAND gate
  Denser (bits/area), but block-at-a-time access
  Cheaper per GB
  Used for USB keys, media storage, …
Flash bits wears out after 1000’s of accesses
  Not suitable for direct RAM or disk replacement
Flash has unusual interface
  can only “reset” bits in large blocks

## Slide 28
I/O vs. CPU Performance
Amdahl’s Law
  Don’t neglect I/O performance as parallelism increases compute performance
Example
  Benchmark takes 90s CPU time, 10s I/O time
  Double the number of CPUs/2 years
    I/O unchanged
Year | CPU time | I/O time | Elapsed time | % I/O time
now | 90s | 10s | 100s | 10%
+2 | 45s | 10s | 55s | 18%
+4 | 23s | 10s | 33s | 31%
+6 | 11s | 10s | 21s | 47%

## Slide 29
RAID
Redundant Arrays of Inexpensive Disks
Big idea:
  Parallelism to gain performance
  Redundancy to gain reliability

## Slide 30: Raid 0
Striping
  Non-redundant disk array!

## Slide 31: Raid 1
Mirrored Disks!
  More expensive
  On failure use the extra copy

## Slide 32: Raid 2-3-4-5-6
Bit Level Striping and Parity Checks!
  As level increases:
    More guarantee against failure, more reliability
    Better read/write performance
Raid 2
Raid 3
Raid 4
Raid 5

## Slide 33
Summary
Disks provide nonvolatile memory
I/O performance measures
  Throughput, response time
  Dependability and cost very important
RAID
  Redundancy for fault tolerance and speed