## Slide 1: Gates and Logic: From Transistors to Logic Gates and Logic Circuits
[Weatherspoon, Bala, Bracy, and Sirer]
Prof. Hakim Weatherspoon
CS 3410
Computer Science
Cornell University

## Slide 2: Goals for Today
From Switches to Logic Gates to Logic Circuits
Understanding the foundations of
  Computer Systems Organization and Programming
Notes: How does my laptop work? How does my phone work? What is the underlying principles and design for these electronics?

## Slide 3: Goals for Today
From Switches to Logic Gates to Logic Circuits
Understanding the foundations of
  Computer Systems Organization and Programming
  e.g. Galaxy Note 9
Notes: How does my laptop work? How does my phone work? What is the underlying principles and design for these electronics?
Galaxy Note 9 https://www.samsung.com/semiconductor/minisite/exynos/products/mobileprocessor/exynos-9-series-9810/
https://en.wikipedia.org/wiki/Samsung_Galaxy_Note_9

## Slide 4: Goals for Today
From Switches to Logic Gates to Logic Circuits
Understanding the foundations of
  Computer Systems Organization and Programming
  e.g. Galaxy Note 9
  with the big.LITTLE DynamicIQ 8-core ARM processor
Notes: How does my laptop work? How does my phone work? What is the underlying principles and design for these electronics?
Galaxy Note 9 https://www.samsung.com/semiconductor/minisite/exynos/products/mobileprocessor/exynos-9-series-9810/
https://en.wikipedia.org/wiki/Samsung_Galaxy_Note_9
4x Exynos M3 @ 2.9 GHz: https://en.wikichip.org/wiki/samsung/microarchitectures/m3
4x Cortex A55 @ 1.9 GHz: https://en.wikipedia.org/wiki/ARM_Cortex-A55
https://en.wikichip.org/wiki/arm_holdings/microarchitectures/cortex-a55

## Slide 5: Goals for Today
From Switches to Logic Gates to Logic Circuits
Understanding the foundations of
  Computer Systems Organization and Programming
  e.g. Galaxy Note 9
  with the big.LITTLE DynamicIQ 8-core ARM processor
 | big Quad Core | LITTLE Quad Core
Architecture | ARM v8 | ARM v8
Process | Samsung 10nm | Samsung 10nm
Frequency | 2.9GHz+ | 1.9GHz
Area | 3.5mm2 | 
Power-ratio | 1 | 0.17
L1 Cache Size | 64 KB I/D Cache | 64 KB I/D Cache
L2 Cache Size | 2 MB Data Cache | 512 KB Data Cache
Notes: How does my laptop work? How does my phone work? What is the underlying principles and design for these electronics?
Galaxy Note 9 https://www.samsung.com/semiconductor/minisite/exynos/products/mobileprocessor/exynos-9-series-9810/
https://en.wikipedia.org/wiki/Samsung_Galaxy_Note_9
4x Exynos M3 @ 2.9 GHz: https://en.wikichip.org/wiki/samsung/microarchitectures/m3
4x Cortex A55 @ 1.9 GHz: https://en.wikipedia.org/wiki/ARM_Cortex-A55
https://en.wikichip.org/wiki/arm_holdings/microarchitectures/cortex-a55

## Slide 6: Goals for Today
From Switches to Logic Gates to Logic Circuits
Logic Gates
  From switches
  Truth Tables
Logic Circuits
  From Truth Tables to Circuits (Sum of Products)
  Identity Laws
Logic Circuit Minimization
  Algebraic Manipulations
  Truth Tables (Karnaugh Maps)
Transistors (electronic switch)

## Slide 7: A switch
Acts as a conductor or insulator.
Can be used to build amazing things…
The Bombe used to break the German
Enigma machine during World War II
Notes: Pictures show the Bombe built by Alan Turing to break the enigma machine ciphers.
They were Fixed-Program Computers came before stored-program computers (general purpose)
The former required re-wiring (e.g. ENIAC took 3 weeks to “re-wire”).

## Slide 8: Basic Building Blocks: Switches to Logic Gates
A | B | Light
OFF | OFF | 
A | B | Light
OFF | OFF | 
OFF | ON | 
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
ON | ON | 
A | B | Light
+
-
A
B
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
ON | ON | 
Truth Table
Notes: Speed and size of a mechanical switch
Truth Table: defines the output for all possible combinations of values for input

## Slide 9: Basic Building Blocks: Switches to Logic Gates
A | B | Light
OFF | OFF | 
A | B | Light
OFF | OFF | 
OFF | ON | 
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
ON | ON | 
A | B | Light
OFF | OFF | 
A | B | Light
OFF | OFF | 
OFF | ON | 
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
ON | ON | 
A | B | Light
A | B | Light
+
-
-
A
B
A
B
A | B | Light
OFF | OFF | OFF
OFF | ON | ON
ON | OFF | ON
ON | ON | ON
Truth Table
+
Notes: Speed and size of a mechanical switch
Truth Table: defines the output for all possible combinations of values for input

## Slide 10: Basic Building Blocks: Switches to Logic Gates
Either (OR)
Both (AND)
A | B | Light
OFF | OFF | 
A | B | Light
OFF | OFF | 
OFF | ON | 
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
A | B | Light
OFF | OFF | 
A | B | Light
OFF | OFF | 
OFF | ON | 
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
ON | ON | 
A | B | Light
+
-
-
A
B
A
B
A | B | Light
OFF | OFF | OFF
OFF | ON | ON
ON | OFF | ON
ON | ON | ON
Truth Table
+
A | B | Light
OFF | OFF | OFF
OFF | ON | OFF
ON | OFF | OFF
ON | ON | ON
Notes: Speed and size of a mechanical switch
Truth Table: defines the output for all possible combinations of values for input

## Slide 11: Basic Building Blocks: Switches to Logic Gates
Either (OR)
Both (AND)
A | B | Light
OFF | OFF | 
A | B | Light
OFF | OFF | 
OFF | ON | 
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
A | B | Light
OFF | OFF | 
A | B | Light
OFF | OFF | 
OFF | ON | 
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
ON | ON | 
A | B | Light
-
-
A | B | Light
OFF | OFF | OFF
OFF | ON | ON
ON | OFF | ON
ON | ON | ON
Truth Table
A | B | Light
OFF | OFF | OFF
OFF | ON | OFF
ON | OFF | OFF
ON | ON | ON
A
B
A
B
OR
AND
Notes: Speed and size of a mechanical switch
Truth Table: defines the output for all possible combinations of values for input

## Slide 12: Basic Building Blocks: Switches to Logic Gates
Either (OR)
Both (AND)
A | B | Light
OFF | OFF | 
A | B | Light
OFF | OFF | 
OFF | ON | 
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
ON | ON | 
-
-
Truth Table
A
B
A
B
OR
AND
A | B | Light
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
0 = OFF
1 = ON
A | B | Light
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Notes: Speed and size of a mechanical switch
Truth Table: defines the output for all possible combinations of values for input

## Slide 13: Basic Building Blocks: Switches to Logic Gates
A
B
A
B
OR
AND
Did you know?
George Boole: Inventor of the idea of logic gates. He was born in Lincoln, England and he was the son of a shoemaker in a low class family.
George Boole (1815-1864)
Notes: E.g. logic statements:
“Jane will only go to the cinema tonight if a good film is on AND she has enough money.”
“Stuart will only go to the birthday party on Sunday if Katie OR Sujit is going too.”

## Slide 14: Takeaway
Binary (two symbols: true and false) is the basis of Logic Design

## Slide 15
Building Functions: Logic Gates
NOT:
AND:
OR:
Logic Gates
  digital circuit that either allows a signal to pass through it or not.
  Used to build logic functions
  There are seven basic logic gates:
  AND, OR, NOT,
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | Out
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | Out
A
B
A
B
A
Notes: Create truth table of AND or OR: state what they do
Did you know? Logic gates allow the computer to do things such as add, divide, multiply, do simple yes and no reasoning in certain situations along with other things.

## Slide 16
Building Functions: Logic Gates
NOT:
AND:
OR:
Logic Gates
  digital circuit that either allows a signal to pass through it or not.
  Used to build logic functions
  There are seven basic logic gates:
  AND, OR, NOT,
  NAND (not AND), NOR (not OR), XOR, and XNOR (not XOR) [later]
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | Out
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | Out
0 | 1
1 | 0
A
B
A
B
A
Notes: Create truth table of AND or OR: state what they do
Did you know? Logic gates allow the computer to do things such as add, divide, multiply, do simple yes and no reasoning in certain situations along with other things.

## Slide 17
Building Functions: Logic Gates
NOT:
AND:
OR:
Logic Gates
  digital circuit that either allows a signal to pass through it or not.
  Used to build logic functions
  There are seven basic logic gates:
  AND, OR, NOT,
  NAND (not AND), NOR (not OR), XOR, and XNOR (not XOR) [later]
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | Out
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | Out
0 | 1
1 | 0
A
B
A
B
A
A | B | Out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
A | B | Out
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
A
B
NAND:
NOR:
Notes: Create truth table of AND or OR: state what they do
Did you know? Logic gates allow the computer to do things such as add, divide, multiply, do simple yes and no reasoning in certain situations along with other things.

## Slide 18
a | b | Out
a
b
Out
iClicker Question
NOT
OR
XOR
AND
NAND
Function:
Symbol:
Truth Table:
Which Gate is this?
Notes: Fill out table
Put, NOT, AND, OR labels in box

## Slide 19
a
b
Out
iClicker Question
NOT
OR
XOR
AND
NAND
Which Gate is this?
a | b | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
XOR: out = 1 if a or b is 1, but not both;
out = 0 otherwise.
out = 1, only if a = 1 AND b = 0
OR a = 0 AND b = 1

## Slide 20
iClicker Question
NOT
OR
XOR
AND
NAND
Which Gate is this?
a | b | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
XOR: out = 1 if a or b is 1, but not both;
out = 0 otherwise.
out = 1, only if a = 1 AND b = 0
OR a = 0 AND b = 1
a
b
Out

## Slide 21
Activity#2: Logic Gates
Fill in the truth table, given the following Logic Circuit made from Logic AND, OR, and NOT gates.
What does the logic circuit do?
a
b
d
Out
a | b | d | Out
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
Notes: Fill out table
Ask rows in audience to fill in different rows of tabel

## Slide 22
Activity#2: Logic Gates
Multiplexor: select (d) between two inputs (a and b) and set one as the output (out)?
out = a, if d = 0
out = b, if d = 1
a
b
d
Out
a | b | d | Out
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Notes: Fill out table
Ask rows in audience to fill in different rows of tabel

## Slide 23: Goals for Today
From Switches to Logic Gates to Logic Circuits
Logic Gates
  From switches
  Truth Tables
Logic Circuits
  From Truth Tables to Circuits (Sum of Products)
  Identity Laws
Logic Circuit Minimization
  Algebraic Manipulations
  Truth Tables (Karnaugh Maps)
Transistors (electronic switch)

## Slide 24: Next Goal
Given a Logic function, create a Logic Circuit that implements the Logic Function…
…and, with the minimum number of logic gates
Fewer gates: A cheaper ($$$) circuit!
Notes: Can get logic circuit from truth table
Minimize logic circuit through algebraic reductions or Karnaugh Maps

## Slide 25
NOT:
AND:
OR:
XOR:
Logic Gates
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | Out
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | Out
0 | 1
1 | 0
A
B
A
B
A
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
Notes: XOR is not a basic Logic Gate since it can be created from AND and OR gates, but it is often used as a basic Logic Operator

## Slide 26
NOT:
AND:
OR:
XOR:
Logic Gates
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | Out
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | Out
0 | 1
1 | 0
A
B
A
B
A
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
A | B | Out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
A | B | Out
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
A
B
NAND:
NOR:
A | B | Out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A
B
XNOR:
Notes: XOR is not a basic Logic Gate since it can be created from AND and OR gates, but it is often used as a basic Logic Operator

## Slide 27
Logic Implementation
How to implement a desired logic function?
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Notes: Draw circuit and go through out=true cases
Have not done cheaply yet

## Slide 28
Logic Implementation
How to implement a desired logic function?
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Write minterms
sum of products:
OR of all minterms where out=1
minterm
a b c
a b c
a b c
a b c
a b c
a b c
a b c
a b c
Notes: Show what out equals

## Slide 29
Logic Implementation
How to implement a desired logic function?
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Write minterms
sum of products:
OR of all minterms where out=1
  E.g. out = c + bc + ac
minterm
a b c
a b c
a b c
a b c
a b c
a b c
a b c
a b c
corollary: any combinational circuit can be implemented in two levels of logic (ignoring inverters)
c
out
b
a
Notes: Show what out equals

## Slide 30
Logic Equations
NOT:
  out = ā = !a = a
AND:
  out = a ∙ b = a & b = a  b
OR:
  out = a + b = a | b = a  b
XOR:
  out = a  b = a + āb
Logic Equations
  Constants: true = 1, false = 0
  Variables: a, b, out, …
  Operators (above): AND, OR, NOT, etc.
Notes: Apologize that there are three ways to represent the same logic equation
XOR is not a basic Logic Gate since it can be created from AND and OR gates, but it is often used as a basic Logic Operator
AND is “product”
OR is “sum”
Read outloud

## Slide 31
Logic Equations
NOT:
  out = ā = !a = a
AND:
  out = a ∙ b = a & b = a  b
OR:
  out = a + b = a | b = a  b
XOR:
  out = a  b = a + āb
Logic Equations
  Constants: true = 1, false = 0
  Variables: a, b, out, …
  Operators (above): AND, OR, NOT, etc.
NAND:
  out = = !(a & b) =  (a  b)
NOR:
  out = = !(a | b) =  (a  b)
XNOR:
  out = = ab +
  .
Notes: Apologize that there are three ways to represent the same logic equation
XOR is not a basic Logic Gate since it can be created from AND and OR gates, but it is often used as a basic Logic Operator
AND is “product”
OR is “sum”
Read outloud

## Slide 32
Identities
Identities useful for manipulating logic equations
  For optimization & ease of implementation
  a + 0 =
  a + 1 =
  a + ā =
  a ∙ 0 =
  a ∙ 1 =
  a ∙ ā =
Notes: Minimization activity
Maybe use picture to go through
Complement a+ā=1 and aā=0

## Slide 33
Identities
Identities useful for manipulating logic equations
  For optimization & ease of implementation
  a + 0 =
  a + 1 =
  a + ā =
  a ∙ 0 =
  a ∙ 1 =
  a ∙ ā =
  a
  1
  1
  0
  a
  0
a
b
a
b
Notes: Minimization activity
Maybe use picture to go through
Complement a+ā=1 and aā=0

## Slide 34
Identities useful for manipulating logic equations
  For optimization & ease of implementation
  =
  =
  a + a b =
  a(b+c) =
  =
Identities
Notes: Minimization activity
Maybe use picture to go through
  De Morgan’s Law: = ∙ and = +
Minimization activity
Maybe use picture to go through
  De Morgan’s Law: ((a+b)) ̅ = a ̅ ∙ b ̅ and ((a ∙b)) ̅ = a ̅ + b ̅

## Slide 35
Identities useful for manipulating logic equations
  For optimization & ease of implementation
  =
  =
  a + a b =
  a(b+c) =
  =
Identities
  ∙
  +
  a
  ab + ac
  + ∙
A
B
A
B
↔
A
B
A
B
↔
Notes: Minimization activity
Maybe use picture to go through
  De Morgan’s Law: = ∙ and = +
Minimization activity
Maybe use picture to go through
  De Morgan’s Law: ((a+b)) ̅ = a ̅ ∙ b ̅ and ((a ∙b)) ̅ = a ̅ + b ̅

## Slide 36: Goals for Today
From Switches to Logic Gates to Logic Circuits
Logic Gates
  From switches
  Truth Tables
Logic Circuits
  From Truth Tables to Circuits (Sum of Products)
  Identity Laws
Logic Circuit Minimization – why?
  Algebraic Manipulations
  Truth Tables (Karnaugh Maps)
Transistors (electronic switch)

## Slide 37
(a+b)a + (a+b)c
= aa + ba + ac + bc
= a + a(b+c) + bc
= a + bc
Minimize this logic equation:
(a+b)(a+c) =
a + 0 = a
a + 1 = 1
a + ā = 1
a · 0 = 0
a · 1 = a
a · ā = 0
a + a b = a
a (b+c) = ab + ac
Minimization Example
Notes: Minimization activity

## Slide 38
a + 0 = a
a + 1 = 1
a + ā = 1
a · 0 = 0
a · 1 = a
a · ā = 0
a + a b = a
a (b+c) = ab + ac
(a+b)(a+c)  a + bc
How many gates were required before and after?
iClicker Question
BEFORE AFTER
2 OR 1 OR
2 OR, 1 AND 2 OR
2 OR, 1 AND 1 OR, 1 AND
2 OR, 2 AND 2 OR
2 OR, 2 AND 2 OR, 1 AND
Notes: Before: 2 OR gates, 1 AND
After: 1 OR gate, 1 AND

## Slide 39
a + 0 = a
a + 1 = 1
a + ā = 1
a · 0 = 0
a · 1 = a
a · ā = 0
a + a b = a
a (b+c) = ab + ac
(a+b)(a+c)  a + bc
How many gates were required before and after?
iClicker Question
BEFORE AFTER
2 OR 1 OR
2 OR, 1 AND 2 OR
2 OR, 1 AND 1 OR, 1 AND
2 OR, 2 AND 2 OR
2 OR, 2 AND 2 OR, 1 AND
Notes: Before: 2 OR gates, 1 AND
After: 1 OR gate, 1 AND

## Slide 40
Checking Equality w/Truth Tables
circuits ↔ truth tables ↔ equations
Example: (a+b)(a+c) = a + bc
a | b | c |  |  |  |  | 
0 | 0 | 0 |  |  |  |  | 
0 | 0 | 1 |  |  |  |  | 
0 | 1 | 0 |  |  |  |  | 
0 | 1 | 1 |  |  |  |  | 
1 | 0 | 0 |  |  |  |  | 
1 | 0 | 1 |  |  |  |  | 
1 | 1 | 0 |  |  |  |  | 
1 | 1 | 1 |  |  |  |  | 

## Slide 41
Checking Equality w/Truth Tables
circuits ↔ truth tables ↔ equations
Example: (a+b)(a+c) = a + bc
a | b | c |  |  |  |  | 
0 | 0 | 0 |  |  |  |  | 
0 | 0 | 1 |  |  |  |  | 
0 | 1 | 0 |  |  |  |  | 
0 | 1 | 1 |  |  |  |  | 
1 | 0 | 0 |  |  |  |  | 
1 | 0 | 1 |  |  |  |  | 
1 | 1 | 0 |  |  |  |  | 
1 | 1 | 1 |  |  |  |  | 
Notes: (a+b)(a+c)
= aa + ab + ac + bc
= a + a(b+c) + bc
= a(1 + (b+c)) + bc
= a + bc

## Slide 42
Checking Equality w/Truth Tables
circuits ↔ truth tables ↔ equations
Example: (a+b)(a+c) = a + bc
 |  |  |  |  |  | bc | RHS
 |  |  |  |  |  | 0 | 0
 |  |  |  |  |  | 0 | 0
 |  |  |  |  |  | 0 | 0
 |  |  |  |  |  | 1 | 1
 |  |  |  |  |  | 0 | 1
 |  |  |  |  |  | 0 | 1
 |  |  |  |  |  | 0 | 1
 |  |  |  |  |  | 1 | 1
a | b | c |  |  |  |  | 
0 | 0 | 0 |  |  |  |  | 
0 | 0 | 1 |  |  |  |  | 
0 | 1 | 0 |  |  |  |  | 
0 | 1 | 1 |  |  |  |  | 
1 | 0 | 0 |  |  |  |  | 
1 | 0 | 1 |  |  |  |  | 
1 | 1 | 0 |  |  |  |  | 
1 | 1 | 1 |  |  |  |  | 
 |  |  | a+b | a+c | LHS |  | 
 |  |  | 0 | 0 | 0 |  | 
 |  |  | 0 | 1 | 0 |  | 
 |  |  | 1 | 0 | 0 |  | 
 |  |  | 1 | 1 | 1 |  | 
 |  |  | 1 | 1 | 1 |  | 
 |  |  | 1 | 1 | 1 |  | 
 |  |  | 1 | 1 | 1 |  | 
 |  |  | 1 | 1 | 1 |  | 

## Slide 43: Takeaway
Binary (two symbols: true and false) is the basis of Logic Design
More than one Logic Circuit can implement same Logic function. Use Algebra (Identities) or Truth Tables to show equivalence.

## Slide 44: Goals for Today
From Switches to Logic Gates to Logic Circuits
Logic Gates
  From switches
  Truth Tables
Logic Circuits
  From Truth Tables to Circuits (Sum of Products)
  Identity Laws
Logic Circuit Minimization
  Algebraic Manipulations
  Truth Tables (Karnaugh Maps)
Transistors (electronic switch)

## Slide 45
Karnaugh Maps
        How does one find the most efficient equation?
          Manipulate algebraically until…?
          Use Karnaugh Maps (optimize visually)
          Use a software optimizer
          For large circuits
          Decomposition & reuse of building blocks

## Slide 46
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Sum of minterms yields
  out = c + bc + a + ac
Minimization with Karnaugh maps (1)

## Slide 47
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Sum of minterms yields
  out = c + bc + a + ac
Karnaugh maps identify which inputs are (ir)relevant to the output
0 | 0 | 0 | 1
1 | 1 | 0 | 1
00 01 11 10
0
1
c
ab
Minimization with Karnaugh maps (2)

## Slide 48
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Sum of minterms yields
  out = c + bc + a + ac
Karnaugh map minimization
  Cover all 1’s
  Group adjacent blocks of 2n 1’s that yield a rectangular shape
  Encode the common features of the rectangle
    out = a + c
0 | 0 | 0 | 1
1 | 1 | 0 | 1
00 01 11 10
0
1
c
ab
Minimization with Karnaugh maps (2)

## Slide 49
Karnaugh Minimization Tricks (1)
Minterms can overlap
  out = b + a + ab
Minterms can span 2, 4, 8 or more cells
  out = + ab
0 | 1 | 1 | 1
0 | 0 | 1 | 0
00 01 11 10
0
1
c
ab
1 | 1 | 1 | 1
0 | 0 | 1 | 0
00 01 11 10
0
1
c
ab

## Slide 50
Karnaugh Minimization Tricks (2)
The map wraps around
  out = d
  out =
1 | 0 | 0 | 1
0 | 0 | 0 | 0
0 | 0 | 0 | 0
1 | 0 | 0 | 1
00 01 11 10
00
01
ab
cd
11
10
0 | 0 | 0 | 0
1 | 0 | 0 | 1
1 | 0 | 0 | 1
0 | 0 | 0 | 0
00 01 11 10
00
01
ab
cd
11
10

## Slide 51
“Don’t care” values can be interpreted individually in whatever way is convenient
  assume all x’s = 1
  out = d
  assume middle x’s = 0
  assume 4th column x = 1
  out =
Karnaugh Minimization Tricks (3)
1 | 0 | 0 | x
0 | x | x | 0
0 | x | x | 0
1 | 0 | 0 | 1
00 01 11 10
00
01
ab
cd
11
10
0 | 0 | 0 | 0
1 | x | x | x
1 | x | x | 1
0 | 0 | 0 | 0
00 01 11 10
00
01
ab
cd
11
10

## Slide 52
0 | 0 | 0 | 1
1 | 1 | 0 | 1
Minimization with K-Maps
  (1) Circle the 1’s (see below)
  (2) Each circle is a logical component of the final equation
  = a + c
00 01 11 10
0
1
c
ab
Rules:
Use fewest circles necessary to cover all 1’s
Circles must cover only 1’s
Circles span rectangles of size power of 2 (1, 2, 4, 8…)
Circles should be as large as possible (all circles of 1?)
Circles may wrap around edges of K-Map
1 may be circled multiple times if that means fewer circles

## Slide 53
Multiplexer
A multiplexer selects between multiple inputs
  out = a, if d = 0
  out = b, if d = 1
Build truth table
Minimize diagram
Derive logic diagram
a
b
d
a | b | d | out
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
Notes: What is the truth table

## Slide 54
Multiplexer Implementation
a | b | d | out
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Build a truth table
  out = bd + a + ab + abd
a
b
d

## Slide 55
Multiplexer Implementation
a | b | d | out
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
a
b
d
Build the Karnaugh map
00 01 11 10
0
1
d
ab

## Slide 56
Multiplexer Implementation
a | b | d | out
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
a
b
d
Build the Karnaugh map
0 | 0 | 1 | 1
0 | 1 | 1 | 0
00 01 11 10
0
1
d
ab

## Slide 57
Multiplexer Implementation
a | b | d | out
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
a
b
d
Derive Minimal Logic Equation
  out = a + bd
0 | 0 | 1 | 1
0 | 1 | 1 | 0
00 01 11 10
0
1
d
ab
d
b
a

## Slide 58: Takeaway
Binary (two symbols: true and false) is the basis of Logic Design
More than one Logic Circuit can implement same Logic function. Use Algebra (Identities) or Truth Tables to show equivalence.
Any logic function can be implemented as “sum of products”. Karnaugh Maps minimize number of gates.

## Slide 59: Administrivia
Dates to keep in Mind
  Prelims: Tue Mar 5th and Thur May 2nd
  Proj 1: Due Fri Feb 15th
  Proj 2: Due Fri Mar 11th
  Proj 3: Due Thur Mar 28th before Spring break
  Final Project: Due Tue May 16th

## Slide 60: iClicker
Attempt to balance the iClicker graph
Register iClicker
  http://atcsupport.cit.cornell.edu/pollsrvc/

## Slide 61: Goals for Today
From Switches to Logic Gates to Logic Circuits
Logic Gates
  From switches
  Truth Tables
Logic Circuits
  From Truth Tables to Circuits (Sum of Products)
  Identity Laws
Logic Circuit Minimization
  Algebraic Manipulations
  Truth Tables (Karnaugh Maps)
Transistors (electronic switch)

## Slide 62: Silicon Valley & the Semiconductor Industry
Transistors:
Youtube video “How does a transistor work”
  https://www.youtube.com/watch?v=IcrBqCFLHIY
Break: show some Transistor, Fab, Wafer photos
Notes: Everything that we have shown them can be constructed in silicon.

## Slide 63
Transistors 101
N-Type Silicon: negative free-carriers (electrons)
P-Type Silicon: positive free-carriers (holes)
P-Transistor: negative charge on gate generates electric field that creates a (+ charged) p-channel connecting source & drain
N-Transistor: works the opposite way
Metal-Oxide Semiconductor (Gate-Insulator-Silicon)
Complementary MOS = CMOS technology uses both p- & n-type transistors
N-type
Off
Insulator
P-type
P-type
Gate
Drain
Source
+
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
+
+
+
N-type
On
Insulator
P-type
P-type
Gate
Drain
Source
+
+
+
+
+
+
+
+
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
+
+
P-type channel created
+
+
+
+
+
—
P-Transistor
P-Transistor
Notes: Negative charge on the gate generates an electric field that creates a positively-charged path between the source and the drain.
Transistors made from semiconductor materials:
MOSFET – Metal Oxide Semiconductor Field Effect Transistor
NMOS, PMOS – Negative MOS and Positive MOS
CMOS – complementary MOS made from PMOS and NMOS transistors

## Slide 64
CMOS Notation
N-type
P-type
Gate input controls whether current can flow between the other two terminals or not.
Hint: the “o” bubble of the p-type tells you that this gate wants a 0 to be turned on
gate
Off/Open
0
On/Closed
1
Off/Open
1
On/Closed
0
gate

## Slide 65
Which of the following statements is false?
P- and N-type transistors are both used in CMOS designs.
As transistors get smaller, the frequency of your processor will keep getting faster.
As transistors get smaller, you can fit more and more of them on a single chip.
Pure silicon is a semi conductor.
Experts believe that Moore’s Law will soon end.
iClicker Question

## Slide 66
2-Transistor Combination: NOT
Logic gates are constructed by combining transistors in complementary arrangements
Combine p&n transistors to make a NOT gate:
p-gate
closes
n-gate
stays open
p-gate
stays open
n-gate
closes
CMOS Inverter :
ground (0)
power source (1)
input
output
p-gate
n-gate
power source (1)
ground (0)
ground (0)
power source (1)
1
0
0
—
—
+
+
1

## Slide 67
Inverter
In | Out
0 | 1
1 | 0
Function: NOT
Symbol:
Truth Table:
in
out
in
out
Vsupply (aka logic 1)
(ground is logic 0)

## Slide 68
NOR Gate
A | B | out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
Function: NOR
Symbol:
Truth Table:
b
a
out
A
out
Vsupply
B
B
A

## Slide 69
Which Gate is this?
A | B | out
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
Function:
Symbol:
Truth Table:
A
out
Vsupply
B
B
A
Vsupply
iClicker Question
NOT
OR
XOR
AND
NAND
Notes: This is a NAND gate:
A B out
0 0
0 1
1 0
1 1

## Slide 70
Which Gate is this?
A | B | out
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Function:
Symbol:
Truth Table:
A
out
Vsupply
B
B
A
Vsupply
iClicker Question
NOT
OR
XOR
AND
NAND
Notes: This is a NAND gate:
A B out
0 0 1
0 1 1
1 0 1
1 1 0

## Slide 71
Building Functions (Revisited)
NOT:
AND:
OR:
NAND and NOR are universal
  Can implement any function with NAND or just NOR gates
  useful for manufacturing
Notes: This is a NAND gate:
A B out
0 0 1
0 1 1
1 0 1
1 1 0

## Slide 72
Building Functions (Revisited)
NOT:
AND:
OR:
NAND and NOR are universal
  Can implement any function with NAND or just NOR gates
  useful for manufacturing
b
a
b
a
a
Notes: This is a NAND gate:
A B out
0 0 1
0 1 1
1 0 1
1 1 0

## Slide 73: Logic Gates
One can buy gates separately
  ex. 74xxx series of integrated circuits
  cost ~$1 per chip, mostly for packaging and testing
Cumbersome, but possible to build devices using gates put together manually

## Slide 74
Then and Now
Intel Haswell
  1.4 billion transistors, 22nm
  177 square millimeters
  Four processing cores
http://techguru3d.com/4th-gen-intel-haswell-processors-architecture-and-lineup/
The first transistor
  One workbench at AT&T Bell Labs
  1947
  Bardeen, Brattain, and Shockley
https://en.wikipedia.org/wiki/Transistor_count

## Slide 75
Then and Now
Intel Broadwell
  7.2 billion transistors, 14nm
  456 square millimeters
  Up to 22 processing cores
https://www.computershopper.com/computex-2015/performance-preview-desktop-broadwell-at-computex-2015
The first transistor
  One workbench at AT&T Bell Labs
  1947
  Bardeen, Brattain, and Shockley
https://en.wikipedia.org/wiki/Transistor_count

## Slide 76
Big Picture: Abstraction
Hide complexity through simple abstractions
  Simplicity
    Box diagram represents inputs and outputs
  Complexity
    Hides underlying NMOS- and PMOS-transistors and atomic interactions
in
out
Vdd
Vss
in
out
out
a
d
b
a
b
d
out

## Slide 77: Summary
Most modern devices made of billions of transistors
  You will build a processor in this course!
  Modern transistors made from semiconductor materials
  Transistors used to make logic gates and logic circuits
We can now implement any logic circuit
  Use P- & N-transistors to implement NAND/NOR gates
  Use NAND or NOR gates to implement the logic circuit
  Efficiently: use K-maps to find required minimal terms