## Slide 1: Gates and Logic: From Transistors to Logic Gates and Logic Circuits
[Weatherspoon, Bala, Bracy, and Sirer]
Prof. Hakim Weatherspoon
CS 3410
Computer Science
Cornell University

## Slide 2: Goals for Today
From Switches to Logic Gates to Logic Circuits
Logic Gates
  From switches
  Truth Tables
Logic Circuits
  From Truth Tables to Circuits (Sum of Products)
  Identity Laws
Logic Circuit Minimization
  Algebraic Manipulations
  Truth Tables (Karnaugh Maps)
Transistors (electronic switch)

## Slide 3: A switch
Acts as a conductor or insulator.
Can be used to build amazing things…
The Bombe used to break the German
Enigma machine during World War II
Notes: Pictures show the Bombe built by Alan Turing to break the enigma machine ciphers.
They were Fixed-Program Computers came before stored-program computers (general purpose)
The former required re-wiring (e.g. ENIAC took 3 weeks to “re-wire”).

## Slide 4: Basic Building Blocks: Switches to Logic Gates
A | B | Light
OFF | OFF | 
A | B | Light
OFF | OFF | 
OFF | ON | 
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
ON | ON | 
A | B | Light
OFF | OFF | 
A | B | Light
OFF | OFF | 
OFF | ON | 
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
ON | ON | 
A | B | Light
A | B | Light
+
-
-
A
B
A
B
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
ON | ON | 
Truth Table
+
Notes: Speed and size of a mechanical switch
Truth Table: defines the output for all possible combinations of values for input

## Slide 5: Basic Building Blocks: Switches to Logic Gates
Either (OR)
Both (AND)
A | B | Light
OFF | OFF | 
A | B | Light
OFF | OFF | 
OFF | ON | 
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
A | B | Light
OFF | OFF | 
A | B | Light
OFF | OFF | 
OFF | ON | 
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
ON | ON | 
A | B | Light
-
-
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
ON | ON | 
Truth Table
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
ON | ON | 
A
B
A
B
OR
AND
Notes: Speed and size of a mechanical switch
Truth Table: defines the output for all possible combinations of values for input

## Slide 6: Basic Building Blocks: Switches to Logic Gates
Either (OR)
Both (AND)
A | B | Light
OFF | OFF | 
A | B | Light
OFF | OFF | 
OFF | ON | 
A | B | Light
OFF | OFF | 
OFF | ON | 
ON | OFF | 
ON | ON | 
-
-
Truth Table
A
B
A
B
OR
AND
A | B | Light
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
0 = OFF
1 = ON
A | B | Light
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
Notes: Speed and size of a mechanical switch
Truth Table: defines the output for all possible combinations of values for input

## Slide 7: Basic Building Blocks: Switches to Logic Gates
A
B
A
B
OR
AND
Did you know?
George Boole: Inventor of the idea of logic gates. He was born in Lincoln, England and he was the son of a shoemaker in a low class family.
George Boole (1815-1864)
Notes: E.g. logic statements:
“Jane will only go to the cinema tonight if a good film is on AND she has enough money.”
“Stuart will only go to the birthday party on Sunday if Katie OR Sujit is going too.”

## Slide 8: Takeaway
Binary (two symbols: true and false) is the basis of Logic Design

## Slide 9
Building Functions: Logic Gates
NOT:
AND:
OR:
Logic Gates
  digital circuit that either allows a signal to pass through it or not.
  Used to build logic functions
  There are seven basic logic gates:
  AND, OR, NOT,
  NAND (not AND), NOR (not OR), XOR, and XNOR (not XOR) [later]
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | Out
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | Out
0 | 1
1 | 0
A
B
A
B
A
A | B | Out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
A | B | Out
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
A
B
NAND:
NOR:
Notes: Create truth table of AND or OR: state what they do
Did you know? Logic gates allow the computer to do things such as add, divide, multiply, do simple yes and no reasoning in certain situations along with other things.

## Slide 10: Goals for Today
From Switches to Logic Gates to Logic Circuits
Logic Gates
  From switches
  Truth Tables
Logic Circuits
  From Truth Tables to Circuits (Sum of Products)
  Identity Laws
Logic Circuit Minimization
  Algebraic Manipulations
  Truth Tables (Karnaugh Maps)
Transistors (electronic switch)

## Slide 11: Next Goal
Given a Logic function, create a Logic Circuit that implements the Logic Function…
…and, with the minimum number of logic gates
Fewer gates: A cheaper ($$$) circuit!
Notes: Can get logic circuit from truth table
Minimize logic circuit through algebraic reductions or Karnaugh Maps

## Slide 12
NOT:
AND:
OR:
XOR:
Logic Gates
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | Out
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | Out
0 | 1
1 | 0
A
B
A
B
A
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
A | B | Out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
A | B | Out
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
A
B
NAND:
NOR:
A | B | Out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A
B
XNOR:
Notes: XOR is not a basic Logic Gate since it can be created from AND and OR gates, but it is often used as a basic Logic Operator

## Slide 13
Logic Implementation
How to implement a desired logic function?
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Notes: Draw circuit and go through out=true cases
Have not done cheaply yet

## Slide 14
Logic Implementation
How to implement a desired logic function?
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Write minterms
sum of products:
OR of all minterms where out=1
minterm
a b c
a b c
a b c
a b c
a b c
a b c
a b c
a b c
Notes: Show what out equals

## Slide 15
Logic Equations
NOT:
  out = ā = !a = a
AND:
  out = a ∙ b = a & b = a  b
OR:
  out = a + b = a | b = a  b
XOR:
  out = a  b = a + āb
Logic Equations
  Constants: true = 1, false = 0
  Variables: a, b, out, …
  Operators (above): AND, OR, NOT, etc.
NAND:
  out = = !(a & b) =  (a  b)
NOR:
  out = = !(a | b) =  (a  b)
XNOR:
  out = = ab +
  .
Notes: Apologize that there are three ways to represent the same logic equation
XOR is not a basic Logic Gate since it can be created from AND and OR gates, but it is often used as a basic Logic Operator
AND is “product”
OR is “sum”
Read outloud

## Slide 16
Identities
Identities useful for manipulating logic equations
  For optimization & ease of implementation
  a + 0 =
  a + 1 =
  a + ā =
  a ∙ 0 =
  a ∙ 1 =
  a ∙ ā =
Notes: Minimization activity
Maybe use picture to go through
Complement a+ā=1 and aā=0

## Slide 17
Identities useful for manipulating logic equations
  For optimization & ease of implementation
  =
  =
  a + a b =
  a(b+c) =
  =
Identities
Notes: Minimization activity
Maybe use picture to go through
  De Morgan’s Law: = ∙ and = +
Minimization activity
Maybe use picture to go through
  De Morgan’s Law: ((a+b)) ̅ = a ̅ ∙ b ̅ and ((a ∙b)) ̅ = a ̅ + b ̅

## Slide 18: Goals for Today
From Switches to Logic Gates to Logic Circuits
Logic Gates
  From switches
  Truth Tables
Logic Circuits
  From Truth Tables to Circuits (Sum of Products)
  Identity Laws
Logic Circuit Minimization – why?
  Algebraic Manipulations
  Truth Tables (Karnaugh Maps)
Transistors (electronic switch)

## Slide 19
Checking Equality w/Truth Tables
circuits ↔ truth tables ↔ equations
Example: (a+b)(a+c) = a + bc
a | b | c |  |  |  |  | 
0 | 0 | 0 |  |  |  |  | 
0 | 0 | 1 |  |  |  |  | 
0 | 1 | 0 |  |  |  |  | 
0 | 1 | 1 |  |  |  |  | 
1 | 0 | 0 |  |  |  |  | 
1 | 0 | 1 |  |  |  |  | 
1 | 1 | 0 |  |  |  |  | 
1 | 1 | 1 |  |  |  |  | 

## Slide 20: Takeaway
Binary (two symbols: true and false) is the basis of Logic Design
More than one Logic Circuit can implement same Logic function. Use Algebra (Identities) or Truth Tables to show equivalence.

## Slide 21: Goals for Today
From Switches to Logic Gates to Logic Circuits
Logic Gates
  From switches
  Truth Tables
Logic Circuits
  From Truth Tables to Circuits (Sum of Products)
  Identity Laws
Logic Circuit Minimization
  Algebraic Manipulations
  Truth Tables (Karnaugh Maps)
Transistors (electronic switch)

## Slide 22
Karnaugh Maps
        How does one find the most efficient equation?
          Manipulate algebraically until…?
          Use Karnaugh Maps (optimize visually)
          Use a software optimizer
          For large circuits
          Decomposition & reuse of building blocks

## Slide 23
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Sum of minterms yields
  out = c + bc + a + ac
Minimization with Karnaugh maps (1)

## Slide 24
a | b | c | out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Sum of minterms yields
  out = c + bc + a + ac
Karnaugh map minimization
  Cover all 1’s
  Group adjacent blocks of 2n 1’s that yield a rectangular shape
  Encode the common features of the rectangle
    out = a + c
0 | 0 | 0 | 1
1 | 1 | 0 | 1
00 01 11 10
0
1
c
ab
Minimization with Karnaugh maps (2)

## Slide 25
Karnaugh Minimization Tricks (1)
Minterms can overlap
  out =
Minterms can span 2, 4, 8 or more cells
  out =
0 | 1 | 1 | 1
0 | 0 | 1 | 0
00 01 11 10
0
1
c
ab
1 | 1 | 1 | 1
0 | 0 | 1 | 0
00 01 11 10
0
1
c
ab

## Slide 26
Karnaugh Minimization Tricks (2)
The map wraps around
  out =
  out =
1 | 0 | 0 | 1
0 | 0 | 0 | 0
0 | 0 | 0 | 0
1 | 0 | 0 | 1
00 01 11 10
00
01
ab
cd
11
10
0 | 0 | 0 | 0
1 | 0 | 0 | 1
1 | 0 | 0 | 1
0 | 0 | 0 | 0
00 01 11 10
00
01
ab
cd
11
10

## Slide 27
“Don’t care” values can be interpreted individually in whatever way is convenient
  assume all x’s = 1
  out =
  assume middle x’s = 0
  assume 4th column x = 1
  out =
Karnaugh Minimization Tricks (3)
1 | 0 | 0 | x
0 | x | x | 0
0 | x | x | 0
1 | 0 | 0 | 1
00 01 11 10
00
01
ab
cd
11
10
0 | 0 | 0 | 0
1 | x | x | x
1 | x | x | 1
0 | 0 | 0 | 0
00 01 11 10
00
01
ab
cd
11
10

## Slide 28
0 | 0 | 0 | 1
1 | 1 | 0 | 1
Minimization with K-Maps
  (1) Circle the 1’s (see below)
  (2) Each circle is a logical component of the final equation
  = a + c
00 01 11 10
0
1
c
ab
Rules:
Use fewest circles necessary to cover all 1’s
Circles must cover only 1’s
Circles span rectangles of size power of 2 (1, 2, 4, 8…)
Circles should be as large as possible (all circles of 1?)
Circles may wrap around edges of K-Map
1 may be circled multiple times if that means fewer circles

## Slide 29
Multiplexer
A multiplexer selects between multiple inputs
  out = a, if d = 0
  out = b, if d = 1
Build truth table
Minimize diagram
Derive logic diagram
a
b
d
a | b | d | out
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
Notes: What is the truth table

## Slide 30: Takeaway
Binary (two symbols: true and false) is the basis of Logic Design
More than one Logic Circuit can implement same Logic function. Use Algebra (Identities) or Truth Tables to show equivalence.
Any logic function can be implemented as “sum of products”. Karnaugh Maps minimize number of gates.

## Slide 31: Goals for Today
From Switches to Logic Gates to Logic Circuits
Logic Gates
  From switches
  Truth Tables
Logic Circuits
  From Truth Tables to Circuits (Sum of Products)
  Identity Laws
Logic Circuit Minimization
  Algebraic Manipulations
  Truth Tables (Karnaugh Maps)
Transistors (electronic switch)

## Slide 32: Silicon Valley & the Semiconductor Industry
Transistors:
Youtube video “How does a transistor work”
  https://www.youtube.com/watch?v=IcrBqCFLHIY
Break: show some Transistor, Fab, Wafer photos
Notes: Everything that we have shown them can be constructed in silicon.

## Slide 33
Transistors 101
N-Type Silicon: negative free-carriers (electrons)
P-Type Silicon: positive free-carriers (holes)
P-Transistor: negative charge on gate generates electric field that creates a (+ charged) p-channel connecting source & drain
N-Transistor: works the opposite way
Metal-Oxide Semiconductor (Gate-Insulator-Silicon)
Complementary MOS = CMOS technology uses both p- & n-type transistors
N-type
Off
Insulator
P-type
P-type
Gate
Drain
Source
+
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
+
+
+
N-type
On
Insulator
P-type
P-type
Gate
Drain
Source
+
+
+
+
+
+
+
+
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
+
+
P-type channel created
+
+
+
+
+
—
P-Transistor
P-Transistor
Notes: Negative charge on the gate generates an electric field that creates a positively-charged path between the source and the drain.
Transistors made from semiconductor materials:
MOSFET – Metal Oxide Semiconductor Field Effect Transistor
NMOS, PMOS – Negative MOS and Positive MOS
CMOS – complementary MOS made from PMOS and NMOS transistors

## Slide 34
CMOS Notation
N-type
P-type
Gate input controls whether current can flow between the other two terminals or not.
Hint: the “o” bubble of the p-type tells you that this gate wants a 0 to be turned on
gate
Off/Open
0
On/Closed
1
Off/Open
1
On/Closed
0
gate

## Slide 35
2-Transistor Combination: NOT
Logic gates are constructed by combining transistors in complementary arrangements
Combine p&n transistors to make a NOT gate:
p-gate
closes
n-gate
stays open
p-gate
stays open
n-gate
closes
CMOS Inverter :
ground (0)
power source (1)
input
output
p-gate
n-gate
power source (1)
ground (0)
ground (0)
power source (1)
1
0
0
—
—
+
+
1

## Slide 36
Inverter
In | Out
0 | 1
1 | 0
Function: NOT
Symbol:
Truth Table:
in
out
in
out
Vsupply (aka logic 1)
(ground is logic 0)

## Slide 37
NOR Gate
A | B | out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
Function: NOR
Symbol:
Truth Table:
b
a
out
A
out
Vsupply
B
B
A

## Slide 38
Building Functions (Revisited)
NOT:
AND:
OR:
NAND and NOR are universal
  Can implement any function with NAND or just NOR gates
  useful for manufacturing
b
a
b
a
a
Notes: This is a NAND gate:
A B out
0 0 1
0 1 1
1 0 1
1 1 0

## Slide 39: Logic Gates
One can buy gates separately
  ex. 74xxx series of integrated circuits
  cost ~$1 per chip, mostly for packaging and testing
Cumbersome, but possible to build devices using gates put together manually

## Slide 40
Then and Now
Intel Haswell
  1.4 billion transistors, 22nm
  177 square millimeters
  Four processing cores
http://techguru3d.com/4th-gen-intel-haswell-processors-architecture-and-lineup/
The first transistor
  One workbench at AT&T Bell Labs
  1947
  Bardeen, Brattain, and Shockley
https://en.wikipedia.org/wiki/Transistor_count

## Slide 41
Then and Now
Intel Broadwell
  7.2 billion transistors, 14nm
  456 square millimeters
  Up to 22 processing cores
https://www.computershopper.com/computex-2015/performance-preview-desktop-broadwell-at-computex-2015
The first transistor
  One workbench at AT&T Bell Labs
  1947
  Bardeen, Brattain, and Shockley
https://en.wikipedia.org/wiki/Transistor_count

## Slide 42
Big Picture: Abstraction
Hide complexity through simple abstractions
  Simplicity
    Box diagram represents inputs and outputs
  Complexity
    Hides underlying NMOS- and PMOS-transistors and atomic interactions
in
out
Vdd
Vss
in
out
out
a
d
b
a
b
d
out

## Slide 43: Summary
Most modern devices made of billions of transistors
  You will build a processor in this course!
  Modern transistors made from semiconductor materials
  Transistors used to make logic gates and logic circuits
We can now implement any logic circuit
  Use P- & N-transistors to implement NAND/NOR gates
  Use NAND or NOR gates to implement the logic circuit
  Efficiently: use K-maps to find required minimal terms