## Slide 1: Numbers and Arithmetic
[Weatherspoon, Bala, Bracy, and Sirer]
Prof. Hakim Weatherspoon
CS 3410
Computer Science
Cornell University

## Slide 2: Big Picture: Building Processor
Simplified Single-cycle processor

## Slide 3: Goals for Today
  Binary Operations
  Number representations
  One-bit and four-bit adders
  Negative numbers and two’s compliment
  Addition (two’s compliment)
  Detecting and handling overflow
  Subtraction (two’s compliment)

## Slide 4: Number Representations
Recall: Binary
  Two symbols (base 2): true and false; 1 and 0
  Basis of Logic Circuits and all digital computers
So, how do we represent numbers in Binary (base 2)?

## Slide 5: Number Representations
Recall: Binary
  Two symbols (base 2): true and false; 1 and 0
  Basis of Logic Circuits and all digital computers
So, how do we represent numbers in Binary (base 2)?
  We can represent numbers in Decimal (base 10).
    E.g. 6 3 7
  Can just as easily use other bases
    Base 2 — Binary
    Base 8 — Octal
    Base 16 — Hexadecimal
1 0 0 1 1 1 1 1 0 1
29 28 27 26 25 24 23 22 21 20
0o 1 1 7 5
83 82 81 80
0x 2 7 d
162 161 160
102 101 100
Notes:     637 has a 1’s place , 10’s place and 100’s place
    Show how to go from

## Slide 6: Number Representations
Recall: Binary
  Two symbols (base 2): true and false; 1 and 0
  Basis of Logic Circuits and all digital computers
So, how do we represent numbers in Binary (base 2)?
  We can represent numbers in Decimal (base 10).
    E.g. 6 3 7
  Can just as easily use other bases
    Base 2 — Binary
    Base 8 — Octal
    Base 16 — Hexadecimal
102 101 100
6∙102 + 3∙101 + 7∙100 = 637
1∙29+1∙26+1∙25+1∙24+1∙23+1∙22+1∙20 = 637
1∙83 + 1∙82 + 7∙81 + 5∙80 = 637
2∙162 + 7∙161 + d∙160 = 637
2∙162 + 7∙161 + 13∙160 = 637
Notes:     637 has a 1’s place , 10’s place and 100’s place
    Show how to go from

## Slide 7
Number Representations: Activity #1 Counting
How do we count in different bases?
  Dec (base 10) Bin (base 2) Oct (base 8) Hex (base 16)
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
.
.
99
100
0
1
2
3
4
5
6
7
10
11
12
13
14
15
16
17
20
21
22
.
.
0
1
2
3
4
5
6
7
8
9
a
b
c
d
e
f
10
11
12
.
.
0
1
10
11
100
101
110
111
1000
1001
1010
1011
1100
1101
1110
1111
1 0000
1 0001
1 0010
.
.
0b 1111 1111 = ?
0b 1 0000 0000 = ?
0o 77 = ?
0o 100 = ?
0x ff = ?
0x 100 = ?
Notes: The base represents the number of unique symbols (decimal has 10, octal has 8, hexadecimal has 16, and binary has 2 unique symbols)
Every group of four bits is called a nibble, every group of 8 bits is a byte

## Slide 8
Number Representations: Activity #1 Counting
How do we count in different bases?
  Dec (base 10) Bin (base 2) Oct (base 8) Hex (base 16)
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
.
.
99
100
0
1
2
3
4
5
6
7
10
11
12
13
14
15
16
17
20
21
22
.
.
0
1
2
3
4
5
6
7
8
9
a
b
c
d
e
f
10
11
12
.
.
0
1
10
11
100
101
110
111
1000
1001
1010
1011
1100
1101
1110
1111
1 0000
1 0001
1 0010
.
.
0b 1111 1111 = 255
0b 1 0000 0000 = 256
0o 77 = 63
0o 100 = 64
0x ff = 255
0x 100 = 256
Notes: Every group of four bits is called a nibble, every group of 8 bits is a byte

## Slide 9: Number Representations
  How to convert a number between different bases?
  Base conversion via repetitive division
  Divide by base, write remainder, move left with quotient
  637  8 = 79 remainder 5
  79  8 = 9 remainder 7
  9  8 = 1 remainder 1
  1  8 = 0 remainder 1
637 = 0o 1175
lsb (least significant bit)
msb (most significant bit)
lsb
msb
Notes: **Convert to a different base instead of same base**
637 = 0o1175 = 0b1001111101 = 0x27D
oct: 637 : 79 : 9 : 1 : 0
bin: 637 : 318 : 159 : 79 : 39 : 19 : 9 : 4 : 2 : 1 : 0
hex: 637 : 39 : 2 : 0

## Slide 10: Number Representations
Convert a base 10 number to a base 2 number
Base conversion via repetitive division
  Divide by base, write remainder, move left with quotient
  637  2 = 318 remainder 1
  318  2 = 159 remainder 0
  159  2 = 79 remainder 1
  79  2 = 39 remainder 1
  39  2 = 19 remainder 1
  19  2 = 9 remainder 1
  9  2 = 4 remainder 1
  4  2 = 2 remainder 0
  2  2 = 1 remainder 0
  1  2 = 0 remainder 1
637 = 10 0111 1101 (can also be written as 0b10 0111 1101)
lsb (least significant bit)
msb (most significant bit)
lsb
msb
Notes: Ask students to write down binary number after we figure it out. The question is did they writ the MSB on the left?
637 = 0o1175 = 0b10 0111 1101 = 0x27D
oct: 637 : 79 : 9 : 1 : 0
bin: 637 : 318 : 159 : 79 : 39 : 19 : 9 : 4 : 2 : 1 : 0
hex: 637 : 39 : 2 : 0

## Slide 11: Clicker Question!
Convert the number 65710 to base 16
What is the least significant digit of this number?
a) D
b) F
c) 0
d) 1
e) 11
Notes: 657 = 0x291
hex: 637 : 39 : 2 : 0

## Slide 12: Clicker Question!
Convert the number 65710 to base 16
What is the least significant digit of this number?
a) D
b) F
c) 0
d) 1
e) 11
Notes: 657 = 0x291
hex: 637 : 39 : 2 : 0

## Slide 13: Number Representations
Convert a base 10 number to a base 16 number
Base conversion via repetitive division
  Divide by base, write remainder, move left with quotient
  657  16 = 41 remainder 1
  41  16 = 2 remainder 9
  2  16 = 0 remainder 2
Thus, 657 = 0x291
lsb
msb
Notes: Is 657 same as 0x 657 ?
657 = 0o1175 = 0b10 0111 1101 = 0x27D
oct: 657 : 79 : 9 : 1 : 0
bin: 657 : 318 : 159 : 79 : 39 : 19 : 9 : 4 : 2 : 1 : 0
hex: 657 : 39 : 2 : 0

## Slide 14: Number Representations
Convert a base 10 number to a base 16 number
Base conversion via repetitive division
  Divide by base, write remainder, move left with quotient
  637  16 = 39 remainder 13
  39  16 = 2 remainder 7
  2  16 = 0 remainder 2
637 = 0x 2 7 13 = ?
Thus, 637 = 0x27d
dec = hex
10 = 0xa
11 = 0xb
12 = 0xc
13 = 0xd
14 = 0xe
15 = 0xf
= bin
= 1010
= 1011
= 1100
= 1101
= 1110
= 1111
lsb
msb
Notes: Is 637 same as 0x 637 ?
637 = 0o1175 = 0b10 0111 1101 = 0x27D
oct: 637 : 79 : 9 : 1 : 0
bin: 637 : 318 : 159 : 79 : 39 : 19 : 9 : 4 : 2 : 1 : 0
hex: 637 : 39 : 2 : 0

## Slide 15: Number Representations
Convert a base 2 number to base 8 (oct) or 16 (hex)
Binary to Hexadecimal
  Convert each nibble (group of four bits) from binary to hex
  A nibble (four bits) ranges in value from 0…15, which is one hex digit
    Range: 0000…1111 (binary) => 0x0 …0xF (hex) => 0…15 (decimal)
  E.g. 0b 10 0111 1101
  2 7 d  0x27d
    Thus, 637 = 0x27d = 0b10 0111 1101
Binary to Octal
  Convert each group of three bits from binary to oct
  Three bits range in value from 0…7, which is one octal digit
    Range: 0000…1111 (binary) => 0x0 …0xF (hex) => 0…15 (decimal)
  E.g. 0b1 001 111 101
  1 1 7 5  0o 1175
    Thus, 637 = 0o1175 = 0b10 0111 1101
Notes: Ask class to convert from binary to octal
637 = 0o1175 = 0b10 0111 1101 = 0x27D
oct: 637 : 79 : 9 : 1 : 0
bin: 637 : 318 : 159 : 79 : 39 : 19 : 9 : 4 : 2 : 1 : 0
hex: 637 : 39 : 2 : 0

## Slide 16: Number Representations Summary
We can represent any number in any base
  Base 10 – Decimal
  Base 2 — Binary
  Base 8 — Octal
  Base 16 — Hexadecimal
102 101 100
1 0 0 1 1 1 1 1 0 1
29 28 27 26 25 24 23 22 21 20
0x 2 7 d
162161160
0o 1 1 7 5
83 82 81 80
6 3 7
6∙102 + 3∙101 + 7∙100 = 637
1∙29+1∙26+1∙25+1∙24+1∙23+1∙22+1∙20 = 637
1∙83 + 1∙82 + 7∙81 + 5∙80 = 637
2∙162 + 7∙161 + d∙160 = 637
2∙162 + 7∙161 + 13∙160 = 637
Notes:     637 has a 1’s place , 10’s place and 100’s place

## Slide 17: Achievement Unlocked!
There are 10 types of people in the world:
Those who understand binary
And those who do not
And those who know this joke was written
in base 2

## Slide 18: Takeaway
Digital computers are implemented via logic circuits and thus represent all numbers in binary (base 2).
We (humans) often write numbers as decimal and hexadecimal for convenience, so need to be able to convert to binary and back (to understand what the computer is doing!).
Notes: We can write any number in any base we like. The most natural base for computers is binary, which is hard to read, which is the reason we use hex and octal. Decimal..

## Slide 19: Today’s Lecture
Binary Operations
  Number representations
  One-bit and four-bit adders
  Negative numbers and two’s compliment
  Addition (two’s compliment)
  Detecting and handling overflow
  Subtraction (two’s compliment)

## Slide 20: Next Goal
Binary Arithmetic: Add and Subtract two binary numbers

## Slide 21: Binary Addition
Addition works the same way regardless of base
  Add the digits in each position
  Propagate the carry
  Unsigned binary addition is pretty easy
  Combine two bits at a time
  Along with a carry
183 + 254
001110
+ 011100
How do we do arithmetic in binary?
1
Carry-out
Carry-in
1
1
1
0
0
0
1
1
1
4
3
7
Notes: Talk about Cin (carry in) and Cout (carry out)
Animate this better
Add another slide
So we need two numbers, the sum, carry in, and carry out

## Slide 22: Binary Addition
Addition works the same way regardless of base
  Add the digits in each position
  Propagate the carry
  Unsigned binary addition is pretty easy
  Combine two bits at a time
  Along with a carry
183 + 254
001110
+ 011100
How do we do arithmetic in binary?
1
437
101010
111
Notes: Talk about Cin (carry in) and Cout (carry out)
Animate this better
Add another slide
So we need two numbers, the sum, carry in, and carry out

## Slide 23: Binary Addition
Binary addition requires
  Add of two bits PLUS carry-in
  Also, carry-out if necessary

## Slide 24: 1-bit Adder
Half Adder
Adds two 1-bit numbers
Computes 1-bit result and 1-bit carry
No carry-in
Clicker Question
What is the equation for Cout?
A + B
AB
A  B
A + !B
!A!B
A | B | Cout | S
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
A
B
S
Cout
Notes: Adds two 1-bit numbers, computes 1-bit result and carry out
Useful for the rightmost binary digit, not much else

## Slide 25: 1-bit Adder
Half Adder
Adds two 1-bit numbers
Computes 1-bit result and 1-bit carry
No carry-in
Clicker Question
What is the equation for Cout?
A + B
AB
A  B
A + !B
!A!B
A | B | Cout | S
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
A
B
S
Cout
Notes: Adds two 1-bit numbers, computes 1-bit result and carry out
Useful for the rightmost binary digit, not much else

## Slide 26: 1-bit Adder
Half Adder
Adds two 1-bit numbers
Computes 1-bit result and 1-bit carry
No carry-in
S = B + A
Cout = AB
A | B | Cout | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
A
B
S
Cout
Cout
S
A
B
Notes: Adds two 1-bit numbers, computes 1-bit result and carry out
Useful for the rightmost binary digit, not much else

## Slide 27: 1-bit Adder
Half Adder
Adds two 1-bit numbers
Computes 1-bit result and 1-bit carry
No carry-in
S = B + A = A  B
Cout = AB
A | B | Cout | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
A
B
S
Cout
Cout
S
A
B
Notes: Adds two 1-bit numbers, computes 1-bit result and carry out
Useful for the rightmost binary digit, not much else

## Slide 28: 1-bit Adder with Carry
Full Adder
Adds three 1-bit numbers
Computes 1-bit result and 1-bit carry
Can be cascaded
Now You Try:
Fill in Truth Table
Create Sum-of-Product Form
Minimization the equation
  Karnaugh Maps (coming soon!)
  Algebraic minimization
Draw the Logic Circuits
A
B
S
Cout
Cin
A | B | Cin | Cout | S
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 

## Slide 29: 1-bit Adder with Carry
Full Adder
Adds three 1-bit numbers
Computes 1-bit result and 1-bit carry
Can be cascaded
A
B
S
Cout
Cin
A | B | Cin | Cout | S
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 
Clicker Question
What is the equation for Cout?
A + B + Cin
!A + !B + ! Cin
A  B  Cin
AB + ACin + BCin
ABCin

## Slide 30: 1-bit Adder with Carry
Full Adder
Adds three 1-bit numbers
Computes 1-bit result and 1-bit carry
Can be cascaded
A
B
S
Cout
Cin
A | B | Cin | Cout | S
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 
Clicker Question
What is the equation for Cout?
A + B + Cin
!A + !B + ! Cin
A  B  Cin
AB + ACin + BCin
ABCin

## Slide 31: 1-bit Adder with Carry
Full Adder
Adds three 1-bit numbers
Computes 1-bit result and 1-bit carry
A
B
S
Cout
Cin
A | B | Cin | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
Cout
S
A
B
Cin
Can be cascaded
S = C + B + A + ABC
Cout = BC + AC + AB + ABC

## Slide 32: 1-bit Adder with Carry
Full Adder
Adds three 1-bit numbers
Computes 1-bit result and 1-bit carry
A
B
S
Cout
Cin
A | B | Cin | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
Cout
S
A
B
Cin
Can be cascaded
S = C + B + A + ABC
Cout = BC + AC + AB + ABC
00 01 11 10
AB
Cin
0
1
S
00 01 11 10
AB
Cin
0
1
Cout

## Slide 33: 1-bit Adder with Carry
Full Adder
Adds three 1-bit numbers
Computes 1-bit result and 1-bit carry
A
B
S
Cout
Cin
A | B | Cin | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
Cout
S
A
B
Cin
Can be cascaded
S = C + B + A + ABC
Cout = BC + AC + AB + ABC
Cout = AB + AC + BC
0 | 1 | 0 | 1
1 | 0 | 1 | 0
00 01 11 10
AB
Cin
0
1
S
0 | 0 | 1 | 0
0 | 1 | 1 | 1
00 01 11 10
AB
Cin
0
1
Cout

## Slide 34: 1-bit Adder with Carry
Full Adder
Adds three 1-bit numbers
Computes 1-bit result and 1-bit carry
A
B
S
Cout
Cin
A | B | Cin | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
Cout
S
A
B
Cin
Can be cascaded
S = C + B + A + ABC
S = (C + B) + A( + BC)
S = (B  C) + A()
S = A  (B  C)
0 | 1 | 0 | 1
1 | 0 | 1 | 0
00 01 11 10
AB
Cin
0
1
S
0 | 0 | 1 | 0
0 | 1 | 1 | 1
00 01 11 10
AB
Cin
0
1
Cout

## Slide 35: 1-bit Adder with Carry
A
B
S
Cout
A | B | Cin | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
Cout
S
A
B
Cin
Cin
Full Adder
Adds three 1-bit numbers
Computes 1-bit result and 1-bit carry
Can be cascaded
S = C + B + A + ABC
S = (C + B) + A( + BC)
S = (B  C) + A()
S = A  (B  C)
Cout = BC + AC + AB + ABC
Cout = AB + AC + BC

## Slide 36: Lab1 1-bit Adder with Carry
A
B
S
Cout
A | B | Cin | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
Cout
A
B
Cin
Full Adder
Adds three 1-bit numbers
Computes 1-bit result and 1-bit carry
Can be cascaded
S = C + B + A + ABC
S = (C + B) + A( + BC)
S = (B  C) + A()
S = A  (B  C)
Cout = BC + AC + AB + ABC
Cout = BC + AC + AB( + C)
Cout = BC + AC + AB
Cout = (B + A)C + AB
Cout = (A  B)C + AB

## Slide 37: 4-bit Adder
4-Bit Full Adder
Adds two 4-bit numbers and carry in
Computes 4-bit result and carry out
Can be cascaded
A[4]
B[4]
S[4]
Cout
Cin
Notes: Adds two 1-bit numbers, along with carry-in, computes 1-bit result and carry out
Can be cascaded to add N-bit numbers

## Slide 38: 4-bit Adder
Adds two 4-bit numbers, along with carry-in
Computes 4-bit result and carry out
Carry-out = overflow indicates result does not fit in 4 bits
Notes: Transition: to do subtraction, just add, but negate one number

## Slide 39: 4-bit Adder
Adds two 4-bit numbers, along with carry-in
Computes 4-bit result and carry out
Carry-out = overflow indicates result does not fit in 4 bits
Notes: Transition: to do subtraction, just add, but negate one number

## Slide 40: Takeaway
Digital computers are implemented via logic circuits and thus represent all numbers in binary (base 2).
We (humans) often write numbers as decimal and hexadecimal for convenience, so need to be able to convert to binary and back (to understand what computer is doing!).
Adding two 1-bit numbers generalizes to adding two numbers of any size since 1-bit full adders can be cascaded.

## Slide 41: Today’s Lecture
Binary Operations
  Number representations
  One-bit and four-bit adders
  Negative numbers and two’s compliment
  Addition (two’s compliment)
  Detecting and handling overflow
  Subtraction (two’s compliment)

## Slide 42: Next Goal
How do we subtract two binary numbers?
Equivalent to adding with a negative number
How do we represent negative numbers?

## Slide 43: 1st Attempt: Sign/Magnitude Representation
IBM 7090, 1959:
“a second-generation transistorized version of the
earlier IBM 709 vacuum tube mainframe computers”
First Attempt: Sign/Magnitude Representation
0111 = 7
1111 = -7
  1 bit for sign (0=positive, 1=negative)
  N-1 bits for magnitude
Problem?
Two zero’s: +0 different than -0
Complicated circuits
-2 + 1 = ???
0000 = +0
1000 = -0
Notes: problems? two zeros, circuit still complicated
e.g. the existence of two forms of the same value (-0 and +0) necessitates two rather than a single comparison when checking for equality with zero.
The IBM 7090 was based in sign-magnitude representation.
The CDC 6000 series and UNIVAC 1100 series computers were based on ones' complement.
Also, in one’s complement, in addition to two zero’s, there is a crazy phenomenon called "end-around carry“: If the carry extends past the end of the word it is said to have "wrapped" around, a condition called an "end-around carry". When this occurs, the bit must be added back in at the right-most bit. This phenomenon does not occur in two's complement arithmetic.
Subtraction is similar, except that borrows are propagated to the left instead of carries. If the borrow extends past the end of the word it is said to have "wrapped" around, a condition called an "end-around borrow". When this occurs, the bit must be subtracted back in at the right-most bit. This phenomenon does not occur in two's complement arithmetic.
The CDC 6000 series and UNIVAC 1100 series computers were based on ones' complement.

## Slide 44: Second Attempt: One’s complement
Second Attempt: One’s complement
  Leading 0’s for positive and 1’s for negative
  Negative numbers: complement the positive number
Problem?
  Two zero’s still: +0 different than -0
  -1 if offset from two’s complement
  Complicated circuits
    Carry is difficult
PDP 1
0111 = 7
1000 = -7
0000 = +0
1111 = -0
Notes: problems? two zeros, circuit still complicated
e.g. the existence of two forms of the same value (-0 and +0) necessitates two rather than a single comparison when checking for equality with zero.
The IBM 7090 was based in sign-magnitude representation.
The CDC 6000 series and UNIVAC 1100 series computers were based on ones' complement.
Also, in one’s complement, in addition to two zero’s, there is a crazy phenomenon called "end-around carry“: If the carry extends past the end of the word it is said to have "wrapped" around, a condition called an "end-around carry". When this occurs, the bit must be added back in at the right-most bit. This phenomenon does not occur in two's complement arithmetic.
Subtraction is similar, except that borrows are propagated to the left instead of carries. If the borrow extends past the end of the word it is said to have "wrapped" around, a condition called an "end-around borrow". When this occurs, the bit must be subtracted back in at the right-most bit. This phenomenon does not occur in two's complement arithmetic.
The CDC 6000 series and UNIVAC 1100 series computers were based on ones' complement.

## Slide 45: Two’s Complement Representation
What is used: Two’s Complement Representation
Nonnegative numbers are represented as usual
  0 = 0000, 1 = 0001, 3 = 0011, 7 = 0111
Leading 1’s for negative numbers
To negate any number:
  complement all the bits (i.e. flip all the bits)
  then add 1
  -1: 1  0001  1110  1111
  -3: 3  0011  1100  1101
  -7: 7  0111  1000  1001
  -8: 8  1000  0111  1000
  -0: 0  0000  1111  0000 (this is good, -0 = +0)
Notes: add 1 and *discard carry*
Add a “Did you know box”
The two's complement of an N-bit number is defined as the *complement* with respect to 2^N, in other words the result of subtracting the number from 2^N. This is also equivalent to taking the *ones' complement* and then adding one, since the sum of a number and its ones' complement is all 1 bits. The two's complement of a number behaves like the negative of the original number in most arithmetic, and positive and negative numbers can coexist in a natural way.
Two's complement is the easiest to implement in hardware, which may be the ultimate reason for its widespread popularity[citation needed]. Remember that processors on the early mainframes often consisted of thousands of transistors – eliminating a significant number of transistors was a significant cost savings. The architects of the early integrated circuit based CPUs (Intel 8080, etc.) chose to use two's complement math. As IC technology advanced, virtually all adopted two's complement technology. Intel, AMD, and IBM POWER chips are all two's complement.[

## Slide 46: Two’s Complement
Non-negatives
(as usual):
+0 = 0000
+1 = 0001
+2 = 0010
+3 = 0011
+4 = 0100
+5 = 0101
+6 = 0110
+7 = 0111
+8 = 1000
Negatives (two’s complement)
flip then add 1
= 1111 -0 = 0000
= 1110 -1 = 1111
= 1101 -2 = 1110
= 1100 -3 = 1101
= 1011 -4 = 1100
= 1010 -5 = 1011
= 1001 -6 = 1010
= 1000 -7 = 1001
= 0111 -8 = 1000
Notes: choose -8 so we have a sign bit
+0 = -0
wraps from +7 to -8
asymmetric: no +8

## Slide 47: Two’s Complement
Non-negatives
(as usual):
+0 = 0000
+1 = 0001
+2 = 0010
+3 = 0011
+4 = 0100
+5 = 0101
+6 = 0110
+7 = 0111
+8 = 1000
Negatives (two’s complement)
flip then add 1
= 1111 -0 = 0000
= 1110 -1 = 1111
= 1101 -2 = 1110
= 1100 -3 = 1101
= 1011 -4 = 1100
= 1010 -5 = 1011
= 1001 -6 = 1010
= 1000 -7 = 1001
= 0111 -8 = 1000
Notes: choose -8 so we have a sign bit
+0 = -0
wraps from +7 to -8
asymmetric: no +8

## Slide 48: Two’s Complement vs. Unsigned
-1 = 1111 = 15
-2 = 1110 = 14
-3 = 1101 = 13
-4 = 1100 = 12
-5 = 1011 = 11
-6 = 1010 = 10
-7 = 1001 = 9
-8 = 1000 = 8
+7 = 0111 = 7
+6 = 0110 = 6
+5 = 0101 = 5
+4 = 0100 = 4
+3 = 0011 = 3
+2 = 0010 = 2
+1 = 0001 = 1
0 = 0000 = 0
4 bit
Unsigned Binary
0 … 15
4 bit
Two’s Complement
-8 … 7

## Slide 49: Clicker Question!
What is the value of the 2s complement number
11010
a) 26
b) 6
c) -6
d) -10
e) -26
Notes: 657 = 0x291
hex: 637 : 39 : 2 : 0

## Slide 50: Clicker Question!
What is the value of the 2s complement number
11010
a) 26
b) 6
c) -6
d) -10
e) -26
11010
00101
______+1
-6 = 00110
(flip)
Notes: 657 = 0x291
hex: 637 : 39 : 2 : 0

## Slide 51: Two’s Complement Facts
Signed two’s complement
  Negative numbers have leading 1’s
  zero is unique: +0 = - 0
  wraps from largest positive to largest negative
N bits can be used to represent
  unsigned: range 0…2N-1
    eg: 8 bits  0…255
  signed (two’s complement): -(2N-1)…(2N-1 - 1)
    E.g.: 8 bits  (1000 000) … (0111 1111)
    -128 … 127
Notes: Why two’s complement works:
Given a set of all possible N-bit values, we can assign the lower (by binary value) half to be the integers from 0 to (2^[N−1]−1) inclusive and the upper half to be −2^[N−1] to −1 inclusive. The upper half can be used to represent negative integers from −2^[N−1] to −1 because, under addition modulo 2^N they behave the same way as those negative integers. That is to say that because i + j mod 2^N = i + (j + 2^N) mod 2^N any value in the set { j + k2^N | k is an integer } can be used in place of j.
For example, with eight bits, the unsigned bytes are 0 to 255. Subtracting 256 from the top half (128 to 255) yields the signed bytes −128 to −1.
The relationship to two's complement is realized by noting that 256 = 255 + 1, and (255 − x) is the ones' complement of x.
http://en.wikipedia.org/wiki/Two%27s_complement

## Slide 52: Sign Extension & Truncation
Extending to larger size
  1111 = -1
  1111 1111 = -1
  0111 = 7
  0000 0111 = 7
Truncate to smaller size
  0000 1111 = 15
  BUT, 0000 1111 = 1111 = -1

## Slide 53: Two’s Complement Addition
-1 = 1111 = 15
-2 = 1110 = 14
-3 = 1101 = 13
-4 = 1100 = 12
-5 = 1011 = 11
-6 = 1010 = 10
-7 = 1001 = 9
-8 = 1000 = 8
+7 = 0111 = 7
+6 = 0110 = 6
+5 = 0101 = 5
+4 = 0100 = 4
+3 = 0011 = 3
+2 = 0010 = 2
+1 = 0001 = 1
0 = 0000 = 0
Addition with two’s complement signed numbers
Addition as usual. Ignore the sign. It just works!
Examples
  1 + -1 =
  -3 + -1 =
  -7 + 3 =
  7 + (-3) =

## Slide 54: Two’s Complement Addition
Addition with two’s complement signed numbers
Addition as usual. Ignore the sign. It just works!
Examples
  1 + -1 = 0001 + 1111 =
  -3 + -1 = 1101 + 1111 =
  -7 + 3 = 1001 + 0011 =
  7 + (-3) = 0111 + 1101 =
-1 = 1111 = 15
-2 = 1110 = 14
-3 = 1101 = 13
-4 = 1100 = 12
-5 = 1011 = 11
-6 = 1010 = 10
-7 = 1001 = 9
-8 = 1000 = 8
+7 = 0111 = 7
+6 = 0110 = 6
+5 = 0101 = 5
+4 = 0100 = 4
+3 = 0011 = 3
+2 = 0010 = 2
+1 = 0001 = 1
0 = 0000 = 0

## Slide 55: Two’s Complement Addition
Addition with two’s complement signed numbers
Addition as usual. Ignore the sign. It just works!
Examples
  1 + -1 = 0001 + 1111 = 0000 (0)
  -3 + -1 = 1101 + 1111 = 1100 (-4)
  -7 + 3 = 1001 + 0011 = 1100 (-4)
  7 + (-3) = 0111 + 1101 = 0100 (4)
-1 = 1111 = 15
-2 = 1110 = 14
-3 = 1101 = 13
-4 = 1100 = 12
-5 = 1011 = 11
-6 = 1010 = 10
-7 = 1001 = 9
-8 = 1000 = 8
+7 = 0111 = 7
+6 = 0110 = 6
+5 = 0101 = 5
+4 = 0100 = 4
+3 = 0011 = 3
+2 = 0010 = 2
+1 = 0001 = 1
0 = 0000 = 0

## Slide 56: Two’s Complement Addition
Addition with two’s complement signed numbers
Addition as usual. Ignore the sign. It just works!
Examples
  1 + -1 = 0001 + 1111 = 0000 (0)
  -3 + -1 = 1101 + 1111 = 1100 (-4)
  -7 + 3 = 1001 + 0011 = 1100 (-4)
  7 + (-3) = 0111 + 1101 = 0100 (4)
  Clicker Question
  Which of the following has problems?
    7 + 1
    -7 + -3
    -7 + -1
    Only (a) and (b) have problems
    They all have problems
-1 = 1111 = 15
-2 = 1110 = 14
-3 = 1101 = 13
-4 = 1100 = 12
-5 = 1011 = 11
-6 = 1010 = 10
-7 = 1001 = 9
-8 = 1000 = 8
+7 = 0111 = 7
+6 = 0110 = 6
+5 = 0101 = 5
+4 = 0100 = 4
+3 = 0011 = 3
+2 = 0010 = 2
+1 = 0001 = 1
0 = 0000 = 0
Notes: 1 + (-1)
(-3) + (-1)
(-7) + 3
7 + (-3)
7 + 1 : overflow
(-7) + (-3) : overflow
(-7) + (-1)
7 + 1 = 0111+0001 = 1000 = -8 (OVERFLOW)! (Had a carry in to the MSB!) Sign of out != sign of in
7 + (-3) 0111+ 1101 = 1100 = -4
-7+-3 = 1001 + 1101 = 0110 (cout = 1) (Did not have a carry in to the MSB)
-7+-1 = 1001 + 1111 = 1000 (cout = 1)

## Slide 57: Two’s Complement Addition
Addition with two’s complement signed numbers
Addition as usual. Ignore the sign. It just works!
Examples
  1 + -1 = 0001 + 1111 = 0000 (0)
  -3 + -1 = 1101 + 1111 = 1100 (-4)
  -7 + 3 = 1001 + 0011 = 1100 (-4)
  7 + (-3) = 0111 + 1101 = 0100 (4)
  Clicker Question
  Which of the following has problems?
    7 + 1 = 1000
    -7 + -3 = 1 0110
    -7 + -1 = 1000
    Only (a) and (b) have problems
    They all have problems
-1 = 1111 = 15
-2 = 1110 = 14
-3 = 1101 = 13
-4 = 1100 = 12
-5 = 1011 = 11
-6 = 1010 = 10
-7 = 1001 = 9
-8 = 1000 = 8
+7 = 0111 = 7
+6 = 0110 = 6
+5 = 0101 = 5
+4 = 0100 = 4
+3 = 0011 = 3
+2 = 0010 = 2
+1 = 0001 = 1
0 = 0000 = 0
Notes: 1 + (-1)
(-3) + (-1)
(-7) + 3
7 + (-3)
7 + 1 : overflow
(-7) + (-3) : overflow
(-7) + (-1)
7 + 1 = 0111+0001 = 1000 = -8 (OVERFLOW)! (Had a carry in to the MSB!) Sign of out != sign of in
7 + (-3) 0111+ 1101 = 1100 = -4
-7+-3 = 1001 + 1101 = 0110 (cout = 1) (Did not have a carry in to the MSB)
-7+-1 = 1001 + 1111 = 1000 (cout = 1)

## Slide 58: Two’s Complement Addition
Addition with two’s complement signed numbers
Addition as usual. Ignore the sign. It just works!
Examples
  1 + -1 = 0001 + 1111 = 0000 (0)
  -3 + -1 = 1101 + 1111 = 1100 (-4)
  -7 + 3 = 1001 + 0011 = 1100 (-4)
  7 + (-3) = 0111 + 1101 = 0100 (4)
  Clicker Question
  Which of the following has problems?
    7 + 1 = 1000 overflow
    -7 + -3 = 1 0110 overflow
    -7 + -1 = 1000 fine
    Only (a) and (b) have problems
    They all have problems
-1 = 1111 = 15
-2 = 1110 = 14
-3 = 1101 = 13
-4 = 1100 = 12
-5 = 1011 = 11
-6 = 1010 = 10
-7 = 1001 = 9
-8 = 1000 = 8
+7 = 0111 = 7
+6 = 0110 = 6
+5 = 0101 = 5
+4 = 0100 = 4
+3 = 0011 = 3
+2 = 0010 = 2
+1 = 0001 = 1
0 = 0000 = 0
Notes: 1 + (-1)
(-3) + (-1)
(-7) + 3
7 + (-3)
7 + 1 : overflow
(-7) + (-3) : overflow
(-7) + (-1)
7 + 1 = 0111+0001 = 1000 = -8 (OVERFLOW)! (Had a carry in to the MSB!) Sign of out != sign of in
7 + (-3) 0111+ 1101 = 1100 = -4
-7+-3 = 1001 + 1101 = 0110 (cout = 1) (Did not have a carry in to the MSB)
-7+-1 = 1001 + 1111 = 1000 (cout = 1)

## Slide 59: Next Goal
In general, how do we detect and handle overflow?

## Slide 60: Overflow
When can overflow occur?
  adding a negative and a positive?
    Overflow cannot occur (Why?)
    Always subtract larger magnitude from smaller
  adding two positives?
    Overflow can occur (Why?)
    Precision: Add two positives, and get a negative number!
  adding two negatives?
    Overflow can occur (Why?)
    Precision: add two negatives, get a positive number!
Rule of thumb:
  Overflow happens iff carry into msb != carry out of msb

## Slide 61: Overflow
When can overflow occur?
  adding a negative and a positive?
    Overflow cannot occur (Why?)
    Always subtract larger magnitude from smaller
  adding two positives?
    Overflow can occur (Why?)
    Precision: Add two positives, and get a negative number!
  adding two negatives?
    Overflow can occur (Why?)
    Precision: add two negatives, get a positive number!
Rule of thumb:
  Overflow happens iff carry into msb != carry out of msb
Notes: Overflow occurs because there are not enough bits to represent the precision/magnitude of the result of the add
MSB
0
Cout = 0 0 Cin = 0
0
a = 0
Cout = 0 b = 0 Cin = 1 (Overflow!)
s = 1
a = 1
Cout = 1 b = 1 Cin = 0 (Overflow!)
s = 0
a = 1
Cout = 1 b = 1 Cin = 1
s = 1

## Slide 62: Overflow
When can overflow occur?
  adding a negative and a positive?
    Overflow cannot occur (Why?)
    Always subtract larger magnitude from smaller
  adding two positives?
    Overflow can occur (Why?)
    Precision: Add two positives, and get a negative number!
  adding two negatives?
    Overflow can occur (Why?)
    Precision: add two negatives, get a positive number!
Rule of thumb:
  Overflow happens iff carry into msb != carry out of msb
A | B | Cin | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
Wrong
Sign
Wrong
Sign
SMSB
AMSB BMSB
Cout_MSB
Cin_MSB
over flow

## Slide 64: Today’s Lecture
Binary Operations
  Number representations
  One-bit and four-bit adders
  Negative numbers and two’s compliment
  Addition (two’s compliment)
  Detecting and handling overflow
  Subtraction (two’s compliment)

## Slide 65: Binary Subtraction
Why create a new circuit?
Just use addition using two’s complement math
  How?

## Slide 66: Binary Subtraction
Two’s Complement Subtraction
  Subtraction is simply addition,
  where one of the operands has been negated
    Negation is done by inverting all bits and adding one
    A – B = A + (-B) = A + ( + 1)
Notes: a – b, where b is so large that –B overflows
B must be -8, so that –B = -8
last bit will change
if a >= 0, will correctly signal overflow
if a < 0, will correctly subtract and not signal overflow

## Slide 67: Binary Subtraction
Two’s Complement Subtraction
  Subtraction is simply addition,
  where one of the operands has been negated
    Negation is done by inverting all bits and adding one
    A – B = A + (-B) = A + ( + 1)
Q: How do we detect and handle overflows?
Q: What if (-B) overflows?
Notes: a – b, where b is so large that –B overflows
B must be -8, so that –B = -8
last bit will change
if a >= 0, will correctly signal overflow
if a < 0, will correctly subtract and not signal overflow

## Slide 68: Two’s Complement Adder
Two’s Complement Adder with overflow detection

## Slide 69: Two’s Complement Adder
Two’s Complement Adder with overflow detection

## Slide 70: Two’s Complement Adder
Two’s Complement Adder with overflow detection
Note: 4-bit adder is drawn for illustrative purposes and may not represent the optimal design.

## Slide 71: Two’s Complement Adder
Two’s Complement Adder with overflow detection
Note: 4-bit adder is drawn for illustrative purposes and may not represent the optimal design.

## Slide 72: Two’s Complement Adder
Two’s Complement Adder with overflow detection

## Slide 73: Two’s Complement Adder
Two’s Complement Adder with overflow detection
Before: 2 inverters, 2 AND gates, 1 OR gate After: 1 XOR gate

## Slide 74: Takeaways
Digital computers are implemented via logic circuits and thus represent all numbers in binary (base 2).
We write numbers as decimal or hex for convenience and need to be able to convert to binary and back (to understand what the computer is doing!).
Adding two 1-bit numbers generalizes to adding two numbers of any size since 1-bit full adders can be cascaded.
Using Two’s complement number representation simplifies adder Logic circuit design (0 is unique, easy to negate). Subtraction is adding, where one operand is negated (two’s complement; to negate: flip the bits and add 1).
Overflow if sign of operands A and B != sign of result S.
Can detect overflow by testing Cin != Cout of the most significant bit (msb), which only occurs when previous statement is true.

## Slide 75: Summary
We can now implement combinational logic circuits
  Design each block
    Binary encoded numbers for compactness
  Decompose large circuit into manageable blocks
    1-bit Half Adders, 1-bit Full Adders,
    n-bit Adders via cascaded 1-bit Full Adders, ...
  Can implement circuits using NAND or NOR gates
  Can implement gates using use PMOS and NMOS-transistors
  And can add and subtract numbers (in two’s compliment)!
  Next time, state and finite state machines…