## Slide 1: State
[Weatherspoon, Bala, Bracy, and Sirer]
Prof. Hakim Weatherspoon
CS 3410
Computer Science
Cornell University

## Slide 2: Goals for Today
State
  How do we store one bit?
  Attempts at storing (and changing) one bit
    Set-Reset Latch
    D Latch
    D Flip-Flops
    Master-Slave Flip-Flops
  Register: storing more than one bit, N-bits
Basic Building Blocks
  Decoders and Encoders

## Slide 3: Goal
How do we store store one bit?

## Slide 4: First Attempt: Unstable Devices
B
A
C

## Slide 5: Second Attempt: Bistable Devices
A
B
A Simple Device
Stable and unstable equilibria?
Notes: How to create state? Feedback.
Show how the signal works

## Slide 6: Third Attempt: Set-Reset Latch
B
Q
A
S
R
Notes: Can you store a value (with this circuit)?
Can you change its value?
Q is comes from Latin language "quiscens" or "the present particle" or "what is present available" or "present output"
How to create state? Feedback.
Show how the signal works

## Slide 7: Third Attempt: Set-Reset Latch
B
R
Q
A
S
Set-Reset (S-R) Latch
Stores a value Q and its complement
S | R | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
S | R | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
S | R | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
S | R | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 

## Slide 8: Third Attempt: Set-Reset Latch
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 |  | 
S | R | Q | 
0 | 0 | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 |  | 
Set-Reset (S-R) Latch
Stores a value Q and its complement
S
R
Q
S
R
Q
Notes: Start with 0, 1 => 0, 1
then 0, 0 => 0, 1
then 1, 0 => 1, 0
then 0, 0 => 1, 0, better yet “stay”
1, 1 is forbidden, b/c going to 0, 0 after goes haywire
i.e.
Start 1,1 => 0,0
Alright. Now change S,R to 0, 0, what happens.
1, 1=>0, 0 -> 0, 0=> 0, 0 -> 0, 0=>1, 1 -> 0, 0=> 0, 0 -> oscillations.
S R=>Q,!Q -> S,R=>Q,!Q -> S, R=>Q,!Q -> S,R => Q,!Q

## Slide 9: Takeaway
Set-Reset (SR) Latch can store one bit and we can change the value of the stored bit. But, SR Latch has a forbidden state.

## Slide 10: Next Goal
How do we avoid the forbidden state of S-R Latch?

## Slide 11: Fourth Attempt: (Unclocked) D Latch
Fill in the truth table?
D
S
R
Q
Q
D
D | Q | 
0 |  | 
1 |  | 
D | Q | 
0 |  | 
1 |  | 
S
R
Q
A | B | OR | NOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
Notes: Start in 0, 0, 1
Change to D = 1
After NOT gate, R = 0
After OR+NOT gates, /Q = 0 (R is already ready then), Q goes to 1
Problem: No way to hold state

## Slide 12: Takeaway
Set-Reset (SR) Latch can store one bit and we can change the value of the stored bit. But, SR Latch has a forbidden state.
(Unclocked) D Latch can store and change a bit like an SR Latch while avoiding the forbidden state.

## Slide 13: Next Goal
How do we coordinate state changes to a D Latch?

## Slide 14: Aside: Clocks
Clock helps coordinate state changes
  Usually generated by an oscillating crystal
  Fixed period
  Frequency = 1/period
1
0
clock
period
clock
high
clock
low
rising edge
falling edge

## Slide 15: Clock Disciplines
Level sensitive
  State changes when clock is high (or low)
Edge triggered
  State changes at clock edge
positive edge-triggered
negative edge-triggered

## Slide 16: Clock Methodology
Clock Methodology
Negative edge, synchronous
Edge-Triggered  signals must be stable near falling edge
“near” = before and after
tsetup thold
clk
compute
save
tsetup
thold
compute
save
compute
tcombinational

## Slide 17: Round 2: D Latch (1)
S
R
D
Q
 | D | Q | 
 | 0 |  | 
 | 1 |  | 
 | D | Q | 
 | 0 |  | 
 | 1 |  | 
D
Q
C
Set
Reset
Inverter prevents SR Latch from entering 1,1 state
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables
Answer:
Q
Q
0
1

## Slide 18: Round 2: D Latch (1)
S
R
D
Q
C | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
C | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
D
Q
C
Set
Reset
No
Change
Level sensitive
Inverter prevents SR Latch from entering 1,1 state
C enables changes
C = 1, D Latch transparent: set/reset (according to D)
C = 0, D Latch opaque: keep state (ignore D)
C
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables
Answer:
Q
Q
0
1

## Slide 19: Round 2: D Latch (1)
S
R
D
Q
C | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
C | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
D
Q
C
Set
Reset
No
Change
Level sensitive
Inverter prevents SR Latch from entering 1,1 state
C enables changes
C = 1, D Latch transparent: set/reset (according to D)
C = 0, D Latch opaque: keep state (ignore D)
C
S | R | Q |  | 
0 | 0 | Q |  | hold
0 | 1 | 0 | 1 | reset
1 | 0 | 1 | 0 | set
1 | 1 | forbidden |  | 
S | R | Q |  | 
0 | 0 | Q |  | hold
0 | 1 | 0 | 1 | reset
1 | 0 | 1 | 0 | set
1 | 1 | forbidden |  | 
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables
Answer:
Q
Q
0
1

## Slide 20: Round 2: D Latch(1)
clk
D
Q
clk | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
clk | D | Q | 
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
D
Q
clk
Level Sensitive D Latch
Clock high: set/reset (according to D)
Clock low: keep state (ignore D)
Notes: Any forbidden S=R=1 inputs? No
Need both truth tables

## Slide 21: Round 3: D Flip-Flop
Edge-Triggered
Data captured when clock high
Output changes only on falling edges
D
Q
D
Q
C
C
X
Q
D
clk
L1
L2
Notes: Master-Slave Flip Flop
- Outputs change only on falling edges
- Data is captured on rising edges
1 cycle delay
but works out perfectly – data for the next stage is ready 1 cycle ahead of time

## Slide 22: Round 3: D Flip-Flop
Clock = 1: L1 transparent L2 opaque
D
Q
D
Q
C
C
X
Q
D
clk
0
1
L1
L2
X
D
D passes through L1 to X
X
Clock = 0: L1 opaque L2 transparent
D
Q
D
Q
C
C
X
Q
D
clk
1
0
L1
L2
X
Q
X passes through L2 to Q
X
When CLK falls (10),
Q gets X, X cannot change
When CLK rises (01),
now X can change,
Q does not change
Notes: Master-Slave Flip Flop
- Outputs change only on falling edges
- Data is captured on rising edges
1 cycle delay
but works out perfectly – data for the next stage is ready 1 cycle ahead of time

## Slide 23: Edge-Triggered D Flip-Flop
clk
D
X
Q
B
A
D
Q
D
Q
C
C
X
Q
D
clk
L1
L2
D Flip-Flop
Edge-Triggered
Data captured when clock is high
Output changes only on falling edges
0
0
1
0
1
Notes: Master-Slave Flip Flop
- Outputs change only on falling edges
- Data is captured on rising edges
1 cycle delay
but works out perfectly – data for the next stage is ready 1 cycle ahead of time

## Slide 24: Takeaway
Set-Reset (SR) Latch can store one bit and we can change the value of the stored bit. But, SR Latch has a forbidden state.
(Unclocked) D Latch can store and change a bit like an SR Latch while avoiding a forbidden state.
An Edge-Triggered D Flip-Flip (aka Master-Slave D Flip-Flip) stores one bit. The bit can be changed in a synchronized fashion on the edge of a clock signal.

## Slide 25: Next Goal
How do we store more than one bit, N bits?

## Slide 26: Registers
Register
D flip-flops in parallel
shared clock
extra clocked inputs: write_enable, reset, …
clk
D0
D3
D1
D2
4
4
4-bit
reg
clk

## Slide 27: Takeaway
Set-Reset (SR) Latch can store one bit and we can change the value of the stored bit. But, SR Latch has a forbidden state.
(Unclocked) D Latch can store and change a bit like an SR Latch while avoiding a forbidden state.
An Edge-Triggered D Flip-Flip (aka Master-Slave D Flip-Flip) stores one bit. The bit can be changed in a synchronized fashion on the edge of a clock signal.
An N-bit register stores N-bits. It is created with N D-Flip-Flops in parallel along with a shared clock.

## Slide 28: An Example: What will this circuit do?
4-bit
reg
Clk
Decoder
+1
4
4
4
16
4

## Slide 29: Decoder Example: 7-Segment LED
7-Segment LED
  photons emitted when electrons fall into holes
d7
d6
d5
d4
d3
d2
d1
d0
Notes: Previous slide would need to display up to 16, so would need a 16-segment LED decoder

## Slide 30: Decoder Example: 7-Segment LED Decoder
3 inputs
encode 0 – 7 in binary
7 outputs
one for each LED
7LED decode

## Slide 31: 7 Segment LED Decoder Implementation
d0
d1
d2
d3
d4
d5
d6
b2 | b1 | b0 | d6 | d5 | d4 | d3 | d2 | d1 | d0
0 | 0 | 0 |  |  |  |  |  |  | 
0 | 0 | 1 |  |  |  |  |  |  | 
0 | 1 | 0 |  |  |  |  |  |  | 
0 | 1 | 1 |  |  |  |  |  |  | 
1 | 0 | 0 |  |  |  |  |  |  | 
1 | 0 | 1 |  |  |  |  |  |  | 
1 | 1 | 0 |  |  |  |  |  |  | 
1 | 1 | 1 |  |  |  |  |  |  | 

## Slide 32: Basic Building Blocks We have Seen
binary
encoder
2N
N
binary
decoder
N
2N
Multiplexor
N
M
N
N
N
N
. . .
0
1
2
2M-1

## Slide 33: Encoders
1
2
3
4
5
6
7
0
encoder
N
. . .
. . .
Log2(N) outputs wires
N Input wires
e.g. Voting:
Can only vote for one out of N
candidates, so N inputs.
But can encode vote efficiently
with binary encoding.
Notes: N possible inputs -> log2(N) wires to encode

## Slide 34: Example Encoder Truth Table
a
b
1
c
d
2
3
4
A 3-bit
encoder
with 4 inputs for simplicity
a | b | c | d |  |  |  | 
0 | 0 | 0 | 0 |  |  |  | 
1 | 0 | 0 | 0 |  |  |  | 
0 | 1 | 0 | 0 |  |  |  | 
0 | 0 | 1 | 0 |  |  |  | 
0 | 0 | 0 | 1 |  |  |  | 
o0
o1
o2
Notes: Implementation . . .
assume 8 choices, exactly one mark detected

## Slide 35: Basic Building Blocks Example: Voting
Ballots
The 3410 optical scan
vote reader
machine
detect
enc
8
3
7
7LED decode

## Slide 36: Basic Building Blocks We have Seen
binary
encoder
2N
N
binary
decoder
N
2N
Multiplexor
N
M
N
N
N
N
. . .
0
1
2
2M-1

## Slide 37: Recap
We can now build interesting devices with sensors
  Using combinational logic
We can also store data values (aka Sequential Logic)
  In state-holding elements
  Coupled with clocks

## Slide 38: Summary
We can now build interesting devices with sensors
  Using combinational logic
We can also store data values
  Stateful circuit elements (D Flip Flops, Registers, …)
  Clock to synchronize state changes