## Slide 1: Finite State Machines
Hakim Weatherspoon
CS 3410
Computer Science
Cornell University
[Weatherspoon, Bala, Bracy, McKee, and Sirer]

## Slide 2: Stateful Components
Combinationial logic
  Output computed directly from inputs
  System has no internal state
  Nothing depends on the past!
Need:
  To record data
  To build stateful circuits
  A state-holding device
  Sequential Logic & Finite State Machines
Inputs
Combinational circuit
Outputs
N
M
Notes: How are we going to stably store state

## Slide 3: Goals for Today
Finite State Machines (FSM)
  How do we design logic circuits with state?
  Types of FSMs: Mealy and Moore Machines
  Examples: Serial Adder and a Digital Door Lock

## Slide 4: Next Goal
How do we design logic circuits with state?

## Slide 5: Finite State Machines

## Slide 6: Finite State Machines
An electronic machine which has
  external inputs
  externally visible outputs
  internal state
Output and next state depend on
  inputs
  current state

## Slide 7: Abstract Model of FSM
Machine is
M = (S, I, O,  )
S: Finite set of states
I: Finite set of inputs
O: Finite set of outputs
: State transition function
Next state depends on present input and present state

## Slide 8: Automata Model
Finite State Machine
  inputs from external world
  outputs to external world
  internal state
  combinational logic
Next State
Current State
Input
Output
Registers
Comb. Logic
Notes: Put sequential logic term on slide

## Slide 9: FSM Example
Legend
state
input/output
start state
A
B
C
D
down/on
up/off
down/on
down/off
up/off
down/off
up/off
up/off
Input: up or down
Output: on or off
States: A, B, C, or D

## Slide 10: FSM Example
Legend
00
01
10
11
1/1
0/0
1/1
1/0
0/1
1/0
0/0
0/0
Input: 0=up or 1=down
Output: 1=on or 0=off
States: 00=A, 01=B, 10=C, or 11=D
S1S0
S1S0
i0i1i2…/o0o1o2…

## Slide 11: Mealy Machine
Next State
Current State
Input
Output
Registers
Comb. Logic
General Case: Mealy Machine
Outputs and next state depend on both current state and input

## Slide 12: Moore Machine
Next State
Current State
Input
Output
Registers
Comb. Logic
Comb. Logic
Special Case: Moore Machine
Outputs depend only on current state

## Slide 13: Moore Machine FSM Example
Legend
input
A
off
B
on
C
off
D
off
down
up
down
down
up
down
up
up
Input: up or down
Output: on or off
States: A, B, C, or D
state out
startout

## Slide 14: Mealy Machine FSM Example
Legend
state
input/output
start state
A
B
C
D
down/on
up/off
down/on
down/off
up/off
down/off
up/off
up/off
Input: up or down
Output: on or off
States: A, B, C, or D

## Slide 15: Activity#2: Create a Logic Circuit for a Serial Adder
Add two infinite input bit streams
  streams are sent with least-significant-bit (lsb) first
…10110
…01111
…00101
Sum: output
Notes: Ask as a clicker question

## Slide 16: Activity#2: Create a Logic Circuit for a Serial Adder
Add two infinite input bit streams
  streams are sent with least-significant-bit (lsb) first
…10110
…01111
…00101
Sum: output
Carry-out
1

## Slide 17: Activity#2: Create a Logic Circuit for a Serial Adder
Add two infinite input bit streams
  streams are sent with least-significant-bit (lsb) first
…10110
…01111
…00101
Sum: output
Carry-in
1

## Slide 18: Activity#2: Create a Logic Circuit for a Serial Adder
Add two infinite input bit streams
  streams are sent with least-significant-bit (lsb) first
…10110
…01111
…00101
Sum: output
Carry-out
1
1

## Slide 19: iClicker Question
Add two infinite input bit streams
  streams are sent with least-significant-bit (lsb) first
…10110
…01111
…00101
How many states are needed to represent FSM
0
1
2
3
4
Notes: Ask as a clicker question

## Slide 20: Strategy for Building an FSM
(1) Draw a state diagram (e.g. Mealy Machine)
(2) Write output and next-state tables
(3) Encode states, inputs, and outputs as bits
(4) Determine logic equations for next state and outputs
(5) Draw the Circuit

## Slide 21: FSM: State Diagram
2 states ___ and ___
Inputs: ___ and ___
Output: ___
…10110
…01111
…00101
Notes: Is this a mealy or moore machine, maybe clicker

## Slide 22: FSM: State Diagram
…10110
…01111
…00101
a
b
z
Two states: S0 (no carry in), S1 (carry in)
Inputs: a and b
Output: z
  z is the sum of inputs a, b, and carry-in (one bit at a time)
  A carry-out is the next carry-in state.

## Slide 23: FSM: State Diagram
…10110
…01111
…00101
a
b
z
Two states: S0 (no carry in), S1 (carry in)
Inputs: a and b
Output: z
  z is the sum of inputs a, b, and carry-in (one bit at a time)
  A carry-out is the next carry-in state.
  Arcs labeled with input bits a and b, and output z
S0
S1
__/_
__/_
__/_
__/_
__/_
__/_
__/_
__/_

## Slide 24: FSM: State Diagram
…10110
…01111
…00101
a
b
z
Two states: S0 (no carry in), S1 (carry in)
Inputs: a and b
Output: z
  z is the sum of inputs a, b, and carry-in (one bit at a time)
  A carry-out is the next carry-in state.
  Arcs labeled with input bits a and b, and output z
S0
S1
00/0
11/1
01/0
11/0
10/0
10/1
00/1
01/1

## Slide 25: iClicker Question
S0
S1
00/0
11/1
01/0
11/0
10/0
10/1
00/1
01/1
Is this a Moore or Mealy Machine?
Moore
Mealy
Cannot be determined

## Slide 26: iClicker Question
S0
S1
00/0
11/1
01/0
11/0
10/0
10/1
00/1
01/1
Is this a Moore or Mealy Machine?
Moore
Mealy
Cannot be determined

## Slide 27: Serial Adder: State Table
S0
S1
00/0
11/1
01/0
11/0
10/0
10/1
00/1
01/1
a | b | Current state | z | Next state
(2) Write down all input and state combinations

## Slide 28: Serial Adder: State Table
S0
S1
00/0
11/1
01/0
11/0
10/0
10/1
00/1
01/1
a | b | Current state | z | Next state
0 | 0 | S0 | 0 | S0
0 | 1 | S0 | 1 | S0
1 | 0 | S0 | 1 | S0
1 | 1 | S0 | 0 | S1
0 | 0 | S1 | 1 | S0
0 | 1 | S1 | 0 | S1
1 | 0 | S1 | 0 | S1
1 | 1 | S1 | 1 | S1
(2) Write down all input and state combinations

## Slide 29: Serial Adder: State Assignment
S0
S1
00/0
11/1
01/0
11/0
10/0
10/1
00/1
01/1
(3) Encode states, inputs, and outputs as bits
Two states, so 1-bit is sufficient
  A single flip-flop will encode the state
a | b | s | z | s'
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 30: Serial Adder: Circuit
a | b | s | z | s'
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
(4) Determine logic equations for next state and outputs
Combinational Logic Equations
  z = b + a + s + abs
  s’ = ab + bs + as + abs
Next State
Current State
Input
Output
a
b
D
Q
s
z
s'
s'
Next State

## Slide 31: Serial Adder: Circuit
a | b | s | z | s'
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
(4) Determine logic equations for next state and outputs
Combinational Logic Equations
  z = b + a + s + abs
  s’ = ab + bs + as + abs
Next State
Current State
Input
Output
a
b
D
Q
s
z
s'
s'
Next State
Comb. Logic

## Slide 32: Sequential Logic Circuits
Next State
Current State
Input
Output
a
b
D
Q
s
z
s'
s'
Next State
Comb. Logic
Strategy:
(1) Draw a state diagram (e.g. Mealy Machine)
(2) Write output and next-state tables
(3) Encode states, inputs, and outputs as bits
(4) Determine logic equations for next state and outputs
  z = b + a + s + abs
  s’ = ab + bs + as + abs

## Slide 33: Which statement(s) is true
(A) In a Moore Machine output depends on both current state and input
(B) In a Mealy Machine output depends on both current state and input
(C) In a Mealy Machine output depends on next state and input (D) All the above are true
(E) None are true

## Slide 34: Which statement(s) is true
(A) In a Moore Machine output depends on both current state and input
(B) In a Mealy Machine output depends on both current state and input
(C) In a Mealy Machine output depends on next state and input (D) All the above are true
(E) None are true

## Slide 35: Mealy Machine
Next State
Current State
Input
Output
Registers
Comb. Logic
General Case: Mealy Machine
Outputs and next state depend on both current state and input

## Slide 36: Moore Machine
Next State
Current State
Input
Output
Registers
Comb. Logic
Comb. Logic
Special Case: Moore Machine
Outputs depend only on current state

## Slide 37: Example: Digital Door Lock
Digital Door Lock
Inputs:
  keycodes from keypad
  clock
Outputs:
  “unlock” signal
  display how many keys pressed so far

## Slide 38: Door Lock: Inputs
Assumptions:
  signals are synchronized to clock
  Password is B-A-B
K
A
B
K | A | B | Meaning
0 | 0 | 0 | Ø (no key)
1 | 1 | 0 | ‘A’ pressed
1 | 0 | 1 | ‘B’ pressed

## Slide 39: Door Lock: Outputs
Assumptions:
  High pulse on U unlocks door
U
D3D2D1D0
4
LED dec
8
Strategy:
(1) Draw a state diagram (e.g. Moore Machine)
(2) Write output and next-state tables
(3) Encode states, inputs, and outputs as bits
(4) Determine logic equations for next state and outputs

## Slide 40: Door Lock: Simplified State Diagram
(1) Draw a state diagram (e.g. Moore Machine)

## Slide 41: Door Lock: Simplified State Diagram
Idle
G1
”0”
Ø
G2
G3
B1
B2
”1”
”2”
”3”, U
”1”
”2”
Ø
Ø
Ø
Ø
“B”
“A”
“B”
else
else
any
any
else
else
B3
”3”
else
(1) Draw a state diagram (e.g. Moore Machine)

## Slide 42: Door Lock: Simplified State Diagram
Idle
G1
”0”
Ø
G2
G3
B1
B2
”1”
”2”
”3”, U
”1”
”2”
Ø
Ø
Ø
Ø
“B”
“A”
“B”
else
else
any
else
(1) Draw a state diagram (e.g. Moore Machine)
else
else

## Slide 43: Door Lock: Simplified State Diagram
Idle
G1
”0”
Ø
G2
G3
B1
B2
”1”
”2”
”3”, U
”1”
”2”
Ø
Ø
Ø
Ø
“B”
“A”
“B”
else
else
any
else
else
else
Cur. State | Output
Idle | “0”
G1 | “1”
G2 | “2”
G3 | “3”, U
B1 | “1”
B2 | “2”
(2) Write output and next-state tables

## Slide 44: Door Lock: Simplified State Diagram
Idle
G1
”0”
Ø
G2
G3
B1
B2
”1”
”2”
”3”, U
”1”
”2”
Ø
Ø
Ø
Ø
“B”
“A”
“B”
else
else
any
else
else
else
(2) Write output and next-state tables
Cur. State | Input | Next State
Idle | Ø | Idle
Idle | “B” | G1
Idle | “A” | B1
G1 | Ø | G1
G1 | “A” | G2
G1 | “B” | B2
G2 | Ø | G2
G2 | “B” | G3
G2 | “A” | Idle
G3 | any | Idle
B1 | Ø | B1
B1 | K | B2
B2 | Ø | B2
B2 | K | Idle

## Slide 45: State Table Encoding
(3) Encode states, inputs, and outputs as bits
Cur. State | Output
Idle | “0”
G1 | “1”
G2 | “2”
G3 | “3”, U
B1 | “1”
B2 | “2”
U
D3D2D1D0
4
dec
8
D3 | D2 | D1 | D0 | U
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
K
A
B
S2 | S1 | S0
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
K | A | B | Meaning
0 | 0 | 0 | Ø (no key)
1 | 1 | 0 | ‘A’ pressed
1 | 0 | 1 | ‘B’ pressed
State | S2 | S1 | S0
Idle | 0 | 0 | 0
G1 | 0 | 0 | 1
G2 | 0 | 1 | 0
G3 | 0 | 1 | 1
B1 | 1 | 0 | 0
B2 | 1 | 0 | 1
Cur. State | Input | Next State
Idle | Ø | Idle
Idle | “B” | G1
Idle | “A” | B1
G1 | Ø | G1
G1 | “A” | G2
G1 | “B” | B2
G2 | Ø | B2
G2 | “B” | G3
G2 | “A” | Idle
G3 | any | Idle
B1 | Ø | B1
B1 | K | B2
B2 | Ø | B2
B2 | K | Idle
S2 | S1 | S0 |  | S’2 | S’1 | S’0
0 | 0 | 0 |  | 0 | 0 | 0
0 | 0 | 0 |  | 0 | 0 | 1
0 | 0 | 0 |  | 1 | 0 | 0
0 | 0 | 1 |  | 0 | 0 | 1
0 | 0 | 1 |  | 0 | 1 | 0
0 | 0 | 1 |  | 1 | 0 | 1
0 | 1 | 0 |  | 0 | 1 | 0
0 | 1 | 0 |  | 0 | 1 | 1
0 | 1 | 0 |  | 0 | 0 | 0
0 | 1 | 1 |  | 0 | 0 | 0
1 | 0 | 0 |  | 1 | 0 | 0
1 | 0 | 0 |  | 1 | 0 | 1
1 | 0 | 1 |  | 1 | 0 | 1
1 | 0 | 1 |  | 0 | 0 | 0
K | A | B
0 | 0 | 0
1 | 0 | 1
1 | 1 | 0
0 | 0 | 0
1 | 1 | 0
1 | 0 | 1
0 | 0 | 0
1 | 0 | 1
1 | 1 | 0
x | x | x
0 | 0 | 0
1 | x | x
0 | 0 | 0
1 | x | x

## Slide 46: Door Lock: Implementation
4
dec
3bit Reg
clk
U
D3-0
S2-0
S’2-0
S2-0
K
A
B
D3 | D2 | D1 | D0 | U
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
S2 | S1 | S0
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
(4) Determine logic equations for next state and outputs
U = S1S0
D0 = S0 + S1S0 + S2
D1 = S1S0 + S1S0 + S1S0

## Slide 47: Door Lock: Implementation
4
dec
3bit Reg
clk
U
D3-0
S2-0
S’2-0
S2-0
K
A
B
S2 | S1 | S0 |  | S’2 | S’1 | S’0
0 | 0 | 0 |  | 0 | 0 | 0
0 | 0 | 0 |  | 0 | 0 | 1
0 | 0 | 0 |  | 1 | 0 | 0
0 | 0 | 1 |  | 0 | 0 | 1
0 | 0 | 1 |  | 0 | 1 | 0
0 | 0 | 1 |  | 1 | 0 | 1
0 | 1 | 0 |  | 0 | 1 | 0
0 | 1 | 0 |  | 0 | 1 | 1
0 | 1 | 0 |  | 0 | 0 | 0
0 | 1 | 1 |  | 0 | 0 | 0
1 | 0 | 0 |  | 1 | 0 | 0
1 | 0 | 0 |  | 1 | 0 | 1
1 | 0 | 1 |  | 1 | 0 | 1
1 | 0 | 1 |  | 0 | 0 | 0
K | A | B
0 | 0 | 0
1 | 0 | 1
1 | 1 | 0
0 | 0 | 0
1 | 1 | 0
1 | 0 | 1
0 | 0 | 0
1 | 0 | 1
1 | 1 | 0
x | x | x
0 | 0 | 0
1 | x | x
0 | 0 | 0
1 | x | x
S0’ = ?
S1’ = ?
S2’ = KA + S0KB + S2 + S1S0K + S2 S0

## Slide 48: Door Lock: Implementation
4
dec
3bit Reg
clk
U
D3-0
S2-0
S’2-0
S2-0
K
A
B
Strategy:
(1) Draw a state diagram (e.g. Moore Machine)
(2) Write output and next-state tables
(3) Encode states, inputs, and outputs as bits
(4) Determine logic equations for next state and outputs

## Slide 49: Door Lock: Implementation
Strategy:
(1) Draw a state diagram (e.g. Moore Machine)
(2) Write output and next-state tables
(3) Encode states, inputs, and outputs as bits
(4) Determine logic equations for next state and outputs
Next State
Current State
Input
Output
Registers
Comb. Logic
Comb. Logic

## Slide 50: Summary
We can now build interesting devices with sensors
  Using combinational logic
We can also store data values
  Stateful circuit elements (D Flip Flops, Registers, …)
  State Machines or Ad-Hoc Circuits