## Slide 1: Finite State Machines
Hakim Weatherspoon
CS 3410
Computer Science
Cornell University
[Weatherspoon, Bala, Bracy, McKee, and Sirer]

## Slide 2: Stateful Components
Combinationial logic
  Output computed directly from inputs
  System has no internal state
  Nothing depends on the past!
Need:
  To record data
  To build stateful circuits
  A state-holding device
  Sequential Logic & Finite State Machines
Inputs
Combinational circuit
Outputs
N
M
Notes: How are we going to stably store state

## Slide 3: Goals for Today
Finite State Machines (FSM)
  How do we design logic circuits with state?
  Types of FSMs: Mealy and Moore Machines
  Examples: Serial Adder and a Digital Door Lock

## Slide 4: Next Goal
How do we design logic circuits with state?

## Slide 5: Finite State Machines

## Slide 6: Finite State Machines
An electronic machine which has
  external inputs
  externally visible outputs
  internal state
Output and next state depend on
  inputs
  current state

## Slide 7: Abstract Model of FSM
Machine is
M = (S, I, O,  )
S: Finite set of states
I: Finite set of inputs
O: Finite set of outputs
: State transition function
Next state depends on present input and present state

## Slide 8: Automata Model
Finite State Machine
  inputs from external world
  outputs to external world
  internal state
  combinational logic
Next State
Current State
Input
Output
Registers
Comb. Logic
Notes: Put sequential logic term on slide

## Slide 9: FSM Example
Legend
state
input/output
start state
A
B
C
D
down/on
up/off
down/on
down/off
up/off
down/off
up/off
up/off
Input: up or down
Output: on or off
States: A, B, C, or D

## Slide 10: FSM Example
Legend
00
01
10
11
1/1
0/0
1/1
1/0
0/1
1/0
0/0
0/0
Input: 0=up or 1=down
Output: 1=on or 0=off
States: 00=A, 01=B, 10=C, or 11=D
S1S0
S1S0
i0i1i2…/o0o1o2…

## Slide 11: Mealy Machine
Next State
Current State
Input
Output
Registers
Comb. Logic
General Case: Mealy Machine
Outputs and next state depend on both current state and input

## Slide 12: Moore Machine
Next State
Current State
Input
Output
Registers
Comb. Logic
Comb. Logic
Special Case: Moore Machine
Outputs depend only on current state

## Slide 13: Moore Machine FSM Example
Legend
input
A
off
B
on
C
off
D
off
down
up
down
down
up
down
up
up
Input: up or down
Output: on or off
States: A, B, C, or D
state out
startout

## Slide 14: Mealy Machine FSM Example
Legend
state
input/output
start state
A
B
C
D
down/on
up/off
down/on
down/off
up/off
down/off
up/off
up/off
Input: up or down
Output: on or off
States: A, B, C, or D

## Slide 15: Activity#2: Create a Logic Circuit for a Serial Adder
Add two infinite input bit streams
  streams are sent with least-significant-bit (lsb) first
  How many states are needed to represent FSM?
  Draw and Fill in FSM diagram
…10110
…01111
…00101
Sum: output
Strategy:
(1) Draw a state diagram (e.g. Mealy Machine)
(2) Write output and next-state tables
(3) Encode states, inputs, and outputs as bits
(4) Determine logic equations for next state and outputs
Notes: Ask as a clicker question

## Slide 16: Activity#2: Create a Logic Circuit for a Serial Adder
Add two infinite input bit streams
  streams are sent with least-significant-bit (lsb) first
…10110
…01111
…00101
Sum: output
Notes: Ask as a clicker question

## Slide 17: Strategy for Building an FSM
(1) Draw a state diagram (e.g. Mealy Machine)
(2) Write output and next-state tables
(3) Encode states, inputs, and outputs as bits
(4) Determine logic equations for next state and outputs
(5) Draw the Circuit

## Slide 18: FSM: State Diagram
2 states ___ and ___
Inputs: ___ and ___
Output: ___
…10110
…01111
…00101
Notes: Is this a mealy or moore machine, maybe clicker

## Slide 19: FSM: State Diagram
…10110
…01111
…00101
a
b
z
S0
S1
__/_
__/_
__/_
__/_
__/_
__/_
__/_
__/_
2 states ___ and ___
Inputs: ___ and ___
Output: ___

## Slide 20: Serial Adder: State Table
a | b | Current state | z | Next state
(2) Write down all input and state combinations
S0
S1
__/_
__/_
__/_
__/_
__/_
__/_
__/_
__/_

## Slide 21: Serial Adder: State Table
a | b | Current state | z | Next state
S0
S1
__/_
__/_
__/_
__/_
__/_
__/_
__/_
__/_
(3) Encode states, inputs, and outputs as bits

## Slide 22: Serial Adder: State Assignment
a | b | s | z | s'
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
S0
S1
__/_
__/_
__/_
__/_
__/_
__/_
__/_
__/_
(4) Determine logic equations for next state and outputs

## Slide 23: Serial Adder: State Assignment
a | b | s | z | s'
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
(4) Determine logic equations for next state and outputs

## Slide 24: Example: Digital Door Lock
Digital Door Lock
Inputs:
  keycodes from keypad
  clock
Outputs:
  “unlock” signal
  display how many keys pressed so far

## Slide 25: Door Lock: Inputs
Assumptions:
  signals are synchronized to clock
  Password is B-A-B
K
A
B
K | A | B | Meaning
0 | 0 | 0 | Ø (no key)
1 | 1 | 0 | ‘A’ pressed
1 | 0 | 1 | ‘B’ pressed

## Slide 26: Door Lock: Outputs
Assumptions:
  High pulse on U unlocks door
U
D3D2D1D0
4
LED dec
8
Strategy:
(1) Draw a state diagram (e.g. Moore Machine)
(2) Write output and next-state tables
(3) Encode states, inputs, and outputs as bits
(4) Determine logic equations for next state and outputs

## Slide 27: Door Lock: Simplified State Diagram
(1) Draw a state diagram (e.g. Moore Machine)

## Slide 28: Door Lock: Simplified State Diagram
Cur. State | Output
(2) Write output and next-state tables

## Slide 29: Door Lock: Simplified State Diagram
(2) Write output and next-state tables
Cur. State | Input | Next State

## Slide 30: Door Lock: Implementation
4
dec
3bit Reg
clk
U
D3-0
S2-0
S’2-0
S2-0
K
A
B
D3 | D2 | D1 | D0 | U
S2 | S1 | S0
(4) Determine logic equations for next state and outputs

## Slide 31: Door Lock: Implementation
4
dec
3bit Reg
clk
U
D3-0
S2-0
S’2-0
S2-0
K
A
B
S2 | S1 | S0 |  | S’2 | S’1 | S’0
K | A | B
(4) Determine logic equations for next state and outputs

## Slide 32: Door Lock: Implementation
4
dec
3bit Reg
clk
U
D3-0
S2-0
S’2-0
S2-0
K
A
B
Strategy:
(1) Draw a state diagram (e.g. Moore Machine)
(2) Write output and next-state tables
(3) Encode states, inputs, and outputs as bits
(4) Determine logic equations for next state and outputs

## Slide 33: Door Lock: Implementation
Strategy:
(1) Draw a state diagram (e.g. Moore Machine)
(2) Write output and next-state tables
(3) Encode states, inputs, and outputs as bits
(4) Determine logic equations for next state and outputs
Next State
Current State
Input
Output
Registers
Comb. Logic
Comb. Logic

## Slide 34: Summary
We can now build interesting devices with sensors
  Using combinational logic
We can also store data values
  Stateful circuit elements (D Flip Flops, Registers, …)
  State Machines or Ad-Hoc Circuits