## Slide 1
The RISC-V Processor
Hakim Weatherspoon
CS 3410
Computer Science
Cornell University
[Weatherspoon, Bala, Bracy, and Sirer]

## Slide 2: Announcements
Check online syllabus/schedule
http://www.cs.cornell.edu/Courses/CS3410/2019sp/schedule
Slides and Reading for lectures
Office Hours
Pictures of all TAs
Dates to keep in Mind
  Prelims: Tue Mar 5th and Thur May 2nd
  Proj 1: Due next Friday, Feb 15th
  Proj3: Due before Spring break
  Final Project: Due when final will be Feb 16th
Schedule is subject to change

## Slide 3: Collaboration, Late, Re-grading Policies
“White Board” Collaboration Policy
  Can discuss approach together on a “white board”
  Leave, watch a movie such as Stranger Things, then write up solution independently
  Do not copy solutions
  Late Policy
  Each person has a total of four “slip days”
  Max of two slip days for any individual assignment
  Slip days deducted first for any late assignment,
  cannot selectively apply slip days
  For projects, slip days are deducted from all partners
  25% deducted per day late after slip days are exhausted
  Regrade policy
  Submit written request within a week of receiving score

## Slide 4: Big Picture: Building a Processor
PC
imm
memory
target
offset
cmp
control
=?
new pc
memory
din
dout
addr
register file
inst
extend
A single cycle processor
alu
+4
+4

## Slide 5: Goal for the next 2 lectures
Understanding the basics of a processor
  We now have the technology to build a CPU!
Putting it all together:
  Arithmetic Logic Unit (ALU)
  Register File
  Memory
    SRAM: cache
    DRAM: main memory
  RISC-V Instructions & how they are executed
5

## Slide 6: RISC-V Register File
PC
imm
memory
target
offset
cmp
control
=?
new pc
memory
din
dout
addr
register file
inst
extend
alu
+4
+4
A single cycle processor

## Slide 7: RISC-V Register File
RISC-V register file
  32 registers, 32-bits each
  x0 wired to zero
  Write port indexed via RW
    on falling edge when WE=1
  Read ports indexed via RA, RB
Dual-Read-Port Single-Write-Port
32 x 32 Register File
QA
QB
DW
RW
RA
RB
WE
32
32
32
1
5
5
5

## Slide 8: RISC-V Register File
RISC-V register file
  32 registers, 32-bits each
  x0 wired to zero
  Write port indexed via RW
    on falling edge when WE=1
  Read ports indexed via RA, RB
RISC-V register file
  Numbered from 0 to 31
  Can be referred by number: x0, x1, x2, … x31
  Convention, each register also has a name:
    x10 – x17  a0 – a7, x28 – x31  t3 – t6
A
B
W
RW
RA
RB
WE
32
32
32
1
5
5
5
x0
x1
…
x31

## Slide 9: iClicker Question
If we wanted to support 64 registers, what would change?
  W, A, B → 64
  RW, RA, RB 5 → 6
  W 32 → 64, RW 5 → 6
  A & B only
A
B
W
RW
RA
RB
WE
32
32
32
1
5
5
5
x0
x1
…
x31

## Slide 10: iClicker Question
If we wanted to support 64 registers, what would change?
  W, A, B → 64
  RW, RA, RB 5 → 6
  W 32 → 64, RW 5 → 6
  A & B only
A
B
W
RW
RA
RB
WE
32
32
32
1
5
5
5
x0
x1
…
x31

## Slide 11: RISC-V Memory
PC
imm
memory
target
offset
cmp
control
=?
new pc
memory
din
dout
addr
register file
inst
extend
alu
+4
+4
A single cycle processor

## Slide 12: RISC-V Memory
32-bit address
32-bit data (but byte addressed)
Enable + 2 bit memory control (mc)
  00: read word (4 byte aligned)
  01: write byte
  10: write halfword (2 byte aligned)
  11: write word (4 byte aligned)
memory
32
addr
2
mc
32
32
E
Din
Dout
 | 0x000fffff
 | . . .
 | 0x0000000b
 | 0x0000000a
 | 0x00000009
 | 0x00000008
 | 0x00000007
 | 0x00000006
 | 0x00000005
 | 0x00000004
 | 0x00000003
 | 0x00000002
 | 0x00000001
 | 0x00000000
0x05
1 byte
address

## Slide 13: Putting it all together: Basic Processor
PC
imm
memory
target
offset
cmp
control
=?
new pc
memory
din
dout
addr
register file
inst
extend
alu
+4
+4
A single cycle processor

## Slide 14: To make a computer
Need a program
Stored program computer
Architectures
von Neumann architecture
Harvard (modified) architecture

## Slide 15: To make a computer
Need a program
Stored program computer
(a Universal Turing Machine)
Architectures
von Neumann architecture
Harvard (modified) architecture
Notes: A stored-program computer is one which stores program instructions in electronic memory. Often the definition is extended with the requirement that the treatment of programs and data in
http://en.wikipedia.org/wiki/Universal_Turing_machine#Stored-program_computer
Davis makes a persuasive argument that Turing's conception of what is now known as "the stored-program computer", of placing the "action table"—the instructions for the machine—in the same "memory" as the input data, strongly influenced John von Neumann's conception of the first American discrete-symbol (as opposed to analog) computer—the EDVAC (Electronic Discrete Variable Automatic Computer) [previous machine, ENIAC (Electronic Numerical Integrator And Computer), was not a stored-program computer, and was not even in binary, it was in decimal].
See video on von Neumann describe the stored-program computer, 34 minutes into video, https://www.youtube.com/watch?v=VTS9O0CoVng
Also, see clip on Turing in the movie The Imitation Game where Turing states that the Bombe will work in breaking the Enigma machine: https://www.youtube.com/watch?v=MM47hsaYWZE

## Slide 16: Putting it all together: Basic Processor
A RISC-V CPU with a (modified) Harvard architecture
  Modified: instructions & data in common address space, separate instr/data caches can be accessed in parallel
CPU
Registers
Data Memory
data, address,
control
ALU
Control
00100000001
00100000010
00010000100
...
Program Memory
10100010000
10110000011
00100010101
...
Notes: The Harvard architecture is a computer architecture with physically separate storage and signal pathways for instructions and data. --- http://en.wikipedia.org/wiki/Harvard_architecture
Under pure von Neumann architecture the CPU can be either reading an instruction or reading/writing data from/to the memory. Both cannot occur at the same time since the instructions and data use the same bus system. In a computer using the Harvard architecture, the CPU can both read an instruction and perform a data memory access at the same time, even without a cache. A Harvard architecture computer can thus be faster for a given circuit complexity because instruction fetches and data access do not contend for a single memory pathway .
Also, a Harvard architecture machine has distinct code and data address spaces: instruction address zero is not the same as data address zero. Instruction address zero might identify a twenty-four bit value, while data address zero might indicate an eight bit byte that isn't part of that twenty-four bit value.
A modified Harvard architecture machine is very much like a Harvard architecture machine, but it relaxes the strict separation between instruction and data while still letting the CPU concurrently access two (or more) memory buses. The most common modification includes separate instruction and data caches backed by a common address space. While the CPU executes from cache, it acts as a pure Harvard machine. When accessing backing memory, it acts like a von Neumann machine (where code can be moved around like data, a powerful technique). This modification is widespread in modern processors such as the ARM architecture and X86 processors. It is sometimes loosely called a Harvard architecture, overlooking the fact that it is actually "modified".

## Slide 17: Takeaway
A processor executes instructions
  Processor has some internal state in storage elements (registers)
A memory holds instructions and data
  (modified) Harvard architecture: separate insts and data
  von Neumann architecture: combined inst and data
A bus connects the two
  We now have enough building blocks to build machines that can perform non-trivial computational tasks

## Slide 18: Next Goal
How to program and execute instructions on a RISC-V processor?

## Slide 19: Instruction Usage
Instructions are stored in memory, encoded in binary
A basic processor
  fetches
  decodes
  executes
  one instruction at a time
pc
adder
cur inst
decode
regs
execute
addr
data
00000000101000010000000000010011
00100000000000010000000000010000
00000000001000100001100000101010
10 x2 x0 op=addi

## Slide 20: Instruction Processing
A basic processor
  fetches
  decodes
  executes
one instruction at a time
00100000000000100000000000001010
00100000000000010000000000000000
00000000001000100001100000101010
5
ALU
5
5
control
Reg. File
PC
Prog
Mem
inst
+4
Data
Mem
Instructions:
stored in memory, encoded in binary

## Slide 21: Levels of Interpretation: Instructions
High Level Language
  C, Java, Python, ADA, …
  Loops, control flow, variables
for (i = 0; i < 10; i++) printf(“go cucs”);
main: addi x2, x0, 10
addi x1, x0, 0
loop: slt x3, x1, x2
...
Assembly Language
  No symbols (except labels)
  One operation per statement
  “human readable machine language”
Machine Language
  Binary-encoded assembly
  Labels become addresses
  The language of the CPU
ALU, Control, Register File, …
Machine Implementation
(Microarchitecture)
Instruction Set Architecture
00000000101000010000000000010011
00100000000000010000000000010000
00000000001000100001100000101010
10 x2 x0 op=addi

## Slide 22: Instruction Set Architecture (ISA)
Different CPU architectures specify different instructions
Two classes of ISAs
  Reduced Instruction Set Computers (RISC)
  IBM Power PC, Sun Sparc, MIPS, Alpha
  Complex Instruction Set Computers (CISC)
  Intel x86, PDP-11, VAX
Another ISA classification: Load/Store Architecture
  Data must be in registers to be operated on
  For example: array[x] = array[y] + array[z]
  1 add ? OR 2 loads, an add, and a store ?
  Keeps HW simple  many RISC ISAs are load/store

## Slide 23: iClicker Question
What does it mean for an architecture to be called a load/store architecture?
Load and Store instructions are supported by the ISA.
Load and Store instructions can also perform arithmetic instructions on data in memory.
Data must first be loaded into a register before it can be operated on.
Every load must have an accompanying store at some later point in the program.

## Slide 24: iClicker Question
What does it mean for an architecture to be called a load/store architecture?
Load and Store instructions are supported by the ISA.
Load and Store instructions can also perform arithmetic instructions on data in memory.
Data must first be loaded into a register before it can be operated on.
Every load must have an accompanying store at some later point in the program.

## Slide 25: Takeaway
A RISC-V processor and ISA (instruction set architecture) is an example a Reduced Instruction Set Computers (RISC) where simplicity is key, thus enabling us to build it!!

## Slide 26: Next Goal
How are instructions executed?
What is the general datapath to execute an instruction?

## Slide 27: Five Stages of RISC-V Datapath
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
Fetch
Decode
Execute
Memory
WB
A single cycle processor – this diagram is not 100% spatial

## Slide 28: Five Stages of RISC-V Datapath
Basic CPU execution loop
  Instruction Fetch
  Instruction Decode
  Execution (ALU)
  Memory Access
  Register Writeback

## Slide 29: Stage 1: Instruction Fetch
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
  Fetch 32-bit instruction from memory
  Increment PC = PC + 4
Fetch
Decode
Execute
Memory
WB

## Slide 30: Stage 2: Instruction Decode
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
  Gather data from the instruction
  Read opcode; determine instruction type, field lengths
  Read in data from register file
  (0, 1, or 2 reads for jump, addi, or add, respectively)
Fetch
Decode
Execute
Memory
WB

## Slide 31: Stage 3: Execution (ALU)
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
  Useful work done here (+, -, *, /), shift, logic operation, comparison (slt)
  Load/Store? lw x2, x3, 32  Compute address
Fetch
Decode
Execute
Memory
WB

## Slide 32: Stage 4: Memory Access
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
  Used by load and store instructions only
  Other instructions will skip this stage
R/W
addr
Data
Data
Fetch
Decode
Execute
Memory
WB

## Slide 33: Stage 5: Writeback
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
  Write to register file
  For arithmetic ops, logic, shift, etc, load. What about stores?
  Update PC
  For branches, jumps
Fetch
Decode
Execute
Memory
WB

## Slide 34: iClicker Question
Which of the following statements is true?
All instructions require an access to Program Memory.
All instructions require an access to Data Memory.
All instructions write to the register file.
Some RISC-V instructions are shorter than 32 bits.
A & C

## Slide 35: iClicker Question
Which of the following statements is true?
All instructions require an access to Program Memory.
All instructions require an access to Data Memory.
All instructions write to the register file.
Some RISC-V instructions are shorter than 32 bits.
A & C

## Slide 36: Takeaway
The datapath for a RISC-V processor has five stages:
  Instruction Fetch
  Instruction Decode
  Execution (ALU)
  Memory Access
  Register Writeback
This five stage datapath is used to execute all RISC-V instructions

## Slide 37: Next Goal
Specific datapaths RISC-V Instructions

## Slide 38: RISC-V Design Principles
Simplicity favors regularity
  32 bit instructions
Smaller is faster
  Small register file
Make the common case fast
  Include support for constants
Good design demands good compromises
  Support for different type of interpretations/classes

## Slide 39: Instruction Types
Arithmetic
  add, subtract, shift left, shift right, multiply, divide
Memory
  load value from memory to a register
  store value to memory from a register
Control flow
  conditional jumps (branches)
  jump and link (subroutine call)
Many other instructions are possible
  vector add/sub/mul/div, string operations
  manipulate coprocessor
  I/O

## Slide 40: RISC-V Instruction Types
Arithmetic/Logical
  R-type: result and two source registers, shift amount
  I-type: result and source register, shift amount in 16-bit immediate with sign/zero extension
  U-type: result register, 16-bit immediate with sign/zero extension
Memory Access
  I-type for loads and S-type for stores
  load/store between registers and memory
  word, half-word and byte operations
Control flow
  UJ-type: jump-and-link
  I-type: jump-and-link register
  SB-type: conditional branches: pc-relative addresses

## Slide 41: RISC-V instruction formats
All RISC-V instructions are 32 bits long, have 4 formats
R-type
I-type
S-type
(SB-type)
U-type
(UJ-type)
31 25 | 24 20 | 19 15 | 14 12 | 11 7 | 6 0
funct7 | rs2 | rs1 | Funct3 | Rd | op
7 bits | 5 bits | 5 bits | 3 bits | 5 bits | 7 bits
31 | 20 | 19 15 | 14 12 | 11 7 | 6 0
imm |  | Rs1 | Funct3 | rd | op
12 bits |  | 5 bits | 3 bits | 5 bits | 7 bits
31 25 | 24 20 | 19 15 | 14 12 | 11 7 | 6 0
imm | rs2 | rs1 | funct3 | imm | Op
7 bits | 5 bits | 5 bits | 3 bits | 5 bits | 7 bits
31 |  |  | 12 | 11 7 | 6 0
imm |  |  |  | rd | op
20 bits |  |  |  | 5 bits | 7 bits
Notes: See Figure 2.18 in the book for RISC-V instruction encoding. Also, see the one page RISC-V Reference Data sheet and reference from 4750: https://www.csl.cornell.edu/courses/ece4750/handouts/ece4750-tinyrv-isa.txt
R-type – ADD, SUB, SLL, XOR, SRL, OR, AND,
– LR.W, SC.W, LR.D, SC.D
I-type – ADDI, SLLI, XORI, SRLI, SRAI, ORI, ANDI
– LB, LH, LW, LD, LBU, LHU, LWU
– JALR
S-type – SB, SH, SW, SD
SB-type – BEQ, BNE, BLT, BGE, BLTU, BGEU
U-type – LUI
UJ-type - JAL

## Slide 42: R-Type (1): Arithmetic and Logic
op | funct3 | mnemonic | description
0110011 | 000 | ADD rd, rs1, rs2 | R[rd] = R[rs1] + R[rs2]
0110011 | 000 | SUB rd, rs1, rs2 | R[rd] = R[rs1] – R[rs2]
0110011 | 110 | OR rd, rs1, rs2 | R[rd] = R[rs1] ¦ R[rs2]
0110011 | 100 | XOR rd, rs1, rs2 | R[rd] = R[rs1]  R[rs2]
00000000011001000100001000110011
31 | 25 24 | 20 19 | 15 14 12 11 | 7 6 | 0
funct7 | rs2 | rs1 | Funct3 | Rd | op
7 bits | 5 bits | 5 bits | 3 bits | 5 bits | 7 bits
Notes: ADD and SUB have the same funct3, 000, but funct7 differs between the two, 0000000 vs 0100000, respectively

## Slide 43: R-Type (1): Arithmetic and Logic
op | funct3 | mnemonic | description
0110011 | 000 | ADD rd, rs1, rs2 | R[rd] = R[rs1] + R[rs2]
0110011 | 000 | SUB rd, rs1, rs2 | R[rd] = R[rs1] – R[rs2]
0110011 | 110 | OR rd, rs1, rs2 | R[rd] = R[rs1] ¦ R[rs2]
0110011 | 100 | XOR rd, rs1, rs2 | R[rd] = R[rs1]  R[rs2]
Example: x4 = x8  x6 # XOR x4, x8, x6
rd, rs1, rs2
00000000011001000100001000110011
31 | 25 24 | 20 19 | 15 14 12 11 | 7 6 | 0
funct7 | rs2 | rs1 | Funct3 | Rd | op
7 bits | 5 bits | 5 bits | 3 bits | 5 bits | 7 bits

## Slide 44: Arithmetic and Logic
Fetch
Decode
Execute
Memory
WB
skip
ALU
PC
Prog.
Mem
+4
5
5
5
Reg. File
control
XOR x4, x8, x6
x8  x6
Example: x4 = x8  x6 # XOR x4, x8, x6
rd, rs1, rs2
x8
x6
XOR
x4

## Slide 45: R-Type (2): Shift Instructions
op | funct3 | mnemonic | description
0110011 | 001 | SLL rd, rs1, rs2 | R[rd] = R[rs1] << R[rs2]
0110011 | 101 | SRL rd, rs1, rs2 | R[rd] = R[rs1] >>> R[rs2] (zero ext.)
0110011 | 101 | SRA rd, rs1, rs2 | R[rd] = R[rt] >>> R[rs2] (sign ext.)
00000000011000100001010000110011
31 | 25 24 | 20 19 | 15 14 12 11 | 7 6 | 0
funct7 | rs2 | rs1 | Funct3 | Rd | op
7 bits | 5 bits | 5 bits | 3 bits | 5 bits | 7 bits
Notes: SRL and SRA have the same funct3, 101, but funct7 differs between the two, 0000000 vs 0100000, respectively

## Slide 46: R-Type (2): Shift Instructions
op | funct3 | mnemonic | description
0110011 | 001 | SLL rd, rs1, rs2 | R[rd] = R[rs1] << R[rs2]
0110011 | 101 | SRL rd, rs1, rs2 | R[rd] = R[rs1] >>> R[rs2] (zero ext.)
0110011 | 101 | SRA rd, rs1, rs2 | R[rd] = R[rt] >>> R[rs2] (sign ext.)
Example: x8 = x4 * 2x6 # SLL x8, x4, x6
x8 = x4 << x6
00000000011000100001010000110011
31 | 25 24 | 20 19 | 15 14 12 11 | 7 6 | 0
funct7 | rs2 | rs1 | Funct3 | Rd | op
7 bits | 5 bits | 5 bits | 3 bits | 5 bits | 7 bits
Notes: SRL and SRA have the same funct3, 101, but funct7 differs between the two, 0000000 vs 0100000, respectively

## Slide 47: Shift
Decode
Execute
WB
Memory
skip
ALU
PC
Prog.
Mem
+4
5
5
5
Reg. File
control
Fetch
SLL x8, x4, x6
x4 << x6
Example: x8 = x4 * 2x6 # SLL x8, x4, x6
x8 = x4 << x6
x4
x6
SLL
x8

## Slide 48: I-Type (1): Arithmetic w/ immediates
00000000010100101000001010010011
31 |  | 20 19 | 15 14 12 11 | 7 6 | 0
imm |  | rs1 | funct3 | rd | op
12 bits |  | 5 bits | 3 bits | 5 bits | 7 bits
op | funct3 | mnemonic | description
0010011 | 000 | ADDI rd, rs1, imm | R[rd] = R[rs1] + sign_extend(imm)
0010011 | 111 | ANDI rd, rs1, imm | R[rd] = R[rs1] & sign_extend(imm)
0010011 | 110 | ORI rd, rs1, imm | R[rd] = R[rs1] ¦ sign_extend(imm)

## Slide 49: I-Type (1): Arithmetic w/ immediates
Example: x5 = x5 + 5 # ADDI x5, x5, 5
x5 += 5
00000000010100101000001010010011
31 |  | 20 19 | 15 14 12 11 | 7 6 | 0
imm |  | rs1 | funct3 | rd | op
12 bits |  | 5 bits | 3 bits | 5 bits | 7 bits
op | funct3 | mnemonic | description
0010011 | 000 | ADDI rd, rs1, imm | R[rd] = R[rs1] + sign_extend(imm)
0010011 | 111 | ANDI rd, rs1, imm | R[rd] = R[rs1] & sign_extend(imm)
0010011 | 110 | ORI rd, rs1, imm | R[rd] = R[rs1] ¦ sign_extend(imm)

## Slide 50: Arithmetic w/ immediates
Fetch
Decode
Execute
Memory
WB
skip
ALU
PC
Prog.
Mem
+4
5
5
5
Reg. File
control
Example: x5 = x5 + 5 # ADDI x5, x5, 5
imm
extend
shamt
16
12

## Slide 51: Arithmetic w/ immediates
Fetch
Decode
Execute
WB
Memory
skip
ALU
PC
Prog.
Mem
+4
5
5
5
Reg. File
control
Example: x5 = x5 + 5 # ADDI x5, x5, 5
imm
extend
shamt
12
32
x5 + 5
ADDI x5, x5, 5
x5
ADDI
x5
5

## Slide 52: iClicker Question
To compile the code y = z + 1, assuming y is stored in X1 and z is stored in X2, you can use the ADDI instruction. What is the largest number for which we can continue to use ADDI?
12
212-1 = 4,095
212-1 -1 = 2,047
216-1 = 65,535
232-1 = ~4.3 billion
Notes: Add a “leave the if clause” option next time.

## Slide 53: iClicker Question
To compile the code y = z + 1, assuming y is stored in X1 and x is stored in X2, you can use the ADDI instruction. What is the largest number for which we can continue to use ADDI?
12
212-1 = 2,047
212-1 = 4,095
216-1 = 65,535
232-1 = ~4.3 billion
Notes: Add a “leave the if clause” option next time.

## Slide 56: U-Type (1): Load Upper Immediate
”
“
WORST
NAME
EVER !
00000000000000000101001010110111
31 |  |  | 12 | 11 7 | 6 0
imm |  |  |  | rd | op
20 bits |  |  |  | 5 bits | 7 bits
op | mnemonic | description
0110111 | LUI rd, imm | R[rd] = sign_ext(imm) << 12

## Slide 57: U-Type (1): Load Upper Immediate
”
“
op | mnemonic | description
0110111 | LUI rd, imm | R[rd] = sign_ext(imm) << 12
Example: x5 = 0x5000 # LUI x5, 5
Example: LUI x5, 0xbeef1
ADDI x5, x5 0x234
What does x5 = ?
0xbeef1234
00000000000000000101001010110111
31 |  |  | 12 | 11 7 | 6 0
imm |  |  |  | rd | op
20 bits |  |  |  | 5 bits | 7 bits
WORST
NAME
EVER !
Notes: The immediate field is sign_extended in RISC-V

## Slide 58: Load Upper Immediate
Fetch
Decode
Execute
Memory
WB
skip
ALU
PC
Prog.
Mem
+4
5
5
5
Reg. File
control
imm
extend
shamt
20
32
Example: x5 = 0x5000 # LUI x5, 5

## Slide 59: Load Upper Immediate
Fetch
Decode
Execute
WB
Memory
skip
ALU
PC
Prog.
Mem
+4
5
5
5
Reg. File
control
imm
extend
shamt
20
32
Example: x5 = 0x5000 # LUI x5, 5
12
0x5000
LUI x5, 5
LUI
x5
5

## Slide 60: RISC-V Instruction Types
Arithmetic/Logical
  R-type: result and two source registers, shift amount
  I-type: result and source register, shift amount in 16-bit immediate with sign/zero extension
  U-type: result register, 16-bit immediate with sign/zero extension
Memory Access
  I-type for loads and S-type for stores
  load/store between registers and memory
  word, half-word and byte operations
Control flow
  U-type: jump-and-link
  I-type: jump-and-link register
  SB-type: conditional branches: pc-relative addresses

## Slide 61: I-Type (2): Load Instructions
00000000010000101010000010000011
31 |  | 20 19 | 15 14 12 11 | 7 6 | 0
imm |  | rs1 | funct3 | rd | op
12 bits |  | 5 bits | 3 bits | 5 bits | 7 bits
signed offsets
base + offset addressing
op | funct3 | mnemonic | Description
0000011 | 000 | LB rd, rs1, imm | R[rd] = Mem[imm+R[rs1]]
0000011 | 001 | LH rd, rs1, imm | R[rd] = Mem[imm+R[rs1]]
0000011 | 010 | LW rd, rs1, imm | R[rd] = Mem[imm+R[rs1]]
0000011 | 011 | LD rd, rs1, imm | R[rd] = Mem[imm+R[rs1]]
0000011 | 100 | LBU rd, rs1, imm | R[rd] = Mem[imm+R[rs1]]
0000011 | 101 | LHU rd, rs1, imm | R[rd] = Mem[imm+R[rs1]]
0000011 | 110 | LWU rd, rs1, imm | R[rd] = Mem[imm+R[rs1]]

## Slide 62: I-Type (2): Load Instructions
Example: x1 = Mem[4+x5] # LW x1, x5, 4
LW x1 4(x5)
00000000010000101010000010000011
31 |  | 20 19 | 15 14 12 11 | 7 6 | 0
imm |  | rs1 | funct3 | rd | op
12 bits |  | 5 bits | 3 bits | 5 bits | 7 bits
op | funct3 | mnemonic | Description
0000011 | 000 | LB rd, rs1, imm | R[rd] = Mem[imm+R[rs1]]
0000011 | 001 | LH rd, rs1, imm | R[rd] = Mem[imm+R[rs1]]
0000011 | 010 | LW rd, rs1, imm | R[rd] = Mem[imm+R[rs1]]
0000011 | 011 | LD rd, rs1, imm | R[rd] = Mem[imm+R[rs1]]
0000011 | 100 | LBU rd, rs1, imm | R[rd] = Mem[imm+R[rs1]]
0000011 | 101 | LHU rd, rs1, imm | R[rd] = Mem[imm+R[rs1]]
0000011 | 110 | LWU rd, rs1, imm | R[rd] = Mem[imm+R[rs1]]
signed offsets
base + offset addressing

## Slide 63: I-Type (2): Load Instructions
op | funct3 | mnemonic | Description
0000011 | 000 | LB rd, rs1, imm | R[rd] = sign_ext(Mem[imm+R[rs1]])
0000011 | 001 | LH rd, rs1, imm | R[rd] = sign_ext(Mem[imm+R[rs1]])
0000011 | 010 | LW rd, rs1, imm | R[rd] = Mem[imm+R[rs1]]
0000011 | 011 | LD rd, rs1, imm | R[rd] = Mem[imm+R[rs1]]
0000011 | 100 | LBU rd, rs1, imm | R[rd] = zero_ext(Mem[imm+R[rs1]])
0000011 | 101 | LHU rd, rs1, imm | R[rd] = zero_ext(Mem[imm+R[rs1]])
0000011 | 110 | LWU rd, rs1, imm | R[rd] = Mem[imm+R[rs1]]
00000000010000101010000010000011
31 |  | 20 19 | 15 14 12 11 | 7 6 | 0
imm |  | rs1 | funct3 | rd | op
12 bits |  | 5 bits | 3 bits | 5 bits | 7 bits
base + offset addressing
signed offsets
Example: x1 = Mem[4+x5] # LW x1, x5, 4
LW x1 4(x5)

## Slide 64: Memory Operations: Load
ALU
PC
Prog.
Mem
+4
5
5
5
Reg. File
control
imm
extend
16
12
Data Mem
addr
Write Enable
Example: x1 = Mem[4+x5] # LW x1, x5, 4
LW x1 4(x5)

## Slide 65: Memory Operations: Load
ALU
PC
Prog.
Mem
+4
5
5
5
Reg. File
control
imm
extend
12
32
LW x1, x5, 4
4+x5
Data Mem
addr
Write Enable
LW
x1
x5
4
Mem[4+x5]
Fetch
Decode
Execute
WB
Memory
Example: x1 = Mem[4+x5] # LW x1, x5, 4
LW x1 4(x5)

## Slide 66: S-Type (1): Store Instructions
op | funct3 | mnemonic | description
0100011 | 000 | SB rs2, rs1, imm | Mem[sign_ext(imm)+R[rs1]] = R[rd]
0100011 | 001 | SH rs2, rs1, imm | Mem[sign_ext(imm)+R[rs1]] = R[rd]
0100011 | 010 | SW rs2, rs1, imm | Mem[sign_ext(imm)+R[rs1]] = R[rd]
signed offsets
base + offset addressing
00001000000000101010000000010011
31 | 25 24 | 20 19 | 15 14 12 11 | 7 6 | 0
imm | rs2 | rs1 | funct3 | imm | Op
7 bits | 5 bits | 5 bits | 3 bits | 5 bits | 7 bits
Notes: The 12-bit immediate in the S-type format is split into two fields,
which supply the lower 5 bits and upper 7 bits. The RISC-V
architects chose this design because it keeps the rs1 and rs2 fields in
the same place in all instruction formats. Keeping the instruction
formats as similar as possible reduces hardware complexity.
Similarly, the opcode and funct3 fields are the same size in all
locations, and they are always in the same place.

## Slide 67: S-Type (1): Store Instructions
op | funct3 | mnemonic | description
0100011 | 000 | SB rs2, rs1, imm | Mem[sign_ext(imm)+R[rs1]] = R[rd]
0100011 | 001 | SH rs2, rs1, imm | Mem[sign_ext(imm)+R[rs1]] = R[rd]
0100011 | 010 | SW rs2, rs1, imm | Mem[sign_ext(imm)+R[rs1]] = R[rd]
signed offsets
base + offset addressing
Example: Mem[128+x5] = x1 # SW x1, x5, 128
SW x1 128(x5)
00001000000000101010000000010011
31 | 25 24 | 20 19 | 15 14 12 11 | 7 6 | 0
imm | rs2 | rs1 | funct3 | imm | Op
7 bits | 5 bits | 5 bits | 3 bits | 5 bits | 7 bits
Notes: The 12-bit immediate in the S-type format is split into two fields,
which supply the lower 5 bits and upper 7 bits. The RISC-V
architects chose this design because it keeps the rs1 and rs2 fields in
the same place in all instruction formats. Keeping the instruction
formats as similar as possible reduces hardware complexity.
Similarly, the opcode and funct3 fields are the same size in all
locations, and they are always in the same place.

## Slide 68: Memory Operations: Load
ALU
PC
Prog.
Mem
+4
5
5
5
Reg. File
control
imm
extend
12
32
SW x1, x5, 128
128+x5
Data Mem
addr
Write Enable
SW
x1
x5
128
Fetch
Decode
Execute
WB
Memory
Example: Mem[4+x5] = x1 # SW x1, x5, 128
SW x1 128(x5)

## Slide 69: Memory Layout Options
# x5 contains 5 (0x00000005)
SB x5, x0, 0
SB x5, x0, 2
SW x5, x0, 8
Two ways to store a word in memory.
Endianness: ordering of bytes within a memory word
 | 0x000fffff
 | ...
 | 0x0000000b
 | 0x0000000a
 | 0x00000009
 | 0x00000008
 | 0x00000007
 | 0x00000006
 | 0x00000005
 | 0x00000004
 | 0x00000003
 | 0x00000002
 | 0x00000001
 | 0x00000000
Notes: Big Endian means store MSB (most significant byte) first

## Slide 70: Little Endian
Endianness: Ordering of bytes within a memory word
1000 | 1001 | 1002 | 1003
0x12345678
Little Endian = least significant part first (RISC-V, x86)
as 4 bytes
as 2 halfwords
as 1 word
70
Clicker Question: What values go in the byte-sized boxes with addresses 1000 and 1001?
a) d)
b) e)
c)
0x8, 0x7
0x78, 0x56
0x1, 0x2
0x12, 0x34
0x87, 0x65
THIS IS WHAT YOUR PROJECTS WILL BE

## Slide 71: Little Endian
Endianness: Ordering of bytes within a memory word
1000 | 1001 | 1002 | 1003
0x12345678
Little Endian = least significant part first (RISC-V, x86)
as 4 bytes
as 2 halfwords
as 1 word
71
Clicker Question: What values go in the byte-sized boxes with addresses 1000 and 1001?
a) d)
b) e)
c)
0x8, 0x7
0x78, 0x56
0x1, 0x2
0x12, 0x34
0x87, 0x65
THIS IS WHAT YOUR PROJECTS WILL BE

## Slide 72: Little Endian
Endianness: Ordering of bytes within a memory word
1000 | 1001 | 1002 | 1003
0x12345678
Big Endian = most significant part first (MIPS, networks)
as 4 bytes
as 2 halfwords
as 1 word
72
Clicker Question: What value goes in the half-word sized box with address 1000?
a) d)
b) e)
c)
THIS IS WHAT YOUR PROJECTS WILL BE
0x1
0x12
0x5678
0x4321
0x1234

## Slide 73: Little Endian
Endianness: Ordering of bytes within a memory word
1000 | 1001 | 1002 | 1003
0x12345678
Big Endian = most significant part first (MIPS, networks)
as 4 bytes
as 2 halfwords
as 1 word
73
Clicker Question: What value goes in the half-word sized box with address 1000?
a) d)
b) e)
c)
THIS IS WHAT YOUR PROJECTS WILL BE
0x1
0x12
0x5678
0x4321
0x1234

## Slide 74: Little Endian
 | 0x000fffff
 | ...
 | 0x0000000b
 | 0x0000000a
 | 0x00000009
 | 0x00000008
 | 0x00000007
 | 0x00000006
 | 0x00000005
 | 0x00000004
 | 0x00000003
 | 0x00000002
 | 0x00000001
 | 0x00000000
Little Endian = least significant part first (RISC-V, x86)
Example:
r5 contains 5 (0x00000005)
SW r5, 8(r0)
Clicker Question: After executing the store, which byte address contains the byte 0x05?
0x00000008
0x00000009
0x0000000a
0x0000000b
I don’t know
WHAT WE USE IN 3410
Notes: Little Endian means store LSB (least significant byte) first

## Slide 75: Little Endian
 | 0x000fffff
 | ...
 | 0x0000000b
 | 0x0000000a
 | 0x00000009
 | 0x00000008
 | 0x00000007
 | 0x00000006
 | 0x00000005
 | 0x00000004
 | 0x00000003
 | 0x00000002
 | 0x00000001
 | 0x00000000
Little Endian = least significant part first (RISC-V, x86)
Example:
r5 contains 5 (0x00000005)
SW r5, 8(r0)
Clicker Question: After executing the store, which byte address contains the byte 0x05?
0x00000008
0x00000009
0x0000000a
0x0000000b
I don’t know
WHAT WE USE IN 3410
Notes: Little Endian means store LSB (least significant byte) first

## Slide 76: Big Endian
 | 0x000fffff
 | ...
 | 0x0000000b
 | 0x0000000a
 | 0x00000009
 | 0x00000008
 | 0x00000007
 | 0x00000006
 | 0x00000005
 | 0x00000004
 | 0x00000003
 | 0x00000002
 | 0x00000001
 | 0x00000000
Big Endian = most significant part first (some MIPS, networks)
Example:
r5 contains 5 (0x00000005)
SW r5, 8(r0)
Clicker Question: After executing the store, which byte address contains the byte 0x05?
0x00000008
0x00000009
0x0000000a
0x0000000b
I don’t know
Notes: Big Endian means store MSB (most significant byte) first

## Slide 77: Big Endian
 | 0x000fffff
 | ...
 | 0x0000000b
 | 0x0000000a
 | 0x00000009
 | 0x00000008
 | 0x00000007
 | 0x00000006
 | 0x00000005
 | 0x00000004
 | 0x00000003
 | 0x00000002
 | 0x00000001
 | 0x00000000
Big Endian = most significant part first (some MIPS, networks)
Example:
r5 contains 5 (0x00000005)
SW r5, 8(r0)
Clicker Question: After executing the store, which byte address contains the byte 0x05?
0x00000008
0x00000009
0x0000000a
0x0000000b
I don’t know
Notes: Big Endian means store MSB (most significant byte) first

## Slide 78: Big Endian Memory Layout
 | 0x000fffff
 | ...
 | 0x0000000b
 | 0x0000000a
 | 0x00000009
 | 0x00000008
 | 0x00000007
 | 0x00000006
 | 0x00000005
 | 0x00000004
 | 0x00000003
 | 0x00000002
 | 0x00000001
 | 0x00000000
SB x5, x0, 2
LB x6, x0, 2
SW x5, x0, 8
LB x7, x0, 8
LB x8, x0, 11
0x05
0x00
0x00
0x00
0x05
 | x0
 | ...
 | x5
 | x6
 | x7
 | x8
0x00000005
0x00000000
0x00000005
0x00000005

## Slide 79: RISC-V Instruction Types
Arithmetic/Logical
  R-type: result and two source registers, shift amount
  I-type: result and source register, shift amount in 16-bit immediate with sign/zero extension
  U-type: result register, 16-bit immediate with sign/zero extension
Memory Access
  I-type for loads and S-type for stores
  load/store between registers and memory
  word, half-word and byte operations
Control flow
  U-type: jump-and-link
  I-type: jump-and-link register
  S-type: conditional branches: pc-relative addresses

## Slide 80: UJ-Type (2): Jump and Link
op | Mnemonic | Description
1101111 | JAL rd, imm | R[rd] = PC+4; PC=PC + sext(imm)
Function/procedure calls
Why?
00000000000000001000001011101111
31 |  |  | 12 | 11 7 | 6 0
imm |  |  |  | rd | op
20 bits |  |  |  | 5 bits | 7 bits
Example: x5 = PC+4 # JAL x5, 16
PC = PC + 16 (i.e. 16 == 8<<1)
Notes: The JAL instruction has now moved to the U-Type format with an explicit destination
register, and the J instruction has been dropped being replaced by JAL with rd=x0. This
removes the only instruction with an implicit destination register and removes the J-Type
instruction format from the base ISA. There is an accompanying reduction in JAL reach, but
a signicant reduction in base ISA complexity.
RISC-V has an asymmetric immediate encoding which means that the immediates are formed by concatenating different bits in an asymmetric order based on the specific immediate formats. Note that in RISC-V all immediates are always sign extended, and the sign-bit for the immediate is always in bit 31 of the instruction. The following diagrams illustrate how to create a 32-bit immediate from each of the five immediate formats. The fields are labeled with the instruction bits used to construct their value. <-- n is used to indicate repeating bit n of the instruction to fill that field and z is used to indicate a bit which is always set to zero.
* J-immediate 31 20 19 12 11 10 5 4 1 0
+----------------------+---------------+--+-----------+-------+--+
| <-- 31 | 19:12 |20| 30:25 | 24:21 |z |
+----------------------+---------------+--+-----------+-------+--+

## Slide 81: Jump and Link
ALU
PC
Prog.
Mem
+4
5
5
5
Reg. File
control
extend
12
32
Data Mem
addr
Write Enable
imm
Example: x5 = PC+4 # JAL x5, 16
PC = PC + 16 (i.e. 16 == 8<<1)

## Slide 82: Jump and Link
ALU
PC
Prog.
Mem
+4
5
5
5
Reg. File
control
imm
extend
Data Mem
addr
Write Enable
+
Could have used ALU for JAL add
Example: x5 = PC+4 # JAL x5, 16
PC = PC + 16 (i.e. 16 == 8<<1)
JAL x5, 16

## Slide 83: I-Type (3): Jump and Link Register
op | funct3 | Mnemonic | Description
1100111 | 000 | JALR rd, rs1, imm | R[rd] = PC+4; PC=(R[rs1]+sign_ex(imm))&0xfffffffe
Function/procedure calls
Why?
00000001000000100000001011100111
31 |  | 20 19 | 15 14 12 11 | 7 6 | 0
imm |  | rs1 | funct3 | rd | op
12 bits |  | 5 bits | 3 bits | 5 bits | 7 bits
Example: x5 = PC+4 # JALR x5, x4, 16
PC = x4 + 16

## Slide 84: Jump and Link Register
ALU
PC
Prog.
Mem
+4
5
5
5
Reg. File
control
imm
extend
Data Mem
addr
Write Enable
+
Example: x5 = PC+4 # JALR x5, x4, 16
PC = x4 + 16

## Slide 85: Jump and Link Register
ALU
PC
Prog.
Mem
+4
5
5
5
Reg. File
control
imm
extend
Data Mem
addr
Write Enable
+
x4 + 16
JALR x5, x4, 16
Example: x5 = PC+4 # JALR x5, x4, 16
PC = x4 + 16

## Slide 86: Moving Beyond Jumps
Can use Jump and link (JAL) or Jump and Link Register (JALR) instruction to jump to 0xabcd1234
What about a jump based on a condition?
# assume 0 <= x3 <= 1
if (x3 == 0) jump to 0xdecafe00
else jump to 0xabcd1234

## Slide 87: SB-Type (2): Branches
op | mnemonic | description
1100011 | BEQ rs1, rs2, imm | PC=(R[rs1] == R[rs2] ? PC+sext(imm)<<1 : PC+4)
1100011 | BNE rs1, rs2, imm | PC=(R[rs1] != R[rs2] ? PC+sext(imm)<<1 : PC+4)
signed
Example: BEQ x5, x1, 128
if(R[x5]==R[x1])
PC = PC + 128 (i.e. 128 == 64<<1)
A word about all these +’s…
00000100000000101000000000010011
31 | 25 24 | 20 19 | 15 14 12 11 | 7 6 | 0
imm | rs2 | rs1 | funct3 | imm | Op
7 bits | 5 bits | 5 bits | 3 bits | 5 bits | 7 bits

## Slide 88: Control Flow: Branches
ALU
PC
Prog.
Mem
+4
5
5
5
Reg. File
control
imm
extend
Data Mem
addr
Write Enable
+
Example: BEQ x5, x1, 128

## Slide 89: Control Flow: Branches
ALU
PC
Prog.
Mem
+4
5
5
5
Reg. File
control
imm
extend
Data Mem
addr
Write Enable
=?
+
Could have used ALU for branch cmp
Could have used ALU for branch add
BEQ
(PC+64<<1
Example: BEQ x5, x1, 128
BEQ x5, x1, 128

## Slide 90: SB-Type (3): Conditional Jumps
op | funct3 | mnemonic | description
1100011 | 100 | BLT rs1, rs2, imm | PC=(R[rs1] <s R[rs2] ? PC + sext(imm)<<1 : PC+4)
1100011 | 101 | BGE rs1, rs2, imm | PC=(R[rs1] >=s R[rs2] ? PC + sext(imm)<<1 : PC+4)
1100011 | 110 | BLTU rs1, rs2 imm | PC=(R[rs1] <u R[rs2] ? PC + sext(imm)<<1 : PC+4)
1100011 | 111 | BGEU rs1, rs2, imm | PC=(R[rs1] >=u R[rs2] ? PC + sext(imm)<<1 : PC+4)
Example: BGE x5, x0, 32
if(R[x5] ≥s R[x0])
PC = PC + 32 (i.e. 32 == 16<<1)
00000000000000101000100000010011
31 | 25 24 | 20 19 | 15 14 12 11 | 7 6 | 0
imm | rs2 | rs1 | funct3 | imm | Op
7 bits | 5 bits | 5 bits | 3 bits | 5 bits | 7 bits
Notes: RISC-V has an asymmetric immediate encoding which means that the
immediates are formed by concatenating different bits in an asymmetric
order based on the specific immediate formats. Note that in RISC-V all
immediates are always sign extended, and the sign-bit for the immediate
is always in bit 31 of the instruction.
The following diagrams illustrate how to create a 32-bit immediate from
each of the five immediate formats. The fields are labeled with the
instruction bits used to construct their value. <-- n is used to indicate
repeating bit n of the instruction to fill that field and z is used to
indicate a bit which is always set to zero.
* B-immediate 31 12 11 10 5 4 1 0
+--------------------------------------+--+-----------+-------+--+
| <-- 31 |7 | 30:25 | 11:8 |z |
+--------------------------------------+--+-----------+-------+--+

## Slide 91: Control Flow: More Branches
ALU
PC
Prog.
Mem
+4
5
5
5
Reg. File
control
imm
extend
Data Mem
addr
Write Enable
=?
offset
+
BGE
PC+16<<1
Could have used ALU for branch cmp
Example: BGE x5, x0, 32
BGE x5, x0, 32
cmp

## Slide 92: RISC-V Instruction Types
Arithmetic/Logical
  R-type: result and two source registers, shift amount
  I-type: result and source register, shift amount in 16-bit immediate with sign/zero extension
  U-type: result register, 16-bit immediate with sign/zero extension
Memory Access
  I-type for loads and S-type for stores
  load/store between registers and memory
  word, half-word and byte operations
Control flow
  U-type: jump-and-link
  I-type: jump-and-link register
  S-type: conditional branches: pc-relative addresses
  ✔
  ✔
  ✔

## Slide 93: iClicker Question
What RISC-V instruction would you use for a:
1. For loop?
2. While loop?
3. Function call?
4. If statement?
5. Return statement?
Jump and Link Register (JALR lr, x2, 0x000FFFF)
Branch Equals (BEQ x1, x2, 0xAAAA)
Branch Less Than (BLT x1, x2, 0xAAAA)
Jump and Link (JAL lr, 0x000FFFF)

## Slide 94
What is the one topic you’re most uncertain about at this point in the class?
Gates & Logic
Circuit Simplification
Finite State Machines
RISC-V Processor
RISC-V Assembly
iClicker Question

## Slide 95: Summary
We have all that it takes to build a processor!
  Arithmetic Logic Unit (ALU)
  Register File
  Memory
RISC-V processor and ISA is an example of a Reduced Instruction Set Computers (RISC)
  Simplicity is key, thus enabling us to build it!
We now know the data path for the MIPS ISA:
register, memory and control instructions