## Slide 1
The RISC-V Processor
Hakim Weatherspoon
CS 3410
Computer Science
Cornell University
[Weatherspoon, Bala, Bracy, and Sirer]

## Slide 2: Announcements
Make sure to go to your Lab Section this week
Completed Proj1 due Friday, Feb 15th
Note, a Design Document is due when you submit Proj1 final circuit
Work alone
BUT use your resources
  Lab Section, Piazza.com, Office Hours
  Class notes, book, Sections, CSUGLab

## Slide 3: Announcements
Check online syllabus/schedule
http://www.cs.cornell.edu/Courses/CS3410/2019sp/schedule
Slides and Reading for lectures
Office Hours
Pictures of all TAs
Project and Reading Assignments
Dates to keep in Mind
  Prelims: Tue Mar 5th and Thur May 2nd
  Proj 1: Due next Friday, Feb 15th
  Proj3: Due before Spring break
  Final Project: Due when final will be Feb 16th
Schedule is subject to change

## Slide 4: Collaboration, Late, Re-grading Policies
“White Board” Collaboration Policy
  Can discuss approach together on a “white board”
  Leave, watch a movie such as Black Lightening, then write up solution independently
  Do not copy solutions
  Late Policy
  Each person has a total of five “slip days”
  Max of two slip days for any individual assignment
  Slip days deducted first for any late assignment,
  cannot selectively apply slip days
  For projects, slip days are deducted from all partners
  25% deducted per day late after slip days are exhausted
  Regrade policy
  Submit written request within a week of receiving score

## Slide 5: Announcements
Level Up (optional enrichment)
  Teaches CS students tools and skills needed in their coursework as well as their career, such as Git, Bash Programming, study strategies, ethics in CS, and even applying to graduate school.
  Thursdays at 7-8pm in 310 Gates Hall, starting this week
  http://www.cs.cornell.edu/courses/cs3110/2019sp/levelup/

## Slide 6: Big Picture: Building a Processor
PC
imm
memory
target
offset
cmp
control
=?
new pc
memory
din
dout
addr
register file
inst
extend
A single cycle processor
alu
+4
+4

## Slide 7: Goal for the next few lectures
Understanding the basics of a processor
  We now have the technology to build a CPU!
Putting it all together:
  Arithmetic Logic Unit (ALU)
  Register File
  Memory
    SRAM: cache
    DRAM: main memory
  RISC-V Instructions & how they are executed
7

## Slide 8: RISC-V Register File
PC
imm
memory
target
offset
cmp
control
=?
new pc
memory
din
dout
addr
register file
inst
extend
alu
+4
+4
A single cycle processor

## Slide 9: RISC-V Register File
RISC-V register file
  32 registers, 32-bits each
  x0 wired to zero
  Write port indexed via RW
    on falling edge when WE=1
  Read ports indexed via RA, RB
Dual-Read-Port Single-Write-Port
32 x 32 Register File
QA
QB
DW
RW
RA
RB
WE
32
32
32
1
5
5
5

## Slide 10: RISC-V Register File
RISC-V register file
  32 registers, 32-bits each
  x0 wired to zero
  Write port indexed via RW
    on falling edge when WE=1
  Read ports indexed via RA, RB
RISC-V register file
  Numbered from 0 to 31
  Can be referred by number: x0, x1, x2, … x31
  Convention, each register also has a name:
    x10 – x17  a0 – a7, x28 – x31  t3 – t6
A
B
W
RW
RA
RB
WE
32
32
32
1
5
5
5
x0
x1
…
x31

## Slide 11: RISC-V Memory
PC
imm
memory
target
offset
cmp
control
=?
new pc
memory
din
dout
addr
register file
inst
extend
alu
+4
+4
A single cycle processor

## Slide 12: RISC-V Memory
32-bit address
32-bit data (but byte addressed)
Enable + 2 bit memory control (mc)
  00: read word (4 byte aligned)
  01: write byte
  10: write halfword (2 byte aligned)
  11: write word (4 byte aligned)
memory
32
addr
2
mc
32
32
E
Din
Dout
 | 0x000fffff
 | . . .
 | 0x0000000b
 | 0x0000000a
 | 0x00000009
 | 0x00000008
 | 0x00000007
 | 0x00000006
 | 0x00000005
 | 0x00000004
 | 0x00000003
 | 0x00000002
 | 0x00000001
 | 0x00000000
0x05
1 byte
address

## Slide 13: Putting it all together: Basic Processor
PC
imm
memory
target
offset
cmp
control
=?
new pc
memory
din
dout
addr
register file
inst
extend
alu
+4
+4
A single cycle processor

## Slide 14: To make a computer
Need a program
Stored program computer
Architectures
von Neumann architecture
Harvard (modified) architecture

## Slide 15: To make a computer
Need a program
Stored program computer
(a Universal Turing Machine)
Architectures
von Neumann architecture
Harvard (modified) architecture
Notes: A stored-program computer is one which stores program instructions in electronic memory. Often the definition is extended with the requirement that the treatment of programs and data in
http://en.wikipedia.org/wiki/Universal_Turing_machine#Stored-program_computer
Davis makes a persuasive argument that Turing's conception of what is now known as "the stored-program computer", of placing the "action table"—the instructions for the machine—in the same "memory" as the input data, strongly influenced John von Neumann's conception of the first American discrete-symbol (as opposed to analog) computer—the EDVAC (Electronic Discrete Variable Automatic Computer) [previous machine, ENIAC (Electronic Numerical Integrator And Computer), was not a stored-program computer, and was not even in binary, it was in decimal].
See video on von Neumann describe the stored-program computer, 34 minutes into video, https://www.youtube.com/watch?v=VTS9O0CoVng
Also, see clip on Turing in the movie The Imitation Game where Turing states that the Bombe will work in breaking the Enigma machine: https://www.youtube.com/watch?v=MM47hsaYWZE

## Slide 16: Putting it all together: Basic Processor
A RISC-V CPU with a (modified) Harvard architecture
  Modified: instructions & data in common address space, separate instr/data caches can be accessed in parallel
CPU
Registers
Data Memory
data, address,
control
ALU
Control
00100000001
00100000010
00010000100
...
Program Memory
10100010000
10110000011
00100010101
...
Notes: The Harvard architecture is a computer architecture with physically separate storage and signal pathways for instructions and data. --- http://en.wikipedia.org/wiki/Harvard_architecture
Under pure von Neumann architecture the CPU can be either reading an instruction or reading/writing data from/to the memory. Both cannot occur at the same time since the instructions and data use the same bus system. In a computer using the Harvard architecture, the CPU can both read an instruction and perform a data memory access at the same time, even without a cache. A Harvard architecture computer can thus be faster for a given circuit complexity because instruction fetches and data access do not contend for a single memory pathway .
Also, a Harvard architecture machine has distinct code and data address spaces: instruction address zero is not the same as data address zero. Instruction address zero might identify a twenty-four bit value, while data address zero might indicate an eight bit byte that isn't part of that twenty-four bit value.
A modified Harvard architecture machine is very much like a Harvard architecture machine, but it relaxes the strict separation between instruction and data while still letting the CPU concurrently access two (or more) memory buses. The most common modification includes separate instruction and data caches backed by a common address space. While the CPU executes from cache, it acts as a pure Harvard machine. When accessing backing memory, it acts like a von Neumann machine (where code can be moved around like data, a powerful technique). This modification is widespread in modern processors such as the ARM architecture and X86 processors. It is sometimes loosely called a Harvard architecture, overlooking the fact that it is actually "modified".

## Slide 17: Takeaway
A processor executes instructions
  Processor has some internal state in storage elements (registers)
A memory holds instructions and data
  (modified) Harvard architecture: separate insts and data
  von Neumann architecture: combined inst and data
A bus connects the two
  We now have enough building blocks to build machines that can perform non-trivial computational tasks

## Slide 18: Next Goal
How to program and execute instructions on a RISC-V processor?

## Slide 19: Instruction Processing
A basic processor
  fetches
  decodes
  executes
one instruction at a time
00100000000000100000000000001010
00100000000000010000000000000000
00000000001000100001100000101010
5
ALU
5
5
control
Reg. File
PC
Prog
Mem
inst
+4
Data
Mem
Instructions:
stored in memory, encoded in binary

## Slide 20: Levels of Interpretation: Instructions
High Level Language
  C, Java, Python, ADA, …
  Loops, control flow, variables
for (i = 0; i < 10; i++) printf(“go cucs”);
main: addi x2, x0, 10
addi x1, x0, 0
loop: slt x3, x1, x2
...
Assembly Language
  No symbols (except labels)
  One operation per statement
  “human readable machine language”
Machine Language
  Binary-encoded assembly
  Labels become addresses
  The language of the CPU
ALU, Control, Register File, …
Machine Implementation
(Microarchitecture)
Instruction Set Architecture
00000000101000010000000000010011
00100000000000010000000000010000
00000000001000100001100000101010
10 x2 x0 op=addi

## Slide 21: Instruction Set Architecture (ISA)
Different CPU architectures specify different instructions
Two classes of ISAs
  Reduced Instruction Set Computers (RISC)
  IBM Power PC, Sun Sparc, MIPS, Alpha
  Complex Instruction Set Computers (CISC)
  Intel x86, PDP-11, VAX
Another ISA classification: Load/Store Architecture
  Data must be in registers to be operated on
  For example: array[x] = array[y] + array[z]
  1 add ? OR 2 loads, an add, and a store ?
  Keeps HW simple  many RISC ISAs are load/store

## Slide 22: Takeaway
A RISC-V processor and ISA (instruction set architecture) is an example a Reduced Instruction Set Computers (RISC) where simplicity is key, thus enabling us to build it!!

## Slide 23: Next Goal
How are instructions executed?
What is the general datapath to execute an instruction?

## Slide 24: Five Stages of RISC-V Datapath
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
Fetch
Decode
Execute
Memory
WB
A single cycle processor – this diagram is not 100% spatial

## Slide 25: Five Stages of RISC-V Datapath
Basic CPU execution loop
  Instruction Fetch
  Instruction Decode
  Execution (ALU)
  Memory Access
  Register Writeback

## Slide 26: Stage 1: Instruction Fetch
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
  Fetch 32-bit instruction from memory
  Increment PC = PC + 4
Fetch
Decode
Execute
Memory
WB

## Slide 27: Stage 2: Instruction Decode
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
  Gather data from the instruction
  Read opcode; determine instruction type, field lengths
  Read in data from register file
  (0, 1, or 2 reads for jump, addi, or add, respectively)
Fetch
Decode
Execute
Memory
WB

## Slide 28: Stage 3: Execution (ALU)
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
  Useful work done here (+, -, *, /), shift, logic operation, comparison (slt)
  Load/Store? lw x2, x3, 32  Compute address
Fetch
Decode
Execute
Memory
WB

## Slide 29: Stage 4: Memory Access
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
  Used by load and store instructions only
  Other instructions will skip this stage
R/W
addr
Data
Data
Fetch
Decode
Execute
Memory
WB

## Slide 30: Stage 5: Writeback
5
ALU
5
5
control
Reg. File
PC
Prog.
Mem
inst
+4
Data
Mem
  Write to register file
  For arithmetic ops, logic, shift, etc, load. What about stores?
  Update PC
  For branches, jumps
Fetch
Decode
Execute
Memory
WB

## Slide 31: Takeaway
The datapath for a RISC-V processor has five stages:
  Instruction Fetch
  Instruction Decode
  Execution (ALU)
  Memory Access
  Register Writeback
This five stage datapath is used to execute all RISC-V instructions

## Slide 32: Next Goal
Specific datapaths RISC-V Instructions

## Slide 33: RISC-V Design Principles
Simplicity favors regularity
  32 bit instructions
Smaller is faster
  Small register file
Make the common case fast
  Include support for constants
Good design demands good compromises
  Support for different type of interpretations/classes

## Slide 34: Instruction Types
Arithmetic
  add, subtract, shift left, shift right, multiply, divide
Memory
  load value from memory to a register
  store value to memory from a register
Control flow
  conditional jumps (branches)
  jump and link (subroutine call)
Many other instructions are possible
  vector add/sub/mul/div, string operations
  manipulate coprocessor
  I/O

## Slide 35: RISC-V Instruction Types
Arithmetic/Logical
  R-type: result and two source registers, shift amount
  I-type: result and source register, shift amount in 16-bit immediate with sign/zero extension
  U-type: result register, 16-bit immediate with sign/zero extension
Memory Access
  I-type for loads and S-type for stores
  load/store between registers and memory
  word, half-word and byte operations
Control flow
  U-type: jump-and-link
  I-type: jump-and-link register
  S-type: conditional branches: pc-relative addresses

## Slide 36: RISC-V instruction formats
All RISC-V instructions are 32 bits long, have 4 formats
R-type
I-type
S-type
U-type
funct7 | rs2 | rs1 | funct3 | rd | op
7 bits | 5 bits | 5 bits | 3 bits | 5 bits | 7 bits
imm |  | rs1 | funct3 | rd | op
12 bits |  | 5 bits | 3 bits | 5 bits | 7 bits
imm | rs2 | rs1 | funct3 | imm | op
7 bits | 5 bits | 5 bits | 3 bits | 5 bits | 7 bits
imm |  |  |  | rd | op
20 bits |  |  |  | 5 bits | 7 bits

## Slide 37: R-Type (1): Arithmetic and Logic
funct7 | rs2 | rs1 | funct3 | rd | op
7 bits | 5 bits | 5 bits | 3 bits | 5 bits | 7 bits
op | funct3 | mnemonic | description
0110011 | 000 | ADD rd, rs1, rs2 | R[rd] = R[rs1] + R[rs2]
0110011 | 000 | SUB rd, rs1, rs2 | R[rd] = R[rs1] – R[rs2]
0110011 | 110 | OR rd, rs1, rs2 | R[rd] = R[rs1] ¦ R[rs2]
0110011 | 100 | XOR rd, rs1, rs2 | R[rd] = R[rs1]  R[rs2]
00000000011001000100001000110011

## Slide 38: Arithmetic and Logic
Fetch
Decode
Execute
Memory
WB
skip
ALU
PC
Prog.
Mem
+4
5
5
5
Reg. File
control

## Slide 39: R-Type (2): Shift Instructions
funct7 | rs2 | rs1 | funct3 | rd | op
7 bits | 5 bits | 5 bits | 3 bits | 5 bits | 7 bits
op | funct3 | mnemonic | description
0110011 | 001 | SLL rd, rs1, rs2 | R[rd] = R[rs1] << R[rs2]
0110011 | 101 | SRL rd, rs1, rs2 | R[rd] = R[rs1] >>> R[rs2] (zero ext.)
0110011 | 101 | SRA rd, rs1, rs2 | R[rd] = R[rt] >>> R[rs2] (sign ext.)
0000000001100010000101000011011

## Slide 40: Shift
Decode
Execute
WB
Memory
skip
ALU
PC
Prog.
Mem
+4
5
5
5
Reg. File
control
Fetch

## Slide 41: I-Type (1): Arithmetic w/ immediates
imm |  | rs1 | funct3 | rd | op
12 bits |  | 5 bits | 3 bits | 5 bits | 7 bits
op | funct3 | mnemonic | description
0010011 | 000 | ADDI rd, rs1, imm | R[rd] = R[rs1] + imm
0010011 | 111 | ANDI rd, rs1, imm | R[rd] = R[rs1] & zero_extend(imm)
0010011 | 110 | ORI rd, rs1, imm | R[rd] = R[rs1] ¦ zero_extend(imm)
00000000010100101000001010010011

## Slide 42: Arithmetic w/ immediates
Fetch
Decode
Execute
Memory
WB
skip
ALU
PC
Prog.
Mem
+4
5
5
5
Reg. File
control
imm
extend
shamt
16
12

## Slide 43: U-Type (1): Load Upper Immediate
”
“
imm |  |  |  | rd | op
20 bits |  |  |  | 5 bits | 7 bits
op | mnemonic | description
0110111 | LUI rd, imm | R[rd] = imm << 16
00000000000000000101001010110111

## Slide 44: Load Upper Immediate
Fetch
Decode
Execute
Memory
WB
skip
ALU
PC
Prog.
Mem
+4
5
5
5
Reg. File
control
imm
extend
shamt
16
12
16
0x50000

## Slide 45: RISC-V Instruction Types
Arithmetic/Logical
  R-type: result and two source registers, shift amount
  I-type: result and source register, shift amount in 16-bit immediate with sign/zero extension
  U-type: result register, 16-bit immediate with sign/zero extension
Memory Access
  I-type for loads and S-type for stores
  load/store between registers and memory
  word, half-word and byte operations
Control flow
  U-type: jump-and-link
  I-type: jump-and-link register
  S-type: conditional branches: pc-relative addresses
  ✔

## Slide 46: RISC-V Instruction Types
Arithmetic/Logical
  R-type: result and two source registers, shift amount
  I-type: result and source register, shift amount in 16-bit immediate with sign/zero extension
  U-type: result register, 16-bit immediate with sign/zero extension
Memory Access
  I-type for loads and S-type for stores
  load/store between registers and memory
  word, half-word and byte operations
Control flow
  U-type: jump-and-link
  I-type: jump-and-link register
  S-type: conditional branches: pc-relative addresses
  ✔

## Slide 47: Summary
We have all that it takes to build a processor!
  Arithmetic Logic Unit (ALU)
  Register File
  Memory
RISC-V processor and ISA is an example of a Reduced Instruction Set Computers (RISC)
  Simplicity is key, thus enabling us to build it!
We now know the data path for the MIPS ISA:
register, memory and control instructions