## Slide 1: Pipelining
Hakim Weatherspoon
CS 3410
Computer Science
Cornell University
[Weatherspoon, Bala, Bracy, McKee, and Sirer]

## Slide 2: Review: Single Cycle Processor
alu
PC
imm
memory
memory
din
dout
addr
target
offset
cmp
control
=?
new pc
register file
inst
extend
+4
+4

## Slide 3: Review: Single Cycle Processor
Advantages
  Single cycle per instruction make logic and clock simple
Disadvantages
  Since instructions take different time to finish, memory and functional unit are not efficiently utilized
  Cycle time is the longest delay
    Load instruction
  Best possible CPI is 1 (actually < 1 w parallelism)
    However, lower MIPS and longer clock period (lower clock frequency); hence, lower performance

## Slide 4: Review: Multi Cycle Processor
Advantages
  Better MIPS and smaller clock period (higher clock frequency)
  Hence, better performance than Single Cycle processor
Disadvantages
  Higher CPI than single cycle processor
Pipelining: Want better Performance
  want small CPI (close to 1) with high MIPS and short clock period (high clock frequency)

## Slide 5: Improving Performance
Parallelism
Pipelining
Both!

## Slide 6: The Kids
Alice
Bob
They don’t always get along…

## Slide 7: The Bicycle

## Slide 8: The Materials
Saw
Drill
Glue
Paint

## Slide 9: The Instructions
N pieces, each built following same sequence:
Saw
Drill
Glue
Paint

## Slide 10: Design 1: Sequential Schedule
Alice owns the room
Bob can enter when Alice is finished
Repeat for remaining tasks
No possibility for conflicts

## Slide 11: Sequential Performance
Elapsed Time for Alice: 4
Elapsed Time for Bob: 4
Total elapsed time: 4*N
Can we do better?
time 1 2 3 4 5 6 7 8 …
Latency:
Throughput:
Concurrency:
Latency: 4 hours/task
Throughput: 1 task/4 hrs
Concurrency: 1
CPI = 4

## Slide 12: Design 2: Pipelined Design
Partition room into stages of a pipeline
One person owns a stage at a time
4 stages
4 people working simultaneously
Everyone moves right in lockstep
Alice
Bob
Carol
Dave

## Slide 13: Design 2: Pipelined Design
Partition room into stages of a pipeline
One person owns a stage at a time
4 stages
4 people working simultaneously
Everyone moves right in lockstep
It still takes all four stages for one job to complete
Alice

## Slide 14: Design 2: Pipelined Design
Partition room into stages of a pipeline
One person owns a stage at a time
4 stages
4 people working simultaneously
Everyone moves right in lockstep
It still takes all four stages for one job to complete
Alice
Bob

## Slide 15: Design 2: Pipelined Design
Partition room into stages of a pipeline
One person owns a stage at a time
4 stages
4 people working simultaneously
Everyone moves right in lockstep
It still takes all four stages for one job to complete
Alice
Bob
Carol
Dave

## Slide 16: Design 2: Pipelined Design
Partition room into stages of a pipeline
One person owns a stage at a time
4 stages
4 people working simultaneously
Everyone moves right in lockstep
It still takes all four stages for one job to complete
Alice
Alice
Alice
Alice

## Slide 17: Pipelined Performance
time 1 2 3 4 5 6 7…
Latency: 4 hrs/task
Throughput: 1 task/hr
Concurrency: 4
CPI = 1

## Slide 18: Pipelined Performance
Time
1 2 3 4 5 6 7 8 9 10
Latency:
Throughput:
CPI =
What if drilling takes twice as long, but gluing and paint take ½ as long?

## Slide 19: Pipelined Performance
Time
1 2 3 4 5 6 7 8 9 10
Latency: 4 cycles/task
Throughput: 1 task/2 cycles
Done: 4 cycles
Done: 6 cycles
CPI = 2
What if drilling takes twice as long, but gluing and paint take ½ as long?
Done: 8 cycles

## Slide 20: Lessons
Principle:
Throughput increased by parallel execution
Balanced pipeline very important
  Else slowest stage dominates performance
Pipelining:
  Identify pipeline stages
  Isolate stages from each other
  Resolve pipeline hazards (next lecture)

## Slide 21
Single Cycle vs Pipelined Processor

## Slide 22: Single Cycle  Pipelining
insn0.fetch, dec, exec
Single-cycle
insn1.fetch, dec, exec
Pipelined
insn0.dec
insn0.fetch
insn1.dec
insn1.fetch
insn0.exec
insn1.exec

## Slide 23: Agenda
5-stage Pipeline
Implementation
Working Example
Hazards
Structural
Data Hazards
Control Hazards

## Slide 24: Review: Single Cycle Processor
alu
PC
imm
memory
memory
din
dout
addr
target
offset
cmp
control
=?
new pc
register file
inst
extend
+4
+4

## Slide 25: Pipelined Processor
alu
PC
imm
memory
memory
din
dout
addr
control
new pc
register file
inst
extend
+4
compute jump/branch targets
Fetch
Decode
Execute
Memory
WB

## Slide 26: Pipelined Processor
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4

## Slide 27: Time Graphs
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Cycle
Latency:
Throughput:
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
Latency: 5 cycles
Throughput: 1 insn/cycle
Concurrency: 5
CPI = 1
add
nand
lw
add
sw

## Slide 28: Principles of Pipelined Implementation
Break datapath into multiple cycles (here 5)
  Parallel execution increases throughput
  Balanced pipeline very important
    Slowest stage determines clock rate
    Imbalance kills performance
Add pipeline registers (flip-flops) for isolation
  Each stage begins by reading values from latch
  Each stage ends by writing values to latch
Resolve hazards

## Slide 29: Pipelined Processor
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4

## Slide 30: Pipeline Stages
Stage | Perform Functionality | Latch values of interest
Fetch | Use PC to index Program Memory, increment PC | Instruction bits (to be decoded) PC + 4 (to compute branch targets)
Decode | Decode instruction, generate control signals, read register file | Control information, Rd index, immediates, offsets, register values (Ra, Rb), PC+4 (to compute branch targets)
Execute | Perform ALU operation Compute targets (PC+4+offset, etc.) in case this is a branch, decide if branch taken | Control information, Rd index, etc. Result of ALU operation, value in case this is a store instruction
Memory | Perform load/store if needed, address is ALU result | Control information, Rd index, etc. Result of load, pass result from execute
Writeback | Select value, write to register file | 

## Slide 31: Instruction Fetch (IF)
Stage 1: Instruction Fetch
Fetch a new instruction every cycle
  Current PC is index to instruction memory
  Increment the PC at end of cycle (assume no branches for now)
Write values of interest to pipeline register (IF/ID)
  Instruction bits (for later decoding)
  PC+4 (for later computing branch targets)

## Slide 32: Instruction Fetch (IF)
PC
instruction memory
new pc
addr
mc
+4
- PC+4
- pc-rel (PC-relative); e.g. JAL, BEQ, BNE
- pc-reg (PC registers); e.g. JALR

## Slide 33: Instruction Fetch (IF)
PC
instruction memory
addr
mc
+4
inst
IF/ID
Rest of pipeline
PC+4
00 = read word
pc-sel
pc-reg
pc-rel

## Slide 34: Decode
Stage 2: Instruction Decode
On every cycle:
  Read IF/ID pipeline register to get instruction bits
  Decode instruction, generate control signals
  Read from register file
Write values of interest to pipeline register (ID/EX)
  Control information, Rd index, immediates, offsets, …
  Contents of Ra, Rb
  PC+4 (for computing branch targets later)

## Slide 35: Decode
ctrl
ID/EX
Rest of pipeline
PC+4
inst
IF/ID
PC+4
Stage 1: Instruction Fetch
register file
WE
Rd
Ra
Rb
D
B
A
B
A
extend
imm
decode
result
dest

## Slide 36: Execute (EX)
Stage 3: Execute
On every cycle:
  Read ID/EX pipeline register to get values and control bits
  Perform ALU operation
  Compute targets (PC+4+offset, etc.) in case this is a branch
  Decide if jump/branch should be taken
Write values of interest to pipeline register (EX/MEM)
  Control information, Rd index, …
  Result of ALU operation
  Value in case this is a memory store instruction

## Slide 37: Execute (EX)
Stage 2: Instruction Decode
pcrel
ctrl
EX/MEM
Rest of pipeline
B
D
ctrl
ID/EX
PC+4
B
A
alu
+
branch?
imm
pcsel
pcreg
target

## Slide 38: MEM
Stage 4: Memory
On every cycle:
  Read EX/MEM pipeline register to get values and control bits
  Perform memory load/store if needed
    address is ALU result
Write values of interest to pipeline register (MEM/WB)
  Control information, Rd index, …
  Result of memory operation
  Pass result of ALU operation

## Slide 39: MEM
ctrl
MEM/WB
Rest of pipeline
Stage 3: Execute
M
D
ctrl
EX/MEM
B
D
memory
din
dout
addr
mc
target
branch?
pcsel
pcrel
pcreg

## Slide 40: WB
Stage 5: Write-back
On every cycle:
  Read MEM/WB pipeline register to get values and control bits
  Select value and write to register file

## Slide 41: WB
Stage 4: Memory
ctrl
MEM/WB
M
D
result
dest

## Slide 42
IF/ID
+4
ID/EX
EX/MEM
MEM/WB
mem
din
dout
addr
PC
inst mem
Rd
Ra
Rb
D
B
A
Rd
Putting it all together
inst
PC+4
B
A
Rt
B
D
M
D
PC+4
imm
OP
Rd
OP
Rd
OP

## Slide 43: iClicker Question
Consider a non-pipelined processor with clock period C (e.g., 50 ns). If you divide the processor into N stages (e.g., 5) , your new clock period will be:
C
N
less than C/N
C/N
greater than C/N

## Slide 44: iClicker Question
Consider a non-pipelined processor with clock period C (e.g., 50 ns). If you divide the processor into N stages (e.g., 5) , your new clock period will be:
C
N
less than C/N
C/N
greater than C/N

## Slide 45: Takeaway
Pipelining is a powerful technique to mask latencies and increase throughput
  Logically, instructions execute one at a time
  Physically, instructions execute in parallel
    Instruction level parallelism
Abstraction promotes decoupling
  Interface (ISA) vs. implementation (Pipeline)

## Slide 46: RISC-V is designed for pipelining
Instructions same length
  32 bits, easy to fetch and then decode
4 types of instruction formats
  Easy to route bits between stages
  Can read a register source before even knowing what the instruction is
Memory access through lw and sw only
  Access memory after ALU

## Slide 47: Agenda
5-stage Pipeline
Implementation
Working Example
Hazards
Structural
Data Hazards
Control Hazards

## Slide 48: Example: Sample Code (Simple)
add x3  x1, x2 nand x6  x4, x5 lw x4  x2, 20 add x5  x2, x5 sw x7  x3, 12
Assume 8-register machine

## Slide 49
PC
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 7-11
op
imm
valB
valA
PC+4
PC+4
target
ALU
result
op
dest
valB
op
dest
ALU
result
mdata
instruction
0
x2
x3
x4
x5
x1
x6
x0
x7
regA
regB
Bits 0-6
data
dest
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
Rd
Inst
mem

## Slide 50: Example: Start State @ Cycle 0
PC
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 7-11
nop
0
0
0
0
0
0
0
nop
0
0
nop
0
0
0
nop
9
12
18
7
36
41
0
22
x2
x3
x4
x5
x1
x6
x0
x7
regA
regB
Bits 0-6
data
dest
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
0
At time 1,
Fetch
add x3 x1 x2
0
4
Add
Nand
Lw
Add
sw
Initial State
0

## Slide 51: Cycle 1: Fetch add
PC
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 7-11
nop
0
0
0
0
4
0
0
nop
0
0
nop
0
0
0
add 3 1 2
9
12
18
7
36
41
0
22
x2
x3
x4
x5
x1
x6
x0
x7
regA
regB
Bits 0-6
data
dest
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
0
4
8
Add
Nand
Lw
Add
sw
0
Fetch:
add 3 1 2
Time: 1
add 3 1 2
/ 2
/ 36
/ 9
/ add
/ 3
/ 4

## Slide 52: Cycle 2: Fetch nand, Decode add
PC
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 7-11
add
3
9
36
4
8
0
0
nop
0
0
nop
0
0
0
nand 6 4 5
9
12
18
7
36
41
0
22
x2
x3
x4
x5
x1
x6
x0
x7
1
2
Bits 0-6
data
dest
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
3
8
12
Add
Nand
Lw
Add
sw
0
Fetch:
nand 6 4 5
Time: 2
nand 6 4 5 add 3 1 2
36
9
3
/ 3
/ 45
/ add
/ 9
/ 3
/ 4
/ 18
/ 7
/ nand
/ 6
/ 8

## Slide 53: Cycle 3: Fetch lw, Decode nand, …
PC
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 7-11
nand
3
7
18
8
8
4
45
add
3
9
nop
3
0
0
lw 4 2 20
9
12
18
7
36
41
0
22
x2
x3
x4
x5
x1
x6
x0
x7
4
5
Bits 0-6
data
dest
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
6
12
16
Add
Nand
Lw
Add
sw
0
Fetch:
lw 4 2 20
Time: 3
36
9
3
lw 4 2 20 nand 6 4 5 add 3 1 2
nand ()
18 = 01 0010
7 = 00 0111
------------------
-3 = 11 1101
/ 4
/ 45
/ 3
/ add
/ 18
/ 7
/ -3
/ nand
/ 7
/ 6
/ 8

## Slide 54: Cycle 4: Fetch add, Decode lw, …
PC
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 7-11
lw
20
18
9
12
16
8
-3
nand
6
7
add
3
45
0
add 5 2 5
9
12
18
7
36
41
0
22
x2
x3
x4
x5
x1
x6
x0
x7
2
4
Bits 0-6
data
dest
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
4
16
20
Add
Nand
Lw
Add
sw
0
Fetch:
add 5 2 5
Time: 4
18
7
6
add 5 2 5 lw 4 2 20 nand 6 4 5 add 3 1 2
45
3

## Slide 55: Cycle 5: Fetch sw, Decode add, …
PC
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 7-11
add
5
7
9
16
20
12
29
lw
4
18
nand
6
-3
0
sw 7 3 12
9
45
18
7
36
41
0
22
x2
x3
x4
x5
x1
x6
x0
x7
2
5
Bits 0-6
data
dest
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
5
20
24
Add
Nand
Lw
Add
sw
0
Fetch:
sw 7 3 12
Time: 5
9
4
-3
6
sw 7 3 12 add 5 2 5 lw 4 20 (2) nand 6 4 5 add 3 1 2
20
45
3

## Slide 56: Cycle 6: Decode sw, …
PC
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 7-11
sw
12
22
45
20
16
16
add
5
7
lw
4
29
99
9
45
18
7
36
-3
0
22
x2
x3
x4
x5
x1
x6
x0
x7
3
7
Bits 0-6
data
dest
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
0
24
28
Add
Nand
Lw
Add
sw
0
No more
instructions
Time: 6
9
5
29
4
7
-3
6
sw 7 3 12 add 5 2 5 lw 4 2 20 nand 6 4 5

## Slide 57: Cycle 7: Execute sw, ...
PC
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 7-11
20
57
sw
7
22
add
5
16
0
9
45
99
7
36
-3
0
22
x2
x3
x4
x5
x1
x6
x0
x7
Bits 0-6
data
dest
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
28
32
Add
Nand
Lw
Add
sw
0
No more
instructions
Time: 7
45
7
16
5
12
99
4
nop nop sw 7 3 12 add 5 2 5 lw 4 2 20

## Slide 58: Cycle 8: Memory sw, ...
PC
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 7-11
sw
7
57
0
9
45
99
16
36
-3
0
22
x2
x3
x4
x5
x1
x6
x0
x7
Bits 0-6
data
dest
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
32
36
Add
Nand
Lw
Add
sw
No more
instructions
Time: 8
57
22
16
5
nop nop nop sw 7 3 12 add 5 2 5

## Slide 59: Cycle 9: Writeback sw, ...
PC
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 7-11
9
45
99
16
36
-3
0
22
x2
x3
x4
x5
x1
x6
x0
x7
Bits 0-6
data
dest
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
36
40
Add
Nand
Lw
Add
sw
No more
instructions
Time: 9
nop nop nop nop sw 7 3 12

## Slide 60: iClicker Question
Pipelining is great because:
You can fetch and decode the same instruction at the same time.
You can fetch two instructions at the same time.
You can fetch one instruction while decoding another.
Instructions only need to visit the pipeline stages that they require.
C and D

## Slide 61: iClicker Question
Pipelining is great because:
You can fetch and decode the same instruction at the same time.
You can fetch two instructions at the same time.
You can fetch one instruction while decoding another.
Instructions only need to visit the pipeline stages that they require.
C and D

## Slide 62: Pipelined Processor
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4

## Slide 63: Agenda
5-stage Pipeline
Implementation
Working Example
Hazards
Structural
Data Hazards
Control Hazards

## Slide 64: Hazards
Correctness problems associated w/ processor design
  Structural hazards
  Same resource needed for different purposes at the same time (Possible: ALU, Register File, Memory)
  Data hazards
    Instruction output needed before it’s available
  Control hazards
    Next instruction PC unknown at time of Fetch

## Slide 65: Dependences and Hazards
Dependence: relationship between two insns
  Data: two insns use same storage location
  Control: 1 insn affects whether another executes at all
  Not a bad thing, programs would be boring otherwise
  Enforced by making older insn go before younger one
    Happens naturally in single-/multi-cycle designs
    But not in a pipeline
Hazard: dependence & possibility of wrong insn order
  Effects of wrong insn order cannot be externally visible
  Hazards are a bad thing: most solutions either complicate the hardware or reduce performance

## Slide 66: iClicker Question
Data Hazards
  register file (RF) reads occur in stage 2 (ID)
  RF writes occur in stage 5 (WB)
  RF written in ½ half, read in second ½ half of cycle
  x10: add x3  x1, x2
  x14: sub x5  x3, x4
1. Is there a dependence?
2. Is there a hazard?
Yes
No
Cannot tell with the information given.

## Slide 67: iClicker Question
Data Hazards
  register file (RF) reads occur in stage 2 (ID)
  RF writes occur in stage 5 (WB)
  RF written in ½ half, read in second ½ half of cycle
  x10: add x3  x1, x2
  x14: sub x5  x3, x4
1. Is there a dependence?
2. Is there a hazard?
Yes
No
Cannot tell with the information given.
for both

## Slide 68: iClicker Follow-up
Which of the following statements is true?
A. Whether there is a data dependence between two instructions depends on the machine the program is running on.
B. Whether there is a data hazard between two instructions depends on the machine the program is running on.
C. Both A & B
D. Neither A nor B

## Slide 69: iClicker Follow-up
Which of the following statements is true?
A. Whether there is a data dependence between two instructions depends on the machine the program is running on.
B. Whether there is a data hazard between two instructions depends on the machine the program is running on.
C. Both A & B
D. Neither A nor B

## Slide 70: Where are the Data Hazards?
IF
ID
MEM
WB
IF
ID
MEM
WB
IF
ID
MEM
WB
IF
ID
MEM
WB
IF
ID
MEM
WB
Clock cycle
1 2 3 4 5 6 7 8 9
time
sub x5, x3, x4
lw x6, x3, 4
or x5, x3, x5
sw x6, x3, 12
add x3, x1, x2

## Slide 71: iClicker
How many data hazards due to x3 only
1
2
3
4
5
sub x5, x3, x4
lw x6, x3, 4
or x5, x3, x5
sw x6, x3, 12
add x3, x1, x2

## Slide 72: Visualizing Data Hazards (1)
IF
ID
MEM
WB
IF
ID
MEM
WB
IF
ID
MEM
WB
IF
ID
MEM
WB
IF
ID
MEM
WB
Clock cycle
1 2 3 4 5 6 7 8 9
sub x5, x3, x4
lw x6, x3, 4
or x5, x3, x5
sw x6, x3, 12
add x3, x1, x2
time
backwards arrows require time travel

## Slide 73: Visualizing Data Hazards (2)
IF
ID
MEM
WB
IF
ID
MEM
WB
IF
ID
MEM
WB
IF
ID
MEM
WB
IF
ID
MEM
WB
Clock cycle
1 2 3 4 5 6 7 8 9
time
sub x5, x3, x4
lw x6, x3, 4
or x5, x3, x5
sw x6, x3, 12
add x3, x1, x2
backwards arrows require time travel

## Slide 74: Visualizing Data Hazards (3)
IF
ID
MEM
WB
IF
ID
MEM
WB
IF
ID
MEM
WB
IF
ID
MEM
WB
IF
ID
MEM
WB
Clock cycle
1 2 3 4 5 6 7 8 9
time
sub x5, x3, x4
lw x6, x3, 4
or x5, x3, x5
sw x6, x3, 12
add x3, x1, x2
backwards arrows require time travel

## Slide 75: Data Hazards
  register file reads occur in stage 2 (ID)
  register file writes occur in stage 5 (WB)
  next instructions may read values about to be written
i.e. add x3, x1, x2
sub x5, x3, x4
How to detect?

## Slide 76
IF/ID
+4
ID/EX
EX/MEM
MEM/WB
mem
din
dout
addr
PC
inst mem
Rd
Ra
Rb
D
B
A
Rd
Detecting Data Hazards
inst
PC+4
B
A
Rt
B
D
M
D
PC+4
imm
OP
Rd
OP
Rd
OP
IF/ID.Rs1 ≠ 0 &&
(IF/ID.Rs1==ID/Ex.Rd
IF/ID.Rs1==Ex/M.Rd
IF/ID.Rs1==M/W.Rd)
repeat for Rs2
add x3, x1, x2
sub x5,x3,x4

## Slide 77: Data Hazards
Data Hazards
  register file reads occur in stage 2 (ID)
  register file writes occur in stage 5 (WB)
  next instructions may read values about to be written
How to detect? Logic in ID stage:
stall = (IF/ID.Rs1 != 0 &&
(IF/ID.Rs1 == ID/EX.Rd || IF/ID.Rs1 == EX/M.Rd || IF/ID.Rs1 == M/WB.Rd))
|| (same for Rs2)

## Slide 78
IF/ID
+4
ID/EX
EX/MEM
MEM/WB
mem
din
dout
addr
PC
inst mem
Rd
Ra
Rb
D
B
A
Rd
Detecting Data Hazards
inst
PC+4
B
A
Rt
B
D
M
D
PC+4
imm
OP
Rd
OP
Rd
OP
detect hazard

## Slide 79: Takeaway
Data hazards occur when a operand (register) depends on the result of a previous instruction that may not be computed yet. A pipelined processor needs to detect data hazards.

## Slide 80: Next Goal
What to do if data hazard detected?

## Slide 81: iClicker
What to do if data hazard detected?
Wait/Stall
Reorder in Software (SW)
Forward/Bypass
All the above
None. We will use some other method

## Slide 82: Possible Responses to Data Hazards
Do Nothing
  Change the ISA to match implementation
  “Hey compiler: don’t create code w/data hazards!”
  (We can do better than this)
Stall
  Pause current and subsequent instructions till safe
Forward/bypass
  Forward data value to where it is needed
  (Only works if value actually exists already)

## Slide 83: Stalling
How to stall an instruction in ID stage
  prevent IF/ID pipeline register update
    stalls the ID stage instruction
  convert ID stage instr into nop for later stages
    innocuous “bubble” passes through pipeline
  prevent PC update
    stalls the next (IF stage) instruction

## Slide 84
inst mem
IF/ID
+4
ID/EX
EX/MEM
MEM/WB
mem
din
dout
addr
PC
Rd
Ra
Rb
D
B
A
Rd
Detecting Data Hazards
inst
PC+4
B
A
Rt
B
D
M
D
PC+4
imm
OP
Rd
OP
Rd
OP
detect hazard
add x3, x1, x2
sub x5, x3, x5
or x6, x3, x4
add x6, x3, x8
If detect hazard
WE=0
MemWr=0
RegWr=0

## Slide 85: Stalling
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add x3, x1, x2 |  |  |  |  |  |  |  |  | 
sub x5, x3, x5 |  |  |  |  |  |  |  |  | 
or x6, x3, x4 |  |  |  |  |  |  |  |  | 
add x6, x3, x8 |  |  |  |  |  |  |  |  | 
time

## Slide 86: Stalling
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add x3, x1, x2 |  |  |  |  |  |  |  |  | 
sub x5, x3, x5 |  |  |  |  |  |  |  |  | 
or x6, x3, x4 |  |  |  |  |  |  |  |  | 
add x6, x3, x8 |  |  |  |  |  |  |  |  | 
time
x3 = 10
x3 = 20
IF
ID
Ex
M
W
IF
ID
Ex
M
W
IF
ID
Ex
M
ID
ID
IF
IF
IF
IF
ID
Ex
3 Stalls
ID

## Slide 87: Stalling
data mem
B
A
B
D
M
D
inst mem
D rD
B
A
Rd
Rd
Rd
WE
WE
Op
WE
Op
rA rB
PC
+4
Op
nop
inst
/stall
add x3,x1,x2
(MemWr=0
RegWr=0)
NOP = If(IF/ID.Rs1 ≠ 0 &&
(IF/ID.Rs1==ID/Ex.Rd IF/ID.Rs1==Ex/M.Rd
IF/ID.Rs1==M/W.Rd))
sub x5,x3,x5
or x6,x3,x4
(WE=0)
STALL CONDITION MET

## Slide 88: Stalling
data mem
B
A
B
D
M
D
inst mem
D rD
B
A
Rd
Rd
Rd
WE
WE
Op
WE
Op
rA rB
PC
+4
Op
nop
inst
/stall
add x3,x1,x2
NOP = If(IF/ID.Rs1 ≠ 0 &&
(IF/ID.Rs1==ID/Ex.Rd IF/ID.Rs1==Ex/M.Rd
IF/ID.Rs1==M/W.Rd))
sub x5,x3,x5
or x6,x3,x4
STALL CONDITION MET
nop
(MemWr=0
RegWr=0)
(MemWr=0
RegWr=0)
(WE=0)

## Slide 89: Stalling
data mem
B
A
B
D
M
D
inst mem
D rD
B
A
Rd
Rd
Rd
WE
WE
Op
WE
Op
rA rB
PC
+4
Op
nop
inst
/stall
add x3,x1,x2
NOP = If(IF/ID.Rs1 ≠ 0 &&
(IF/ID.Rs1==ID/Ex.Rd IF/ID.Rs1==Ex/M.Rd
IF/ID.Rs1==M/W.Rd))
sub x5,x3,x5
or x6,x3,x4
STALL CONDITION MET
nop
(MemWr=0
RegWr=0)
nop
(MemWr=0
RegWr=0)
(MemWr=0
RegWr=0)
(WE=0)

## Slide 90: Stalling
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add x3, x1, x2 |  |  |  |  |  |  |  |  | 
sub x5, x3, x5 |  |  |  |  |  |  |  |  | 
or x6, x3, x4 |  |  |  |  |  |  |  |  | 
add x6, x3, x8 |  |  |  |  |  |  |  |  | 
time
x3 = 10
x3 = 20
IF
ID
Ex
M
W
IF
ID
Ex
M
W
IF
ID
Ex
M
ID
ID
IF
IF
IF
IF
ID
Ex
3 Stalls
ID

## Slide 91: Stalling
How to stall an instruction in ID stage
  prevent IF/ID pipeline register update
    stalls the ID stage instruction
  convert ID stage instr into nop for later stages
    innocuous “bubble” passes through pipeline
  prevent PC update
    stalls the next (IF stage) instruction

## Slide 92: Takeaway
Data hazards occur when a operand (register) depends on the result of a previous instruction that may not be computed yet. A pipelined processor needs to detect data hazards.
Stalling, preventing a dependent instruction from advancing, is one way to resolve data hazards.
Stalling introduces NOPs (“bubbles”) into a pipeline. Introduce NOPs by (1) preventing the PC from updating, (2) preventing writes to IF/ID registers from changing, and (3) preventing writes to memory and register file.
*Bubbles in pipeline significantly decrease performance.

## Slide 93: Possible Responses to Data Hazards
Do Nothing
  Change the ISA to match implementation
  “Compiler: don’t create code with data hazards!”
  (Nice try, we can do better than this)
Stall
  Pause current and subsequent instructions till safe
Forward/bypass
  Forward data value to where it is needed
  (Only works if value actually exists already)
Notes: Nothing: Modify ISA to match implementation
Stall: Pause current and all subsequent instruction
Forward/Bypass: Steal correct value from elsewhere in pipeline

## Slide 94: Forwarding
Forwarding bypasses some pipelined stages forwarding a result to a dependent instruction operand (register).
Three types of forwarding/bypass
  Forwarding from Ex/Mem registers to Ex stage (MEx)
  Forwarding from Mem/WB register to Ex stage (WEx)
  RegisterFile Bypass

## Slide 95: Add the Forwarding Datapath
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rs2
WE
WE
MC
Rs1
MC
forward unit
detect hazard
IF/ID
ID/Ex
Ex/Mem
Mem/WB
Notes: draw control signals

## Slide 96: Forwarding Datapath
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rs2
WE
WE
MC
Rs1
MC
forward unit
detect hazard
IF/ID
ID/Ex
Ex/Mem
Mem/WB
Three types of forwarding/bypass
Forwarding from Ex/Mem registers to Ex stage (MEx)
Forwarding from Mem/WB register to Ex stage (W  Ex)
RegisterFile Bypass
Notes: draw control signals

## Slide 97: Forwarding Datapath 1: Ex/MEM  EX
add x3, x1, x2 |  |  |  |  |  |  | 
sub x5, x3, x1 |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
IF
ID
Ex
M
W
IF
ID
Ex
M
W
add x3, x1, x2
sub x5, x3, x1
Problem: EX needs ALU result that is in MEM stage
Solution: add a bypass from EX/MEM.D to start of EX
Ex/Mem

## Slide 98: Forwarding Datapath 1: Ex/MEM  EX
data mem
inst mem
D
B
A
add x3, x1, x2
sub x5, x3, x1
Ex/Mem
Detection Logic in Ex Stage:
forward = (Ex/M.WE && EX/M.Rd != 0 &&
ID/Ex.Rs1 == Ex/M.Rd)
|| (same for Rs2)

## Slide 99: Forwarding Datapath 2: Mem/WB EX
data mem
inst mem
D
B
A
add x3, x1, x2
sub x5, x3, x1
Problem: EX needs value being written by WB
Solution: Add bypass from WB final value to start of EX
or x6, x3, x4
add x3, x1, x2 |  |  |  |  |  |  |  | 
sub x5, x3, x1 |  |  |  |  |  |  |  | 
or x6, x3, x4 |  |  |  |  |  |  |  | 
IF
ID
Ex
M
IF
ID
IF
Ex
ID
Problem: EX needs value being written by WB
Solution: Add bypass from WB final value to start of EX
Mem/WB

## Slide 100: Forwarding Datapath 2: Mem/WB EX
data mem
inst mem
D
B
A
add x3, x1, x2
sub x5, x3, x1
Problem: EX needs value being written by WB
Solution: Add bypass from WB final value to start of EX
or x6, x3, x4
add x3, x1, x2 |  |  |  |  |  |  |  | 
sub x5, x3, x1 |  |  |  |  |  |  |  | 
or x6, x3, x4 |  |  |  |  |  |  |  | 
IF
ID
Ex
M
W
IF
ID
IF
W
Ex
M
W
ID
Ex
M
Problem: EX needs value being written by WB
Solution: Add bypass from WB final value to start of EX
Mem/WB

## Slide 101: Forwarding Datapath 2: Mem/WB EX
data mem
inst mem
D
B
A
add x3, x1, x2
sub x5, x3, x1
or x6, x3, x4
Mem/WB
Detection Logic:
forward = (M/WB.WE && M/WB.Rd != 0 &&
ID/Ex.Rs1 == M/WB.Rd &&
not (Ex/M.WE && Ex/M.Rd != 0 &&
ID/Ex.Rs1 == Ex/M.Rd)
|| (same for Rs2)

## Slide 102: Register File Bypass
data mem
inst mem
D
B
A
Problem: Reading a value that is currently being written
Solution: just negate register file clock
  writes happen at end of first half of each clock cycle
  reads happen during second half of each clock cycle
add x3, x1,x2
sub x5, x3, x1
or x6, x3, x4
add x6, x3, x8

## Slide 103: Register File Bypass
data mem
inst mem
D
B
A
add x3, x1,x2
sub x5, x3, x1
or x6, x3, x4
add x6, x3, x8
add x3, x1, x2 |  |  |  |  |  |  |  |  | 
sub x5, x3, x1 |  |  |  |  |  |  |  |  | 
or x6, x3, x4 |  |  |  |  |  |  |  |  | 
add x6, x3, x8 |  |  |  |  |  |  |  |  | 
IF
ID
Ex
M
W
IF
ID
IF
W
Ex
M
W
ID
Ex
M
IF
ID
Ex
M
W

## Slide 104: Agenda
5-stage Pipeline
Implementation
Working Example
Hazards
Structural
Data Hazards
Control Hazards

## Slide 105: Forwarding Example 2
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add x3, x1, x2 |  |  |  |  |  |  |  |  | 
sub x5, x3, x5 |  |  |  |  |  |  |  |  | 
lw x6, x3, 4 |  |  |  |  |  |  |  |  | 
or x5, x3, x6 |  |  |  |  |  |  |  |  | 
sw x6, x3, 12 |  |  |  |  |  |  |  |  | 
time
Notes: identify hazards then draw; if “or” had used r6, would have needed to stallx

## Slide 106: Forwarding Example 2
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add x3, x1, x2 |  |  |  |  |  |  |  |  | 
sub x5, x3, x5 |  |  |  |  |  |  |  |  | 
lw x6, x3, 4 |  |  |  |  |  |  |  |  | 
or x5, x3, x6 |  |  |  |  |  |  |  |  | 
sw x6, x3, 12 |  |  |  |  |  |  |  |  | 
time
IF
ID
Ex
M
W
IF
ID
IF
W
Ex
M
W
ID
Ex
M
IF
ID
Ex
M
W
IF
ID
Ex
M
W
Notes: identify hazards then draw; if “or” had used x6, would have needed to stall

## Slide 107: Forwarding Example 2
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add x3, x1, x2 |  |  |  |  |  |  |  |  | 
sub x5, x3, x5 |  |  |  |  |  |  |  |  | 
lw x6, x3, 4 |  |  |  |  |  |  |  |  | 
or x5, x3, x6 |  |  |  |  |  |  |  |  | 
sw x6, x3, 12 |  |  |  |  |  |  |  |  | 
time
IF
ID
Ex
M
W
IF
ID
IF
W
Ex
M
W
ID
Ex
M
IF
ID
Ex
M
W
IF
ID
Ex
M
W
backwards arrows require time travel

## Slide 108: Load-Use Hazard Explained
data mem
inst mem
D
B
A
lw x4, x8, 20
or x5, x3, x4
Data dependency after a load instruction:
  Value not available until after the M stage
  Next instruction cannot proceed if dependent
THE KILLER HAZARD
Notes: often see lw …; nop; …
we will stall for our project 2

## Slide 109: Load-Use Stall
data mem
inst mem
D
B
A
lw x4, x8, 20 |  |  |  |  |  |  |  |  | 
or x6, x4, x1 |  |  |  |  |  |  |  |  | 
lw x4, x8, 20
or x6, x4, x1

## Slide 110: Load-Use Stall (1)
data mem
inst mem
D
B
A
lw x4, x8, 20
or x6, x4, x1
lw x4, x8, 20 |  |  |  |  |  |  |  |  | 
or x6, x4, x1 |  |  |  |  |  |  |  |  | 
IF
ID
Ex
IF
ID

## Slide 111: Load-Use Stall (2)
data mem
inst mem
D
B
A
lw x4, x8, 20
or x6, x4, x1
lw x4, x8, 20 |  |  |  |  |  |  |  |  | 
or x6, x4, x1 |  |  |  |  |  |  |  |  | 
IF
ID
Ex
IF
ID*
NOP
M
W
Ex
M
W
ID
Stall
Notes: requires one bubble

## Slide 112: Load-Use Stall (3)
data mem
inst mem
D
B
A
lw x4, x8, 20
or x6, x4, x1
lw x4, x8, 20 |  |  |  |  |  |  |  |  | 
or x6, x4, x1 |  |  |  |  |  |  |  |  | 
IF
ID
Ex
IF
ID*
NOP
M
W
Ex
M
W
ID
Stall

## Slide 113: Load-Use Detection
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rs2
WE
WE
MC
Rs1
MC
forward unit
detect hazard
IF/ID
ID/Ex
Ex/Mem
Mem/WB
Rd
MC
Stall = If(ID/Ex.MemRead &&
IF/ID.Rs1 == ID/Ex.Rd
Notes: It happens in an earlier stage. You stall since you don’t want to go ahead from the ID stage unless you are ready.
Walk through what happens with a

## Slide 114: Incorrectly Resolving Load-Use Hazards
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rs2
WE
WE
MC
Rs1
MC
forward unit
detect hazard
IF/ID
ID/Ex
Ex/Mem
Mem/WB
Rd
MC
Most frequent 3410 non-solution to load-use hazards
Why is this “solution” so so so so so so awful?

## Slide 115: iClicker Question
Forwarding values directly from Memory to the Execute stage without storing them in a register first:
Does not remove the need to stall.
Adds one too many possible inputs to the ALU.
Will cause the pipeline register to have the wrong value.
Halves the frequency of the processor.
Both A & D

## Slide 116: iClicker Question
Forwarding values directly from Memory to the Execute stage without storing them in a register first:
Does not remove the need to stall.
Adds one too many possible inputs to the ALU.
Will cause the pipeline register to have the wrong value.
Halves the frequency of the processor.
Both A & D

## Slide 117: Resolving Load-Use Hazards
  RISC-V Solution : Load-Use Stall
  Stall must be inserted so that load instruction can go through and update the register file.
  Forwarding from RAM is not an option.
  In some cases, real world compilers can optimize to avoid these situations.

## Slide 118: Takeaway
Data hazards occur when a operand (register) depends on the result of a previous instruction that may not be computed yet. A pipelined processor needs to detect data hazards.
Stalling, preventing a dependent instruction from advancing, is one way to resolve data hazards. Stalling introduces NOPs (“bubbles”) into a pipeline. Introduce NOPs by (1) preventing the PC from updating, (2) preventing writes to IF/ID registers from changing, and (3) preventing writes to memory and register file. Bubbles (nops) in pipeline significantly decrease performance.
Forwarding bypasses some pipelined stages forwarding a result to a dependent instruction operand (register). Better performance than stalling.

## Slide 119: Quiz
Find all hazards, and say how they are resolved:
add x3, x1, x2
nand x5, x3, x4
add x2, x6, x3
lw x6, x3, 24
sw x6, x2, 12
Notes: Find all hazards, and say how they are resolved

## Slide 120: Quiz
Find all hazards, and say how they are resolved:
add x3, x1, x2
nand x5, x3, x4
add x2, x6, x3
lw x6, x3, 24
sw x6, x2, 12
5 Hazards
Notes: Find all hazards, and say how they are resolved

## Slide 121: Quiz
Find all hazards, and say how they are resolved:
add x3, x1, x2
nand x5, x3, x4
add x2, x6, x3
lw x6, x3, 24
sw x6, x2, 12
5 Hazards
Forwarding from Ex/MEx (MEx)
Forwarding from M/WEx (WEx)
RegisterFile (RF) Bypass
Forwarding from M/WEx (WEx)
Stall
+ Forwarding from M/WEx (WEx)
Notes: Find all hazards, and say how they are resolved

## Slide 122: Quiz
Find all hazards, and say how they are resolved: add x3, x1, x2 sub x3, x2, x1 nand x4, x3, x1 or x0, x3, x4 xor x1, x4, x3 sb x4, x0, 1
Hours and hours of debugging!
Notes: 6 hazards
be careful of store (no x0)
be careful or x0 (never a hazard)

## Slide 123: Data Hazard Recap
Delay Slot(s)
  Modify ISA to match implementation
Stall
  Pause current and all subsequent instructions
Forward/Bypass
  Try to steal correct value from elsewhere in pipeline
  Otherwise, fall back to stalling or require a delay slot
Tradeoffs?
Notes: 1: ISA tied to impl; messy asm; impl easy & cheap; perf depends on asm.
2: ISA correctness not tied to impl; clean+slow asm, or messy+fast asm; impl easy and cheap; same perf as 1. 3: ISA perf not tied to impl; clean+fast asm; impl is tricky; best perf

## Slide 124: Agenda
5-stage Pipeline
Implementation
Working Example
Hazards
Structural
Data Hazards
Control Hazards

## Slide 125: A bit of Context
i = 0;
do {
n += 2;
i++;
} while(i < max)
i = 7;
n--;
x10 addi x1, x0, 0 # i=0
x14 Loop: addi x2, x2, 2 # n += 2
x18 addi x1, x1, 1 # i++
x1C blt x1, x3, Loop # i<max?
x20 addi x1, x0, 7 # i = 7
x24 subi x2, x2, 1 # n--
i  x1
Assume:
n  x2
max  x3

## Slide 126: Control Hazards
Control Hazards
  instructions are fetched in stage 1 (IF)
  branch and jump decisions occur in stage 3 (EX)
   next PC not known until 2 cycles after branch/jump
x1C blt x1, x3, Loop
x20 addi x1, x0, 7
x24 subi x2, x2, 1
Branch not taken?
No Problem!
Branch taken?
Just fetched 2 insns
 Zap & Flush

## Slide 127: Zap & Flash
data mem
inst mem
D
B
A
prevent PC update
clear IF/ID latch
branch continues
PC
+4
branch calc
decide branch
If branch Taken
New PC = 14
Zap
1C | blt x1,x3,L |  |  |  |  |  |  |  | 
20 | addi x1,x0,7 |  |  |  |  |  |  |  | 
24 | subi x2,x2,1 |  |  |  |  |  |  |  | 
NOP
IF
ID
Ex
M
W
IF
ID
NOP
NOP
NOP
IF
NOP
NOP
NOP
IF
ID
Ex
M
W
14 L:addi x2,x2,2
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 128: Zap & Flash
data mem
inst mem
D
B
A
prevent PC update
clear IF/ID latch
branch continues
PC
+4
branch calc
decide branch
If branch Taken
New PC = 14
Zap
1C | blt x1,x3,L |  |  |  |  |  |  |  | 
20 | addi x1,x0,7 |  |  |  |  |  |  |  | 
24 | subi x2,x2,1 |  |  |  |  |  |  |  | 
NOP
IF
ID
Ex
M
W
IF
ID
NOP
NOP
NOP
IF
NOP
NOP
NOP
IF
ID
Ex
M
W
14 L:addi x2,x2,2
For every taken branch? OUCH!!!
Notes: branch decision in EX
need 2 stalls, and maybe kill

## Slide 129: Reducing the cost of control hazard
Resolve Branch at Decode
  Some groups do this for Project 3, your choice
  Move branch calc from EX to ID
  Alternative: just zap 2nd instruction when branch taken
Branch Prediction
  Not in 3410, but every processor worth anything does this (no offense!)

## Slide 130: Problem: Zapping 2 insns/branch
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
New PC = 14
1C | blt x1,x3,L |  |  |  |  |  |  |  | 
20 | addi x1,x0,7 |  |  |  |  |  |  |  | 
24 | subi x2,x2,1 |  |  |  |  |  |  |  | 
IF
ID
Ex
IF
ID
IF
Zap!
If branch Taken
Zap
Notes: Pipeline is humming

## Slide 131: Soln #1: Resolve Branches @ Decode
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
New PC = 1C
1C | blt x1,x3,L |  |  |  |  |  |  |  | 
20 | addi x1,x0,7 |  |  |  |  |  |  |  | 
24 | L: addi x2,x2,2 |  |  |  |  |  |  |  | 
IF
ID
Ex
IF
ID
IF
One Zap!
If branch Taken
One Zap

## Slide 132: Branch Prediction
Most processor support Speculative Execution
  Guess direction of the branch
    Allow instructions to move through pipeline
    Zap them later if guess turns out to be wrong
  A must for long pipelines

## Slide 133: Speculative Execution: Loops
Pipeline so far
  “Guess” (predict) that the branch will not be taken
We can do better!
  Make prediction based on last branch
  Predict “take branch” if last branch “taken”
  Or Predict “do not take branch” if last branch “not taken”
  Need one bit to keep track of last branch

## Slide 134: Speculative Execution: Loops
While (x3 ≠ 0) {…. x3--;}
Top: BEQ x3, x0, End
J Top
End:
While (r3 ≠ 0) {…. r3--;}
Top2: BEQ x3, x0, End2
J Top
End2:
What is accuracy of branch predictor?
Wrong twice per loop!
Once on loop enter and exit
We can do better with 2 bits

## Slide 135: Speculative Execution: Branch Execution
Predict Taken 2 (PT2)
Branch Taken (T)
Predict Taken 1 (PT1)
Predict Not Taken 1 (PT1)
Predict Not Taken 2 (PT2)
Branch Not Taken (NT)
Branch Taken (T)
Branch Not Taken (NT)
Branch Taken (T)
Branch Not Taken (NT)
Notes: 2 bit prediction scheme

## Slide 136: Summary
Control hazards
  Is branch taken or not?
  Performance penalty: stall and flush
Reduce cost of control hazards
  Move branch decision from Ex to ID
    2 nops to 1 nop
  Branch prediction
    Correct. Great!
    Wrong. Flush pipeline. Performance penalty

## Slide 137: Hazards Summary
Data hazards
Control hazards
Structural hazards
  resource contention
  so far: impossible because of ISA and pipeline design
Notes: Q: what if we had a “copy 0(r3), 4(r3)” instruction, as the x86 does, or “add r4, r4, 0(r3)”?
A: structural hazard

## Slide 138: Hazards Summary
Data hazards
  register file reads occur in stage 2 (IF)
  register file writes occur in stage 5 (WB)
  next instructions may read values soon to be written
Control hazards
  branch instruction may change the PC in stage 3 (EX)
  next instructions have already started executing
Structural hazards
  resource contention
  so far: impossible because of ISA and pipeline design

## Slide 139: Data Hazard Takeaways
Data hazards occur when a operand (register) depends on the result of a previous instruction that may not be computed yet. Pipelined processors need to detect data hazards.
Stalling, preventing a dependent instruction from advancing, is one way to resolve data hazards. Stalling introduces NOPs (“bubbles”) into a pipeline. Introduce NOPs by (1) preventing the PC from updating, (2) preventing writes to IF/ID registers from changing, and (3) preventing writes to memory and register file. Nops significantly decrease performance.
Forwarding bypasses some pipelined stages forwarding a result to a dependent instruction operand (register). Better performance than stalling.

## Slide 140: Control Hazard Takeaways
Control hazards occur because the PC following a control instruction is not known until control instruction is executed. If branch is taken  need to zap instructions. 1 cycle performance penalty.
We can reduce cost of a control hazard by moving branch decision and calculation from Ex stage to ID stage.

## Slide 141: Have a great February Break!!