## Slide 1: Pipelining
Hakim Weatherspoon
CS 3410
Computer Science
Cornell University
[Weatherspoon, Bala, Bracy, McKee, and Sirer]

## Slide 2: Review: Single Cycle Processor
alu
PC
imm
memory
memory
din
dout
addr
target
offset
cmp
control
=?
new pc
register file
inst
extend
+4
+4

## Slide 3: Review: Single Cycle Processor
Advantages
  Single cycle per instruction make logic and clock simple
Disadvantages
  Since instructions take different time to finish, memory and functional unit are not efficiently utilized
  Cycle time is the longest delay
    Load instruction
  Best possible CPI is 1 (actually < 1 w parallelism)
    However, lower MIPS and longer clock period (lower clock frequency); hence, lower performance

## Slide 4: Review: Multi Cycle Processor
Advantages
  Better MIPS and smaller clock period (higher clock frequency)
  Hence, better performance than Single Cycle processor
Disadvantages
  Higher CPI than single cycle processor
Pipelining: Want better Performance
  want small CPI (close to 1) with high MIPS and short clock period (high clock frequency)

## Slide 5: Improving Performance
Parallelism
Pipelining
Both!

## Slide 6: The Kids
Alice
Bob
They don’t always get along…

## Slide 7: The Bicycle

## Slide 8: The Materials
Saw
Drill
Glue
Paint

## Slide 9: The Instructions
N pieces, each built following same sequence:
Saw
Drill
Glue
Paint

## Slide 10: Design 1: Sequential Schedule
Alice owns the room
Bob can enter when Alice is finished
Repeat for remaining tasks
No possibility for conflicts

## Slide 11: Sequential Performance
Elapsed Time for Alice: 4
Elapsed Time for Bob: 4
Total elapsed time: 4*N
Can we do better?
time 1 2 3 4 5 6 7 8 …
Latency:
Throughput:
Concurrency:
CPI =

## Slide 12: Design 2: Pipelined Design
Partition room into stages of a pipeline
One person owns a stage at a time
4 stages
4 people working simultaneously
Everyone moves right in lockstep
Alice
Bob
Carol
Dave

## Slide 13: Pipelined Performance
time 1 2 3 4 5 6 7…
Latency:
Throughput:
Concurrency:
CPI =

## Slide 14: Pipelined Performance
Time
1 2 3 4 5 6 7 8 9 10
Latency:
Throughput:
CPI =
What if drilling takes twice as long, but gluing and paint take ½ as long?

## Slide 15: Lessons
Principle:
Throughput increased by parallel execution
Balanced pipeline very important
  Else slowest stage dominates performance
Pipelining:
  Identify pipeline stages
  Isolate stages from each other
  Resolve pipeline hazards (next lecture)

## Slide 16
Single Cycle vs Pipelined Processor

## Slide 17: Single Cycle  Pipelining
insn0.fetch, dec, exec
Single-cycle
insn1.fetch, dec, exec
Pipelined
insn0.dec
insn0.fetch
insn1.dec
insn1.fetch
insn0.exec
insn1.exec

## Slide 18: Agenda
5-stage Pipeline
Implementation
Working Example
Hazards
Structural
Data Hazards
Control Hazards

## Slide 19: Review: Single Cycle Processor
alu
PC
imm
memory
memory
din
dout
addr
target
offset
cmp
control
=?
new pc
register file
inst
extend
+4
+4

## Slide 20: Pipelined Processor
alu
PC
imm
memory
memory
din
dout
addr
control
new pc
register file
inst
extend
+4
compute jump/branch targets
Fetch
Decode
Execute
Memory
WB

## Slide 21: Pipelined Processor
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4

## Slide 22: Time Graphs
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Cycle
Latency:
Throughput:
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
Latency:
Throughput:
Concurrency:
CPI =
add
nand
lw
add
sw

## Slide 23: Principles of Pipelined Implementation
Break datapath into multiple cycles (here 5)
  Parallel execution increases throughput
  Balanced pipeline very important
    Slowest stage determines clock rate
    Imbalance kills performance
Add pipeline registers (flip-flops) for isolation
  Each stage begins by reading values from latch
  Each stage ends by writing values to latch
Resolve hazards

## Slide 24: Pipelined Processor
Write- Back
Memory
Instruction Fetch
Execute
Instruction Decode
extend
register file
control
alu
memory
din
dout
addr
PC
memory
new pc
inst
IF/ID
ID/EX
EX/MEM
MEM/WB
imm
B
A
ctrl
ctrl
ctrl
B
D
D
M
compute jump/branch targets
+4

## Slide 25: Pipeline Stages
Stage | Perform Functionality | Latch values of interest
Fetch | Use PC to index Program Memory, increment PC | Instruction bits (to be decoded) PC + 4 (to compute branch targets)
Decode | Decode instruction, generate control signals, read register file | Control information, Rd index, immediates, offsets, register values (Ra, Rb), PC+4 (to compute branch targets)
Execute | Perform ALU operation Compute targets (PC+4+offset, etc.) in case this is a branch, decide if branch taken | Control information, Rd index, etc. Result of ALU operation, value in case this is a store instruction
Memory | Perform load/store if needed, address is ALU result | Control information, Rd index, etc. Result of load, pass result from execute
Writeback | Select value, write to register file | 

## Slide 26: Instruction Fetch (IF)
Stage 1: Instruction Fetch
Fetch a new instruction every cycle
  Current PC is index to instruction memory
  Increment the PC at end of cycle (assume no branches for now)
Write values of interest to pipeline register (IF/ID)
  Instruction bits (for later decoding)
  PC+4 (for later computing branch targets)

## Slide 27: Instruction Fetch (IF)
PC
instruction memory
new pc
addr
mc
+4

## Slide 28: Decode
Stage 2: Instruction Decode
On every cycle:
  Read IF/ID pipeline register to get instruction bits
  Decode instruction, generate control signals
  Read from register file
Write values of interest to pipeline register (ID/EX)
  Control information, Rd index, immediates, offsets, …
  Contents of Ra, Rb
  PC+4 (for computing branch targets later)

## Slide 29: Decode
ctrl
ID/EX
Rest of pipeline
PC+4
inst
IF/ID
PC+4
Stage 1: Instruction Fetch
register file
WE
Rd
Ra
Rb
D
B
A
B
A
imm

## Slide 30: Execute (EX)
Stage 3: Execute
On every cycle:
  Read ID/EX pipeline register to get values and control bits
  Perform ALU operation
  Compute targets (PC+4+offset, etc.) in case this is a branch
  Decide if jump/branch should be taken
Write values of interest to pipeline register (EX/MEM)
  Control information, Rd index, …
  Result of ALU operation
  Value in case this is a memory store instruction

## Slide 31: Execute (EX)
Stage 2: Instruction Decode
ctrl
EX/MEM
Rest of pipeline
B
D
ctrl
ID/EX
PC+4
B
A
alu
imm
target

## Slide 32: MEM
Stage 4: Memory
On every cycle:
  Read EX/MEM pipeline register to get values and control bits
  Perform memory load/store if needed
    address is ALU result
Write values of interest to pipeline register (MEM/WB)
  Control information, Rd index, …
  Result of memory operation
  Pass result of ALU operation

## Slide 33: MEM
ctrl
MEM/WB
Rest of pipeline
Stage 3: Execute
M
D
ctrl
EX/MEM
B
D
memory
din
dout
addr
mc
target

## Slide 34: WB
Stage 5: Write-back
On every cycle:
  Read MEM/WB pipeline register to get values and control bits
  Select value and write to register file

## Slide 35: WB
Stage 4: Memory
ctrl
MEM/WB
M
D
result

## Slide 36
IF/ID
+4
ID/EX
EX/MEM
MEM/WB
mem
din
dout
addr
PC
inst mem
Rd
Ra
Rb
D
B
A
Rd
Putting it all together
inst
PC+4
B
A
Rt
B
D
M
D
PC+4
imm
OP
Rd
OP
Rd
OP

## Slide 37: Takeaway
Pipelining is a powerful technique to mask latencies and increase throughput
  Logically, instructions execute one at a time
  Physically, instructions execute in parallel
    Instruction level parallelism
Abstraction promotes decoupling
  Interface (ISA) vs. implementation (Pipeline)

## Slide 38: RISC-V is designed for pipelining
Instructions same length
  32 bits, easy to fetch and then decode
4 types of instruction formats
  Easy to route bits between stages
  Can read a register source before even knowing what the instruction is
Memory access through lw and sw only
  Access memory after ALU

## Slide 39: Agenda
5-stage Pipeline
Implementation
Working Example
Hazards
Structural
Data Hazards
Control Hazards

## Slide 40: Example: Sample Code (Simple)
add x3  x1, x2 nand x6  x4, x5 lw x4  x2, 20 add x5  x2, x5 sw x7  x3, 12
Assume 8-register machine

## Slide 41
PC
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 7-11
Bits 15-19
op
Rt
imm
valB
valA
PC+4
PC+4
target
ALU
result
op
dest
valB
op
dest
ALU
result
mdata
instruction
0
x2
x3
x4
x5
x1
x6
x0
x7
regA
regB
Bits 0-6
data
dest
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
M
U
X
Rd
Inst
mem

## Slide 42: Example: Start State @ Cycle 0
PC
Register file
M
U
X
A
L
U
M
U
X
4
Data
mem
+
M
U
X
Bits 7-11
Bits 15-19
nop
0
0
0
0
0
0
0
0
nop
0
0
nop
0
0
0
nop
9
12
18
7
36
41
0
22
x2
x3
x4
x5
x1
x6
x0
x7
regA
regB
Bits 0-6
data
dest
IF/ID
ID/EX
EX/MEM
MEM/WB
extend
M
U
X
0
At time 1,
Fetch
add x3 x1 x2
0
4
Add
Nand
Lw
Add
sw
Initial State
0

## Slide 43: Agenda
5-stage Pipeline
Implementation
Working Example
Hazards
Structural
Data Hazards
Control Hazards

## Slide 44: Hazards
Correctness problems associated w/ processor design
  Structural hazards
  Same resource needed for different purposes at the same time (Possible: ALU, Register File, Memory)
  Data hazards
    Instruction output needed before it’s available
  Control hazards
    Next instruction PC unknown at time of Fetch

## Slide 45: Dependences and Hazards
Dependence: relationship between two insns
  Data: two insns use same storage location
  Control: 1 insn affects whether another executes at all
  Not a bad thing, programs would be boring otherwise
  Enforced by making older insn go before younger one
    Happens naturally in single-/multi-cycle designs
    But not in a pipeline
Hazard: dependence & possibility of wrong insn order
  Effects of wrong insn order cannot be externally visible
  Hazards are a bad thing: most solutions either complicate the hardware or reduce performance

## Slide 46: Where are the Data Hazards?
Clock cycle
1 2 3 4 5 6 7 8 9
time
sub x5, x3, x4
lw x6, x3, 4
or x5, x3, x5
sw x6, x3, 12
add x3, x1, x2

## Slide 47: Data Hazards
  register file reads occur in stage 2 (ID)
  register file writes occur in stage 5 (WB)
  next instructions may read values about to be written
i.e. add x3, x1, x2
sub x5, x3, x4
How to detect?

## Slide 48
IF/ID
+4
ID/EX
EX/MEM
MEM/WB
mem
din
dout
addr
PC
inst mem
Rd
Ra
Rb
D
B
A
Rd
Detecting Data Hazards
inst
PC+4
B
A
Rt
B
D
M
D
PC+4
imm
OP
Rd
OP
Rd
OP
IF/ID.Rs1 ≠ 0 &&
(IF/ID.Rs1==ID/Ex.Rd
IF/ID.Rs1==Ex/M.Rd
IF/ID.Rs1==M/W.Rd)
repeat for Rs2
add x3, x1, x2
sub x5,x3,x4

## Slide 49: Data Hazards
Data Hazards
  register file reads occur in stage 2 (ID)
  register file writes occur in stage 5 (WB)
  next instructions may read values about to be written
How to detect? Logic in ID stage:
stall = (IF/ID.Rs1 != 0 &&
(IF/ID.Rs1 == ID/EX.Rd || IF/ID.Rs1 == EX/M.Rd || IF/ID.Rs1 == M/WB.Rd))
|| (same for Rs2)

## Slide 50
IF/ID
+4
ID/EX
EX/MEM
MEM/WB
mem
din
dout
addr
PC
inst mem
Rd
Ra
Rb
D
B
A
Rd
Detecting Data Hazards
inst
PC+4
B
A
Rt
B
D
M
D
PC+4
imm
OP
Rd
OP
Rd
OP
detect hazard

## Slide 51: Takeaway
Data hazards occur when a operand (register) depends on the result of a previous instruction that may not be computed yet. A pipelined processor needs to detect data hazards.

## Slide 52: Next Goal
What to do if data hazard detected?

## Slide 53: Possible Responses to Data Hazards
Do Nothing
  Change the ISA to match implementation
  “Hey compiler: don’t create code w/data hazards!”
  (We can do better than this)
Stall
  Pause current and subsequent instructions till safe
Forward/bypass
  Forward data value to where it is needed
  (Only works if value actually exists already)

## Slide 54: Stalling
How to stall an instruction in ID stage
  prevent IF/ID pipeline register update
    stalls the ID stage instruction
  convert ID stage instr into nop for later stages
    innocuous “bubble” passes through pipeline
  prevent PC update
    stalls the next (IF stage) instruction

## Slide 55
inst mem
IF/ID
+4
ID/EX
EX/MEM
MEM/WB
mem
din
dout
addr
PC
Rd
Ra
Rb
D
B
A
Rd
Detecting Data Hazards
inst
PC+4
B
A
Rt
B
D
M
D
PC+4
imm
OP
Rd
OP
Rd
OP
detect hazard
add x3, x1, x2
sub x5, x3, x5
or x6, x3, x4
add x6, x3, x8
If detect hazard
WE=0
MemWr=0
RegWr=0

## Slide 56: Stalling
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add x3, x1, x2 |  |  |  |  |  |  |  |  | 
sub x5, x3, x5 |  |  |  |  |  |  |  |  | 
or x6, x3, x4 |  |  |  |  |  |  |  |  | 
add x6, x3, x8 |  |  |  |  |  |  |  |  | 
time

## Slide 57: Stalling
data mem
B
A
B
D
M
D
inst mem
D rD
B
A
Rd
Rd
Rd
WE
WE
Op
WE
Op
rA rB
PC
+4
Op
nop
inst
/stall
add x3,x1,x2
(MemWr=0
RegWr=0)
NOP = If(IF/ID.rA ≠ 0 &&
(IF/ID.rA==ID/Ex.Rd IF/ID.rA==Ex/M.Rd
IF/ID.rA==M/W.Rd))
sub x5,x3,x5
or x6,x3,x4
(WE=0)
STALL CONDITION MET

## Slide 58: Stalling
data mem
B
A
B
D
M
D
inst mem
D rD
B
A
Rd
Rd
Rd
WE
WE
Op
WE
Op
rA rB
PC
+4
Op
nop
inst
/stall
add x3,x1,x2
NOP = If(IF/ID.rA ≠ 0 &&
(IF/ID.rA==ID/Ex.Rd IF/ID.rA==Ex/M.Rd
IF/ID.rA==M/W.Rd))
sub x5,x3,x5
or x6,x3,x4
STALL CONDITION MET
nop
(MemWr=0
RegWr=0)
(MemWr=0
RegWr=0)
(WE=0)

## Slide 59: Stalling
data mem
B
A
B
D
M
D
inst mem
D rD
B
A
Rd
Rd
Rd
WE
WE
Op
WE
Op
rA rB
PC
+4
Op
nop
inst
/stall
add x3,x1,x2
NOP = If(IF/ID.rA ≠ 0 &&
(IF/ID.rA==ID/Ex.Rd IF/ID.rA==Ex/M.Rd
IF/ID.rA==M/W.Rd))
sub x5,x3,x5
or x6,x3,x4
STALL CONDITION MET
nop
(MemWr=0
RegWr=0)
nop
(MemWr=0
RegWr=0)
(MemWr=0
RegWr=0)
(WE=0)

## Slide 60: Stalling
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add x3, x1, x2 |  |  |  |  |  |  |  |  | 
sub x5, x3, x5 |  |  |  |  |  |  |  |  | 
or x6, x3, x4 |  |  |  |  |  |  |  |  | 
add x6, x3, x8 |  |  |  |  |  |  |  |  | 
time
x3 = 10
x3 = 20

## Slide 61: Stalling
How to stall an instruction in ID stage
  prevent IF/ID pipeline register update
    stalls the ID stage instruction
  convert ID stage instr into nop for later stages
    innocuous “bubble” passes through pipeline
  prevent PC update
    stalls the next (IF stage) instruction

## Slide 62: Takeaway
Data hazards occur when a operand (register) depends on the result of a previous instruction that may not be computed yet. A pipelined processor needs to detect data hazards.
Stalling, preventing a dependent instruction from advancing, is one way to resolve data hazards.
Stalling introduces NOPs (“bubbles”) into a pipeline. Introduce NOPs by (1) preventing the PC from updating, (2) preventing writes to IF/ID registers from changing, and (3) preventing writes to memory and register file.
*Bubbles in pipeline significantly decrease performance.

## Slide 63: Possible Responses to Data Hazards
Do Nothing
  Change the ISA to match implementation
  “Compiler: don’t create code with data hazards!”
  (Nice try, we can do better than this)
Stall
  Pause current and subsequent instructions till safe
Forward/bypass
  Forward data value to where it is needed
  (Only works if value actually exists already)

## Slide 64: Forwarding
Forwarding bypasses some pipelined stages forwarding a result to a dependent instruction operand (register).
Three types of forwarding/bypass
  Forwarding from Ex/Mem registers to Ex stage (MEx)
  Forwarding from Mem/WB register to Ex stage (WEx)
  RegisterFile Bypass

## Slide 65: Add the Forwarding Datapath
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
forward unit
detect hazard
IF/ID
ID/Ex
Ex/Mem
Mem/WB

## Slide 66: Forwarding Datapath
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rb
WE
WE
MC
Ra
MC
forward unit
detect hazard
IF/ID
ID/Ex
Ex/Mem
Mem/WB
Three types of forwarding/bypass
Forwarding from Ex/Mem registers to Ex stage (MEx)
Forwarding from Mem/WB register to Ex stage (W  Ex)
RegisterFile Bypass

## Slide 67: Forwarding Datapath 1: Ex/MEM  EX
add x3, x1, x2 |  |  |  |  |  |  | 
sub x5, x3, x1 |  |  |  |  |  |  | 
data mem
inst mem
D
B
A
add x3, x1, x2
sub x5, x3, x1
Problem: EX needs ALU result that is in MEM stage
Solution: add a bypass from EX/MEM.D to start of EX
Ex/Mem

## Slide 68: Forwarding Datapath 1: Ex/MEM  EX
data mem
inst mem
D
B
A
add x3, x1, x2
sub x5, x3, x1
Ex/Mem
Detection Logic in Ex Stage:
forward = (Ex/M.WE && EX/M.Rd != 0 &&
ID/Ex.Rs1 == Ex/M.Rd)
|| (same for Rs1)

## Slide 69: Forwarding Datapath 2: Mem/WB EX
data mem
inst mem
D
B
A
add x3, x1, x2
sub x5, x3, x1
Problem: EX needs value being written by WB
Solution: Add bypass from WB final value to start of EX
or x6, x3, x4
add x3, x1, x2 |  |  |  |  |  |  |  | 
sub x5, x3, x1 |  |  |  |  |  |  |  | 
or x6, x3, x4 |  |  |  |  |  |  |  | 
Problem: EX needs value being written by WB
Solution: Add bypass from WB final value to start of EX
Mem/WB

## Slide 70: Forwarding Datapath 2: Mem/WB EX
data mem
inst mem
D
B
A
add x3, x1, x2
sub x5, x3, x1
or x6, x3, x4
Mem/WB
Detection Logic:
forward = (M/WB.WE && M/WB.Rd != 0 &&
ID/Ex.Rs1 == M/WB.Rd &&
not (ID/Ex.WE && Ex/M.Rd != 0 &&
ID/Ex.Rs1 == Ex/M.Rd)
|| (same for Rs2)

## Slide 71: Register File Bypass
data mem
inst mem
D
B
A
Problem: Reading a value that is currently being written
Solution: just negate register file clock
  writes happen at end of first half of each clock cycle
  reads happen during second half of each clock cycle
add x3, x1,x2
sub x5, x3, x1
or x6, x3, x4
add x6, x3, x8

## Slide 72: Register File Bypass
data mem
inst mem
D
B
A
add x3, x1,x2
sub x5, x3, x1
or x6, x3, x4
add x6, x3, x8
add x3, x1, x2 |  |  |  |  |  |  |  |  | 
sub x5, x3, x1 |  |  |  |  |  |  |  |  | 
or x6, x3, x4 |  |  |  |  |  |  |  |  | 
add x6, x3, x8 |  |  |  |  |  |  |  |  | 

## Slide 73: Agenda
5-stage Pipeline
Implementation
Working Example
Hazards
Structural
Data Hazards
Control Hazards

## Slide 74: Forwarding Example 2
Clock cycle
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 
add x3, x1, x2 |  |  |  |  |  |  |  |  | 
sub x5, x3, x5 |  |  |  |  |  |  |  |  | 
lw x6, x3, 4 |  |  |  |  |  |  |  |  | 
or x6, x3, x4 |  |  |  |  |  |  |  |  | 
sw x6, x3, 12 |  |  |  |  |  |  |  |  | 
time

## Slide 75: Load-Use Hazard Explained
data mem
inst mem
D
B
A
lw x4, x8, 20
or x6, x3, x4
Data dependency after a load instruction:
  Value not available until after the M stage
  Next instruction cannot proceed if dependent
THE KILLER HAZARD

## Slide 76: Load-Use Stall
data mem
inst mem
D
B
A
lw x4, x8, 20 |  |  |  |  |  |  |  |  | 
or x6, x4, x1 |  |  |  |  |  |  |  |  | 
lw x4, x8, 20
or x6, x4, x1

## Slide 77: Load-Use Stall (1)
data mem
inst mem
D
B
A
lw x4, x8, 20
or x6, x4, x1
lw x4, x8, 20 |  |  |  |  |  |  |  |  | 
or x6, x4, x1 |  |  |  |  |  |  |  |  | 
IF
ID
Ex
IF
ID
load-use stall

## Slide 78: Load-Use Detection
data mem
imm
B
A
B
D
M
D
inst mem
D
B
A
Rd
Rd
Rs2
WE
WE
MC
Rs1
MC
forward unit
detect hazard
IF/ID
ID/Ex
Ex/Mem
Mem/WB
Rd
MC
Stall = If(ID/Ex.MemRead &&
IF/ID.Rs1 == ID/Ex.Rd

## Slide 79: Resolving Load-Use Hazards
  RISC-V Solution : Load-Use Stall
  Stall must be inserted so that load instruction can go through and update the register file.
  Forwarding from RAM (Memory) is not an option.
  In some cases, real world compilers can optimize to avoid these situations.

## Slide 80: Takeaway
Data hazards occur when a operand (register) depends on the result of a previous instruction that may not be computed yet. A pipelined processor needs to detect data hazards.
Stalling, preventing a dependent instruction from advancing, is one way to resolve data hazards. Stalling introduces NOPs (“bubbles”) into a pipeline. Introduce NOPs by (1) preventing the PC from updating, (2) preventing writes to IF/ID registers from changing, and (3) preventing writes to memory and register file. Bubbles (nops) in pipeline significantly decrease performance.
Forwarding bypasses some pipelined stages forwarding a result to a dependent instruction operand (register). Better performance than stalling.

## Slide 81: Quiz
Find all hazards, and say how they are resolved:
add x3, x1, x2
nand x5, x3, x4
add x2, x6, x3
lw x6, x3, 24
sw x6, x2, 12
Notes: Find all hazards, and say how they are resolved

## Slide 82: Quiz
Find all hazards, and say how they are resolved: add x3, x1, x2 sub x3, x2, x1 nand x4, x3, x1 or x0, x3, x4 xor x1, x4, x3 sb x4, x0, 1

## Slide 83: Data Hazard Recap
Delay Slot(s)
  Modify ISA to match implementation
Stall
  Pause current and all subsequent instructions
Forward/Bypass
  Try to steal correct value from elsewhere in pipeline
  Otherwise, fall back to stalling or require a delay slot
Tradeoffs?

## Slide 84: Agenda
5-stage Pipeline
Implementation
Working Example
Hazards
Structural
Data Hazards
Control Hazards

## Slide 85: A bit of Context
i = 0;
do {
n += 2;
i++;
} while(i < max)
i = 7;
n--;
x10 addi x1, x0, 0 # i=0
x14 Loop: addi x2, x2, 2 # n += 2
x18 addi x1, x1, 1 # i++
x1C blt x1, x3, Loop # i<max?
x20 addi x1, x0, 7 # i = 7
x24 subi x2, x2, 1 # n--
i  x1
Assume:
n  x2
max  x3

## Slide 86: Control Hazards
Control Hazards
  instructions are fetched in stage 1 (IF)
  branch and jump decisions occur in stage 3 (EX)
   next PC not known until 2 cycles after branch/jump
x1C blt x1, x3, Loop
x20 addi x1, x0, 7
x24 subi x2, x2, 1
Branch not taken?
No Problem!
Branch taken?
Just fetched 2 insns
 Zap & Flush

## Slide 87: Zap & Flash
data mem
inst mem
D
B
A
prevent PC update
clear IF/ID latch
branch continues
PC
+4
branch calc
decide branch
If branch Taken
New PC = 14
Zap
1C | blt x1,x3,L |  |  |  |  |  |  |  | 
20 | addi x1,x0,7 |  |  |  |  |  |  |  | 
24 | subi x2,x2,1 |  |  |  |  |  |  |  | 
14 L:addi x2,x2,2

## Slide 88: Reducing the cost of control hazard
Resolve Branch at Decode
  Some groups do this for Project 3, your choice
  Move branch calc from EX to ID
  Alternative: just zap 2nd instruction when branch taken
Branch Prediction
  Not in 3410, but every processor worth anything does this (no offense!)

## Slide 89: Problem: Zapping 2 insns/branch
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
New PC = 14
1C | blt x1,x3,L |  |  |  |  |  |  |  | 
20 | addi x1,x0,7 |  |  |  |  |  |  |  | 
24 | subi x2,x2,1 |  |  |  |  |  |  |  | 

## Slide 90: Soln #1: Resolve Branches @ Decode
data mem
inst mem
D
B
A
PC
+4
branch calc
decide branch
New PC = 1C
1C | blt x1,x3,L |  |  |  |  |  |  |  | 
20 | addi x1,x0,7 |  |  |  |  |  |  |  | 
24 | subi x2,x2,1 |  |  |  |  |  |  |  | 

## Slide 91: Branch Prediction
Most processor support Speculative Execution
  Guess direction of the branch
    Allow instructions to move through pipeline
    Zap them later if guess turns out to be wrong
  A must for long pipelines

## Slide 92: Summary
Control hazards
  Is branch taken or not?
  Performance penalty: stall and flush
Reduce cost of control hazards
  Move branch decision from Ex to ID
    2 nops to 1 nop
  Branch prediction
    Correct. Great!
    Wrong. Flush pipeline. Performance penalty

## Slide 93: Hazards Summary
Data hazards
Control hazards
Structural hazards
  resource contention
  so far: impossible because of ISA and pipeline design

## Slide 94: Hazards Summary
Data hazards
  register file reads occur in stage 2 (IF)
  register file writes occur in stage 5 (WB)
  next instructions may read values soon to be written
Control hazards
  branch instruction may change the PC in stage 3 (EX)
  next instructions have already started executing
Structural hazards
  resource contention
  so far: impossible because of ISA and pipeline design

## Slide 95: Data Hazard Takeaways
Data hazards occur when a operand (register) depends on the result of a previous instruction that may not be computed yet. Pipelined processors need to detect data hazards.
Stalling, preventing a dependent instruction from advancing, is one way to resolve data hazards. Stalling introduces NOPs (“bubbles”) into a pipeline. Introduce NOPs by (1) preventing the PC from updating, (2) preventing writes to IF/ID registers from changing, and (3) preventing writes to memory and register file. Nops significantly decrease performance.
Forwarding bypasses some pipelined stages forwarding a result to a dependent instruction operand (register). Better performance than stalling.

## Slide 96: Control Hazard Takeaways
Control hazards occur because the PC following a control instruction is not known until control instruction is executed. If branch is taken  need to zap instructions. 1 cycle performance penalty.
We can reduce cost of a control hazard by moving branch decision and calculation from Ex stage to ID stage.